# Introduction

This note takes the Naming Convention Specification (H-P-1-ASPI-SP-0141) for the Herschel/Planck satellites’ database and applies it to the SPIRE instrument to provide a recommended naming convention for the SPIRE Mission Implementation Base (MIB).

The SPIRE MIB contains Monitor and Command packets, Monitor and Command parameters plus the corresponding calibration curves and displays.

The following naming convention shall be used:

| Item | scos-name | Name | Convention | ASPI comments |
| --- | --- | --- | --- | --- |
| Command parameter | cpc_pname | SPinnppp | 5130 | OK |
| Monitor parameter | pcf_name | SMinnppp | 5130 | OK |
| Command packet | ccf_cname | SCinnppp | 4580 | OK |
| Monitor packet | pid_spid | 19nnnnppp | 4380 | (1) |
| Command num calibration | cca_numbr |  |  | (2) |
| Command txt calibration | paf_numbr |  |  | (2) |
| Monitor num calibration | caf_numbr |  |  | (2) |
| Monitor txt calibration | txf_numbr |  |  | (2) |
| Polynomial calibration | mcf_ident |  |  | (2) |
| Numerical display | and | SAinnppp | 6150 | OK |
| Graphical display | grd | SGinnppp | 6150 | OK |
| Scrolling display | srd | SLinnppp | 6150 | OK |

(*) ASPI SCOS mnemo are issued from issue 5.0 of SCOS-2000 database import ICD.

- Due to an error in previous issue and due to PACS needs, has been changed

- If you are using a SCOS-2000 version supporting only calibration identifier coded as Number(4), please code any curve reference under Number(3) format unique for all your curves (maximum number of curves is 1000) - If you are using a SCOS-2000 version supporting calibration identifier coded over as Char(10) please code the common curves (shared by several parameters) according to 5370 ("289 nnn") and the specific curve (associated to one and only one parameter) according to 5375 ("HP xxx ppp cc" for command parameter or "HM xxx ppp cc" for monitoring parameter)

Where:

- i is the System Element ID (see section 2.1)

- nn, nnn and nnnn are running numbers starting at zero and incrementing (warning : this limits the number of command parameter, monitor parameter and command packet to 99 per system element ID. The naming convention allows for some identifiers "nn" to be 2 alphanumerics)

- ttt is the System Element number (see section 2.1)

- rrr is the Real Element number (see section 2.3)

- ppp is the Position Identifier  (see section 2.2)

# Identifiers

Identifiers are defined in the Naming Convention Specification with SPIRE allocated particular numbers and characters for the various fields. This section defines how these are used in the SPIRE naming convention.

## System Elements

Each distinct type of subsystem in the instrument (called a System Element Type) is assigned a unique id and number:

| System Element Type | ID | ASPI comments | Number |
| --- | --- | --- | --- |
| OBS | B | OK | 480 |
| DPU | P | OK | 490 |
| DCU | D | OK | 500 |
| MCU | M | OK | 510 |
| SCU | S | OK | 520 |

## Position Identifiers

Each model of the instrument (including a ‘theoretical’ model) is composed of a set of System Elements. This may include more than one System Element of any given type. Each distinct System Element for each instrument model is assigned a unique number. This unique number is also used as the Position Identifier.

|  | Model |
| --- | --- |
| System Element | Theoretical | AVM | QM | FM | FS |
| OBS | 480 | 481 | 483 | 485 | 487 |
| DPU | 490 | 4911 4922 | 4931 4942 | 4951 4962 | 4971 4982 |
| DCU | 500 | 501 | 503 | 505 | 507 |
| MCU | 510 | 511 | 513 | 515 | 517 |
| SCU | 520 | 521 | 523 | 525 | 527 |

ASPI suggest the following implementation (refer to answer to ASPI comments to HIFI summary) :

|  | Model |
| --- | --- |
| System Element | Theoretical | AVM | QM | FM | FS |
| OBS | 480 | 480 | 480 | 480 | 480 |
| DPU | 490 | 4901 4912 | 4901 4912 | 4901 4912 | 4901 4912 |
| DCU | 500 | 500 | 500 | 500 | 500 |
| MCU | 510 | 510 | 510 | 510 | 510 |
| SCU | 520 | 520 | 520 | 520 | 520 |

The "theoretical" position identifier is not needed.

1. Valid for prime element

2. Valid for redundant element

## Real Element Numbers

These numbers identify individual configurations of each System Element (there may be more than one configuration if, for example, electronic boards have to be exchanged during testing). The table below gives the Real Element Number for the first configuration of the System Element. They should be incremented by 1 for each new configuration.

|  | Model |
| --- | --- |
| System Element | AVM | QM | FM | FS |
| OBS | 100 | 300 | 500 | 700 |
| DPU | 1001 2002 | 3001 4002 | 5001 6002 | 7001 8002 |
| DCU | 100 | 300 | 500 | 700 |
| MCU | 100 | 300 | 500 | 700 |
| SCU | 100 | 300 | 500 | 700 |

1. Valid for prime element

2. Valid for redundant element

OK