# Introduction

This note takes the Naming Convention Specification (H-P-1-ASPI-SP-0141) for the Herschel/Planck satellites’ database and applies it to the PACS instrument to provide a recommended naming convention for the PACS Mission Implementation Base (MIB).

The PACS MIB contains Monitor and Command packets, Monitor and Command parameters plus the corresponding calibration curves and displays.

The following naming convention shall be used:

| Item | scos-name | Name | Convention | ASPI comments |
| --- | --- | --- | --- | --- |
| Command parameter | cpc_pname | PPnnnppp | 5130 | OK |
| Monitor parameter | pcf_name | PMnnnppp | 5130 | OK |
| Command packet | ccf_cname | PCnnnppp | 4580 | OK |
| Monitor packet | pid_spid | 16nnnnppp | 4380 | (1) |
| Command num calibration | cca_numbr |  |  | (2) |
| Command txt calibration | paf_numbr |  |  | (2) |
| Monitor num calibration | caf_numbr |  |  | (2) |
| Monitor txt calibration | txf_numbr |  |  | (2) |
| Polynomial calibration | mcf_ident |  |  | (2) |
| Numerical display | dpf_numbe | PAnnnppp | 6150 | OK |
| Graphical display | gpf_numbe | PGnnnppp | 6150 | OK |
| Scrolling display | spf_numbe | PLnnnppp | 6150 | OK |

- Due to an error in previous issue and due to PACS needs, has been changed

- If you are using a SCOS-2000 version supporting only calibration identifier coded as Number(4), please code any curve reference under Number(3) format unique for all your curves (maximum number of curves is 1000) - If you are using a SCOS-2000 version supporting calibration identifier coded over as Char(10) please code the common curves (shared by several parameters) according to 5370 ("289 nnn") and the specific curve (associated to one and only one parameter) according to 5375 ("HP xxx ppp cc" for command parameter or "HM xxx ppp cc" for monitoring parameter)

Where:

- nnn and nnnn are running numbers starting at zero and incrementing

- ttt is the System Element number, for PACS it is a number in the range 380-429 (see section 2.1)

- ppp is the Position Identifier number, for PACS is a number in the range [380-427] U [428]  (see section 0)

- rrr is the Real Element number (see section 2.3)

# Identifiers

Identifiers are defined in the Naming Convention Specification with PACS allocated particular numbers and characters for the various fields. This section defines how these are used in the PACS naming convention.

## System Elements

Each distinct type of subsystem in the instrument (called a System Element Type) is assigned a unique number:

| System Element Type | Number | ASPI comments |
| --- | --- | --- |
| DPU | 380 | OK |
| SPUL | 390 | OK |
| SPUS | 400 | OK |
| BOL | 410 | OK |
| DMC | 420 | OK |

## Position Identifiers

Each model of the instrument (including a ‘theoretical’ model) is composed of a set of System Elements. This may include more than one System Element of any given type. Each distinct System Element for each instrument model is assigned a unique number. This unique number is also used as the Position Identifier.

|  | Model |
| --- | --- |
| System Element | Theoretical | AVM | QM | FM | FS |
| DPU nominal DPU redundant | 380 | 380 | 380 381 | 380 381 | 380 381 |
| SPUL nominal SPUL redundant | 390 | 390 | 390 391 | 390 391 | 390 391 |
| SPUS nominal SPUS redundant | 400 | 400 401 | 400 401 | 400 401 | 400 401 |
| BOL | 410 | 410 | 410 | 410 | 410 |
| DMC | 420 | 420 | 420 | 420 | 420 |

ASPI comments : OK

## Real Element Numbers

This numbers identify the real Element.

|  | Model |
| --- | --- |
| System Element | AVM | QM | FM | FS |
| DPU | 380 | 380 | 380 | 380 |
| SPUL | 390 | 390 | 390 | 390 |
| SPUS | 400 | 400 | 400 | 400 |
| BOL | 410 | 410 | 410 | 410 |
| DMC | 420 | 420 | 420 | 420 |

ASPI comments :

No - There is not any constraints on the real element number (except its limitation over 3 numerical digits [000-999]) but for a same "subsystem" for you ("real element"  for ASPI the number shall be differents (one to one correspondance with serial number). The ASPI proposal is :

|  | Model |
| --- | --- |
| System Element | AVM | QM | FM | FS |
| DPU | 380 | 381 | 382 | 383 |
| SPUL | 380 | 381 | 382 | 383 |
| SPUS | 380 | 381 | 382 | 383 |
| BOL | 380 | 381 | 382 | 383 |
| DMC | 380 | 381 | 382 | 383 |

the following implementation is also valid :

|  | Model |
| --- | --- |
| System Element | AVM | QM | FM | FS |
| DPU | 0 | 1 | 2 | 3 |
| SPUL | 4 | 5 | 6 | 7 |
| SPUS | 8 | 9 | 10 | 11 |
| BOL | 12 | 13 | 14 | 15 |
| DMC | 16 | 17 | 18 | 19 |

the following implementation is also valid :

|  | Model |
| --- | --- |
| System Element | AVM | QM | FM | FS |
| DPU | 0 | 1 | 2 | 3 |
| SPUL | 0 | 1 | 2 | 3 |
| SPUS | 0 | 1 | 2 | 3 |
| BOL | 0 | 1 | 2 | 3 |
| DMC | 0 | 1 | 2 | 3 |