# Introduction

This document show how the naming conventions (H-P-1-ASPI-SP-0141) specified by ASPI can be applied to the Planck/HFI for a subset of items.

The following table indicates how to format the SCOS name.

| Item | scos-name | Name | Convention | ASPI |
| --- | --- | --- | --- | --- |
| Command parameter name | cpc_pname | HP xxx ppp | 5130 | OK |
| Monitor parameter name | pcf_name | HM xxx ppp | 5130 | OK |
| TC packet identifier | ccf_cname | HC xxx ppp | 4580 | OK |
| TM packet number | pid_spid | 08 nnnn ppp | 4380 | (1) |
| Command num calibration | cca_numbr |  |  | (2) |
| Command txt calibration | paf_numbr |  |  | (2) |
| Monitor num calibration | caf_numbr |  |  | (2) |
| Monitor txt calibration | txf_numbr |  |  | (2) |
| Polynomial calibration | mcf_IDENT |  |  | (2) |
| Numerical display | dpf_numbe | HA nnn ppp | 6100 | OK |
| Graphical display | Gpf_Numbe | HG nnn ppp | 6110 | OK |
| Scrolling display | scf_numbe | HL nnn ppp | 6130 | OK |
| TM Parameter Identifier | pcf_pid | 0 - 65535 | 7800?? | OK |
| Monitoring text curve id | TXF_numbr |  |  | (2) |
| Monitor packet identifier variable length | pid_tpsd | 08 nnnn ppp | 4380 | (1) |
| TC packet header | tcp_id | HXTCPS aa bb | 4505 | OK (3) |
| TC packet header parameter | pcpc_pname | HY xxx ppp | 5130 | OK (3) |
| Command Sequence | cSf_name | HS xxx ppp | 4660 | OK |
| Command sequence formal parameter | csp_fname | HF xxx ppp | 4074 |  |
| Verification stage identifier | cvs_id | 00001 – 02999 |  | OK |
| Command parameter set | pst_name | HT xxx ppp | 5215 |  |
| Command parameter set value | psv_pvsid | HVxxx ppp | 5225 |  |
| Command textual curve | paf_numbr |  |  | (2) |

- Due to an error in previous issue and due to PACS needs, has been changed

- If you are using a SCOS-2000 version supporting only calibration identifier coded as Number(4), please code any curve reference under Number(3) format unique for all your curves (maximum number of curves is 1000) - If you are using a SCOS-2000 version supporting calibration identifier coded over as Char(10) please code the common curves (shared by several parameters) according to 5370 ("289 nnn") and the specific curve (associated to one and only one parameter) according to 5375 ("HP xxx ppp cc" for command parameter or "HM xxx ppp cc" for monitoring parameter)

ttt is a number in the range [240-287] U [289] type of system element for HFI

aa service type of the TC

bb service sub-type of the TC

nnn is a running number 000-999

nnnn is a running number 0000-9999

rrr  real element

ppp is a number in the range [240-287] U [289]   position  allocation for HFI

xxx is in the range (0-9) and (A-Z but not O,Q,I)

cc is the condition number (for conditioned calibration curve) - If not supported by your SCOS-2000 version to be forced to "00".

## System Element (ttt)

| Subsystem | Number | ASPI |
| --- | --- | --- |
| OBSW | 240 | OK |
| DPU | 250 | OK |
| 4KDCE | 260 | OK |
| DCE | 270 | OK |
| REU | 280 | OK |

## Position Identifier (ppp)

| Subsystem | Theoretical | CQM | PFM | FS | ASPI |
| --- | --- | --- | --- | --- | --- |
| OBSW | 240 |  |  |  | OK |
| DPU prime | 250 | 250 | 250 | 250 | OK |
| DPU redundant |  |  | 251 |  | OK |
| 4KDCE | 260 | 260 | 260 | 260 | OK |
| DCE | 270 | 270 | 270 | 270 | OK |
| REU prime | 280 | 280 | 280 | 280 | OK |
| REU redundant |  |  | 281 |  | OK |

## Real Element number (rrr)

| Subsystem | CQM | PFM | FS | ASPI |
| --- | --- | --- | --- | --- |
| OBSW | 100 | 300 | 500 | OK |
| DPU prime | 100 | 300 | 500 | OK |
| DPU redundant |  | 200 |  | OK |
| 4KDCE | 100 | 300 | 500 | OK |
| DCE | 100 | 300 | 500 | OK |
| REU prime | 100 | 300 | 500 | OK |
| REU redundant |  | 200 |  | OK |

# PCF_NAME versus PCF_PID

In order to associate easily the PCF_NAME (Monitoring parameter identifier) and the PCF_PID (OBSW parameter identifier used in PSICD service 3), the same numerical value on 3 digits (000 to 999) is taken in association with the sub-system Position Identifier (only the 2 high order digit for the PCF_PID - ASPI comments : "well done" for nominal / redundant).

| Subsystem | PCF_NAME | PCF_PID | ASPI |
| --- | --- | --- | --- |
|  | HM | xxx | ppp | xxxxx | OK |
| OBSW | HM | 0 – 999 | 240 | 24000 – 24999 | OK |
| DPU prime | HM | 0 – 999 | 250 | 25000 – 25999 | OK |
| DPU redundant | HM | 0 – 999 | 251 | 25000 – 25999 | OK |
| 4KDCE | HM | 0 – 999 | 260 | 26000 – 26000 | OK |
| DCE | HM | 0 – 999 | 270 | 27000 – 27999 | OK |
| REU prime | HM | 0 – 999 | 280 | 28000 – 28999 | OK |
| REU redundant | HM | 0 – 999 | 281 | 28000 – 28999 | OK |

Note : this allocation applies for HFI software, different allocation will be provided automatically by HPSDB for CDMS software (for HFI parameters processed by CDMS : FDIR, …)

# PCF_NAME versus calibration names

The nnn digit  of the CCA_NUMBR, PAF_NUMBR, CAF_NUMBR, TXF_NUMBR and MCF_NUMBR shall be the same as the PCF_NAME and PCF_PID. Therefore the range of the calibration numbers for a given sub-system stays the same.

Example:

| Parameter Description | PCF_NAME | PCF_PID | CAF_NUMBR | ASPI |
| --- | --- | --- | --- | --- |
| REU Prime cryogenic temperature #0 | HM 515 280 | 28515 | 280 515 rrr | (2) |

First instanciation for the first calibration of CQM REU cryogenic temperature #0:

| Parameter Description | PCF_NAME | PCF_PID | CAF_NUMBR | ASPI |
| --- | --- | --- | --- | --- |
| REU Prime cryogenic temperature #0 | HM 515 280 | 28515 | 280 515 100 | (2) |

# Range of value for TC Packet identifier (CCF_CNAME)

A first repartition of the xxx numerical value is given below in function of the sub-system and the Planck PS.ICD service type:

| Subsystem | PS.ICD service type | HC | xxx | ppp | ASPI |
| --- | --- | --- | --- | --- | --- |
| OBSW (On-board management) | 8 (unified) | HC | 000 – 149 | 240 | OK |
| OBSW (Science management) | 8 (unified) | HC | 150 – 299 | 240 | OK |
| OBSW (General services) | 3, 9, 14, 17 | HC | 300 – 399 | 240 | OK |
| DPU prime | 6 & 8 (private) | HC | 300 – 399 | 250 | OK |
| DPU redundant | 6 & 8 (private) | HC | 400 – 499 | 251 | OK |
| 4KDCE | 6 & 8 (private) | HC | 500 – 599 | 260 | OK |
| DCE | 6 & 8 (private) | HC | 600 – 699 | 270 | OK |
| REU prime | 6 & 8 (private) | HC | 600 – 699 | 280 | OK |
| REU redundant | 6 & 8 (private) | HC | 700 – 799 | 281 | OK |

Let us note that the general TC are always sent to OBSW (ppp = 240). ASPI comment : right.

# Telemetry packet number PID_SPID

ASPI comment : Refer to (1)

The PID_SPID is a number N10 with ttt nnnn ppp.

The PID_SPID shall be formatted as 240nnnn240 (possible update to 08nnnn240 - ASPI comment : confirmed refer to (1) ). The numerical value nnnn is separated in 2 field:

2 high order digit gives the Planck PS.ICD service type

2 low order digit gives the packet numbering range for a Planck PS.ICD service sub-type.

| Planck PS.ICD service type and subtype | Nnnn | ASPI |
| --- | --- | --- |
| HSK packet TM(3,25) | 0300 – 0319 | OK |
| Diagnostic packet TM(3,36) | 0320 – 0339 | OK |
| Event Report TM(5,1) | 0500 – 0519 | OK |
| Exception Report TM(5,2) | 0520 – 0539 | OK |
| Alarm Report TM(5,4) | 0540 – 0559 | OK |
| Nominal Science | 2100 | OK |
| Science Type B1 | 2101 | OK |
| Science Type B2 | 2102 | OK |
| Diagnostic Science | 2103 | OK |
| Auxiliary Science | 2104 | OK |
| TC Acceptance Report TM(1,1) | 0100 | OK |
| TC Acceptance Report TM(1,2) | 0101 | OK |
| TC Acceptance Report TM(1,7) | 0102 | OK |
| TC Acceptance Report TM(1,8) | 0103 | OK |
| HSK Parameter Report TM (3,10) | 0340-0359 | OK |
| Diagnostic Parameter Report TM (3,12) | 0360-0379 | OK |
| Memory dump TM(6,6) | 0600-0619 | OK |
| Memory Check TM(6,10) | 0620-0639 | OK |
| Function Status Report TM(8,6) | 0800 – 0819 | OK |
| Time Verification Report TM(9,9) | 0900 | OK |
| Enabled Telemetry Packet Report TM(14,4) | 1400 | OK |

Some range  is open to sub-division. Others can be set to a unique value.