## Overview

1.) ASAP SPIRE model

## 2.) Geometry in the center of telescope mirror (M1-baffle, cone baffle)

3.) Results: Tables on fluxes and irradiances onto SPIRE objects

ASAP-SPIRE-MODEL(					M4+M4-aperture		FP_UNIT

=chopper		REF=0.7

| detector cold stop M9 |  | FPIN PFIL1 M3 |
| --- | --- | --- |

ASAP-SPIRE-MODEL(: made compatible with the data in the SPIRE design description

result: much better imaging quality, especially pupil imaging

footprint pictures (distributed by e-mail) should enable confirmation of validity of present ASAP model by RAL

|  | rays from rim of secondary mirror imaged onto cold stop the cold stop (outer blue annular ring) is larger than the image of the secondary mirror |
| --- | --- |

Backward trace from SPIRE detector via cold stop to the telescope secondary mirror: ( also part of the hexapod surfaces can be seen by the detector

ASAP-SPIRE-MODEL

Within SPIRE the entrance box ('FP_UNIT') has great influence on the radiation transported towards surfaces and edges, if the walls are reflecting.

The tables on results contain values for

- wall reflectivity 0.7 (as received)

- wall reflectivity 0.0 (as comparison to the ideal situation)

M1-baffle and Cryostat-baffle

Present M1-baffle (as delivered in the ASAP telescope model) has

- An inner tube with diameter 325 mm, length 176.2 mm

- A flat disk filling the gap to the telescope mirror M1 nearly completely

- A tube at the inner rim of M1 with length 80 mm

The transition to the cryostat objects is not designed yet (therefore has to be considered in the calculations with increased emissivity, listed in the tables as ‚grey cone‘).

|  | M1-baffle ‚grey cone‘). cryostat baffle CVV radiation shields |
| --- | --- |

|  | Alternative: cone baffle conical shape wherever possible, large radius (cutouts for cyrostat cover etc.) CVV radiation shields |
| --- | --- |

| Advantages of M1-baffle smaller opening in the center of M1 w.r.t. moon/earth (smaller moon/earth straylight to be expected) | Advantages of cone baffle the cone sends a fraction of the thermal radiation outwards (towards +X, see sketch) reduced thermal radiation onto focal planes because: the emitting surfaces have a larger radial distance to the telescope axis, so a larger part of the solid angle is occupied by the cold space reduced specular path from the telescope focal plane via cone baffle via M2 towards the sunshade and the gap between sunshade and M1 (see sketch) |
| --- | --- |

|  | all rays in this plot have an initial direction downwards the cone baffle redirects some of the radiation upwards (of course, the cone in Herschel will not be contiguous) |
| --- | --- |

specular paths:    sunshade(M2(M1-baffle(focal plane

specular paths:   sunshade(M2(cone baffle(focal plane

Results.-> Scattering within SPIRE.

### Thermal filter 1 (PFIL1) is that object which receives the largest irradiation

(within SPIRE within the field of view of the detector).

Thus scattering by this object has the largest effect.

No scattering function was delivered, a tentative calculation with the scattering function for the SPIRE mirrors leads to negligible irradiance onto the detector.

Example (the irradiance onto PFIL1 is 'realistic', not worst case):

| detector irradiance by thermal radiation of telescope mirrors set to | 100 |
| --- | --- |
| thermal irradiance onto PFIL1 | 64 |
| BSDF for scattering by PFIL1 | 0.1/( 1/sr |
| irradiance onto detector | 0.069 |

Thus BSDFs approaching 0.01 may be important, the present BSDFs for SPIRE mirrors are not important. Therefore the following tables do not contain any further scattering function for SPIRE objects.

|  | BSDFs of SPIRE mirrors (670 micrometer) |
| --- | --- |

Results.-> Diffraction within SPIRE.

The backward trace within SPIRE shows that the SPIRE detector can see the edges of

M9   cold stop   M8   (M6)   (M4)   (objects in () only marginally or not at all).

The objects irradiated by strong sources (thermal, moon/earth) are

input edge (FPIN), thermal filter 1 (PFIL1), M3, output edge of the FP_UNIT (FPOUT).

There is no correspondece, so relevant single diffraction paths do not exist (within SPIRE).

For double diffraction the situation is favourable too. The strongly irradiated FPIN-edge can see M4 only marginally (if at all). Radiation from the edges of PFIL1, M3, and FPOUT can see M4. It depends on the reflectivity of the walls of the FP-UNIT how much these objects are irradiated. Double diffraction is expected to play no important role, if the reflectivity is not high.

If the FP_UNIT has significant specular reflection, then the diffraction calculations will be very difficult. Reason: there is a mixture of angles of incidence onto the edges (except the first one), so the angles of diffraction are difficult to select.

These difficulties led us concentrate on the specular paths (up to now) considered more important.

Results.

All results are presented as relative numbers w.r.t. the thermal radiation of the telescope mirrors M1 and M2.

Their contribution has been set to 100 so:

the violation of the 10% thermal emission requirement occurs if the numbers exceed 10.

the violation of the 1% moon/earth requirement occurs if the numbers exceed 1.

The tables shall give an overview on the real situation, so the same temperature has been assumed for telescope, baffles and cryostat.

A worst case assumption has to use a lower temperature for the telescope mirrors and a higher temperature for the other objects. Then all thermal emission cases have to be multiplied by a factor of 1.9 for 80 micrometer wavelength (1.3 for 670 micrometer).

For the sunshade case a multiplication has been done already with a factor of 6.0 allowing for a temperatue 200 K (sunshade) / 80 K (telescope mirrors).

If emitting objects have been considered as grey bodies, then the emissivity ratios are listed.

The tables contain reflectivites of the walls of the SPIRE FP_UNIT of 0.7 and 0.0.

| FLUXES AND IRRADIANCES ONTO SPIRE OBJECTS (SPECULAR REFLECTION) |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| intercepting object |  | FP_UNIT absorbing | FP_UNIT reflecting |
| in SPIRE | area (mm^2) | flux | irradiance | flux | irradiance |
| M1 as emitting object |
| PFIL1 | 5095.4 |  |  | 96.161 | 17.023 |
| DETECTOR | 902.0 | 45.682 | 45.682 | 45.899 | 45.899 |
| M2 as emitting object |
| PFIL1 | 5095.4 |  |  | 102.616 | 18.165 |
| DETECTOR | 902.0 | 54.318 | 54.318 | 54.320 | 54.320 |
| sum on detector |  | 100.000 | 100.000 | 100.219 | 100.219 |

| FLUXES AND IRRADIANCES ONTO SPIRE OBJECTS (SPECULAR REFLECTION) |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| intercepting object |  | FP_UNIT absorbing | FP_UNIT reflecting |
| in SPIRE | area (mm^2) | flux | irradiance | flux | irradiance |
| M1-baffle inner side as object emitting towards -X |  |  |  |  |  |
| FPIN | 10518.0 | 5924.004 | 508.029 | 5924.004 | 508.029 |
| PFIL1 | 5095.4 | 256.151 | 45.345 | 1049.356 | 185.761 |
| M3 | 8636.3 | 151.540 | 15.827 | 572.023 | 59.744 |
| FPOUT | 7619.9 | 115.599 | 13.684 | 305.909 | 36.212 |
| M4+M4-APERTURE | 6031.9 | 117.246 | 17.533 | 118.616 | 17.738 |
| DETECTOR | 902.0 | 0.00E+00 | 0.00E+00 | 0.121 | 0.121 |

| FLUXES AND IRRADIANCES ONTO SPIRE OBJECTS (SPECULAR REFLECTION) |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| intercepting object |  | FP_UNIT absorbing | FP_UNIT reflecting |
| in SPIRE | area (mm^2) | flux | irradiance | flux | irradiance |
| M1-baffle inner side as object emitting towards +X |
| PFIL1 | 5095.4 | 0.082 | 0.015 | 0.088 | 0.016 |
| DETECTOR | 902.0 |  |  | 1.40E-04 | 1.40E-04 |
| M1-baffle flat as object emitting towards +X |
| PFIL1 | 5095.4 | 1.688 | 0.299 | 1.920 | 0.340 |
| DETECTOR | 902.0 | 0.366 | 0.366 | 0.366 | 0.366 |
| grey cone above cryostat emitting towards -X | emissivity ratio w.r.t. M1&M2 | 30.0 |
| FPIN | 10518.0 | 229686.997 | 19697.440 | 229686.997 | 19697.440 |
| PFIL1 | 5095.4 | 10349.949 | 1832.191 | 45982.072 | 8139.937 |
| M4+M4-APERTURE | 6031.9 | 2590.387 | 387.365 | 4170.422 | 623.643 |
| DETECTOR | 902.0 | 0.00E+00 | 0.00E+00 | 19.863 | 19.863 |

| FLUXES AND IRRADIANCES ONTO SPIRE OBJECTS (SPECULAR REFLECTION) |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| intercepting object |  | FP_UNIT absorbing | FP_UNIT reflecting |
| in SPIRE | area (mm^2) | flux | irradiance | flux | irradiance |
| cavity, inner tube, inner surface as emitting object |
| FPIN | 10518.0 | 14820.810 | 1270.999 | 14820.810 | 1270.999 |
| PFIL1 | 5095.4 | 207.253 | 36.689 | 2046.894 | 362.350 |
| M4-APERTURE | 6031.9 |  |  | 118.360 | 17.700 |
| DETECTOR | 902.0 | 0.079 | 0.079 | 9.60E-06 | 9.60E-06 |
| cryostat; grey surfaces as emitting objects | emissivity ratio w.r.t. M1&M2 | 10.0 |
| FPIN | 10518.0 | 112721.70 | 9666.76 | 112721.70 | 9666.76 |
| PFIL1 | 5095.4 | 129.566 | 22.936 | 16625.87 | 2943.18 |
| M4-APERTURE | 6031.9 |  |  | 292.88 | 43.80 |
| DETECTOR | 902.0 | 2.46E-05 | 2.46E-05 | 0.48 | 0.48 |

| FLUXES AND IRRADIANCES ONTO SPIRE OBJECTS (SPECULAR REFLECTION) |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| intercepting object |  | FP_UNIT absorbing | FP_UNIT reflecting |
| in SPIRE | area (mm^2) | flux | irradiance | flux | irradiance |
| sum for configuration with M1-baffle, thermal emission |
| FPIN | 10518.0 | 363153.513 | 31143.228 | 363153.513 | 31143.228 |
| PFIL1 | 5095.4 | 10944.689 | 1937.474 | 66784.016 | 11822.384 |
| M4-APERTURE | 6031.9 | 2707.633 | 404.898 | 4700.276 | 702.877 |
| DETECTOR | 902.0 | 0.445 | 0.445 | 20.834 | 20.834 |
| sum for configuration with M1-baffle without grey cone, thermal emission |
| DETECTOR |  | 0.445 | 0.445 | 0.971 | 0.971 |

| FLUXES AND IRRADIANCES ONTO SPIRE OBJECTS (SPECULAR REFLECTION) |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| intercepting object |  | FP_UNIT absorbing | FP_UNIT reflecting |
| in SPIRE | area (mm^2) | flux | irradiance | flux | irradiance |
| conebaffle as object emitting towards -X |
| FPIN | 10518.0 | 12232.73 | 1049.051 | 12232.73 | 1049.051 |
| PFIL1 | 5095.4 | 129.880 | 22.992 | 1772.678 | 313.807 |
| M4-APERTURE | 6031.9 |  |  | 18.297 | 2.736 |
| DETECTOR | 902.0 | 8.34E-06 | 8.34E-06 | 0.336 | 0.336 |
| conebaffle as object emitting towards +X |
| PFIL1 | 5095.4 |  |  |  |  |
| DETECTOR | 902.0 |  |  | 0.235 | 0.235 |

| FLUXES AND IRRADIANCES ONTO SPIRE OBJECTS (SPECULAR REFLECTION) |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| intercepting object |  | FP_UNIT absorbing | FP_UNIT reflecting |
| in SPIRE | area (mm^2) | flux | irradiance | flux | irradiance |
| cryostat; grey surfaces as emitting objects (copied from case M1-baffle) | emissivity ratio w.r.t. M1&M2 | 10.0 |
| FPIN | 10518.0 | 112721.70 | 9666.76 | 112721.70 | 9666.76 |
| PFIL1 | 5095.4 | 129.566 | 22.936 | 16625.87 | 2943.18 |
| M4-APERTURE | 6031.9 |  |  | 292.88 | 43.80 |
| DETECTOR | 902.0 | 2.46E-05 | 2.46E-05 | 0.48 | 0.48 |
| sum for cone configuration, thermal emission |
| FPIN | 10518.0 | 124954.433 | 10715.811 | 124954.433 | 10715.811 |
| PFIL1 | 5095.4 | 259.446 | 45.928 | 18398.549 | 3256.987 |
| DETECTOR | 902.0 | 0.000 | 0.000 | 1.056 | 1.056 |

| FLUXES AND IRRADIANCES ONTO SPIRE OBJECTS (SPECULAR REFLECTION) |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| intercepting object |  | FP_UNIT absorbing | FP_UNIT reflecting |
| in SPIRE | area (mm^2) | flux | irradiance | flux | irradiance |
| moon at 13 degrees (M1-baffle) |
| PFIL1 | 5095.4 |  |  | 694.861 | 123.007 |
| DETECTOR | 902.0 |  |  | 0.006 | 0.006 |
| earth at 23 degrees (M1-baffle) |
| PFIL1 | 5095.4 |  |  | 1781.820 | 315.425 |
| DETECTOR | 902.0 |  |  | 0.029 | 0.029 |

detector results preliminary: leak for specular rays detected (a few rays were transferred through a wall in SPIRE), thus detector results too large; investigation planned

| FLUXES AND IRRADIANCES ONTO SPIRE OBJECTS (SPECULAR REFLECTION) |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| intercepting object |  | FP_UNIT absorbing | FP_UNIT reflecting |
| in SPIRE | area (mm^2) | flux | irradiance | flux | irradiance |
| moon at 13 degrees, conebaffle |  |  |  |  |  |
| PFIL1 | 5095.4 |  |  | 782.927 | 138.597 |
| DETECTOR | 902.0 |  |  | 0.001 | 0.001 |
| earth at 23 degrees, conebaffle |  |  |  |  |  |
| PFIL1 | 5095.4 |  |  | 32053.630 | 5674.267 |
| DETECTOR | 902.0 |  |  | 0.004 | 0.004 |

detector results preliminary: leak for specular rays detected (a few rays were transferred through a wall in SPIRE), thus detector results too large; investigation planned

Summary on the tables with straylight results.

The cone baffle shows less thermal impact into the experiments than the present M1-baffle+cryostat baffle (although also a cylindrical baffle could be optimized).

The disadvantage of the cone baffle w.r.t moon/earth has to be weighted with the advantage w.r.t thermal emission.

The experiments should avoid reflecting internal walls as far as possible.

Further cases to be calculated (sunshade, CVV, radiations shields; PACS).

Some 'leaks' may have lead to an overestimation of certain straylight results, reason for leaks to be found.