| Tipo Doc.: Doc.Type: | REPORT SPIRE-CGS-REP-001294 | N° DRD: DRD N°: | N.A. |
| --- | --- | --- | --- |
| N° Doc.: Doc. N°: | DPU-RP-CGS-031 | Ediz.: Issue: | 1 | Data: Date: | 24/04/2002 | Pagina Page | 1 | Di Of | 71 |
| Titolo : Title : | EM DC/DC CONVERTER BOARD (SPIRE VERSION) P/N DPU-EM-300.00-0 S/N 03 ELECTRICAL AND FUNCTIONAL TEST REPORT |

|  | Nome & Funzione Name & Function | Firma Signature | Data Date |  | LISTA DI DISTRIBUZIONE DISTRIBUTION LIST | N | A | I |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Preparato da: Prepared by: | FIRST-DPU TEAM |  |  |  | Interna / Internal |  |  |  |
|  |  |  |  |  | Francini E. (PA/QA) Sciortino A. (DT/EE) Longoni A. (DP/PL) Vucetich L. (DT/EE) | 1 1 1 1 | X X X X |  |
| Approvato da: Approved by: | Francini E. (PA/QA) Di Gioia L. (PC/CC) Sciortino A. (DT/EE) |  |  |  |  |  |  |  |
| Applicazione autorizzata da: Application authorized by: | Longoni A. (DP/PL) |  |  |  | Esterna / External |  |  |  |
|  |  |  |  |  | Orfei R. (CNR-IFSI) | 1 | X |  |
| Customer / Higher Level Contractor |  |  |  |  |  |
| Accettato da: Accepted by: |  |  |  |  |  |  |  |  |
| Approvato da: Approved by: |  |  |  |  |  |  |  |  |
|  |  |  |  |  | N=Numero di copie A=Applicazione I=Informazione N=Number of copy A=Application I=Information |

| Gestione documenti: Data Management: |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | Firma / Signature Data / Date |  | File: | DPU-RP-CGS-031_Is1.doc |

| REGISTRAZIONE DELLE MODIFICHE / CHANGE RECORD |
| --- |
| EDIZIONE ISSUE | DATA DATE | AUTORIZZAZIONE CHANGE AUTHORITY | OGGETTO DELLA MODIFICA E SEZIONI AFFETTE REASON FOR CHANGE AND AFFECTED SECTIONS |
| 1 | 24/04/2002 |  |  |

| LISTA DELLE PAGINE VALIDE / LIST OF VALID PAGES |
| --- |
| PAGINA PAGE | EDIZIONE ISSUE | PAGINA PAGE | EDIZIONE ISSUE | PAGINA PAGE | EDIZIONE ISSUE | PAGINA PAGE | EDIZIONE ISSUE | PAGINA PAGE | EDIZIONE ISSUE |
| 1 - 71 | 1 |  |  |  |  |  |  |  |  |

TABLE OF CONTENT

1.	SCOPE	6

2.	documents	7

2.1	applicable documents	7

2.2	reference documents	7

3.	acronyms	8

4.	participants required	9

4.1	general	9

4.2	responsibility	9

4.3	qa witness of test and sign-off	9

4.4	Non conformance and failures	9

4.5	calibration requirements	9

5.	test article	10

5.1	description	10

5.1.1	pin function	11

5.2	test matrix	14

6.	test configuration	15

6.1	requirements cross reference	15

6.2	tests applicability	15

7.	INSTRUMENTATION AND TEST EQUIPMENT	16

8.	test condition	18

9.	Test data sheets	18

9.1	data sheets filling up	18

ISOLATION VERIFICATION	21

10.	test procedure variation sheets	50

PROCEDURE VARIATION SHEET     ref. N°: 01	50

PROCEDURE VARIATION SHEET     ref. N°: 02	51

PROCEDURE VARIATION SHEET     ref. N°: 03	52

11.	ANNEX TO THE PROCEDURE	53

11.1	ANNEX 1: Test set up for input impedance measurement	53

11.2	ANNEX 2: POWER BUS IMPEDANCE	54

11.3	ANNEX 3: TEST SET UP FOR CONDUCED EMISSION FREQUENCY DOMAIN DM	55

11.4	ANNEX 4: LIMIT FOR CEP-DIFFERENTIAL MODE	56

11.5	ANNEX 5: TEST SET UP FOR CONDUCED EMISSION FREQUENCY DOMAIN CM	57

11.6	ANNEX 6: NB CE POWER LINES-COMMON MODE	58

11.7	ANNEX 7: TEST SET UP FOR CONDUCED EMISSION TIME DOMAIN	59

11.8	ANNEX 8  Inrush current 26v  (f5.9)	60

11.9	annex 9  inrusch current 29v ( f5.5)	61

11.10	annex 10  input impedance  (f6.3)	62

11.11	annex 11  ce input power line d.m.   ambient noise  (f12.3)	63

11.12	annex 12  ce input power line d.m.   positive line  (f12.4)	64

11.13	annex 13  ce input power line d.m. negative line ambient noise (f12.7)	65

11.14	annex 14  ce input power line d.m.   negative line  (f12.8)	66

11.15	annex 15  ce input power line c.m.   ambient noise  (f13.3)	67

11.16	annex 16 ce input power line c.m.     (f13.4)	68

11.17	annex 17  current ripple positive input power line (f14.4)	69

11.18	annex 18  current ripple return input power line (f14.6)	70

10mA/div	70

12.	conclusions	71

LIST OF TABLES

Tab. 5-1 DC-DC Converter board: P1 pin function	12

Tab. 5-2 DC-DC Converter board: P2 pin function	13

Tab. 5-3 TEST MATRIX	14

Tab. 6-1 REQUIREMENTS CROSS REFERENCE	15

Tab. 7-1 INSTRUMENT LIST	17

LIST OF FIGURES

Fig. 5-1 DC/DC Board functional diagram (“DPU+PL version”)	11

# SCOPE

The aim of the present document is to provide a detailed test report of EM DC/DC BOARD P/N DPU-EM-300.00-0 S/N 03 (SPIRE version) to be used to supply the Data Processing Units (DPU version) developed in the framework of the HSO/FIRST program.

The test to be performed according to the Test Procedure [AD 6] are to demonstrate the compliance of the above item to the requirements specified in the applicable document as part of the overall verification program.

For the “DPU version” of the DC/DC converter board, only test  applicable to “DPU version” must be considered.

# documents

## applicable documents

[AD1]:	CNR.IFSI.2000TR01 "Documento di Specifiche Tecniche per il Contratto delle Data Processing Units del Satellite First dell'ESA"    IFSI (Issue: 1 - 15/09/2000)

[AD2]:	Technical proposal CGS (Ref. S9-030 November 99)

[AD3]:	“Allegato Tecnico al Contratto ASI"

[AD4]:	 Product Assurance Plan for the FIRST DPU (DPU-PL-CGS-001 Issue 1 Jan. 2001)

[AD5]:	DC/DC Board Specification DPU-SP-CGS-004-Iussue 1 dated May 21st 2001

[AD6]:	EM/QM/FM DC/DC Converter Board Electrical and Functional Test Procedure DPU-PR-CGS-003-Issue 1 dated Feb. 04st 2002

## reference documents

[RD1] - 	FIRST/Planck Instrument Interface Document Part A. (Ref. SCI-PT-IIDA-04624 Issue-Rev. No. : 1/1)

[RD2] - 	FIRST/Planck Instrument Interface Document Part B - Instrument “HIFI” (Ref. SCI-PT-IIDB/HIFI-02125 Issue-Rev No. : 1/0)

# acronyms

| AD | Applicable Document Number |
| --- | --- |
| BB | Broadband |
| CE | Conducted Emission |
| C.I. | Configuration Item. Also called Part Number (P/N) |
| CGS | Carlo Gavazzi Space |
| CS | Conducted Susceptibility |
| DPU | Data Processing Unit |
| EMC | Electro-Magnetic Compatibility |
| EMI | Electro-Magnetic Interference |
| FIRST | Far Infra-Red and Sub-millimeter Telescope |
| FPU | Focal Plane Unit |
| FCU | Focal Control Unit |
| GND | Ground |
| HIFI | Heterodyne Instrument for First |
| HK | House Keeping |
| ICD | Interface Control Document |
| ICU | Instrument Control Unit |
| IID | Instrument Interface Document |
| I/F | Interface |
| LCL | Latching Current Limiter |
| NA | Not Applicable |
| NB | Narrowband |
| OCP | Over-Current Protection |
| OVP | Over-Voltage Protection |
| P/N | Part Number. Also called Configuration Item C.I. |
| PA | Product Assurance |
| PACS | Photoconductor Array Camera and Spectrometer |
| PDU | Power Distribution Unit |
| PL | Payload |
| PVS | Procedure Variation Sheet |
| QA | Quality Assurance |
| RD# | Reference Document Number |
| RE | Radiated Emission |
| RS | Radiated Susceptibility |
| RTN | Return Line |
| S/C | Spacecraft |
| S/N | Serial Number |
| SPIRE | Spectral and Photometric Imaging receiver |
| TBC | To Be Confirmed |
| TBD | To Be Determined |
| TM/TC | Telemetry & Tele-command |
| uut | Unit Under Test |

# participants required

## general

All test will be performed under QA surveillance in accordance with, and following detailed procedure of applicable PA Plan. Start of the Test shall be notified to Prime Contractor and/or Customer as applicable.

## responsibility

The technical responsibility for testing and test results is up to the Engineering department.

QA is responsible for ensuring that all the agreed procedures are carefully observed, that test equipment and instrumentation used during testing is calibrated and within validity date: that the test data sheets are recorded in the Test Report and signed by the operators and QA witnesses, that all non conforming condition and test results are properly documented and notified to the Prime Contractor, and that all requirements of applicable PA Plan, specification and Statement of Work pertaining to the acceptance tests, are fully satisfied.

## qa witness of test and sign-off

QA inspector, or its delegate, shall witness the tests described in this procedure in accordance to the requirement specified in the applicable PA Plans.

## Non conformance and failures

Any malfunction/defect which occurs during the test will be processed along the Non Conformance Procedure described in the applicable PA Plans.

## calibration requirements

All instruments used for testing shall be calibrated.

Evidence of certification shall be provided by a label attached to the instruments itself, showing the calibration date, the expiring date and the signature of the operator.

# test article

The test article consists as in following table:

| Item | Model | Remarks | P/N | S/N |
| --- | --- | --- | --- | --- |
| DC/DC converter SPIRE | EM | DPU Version | DPU-EM-300.00-0 | 03 |

Before starting the test, the P/N and S/N of the test article(s) to be tested shall be recorded on the step-by-step procedure sheets under the table cell “UNIT UNDER TEST”.

## description

The DC/DC board (Push-Pull topologies) must provide a set of supply voltages for to the DPU internal electronics of the payload experiments HIFI, PACS and SPIRE. For the payload experiment HIFI only, the DC/DC board must provide a further external set of supply voltages for the HIFI/FCU unit.

Therefore the board must provide, considering the DPU+PL version, the following two sets of output voltages:

- “DPU-Outputs” to supply the DPU internal electronics

- “PL-Outputs” to supply the payload instrument HIFI/FCU unit.

In the DPU version only the DPU-Outputs shall be provided.

DPU-Outputs and PL-Outputs shall be isolated from primary power side and from each other ( except for DPU RTN output that are connected together at board side) as described in [AD5].

The DC/DC board shall switch on automatically when the input voltage is within the range established in [AD5].

Fig. 5-1 DC/DC Board functional diagram (“DPU+PL version”)

### pin function

In the following tables the pin function of the board is reported

| Pin # | Signal | Pin # | Signal | Pin # | Signal |
| --- | --- | --- | --- | --- | --- |
| 1 | +5VD | 33 | +5VD | 65 | +5VCORE |
| 2 | +VEEPROM | 34 | +2.5VFPGA | 66 | +5VCORE |
| 3 | +VFIFO | 35 | +5VBU61582 | 67 | NOT USED |
| 4 | NOT USED | 36 | +VIFMEZZ | 68 | NOT USED |
| 5 | NOT USED | 37 | NOT USED | 69 | NOT USED |
| 6 | NOT USED | 38 | NOT USED | 70 | NOT USED |
| 7 | NOT USED | 39 | NOT USED | 71 | NOT USED |
| 8 | NOT USED | 40 | NOT USED | 72 | NOT USED |
| 9 | NOT USED | 41 | NOT USED | 73 | NOT USED |
| 10 | NOT USED | 42 | NOT USED | 74 | NOT USED |
| 11 | NOT USED | 43 | NOT USED | 75 | NOT USED |
| 12 | NOT USED | 44 | NOT USED | 76 | NOT USED |
| 13 | NOT USED | 45 | NOT USED | 77 | NOT USED |
| 14 | NOT USED | 46 | NOT USED | 78 | NOT USED |
| 15 | NOT USED | 47 | NOT USED | 79 | NOT USED |
| 16 | NOT USED | 48 | NOT USED | 80 | NOT USED |
| 17 | DGND | 49 | NOT USED | 81 | DGND |
| 18 | BONDING | 50 | BONDING | 82 | BONDING |
| 19 | BONDING | 51 | BONDING | 83 | BONDING |
| 20 | NOT USED | 52 | NOT USED | 84 | NOT USED |
| 21 | NOT USED | 53 | NOT USED | 85 | NOT USED |
| 22 | NOT USED | 54 | NOT USED | 86 | NOT USED |
| 23 | NOT USED | 55 | NOT USED | 87 | NOT USED |
| 24 | NOT USED | 56 | NOT USED | 88 | NOT USED |
| 25 | NOT USED | 57 | NOT USED | 89 | NOT USED |
| 26 | NOT USED | 58 | NOT USED | 90 | NOT USED |
| 27 | NOT USED | 59 | NOT USED | 91 | NOT USED |
| 28 | NOT USED | 60 | NOT USED | 92 | NOT USED |
| 29 | -15VA | 61 | -15VA | 93 | -15VA |
| 30 | AGND | 62 | AGND | 94 | AGND |
| 31 | +15VA | 63 | +15VA | 95 | +15VA |
| 32 | DGND | 64 | DGND | 96 | DGND |

Tab. 5-1 DC-DC Converter board: P1 pin function

| Pin # | Signal | Pin # | Signal | Pin # | Signal |
| --- | --- | --- | --- | --- | --- |
| 1 | +28V | 33 | +28V | 65 | +28V |
| 2 | NOT USED | 34 | NOT USED | 66 | NOT USED |
| 3 | +28V_RTN | 35 | +28V_RTN | 67 | +28V_RTN |
| 4 | NOT USED | 36 | NOT USED | 68 | NOT USED |
| 5 | SYNCH_MAIN+ | 37 | SYNCH_MAIN+ | 69 | SYNCH_MAIN+ |
| 6 | SYNCH_MAIN- | 38 | SYNCH_MAIN- | 70 | SYNCH_MAIN- |
| 7 | SYNCH_RED+ | 39 | SYNCH_RED+ | 71 | SYNCH_RED+ |
| 8 | SYNCH_RED- | 40 | SYNCH_RED- | 72 | SYNCH_RED- |
| 9 | NOT USED | 41 | NOT USED | 73 | NOT USED |
| 10 | INCUR_MNT | 42 | +5V_MNT | 74 | +15V_ MNT |
| 11 | RTN_MNT0 | 43 | RTN_MNT1 | 75 | RTN_MNT2 |
| 12 | -15V_MNT | 44 | +TEMP_MNT | 76 | AINP5 |
| 13 | RTN_MNT3 | 45 | RTN_MNT4 | 77 | RTN_MNT5 |
| 14 | AINP6 | 46 | NOT USED | 78 | NOT USED |
| 15 | RTN_MNT6 | 47 | AGND | 79 | AGND |
| 16 | NOT USED | 48 | NOT USED | 80 | NOT USED |
| 17 | NOT USED | 49 | NOT USED | 81 | NOT USED |
| 18 | NOT USED | 50 | NOT USED | 82 | NOT USED |
| 19 | NOT USED | 51 | NOT USED | 83 | NOT USED |
| 20 | NOT USED | 52 | NOT USED | 84 | NOT USED |
| 21 | NOT USED | 53 | NOT USED | 85 | NOT USED |
| 22 | +16V_PL_OUT | 54 | +16V_PL_OUT | 86 | +16V_PL_OUT |
| 23 | -16V_PL_OUT | 55 | -16V_PL_OUT | 87 | -16V_PL_OUT |
| 24 | ±16V_PL_RTN | 56 | ±16V_PL_RTN | 88 | ±16V_PL_RTN |
| 25 | +5.6V_PL_OUT | 57 | +5.6V_PL_OUT | 89 | +5.6V_PL_OUT |
| 26 | +5.6V_PL_RTN | 58 | +5.6V_PL_RTN | 90 | +5.6V_PL_RTN |
| 27 | +18V_PL_OUT | 59 | +18V_PL_OUT | 91 | +18V_PL_OUT |
| 28 | -18V_PL_OUT | 60 | -18V_PL_OUT | 92 | -18V_PL_OUT |
| 29 | ±18V_PL_RTN | 61 | ±18V_PL_RTN | 93 | ±18V_PL_RTN |
| 30 | +8V_PL_OUT | 62 | +8V_PL_OUT | 94 | +8V_PL_OUT |
| 31 | +8V_PL_RTN | 63 | +8V_PL_RTN | 95 | +8V_PL_RTN |
| 32 | NOT USED | 64 | NOT USED | 96 | NOT USED |

Tab. 5-2 DC-DC Converter board: P2 pin function

## test matrix

This procedure is applicable to EM, QM and FM models according to the following test matrix.

- Electrical procedure (E)

- Functional procedure (F)

| Procedure Step | TEST | EM | QM | FM |
| --- | --- | --- | --- | --- |
| E1 | Isolation verification | X | X | X |
| E2 | Minimum loads and DC/DC internal power consumption during shut-down | X | X | X |
| E3 | Switching Frequency | X | X | X |
| F1 | Output voltage regulation-Load regulation | X | X | X |
| F2 | Output voltage regulation-Line regulation | X | X | X |
| F3 | Ripple and Spikes | X | X | X |
| F4 | Efficiency and power consumption | X | X | X |
| F5 | Inrush Current | X | X | X |
| F6 | Input Impedance | X |  |  |
| F7 | Input protection | X | X | X |
| F8 | DPU Output protections | X | X | X |
| F9 | Regulated PL Outputs Protections | X | X | X |
| F10 | Voltage monitors | X | X | X |
| F11 | Temperature monitor | X | X | X |
| F12 | CE on Input Power Line; Frequency Domain, Differential Mode, NB | X | X |  |
| F13 | CE on Input Power Line; Frequency Domain, Common Mode, NB | X | X |  |
| F14 | Current Ripple, Time Domain, Differential Mode | X | X |  |

Tab. 5-3 TEST MATRIX

# test configuration

Test set up are described in the step-by-step procedure sheets provided in § 11.

## requirements cross reference

Cross reference among requirements and procedure steps is provided in table 6.-1

Tab. 6-1 REQUIREMENTS CROSS REFERENCE

| REQ. n° (of DPU-SP-CGS-004 Is_1) | CGS SPEC. | PROCEDURE STEP | REMARKS |
| --- | --- | --- | --- |
| Paragraph 9.1 | DPU-SP-CGS-004 Issue1 | E1 |  |
| Paragraph 9.2 | DPU-SP-CGS-004 Issue1 | E1 |  |
| Paragraph 9.3 | DPU-SP-CGS-004 Issue1 | E1 |  |
| Paragraph 7.1 | DPU-SP-CGS-004 Issue1 | F1, F2, F3 |  |
| Paragraph 7.2.1 | DPU-SP-CGS-004 Issue1 | F1, F2, F3 |  |
| Paragraph 7.2.2 | DPU-SP-CGS-004 Issue1 | F1, F2, F3 |  |
| Chapter 7. | DPU-SP-CGS-004 Issue1 | F4 |  |
| Paragraph 8.2 | DPU-SP-CGS-004 Issue1 | F5 |  |
| Paragraph 8.1.4 | DPU-SP-CGS-004 Issue1 | F6 |  |
| Paragraph 8.4 | DPU-SP-CGS-004 Issue1 | F7 |  |
| Paragraph 7.1.1 | DPU-SP-CGS-004 Issue1 | F8 |  |
| Paragraph 7.2.1.1 | DPU-SP-CGS-004 Issue1 | F9 |  |
| Paragraph 8.5 | DPU-SP-CGS-004 Issue1 | F10, F11 |  |
| Paragraph 10.1.1 | DPU-SP-CGS-004 Issue1 | F12 |  |
| Paragraph 10.1.2 | DPU-SP-CGS-004 Issue1 | F13 |  |
| Paragraph 10.1.3 | DPU-SP-CGS-004 Issue1 | F14 |  |

## tests applicability

| Item | Applicable Tests |
| --- | --- |
| DC/DC converter SPIRE | E1;E2;E3;F1;F2:F3;F4;F5;F6;F7;F8;F10;F11;F12;F13 |
| DC/DC converter HIFI | E1;E2;E3;F1;F2:F3;F4;F5;F6;F7;F8;F9;F10;F11;F12;F13 |
| DC/DC converter PACS | E1;E2;E3;F1;F2:F3;F4;F5;F6;F7;F8;F10;F11;F12;F13 |

# INSTRUMENTATION AND TEST EQUIPMENT

The complete list of the instrumentation used during the test shall be recorded in table 7.-1.

The list shall be filled up during tests and reported in Test Report.

Tab. 7-1 INSTRUMENT LIST

| N. | EQUIPMENT | MANUFACTURER | P/N | S/N | NEXT CAL. DATE | REMARKS |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Multimeter | Fluke | 45 | 5415119 | 17/04/2002 |  |
| 2 | Multimeter | Hewlett Packard | 34401A | 3146A12807 | 17/04/2002 |  |
| 3 | Current probe | Tektronix | TM502A | B022557 | 17/04/2002 |  |
| 4 | Current probe amplifier | Tektronix | AM503 | B047991 | 17/04/2002 |  |
| 5 | Oscilloscope | Tektronix | TDS224 | B020221 | 17/04/2002 |  |
| 6 | Dual power supply | B.A.S. | 6303A | 998090 |  |  |

# test condition

- The CI shall be tested in its defined configuration: all electrical loads shall be present and the CI interface function(s) shall be simulated.

- Unless otherwise specified, all measurements are to be performed at the following ambient condition:

| Temperature | 25 °C +/- 3°C |
| --- | --- |
| Relative humidity | between 30 % and 60 % RH |
| Pressure | Ambient |
| Cleanliness | 100000 class |

- All tests, unless otherwise specified, shall be performed internally to CGS laboratories in a proper area. General disposition shall be applied to maximize personnel safety from potential hazards

- Connectors savers shall be used on FM/QM model as applicable to protect the UUT interface connectors.

- Skilled personnel shall be employed

- All used instruments shall meet the necessary accuracy and shall not degrade the UUT performances.

# Test data sheets

The step-by-step procedure sheets are provided in the following pages.

## data sheets filling up

The following fields of the data sheets:

- UUT DATA (including Model, Item, C.I., S/N)

- Measured value

shall be filled up during the test performances and shall be part of the Test Report together with photographs, sketches, etc. eventually useful to document the test execution/result.

Remarks field shall be used as a minimum to provide,  where appropriate,  reference to NCRs and PVS.

Test Report reference data shall be added in the relevant field.

Each data sheet (including the attachments) shall be certified by QA stamp and signature together with the Test Conductor signature and date.

This page is intentionally left blank.

This page is intentionally left blank.

| E1 | ISOLATION VERIFICATION |  |  | If the board under test is a “DPU Version”, only the DPU pins are object of this test. |
| --- | --- | --- | --- | --- |
|  | The board shall be in OFF condition, disconnected from any cable or test equipment and placed on an insulated table. | OK | OK | OBJECTIVE: Verification of isolation between each output power return line and between power return lines and chassis. |
| E1.1 | Verify that DC isolation between each outputs power return lines is higher than 1M( (except for DPU output return lines that are tied together at board level) | OK | OK |  |
| E1.2 | Verify that DC isolation between each outputs power return line and bonding pins is higher than 1M( | OK | OK |  |
| E1.3 | Verify that DC isolation between each output power return lines and input return line is higher than 1M( | OK | OK |  |
| E1.4 | Verify that AC isolation between each output power return lines and bonding pins is lower than 50nF | OK | OK |  |
| E1.5 | Verify that AC isolation between each output power return lines and input line is lower than 5nF | OK | OK |  |
| E1.6 | Verify that DC isolation between input power return line and chassis is higher than 1M( shunted by no more than 5nF | OK | OK |  |

| E2 | Minimum loads and DC/DC internal power consumption during shut-down |  |  | OBJECTIVE: Verification of power consumption |
| --- | --- | --- | --- | --- |
|  |  |  |  | INSTRUMENTATION: Power supply Voltmeter and Ammeter. |
| E2.1 | Power the board through the input connectors at 26V (Ilimit=1A) with minimum loads connected as for table below |  |  |  |
| E2.2 | Output Voltage (V) Min Current (mA) DPU Electronic +5 1000 DPU Electronic +15 0 DPU Electronic -15 0 DPU Electronic +2,5 0 HIFI 5,6 0 HIFI 16 0 HIFI -16 0 HIFI 8 0 HIFI 18 0 HIFI -18 0 Measure the value of current absorbed by the board | <0.5A | 0.355A |  |
| E2.3 | Power the board through the input connectors at 28V with minimum loads connected |  |  |  |
| E2.4 | Measure the value of current absorbed by the board | <0.5A | 0.337A |  |
| E2.5 | Power the board through the input connectors at 29V with minimum loads connected |  |  |  |
| E2.6 | Measure the value of current absorbed by the board | <0.5A | 0.329A |  |
| E.2.7 | Decrease the input voltage until the UV protection is reached (at about 24V the DC/DC converter shut-down) |  |  |  |
| E.2.8 | Measure the input power consumption and report the value. | < 1W < 2,8W | 0.736W N.A. | DPU Version DPU+PL Version |

| E3 | SWITCHING FREQUENCY |  |  | OBJECTIVE: Verification of switching frequency |
| --- | --- | --- | --- | --- |
|  |  |  |  | INSTRUMENTATION: Oscilloscope |
| E3.1 | Connect an oscilloscope probe between, gate and source dedicated test points of Q9.(DPU section) |  |  |  |
| E3.2 | Measure the frequency of the driving signal and verify that the frequency is within the expected value | 55kHz ( 10% | 54.95KHz |  |
| E3.3 | Connect an oscilloscope probe between gate and source dedicated test points of Q10. .(DPU section) |  |  |  |
| E3.4 E3.3 | Measure the frequency of the driving signal and verify that the frequency is within the expected value Measure the time between Gate rise edge of MOSFETs Q9 and Q10 and verify that the corresponding frequency is within the expected value. .(DPU section) Connect an oscilloscope probe between gate and source dedicated test points of Q7.(PL section) | 55kHz ( 10% 110KHz ( 10% | 54.95KHz 111.1 KHz |  |
| E3.4 | Measure the frequency of the diving signal and verify that the frequency is within the expected value | 55Hz ( 10% | N.A. | Only DPU+PL Version |
|  | Connect an oscilloscope probe between gate and source dedicated test points of Q8.(PL section) Measure the frequency of the diving signal and verify that the frequency is within the expected value Measure the time between Gate rise edge of MOSFETs Q7 and Q8 and verify that the corresponding frequency is within the expected value. .(PL section) | 55kHz ( 10% 110KHz ( 10% | N.A. N.A. | Only DPU+PL Version |
| E3.5 | Verify that the switching frequency of DPU and PL are synchronized | OK | N.A. | Only DPU+PL Version |
| F1 | OUTPUT VOLTAGE REGULATION/LOAD REGULATION |  |  | OBJECTIVE: Verify output voltage regulation with different load conditions |
|  | UUT must be powered at 28Vin and load condition as in the following table: Output Voltage (V) Min Current (mA) Max Current (mA) DPU Electronic +5 1000 3.500 DPU Electronic +15 0 100 DPU Electronic -15 0 250 DPU Electronic +2,5 0 200 HIFI 5,6 0 240 HIFI 16 0 190 HIFI -16 0 150 HIFI 8 0 350 HIFI 18 0 330 HIFI -18 0 230 |  |  |  |
|  |  |  |  | INSTRUMENTATION: Voltmeter, Ammeter |
| F1.1 | Set the outlet +5VD at Imax |  |  |  |
| F1.2 | Set the other outlets at Imin |  |  |  |
| F1.3 | Measure voltage across outlet +5VD (DPU) | Vmin = 4.75V Vmax = 5.25V | 4.98V |  |
| F1.4 | Set the outlet +5VD at Imin |  |  |  |
| F1.5 | Set the other outlets at Imax |  |  |  |
| F1.6 | Measure voltage across outlet +5VD(DPU) | Vmin = 4.75V Vmax = 5.25V | 5.01V |  |
| F1.7 | Set the outlet +15VA at Imax |  |  |  |
| F1.8 | Set the other outlets at Imin |  |  |  |
| F1.9 | Measure voltage across outlet +15VA (DPU) | Vmin = 14.25V Vmax = 15.75V | 15.028V |  |
| F1.10 | Set the outlet +15VA at Imin |  |  |  |
| F1.11 | Set the other outlets at Imax |  |  |  |
| F1.12 | Measure voltage across outlet +15VA (DPU) | Vmin = 14.25V Vmax = 15.75V | 15.040V |  |
| F1.13 | Set the outlet -15VA at Imax |  |  |  |
| F1.14 | Set the other outlets at Imin |  |  |  |
| F1.15 | Measure voltage across outlet -15VA (DPU) | Vmin = -15.75V Vmax = -14.25V | -15.130V |  |
| F1.16 | Set the outlet -15VA at Imin |  |  |  |
| F1.17 | Set the other outlets at Imax |  |  |  |
| F1.18 | Measure voltage across outlet -15VA(DPU) | Vmin = -15.75V Vmax = -14.25V | -15.183V |  |
| F1.19 | Set the outlet +2.5VFPGA at Imax |  |  |  |
| F1.20 | Set the other outlets at Imin |  |  |  |
| F1.21 | Measure voltage across outlet +2.5VFPGA(DPU) | Vmin = 2.375V Vmax = 2.625V | 2.483V |  |
| F1.22 | Set the outlet +2.5VFPGA at Imin |  |  |  |
| F1.23 | Set the other outlets at Imax |  |  |  |
| F1.24 | Measure voltage across outlet +2.5VFPGA (DPU) | Vmin = 2.375V Vmax = 2.625V | 2.484V |  |
| F1.25 | Set the outlet +5.6V_PL_OUT at Imax |  |  |  |
| F1.26 | Set the other outlets at Imin |  |  |  |
| F1.27 | Measure voltage across outlet +5.6V_PL_OUT | Vmin = 5.5V Vmax = 5.8V | N.A. | Only DPU+PL Version |
| F1.28 | Set the outlet +5.6V_PL_OUT at Imin |  |  |  |
| F1.29 | Set the other outlets at Imax |  |  |  |
| F1.30 | Measure voltage across outlet +5.6V_PL_OUT | Vmin = 5.5V Vmax = 5.8V | N.A. | Only DPU+PL Version |
| F1.31 | Set the outlet +16V_PL_OUT at Imax |  |  |  |
| F1.32 | Set the other outlets at Imin |  |  |  |
| F1.33 | Measure voltage across outlet +16V_PL_OUT | Vmin = +15.6V Vmax = +16.4V | N.A. | Only DPU+PL Version |
| F1.34 | Set the outlet +16V_PL_OUT at Imin |  |  |  |
| F1.35 | Set the other outlets at Imax |  |  |  |
| F1.36 | Measure voltage across outlet +16V_PL_OUT | Vmin = +15.6V Vmax = +16.4V | N.A. | Only DPU+PL Version |
| F1.37 | Set the outlet -16V_PL_OUT at Imax |  |  |  |
| F1.38 | Set the other outlets at Imin |  |  |  |
| F1.39 | Measure voltage across outlet -16V_PL_OUT | Vmin = -16.4V Vmax = -15.6V | N.A. | Only DPU+PL Version |
| F1.40 | Set the outlet -16V_PL_OUT at Imin |  |  |  |
| F1.41 | Set the other outlets at Imax |  |  |  |
| F1.42 | Measure voltage across outlet -16V_PL_OUT | Vmin = -16.4V Vmax = -15.6V | N.A. | Only DPU+PL Version |
| F1.43 | Set the outlet +8V_PL_OUT at Imax |  |  |  |
| F1.44 | Set the other outlets at Imin |  |  |  |
| F1.45 | Measure voltage across outlet +8V_PL_OUT | Vmin = +7V Vmax = +9V | N.A. | Only DPU+PL Version |
| F1.46 | Set the outlet +8V_PL_OUT at Imin |  |  |  |
| F1.47 | Set the other outlets at Imax |  |  |  |
| F1.48 | Measure voltage across outlet +8V_PL_OUT | Vmin = +7V Vmax = +9V | N.A. | Only DPU+PL Version |
| F1.49 | Set the outlet +18V_PL_OUT at Imax |  |  |  |
| F1.50 | Set the other outlets at Imin |  |  |  |
| F1.51 | Measure voltage across outlet +18V_PL_OUT | Vmin = +17V Vmax = +20V | N.A. | Only DPU+PL Version |
| F1.52 | Set the outlet +18V_PL_OUT at Imin |  |  |  |
| F1.53 | Set the other outlets at Imax |  |  |  |
| F1.54 | Measure voltage across outlet +18V_PL_OUT | Vmin = +17V Vmax = +20V | N.A. | Only DPU+PL Version |
| F1.55 | Set the outlet -18V_PL_OUT at Imax |  |  |  |
| F1.56 | Set the other outlets at Imin |  |  |  |
| F1.57 | Measure voltage across outlet -18V_PL_OUT | Vmin = -17V Vmax = -20V | N.A. | Only DPU+PL Version |
| F1.58 | Set the outlet -18V_PL_OUT at Imin |  |  |  |
| F1.59 | Set the other outlets at Imax |  |  |  |
| F1.60 | Measure voltage across outlet -18V_PL_OUT | Vmin = -17V Vmax = -20V | N.A. | Only DPU+PL Version |

| F2 | OUTPUT VOLTAGE REGULATION/LINE REGULATION |  |  | OBJECTIVE: Verify output voltage regulation with different line conditions |
| --- | --- | --- | --- | --- |
|  |  |  |  | INSTRUMENTATION: Voltmeter, Ammeter |
| F2.1 | Power the board through the input connectors at 26V |  |  |  |
| F2.2 | Set all outputs to Imax |  |  |  |
| F2.3 | Measure voltage across outlet +5VD | Vmin = 4.75V Vmax = 5.25V | 4.97V |  |
| F2.4 | Measure voltage across outlet +15VA | Vmin = 14.25V Vmax = 15.75V | 15.02V |  |
| F2.5 | Measure voltage across outlet -15VA | Vmin = -15.75V Vmax = -14.25V | -15.16V |  |
| F2.6 | Measure voltage across outlet +2.5VFPGA | Vmin = 2.375V Vmax = 2.625V | 2.47V |  |
| F2.7 | Measure voltage across outlet +5.6V_PL_OUT | Vmin = 5.5V Vmax = 5.8V | N.A. | Only DPU+PL Version |
| F2.8 | Measure voltage across outlet +16V_PL_OUT | Vmin = +15.6V Vmax = +16.4V | N.A. | Only DPU+PL Version |
| F2.9 | Measure voltage across outlet -16V_PL_OUT | Vmin = -16.4V Vmax = -15.6V | N.A. | Only DPU+PL Version |
| F2.10 | Measure voltage across outlet +8V_PL_OUT | Vmin = +7V Vmax = +9V | N.A. | Only DPU+PL Version |
| F2.11 | Measure voltage across outlet +18V_PL_OUT | Vmin = +17V Vmax = +20V | N.A. | Only DPU+PL Version |
| F2.12 | Measure voltage across outlet -18V_PL_OUT | Vmin = -17V Vmax = -20V | N.A. | Only DPU+PL Version |
| F2.13 | Power the board through the input connectors at 29V |  |  |  |
| F2.14 | Set all of outputs to Imax |  |  |  |
| F2.16 | Measure voltage across outlet +5VD | Vmin = 4.75V Vmax = 5.25V | 4.97V |  |
| F2.17 | Measure voltage across outlet +15VA | Vmin = 14.25V Vmax = 15.75V | 15.02V |  |
| F2.18 | Measure voltage across outlet -15VA | Vmin = -15.75V Vmax = -14.25V | -15.16V |  |
| F2.19 | Measure voltage across outlet +2.5VFPGA | Vmin = 2.375V Vmax = 2.625V | 2.47V |  |
| F2.20 | Measure voltage across outlet +5.6V_PL_OUT | Vmin = 5.5V Vmax = 5.8V | N.A. | Only DPU+PL Version |
| F2.21 | Measure voltage across outlet +16V_PL_OUT | Vmin = +15.6V Vmax = +16.4V | N.A. | Only DPU+PL Version |
| F2.22 | Measure voltage across outlet -16V_PL_OUT | Vmin = -16.4V Vmax = -15.6V | N.A. | Only DPU+PL Version |
| F2.23 | Measure voltage across outlet +8V_PL_OUT | Vmin = +7V Vmax = +9V | N.A. | Only DPU+PL Version |
| F2.24 | Measure voltage across outlet +18V_PL_OUT | Vmin = +17V Vmax = +20V | N.A. | Only DPU+PL Version |
| F2.25 | Measure voltage across outlet -18V_PL_OUT | Vmin = -17V Vmax = -20V | N.A. | Only DPU+PL Version |

| F3 | RIPPLE AND SPIKES |  |  | OBJECTIVE: Verify output voltage spikes and ripple |
| --- | --- | --- | --- | --- |
|  |  |  |  | INSTRUMENTATION: Oscilloscope. Spikes measurements shall be performed with a 50MHz BW Oscilloscope. For ripple measurements, a 2MHz BW limitation shall be introduced. |
| F3.1 | Load the board with a dummy load. The dummy load shall sink a DC load current of Imax in parallel with a 20 uF capacitance in series with a 10 Ohm resistance |  |  |  |
| F3.2 | Measure ripple of outlet +5VD in differential mode | < 200mVpp | 164mVpp | See PVS 01 |
| F3.3 | Measure spikes of outlet +5VD in differential mode | < 100mVpp | 37mVpp | See PVS 01 |
| F3.4 | Measure ripple of outlet +15VA in differential mode | < 400mVpp | 16mVpp | See PVS 01 |
| F3.5 | Measure spikes of outlet +15VA in differential mode | < 200mVpp | 12mVpp | See PVS 01 |
| F3.6 | Measure ripple of outlet -15VA in differential mode | < 400mVpp | 4.4mVpp | See PVS 01 |
| F3.7 | Measure spikes of outlet -15VA in differential mode | < 200mVpp | 4.4mVpp | See PVS 01 |
| F3.8 | Measure ripple of outlet +2.5VFPGA in differential mode | < 200mVpp | 12mVpp | See PVS 01 |
| F3.9 | Measure spikes of outlet +2.5VFPGA in differential mode | < 100mVpp | 50mVpp | See PVS 01 |
| F3.10 | Measure ripple of outlet +5.6V_PL_OUT in differential mode | 140mVpp | N.A. | Only DPU+PL Version |
| F3.11 | Measure spikes of outlet +5.6V_PL_OUT in differential mode | 100mVpp | N.A. | Only DPU+PL Version |
| F3.12 | Measure ripple of outlet +16V_PL_OUT in differential mode | 140mVpp | N.A. | Only DPU+PL Version |
| F3.13 | Measure spikes of outlet +16V_PL_OUT in differential mode | 100mVpp | N.A. | Only DPU+PL Version |
| F3.14 | Measure ripple of outlet -16V_PL_OUT in differential mode | 140mVpp | N.A. | Only DPU+PL Version |
| F3.15 | Measure spikes of outlet -16V_PL_OUT in differential mode | 100mVpp | N.A. | Only DPU+PL Version |
| F3.16 | Measure ripple of outlet +8V_PL_OUT in differential mode | 850mVpp | N.A. | Only DPU+PL Version |
| F3.17 | Measure spikes of outlet +8V_PL_OUT in differential mode | 200mVpp | N.A. | Only DPU+PL Version |
| F3.18 | Measure ripple of outlet +18V_PL_OUT in differential mode | 1400mVpp | N.A. | Only DPU+PL Version |
| F3.19 | Measure spikes of outlet +18V_PL_OUT in differential mode | 200mVpp | N.A. | Only DPU+PL Version |
| F3.20 | Measure ripple of outlet -18V_PL_OUT in differential mode | 1400mVpp | N.A. | Only DPU+PL Version |
| F3.21 | Measure spikes of outlet -18V_PL_OUT in differential mode | 200mVpp | N.A. | Only DPU+PL Version |

| F4 | EFFICIENCY AND POWER CONSUMPTION |  |  | OBJECTIVE: Verify efficiency of the DC/DC board |
| --- | --- | --- | --- | --- |
|  | UUT must be powered at Vin =28V |  |  | INSTRUMENTATION: Voltmeter, Amperometer r |
| F4.1 | Set at Imax all outputs as following table: |  |  | Full load is obtained only in DPU+PL Version |
|  | Output Voltage (V) Max Current (mA) DPU Electronic +5 3.500 DPU Electronic +15 100 DPU Electronic -15 250 DPU Electronic +2,5 200 HIFI 5,6 240 HIFI 16 190 HIFI -16 150 HIFI 8 350 HIFI 18 330 HIFI -18 230 |  |  |  |
|  | Measure input current | <2.6A and >1.9A <1.5A and >0.9A | N.A. 1.171A | DPU+PL Version DPU Version |
|  | Calculate Pin=Vin*Iin | <72.8W and >67.2W <42W and >28W | N.A. 32.79W | DPU+PL Version DPU Version |
| F4.2 | Calculate Pout as the sum of all power outputs | <50W and >40W <25W and >20W | N.A. 21.39W | DPU+PL Version DPU Version |
| F4.3 | Calculate DC/DC Converter efficiency with Efficiency is given by: [%] | >70% >65% | N.A. 65.2% | DPU+PL Version DPU Version |

| F5 | INRUSH CURRENT |  |  | OBJECTIVE: Verify the inrush current |
| --- | --- | --- | --- | --- |
|  |  |  |  | INSTRUMENTATION: Multimeter, Oscilloscope, Current Probe |
| F5.1 | Place the current probe on positive power lead of the 28V Main Bus |  |  |  |
| F5.2 | Set Vbus at 29V |  |  |  |
| F5.3 | Set at Imax all outlets |  |  |  |
| F5.4 | Switch ON the Main Bus |  |  |  |
| F5.5 | Make hardcopy of the inrush current | See Remark | OK SEE ANNEX 9 | Note: The DC/DC board inrush current due to DC/DC board switch on shall be limited to 1.5 times the DC/DC input peak current, specified as 1.2 the nominal current. The duration of the inrush peak shall not exceed 0.5ms The rate of change (slope) of the inrush current shall not exceed 50mA/usec |
| F5.6 | Set Vbus at 26V |  |  |  |
| F5.7 | Set at Imax all outlets |  |  |  |
| F5.8 | Switch ON the Main Bus |  |  |  |
| F5.9 | Make hardcopy of the inrush current | See Remark | OK SEE ANNEX 8 | Note: The DC/DC board inrush current due to DC/DC board switch on shall be limited to 1.5 times the DC/DC input peak current, specified as 1.2 the nominal current. The duration of the inrush peak shall not exceed 0.5ms The rate of change (slope) of the inrush current shall not exceed 50mA/usec |

| F6 | INPUT IMPEDANCE |  |  | OBJECTIVE: Verify input impedance of DC/DC board |
| --- | --- | --- | --- | --- |
|  |  |  |  | INSTRUMENTATION: Oscilloscope, gain phase |
| F6.1 | The measurement of input impedance of the DC/DC board shall be performed with a set-up as shown in ANNEX 1 |  |  | Analyzer with test set-up of annex 1A |
| F6.2 | Set at Imax all outputs |  |  |  |
| F6.3 | Measure the input impedance of the DC/DC board and annex the plot |  | SEE ANNEX 10 |  |
| F6.4 | Verify that impedance measurement is 6dB higher than the power bus impedance mask. | OK | OK | NOTE: The power bus impedance mask is shown in the ANNEX 2 |

| F7 | INPUT PROTECTION |  |  | OBJECTIVE: Verify input protection |
| --- | --- | --- | --- | --- |
|  |  |  |  | INSTRUMENTATION: Voltmeter |
| F7.1 | Starting from 28V decrease the input voltage power bus and verify that DC/DC converter output voltages switch OFF. | >23V < 25V | 23.15V |  |
| F7.2 | Increase than input voltage and verify that DC-DC properly works | >23V < 25V | 23.60V |  |

| F8 | DPU OUTPUT PROTECTIONS |  |  | OBJECTIVE: Verify DPU output protections |
| --- | --- | --- | --- | --- |
|  |  |  |  | INSTRUMENTATION: Voltmeter, Ammeter |
| F8.1 | Check the over-voltage protection (OVP) on +5VD outlet (this test will be done before the board closure) |  |  |  |
| F8.2 | Power on the UUT at 28Vdc and maximum load: |  |  |  |
| F8.3 | -Via dedicated jumper, placed in series to R158 (+5VD output voltage sense), connect a voltage generator referred to DGND . Starting from 0V increase the voltage until the protection voltage value is reached ( controller shut-down and all outlet switch to OFF) and report the voltage value. Verify that the input power consumption is lower than 2.8W. | 5.5 (10% V | 5.54V | See PVS 02 |
| F8.7 | Check the over-current protections on +5VD outlet. |  |  |  |
| F8.8 | The test shall be performed as follow: |  |  |  |
| F8.9 | -Connect to the +5VD outlet a variable load. |  |  |  |
| F8.10 | -Place the current probe on positive power lead of the +5VD outlet. |  |  |  |
| F8.11 | -By reducing the load resistance increase the current through the +5VD outlet. When the OVC protection threshold is reached the DC/DC outlets switch to OFF and the power consumption became lower than 2,8W. | < 2W (DPU+PL) 1W < 1.5W (DPU) | 1.32W | See PVS 02 |
| F8.12 | Verify that the measured over-current protection values is as expected. | 4000(10%mA TBC | 4.12A | See PVS 02 |
| F8.13 | Check the over-current protections on +15VA outlet . |  |  |  |
| F8.14 | The test shall be performed in the following manner: |  |  |  |
| F8.15 | -Connect to the +15VA outlet a variable load. |  |  |  |
| F8.16 | -Place the current probe on positive power lead of the +15VA outlet. |  |  |  |
| F8.17 | -By reducing the load resistance increase the current across the +15VA outlet . When the OVC protection threshold is reached the DC/DC outlets switch to OFF and the power consumption became lower than 2,8W. | < 2W (DPU+PL) 1W < 1.5W (DPU) | 1.32W | See PVS 02 |
| F8.18 | Verify that the measured over-current protection values is as expected. | 200(10%mA | 204mA |  |
| F8.19 | Check the over-current protections on -15VA outlet. |  |  |  |
| F8.20 | The test shall be performed in the following manner: |  |  |  |
| F8.21 | -Connect to the -15VA outlet a variable load. |  |  |  |
| F8.22 | -Place the current probe on negative power lead of the -15VA outlet. |  |  |  |
| F8.23 | -By reducing the load resistance increase the current across the -15VA outlet . When the OVC protection threshold is reached the DC/DC outlets switch to OFF and the power consumption became lower than 2,8W. | < 2W (DPU+PL) 1W < 1.5W (DPU) |  |  |
| F8.24 | Verify that the measured over-current protection values is as expected. | 500(10%mA | 534mA |  |

| F9 | REGULATED PL OUTPUTS PROTECTIONS (IS) |  |  | OBJECTIVE: Verify the regulated output protections |
| --- | --- | --- | --- | --- |
|  |  |  |  | INSTRUMENTATION: Voltmeter, Ammeter |
| F9.1 | Check the over-voltage protections with crow-bar on +5.6V_PL_OUT outlet using the following set-up Power on the UUT with 28V input . Connect all output to the loads. By means of external power voltage generator ( limited to 2Amax)simulate an Over Voltage condition on the output. Starting from 0V increase the external voltage generator to about 6V on outlet DC/DC pin. Disconnect the output voltage generator and verify that the output is in on condition ( 5,6V) Reconnect the generator at 0V Increase the voltage to about 6,5V ( over voltage threshold).and when the current flown into outlet line (due to shunt transistor of the outlet) switch off the external generator and report the voltage and current values. Remove the external power supply and verify that the output voltage is equal to 0V. Verify that all other outputs properly work | 6.5(5%V <2A | N.A. | Only DPU+PL Version |
| F9.2 | Check the over-voltage protections on +16V_PL_OUT outlet |  |  |  |
| F9.3 | Power on the UUT with 28V input . Connect all output to the loads. By means of external power voltage generator ( limited to 100mA)simulate an Over Voltage condition on the output. Starting from 0V increase the external voltage generator to about 16,3V on outlet DC/DC pin. Disconnect the output voltage generator and verify that the output is in on condition ( 16V) Reconnect the generator at 0V Increase the voltage to 18V ( over voltage threshold) ,and switch off the external generator . Remove the external power supply and verify that the output voltage is equal to 0V. Verify that all other outputs properly work | OK 17.2(5%V | N.A. | Only DPU+PL Version |
| F9.4 | Check the over-voltage protections on -16V_PL_OUT outlet |  |  | Only DPU+PL Version |
| F9.5 | Power on the UUT with 28V input . Connect all output to the loads. By means of external power voltage generator ( limited to 100mA)simulate an Over Voltage condition on the output. Starting from 0V increase the external voltage generator to about -16,3V on outlet DC/DC pin. Disconnect the output voltage generator and verify that the output is in on condition ( -16V) Reconnect the generator at 0V Increase the voltage to - 18V ( over voltage threshold) ,and switch off the external generator . Remove the external power supply and verify that the output voltage is equal to 0V. Verify that all other outputs properly work | -17.2(5%V | N.A. | Only DPU+PL Version |
| F9.6 | Check the current limitation on +5.6V_PL_OUT outlet. |  | N.A. | Only DPU+PL Version |
| F9.7 | The test shall be performed in the following manner: |  | N.A. | Only DPU+PL Version |
| F9.8 | -Connect to the +5.6V _PL_OUT outlet a variable load. |  | N.A. | Only DPU+PL Version |
| F9.9 | -Place the current probe on negative power lead of the +5.6V _PL_OUT outlet. |  | N.A. | Only DPU+PL Version |
| F9.9 | -By reducing the load resistance increase the current through the +5.6V _PL_OUT outlet. |  |  |  |
| F9.10 | Verify that the measured current limitation value is as expected. | 285(5%mA | N.A. | Only DPU+PL Version |
| F9.11 | Check the current limitation on +16V_PL_OUT outlet. |  |  |  |
| F9.12 | The test shall be performed in the following manner: |  |  |  |
| F9.13 | -Connect to the +16V_PL_OUT outlet a variable load. |  |  |  |
| F9.14 | -Place the current probe on negative power lead of the +16V_PL_OUT outlet. |  |  |  |
| F9.15 | -By reducing the load resistance increase the current through the +16V_PL_OUT outlet. |  |  |  |
| F9.16 | Verify that the measured current limitation value is as expected. | 285(5%mA | N.A. | Only DPU+PL Version |
| F9.17 | Check the current limitation on -16V_PL_OUT outlet. |  |  |  |
| F9.18 | The test shall be performed in the following manner: |  |  |  |
| F9.19 | -Connect to the -16V_PL_OUT outlet a variable load. |  |  |  |
| F9.20 | -Place the current probe on negative power lead of the -16V_PL_OUT outlet. |  |  |  |
| F9.21 | -By reducing the load resistance increase the current through the -16V_PL_OUT outlet. |  |  |  |
| F9.22 | Verify that the measured current limitation value is as expected. | 285(5%mA | N.A. | Only DPU+PL Version |

| F10 | VOLTAGE MONITORS |  |  | OBJECTIVE: Verify voltage monitors |
| --- | --- | --- | --- | --- |
|  |  |  |  | INSTRUMENTATION: Voltmeter |
| F10.1 | Check the telemetry of +5V_MNT outlet |  |  |  |
| F10.2 | Measurement has to be performed between pin 42 of connector P2B and pin 43f connector P2B | 4.17(5% | 4.16V | Notes: Scale of telemetry: 0V( 0V, 6V( 5V Accuracy: (5% |
| F10.3 | Check the telemetry of +15V_MNT outlet |  |  |  |
| F10.4 | Measurement has to be performed between pin 74 of connector P2C and pin 75 connector P2C | 4.17(5% | 4.09V | Notes: Scale of telemetry: 0V( 0V, 18V(5V Accuracy: (5% |
| F10.5 | Check the telemetry of -15V_MNT outlet |  |  |  |
| F10.6 | Measurement has to be performed between pin 12 of connector P2A and pin 13f connector P2A | 4.17(5% | 4.17V | Notes: Scale of telemetry: 0V( 0V, -18V( 5V Accuracy: (5% |

| F11 | TEMPERATURE MONITOR |  |  | OBJECTIVE: Verify temperature monitor |
| --- | --- | --- | --- | --- |
|  |  |  |  | INSTRUMENTATION: Power supply, multimeter |
| F11.1 | Check the telemetry of +TEMP_MNT |  |  |  |
|  | Set limitation current of power supply to 50mA |  |  | Notes: Scale of telemetry: -50°C( 0V, +80°C( 5V Accuracy: (5% |
|  | Measure resistance Rmis between TP1 and TP3 | Rmis | 8673( |  |
|  | Supply TP1 (Positive) and TP3(Negative) with the following voltage: |  | 1.933V |  |
| F11.2 | Measure voltage between pin 44 and 45 of connector P2B | 0(96mV | +9.6mV | -50°C Case |
|  | Supply TP1 (Positive) and TP3(Negative) with the following voltage V: |  | 3.060V |  |
| F11.2 | Measure voltage between pin 44 and 45 of connector P2B | 5V(154mV | 4.979V | 80°C Case |

| F12 | CE on Input Power Line; Frequency Domain, Differential Mode, NB |  |  | OBJECTIVE: Verify the conducted emission differential mode on input power line |
| --- | --- | --- | --- | --- |
|  |  |  |  | INSTRUMENTATION: Spectrum analyzer with preselector |
| F12.1 | The measurement shall be performed with a test set-up as shown on ANNEX 3 |  |  |  |
| F12.2 | Set the outputs at Imax |  |  |  |
| F12.3 | Take measurements of the ambient noise (positive input line) and make hardcopy | OK | OK (See Annex 11) | See PVS 03 |
| F12.4 | Switch on the UUT, repeat the measurements and make hardcopy (positive input line) | OK | OK (See Annex 12) | See PVS 03 |
| F12.5 | Verify that the measurements are as expected | OK | OK |  |
| F12.6 | Set the outputs at Imax |  |  |  |
| F12.7 | Take measurements of the ambient noise (return line) and make hardcopy | OK | OK (See Annex 13) | See PVS 03 |
| F12.8 | Switch on the UUT, repeat the measurements and make hardcopy (return line) | OK | OK (See Annex 14) | See PVS 03 |
| F12.9 | Verify that the measurements are as expected | OK | OK (see note nearby) | NOTE: Narrow-Band conducted emission Differential Mode in the frequency range 30Hz 50MHz generated by the DC/DC board on the input power line shall not exceed the following adjustable limit: For Nominal DC input current less than 1A, use the curve in ANNEX 4 For Nominal DC input current greater than 1A, increase the level (in dBmA) of the curve in ANNEX 4 by 10*Log[I (A)]. I(A) is the nominal input current in Ampere. |

| F13 | CE on Input Power Line; Frequency Domain, COMMON Mode, NB |  |  | OBJECTIVE: Verify the conducted emission common mode on input power line |
| --- | --- | --- | --- | --- |
|  |  |  |  | INSTRUMENTATION: Spectrum analyzer with preselector |
| F13.1 | The measurement shall be performed with a test set-up as shown in ANNEX 5 |  |  |  |
| F13.2 | Set the outputs at Imax |  |  |  |
| F13.3 | Take measurements of the ambient noise and make hardcopy | OK | OK (See Annex 15) | See PVS 03 |
| F13.4 | Switch on the UUT, repeat the measurements and make hardcopy | OK | OK (See Annex 16) | See PVS 03 |
| F13.5 | Verify that the measurements are as expected | OK | OK (see note nearby) | NOTE: Narrow-Band conducted emission Differential Mode in the frequency range 10kHz 50MHz generated by the DC/DC board on the input power line shall not exceed the following adjustable limit: For Nominal DC input current less than 1A, use the curve in ANNEX 6 For Nominal DC input current greater than 1A, increase the level (in dBmA) of the curve in ANNEX 6 by 10*Log[I (A)]. I(A) is the nominal input current in Ampere. |

| F14 | CURRENT RIPPLE, TIME Domain, Differential Mode |  |  | OBJECTIVE: Verify current ripple on input power line |
| --- | --- | --- | --- | --- |
|  |  |  |  | INSTRUMENTATION: Oscilloscope |
| F14.1 | The measurement shall be performed with a test set-up as shown in ANNEX 7 |  |  |  |
| F14.2 | Set the outputs at Imax |  |  |  |
| F14.3 | Place the current probe on positive power lead of the power line |  |  |  |
| F14.4 | Record the current ripple and make hardcopy | OK | OK (See Annex 17) | See PVS 03 |
| F14.5 | Place the current probe on return power lead of the power line. |  |  |  |
| F14.6 | Record the current ripple and make hardcopy | OK | OK (See Annex 18) | See PVS 03 |
| F14.7 | Verify that the measurements are as expected |  | OK (see note nearby) | NOTE: Differential mode, time domain current ripple and spikes on the input power line of the DC/DC board shall not exceed the following limits: For nominal DC input current less than 1A: Ripple: less than 20mApp. Spikes, including ripple: less than 60mApp For nominal DC input current greater than 1A: Ripple: multiply 20mApp by a factor (I(A), I(A) is the nominal input current in Ampere Spikes, including ripple: multiply 60mApp by a factor (I(A), I(A) is the nominal input current in Ampere. |

# test procedure variation sheets

| PROCEDURE VARIATION SHEET ref. N°: 01 |
| --- |
| Test Procedure Ref.: DPU-PR-CGS-003 Issue 1 | Page Revised: 31 | Paragraph Revised: F3.2÷F3.9 |
| Description of Change: |
| F3.2 EXPECTED VALUE: WAS 200 mVpp IS < 200 mVpp F3.3 EXPECTED VALUE: WAS 100 mVpp IS < 100 mVpp F3.4 EXPECTED VALUE: WAS 400 mVpp IS < 400 mVpp F3.5 EXPECTED VALUE: WAS 200 mVpp IS < 200 mVpp F3.6 EXPECTED VALUE: WAS 400 mVpp IS < 400 mVpp F3.7 EXPECTED VALUE: WAS 200 mVpp IS < 200 mVpp F3.8 EXPECTED VALUE: WAS 200 mVpp IS < 200 mVpp F3.9 EXPECTED VALUE: WAS 100 mVpp IS < 100 mVpp |
| Reason for Change: |
| Typing error. |
| CONCURRENCE |
| Test Cond. | QA | System Eng. |  | Customer |
| Date | Date | Date |  | Date |

| PROCEDURE VARIATION SHEET ref. N°: 02 |
| --- |
| Test Procedure Ref.: DPU-PR-CGS-003 Issue 1 | Page Revised: 38 | Paragraph Revised: F8.3, F8.11, F8.12, F8.17, F8.23 |
| Description of Change: |
| F8.3 EXPECTED VALUE: WAS 5.5V IS 5.5±10%V F8.11 EXPECTED VALUE: WAS 2W (DPU+PL) 1W (DPU) IS <2W (DPU+PL) <1.5W (DPU) F8.12 EXPECTED VALUE: WAS 4000±10%mA TBC IS 4000±10%mA F8.17 EXPECTED VALUE: WAS 2W (DPU+PL) 1W (DPU) IS <2W (DPU+PL) <1.5W (DPU) F8.23 EXPECTED VALUE: WAS 2W (DPU+PL) 1W (DPU) IS <2W (DPU+PL) <1.5W (DPU) |
| Reason for Change: |
| Typing error. |
| CONCURRENCE |
| Test Cond. | QA | System Eng. |  | Customer |
| Date | Date | Date |  | Date |

| PROCEDURE VARIATION SHEET ref. N°: 03 |
| --- |
| Test Procedure Ref.: DPU-PR-CGS-003 Issue 1 | Pages Revised: 45,46,47 | Paragraph Revised: F12.3, F12.4, F12.7, F12.8, F13.3, F13.4, F14.4, F14.6 |
| Description of Change: |
| F12.3 EXPECTED VALUE: WAS Blank IS OK F12.4 EXPECTED VALUE: WAS Blank IS OK F12.7 EXPECTED VALUE: WAS Blank IS OK F12.8 EXPECTED VALUE: WAS Blank IS OK F13.3 EXPECTED VALUE: WAS Blank IS OK F13.4 EXPECTED VALUE: WAS Blank IS OK F14.4 EXPECTED VALUE: WAS Blank IS OK F14.6 EXPECTED VALUE: WAS Blank IS OK |
| Reason for Change: |
| Typing error. |
| CONCURRENCE |
| Test Cond. | QA | System Eng. |  | Customer |
| Date | Date | Date |  | Date |

# ANNEX TO THE PROCEDURE

## ANNEX 1: Test set up for input impedance measurement

## ANNEX 2: POWER BUS IMPEDANCE

## ANNEX 3: TEST SET UP FOR CONDUCED EMISSION FREQUENCY DOMAIN DM

## ANNEX 4: LIMIT FOR CEP-DIFFERENTIAL MODE

## ANNEX 5: TEST SET UP FOR CONDUCED EMISSION FREQUENCY DOMAIN CM

## ANNEX 6: NB CE POWER LINES-COMMON MODE

## ANNEX 7: TEST SET UP FOR CONDUCED EMISSION TIME DOMAIN

## ANNEX 8  Inrush current 26v  (f5.9)

- I peak:	1.42A

- I nom:		1.24A

- Rate:		0.175 [mA/us]

## annex 9  inrusch current 29v ( f5.5)

- I peak:	1.30A

- I nom:		1.12A

- Rate:		0.229 [mA/us]

## annex 10  input impedance  (f6.3)

## annex 11  ce input power line d.m.   ambient noise  (f12.3)

## annex 12  ce input power line d.m.   positive line  (f12.4)

## annex 13  ce input power line d.m. negative line ambient noise (f12.7)

## annex 14  ce input power line d.m.   negative line  (f12.8)

## annex 15  ce input power line c.m.   ambient noise  (f13.3)

## annex 16 ce input power line c.m.     (f13.4)

## annex 17  current ripple positive input power line (f14.4)

## annex 18  current ripple return input power line (f14.6)

10mA/div

# conclusions

The unit DC-DC Converter Board DPU-EM-300.00-0 S/N 03 was tested according to the specification and following the procedures DPU-PR-CGS-003 Issue 1.

The results of the tests are contained in this document. All the measurements are in agreement with the specifications.

# Text boxes

DATE:			10/04/02

TEST CONDUCTOR:

DATE:			10/04/02

TEST CONDUCTOR:

DATE:			10/04/02

TEST CONDUCTOR:

DATE:			10/04/02

TEST CONDUCTOR:

DATE:			10/04/02

TEST CONDUCTOR:

DATE:			10/04/02

TEST CONDUCTOR:

DATE:			10/04/02

TEST CONDUCTOR:

DATE:			10/04/02

TEST CONDUCTOR:

DATE:			10/04/02

TEST CONDUCTOR:

DATE:			10/04/02

TEST CONDUCTOR:

DATE:			10/04/02

TEST CONDUCTOR:

10/04/2002

09/04/2002

-

+

EXTERNAL

POWER

SUPPLY

V

A

+5.6_PL_RTN

+5.6_PL_OUT

LOAD

DC/DC

CONVERTER

09/04/2002

10/04/2002

10/04/2002

10/04/2002

24/04/2002

10/04/2002

09/04/2002

09/04/2002

09/04/2002

09/04/2002

09/04/2002

09/04/2002

09/04/2002

09/04/2002

09/04/2002

09/04/2002

09/04/2002

09/04/2002

08/04/2002

08/04/2002

08/04/2002

08/04/2002

08/04/2002

08/04/2002

08/04/2002

08/04/2002

08/04/2002

08/04/2002

See PVS 02

1.32W