| Telefax/Telecopy |
| --- |
| SPIRE-AST-COM-001354 |
| Datum/Date: | 09.08.02 |  |  | Herschel |
| An/To: | +44 29 2087 4203 University of Wales, Cardiff (SPIRE) Prof. Matt Griffin |  | Kopie an/ Copy to: | +33 04 9292 3010 ALCATEL SPACE Cannes Jean Jacques Juillet +31 71 565 5244 ESTEC Thomas Passvogel +44 1235 44 6667 RAL K.King |
| Abs./Sender: Abt./Dep.: Tel./Phone: Fax/Fax: E-Mail: Ref.: | G.Peters ED 37/Herschel +49 75 45 8-4275 +49 75 45 8-42 43 Gerhard.Peters@astrium-space.com HP-ASED-FX-0510-02 |
| Seite/Page: 1 von/of 4 Seiten/Pages |
| Betreff/Subj.: | Reduction of HERSCHEL CVV Feed Through Connectors for SPIRE |

Dear Sirs,

We have reached now a stage close to the final definition of the Herschel Cryo harness. A review together with the ESA project of the complexity and the technical risk showed that there are significant advantages to the system and hence ultimately to the instruments when reducing the amount of Feed Through connectors in the HERSCHEL Cryostat Vacuum Vessel.

The goal is to avoid the middle connector ring.

Looking through your SPIRE Harness Definition Document SPIRE-RAL-PRJ-000608

Issue 1.0, Date 08/07/2002 and considering the required pins we found, that we can reduce the 26 Feed Through Connectors currently allocated to the Spire system to an amount of 14 to 15 connectors with 100 pins each.

Please find in the following a proposed allocation of Spire JFET and FPU connectors to the Feed Through´s

| JFS Conn | Function | used Pins CVV Connector | Feed Through Connector Change to | used Pins CVV Connector |
| --- | --- | --- | --- | --- |
| J05 | SLW JFET 01-12 | 24+1G/S=25 |  | SPIRE FTh 01 (CVV ring connector number tbd) Part of C1 harness | 74+6S/G (80 of 100) |
| J06 | SLW JFET 13-24 | 24+1G/S=25 |  |  |  |
| J09 | Spec Bias Tail A | 26+4S/G=30 |  |  |  |

Grounding/Shielding Concept not clear, please explain (A) wires/contacts

| J07 | PTC | 8+1G/S=9 |  | SPIRE FTh 02 (CVV ring connector number tbd) Part of C2 C3 harness | 58+7S/G (65 of 100) |
| --- | --- | --- | --- | --- | --- |
| J26 | PSW Biases B Re | 24+2S=26 |  |  |  |
| J28 | PMW/PLW Bias B Re | 26+4S/G=29 |  |  |  |

| J01 | SSW JFET Bol 01-12 | 24+1G/S=25 |  | SPIRE FTh03 (CVV ring connector number tbd) | 88 + 4 G/S (92 of 100) |
| --- | --- | --- | --- | --- | --- |
| J02 | SSW JFET Bol 13-24 | 24+1G/S=25 |  |  |  |
| J03 | SSW JFET Bol 25-36 | 24+1G/S=25 |  |  |  |
| J04 | SSW JFET Bol 37-42 + 2 Spare | 16+1G/S=17 |  |  |  |

| J10 | Spec Bias TailB | 26+4S/G=30 |  | SPIRE FTh04 (CVV ring connector number tbd) Part of C1 C3 harness | 76 + 10 S/G (86 of 100) |
| --- | --- | --- | --- | --- | --- |
| J25 | PSW Biases A Pr | 24+2S=26 |  |  |  |
| J27 | PMW/PLW Bias A Pr | 26+4S/G=30 |  |  |  |

Grounding/Shielding Concept not clear, please explain (Ax,Bx,Cx,Dx) wires/contacs

| J21 | PMW 01-09 + 3 Spare | 24+1S/G=25 | 6wires spare | SPIRE FTh05 (CVV ring connector number tbd) ( C4 Harness ) | 96 + 4 S/G (100 of 100) 6 spares |
| --- | --- | --- | --- | --- | --- |
| J22 | PMW 10-21 | 24+1S/G=25 |  |  |  |
| J23 | PMW 22-33 | 24+1S/G=25 |  |  |  |
| J24 | PMW 34-45 | 24+1S/G=25 |  |  |  |

Spares wires could be used for Faraday and Overall Shield

| J17 | PMW 01-09 + 3 Spare | 24+1S/G=25 |  | SPIRE FTh06 (CVV ring connector number tbd) ( C5 Harness ) | 96 + 4 S/G (100 of 100) No spares! |
| --- | --- | --- | --- | --- | --- |
| J18 | PMW 10-21 | 24+1S/G=25 |  |  |  |
| J19 | PMW 22-33 | 24+1S/G=25 |  |  |  |
| J20 | PMW 34-45 | 24+1S/G=25 |  |  |  |

Pins for Faraday and Overall Shield needed !

| J13 | PLW | 24+1S/G=25 | Spares? | SPIRE FTh07 (CVV ring connector number tbd) ( C6 Harness ) | 96 + 4 S/G (100 of 100) Spares ? |
| --- | --- | --- | --- | --- | --- |
| J14 | PLW | 24+1S/G=25 |  |  |  |
| J15 | PLW | 24+1S/G=25 |  |  |  |
| J16 | PLW | 24+1S/G=25 |  |  |  |

Spares like C4 ?

| J09 | PSW | 24+1S/G=25 | Spares? | SPIRE FTh08 (CVV ring connector number tbd) ( C7 Harness ) | 96 + 4 S/G (100 of 100) Spares ? |
| --- | --- | --- | --- | --- | --- |
| J10 | PSW | 24+1S/G=25 |  |  |  |
| J11 | PSW | 24+1S/G=25 |  |  |  |
| J12 | PSW | 24+1S/G=25 |  |  |  |

Spares like C4 ?

| J05 | PSW | 24+1S/G=25 | Spares? | SPIRE FTh09 (CVV ring connector number tbd) ( C8 Harness ) | 96 + 4 S/G (100 of 100) Spares ? |
| --- | --- | --- | --- | --- | --- |
| J06 | PSW | 24+1S/G=25 |  |  |  |
| J07 | PSW | 24+1S/G=25 |  |  |  |
| J08 | PSW | 24+1S/G=25 |  |  |  |

Spares like C4 ?

| J01 | PSW | 24+1S/G=25 | Spares? | SPIRE FTh10 (CVV ring connector number tbd) ( C9 Harness ) | 96 + 4 S/G (100 of 100) Spares ? |
| --- | --- | --- | --- | --- | --- |
| J02 | PSW | 24+1S/G=25 |  |  |  |
| J03 | PSW | 24+1S/G=25 |  |  |  |
| J04 | PSW | 24+1S/G=25 |  |  |  |

Spares like C4 ?

| J19 | FA Cooler P | 32+1S=33 |  | SPIRE FTh11 (CVV ring connector number tbd) (C10 Harness) | 80 + 4 Shd (84 of 100) |
| --- | --- | --- | --- | --- | --- |
| J21 | FA Spect. Stim P | 20+1S=21 |  |  |  |
| J23 | FB Therm P | 28+2S=30 |  |  |  |

| J25 | FB BSM P | 30+6S=36 |  | SPIRE FTh12 (CVV ring connector number tbd) (C11 Harness) | 78 + 16 Shd (94 of 100) |
| --- | --- | --- | --- | --- | --- |
| J27 | FC SMEC Launch P | 26+4S=30 |  |  |  |
| J29 | FC SMEC Control P | 22+6S=28 |  |  |  |

| J20 | FD Cooler R | 32+1S=33 |  | SPIRE FTh13 (CVV ring connector number tbd) (C12 Harness) | 80 + 4 Shd (84 of 100) |
| --- | --- | --- | --- | --- | --- |
| J22 | FD Spect. Stim R | 20+1S=21 |  |  |  |
| J24 | FE Therm R | 28+2S=30 |  |  |  |

| J26 | FE BSM R | 30+6S=36 |  | SPIRE FTh14 (CVV ring connector number tbd) (C13 Harness) | 78 + 16 Shd (94 of 100) |
| --- | --- | --- | --- | --- | --- |
| J28 | FF SMEC Launch R | 26+4S=30 |  |  |  |
| J30 | FF SMEC Control R | 22+6S=28 |  |  |  |

Before going too far with the implementation we would like to ask you for your comments, e.g. any restrictions in grouping, EMC classes, redundancy distribution, mixing high current lines with amplifier lines etc, especially in the region of JFET Faradays and Ground wires

However, if this proposal does not correspond to your needs, please give us a counterproposal which follows the redline shown before.

Due to the high criticality could you provide your agreement, respectively comments/ counterproposal  by end August 2002 at the latest.

Kind regards

Astrium GmbH

i. A.    A.von Ivady						i. A.    R.Stritter