| ID | Document | Section | Raised by | Comment | Response |
| --- | --- | --- | --- | --- | --- |
| GEN 1 | All |  | EAC (PA) | There is no CIDL Configured Item Document/Drawing List. (ESA and SPIRE requirement). |  |
| 2 | All |  | EAC (PA) | There are several TBW's or will insert XYZ here when ready throughout the set of documents. |  |
| 3 | All |  | EAC (PA) | DCU Design document, purpose and scope of this document be TBW, should not still be undefined at this stage |  |
| 4 | All |  | EAC (PA) | PA Plan is missing from this document list. |  |

| ID | Document | Section | Raised by | Comment | Response |
| --- | --- | --- | --- | --- | --- |
| DRCU1 | DRCU Spec. Doc. SAP-PRJ-000461 (Sap-SPIRE-CCA-25-00) | 2.1 | BMS | Figure 2.1a is scrambled Figure 2.1a has “OEP” outside the FPU – it should be inside |  |
| 2 | ditto | DRCU-REQ-45 | BMS | …and here’s the rub! When does the filtering get specified? |  |
| 3 | ditto | Fig 4.2-b | BMS | This figure does not accord with the power supplies specified elsewhere in the document (DRCU-REQ-43 and DRCU-REQ-99) and is therefore confusing – remove or replace. |  |
| 4 | Ditto Also applies to DRCU/DPU I/F Doc | DRCU-REQ-79 (and maybe elsewhere) | BMS | Parameter names used here are not consistent with the interface specification. In the interface doc (…) it uses FPUTEMP# -here the temperatures have more meaningful names – use these please! |  |
| 5 | ditto Also applies to DRCU/DPU I/F Doc | DRCU-REQ-83 | BMS | Please define the SCUSTATUS word as soon as possible – it does not appear at all in the I/F parameter list although it can be requested by dedicated command! (cf. ICD section 2.2.14.3 and 2.2.15) |  |
| 6 | ditto | DRCU-REQ-85 DRCU-REQ-86 | BMS | Wrong document called up – should be AD24? |  |
| 7 | ditto | DRCU-REQ-88 | BMS | Number of steps for full range operation is over specified – PCAL requirement is for 256 steps – if it is convenient to have a single type of DAC then o.k. else it is unnecessary. |  |
| 8 | ditto | 4.6.1 | BMS/JD | Post regulation is shown for LIA supplies but not for DAQ/Bias supplies. Where does this happen? |  |
| 9 | ditto | 4.7.3 | BMS | Can we have an extra requirement that the outputs of all FPGA controlled supplies (heaters; mechanism drives etc) are kept low during initialisation and are kept low until commanded otherwise. |  |
| 10 | ditto | DRCU-REQ-120 | BMS | What does S/W crash refer to? The DPU or any software local to the DRCU? |  |
| 11 | ditto | 4.7.5 | BMS | Please check this against the Operating Modes document version 3 issued Jan 2002 as the naming of modes has been changed and we have defined two standby modes one for PHOT and one for SPEC. |  |
| 12 | ditto | DRCU-REQ-122 | BMS | Reword and add new requirement: 122: The DRCU shall provide capabilities for the DPU to detect internal failures 122 bis: The MCU shall provide capabilities to detect and handle failures in the sub-system that might cause immediate danger to the mechanism. |  |
| 13 | ditto | 4.9.3 | BMS | The diagram is unreadable – please make it bigger. |  |
| 14 | ditto | 5.1.3 | BMS | Are these requirements still relavant given that the interface drawing exists? |  |
| 15 | ditto | 8 | BMS | The reliability figure for the DCU has been discussed in a technical note. The FMECA has covered the rest of the reliability discussion? |  |
| 16 | ditto | 11 and section 1.3 | BMS | AD13 through 17 aren’t mentioned/used – did they go missing? |  |
| 17 | ditto | 12 | BMS | Table is incorrect? QM1 and QM2 do not have Flight Equivalent power supplies with or without redundancy. |  |
| 18 | ditto | 4.4.3 | PH | REQ-85, the range for the SCAL 4% and 2% source (T-SCAL2, TSCAL4 is listed as 10K to 80K. This should read 4K to 150K |  |

| ID | Document | Section | Raised by | Comment | Response |
| --- | --- | --- | --- | --- | --- |
| ICD 1 | DRCU ICD SPIRE-SAP-PRJ-000451 (Sap-SPIRE-CCA-075-02) | 5.4.3.2.1 | DKG | Include jumper connections from pins 1 to 21; 2 to 22, 20 to 30; 4 to 24; 5 to 25; 3 to 6 of J29 and also J30 to allow for robustness in the SMEC Launch Latch drives. |  |

| ID | Document | Section | Raised by | Comment | Response |
| --- | --- | --- | --- | --- | --- |
| DCU1 | DCU Design Description SAp-SPIRE-FP-0063-02 | 3.2 | BMS | What does this table mean? It is not complete. |  |
| 2 | ditto | Whole doc. | BMS | Circuit diagrams are unreadable (e.g. Picture 4-8) |  |
| 3 | ditto | 4.1.3.1 4.1.6.1 | BMS | I believe the offset in the first part of the picture comes from the JFETs? Please identify the source of the offset is the text or on the picture. |  |
| 4 | ditto | 4.1.3.2 4.1.3.3 4.1.6.2 4.1.6.3 | BMS | Can we have the transfer functions of the filters in tabular or polynomial form please. Then we can use them in the instrument models. |  |
| 5 | ditto | 4.1.8.1 | BMS | The description is a bit hard to follow! What is the final relationship between DATA and the amplitude of the bias that is actually output from the circuit? Is the statement about the resistors associated with the absence of the redundant cards from QM1 or does it represent a design option? |  |
| 6 | ditto | 4.1.8.1 4.1.11 | BMS | There is no description of how the phase of the demodulation signal is altered for each BDA module? I hope this is implemented! |  |
| 7 | ditto | 4.1.12.1 | BMS | Is FRAME=0 equivalent to continuous output of frames as specified in the ICD? Do both FRAME and START have to be high for data to be output? |  |
| 8 | ditto | 4.1.12.3 (Page 61) | BMS | Is an average of two values at all useful? Why isn’t it 4 values as in the photometer? |  |
| 9 | ditto | 4.1.12.5 | BMS | I think I understand how it works but it isn’t completely obvious from this section! Just a leetle more explanation? |  |
| 10 | ditto | 4.1.12.7 | BMS | Do 1 and 2 represent design options to be decided upon? |  |

| ID | Document | Section | Raised by | Comment | Response |
| --- | --- | --- | --- | --- | --- |
| SCU1 | SCU Design Description SEDI/SCU/MM /2002-1 | 1.1.3 | BMS | We don’t seem to have a copy of AD5? SEDI-SPIRE-OG-0001-02 |  |
| 2 | ditto | 2.1 | BMS | Block diagram shows “AC Modulation(x4)” – why is this when there is only one AC temperature channel? |  |
| 3 | ditto | 2.2 3.1 3.2 | BMS | We would like some clarification of the operation of the acquisition sequencer and the data frame transfer: i) Which takes priority – the Acquisition Sequencer or the Get Parameter request? We wish to have the data in the frames at even sampling rates – therefore we would wish the Acquisition Sequencer to have priority. A timing diagram would be useful ii) Does the FPGA assemble a complete data then transfer it, or does it transfer the payload piecewise? |  |
| 4 | ditto | 3.2.1.1 | BMS | Similar comment – Data Frame and Packet used interchangeably – please use Data Frame as packet means something else to the DPU. |  |
| 5 | ditto | 4.1.1 4.2.1 4.3.1 | BMS | Maximum lead resistances are specified in the DRCU Specification document and the Harness Definition Document. These should be used to specify the design? |  |
| 6 | ditto | 4.1.4.5 4.2.4.4 | BMS | Does this test mean that the effect of the lead resistance can be ignored? The lead resistance does not seem to be included in the simulation – what is the dissipation going to be in the cryoharness? |  |
| 7 | ditto | 4.2.4.1 | BMS | Check with Lionel Duband whether 4pW is significant in terms of the operation of the heat switch sorption pump. |  |
| 8 | ditto | 4.3.1 | BMS | The Spec Doc (AD1) specifies 6 kfor the heater resistance |  |
| 9 | ditto | 4.4.1.2 4.4.1.3 | BMS | This is an incorrect description of the SCAL sources – the Spec. Doc (AD1 v0.92) has the correct specification (2% and 4% sources) with both types of source having the specification as for “SCALP”. The “SCALF” drive is not required, we need 2x the “SCALP” design. |  |
| 10 | ditto | 4.8 | BMS | Is this power supply monitoring associated with the SCU staus word? |  |
| 11 | ditto | 5.2.1 | BMS | How does this work? Analogue or digital? |  |
| 12 | ditto | 6.1 | BMS | The notes on the next page make explicit that all output voltages and currents are held low in the reset state. Maybe make this clear in this section? Also is it really true that the SCU is “stateless” when it leaves reset? I hope that the outputs are definitively held low until commanded otherwise? |  |
| 13 | ditto | 6.2 | BMS | Its not clear how the sampling frequency is set – FRAMECONF? It is reasonably urgent that the SCUSTATUS word is defined as this will be used for error detection in flight and we need to get on with the FDIR. |  |
| 14 | ditto | 7.1 | BMS | Read DRCU-REQ-89 in the latest version of AD1 v0.92 Both SCAL devices are four wire to allow remote sensing of voltage and therefore current stabilisation? |  |
| 15 | ditto | 4.4 | PH | Description of SCAL out of date, flood and point sources no longer used |  |
| DPU-ICD 1 | DRCU to DPU ICD Sap-SPIRE-CCA-076-02 | General comment | RCI at IFSI | One very important comment is that, as far as we know, the DRCU-DPU ICD is the one we wrote (SPIRE-IFS-PRJ-000650 of 2/4/2001). We always said that we will discuss and include in that document the DRCU people comments, but the need of a single document is to avoid ambiguities and unnecessary efforts (i.e. we are the custodian of the ICD). |  |
| 2 | ditto | 2.1.1 | RCI | DRCU subsystems, if addressed individually reply with a response word with the following ..... Should read: DRCU subsystems, if addressed individually with SYN0=0 reply with a response word with the following ... |  |
| 3 | Ditto | 2.4.1.2 | RCI | when a "Set_parameter" command is received the subsystem responds to the DPU by transferring a command acknowledge word (positive or negative) on the response line. Should read: When a "Set_parameter" command with SYN0=0 is received the subsystem responds to the DPU by transferring a command acknowledge word (positive or negative) on the response line. |  |
| 4 | Ditto | 2.1.5.1 | RCI | The RES signal shall by modified on the rising edge of the CLK signal and being sampled by the DPU on the next falling edge of the CLK signal. Should read: The RES signal shall be modified on the falling edge of the CLK signal and being sampled by the DPU on the next rising edge of the CLK signal. |  |
| 5 | Ditto | 2.1.5.3 | RCI | Delta T1 is missing in the max command rate formula. In any case the formula is very optimistic as the actual max rate (if SYN0=0) is around 500 commands per second. |  |
| 6 | Ditto | 2.2.5.2 | KJK | Add / to SetGetPhotoJfetPwr and SetGetPhotoOffset In SetGetPhotoOffset the channel number can only be 0 to 31 (not 0 to 32), which presumably correspond to channel numbers 1 to 32 in table 2.2.6.4. Similarly for SetGetSpectroOffset. |  |
| 7 | Ditto | 2.2.5.3 | KJK | SetGetSpectroHeaterPwr should be SetGetSpectroHeaterBias (to be consistant with Photo table) |  |
| 8 | Ditto | 2.2.6.1.4 | KJK | Description for SetDemodPh should be 'Set the bolometer group demodulation phase shift' |  |
| 9 | Ditto | 2.2.6.1.6 | KJK | Heading should be PhotoHeaterBias to be consistant with table 2.2.5.2. |  |
| 10 | Ditto | 2.2.6.5.8 | KJK | Description for GetSpLWJfetVSS should be 'Get S-LW JFET source voltage' Description for SetSpLWJfetVSS should be 'Set S-LW JFET source voltage' |  |
| 11 | Ditto | 2.2.6.7.1 | KJK | I imply from the desciption of the science frames in section 2.3.5 that if bit 3 is set to 1 (test) then bits 2 to 0 may only be set to 0 or 4. What happens for other combinations? |  |
| 12 | Ditto | 2.2.7.1 | KJK | If PhotoDivBias (why not BiasDiv - see 2.2.6.1.1?) is set to 0 the sampling frequency will be infinite! What actually happens? Presumably setting Channel_P1 to 0 selects Channel 1 of LIA_P1 etc? |  |
| 13 | Ditto | 2.2.7.2 | KJK | If SpectroBiasDiv (why is it BiasDiv rather than DivBias?) is set to 0 the sampling frequency will be infinite! What actually happens? Presumably setting Channel_S1 to 0 selects Channel 0 of LIA_S1 etc? |  |
| 14 | Ditto | 2.2.7.3 | KJK | Data modes 05 and 06 are reversed with respect to section 2.2.6.7.1 |  |
| 15 | ditto | 2.2.8.1 | KJK | Step 1: to set the Photo Bias Frequency the parameter is PhotoMClkDiv Step 2: to set the Photo Sampling Frequency the parameter id PhotoBiasDiv (or PhotoDivBias) Step 3: There are 448 cases for each BDA Step 25: Why has value EF been chosen? Step 30: There are 448 cases for each BDA Step 38: Why has value EF been chosen? |  |
| 16 | Ditto | 2.2.8.4.1 | KJK | Step 1: Ther is no such command Step 1: Ther is no such command |  |
| 17 | Ditto | 2.2.15 | KJK | There are parameters that are missing compared to previous version of the ICD, such as DAQ and LIA voltage supplies. Is this deliberate or are they to be found somewhere else? |  |
| 18 | Ditto | 2.3.5.3.1. | KJK | The table shows a Data Structure length of 294 for frames of Photometer Full Array. There are 288 detector channels to be sampled (see table 2.3.5.3.2). There is one word at the end of the Data Structure containing the ADC Status. What are the other 5 words? Similarly the other Frame lengths are 5 words longer than necessary - or does the table give the total length of the frame rather than the length of the Data Structure? |  |
| 19 | Ditto | 2.3.5.3.2 | KJK | It is not clear in which order the pixels are stored in the data frame. Can I assume that the pixels are stored in the order reading across each row (CH1/LIA_P1, CH16/LIA_P2 .....) for each row in turn, starting at the top? Is it true that the first 144 data in this table correspond to the Photometer SW array, the next 96 data correspond to the MW Array and the final 48 data correspond to the LW array? And this is the order in which they will appear in Frame IDs 2, 3, and 4? Is the arrangement similar for the spectrometer table? |  |
| 20 | Ditto | 2.3.5.3.4 | KJK | I believe frame type T4 contains the 32 bit time reference of the crossing, rather than the delta time. Can you confirm this? I would have expected Frame Type T7 to contain similar data to type T6 (i.e. jiggle position and error signal) Again the table seesm to give the Total Frame Length rather than the Data Structure length. Please clarify. |  |
| 21 | Ditto | 2.3.5.3.5 | KJK | Why is the Frame T10 of length 30. This implies only 25 hsk parameters, but my reading of section 2.2.14 indicates more parameters are available. Please put a table of which parameters go where in the Frame. |  |
| 22 | Ditto | 2.3.6 | KJK | I have tried to understand the reference document but I think there is more information needed to allow someone to calculate the pseudo random sequence expected. We need to know which bits are being fed back into the register and whether they are being modified before being fed back. A table of the first few values for each LFSR would be useful to allow us to check our code. Please clarify whether all the data in a single frame has the same value or is a new value calculated for each data in the frame? |  |