### Original draft November 2002

Issue 0.3 April 2003

##### Commanding changed in line with

DRCU/DPU Interface Document - SPIRE-SAP-PRJ-001324 issue 1.0 14/02/2003

MCU/DPU Comand List ICD - LAM/ELE/SPI/011011 Issue 3.0 15/01/2003

SCU Design Description - SEDI-SCU-MM-2002-1 0.7 17/02/2003

DCU Design Description - SAp-SPIRE-FP-0063-02 Issue 0.3 18/02/2003

Issue 1.0 11 June 2003

MCU Commanding/reaction section completed

DCU Commanding for Photometer completed

# SCU

General description:

The SCU provides power; signal conditioning and data acquisition for the heaters and thermistors on the SPIRE FPU.  This includes the heaters necessary for the 300 mK cooler operation; the heaters for the calibration sources and all temperature sensors on the cold FPU except those associated with the detectors.  The unit is powered on when the 28 V power is applied to the DRCU power supply unit.   At power on the FPGA enters a reset state, boots in some fashion, counts its fingers and sets the ScuStatus word to some TBD value.  It is then ready to accept commands from the DPU.

##### In this version of the document I have used guessitimated conversion curves – CEA have now provided more accurate simulated curves which I will use in future.  I have still left out the detector stuff as this requires more work.

| Command sent | Parameter that should respond | Status/value before | Status/value after | Comment |
| --- | --- | --- | --- | --- |
| Request to CDMS to switch on 28V line to DRCU | ScuStatus | Undetermined | 0x0000 | If any of first three bits set then an error has occurred |
|  | ScuCHTp05 | Undetermined | 0xB554 | Used 0.366 mV/ADU over +-12V with 215-1 = 0V |
|  | ScuCHTp09 | Undetermined | 0xE00D | Ditto |
|  | ScuCHTn09 | Undetermined | 0x1FF0 | Ditto |
|  | ScuCHTp25 | Undetermined | 0x9AAD | Ditto |
|  | CsuTempRd | Undetermined | 0x4001 | Complete guess Need conversion curve between ADC value and temperature |
|  | TsuTempRd | Undetermined | 0x4002 | Guess again – bit different to make sure in right place |
|  | PsuTemp1Rd | Undetermined | 0x4004 | Ditto |
|  | PsuTemp2Rd | Undetermined | 0x4008 | Ditto |

# Telemetry

The SCU “science” data nominally consists of 17 temperatures plus the currents and voltages for the three calibrators.  There are two frame types defined – nominal and test.  The frame type, sampling rate and the number of frames to send are set up by command before a request to start sending data.  One can either request a given number of frames or continuous data transfer.  In the latter case a command must be sent to stop the data transfer at the appropriate time.

| Command sent | Parameter that should respond | Status/value before | Status/value after | Comment |
| --- | --- | --- | --- | --- |
| SetFrameConf | FrameConf | 0x0000 (TBC) | 0x004F | Bit 15 is type 0 is normal 1 is test Bits 0-7 set rate as 80/(value+1) Hz Sets 1 Hz sampling normal frame |
| SetSeqLength | SeqLength | 0x0000 | 0x001F | Sets 31 frames to be sent |
| SetFrameCtrl | FrameCtrl | 0x0000 | 0x0001 | Bit 0 starts and stops frame transfer – reset at end of 31 frames (TBC) |
|  | ScuStatus | 0x0000 | 0x0004 during transfer 0x0000 at end of transfer | Bit 4 is a mirror of FrameCtrl bit 0 |

# Thermistors

General Description:

There are 16 “normal” thermistors on SPIRE.  These are switched on by applying a small, stabilised current and the temperature is calculated from measurement of the voltage across the devices.  Each of the sixteen temperature channels is individually commanded on and off and the corresponding parameter will change from 0 to a value dependent on the temperature as the current is applied.

| Command sent | Parameter that should respond | Status/value before | Status/value after | Comment |
| --- | --- | --- | --- | --- |
| TempOnOff 0xFFFF | TempOnOff | 0x0000 | 0xFFFF | 16 bits of on/off to address 16 temp channels. All temps on. |
|  | CPHPtemp CPHStemp CEHStemp CSHTtemp SOBtemp SL0temp PL0temp SUBtemp BAFtemp BSMStemp SCL2temp SCL4temp SCSTtemp FTSStemp FTSMtemp BSMMtemp | All 0x0000 | 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) 0x0DAC (ltg) 0x0DAC (ltg) 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) | In fact the response curves are non-linear – to make things easy I have two thermistor temepratures following the SCU design description – Low Temperature Group (ltg) with 0.5 mK/Bit linear over 1-2 K range High Temperature Group (htg)with 2 mK/bit over the 3-6 K temperature range I have ignored offsets and thermistors will move from one group to another depending on the temperature |
| TempOnOff 0x0000 | TempOnOff | 0xFFFF | 0x0000 | Turns temp sensor N on or off – send this command for each or does parameter address lots of them? |
|  | CPHPtemp CPHStemp CEHStemp CSHTtemp SOBtemp SL0temp PL0temp SUBtemp BAFtemp BSMStemp SCL2temp SCL4temp SCSTtemp FTSStemp FTSMtemp BSMMtemp | 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) 0x0DAC (ltg) 0x0DAC (ltg) 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) 0x08CA (htg) | All 0x0000 | Need conversion curve for ADC value to temperature for Cernox 1030’s Need table of which one is which. |

# PCAL

General description:

There is only one nominal PCAL operational mode.  When the PCAL heater current is commanded there is nominally no reaction from any other sub-system parameter except that the detectors will give a signal.  The waveform of the PCAL output is controlled by sending successive commands to set the current.

The PCAL heater supply is “four wire” which allows direct measurement of the voltage across the devices.  This parameter is reported in the housekeeping as well as the commanded set current.

| Command sent | Parameter that should respond | Status/value before | Status/value after | Comment |
| --- | --- | --- | --- | --- |
| SetPhCalBias 0x07FD | PhCalBias | 0x0000 | 0x07FD | Assume 4.5 mA full scale for 4095 steps 1.1 A/step This sets current to half way ~2.25 mA |
|  | PhCalVolt | 0x0000 | 0x08BC + 0x1721*(1-et/0.1) Where t is time in seconds | I have bodged this from reading the SCU and PCAL design description using 76 V/bit to describe a change in voltage given by V(t)= 0.17+0.45(1-exp(t/0.1). |

# SCAL

General Description

There is only one nominal SCAL operational mode.  When the SCAL-2 or SCAL-4 current is commanded the SCAL-2 or 4 thermistor responds with a TBD time constant as the calibrator warms up.  The temperature is achieved as quickly as possible and then stabilised using software control in the DPU.  The power falling on the detectors will increase with the SCAL temperature but this is only DC power so is not seen as signal – only increased noise.  Before the thermistors can respond they must be switched on.

The SCAL-2 and SCAL-4 heater supplies are “four wire” which allows direct measurement of the voltage across the devices.  This parameter is reported in the housekeeping as well as the set current.

| Command sent | Parameter that should respond | Status/value before | Status/value after | Comment |
| --- | --- | --- | --- | --- |
| SetSCal4Bias 0x068F | ScaI4Bias | 0x0000 | 0x068F | Set up for 5.5 mA full scale over 4095 steps 1.34 A/step This sets 2.25 mA – equivalent to ~2.5 mW dissipation in source. |
|  | SCal4Volt | 0x0000 | 0x08BC + 0x23FA*(1-et/5) t is time in seconds | Assume same as PCAL for the time being with a 5 second time constant (wrong but otherwise we wait for ever!). In dec the voltage is V(t) = 0.17+0.7(1-exp(t/5) |
|  | SCL4temp | 0x08CA | 0x08CA + 0x9376*(1-e-t/5) | Response curve is actually non-linear – here I have assumed 2 mK/Bit linear from 4.5 K to 80 K. |
| SetSCal2Bias 0x068F | Scal2Bias | 0x0000 | 0x068F | Same as SCAL-4 |
|  | Scal2Volt | 0x0000 | 0x08BC + 0x23FA*(1-et/5) t is time in seconds | Ditto |
|  | SCL2Temp | 0x08CA | 0x08CA + 0x9376*(1-e-t/5) | Ditto |

# Cooler

General Description:

The cooler has two operational modes – recycle and cooling.  During the recycle mode the current to the evaporator heat switch is set high, the evaporator thermistors, both “sub-K” and “normal”, will read 1.7 K.  At the same time, the current to the pump heat switch is set low.  The pump heater current is set under software control to keep the temperature of the pump, registered by the pump thermistor, at TBD K for some length of time (about 30 minutes).  At the end of this period the current to the pump heat switch is set high and (a short time later) the current to the evaporator is set low.  Following this the pump temperature will fall to ~1.8 K and the evaporator temperature will fall to ~300 mK – this is the cooling operating mode condition.  In table below the command sequence is set out for recycling the cooler and leaving it in the cold condition.

All the heater supplies are “four wire” which allows direct measurement of the voltage across the devices.  Only the voltage is reported in the housekeeping and NOT the set current because the same parameter name/address is used for the Set and Get commands for the heater control  – see comment below.

| Command sent | Parameter that should respond | Status/value before | Status/value after | Comment |
| --- | --- | --- | --- | --- |
| SetSubKOnOff 0x0001 | SubKOnOff | 0x0000 | 0x0001 | Switches on the sub-K thermistor |
|  | SubKTempP | 0x0000 | 0x05DC | When the cooler is first turned on the evaporator (where the sub-K sensor is located) will be at the L1 temperature (or thereabouts) The SubK is highly non-linear – at 1.75 and 4.5 K I assume 3 mK/bit – see below for strange response curve |
| SetEVHSHeatCur 0x0800 | EVHSHeatCur | 0x0000 | 0x0800 | This closes the evaporator heat switch connecting it directly to L0. Complete guesswork for the value here! |
|  | EVHSHeatVolt | 0x0000 | 0x61F7 | SCU design desc. gives voltage across the switch is given by V=9.31e-4*DAC +2.57e-4 |
|  | SubKTempP | 0x05DC | 0x0247 | Evaporator falls to L0 temperature. Assume instantly for these purposes. Again 3 mK/bit |
| SetSPHeaterCur 0x0708 | SPHeaterCur | 0x0000 | 0x0708 | At the beginning of the recycle the heater is set to 200 mW - about 22 mA (TBC). I assume 1.22e-5 A/DAC bit |
|  | SPHeaterVolt | 0x0000 | 0x1C30 | Can take ADC= 3280Vsense from CEA document – this equivalent to 2.2 V as given in SCU Design Desc. In fact it should follow the resistance but this will do. |
|  | CPHPtemp | 0x08CA | 0x08CA + 0x4556(1-et/300) | For now can assume an RC response with time constant of 5 minutes to get to 40 K. Assume thermistor value is given by 2 mK/bit linear from 4.5 to 40 K. |
| SetSPHeaterCur 0x0287 | SPHeaterCur | 0x0708 | 0x0287 | Once the pump gets hot (>40 K) the current is backed off to keep it at a (more or less) fixed temperature. Here I assume backed to 25 mW or 7.9 mA – relationship as before. |
|  | SPHeaterVolt | 0x1C30 | 0x07B0 | This equivalent to 0.6V as given in SCU Design Desc. |
|  | CPHPtemp | 0x4E20 | 0x4E20 | Assume for now that the system behaves perfectly – i.e. it gets to 40-K in 5 min and just sits there when the current is backed off. |
| SetSPHeaterCur 0x0000 | SPHeaterCur | 0x0287 | 0x0000 | After some time the heater is switched off |
|  | SPHeaterVolt | 0x07B0 | 0x0000 | Voltage also falls to zero |
|  | CPHPtemp | 0x4E20 | 0x4E20 | Once the heat is removed the pump will actually cool – but very slowly – ignore this for now. |
| SetSPHSHeatCur | SPHSHeatCur | 0x0000 | 0x0800 | This closes the pump heat switch connecting it directly to L0. Complete guesswork for the value here! |
|  | SPHSHeatVolt | 0x0000 | 0x61F7 | SCU design desc. gives voltage across the switch is given by V=9.31e-4*DAC +2.57e-4 |
|  | CPHPtemp | 0x4E20 | 0x4E20 – 0x4AB5(1-e-t/60) t is time in seconds | When the heat switch closes the pump temperature falls to 1.75 K with some time constant – here assumed as 1 minute – 2mK/Bit over 40 to 1.75 K range |
| SetEVHSHeatB 0x0000 | EVHSHeatCur | 0x0800 | 0x0000 | This opens the evaporator heat switch allowing the evaporator temperature to fall as the 3He is pumped. |
|  | EVHSHeatVolt | 0x61F7 | 0x0000 | As current is switched off voltage falls to 0 as well |
|  | SubKTempP | 0x06D6 | 1.75 – 1.45(1 – e-t/60) This is dec see below for hex conversion | Evaporator falls to 300 mK with some time constant – assume 1 minute – not correct but we can’t wait all day!. The resolution versus temperature is weird – see below – and should be replicated as the temperature will appear to rise before it falls! This is the “cooling” operating condition – these values are maintained during all observations. |

### SubKtemp conversion curve

Coefficients for resolution versus temperature (in IDL syntax) are approximately:

cf=[0.032015060,-0.0039288996,-1.1377826,3.3303894,-1.2193793]

So the temperature resolution will follow this curve as a function of temperature (in K)

mK/bit(T)= cf(0)+cf(1)*htemp+cf(2)*htemp^2+cf(3)*htemp^3+cf(4)*htemp^4

This combined with the exponential decay in temperature results in the response in terms of ADU as a function of time looking like this.

Simulated response of the SubKtemp parameter as the evaporator cools to 300 mK.  ADU is dec here – convert to Hex for simulator output.

# MCU

General Description:

The SMEC and BSM are controlled by a motion control unit based on a DSP – this appears as hardware to the outside world although it has a reasonably sophisticated “firmware” system for motion control.  The first operation for the MCU is to switch it on and get it initialised.  The unit is powered by a command to the SCU to switch supply from the power supply unit to the MCU.  The DSP is commanded to boot from PROM and the boot status word is set.  The unit is now ready to accept commands from the DPU.

| Command sent | Parameter that should respond | Status/value before | Status/value after | Comment |
| --- | --- | --- | --- | --- |
| DrelOnOff 0x0004 This is a command to the SCU | P5V | Undetermined | 0xA804 | Assume MCU voltages digitised to (16 V fullscale this is 0.488 mV/bit with 0V = 0x7FFF |
|  | P15V | Undetermined | 0xF810 | Ditto |
|  | M15V | Undetermined | 0x07ED | Ditto |
|  | P13V | Undetermined | 0xE80E | Ditto |
|  | M13V | Undetermined | 0x17EF | Ditto |
|  | MACTemp | Undetermined | 0x1000 | Same as for SCU board temps |
|  | SMECTemp | Undetermined | 0x1000 | Ditto |
|  | BSMTemp | Undetermined | 0x1000 | Ditto |
| SetDownLoadConf 0xC000 Wait 10 seconds to simulate boot of DSP | BootStatusRegister | Undetermined | 0x0004 | Set to this value during simulated upload |
| After 10 seconds | BootStatusRegister | 0x0004 | 0x0001 | Simulates successful boot from PROM |
| SetBootRAM 0x0001 | BootRAM | 0x0000 | 0x0001 | Launches program from RAM |

# Launch Latches

# The SMEC has a physical movement restriction provided by a solenoid type latch.  This must be activated and moved to an “unlatched” position before the mechanism can be used.  A dedicated command is provided for each latch to engage/disengage it.  The status of the latch is set following the command to be the same as the command – there is no independent confirmation of the latch status except through EGSE.

Comments:

The BSM latch will not be fitted so the command is now redundant.

Need to make the inadvertent use of the “latch engage” and “latch disengage” commands difficult or impossible.  Methods of doing this could be a double command scenario or by only allowing the commands when the SMEC status shows the SMEC is in the correct position.  This is being discussed as part of the OBS specification.

| Command sent | Parameter that should respond | Status/value before | Status/value after | Comment |
| --- | --- | --- | --- | --- |
| SetSLaunchLatch 0x0001 | SlaunchLatch | 0x0002 Disengaged | 0x0001 Engaged | The parameter that is read back is a reflection of the command sent – NOT an indication that anything has actually happened! |
| SetSLaunchLatch 0x0002 | SetSlaunchLatch | 0x0001 Engaged | 0x0002 Disengaged | Ditto |

# Telemetry

The data sampling and collection is initiated independently from the mechanism operation.  The sampling rate is determined as a fixed number of cycles of the basic DSP software cycle time of 360 sec.  There are two packet types for nominal operation “10” which is the SMEC data and “12” which is the BSM data.  During nominal scan mode operations we expect to sample the SMEC packet at 240 Hz (11 DSP cycles) and the BSM packet at up to 64 Hz (44 DSP cycles) (assume just these two speeds for now – different ops. Modes may need other sampling rates).  The values of the parameters in the packets should reflect what is going on with the subsystem – so during scanning for instance the encoder and LVDT position values should increase in the same manner as the housekeeping values.

The appropriate frame type and the transfer of the frames should all be set up and running before the sub-system is operated.   If continuous data transfer has been requested it must be stopped by command at the appropriate time – i.e. the end of operations.  In nominal operations the DPU command sequences will take care of all this.

Here are the command responses expected for setting first the SMEC packet followed by setting the BSM packet followed by setting no packet transfer.

This is the commanding scheme as defined in the MCU ICD v3.0 and DRCU/DPU ICD v1.0 and therefore implemented in the QM0 MCU.  We are seeking a change to this command scheme to the one defined in the MCU ICD v3.1 which separates the definition of the sampling frequency from the action starting the frame transfer.

| Command sent | Parameter that should respond | Status/value before | Status/value after | Comment |
| --- | --- | --- | --- | --- |
| SetTP10SampFreq 0x000B | TP10SampFreq | 0x0000 Packet 10 not being sent | 0x000B | This sets 240 Hz sampling of the SMEC packet. The packets start being sent when this command executes |
|  | TelemetryStatus | 0x0000 No packet being sent | 0x0001 Packet 10 is being sent | This is a new parameter since last issue – I assume the bit pattern is: 0 – TP10 on/off 1 - TP12 on/off 2 – TP14 on/off 3 – TP15 on/off |
| SetTP10SampFreq 0x0000 | TP10SampFreq | 0x000B Packet 10 is being sent | 0x0000 | This turns off packet 10 transmission |
|  | TelemetryStatus | 0x0001 Packet 10 is being sent | 0x0000 No packet being sent | See above |
| SetTP12SampFreq 0x002C | TP10SampFreq | 0x0000 | 0x002C | This sets ~64 Hz sampling and the packets start being sent when this command executes |
|  | TelemetryStatus | 0x0000 No packet being sent | 0x0002 Packet 12 is being sent | See above |
| SetTP12SampFreq 0x0000 | TP10SampFreq | 0x002C | 0x0000 | This sets ~64 Hz sampling and the packets start being sent when this command executes |
|  | TelemetryStatus | 0x0002 Packet 12 is being sent | 0x0000 No packet being sent | See above |

# SMEC

The SMEC has two nominal operating modes: step and look and rapid scan.  In both cases, the mechanism must first be initialised by switching it on and finding the home position.

# Initialisation

The first stage of initialisation is to apply power to the various parts of the SMEC system – namely:

The optical encoder pre-amplifier (I can’t see the command to do this – I assume it comes on with the power up?)

The optical encoder LED

The LVDT

The motor drive current amplifier

To do this safely the system must also be commanded definitively into open loop control mode.  Once the power has been applied the SMEC can be sent to home position which I assume to be at –3.2 mm from the ZPD.  I also assume that the encoder increment step zero is at the mechanical end stop which is –5 mm from the ZPD.  These values are almost certainly wrong but serve to illustrate the operation.  Finding the home position is an automatic procedure within the MCU unit.

Switching on the optical encoder LED will cause a signal to be seen on each of the three photodiodes within the optical encoder.  If the encoder is switched on successfully the SMEC status Encoder Signals bit is set high.

Switching on the LVDT will lead to a signal on the LVDT AC and DC signals.  There is a more-or-less linear relationship between the LVDT signal and position within a (4 mm range around ZPD Outside of this range the relationship is highly non-linear (see appendix with a note on this from Didier).   For the present purposes I assume that the signal saturates at the 4 mm value at either end of the (4 mm range.

With everything switched, on the SMEC is commanded to initialise itself; the result is that the SMEC ends up at the Home position and the MCU knows where it is in terms of encoder position.  After the SMEC has been sent to the home position the optical encoder and LVDT position should have definitive values and the SMEC status Home bit is set high.

Once the SMEC has been initialised it can be commanded to closed loop mode on the optical encoder.  Doing this causes the SMEC status Open/Closed Loop bit to be set high as long as there is no error status flag set (this needs more description/explanation from Didier – for present purposes can we assume that the SmecStatus bit 1 has to be 0 – i.e. no error flag is set?  Should other things also be checked – like the encoder is set correctly etc).

# Operation

Once the initialisation is completed successfully the SMEC operation is straightforward.  In scan mode the start and stop positions; the velocity and the number of scans to execute are commanded separately followed by a command to commence scanning in the desired mode (saw tooth or triangular).  As the mechanism scans, the motor current, back e.m.f and the encoder position will follow the mechanism motion.  The SMEC Status Scientific Operation bit is set high for the duration of the operation.  When the SMEC position is within the range of the LVDT, the LVDT Position value will also follow the motion.

In step mode the stop position is commanded followed by an instruction to move.  This causes the SMEC to move as fast a possible to the commanded position.  The encoder position will change to the commanded position and the motor current and back e.m.f will also respond.  When the SMEC position is within the range of the LVDT, the LVDT position will also change.  For the present purpose we can assume that the LVDT and encoder will give the same position.

Version 0.3 Notes:

I have made up all the conversion curves based on what I have from Didier from the benchtop testing.  It may not be quite right but it will do for the present purposes.

Questions/comments:

There ought to be a DPU housekeeping parameter to indicate that packets are being received from the MCU.

How does Home position get found following scan mode or step and look operation?  Can the mechanism be commanded “Go Home” with the status bit being set as necessary.

Also (see below) the step and look operation needs some more thought – we need to be able to command the number of repeat scans (if any) and to indicate – by the status bit? – that the SMEC is still in scientific operation mode during the whole of a step and look scan.

The SMEC status definition used here is the old one – Didier has proposed a new definition which I’ll use when it has been agreed.

Need to sort out how the Error Code is used to indicate that all is well – this is still not described in the ICD – note that the new SMECStatus proposal uses Status bits to indicate error conditions – the error code could be suppressed?

| Command sent | Parameter that should respond | Status/value before | Status/value after | Comment |
| --- | --- | --- | --- | --- |
| SetSEncoderPwr 0x0003 | SencoderPwr | 0x0000 | 0x0003 | Sets encoder LED to ~half power |
|  | SmecStatus | 0x0000 | 0x0080 | Bit 7 is set to show that the encoder LED has been switched on. |
|  | SEncoderSignal1 | 0x0000 | 0x7FFF | Completely made up see simulated conversion curve below! |
|  | SEncoderSignal2 | 0x0000 | 0xC9E8 | Completely made up see simulated conversion curve below! |
|  | SEncoderSignal3 | 0x0000 | 0x3616 | Completely made up see simulated conversion curve below! |
| SetSLVDTPwr 0x0001 | LVDTPwr | 0x0000 | 0x0001 | Switches power on to LVDT |
|  | LVDTAC | 0x0000 | 0x1DB7 | Conversion curve is as defined below taken from DF’s note. Conversion is assumed to be valid only between (5 mm from ZPD. This is smoothed signal |
|  | LVDTDC | 0x0000 | 0x1DBA | This is noisy version of LVDT signal – simulated as “slightly different” from LVDTAC |
|  | LVDTposition | 0x0000 | 0x0000 | LVDT position will read full negative range until the SMEC is initialised (?) |
| SetStrajMode 0x0004 (Cross check with Didier) | StrajMode | 0x0000 | 0x0004 | Sets the mode to initialisation. Not sure if the value 4 is set or bit 4 is set? |
|  | SmecStatus | 0x0080 | 0x0188 | Mechanism ends up at Home (bit 3?) Encoder has been initialised (bit 8?) |
|  | SEncoderSignal1 | 0x7FFF | 0xD527 | Completely made up see simulated conversion curve below! |
|  | SEncoderSignal2 | 0xC9E8 | 0x5A4F | Completely made up see simulated conversion curve below! |
|  | SEncoderSignal3 | 0x3616 | 0x5085 | Completely made up see simulated conversion curve below! |
|  | LVDTAC | 0x1DB7 | 0x315F | Home position is 1800 microns from mech. End stop (-3.2 mm from ZPD) |
|  | LVDTDC | 0x1DBA | 0x3165 | Bit different just for the sake of it. |
|  | LVDT Position | 0x0000 | 0x0709 | Ah! How does this get counted? I am assuming in microns from the mechanical reference to keep it in line with the optical; encoder. This is 1801 dec. |
|  | SMotorCurrent | 0x0000 | 0x03E8 | Completely fictitious assuming value 1000 at home rising to 50000 at full scale |
|  | SBEMF | 0x0000 | 0x03E8 | Total nonsense but assume same as current |
|  | EncoderIncrPosition | 0x0000 | 0x0708 | This is position 1800 – as for LVDTPosition |
|  | EncoderFinePosition | 0x0000 | 0x0000 | This is the position at 10 nm/bit – assume its zero at Home |
| SetSLoopMode 0x0001 | SloopMode | 0x0000 | 0x0001 | Loop is closed on the encoder using signals from 0th and 1st order. |
|  | SmecStatus | 0x0188 | 0x0588 | Status bit 10 is set? |

The SMEC is now initialised at HOME position 0 the next table deals with commands for the scan and step and look modes of operation.

| Command sent | Parameter that should respond | Status/value before | Status/value after | Comment |
| --- | --- | --- | --- | --- |
| SetSScanFwdSpeed | SScanFwdSpeed | 0x0000 | 0x1388 | Set the speed for the forward going scans. Value set as 0.1 m/s per bit – set here to 500 m/s |
| SetSScanRevSpeed | SScanFwdSpeed | 0x0000 | 0x1388 | Ditto for the reverse going scans. Set at the same speed. |
| SetSScanNumber 0x0002 | SScanNumber | 0x0000 | 0x0002 | Sets number of scans to do 2 here (one back one rev?) Default value is for infinite? |
| SetSTrajStartPosition 0x076C | STrajStartPosition | 0x0000 | 0x076C | Start scan at –3.1 mm from ZPD – step 1900 |
| SetSTrajEndPosition 0x1FA4 | STrajEndPosition | 0x0000 | 0x1FA4 | Scan to +3.1 mm from ZPD – step 8100 |
| SetStrajMode 0x0002 (Forward and reverse scanning) | StrajMode | 0x0000 | 0x0002 | Not sure if value 2 is set or bit 2 is set |
|  | SmecStatus | 0x1088 | 0x9080 during operation 0x1088 at end of operation | Mechanism starts and ends up at Home (correct?) Also bit 16 gets set during operation to indicate something is going on |
|  | SEncoderSignal1 | 0xD527 | Follows position with D=1900 at start and D=8100 at end incrementing by 500 per sec | Completely made up see simulated conversion curve below! |
|  | SEncoderSignal2 | 0x5A4F | Follows position with D=1900 at start and D=8100 at end incrementing by 500 per sec | Completely made up see simulated conversion curve below! |
|  | SEncoderSignal3 | 0x5085 | Follows position with D=1900 at start and D=8100 at end incrementing by 500 per sec | Completely made up see simulated conversion curve below! |
|  | LVDTAC | 0x315F | Goes to 0x33D4 at start of scan then Increases at 3145 ADUs/sec until 0xCC2A then decreases at 3145 ADUs/sec until 0x33D4. At end of operation goes to 0x315F | At Home at start and end of operation. |
|  | LVDTDC | 0x3165 | As above with some noise added! | At Home at start and end of operation. |
|  | LVDT Position | 0x0709 | Goes to 0x076D at start of scan then Increases at 500 ADUs/sec until 0x1FA5 then decreases at 500 ADUs/sec until 0x076D. At end of operation goes to 0x0709 | Starts and finishes at home. |
|  | SMotorCurrent | 0x03E8 | Goes to 0x041F at start of scan then Increases at 700 ADUs/sec until 0x2607 then decreases at 700 ADUs/sec until 0x041F. At end of operation goes to 0x03E8 | This is fantasy again! Need real conversion curve between motor current and physical position |
|  | SBEMF | 0x03E8 | Goes to 0x041F at start of scan then Increases at 700 ADUs/sec until 0x2607 then decreases at 700 ADUs/sec until 0x041F. At end of operation goes to 0x03E8 | This is fantasy again! Need real conversion curve between motor back e.m.f and physical position |
|  | EncoderIncrPosition | 0x0708 | Goes to 0x076C at start of scan then Increases at 500 ADUs/sec until 0x1FA4 then decreases at 500 ADUs/sec until 0x076C. At end of operation goes to 0x0709 | Start and finishes at home |
|  | EncoderFinePosition | 0x0000 | Increments at 50000 ADU/sec for forward scan then decrements at 50000 ADU/sec for reverse scan Reset to 0 at end of scan | This is the position at 10 nm/bit – assume its zero at Home – increments to 216-1 then wraps round. Not sure what happens at home position – I assume it gets reset – this is convenient for testing here anyway. |
|  | ActualVelocity | 0x0000 | 0x1388 during scan in both directions | In reality it will have some noise should add random noise with amplitude of 10 How do we indicate scan direction – should this value have a sign bit? |
|  | MeanSpeed | 0x0000 | 0x1388 during scan in both directions | In reality it may have some noise – this is o.k. for now How do we indicate scan direction? |
| SetSTrajMode 0x0001 (Moves mechanism to value set by StrajEndPosition) | STrajMode | 0x0000 | 0x0001 | Not sure if value 1 is set or bit 1 is set |
|  | SmecStatus | 0x1088 | 0x9080 during operation 0x1088 at end of operation? | Indicates mechanism is doing something and then that its idle This needs to change we need a bit to be set during whole of step and look scan? |
|  | SEncoderSignal1 | 0xD527 | 0x580D (D=8100) | Completely made up see simulated conversion curve below! |
|  | SEncoderSignal2 | 0x5A4F | 0x52A8 | Completely made up see simulated conversion curve below! |
|  | SEncoderSignal3 | 0x5085 | 0xD548 | Completely made up see simulated conversion curve below! |
|  | LVDTAC | 0x315F | 0xCC2A | Starts at home goes to end of scan position |
|  | LVDTDC | 0x3165 | 0xCC2A | Starts at home goes to end of scan position |
|  | LVDT Position | 0x0709 | 0x1FA5 | Starts at home goes to end of scan position |
|  | SMotorCurrent | 0x03E8 | 0x2607 | Comment as before |
|  | SBEMF | 0x03E8 | 0x2607 | Comment as before |
|  | EncoderIncrPosition | 0x0708 | 0x1FA4 | Starts at home goes to end of scan position |
|  | EncoderFinePosition | 0x0000 | Set to random vale between 0 and 216-1 | This is the position at 10 nm/bit – assume its zero at Home – and we get some jitter for the position setting. |

### Encoder signals simulation

I assume that the three encoder signals respond in the following fashion as a function of distance, D, from the mechanical reference in microns (psuedo code):

ADU = 215-1 + (sin(D/2+ { case encoder eq 1,2,3 (0, 2/3, 4/3) } )/4.577x10-5)

### LVDT Signal Simulation

Taken from Didier Ferrand’s note on the bench measurements of the Schaevitz MHR100.  The ADU for the signal is linear (ish) over the range from –4 mm to +4 mm from the centre of the LVDT range

ADU = (215-1) + 6.29 (D-5000)

D is the distance from mechanical end stop –i.e. encoder increment step 0.  ZPD is supposed to be at 5 mm (or 5000 steps) from the mechanical stop.

# BSM

The Beam Steering Mirror (BSM) has two separately controlled axes – CHOP and JIGGLE.  It is controlled by directly commanding the position of either axis from the DPU.  Once a position is commanded the MCU controls the motion to get to the given position.   The chop mode of the instrument is carried out by sending a series of commands to the MCU from the DPU – i.e. there will be no autonomous chop operation – unlike the SMEC scanning.

| Command sent | Parameter that should respond | Status/value before | Status/value after | Comment |
| --- | --- | --- | --- | --- |
| SetCSensorPwr 0x0001 | CsensorPower | 0x0000 | 0x0001 | Turn on the chop sensor |
|  | ChopStatus (bit N) | 0 | 1 | Bit values not yet defined? |
|  | CMagnetoresistiveSignal | 0x0000 | 0x8000 | The actual value of the sensor output Assumes starts at middle of range |
| SetJSensorPwr 0x0001 | JsensorPower | 0x0000 | 0x0001 | Turn on the jiggle sensor |
|  | JigStatus (bit N) | 0 | 1 | Bit values not yet defined? |
|  | JMagnetoresistiveSignal | 0x0000 | 0x8000 | The actual value of the sensor output Assumes starts at middle of range |
| SetBSMMove 0x0000 | BSMMove | Undefined? | 0x0000 | This means the axes move independently when the TargetPosition is set. What is the value of this when the MCU boots? I think this should be the default and therefore this command is redundant? |
|  | ChopStatus(Bit N) | 0 | 1 | Bit set to reflect operating mode? |
|  | JigStatus(Bit N) | 0 | 1 | Bit set to reflect operating mode? |
| SetChopTargetPosition | ChopTarget Position | 0x0000 | 0x8000 | Set the desired position to the middle of the range as well |
| SetJigTargetPosition | JigTarget Position | 0x0000 | 0x8000 | Set the desired position to the middle of the range as well |
| SetChopLoopMode 0x0001 | ChopStatus (Bit N) | 0 | 1 | This closes the servo loop between the motor drive and the position sensor – if all is working properly nothing should happen! There should be a Status bit that tells us this has happened successfully - Bit values not yet defined? |
|  | CmeanPositionError | Undefined | 0x0000 | As the loop closes the error signal should be 0? What is the value before the loop is closed? |
| SetJigLoopMode 0x0001 | JigStatus (Bit N) | 0 | 1 | This closes the servo loop between the motor drive and the position sensor – if all is working properly nothing should happen! There should be a Status bit that tells us this has happened successfully - Bit values not yet defined? |
|  | JmeanPositionError | Undefined | 0x0000 | As the loop closes the error signal should be 0? What is the value before the loop is closed? |
| SetBSMMove 0x0001 | BSMMove | 0x0000 | 0x0001 | This means the axes synchronously move to the position set by TargetPosition only when a further BSMMove(1) command is sent. On issuing the command at this time nothing happens except the mode is changed? I think this is necessary otherwise I can’t see logically how we get out of the other mode without the BSM moving!? |
|  | ChopStatus(Bit N) | 0 | 1 | Bit set to reflect operating mode? |
|  | JigStatus(Bit N) | 0 | 1 | Bit set to reflect operating mode? |

The BSM is now initialised at its “rest” – zero current – position and can now be used operationally.  The following commands move the BSM to an example position – repeat as required for chop/jiggle modes.

| Command sent | Parameter that should respond | Status/value before | Status/value after | Comment |
| --- | --- | --- | --- | --- |
| SetChopTargetPosition | ChopTarget Position | 0x8000 | 0xAAAB | Set the desired position to positive half range in chop (see below) |
| SetJigTargetPosition | JigTarget Position | 0x8000 | 0x8AAB | Set the desired position to positive half range in jiggle (see below) |
| SetBSMMove 0x0001 | CMagnetoresistiveSignal | 0x8000 | 0xA55B | See conversion curve below |
|  | CmotorCurrent | 0x8000 | 0x4CCD | Starts at zero goes to –20 mA |
|  | CBEMF | 0x8000 | 0x4CCD | Follows current exactly (wrong but what can you do!) |
|  | CmeanPositionError | 0x0000 | 0x0000 | Should be zero |
|  | JMagnetoresistiveSignal | 0x8000 | 0x8957 | See conversion curve below |
|  | JMotorCurrent | 0x8000 | 0x7333 | Starts at zero goes to –5 mA |
|  | JBEMF | 0x8000 | 0x7333 | Follows current exactly (wrong but what can you do!) |
|  | JmeanPositionError | 0x0000 | 0x0000 | Should be 0 |

### Conversion curve for commanded position

Assume that 215 bits represents 1.5x full deviation in chop axis (guesswork!) – so this means 0.00549316 arcsec/bit for commands and – given P is position in (arcsec about the rest position we have:

TargetPosition = (215)+ P/0.00549316 adu

Assume this is true for both jiggle and chop.  In the example given in the tables the chop and jiggle are commanded to half range: +60 arcsec and +15 arsec respectively, or 43691 and 35499 dec.

### Conversion curve for position sensor output

Kludged from Didier’s document – assume (7V is full scale movement on chop ((2 arcmin) digitise to (12V full scale (0.366e-3 V/bit) this gives 19126 ADU for 120 arcsec deflection or 0.00627418 arcsec/bit

MagnetoresistiveSignal = (215-1) + P/0.00627418 adu

P is position in (arcsec from boresight.   For simplicity use this on both axes.

### Conversion curve for motor current and BEMF

Assume current is zero at rest position and goes (50 mA full scale or 0.00152588 mA/bit.  Assume BEMF is the same (wrong but needs proper calibration).  Just for fun assume that positive deflection requires negative current.  So +120 arcsec needs –40 mA giving 3 arcsec/mA in each axis.  So the current (and BEMF) conversion used for the simulator is:

Current = 215 – P/ 0.00457764 adu

## DCU

The DCU provides power; signal conditioning and data acquisition for the detectors on the SPIRE FPU.   The unit is powered on when the 28 V power is applied to the DRCU power supply unit.   A separate command is sent to the SCU to switch on EITHER the photometer or the spectrometer LIA cards – in the commands given below it is assumed we go into one or other mode following power up not from one to the other.  Note also that the parameters listed here are accessed by the DCU GetHKChannel command with the appropriate ID and not as separate “Getparam” commands.

I assume that at power on the FPGA enters a reset state, boots in some fashion, counts its fingers and starts sending housekeeping when asked.  It is then ready to accept commands from the DPU.  I assume this is the same as for the SCU as it is a standard interface?

| Command sent | Parameter that should respond | Status/value before | Status/value after | Comment |
| --- | --- | --- | --- | --- |
| Request to CDMS to switch on 28V line to DRCU | DAQ_IF_TEMP | Undetermined | 0x4001 | Complete guess Need conversion curve between ADC value and temperature |
|  | BIAS_TEMP | Undetermined | 0x4002 | Guess again – bit different to make sure in right place |
|  | LIA_B#_TEMP (12 boards in all # = 1 to 12) | Undetermined | 0x4003 | Guess again – bit different to make sure in right place |
|  | PWR_STATUS (12 bits – one for each LIA card) | Undetermined | 0x0000 | Bits only set when LIA cards are turned on |
|  | BDAQ_P5 | Undetermined | 0xB554 | Used 0.366211 mV/ADU over +-12V with 215-1 = 0V |
|  | BDAQ_P9 | Undetermined | 0xE00D | ditto |
|  | BDAQ_N9 | Undetermined | 0x1FF0 | ditto |
| SCU Command DrelOnoff 0x0002 | PWR_STATUS | 0x0000 | 0x01FF | Photometer LIA cards switched on – I assume bits 0-8 are P and 9-11 are S? |
|  | LIAP_P5 | 0x0000 | 0xB554 | Used 0.366211 mV/ADU over +-12V with 215-1 = 0V |
|  | LIAP_P9 | 0x0000 | 0xE00D | ditto |
|  | LIAP_N9 | 0x0000 | 0x1FF0 | ditto |
| SCU Command DrelOnoff 0x0004 | PWR_STATUS | 0x0000 | 0x0E00 | Spectrometer LIA cards switched on – I assume bits 0-8 are P and 9-11 are S? |
|  | LIAP_P5 | 0x0000 | 0xB554 | Used 0.366211 mV/ADU over +-12V with 215-1 = 0V |
|  | LIAP_P9 | 0x0000 | 0xE00D | ditto |
|  | LIAP_N9 | 0x0000 | 0x1FF0 | ditto |

Initialisation

The DRCU/DPU ICD has a pretty comprehensive commanding scenario set out.  As far as I can tell apart from the housekeeping reflecting the commanded values or status – no other parameters change for ANY of the DCU commands!  The only thing that happens is that the detector offsets will change (to a value commensurate with the combination of the bias amplitude and the background power) and the detector noise will increase.

These commands set up the photometer JFETs; bias levels and bias frequencies and run the automatic offset routine.  A similar set of commands is used for the spectrometer I won’t bother to repeat them.

The command order used here is slightly different from those proposed in the ICD and starts with switching up the JFETs and then the detector conditioning voltages.

The thermal control system will be dealt with separately at some future date.

| Command sent | Parameter that should respond | Status/value before | Status/value after | Comment |
| --- | --- | --- | --- | --- |
| SetPhSWJfetVSS# # =1 to 6 0x007F | PhSWJfetVSS# | 0x0000 | 0x007F | All SW detector JFET source voltages switched to half level. There is no indication that anything has happened except reflection of commanded value |
| SetPhMWJfetVSS# # =1 to 4 0x007F | PhMWJfetVSS# | 0x0000 | 0x007F | All MW detector JFET source voltages switched to half level. There is no indication that anything has happened except reflection of commanded value |
| SetPhLWJfetVSS# # =1 to 2 0x007F | PhMWJfetVSS# | 0x0000 | 0x007F | All LW detector JFET source voltages switched to half level. There is no indication that anything has happened except reflection of commanded value |
| SetPhSWJfetPwr 0x003F | PhSWJfetPwr | 0x0000 | 0x003F | All SW JFET drain voltages are switched high. There is no indication that anything has happened except reflection of commanded value |
| SetPhMWJfetPwr 0x003F | PhMWJfetPwr | 0x0000 | 0x003F | All MW and LW JFET drain voltages are switched high. There is no indication that anything has happened except reflection of commanded value |
| SetPhotoHeaterBias 0x007F | PhotoHeaterBias | 0x0000 | 0x007F | The heater in the JFET modules is set to half power for a few minutes (say 1 for these purposes)…. |
| SetPhotoHeaterBias 0x0000 | PhotoHeaterBias | 0x007F | 0x0000 | And then heater switched off |

The photometer JFETs should now be switched on and at there operating voltage.  At this stage there is no definitive indication that this has actually happened – i.e. no independent confirmation is available of the temperature of the JFETs or that the voltages are actually appearing at the JFET membranes.  We have to wait until the detectors and LIAs are operating.  Again I have changed the order of the commanding compared to the DRCU/DPU ICD.  Here the bias frequency is set first – i.e. the LIAs begin to operate - and the noise checked before the amplitude; phase and offset are set.   The sampling of the detector data is synchronous with the sinusoidal bias voltage frequency in order to avoid aliasing.   The bias frequency is set as a division of the DCU 10 MHz master clock and will be between ~50 and 300 Hz.  The sampling rate is set as a division of the bias frequency.

| Command sent | Parameter that should respond | Status/value before | Status/value after | Comment |
| --- | --- | --- | --- | --- |
| SetPhotoBiasFreq 0x0062 | PhotoBiasFreq | 0x0000 | 0x0062 | Sets the bias frequency to ~200 Hz (10MHz/(512x98) |
| SetPhotoSampFreq 0x000C | PhotoSampFreq | 0x0000 | 0x000C | Sets the sampling frequency to ~15.3 Hz (200/(1+12)) |
| SetPhotoBiasMode 0x00FF | PhotoBiasMode | 0x0000 | 0x00FF | Starts the bias generation in sine mode and sets the LIA references running I am assuming this is what happens - CCara to confirm. |

I believe at this point the amplifiers should be working and it should be possible to sample the data – noise – coming from the JFETS.  The signal level should reflect the JFET noise of ~15 nV/Hz-1/2.  If we assume 5 Hz bandwidth, gain of ~450x12 and 16 bits digitisation at the ADC with 5 V full scale (2.3951 V/bit ), there will be random noise on the signal with an amplitude of ~2.4 bits.

This is actually the only test we have available that all is well.  See the last section for how the science data collection gets set up.  Meanwhile let’s turn on the detectors!  First set the amplitude then set the phase.  Once this is done – on the assumption that the phase is set correctly – we can run the automatic offset operation.

| Command sent | Parameter that should respond | Status/value before | Status/value after | Comment |
| --- | --- | --- | --- | --- |
| SetPhotoBiasAmplSW 0x004D | PhotoBiasAmplSW | 0x0000 | 0x004D | Sets bias to ~60 mV. The parameter read back is the DAC value |
| SetPhotoBiasAmplMW 0x004D | PhotoBiasAmplMW | 0x0000 | 0x004D | Sets bias to ~60 mV. The parameter read back is the DAC value |
| SetPhotoBiasAmplLW 0x004D | PhotoBiasAmplLW | 0x0000 | 0x004D | Sets bias to ~60 mV. The parameter read back is the DAC value |
| SetPhotoDemodSW | PhotoDemodSW | 0x0000 | 0x007F | Phase set to 180 degrees. The parameter read back is the DAC value |
| SetPhotoDemodMW | PhotoDemodMW | 0x0000 | 0x007F | Phase set to 180 degrees. The parameter read back is the DAC value |
| SetPhotoDemodLW | PhotoDemodLW | 0x0000 | 0x007F | Phase set to 180 degrees. The parameter read back is the DAC value |
| SetDataMode 0x0010 | DataMode | 0x0000 (?) | 0x0010 | This sets the operational mode to the automatic offset setting for the photometer. After a few seconds the offset values will respond if the electronics chain and detectors are working normally. Note that the default – i.e. a value of 0x0000 - is “photometer normal” |
|  | LIAP#Offset # = 1 to 9 The 32 channel IDs per LIA card are encoded in bits 4 to 8 and the offset value in 0 to 3 | 0x0000 | 0x0nn3 where nn goes from 0 to 1F for the channel number | Offset is a four bit number related to the bias and the resistance of the bolometer – let us assume it is fix(60/200x16) = 3 for the purposes of the simulation |
| SetDataMode 0x0000 | DataMode | 0x0010 | 0x0000 | Set the operational mode to normal bolometer again – noise at ~2-3 bits should appear on the science data. |

# Telemetry

These commands set the number of frames to be sent to the DPU – here set to be continuous – and the start and stop of the frame transmission.  The frame type is defined by DataMode this was set previously to full photometer.

| Command sent | Parameter that should respond | Status/value before | Status/value after | Comment |
| --- | --- | --- | --- | --- |
| SetFrameCount 0x0000 | FrameCount | 0x0000 | 0x0000 | It doesn’t appear that this command is necessary to get continuous frame transfer? |
| SetStartFrame 0x0001 | StartFrame | 0x0000 | 0x0001 | Starts frame transfer – something in the DPU should respond to frames starting to be sent? Send a few and then…. |
| SetStartFrame 0x0000 | StartFrame | 0x0001 | 0x0000 | Stops frame transfer – something in the DPU should respond to frames stopping being sent? |