## Slide 1
Instrument Design and Performance Update Matt Griffin Cardiff University

## Slide 2: Instrument Design Drivers
• Photometer - Deep mapping with highest efficiency and largest possible field of view - Multi-band coverage with simultaneous observation - Point and compact source observation with high efficiency
• Spectrometer - Sensitivity optimised for point/compact source spectroscopy - Imaging spectroscopy with maximum available field of view - Wide wavelength coverage - Variable spectral resolution (few x 10 to few x 100)
• Both - Thermal background dominated by the Herschel telescope - Simplicity, affordability, reliability, ease of operation - Complementary to other Herschel instruments and other facilities

## Slide 3: Instrument Summary
• 3-band imaging photometer - 250, 360, 520 m (simultaneous observation) -  ~ 3 - 4 x 8 arcminute field of view - Diffraction limited beams (17, 24, 35”) • Imaging FTS - 200 - 670 m - 2.6 arcminute field of view -  = 0.04 – 2 cm-1 ( ~ 20 - 1000 at 250 m) • Design features - Sensitivity limited by thermal emission from the telescope (Assumption: 80 K;  = 4%) - 3He cooled detector arrays (0.3 K) - Feedhorn-coupled spider web NTD bolometers - Minimal use of mechanisms - Beam steering mirror; FTS mirror drive - No on-board data processing or compression - Simple commanding scheme
PACS
HIFI
SPIRE
Cryostat lid
Baffle
Herscheloptical bench

## Slide 4: SPIRE Functional Block Diagram

## Slide 5: Design Changes Since IBDR
• Deletion of shutter (CTA will provide representative photon background) • Definition of grounding scheme in September 2002 • Thermal straps: - 300 mK design evolved - Level-0 in redesign - Level-3 (15-K) dedicated JFET thermal strap implemented to dump heat into the boil-off gas • FPU and detector box supports - Change from stainless steel to carbon fibre proposed
• Cold redundancy implemented for PCAL

## Slide 6: Instrument Design Overview
See SPIRE Design Description
(SPIRE-RAL-PRJ-000620)
for a comprehensive overview and description of the instrument

## Slide 7: Viewgraph from IBDR Presentation
Instrument design is stable and meets scientific requirements
SPIRE has already started to allow schedule to take priority over scientific optimisation of instrument performance
Main remaining technical challenges require “hard work” rather than new developments
  Thermal mechanical engineering
    Thermal straps: good progress but a lot to be done
    JFET dissipation: Not to be a major system problem but work needed to prevent performance degradation
    System-level thermal modelling urgently needed to assess whether the instrument as designed will operate in the right environment
    STM programme will provide early verification of performance and mitigate risk
  EMC and microphonics
  Stray light minimisation and prediction: requires system-level modelling
  Subsystem performance (esp. mechanisms, detectors)

## Slide 8
Sensitivity Models
• Sensitivity estimates detailed in SPIRE-QMW-NOT-000642 Issue 3.0 - Photometer sensitivity model updated - FTS model not updated (but new estimates are presented here)

## Slide 9
Model Updates
• Physical bolometer model incorporated
• Telescope obscuration up from 3% to 13%
• Lower bolometer Ro (was 180 , now 100 )
• Additional 2 noise contribution due to LIA demodulation included
• Nominal bolometer temperature up to 320 mK
• Overall transmission increased from 30% to 40%
• Feed efficiencies increased slightly
• Nominal, best and worst case values studied for all parameters

## Slide 10
Best, Nominal and Worst Case Parameters
#
• Telescope temperature 60 80 90
• Telescope emissivity 0.02 0.04 0.06
• Feedhorn/cavity efficiency 0.8 0.7 0.6
• Bolometer Ro () 180 100 70
• Bolometer temperature (mK) 300 320 340
• JFET noise (nV Hz-1/2) 7 10 15
• Bolometer yield 0.9 0.8 0.75
• Overall inst. transmission 0.48 0.4 0.32
• Observing efficiency 0.95 0.85 0.75
Best Nominal Worst

## Slide 11
Background Power, NEP and DQE (Nominal Case)

## Slide 12
Photometer Sensitivity (Nominal Case)
AO estimates (point source, 5- 1-hr) < 4 mJy in all three bands

## Slide 13
Mapping Speed (Best Case)

## Slide 14
Mapping Speed (Worst Case)

## Slide 15
Line Spectroscopy (Nominal Case)
AO estimate: 5- 1-hr: 4 x 10-17 W m-2 in 200-400 m band

## Slide 16
Line Spectroscopy (Best Case)

## Slide 17
Line Spectroscopy (Worst Case)

## Slide 18
Low-Resolution Spectrophotometry (Nominal Case)
AO proposal estimate: 5-; 1-hr: 130 mJy in 200-400 m band

## Slide 19: Thermal Stability: Thermal Control Hardware now Baselined
BDA hits limit at ~29.5 hours
Useable time for scan mode
300 mK: 0.6 to 1.2 K/Hz1/2 0.06 mK hr-1