Alignment Overview

The following table summarises the achievable alignment results (based on FEM analysis) and compares the results with the requirement.

Instruments w.r.t. Telescope (95% Confidence Level)

|  | PACS | SPIRE | HIFI | Telescope | Remarks |
| --- | --- | --- | --- | --- | --- |
| Achievable X Direction System Level | 5.1mm | 5.0mm | 7.4mm |  | w/o margin |
| Requirement • H-EPLM Requirement Specification • HIFI | 7.0mm | 7.7mm | 8.5mm 8.5mm |  | 2) |
| Instruments / Telescope Contribution • Uncertainty • Bias • Thermoelastic | 1.0mm 0mm 0.1mm | 0.5mm 0mm 0.1mm | 2.7mm 2.0mm 0.1mm | 4.3mm 3) 3) |  |
| Achievable Lateral System Level | 3.8mm | 4.2mm | 16.3mm |  | 1) |
| Requirement • H-EPLM Requirement Specification • HIFI | 7.0mm | 9.5mm | 24mm 24mm |  | 2) |
| Instruments / Telescope Contribution • Uncertainty • Bias • Thermoelastic | 0.5mm 0.5mm 0.1mm | 1.3mm 0mm 0.1mm | 10mm 1mm 0.1mm | 1.14mm 3) 3) |  |

- Pupil mismatch in M2 Plane

- Proposed by HIFI

- Uncertainty value includes bias and thermoelastics as agreed during HOWG Meeting, dated 11./12.06.02