### ANNEX 1 : list of applicable WU MICD

Source : CR H-P-ASP-CR-0469 sent to ALS by ASP on 22/07/03

Update of following interface drawings

For Herschel:

FH3DH and FH3DV: DR-521-001, Iss 1, dated 04/07/03

FHFCU: 324-E-5000, Iss b, 07/07/03

FHLCU: SRC/LCU/SP/2001-012, Iss 8, 12/06/03

FPBOLC: PACS-MX-2000 000 D, Iss D, Sep 02

FHSPU: FPL-ID-SPU-00002-CRS, Iss 3, 02/04/03

CCU: HP-2-PANT-ID-0035, Iss 1, 27/02/03

For Planck

4K CAU: PLS114FS002SA, Indice A, 22/07/03

4K CRU: CDE-ID-1275-00002-CRS, Iss 1 dr, 13/05/03

REBA: FPL-ID-REB-0002-CRS, Iss 3, 02/04/03

Corresponding lists of applicable drawings for Herschel and Planck are given in following tables

Instrument Warm Units reference table (Herschel SVM)

| INSTR. | ACRONYM | PRJ CODE | LATEST APPLICABLE DOCUMENT (FOR ALS) | REFERENCE DWG |
| --- | --- | --- | --- | --- |
|  |  |  |  | NUMBER | ISS. | DATE |
| HIFI | FH3DH (1) |  | CR 469 | DR 521-001 | 1 | 04-07-03 |
|  | FH3DV (1) |  | CR 469 | DR 521-001 | 1 | 04-07-03 |
|  | FHFCU |  | CR 469 | 324-E-5000 | b | 07-07-03 |
|  | FHHRH |  | CR 311 | CESR-HRS-MD-3151-103 | 3.4 | 08-11-02 |
|  | FHHRV |  | CR 311 | CESR-HRS-MD-3151-103 | 3.4 | 08-11-02 |
|  | FHICU |  | AD 4 | HER H004/02 |  | 10-02-02 |
|  | FHLCU |  | CR 469 | SRC/LCU/SP/2001-012 | 8 | 12-06-03 |
|  | FHLSU |  | CR 422 | ICD-HIF-157704 | P1 | 19-02-03 |
|  | FHWEH |  | CR 308 | WBE/DR/2000 | B rev 6 | 04-11-02 |
|  | FHWEV |  | CR 308 | WBE/DR/2000 | B rev 6 | 04-11-02 |
|  | FHWOH |  | CR 309 Issue 2 | UC 00.00 | 4 | 24-03-03 |
|  | FHWOV |  | CR 309 Issue 2 | UC 00.00 | 4 | 24-03-03 |
| PACS | FPBOLC |  | AD 5 + CR 469 | PACS-MX-2000 000 D | D | XX-09-02 |
|  | FPDPU |  | AD 5 | HER 005/02 |  | 02-05-02 |
|  | FPMEC-DEC |  | CR 394 | ME.HES.114P.S.001SA ind A (date 07-04-03) |  | 13-12-02 |
|  | FPSPU |  | AD 5 + CR 469 | FPL-ID-SPU-00002-CRS | 3 | 02-04-03 |
| SPIRE | HSDCU | FSDCU | CR 425 | SPIR-MX-5100 000 D | D | XX-10-02 |
|  | HSDPU | FSDPU | CR 425 | HER S005/03 | 4 | 23-02-03 |
|  | HSFCU | FSFCU | CR 425 | SPIR-MX-5200 000 F | F | XX-10-02 |

Latest applicable IID-B:

| INSTRUMENT | A.D. | ISSUE | REV. | DATE |
| --- | --- | --- | --- | --- |
| HIFI | 4 | 2 | 2 | 26-06-02 |
| PACS | 5 | 2 | 1 | 01-07-02 |
| SPIRE | 6 | 2 | 2 | 01-07-02 |

Interface to the Cryostat Control Unit (Herschel only)

Cryostat Control Unit reference table (Herschel SVM)

| ACRONYM | REFERENCE DOC | REFERENCE DWG |
| --- | --- | --- |
|  | NUMBER | ISSUE | DATE | NUMBER | ISSUE | DATE |
| CCU | HP-2-PANT-ID-23808.0 |  |  | HP-2-PANT-ID-0035 | 1 | 27-02-03 |

Instrument Warm Units reference table (Planck SVM)

| INSTR. | ACRONYM | PRJ CODE | LATEST APPLICABLE DOCUMENT | REFERENCE DWG |
| --- | --- | --- | --- | --- |
|  |  |  |  | NUMBER | ISS. | DATE |
| HFI | 4CAU | PHDB | AD 7 + CR 387 + CR 469 | PLS.114F.S.002SA | A | 22/07/03 |
|  | 4CCU | PHDA | AD 7 + ICD-PLANCK4K-AST-012 Issue 2 | CD65720 SHEET 1/2 & 2/2 | 01 | 08-03-02 |
|  | 4CRU | PHDJ | AD 7 + CR 469 | CDE-ID-1275-00002-CRS | 1 draft | 13/05/03 |
|  | HeTANK | PHEAA/B | AD 7 | F4060A RSKTO51A1006 | AD | 15-01-98 |
|  | 4KCDE | PHDC | AD 7 + IC-PHDC-000009-SEA Issue 2 draft A +CR 387 | O-KE-0151-001-E | E | 11/09/02 |
|  | DCCU | PHEC | AD 7+CR 387 | H0201C006 H0201C009 | A A | 30-03-03 30-03-03 |
|  | DPU | PHBA-N/R | AD 7+CR 387 | I592EB003 | B | 02/12/02 |
|  | PAU | PHCBA | AD 7 +CR 337 Issue 2 | 7137-QD0-000 | A | 13-05-03 |
|  | REU | PHCBC | AD 7 +CR 344 | REU ICD IF- PHCBC282-200050-CESR+updated drawing | V2 | 30/01/03 |
| LFI | BEU | PLBEU | AD 8 | Draft sheet 1/2 & 2/2 | DRAFT | 12-06-02 |
|  | DAE-PB | PLAEF | AD 8 | Draft sheet 1/2 & 2/2 | DRAFT | 22-03-02 |
|  | REBA | PLREN/R | AD 8+ CR 469 | FPL-ID-REB-0002-CRS | 3 | 02-04-03 |
| SCS | SCC | PSM3/R3 | AD 8 +CR 338 | 10203010 4 sheets | X20 | 21/02/02 (erroneous) |
|  | SCE | PSM4/R4 | AD 8 | 941000 941001 |  | 18/01/02 09/04/02 |

Latest applicable IID-B:

| INSTRUMENT | A.D. | ISSUE | REV. | DATE |
| --- | --- | --- | --- | --- |
| HFI | 7 | 2 | 1 | 01-07-02 |
| LFI | 8 | 2 | 1 | 01-07-02 |
| SCS | 8 | 2 | 1 | 01-07-02 |

Interfaces to the Customer Furnished Equipment (SREM, VMC)

Customer Furnished Equipment reference table (Herschel/Planck SVM)

| ACRONYM | REFERENCE DOC | REFERENCE DWG |
| --- | --- | --- |
|  | NUMBER | ISSUE | DATE | NUMBER | ISSUE | DATE |
| SREM | SREM-DI-CSAG-003 | 1.2 | 15-12-00 | CR 207 374 AZ C | AC | 27-01-99 |
| VMC |  |  |  |  |  |  |
| FOG |  |  |  | DT0051932 | 01 rev 00 |  |

XXX = HES for Herschel or PLS for Planck

### ANNEX 2 : sum up of ASED comments (mail from 28/07/03)

Pour :	ken.pletinckx@nexans.com

Cc :	gbottaro@to.alespazio.it

stephane.dassy@nexans.com

ofratacci@to.alespazio.it

Objet :	Sum up of splinter with ASED

Hello everybody,

in order to support the telecon this afternoon, here is the list of the outcomes of splinter session on Cryo-harness in SVM with Astrium (ASED) :

General :

1) A common database giving WU ICDs (M+E) and CAD models shall be managed by ASP on a ftp server accessible to all parties involved.

The following comments are to be considered as looking to the lateral panel from SVM center. They are based on the preliminary CryoH. routing CAD models delivered by ASED during the QPM. The models have been transmitted to ALS.

PACS panel :

1) ASED needs more space between DECMEC & BOLC to route CryoH, the power H. supplying DECMEC shall then be routed on DECMEC's small lateral side. Signal H. shall be put also as close as possible to the DECMEC.

Nota : segragation of harness class to be assessed

2) DECMEC J17 and redundant J117 connectors appear to be simultaneously connected to CryoH. and WIH. To be checked.

SPIRE panel :

1) the area at the left of the FSFCU shall be enlarged, leading to grouping of thermal ctrl/analog H.

2) OBDH H. loop currently located in the middle of the shear webs shall be shifted close to the left web as much as possible. If the antenna is blocking, the loop shall be shifted to the right web.

The centered area of the shear webs is dedicated to CCU H. routing

3) WIH on top of FSDCU unit shall be routed closer to the unit in order to free space for CryoH. routing and connection.

HIFI -Y-Z panel :

1) FHFCU area : additional space needed for CryoH. accommodation but pending on following actions

* FCU connectors changing => re-routing to be assessed by ASED

* Up-converter : accommodation to be assessed by ALS

* CryoH. routing update in FCU left area, ASED

* WIH to be updated accordingly in this area

HIFI -Y panel :

1) WIH on top of FHLCU and FHLSU shall be routed closer to units in order to increase the space for the CryoH. routing

2) FHLCU J03 and J23 connectors are connected simultaneously to CryoH. and WIH. To be checked.

3) Routing on top of FHLSU : due to possible new IF for LOU WG, the routing of WIH / SVM H./ all non CryoH. shall be restricted to the minimum on top of FHLSU.

4) The LOU WG IF is on-going, as soon as information is available, this will be passed to ALS/Nexans

Star Trackers routing

ASED requests the routing of Star Trackers to ALS in order to check the compatibility with CryoH.

Cone Telescope H. bracket relocation

ASED has agreed the new location of the bracket proposed by ALS

Best regards.

Baptiste Marchand.

### ANNEX 3 : SPIRE panel latest configuration

### ANNEX 4 : Instruments comments (mail from 22/07/03)

Pour :	ken.pletinckx@nexans.com

stephane.dassy@nexans.com

cc :	gbottaro@to.alespazio.it

ofratacci@to.alespazio.it

Bernard Collaudin/ALCATEL-SPACE@ALCATEL-SPACE

Objet :	comments from Instruments

Dear all,

in order to support the discussion for tomorrow,

we have received the following comments from Instruments up to now :

(Astrium comments for Herschel Cryohrn are not included and will be reviewed tomorrow)

HERSCHEL

HIFI :

1) Bundles of different EMC classes are running close together. This

should be avoided or metalic barriers should be used.

2) For EMC reasons the RF cabling and analog signal cables between these

units should be routed close together and close to the baseplate. For

the analog signal harness specific connectors are used to make this

possible.

3) The backshells foreseen for HIFI are the following Glenair types:

550T039M1R9H0-03B, size E, TOP entry

550E039M1R9J0-03B, size E, END entry

and the equivalent types for size A, B and C.

4) The receptacles for all coaxial  (not only semi-rigid) cables,

located on the connectors brackets, are:

Type: ESCC 340200304B101, Manufacturer: Radiall/France

5) the pictures of the special connectors (for the WEH-WOH and WEV-WOV harness) are attached to this

mail.

As shown the cabling can route directly below these conectors on the

base plates.

I requested also a drawing of these connectors, which will be sent as

soon as possible, but to get an impression of the dimension you need to

know that the grid on these pictures is 5x5mm.

<<P7101322.JPG>>

<<P7101321.JPG>>

<<P7101320.JPG>>

SPIRE :

1) Please specify the details of the 4 harness wide clamp

base shown bottom

right in VueF of drg HP-NXH-DR-XXXX.

J-L of CEA points out that it needs to fit with margin on the flat

surface shown, not

overhang over the power supply base's joint.

PACS :

1) the back shell information as well finalized WEU drawings are missing.

These information was requested very often from our partner institutes but

it is not yet available.

2) in the Herschel - PACS table the identifier FPFPU P09 is missing.

PLANCK

HFI 4K

1) J9 on the 4K CDE goes to the Ancillary unit and not on the Compressor. J9 is the 15 way connector with Compressor A & B temperatures and PPO A & B temperatures.

2) The small connector on the ancillary unit does not connect to the CDE but runs along the connecting pipework to the

disconnection box.

3) The information you need for the HFI 4KCDE harnesses can be found in table 2 of the attached document (backshell).

HFI 0.1 K

1) We are also somewhat discovering accommodation changes (such as redondant

DPU now sitting on the same panel as the Nominal one), possible new

splitting of the harnesses linking the DPUs to the DCE (which may imply new

connectors, different geometry of covers,...), we lack a drawing showing the

routing between these units,...

LFI

1)  we send in annex the list of the BEU harness with indication about bundle characteristics.

Best regards.

Baptiste Marchand.

### ANNEX 4 bis

Content of HIFI conn views.zip :

Backshells for WEH/V and WOH/V.

Nota : dimensions of the grid on the pictures is 5x5 mm

### ANNEX 4 ter : 4K CAU connection

### ANNEX 4 quarterio

| Connector | Connector Type | Backshell | Function |
| --- | --- | --- | --- |
| PHDC-P3A | 340100201B DEMA9SNMBFO | 100P1574-09-1-C Polamco Ltd. | Compressor A Drive Outputs |
| PHDC-P3B | 340100201B DEMA9SNMBFO | 100P1574-09-1-C Polamco Ltd. | Compressor B Drive Outputs |
| PHDC-P4A | 340100201B DEMA9PNMBFO | 100P1574-09-1-C Polamco Ltd. | Position Pick-off (PPO) A |
| PHDC-P4B | 340100201B DEMA9PNMBFO | 100P1574-09-1-C Polamco Ltd. | Position Pick-off (PPO) B |
| PHDC-P5 | SCBM5W5M0000G | 100P1574-15-1-C Polamco Ltd. | Force Inputs |
| PHDC-P6 | 340100202B DCM62PNMBFO | 100P1574-37-1-C Polamco Ltd. | Ancillary Inputs |
| PHDC-P8 | 340100201B DAM15PNMBFO | N/A | Transport Link |
| PHDC-P9 | 340100201B DAM15PNMBFO | 100P1574-15-1-C Polamco Ltd. | Compressor Temperatures |
| PHDD-P120 | 340100201B DEMA9PNMBFO | 100P1574-09-1-C Polamco Ltd. | Compressor A Drive Outputs |
| PHDD-P121 | 340100201B DEMA9PNMBFO | 100P1574-09-1-C Polamco Ltd. | Compressor B Drive Outputs |
| PHDD-P122 | 340100201B DEMA9SNMBFO | 100P1574-09-1-C Polamco Ltd. | Position Pick-off (PPO) A |
| PHDD-P123 | 340100201B DEMA9SNMBFO | 100P1574-09-1-C Polamco Ltd. | Position Pick-off (PPO) B |
| PHDD-P124a | 340200801B301 | N/A | Force Input a |
| PHDD-P124b | 340200801B301 | N/A | Force Input b |
| PHDD-P124c | 340200801B301 | N/A | Force Input c |
| PHDD-P124d | 340200801B301 | N/A | Force Input d |
| PHDD-Pxxx | 340100202B DCMA62SNMBFO | 100P1574-37-1-C Polamco Ltd. | Ancillary Inputs |
| PHDD-Pyyy | 340100201B DEMA9SNMBFO | 100P1574-15-1-C Polamco Ltd. | Compressor Temperatures |

### ANNEX 5 PAU backshell IDS

### ANNEX 6 – LFI bundles characteristics