Delivery Review Board Minutes 	    SPIRE-RAL-MOM-001768

Cooler

CQM

19/8/03

Lionel Duband, Bruce Swinyard, Eric Clark, Eric Sawyer, John Delderfield

Agenda.

Incoming inspection  (ref  SPIRE-RAL-REP-001767)

EIDP review

Acceptance review including test results

Plans for integration

Integration

Incoming inspection will be completed this pm.

Satisfactory, report completed by Eric Clark.

# EIDP review

| Section | Title | Comments |  |
| --- | --- | --- | --- |
| 1 | C of C | OK |  |
| 2 | Shipping docs | OK |  |
| 3 | Open work | Non identified in this section, but there are some missing documents |  |
| 4 | Transport and handling | OK |  |
| 5 | CIDL/ASCL | OK |  |
| 6 | Interface and top level drawings | OK |  |
| 7 | Age sensitive items | OK |  |
| 8 | Temp installation record | OK |  |
| 9 | Log book | Historical log to be supplied |  |
| 10 | List of waivers | No waivers |  |
| 11 | NCRs | One open (heat switch) |  |
| 12 | Mass record | 1741 gms (1800 allocation) |  |
| 13 | Cleanliness statement | OK |  |
| 14 | Operating manual | To be supplied |  |
| 15 | Test records | OK |  |

# Integration

Carried out 20/8/03 am.  No problems identified.

Note.  It is recommended that a “red tag” be attached to the cooler when the transit screws are in place.  The label should read TRANSIT SCREWS FITTED.  The tag to be left in place until the screws are removed.

Acceptance review.

The test results were reviewed and discussed.

Tests with straps of lower conductivity have not been carried out.

It may be possible to do some tests on the PACS cooler, depending upon when it is required by PACS.

From the test results it is estimated that the evaporator heat switch off conductance is about 8(W more that it should be.  This is probably caused by touching of the inner and out switch tubes.

Flight switches will be down selected from a larger batch. Radiography may be possible.

The CQM cooler is accepted by SPIRE

Eric Sawyer - RAL

Lionel Duband – CEA/SBT