| SUBJECT: | SPIRE DRCU Integration Test SpecificationSPIRE DRCU Integration Test Specification |
| --- | --- |
| PREPARED BY: | Ken KingKen King |
| DOCUMENT No: | SPIRE-RAL-DOC-001799SPIRE-RAL-DOC-001799 |
| ISSUE: | Issue 1.0 Draft 1Issue 1.0 Draft 1 | Date: | 5th September 20035th September 2003 |
| APPROVED BY: |  | Date: |  |

Distribution

| RAL | Dave Smith |
| --- | --- |
|  | Ken King |
|  | Bruce Swinyard |
|  | Tanya Lim |
|  | Sunil Sidher |
|  | Asier Aramburu |
| CEA | Jean-Louis Augueres |
|  | Christophe Cara |

# Change Record

| ISSUE | DATE | Changes |
| --- | --- | --- |
| 1.0 Draft 1 | 8th September 2003 | 1st Draft for comment |
| 1.0 Draft 2 | 12th September | Updated following discussions |

# Table of Contents

1.	Introduction	6

1.1	Scope	6

1.2	Structure of Document	6

1.3	Documents	Error! Bookmark not defined.

2.	Test Summaries	7

2.1	SCU tests	7

2.2	MCU tests	7

2.3	SMEC tests	Error! Bookmark not defined.

2.4	BSM tests	Error! Bookmark not defined.

2.5	PCAL test	Error! Bookmark not defined.

2.6	SCAL tests	Error! Bookmark not defined.

2.7	DCU tests	8

3.	Summary of test condition and test flow	9

3.1	Summary of test condition	Error! Bookmark not defined.

3.2	Test flow	Error! Bookmark not defined.

4.	Test Specification	11

4.1	SCU-01, DRCU Switch-On	11

4.2	SCU-02, SCU High-Speed Interface Data Sequence Test	13

4.3	SCU-03, SCU High-Speed Interface Timing Test	15

4.4	SCU-04, SCU Low-Speed Interface Test	18

4.5	DCU-01, DCU High-Speed Interface Data Sequence Test	21

4.6	DCU-02, DCU High-Speed Interface Timing Test	23

4.7	DCU-03, DCU Low-Speed Interface Test	29

4.8	MCU-01, MCU power on	32

4.9	MCU-02, MCU High-Speed Interface Nominal Data Test	34

4.10	MCU-03, MCU High-Speed Interface Data PerformanceTest	37

4.11	SCU-04, SCU Low-Speed Interface Test	40

Figures

TBW

Tables

TBW

Glossary

| AD | Applicable Document |
| --- | --- |
| AIV | Assembly Integration and Verification |
| AVM | Avionics Model |
| BSM | Beam Steering Mechanism |
| CQM | Cryogenic Qualification Model |
| DCU | Detector Control Unit |
| DPU | Digital Processing Unit |
| DRCU | Detector Readout and Control Unit |
| EGSE | Electrical Ground Support Equipment |
| FLT | Flight Level Test |
| FTS | Fourier Transform Spectrometer |
| HOB | Herschel Optical Bench |
| ILT | Instrument Level Test |
| IST | Integrated System Test |
| MCU | Mechanism Control Unit |
| MGSE | Mechanical Ground Support Equipment |
| N/A | Not Applicable |
| PCAL | Photometer Calibrator source |
| PFM | Proto-Flight Model |
| PLT | Payload Level Test |
| RAL | Rutherford Appleton Laboratory |
| RD | Reference Document |
| SCAL | Spectrometer Calibrator source |
| SCU | Subsystem Control Unit |
| SMEC | Spectrometer Mechanism |
| SPIRE | Spectral and Photometric Imaging Receiver |
| STM | Structural Test Model |
| TBC | To Be Confirmed |
| TBD | To Be Defined |
| TFCS | Test Facility Control System |
| AD | Applicable Document |
| AIV | Assembly Integration and Verification |
| AVM | Avionics Model |

# Introduction

## Scope

This document contains the specification of the Integration tests to be performed on the SPIRE Warm Electronics. These tests exercise the interface between the DPU and DRCU and check that data is transferred in both directions according to the interface specification.

## Structure of Document

Section 2 gives a short summary of each test. Section 3 indicates the expected test sequence and section 4 gives the specification of each test. Section 5 lists the test procedures and scripts used in the specifications but defined elsewhere.

### Applicable Documents

|  | Title | Author | Reference | Date |
| --- | --- | --- | --- | --- |

### Reference Documents

|  | Title | Author | Reference | Date |
| --- | --- | --- | --- | --- |
| RD01 | SCU Qm1 Functional Test Plan in LTU/SCU/FPU Simulator Confriguration | H Triou | SAp-SPIRE-HT-0122-03, Issue 1.0 Draft | 05/08/2003 |
| RD02 | MCU QM0 Functional Test Plan and Test procedures | Didier Ferrand | LAM/ELE/SPI/080703, Issue 1.0 | 29/072003 |
| RD03 | SPIRE Data ICD | K.J. King | SPIRE-RAL-PRJ-001078, Issue 1.1 Draft 3 | 13/08/2003 |
| RD04 | DRCU/DPU ICD | Pinsard, Ferrand, Mur | Sap-SPIRE-CCa-076-02, Issue 1.0 | 14/02/2003 |
| RD05 | Subsystem reaction for specification for the instrument simulator | Bruce Swinyard | SPIRE-RAL-NOT-001715, Issue 1.0 | 11/06/2003 |
| RD06 | Operating modes for the SPIRE instrument | Bruce Swinyard, Matt Griffin | SPIRE-RAL-DOC-000320, Issue 3.0 | 04/01/2002 |

# Test Summaries

## SCU tests

### INT-SCU-01, DRCU Switch on

This procedure allows the DRCU to be powered on and checks the basic housekeeping telemetry contents.

### INT-SCU-02, SCU High-Speed Interface Nominal Data Test

Request different amounts of SCU science frames at the nominal operational rate and check correct receipt

### INT-SCU-03, SCU High-Speed Interface Data Performance Test

Checking the performance and timing of SCU science frame generation:

The following tests are made

Generation of DCU packets at 80, 40, 20 and 10Hz

Generation of Test Packets at 80Hz

For each frame type the reset of the Time Stamp word in data frames is checked and

the frame rate accuracy

### INT-SCU-04, SCU Low-Speed Interface Test

Checking the operation of the interface registers and their commands:

The test sends commands to the subsystem interface, which passes them on to the subsystem.

The time between the command being passed to the subsystem and the response from the subsystem being returned to the interface is termed the Subsystem Delay

When reading a register in the subsystem the delay should be ~ 3 steps

When reading from a component (e.g. an ADC) the delay is ~ 16-23 steps

If a time out occurs a delay of 255 steps is returned

This test sets the interface into various states and checks the response

## MCU tests

### INT-MCU-01, MCU power on

To power on the MCU into a state ready to execute SMEC or BSM commands:

This procedure also tests the low speed interface to the MCU, used for command and housekeeping data transfer

Apply power to MCU from SCU and boot the MCU DSP ROM software, checking voltages and status

### INT-MCU-02, MCU High-Speed Interface Nominal DataTest

Checking transfer of MCU Nominal  Science data frames:

Request science frames at frequencies associated with nominal operations and in various quantities and check correct receipt.

Number of frames and frequencies are:

SMEC: ~1000 and continuous frames at 253Hz

BSM: ~250 and continuous at 63Hz

SMEC+BSM (Scanning mode):  continuous at 253+16Hz)

### INT-MCU-03, High-Speed Interface Data PerformanceTest

Checking the performance and timing of MCU science frame generation.

The following tests are made

Generation of SMEC packets at 320Hz

Generation of BSM packets at 80Hz

Generation of Test Packets at 400Hz

Generation of Engineering packets at 400Hz

For each frame type the reset of the Time Stamp word in data frames is checked and

the frame rate accuracy

### INT-MCU-04, MCU Low-Speed Interface Test

Checking the operation of the interface registers and their commands

## DCU tests

### INT-DCU-01, DCU High-Speed Interface Nominal Data Test

Checking transfer of DCU Science data frames:

Request science frames at various frequencies and in various quantities and check correct receipt

### INT-DCU-02, DCU High-Speed Interface Data Performance Test

Checking the performance and timing of DCU science frame generation

### INT-DCU-03, DCU Low-Speed Interface Test

Checking the operation of the interface registers and their commands:

The test sends commands to the subsystem interface, which passes them on to the subsystem.

The time between the command being passed to the subsystem and the response from the subsystem being returned to the interface is termed the Subsystem Delay

When reading a register in the subsystem the delay should be ~ 3 steps

When reading from a component (e.g. an ADC) the delay is ~ 16-23 steps

If a time out occurs a delay of 255 steps is returned

This test sets the interface into various states and checks the response

# test Sequence

In this section the sequence of tests is provided based on the given starting conditions for each test

## Test Flow

The following diagram shows the instrument configurations used during the integration testing and the tests which may be run from each configuration

## Test Sequence

It is planned that the procedures will be carried out in the following order:

| Procedure | Estimated Duration | Comments |
| --- | --- | --- |
| DPU ON |  |  |
| SCU-01 |  |  |
| SCU-02 |  |  |
| SCU-03 |  |  |
| SCU-04 |  |  |
| DCU-01 |  |  |
| DCU-02 |  |  |
| DCU-03 |  |  |
| MCU-01 |  |  |
| MCU-02 |  |  |
| MCU-03 |  |  |
| MCU-04 |  |  |
| MCU OFF |  |  |
| DRCU OFF |  |  |
| DPU OFF |  |  |

# Test Specification

## SCU-01, DRCU Switch-On

| ID: | SCU-01 |
| --- | --- |
| Test name: | DRCU Switch On |
| Purpose | Power on the DRCU |
| Description of test: | This procedure allows the DRCU to be powered on and checks the basic housekeeping telemetry contents. This test implicitly tests the low-speed interface to the SCU |
| Test Type: | Interface Check |
| Instrument Models: | AVM/CQM/PFM/FS |
| Redundancy: | This test can be applied to both Prime and Redundant systems |
| Instrument Configuration: | SPIRE in ‘On’ Mode: DPU powered on and generating housekeeping telemetry |
| EGSE Configuration: | SCOS-2000 required |
| Level | ILT/PLT/IST/FLT |
| Test Conditions: | FPU Warm or Cold, or FPU Simulator |
| Constraints: |  |
| Outline procedure and analysis: |  | Setup EGSE | Select SCOS display (DPU and OBS_PARAMETERS) Send SET_BBID(TBD) |
|  |  | Stop Housekeeping requests to DRCU Stop Critical Housekeeping Stop Nominal Housekeeping Check both housekeeping reports have stopped | Send CLEAR_HK_REPORT (0) Send CLEAR_HSK_REPORT (1) |
|  |  | Power on DRCU Apply 28v bus Check input currents to DRCU | For QM1: switch on power supplies (see procedure). For other models, TBD For QM1 record and check power supply currents. For other models, TBD |
|  |  | Restart Housekeeping requests to DRCU Start Critical Housekeeping Start Nominal Housekeeping Check both housekeeping reports have started | Send DEFINE_NEW_HK_REPORT (0,0x300,2000,1,0,0) Send DEFINE_NEW_HK_REPORT (1,0x301,1000,1,1,1) |
|  |  | Check SCU status | SCUSTAT = 0x0000 SCUTEMPSTAT = 0x0000 SCUDCDCSTAT = 0x0000 SUBKSTAT = 0x0000 SCU+5V = 0xB554 SCU+9V = 0xE00D SCU-9V = 0x1FF0 SCU25V = 0x9AAD SCUREF = TBD SCUGND = 0x7FFF, TBC SPHSV = 0x7FFF, TBC EVHSV = 0x7FFF, TBC TCHTRV = 0x7FFF, TBC SPHTRV = 0x7FFF, TBC PCALV = 0x7FFF, TBC SCAL2V = 0x7FFF, TBC SCAL4V = 0x7FFF, TBC BIASP5V = 0xB554 BIASP9V = 0xE00D BIASN9V = 0x1FF0 LIASTAT = 0x0000 PSWJFETSTAT = 0x0000 PMLWJFETSTAT = 0x0000 SPECJFETSTAT = 0x0000 |
| Success/Failure Criteria: | Procedure completed with no errors |

Comments/Open issues:

## SCU-02, SCU High-Speed Interface Nominal Data Test

| ID: | SCU-02 |
| --- | --- |
| Test name: | SCU High-Speed Interface Data Test |
| Purpose | Checking transfer of SCU Science data frames |
| Description of test: | Request different amounts of SCU science frames at the nominal operational rate and check correct receipt |
| Test Type: | Interface Check |
| Instrument Models: | AVM/CQM/PFM/FS |
| Redundancy: | This test can be applied to both Prime and Redundant systems |
| Instrument Configuration: | SPIRE in ‘REDY’ mode: DPU and DRCU Powered on |
| EGSE Configuration: | SCOS 2000 required QLA required |
| Level | ILT/PLT/IST/FLT |
| Test Conditions: | FPU Warm or Cold, or FPU Simulator |
| Constraints: |  |
| Outline procedure and analysis: | b | Setup EGSE | Set SCOS Display (SCU_PARAMETERS) Set QLA Scrolling display of SCU Science packet header parameters (SCUOBSID, SCUBBID, SCUBLKLEN, SCUFRAMEID, SCUFRAMETIME, SCUADCFLAGS) Use GUI to change display to HEX Set QLA Clock display of SCUFRAMECNT and note the value Note OBSID value Send SET_BBID(TBD) |
|  |  | Setup Data contents For QM1: Load SCU parameter file 1 Switch on temperature channels Switch on SubK temp Check Housekeeping values on SCOS Display | TBD Send SEND_DRCU_COMMAND (A085FFFF) Send SEND_DRCU_COMMAND (A0860001) |
|  |  | Request Nominal data Rate (80Hz) | Send SEND_DRCU_COMMAND (A0830000) |
|  |  | Request 1 frame Stop data generation Set sequence length to 1 Start data generation Wait 1 sec Flush SCU FIFO | Send SEND_DRCU_COMMAND (A0820000) Send SEND_DRCU_COMMAND (A0840001) Send SEND_DRCU_COMMAND (A0820001) Send FLUSH_FIFO (0x4000) |
|  |  | Check 1 frame received, with correct contents | SCUFRAMECNT has incremented by 1 SCUOBSID = OBSID value SCUBBID = BBID SCUBLKLEN = 30 SCUFRAMEID = 0x20 SCUADCFLGS = 0 |
|  |  | Request 10 frames Stop data generation Set sequence length to 10 Start data generation Wait 1 sec Flush SCU FIFO | Send SEND_DRCU_COMMAND (A0820000) Send SEND_DRCU_COMMAND (A084000A) Send SEND_DRCU_COMMAND (A0820001) Send FLUSH_FIFO (0x4000) |
|  |  | Check 10 frames received, with correct contents | SCUFRAMECNT has incremented by 10 For each frame check SCUOBSID = OBSID value SCUBBID = BBID SCUBLKLEN = 30 SCUFRAMEID = 0x20 SCUADCFLGS = 0 Check SCUFRAMETIME increases (unless it wraps around) |
|  |  | Request 31 frames Stop data generation Set sequence length to 31 Start data generation Wait 1 sec Flush SCU FIFO Check 31 frames received, with correct contents | Send SEND_DRCU_COMMAND (A0820000) Send SEND_DRCU_COMMAND (A084001F) Send SEND_DRCU_COMMAND (A0820001) Send FLUSH_FIFO (0x4000) TBD |
|  |  | Check 31 frames received, with correct contents | SCUFRAMECNT has incremented by 31 For each frame check SCUOBSID = OBSID value SCUBBID = BBID SCUBLKLEN = 30 SCUFRAMEID = 0x20 SCUADCFLGS = 0 Check SCUFRAMETIME increases (unless it wraps around) |
|  |  | Request continuous frames Stop data generation Set sequence length to 0 Start data generation Wait 60 sec Stop data generation Flush SCU FIFO | Send SEND_DRCU_COMMAND (A0820000) Send SEND_DRCU_COMMAND (A0840000) Send SEND_DRCU_COMMAND (A0820001) Send SEND_DRCU_COMMAND (A0820000) Send FLUSH_FIFO (0x4000) |
|  |  | Check frames received OK | Check no errors in transmission (no event packets received) Check SCUFRAMECNT has incremented by approximately 4800 |
| Success/Failure Criteria: | Procedure completed with no errors |

Comments/Open issues:

## SCU-03, SCU High-Speed Interface Data Performance Test

| ID: | SCU-03 |
| --- | --- |
| Test name: | SCU High-Speed Interface Timing Test |
| Purpose | Checking the performance and timing of SCU science frame generation. |
| Description of test: | The following tests are made Generation of DCU packets at 80, 40, 20 and 10Hz Generation of Test Packets at 80Hz For each frame type the reset of the Time Stamp word in data frames is checked and the frame rate accuracy |
| Test Type: | Interface Test |
| Instrument Models: | AVM/CQM/PFM/FS |
| Redundancy: | This test can be applied to both Prime and Redundant systems |
| Instrument Configuration: | SPIRE in ‘READY’ mode: DPU and DRCU Powered on |
| EGSE Configuration: | SCOS 2000 required QLA required |
| Level | ILT/PLT/IST/FLT |
| Test Conditions: | FPU Warm or Cold, or FPU Simulator |
| Constraints: |  |
| Outline procedure and analysis: |  | Setup EGSE | Set SCOS Display (DPU and OBS_PARAMETERS) Set QLA Scrolling display of SCU Science packet header |
|  |  | Setup Data contents For QM1: Load SCU parameter file 1 Switch on temperature channels Switch on SubK temp | TBD Send SEND_DRCU_COMMAND (A085FFFF) Send SEND_DRCU_COMMAND (A0860001) |
|  |  | Setup Data generation Request sequence of 10 Frames Reset Time Stamp Wait 30 seconds | Send SEND_DRCU_COMMAND (A084000A) Send SYNC_DRCU_COUNTERS () |
|  |  | Test 80Hz generation Stop data generation Set frame rate to 80Hz Reset Time Stamp Start data generation Wait 1 sec Flush SCU FIFO Check time between frames corresponds to ~12.5ms Check Time Stamp in frames is less than 30 seconds | Send SEND_DRCU_COMMAND (A0820000) Send SEND_DRCU_COMMAND (A0830000) Send SYNC_DRCU_COUNTERS () Send SEND_DRCU_COMMAND (A0820001) Send FLUSH(0x4000) TBD TBD |
|  |  | Test 40Hz generation Stop data generation Set frame rate to 40Hz Reset Time Stamp Start data generation Wait 1 sec Flush SCU FIFO Check time between frames corresponds to ~25ms | Send SEND_DRCU_COMMAND (A0820000) Send SEND_DRCU_COMMAND (A0830001) Send SYNCHRONIZE_DRCU() Send SEND_DRCU_COMMAND (A0820001) Send FLUSH(0x4000) TBD |
|  |  | Test 20Hz generation Stop data generation Set frame rate to 20Hz Reset Time Stamp Start data generation Wait 1 sec Flush SCU FIFO Check time between frames corresponds to ~50ms | Send DRCU_CMD(A0820000) Send DRCU_CMD(A0830003) Send SYNCHRONIZE_DRCU() Send DRCU_CMD(A0820001) Send FLUSH(0x4000) TBD |
|  |  | Test 10Hz generation Stop data generation Set frame rate to 10Hz Reset Time Stamp Start data generation Wait 1 sec Flush SCU FIFO Check time between frames corresponds to ~50ms | Send DRCU_CMD(A0820000) Send DRCU_CMD(A0830007) Send SYNCHRONIZE_DRCU() Send DRCU_CMD(A0820001) Send FLUSH(0x4000) TBD |
|  |  | Test Test Pattern generation Stop data generation Set frame rate to 80Hz with Test Pattern Data Reset Time Stamp Start data generation Wait 1 sec Flush SCU FIFO Check time between frames corresponds to ~12.5ms Check Test Pattern is correct Stop data generation Set nominal data mode | Send DRCU_CMD(A0820000) Send DRCU_CMD(A0838003) Send SYNCHRONIZE_DRCU() Send DRCU_CMD(A0820001) Send FLUSH(0x4000) TBD TBD Send DRCU_CMD(A0820000) Send DRCU_CMD(A0830000) |
| Success/Failure Criteria: | Procedure completed with no errors |

Comments/Open issues:

## SCU-04, SCU Low-Speed Interface Test

| ID: | SCU-04 |
| --- | --- |
| Test name: | SCU Low-Speed Interface Test |
| Purpose | Checking the operation of the interface registers and their commands |
| Description of test: | The test sends commands to the subsystem interface, which passes them on to the subsystem. The time between the command being passed to the subsystem and the response from the subsystem being returned to the interface is termed the Subsystem Delay When reading a register in the subsystem the delay should be ~ 3 steps When reading from a component (e.g. an ADC) the delay is ~ 16-23 steps If a time out occurs a delay of 255 steps is returned This test sets the interface into various states and checks the response |
| Test Type: | AVM/CQM/PFM/FS |
| Instrument Models: | This test can be applied to both Prime and Redundant systems |
| Redundancy: | SPIRE in ‘READY’ mode: DPU and DRCU Powered on |
| Instrument Configuration: | SCOS 2000 required QLA required |
| EGSE Configuration: | ILT/PLT/IST/FLT |
| Level | FPU Warm or Cold, or FPU Simulator |
| Test Conditions: | AVM/CQM/PFM/FS |
| Constraints: |  |
| Outline procedure and analysis: |  | Setup EGSE | Set SCOS Display (SCU PARAMETERS) |
|  |  | Stop Housekeeping requests to DRCU Stop Critical Housekeeping Stop Nominal Housekeeping Check Housekeeping has stopped | Send CLEAR_HK_REPORT(0) Send CLEAR_HK_REPORT(1) |
|  |  | Check Timeout Reset Subsystem Check command status in DPU Science Frame Send a command to the subsystem Check command status in DPU Science Frame Remove Subsystem Reset Send a command to the subsystem Check returned value in DPU Science Frame | Send RUN_VM(101, SCU_CMD, 1, 0xA0010005) SCUIFSTAT = 0x0000 Send RUN_VM(101, SCU_CMD, 1, 0xA8840000) SCUIFSTAT = 0x0038 SCUSSDEL = 0x0100 Send SEND_DRCU_COMMAND (A0010007) Send RUN_VM(101, SCU_CMD, 1, 0xA8840000) RESPONSE = 0x0000 |
|  |  | Check Data Interface Reset Data Interface Check interface status in DPU Science Frame Remove Data Interface Reset Check interface status in DPU Science Frame | Send RUN_VM(101, SCU_CMD, 1, 0xA0010003) SCUIFSTAT = 0x0000 SCUIFCTRL = 0x0003 Send RUN_VM(101, SCU_CMD, 1, 0xA0010007) SCUIFSTAT = 0x0000 SCIIFCTRL = 0x0007 |
|  |  | Check Subsystem Delay Read a register Check Subsystem Delay in DPU Science Frame Read an ADC Check Subsystem Delay in DPU Science Frame | Send RUN_VM(101, SCU_CMD, 1, 0xA8840000) SCUSSDEL = 2 or 3 Send RUN_VM(101, SCU_CMD, 1, 0xA8C90000) SCUSSDEL = 16 to 23 |
|  |  | Check Latch up Reset Read a Latchup status Check Latchup Status in DPU Science Frame Reset Latchup status Read a Latchup status Check Latchup Status in DPU Science Frame Remove Latchup Reset | Send RUN_VM(101, SCU_CMD, 1, 0xA8800000) RESPONSE = 0, 1or 2 Send SEND_DRCU_COMMAND(A0810000) Send RUN_VM(101, SCU_CMD, 1, 0xA8800000) RESPONSE = 0 Send SEND_DRCU_COMMAND(A0810001) |
|  |  | Restart Housekeeping requests to DRCU Start Critical Housekeeping Start Nominal Housekeeping Check Hsk has started | Send DEFINE_NEW_HK_REPORT (0,0x300,2000,1,0,0) Send DEFINE_NEW_HK_REPORT (1,0x301,1000,1,1,1) |
| Success/Failure Criteria: | Procedure completed with no errors |

Comments/Open issues:

## DCU-01, DCU High-Speed Interface Nominal Data Test

| ID: | DCU-01 |
| --- | --- |
| Test name: | DCU High-Speed Interface Nominal Data Test |
| Purpose | Checking transfer of DCU Science data frames |
| Description of test: | Request science frames at various frequencies and in various quantities and check correct receipt |
| Test Type: | Interface Check |
| Instrument Models: | AVM/CQM/PFM/FS |
| Redundancy: | This test can be applied to both Prime and Redundant systems |
| Instrument Configuration: | SPIRE in ‘READY’ mode: DPU and DRCU Powered on |
| EGSE Configuration: | SCOS 2000 required QLA required |
| Level | ILT/PLT/IST/FLT |
| Test Conditions: | FPU Warm or Cold, or FPU Simulator |
| Constraints: |  |
| Outline procedure and analysis: | b | Setup EGSE | Set SCOS Display (DPU and OBS_PARAMETERS) Set QLA Scrolling display of DCU Science packet header |
|  |  | Setup Data contents Set Data Mode (Full Photometer) | Send DRCU_CMD(843C0000) |
|  |  | Set Nominal data Rate (15Hz) Set Bias Frequency (200Hz) Set Sample frequency (15.3Hz) | Send DRCU_CMD(84190062) Send DRCU_CMD(8418000C) |
|  |  | Request 1 frame Stop data generation Set sequence length to 1 Start data generation Wait 1 sec Flush DCU FIFO Check 1 frame received, with correct contents | Send DRCU_CMD(843E0000) Send DRCU_CMD(843D0001) Send DRCU_CMD(843E0001) Send FLUSH(0x1000) TBD |
|  |  | Request 10 frames Stop data generation Set sequence length to 10 Start data generation Wait 1 sec Flush DCU FIFO Check 10 frames received, with correct contents | Send DRCU_CMD(843E0000) Send DRCU_CMD(843D000A) Send DRCU_CMD(843E0001) Send FLUSH(0x1000) TBD |
|  |  | Request 100 frames Stop data generation Set sequence length to 100 Start data generation Wait 10 sec Flush DCU FIFO Check 100 frames received, with correct contents | Send DRCU_CMD(843E0000) Send DRCU_CMD(843D0064) Send DRCU_CMD(843E0001) Send FLUSH(0x1000) TBD |
|  |  | Request continuous frames Stop data generation Set sequence length to 0 Start data generation Wait 600 sec Stop data generation Flush DCU FIFO Check frames received OK | Send DRCU_CMD(843E0000) Send DRCU_CMD(843D0000) Send DRCU_CMD(843E0001) Send DRCU_CMD(843E0000) Send FLUSH(0x1000) TBD |
| Success/Failure Criteria: | Procedure completed with no errors |

Comments/Open issues:

## DCU-02, DCU High-Speed Interface Data Performance Test

| ID: | DCU-03 |
| --- | --- |
| Test name: | DCU High-Speed Interface Data Performance Test |
| Purpose | Checking the performance and timing of DCU science frame generation. |
| Description of test: |  |
| Test Type: | Interface Test |
| Instrument Models: | AVM/CQM/PFM/FS |
| Redundancy: | This test can be applied to both Prime and Redundant systems |
| Instrument Configuration: | SPIRE in ‘READY’ mode: DPU and DRCU Powered on |
| EGSE Configuration: | SCOS 2000 required QLA required |
| Level | ILT/PLT/IST/FLT |
| Test Conditions: | FPU Warm or Cold, or FPU Simulator |
| Constraints: |  |
| Outline procedure and analysis: |  | Setup EGSE | Set SCOS Display (DPU and OBS_PARAMETERS) Set QLA Scrolling display of DCU Science packet header |
|  |  | Setup Photometer Data generation Set Bias Frequency (200Hz) Request sequence of 10 Frames | Send DRCU_CMD(84190062) Send DRCU_CMD(843D000A) |
|  |  | Setup to Test Nominal Phot ometer Mode Set Data Mode (Full Photometer) Reset Time Stamp Wait 30 seconds | Send DRCU_CMD(843C0000) Send SYNCHRONIZE_DRCU() |
|  |  | Test 15Hz generation Stop data generation Set frame rate to 15Hz Reset Time Stamp Start data generation Wait 1 sec Flush DCU FIFO Check time between frames corresponds to ~60ms Check Time Stamp in frames is less than 30 seconds | Send DRCU_CMD(843E0000) Send DRCU_CMD(8418000C) Send SYNCHRONIZE_DRCU() Send DRCU_CMD(843E0001) Send FLUSH(0x1000) TBD TBD |
|  |  | Test 25Hz generation Stop data generation Set frame rate to 25Hz Reset Time Stamp Start data generation Wait 1 sec Flush DCU FIFO Check time between frames corresponds to ~40ms | Send DRCU_CMD(843E0000) Send DRCU_CMD(84180007) Send SYNCHRONIZE_DRCU() Send DRCU_CMD(843E0001) Send FLUSH(0x1000) TBD |
|  |  | Setup toTest Non-nominal Photometer modes Set frame rate to 15Hz | Send DRCU_CMD(8418000C) |
|  |  | Test Offset Mode Stop data generation Set Data Mode to Offsets Reset Time Stamp Start data generation Wait 1 sec Flush DCU FIFO Check time between frames corresponds to ~60ms Check Data Contents | Send DRCU_CMD(843E0000) Send DRCU_CMD(843C0010) Send SYNCHRONIZE_DRCU() Send DRCU_CMD(843E0001) Send FLUSH(0x1000) TBD TBD |
|  |  | Test Test Pattern Mode Stop data generation Set Data Mode to Test Pattern Reset Time Stamp Start data generation Wait 1 sec Flush DCU FIFO Check time between frames corresponds to ~60ms Check Data Contents | Send DRCU_CMD(843E0000) Send DRCU_CMD(843C0008) Send SYNCHRONIZE_DRCU() Send DRCU_CMD(843E0001) Send FLUSH(0x1000) TBD TBD |
|  |  | Test PSW Mode Stop data generation Set Data Mode to PSW Reset Time Stamp Start data generation Wait 1 sec Flush DCU FIFO Check time between frames corresponds to ~60ms Check Data Contents | Send DRCU_CMD(843E0000) Send DRCU_CMD(843C0001) Send SYNCHRONIZE_DRCU() Send DRCU_CMD(843E0001) Send FLUSH(0x1000) TBD TBD |
|  |  | Test PMW Mode Stop data generation Set Data Mode to PMW Reset Time Stamp Start data generation Wait 1 sec Flush DCU FIFO Check time between frames corresponds to ~60ms Check Data Contents | Send DRCU_CMD(843E0000) Send DRCU_CMD(843C0002) Send SYNCHRONIZE_DRCU() Send DRCU_CMD(843E0001) Send FLUSH(0x1000) TBD TBD |
|  |  | Test PLW Mode Stop data generation Set Data Mode to PLW Reset Time Stamp Start data generation Wait 1 sec Flush DCU FIFO Check time between frames corresponds to ~60ms Check Data Contents | Send DRCU_CMD(843E0000) Send DRCU_CMD(843C0003) Send SYNCHRONIZE_DRCU() Send DRCU_CMD(843E0001) Send FLUSH(0x1000) TBD TBD |
|  |  | Setup Spectrometer Data generation Set Bias Frequency (160Hz) Request sequence of 10 Frames | Send DRCU_CMD(8439007A) Send DRCU_CMD(843D000A) |
|  |  | Setup to Test Nominal Spectrometer Mode Set Data Mode (Full Spectrometer) Reset Time Stamp Wait 30 seconds | Send DRCU_CMD(843C0004) Send SYNCHRONIZE_DRCU() |
|  |  | Test 80Hz generation Stop data generation Set frame rate to 80Hz Reset Time Stamp Start data generation Wait 1 sec Flush DCU FIFO Check time between frames corresponds to ~12.5ms Check Time Stamp in frames is less than 30 seconds | Send DRCU_CMD(843E0000) Send DRCU_CMD(84380001) Send SYNCHRONIZE_DRCU() Send DRCU_CMD(843E0001) Send FLUSH(0x1000) TBD TBD |
|  |  | Setup toTest Non-nominal Spectrometer modes None, TBC |  |
|  |  | Test Offset Mode Stop data generation Set Data Mode to Offsets Reset Time Stamp Start data generation Wait 1 sec Flush DCU FIFO Check time between frames corresponds to ~12.5ms Check Data Contents | Send DRCU_CMD(843E0000) Send DRCU_CMD(843C0014) Send SYNCHRONIZE_DRCU() Send DRCU_CMD(843E0001) Send FLUSH(0x1000) TBD TBD |
|  |  | Test Test Pattern Mode Stop data generation Set Data Mode to Offsets Reset Time Stamp Start data generation Wait 1 sec Flush DCU FIFO Check time between frames corresponds to ~12.5ms Check Data Contents | Send DRCU_CMD(843E0000) Send DRCU_CMD(843C000C) Send SYNCHRONIZE_DRCU() Send DRCU_CMD(843E0001) Send FLUSH(0x1000) TBD TBD |
|  |  | Test SSW Mode Stop data generation Set Data Mode to SSW Reset Time Stamp Start data generation Wait 1 sec Flush DCU FIFO Check time between frames corresponds to ~12.5ms Check Data Contents | Send DRCU_CMD(843E0000) Send DRCU_CMD(843C0006) Send SYNCHRONIZE_DRCU() Send DRCU_CMD(843E0001) Send FLUSH(0x1000) TBD TBD |
|  |  | Test SLW Mode Stop data generation Set Data Mode to SLW Reset Time Stamp Start data generation Wait 1 sec Flush DCU FIFO Check time between frames corresponds to ~12.5ms Check Data Contents | Send DRCU_CMD(843E0000) Send DRCU_CMD(843C0005) Send SYNCHRONIZE_DRCU() Send DRCU_CMD(843E0001) Send FLUSH(0x1000) TBD TBD |
|  |  | Reset to Nominal Modes Stop data generation Set Data Mode to Full Photometer | Send DRCU_CMD(843E0000) Send DRCU_CMD(843C0000) |
| Success/Failure Criteria: | Procedure completed with no errors |

Comments/Open issues:

## DCU-03, DCU Low-Speed Interface Test

| ID: | DCU-03 |
| --- | --- |
| Test name: | DCU Low-Speed Interface Test |
| Purpose | Checking the operation of the interface registers and their commands |
| Description of test: | The test sends commands to the subsystem interface, which passes them on to the subsystem. The time between the command being passed to the subsystem and the response from the subsystem being returned to the interface is termed the Subsystem Delay When reading a register in the subsystem the delay should be ~ 3 steps When reading from a component (e.g. an ADC) the delay is ~ 16-23 steps If a time out occurs a delay of 255 steps is returned This test sets the interface into various states and checks the response |
| Test Type: | AVM/CQM/PFM/FS |
| Instrument Models: | This test can be applied to both Prime and Redundant systems |
| Redundancy: | SPIRE in ‘READY’ mode: DPU and DRCU Powered on |
| Instrument Configuration: | SCOS 2000 required QLA required |
| EGSE Configuration: | ILT/PLT/IST/FLT |
| Level | FPU Warm or Cold, or FPU Simulator |
| Test Conditions: | AVM/CQM/PFM/FS |
| Constraints: |  |
| Outline procedure and analysis: |  | Setup EGSE | Set SCOS Display (DCU PARAMETERS) |
|  |  | Stop Housekeeping requests to DRCU Stop Critical Housekeeping Stop Nominal Housekeeping Check Hsk has stopped | Send CLEAR_HSK_DEFN(0) Send CLEAR_HSK_DEFN(1) |
|  |  | Check Timeout Reset Subsystem Check command status in DPU Science Frame Send a command to the subsystem Check command status in DPU Science Frame Remove Subsystem Reset Send a command to the subsystem Check returned value in DPU Science Frame | Send RUN_VM(101, DCU_CMD, 1, 0x80010005) DCUIFSTAT = 0x0000 Send RUN_VM(101, DCU_CMD, 1, 0x8C000000) DCUIFSTAT = 0x0038 DCUSSDEL = 0x0100 Send DRCU_CMD(80010007) Send RUN_VM(101, DCU_CMD, 1, 0x8C000000) RESPONSE = 0x0000 |
|  |  | Check Data Interface Reset Data Interface Check interface status in DPU Science Frame Remove Data Interface Reset Check interface status in DPU Science Frame | Send RUN_VM(101, DCU_CMD, 1, 0x80010003) DCUIFSTAT = 0x0000 DCUIFCTRL = 0x0003 Send RUN_VM(101, DCU_CMD, 1, 0x80010007) DCUIFSTAT = 0x0000 DCIIFCTRL = 0x0007 |
|  |  | Check Subsystem Delay Read a register Check Subsystem Delay in DPU Science Frame Read an ADC Check Subsystem Delay in DPU Science Frame | Send RUN_VM(101, DCU_CMD, 1, 0xC0000000) DCUSSDEL = 2 or 3 Send RUN_VM(101, DCU_CMD, 1, 0x8C330000) DCUSSDEL = 16 to 23 |
|  |  | Restart Housekeeping requests to DRCU Start Critical Housekeeping Start Nominal Housekeeping Check Hsk has started | Send DEFINE_HSK_REPORT( 0,0x300,2000,1,0,0) Send DEFINE_HSK_REPORT( 1,0x301,1000,1,1,1) |
| Success/Failure Criteria: | Procedure completed with no errors |

Comments/Open issues:

This test requires a Command List which send a given DRCU command and returns the response, and the I/F status words

## MCU-01, MCU power on

| ID: | MCU-01 |
| --- | --- |
| Test name: | MCU Power On |
| Purpose | To power on the MCU into a state ready to execute SMEC or BSM commands. This procedure also tests the low speed interface to the MCU, used for command and housekeeping data transfer |
| Description of test: | Apply power to MCU from SCU and boot the MCU DSP ROM software, checking voltages and status |
| Test Type: | Configuration |
| Instrument Models: | AVM/CQM/PFM/FS |
| Redundancy: | prime and redundant |
| Instrument Initial Configuration: | SPIRE in READY mode |
| EGSE Configuration: | SCOS-2000 required |
| Level | ILT/PLT/IST/FLT |
| Test Conditions: | Warm and cold |
| Constraints: | None |
| Outline procedure and analysis: |  | Setup EGSE | Select SCOS display (MCU_PARAMETERS) |
|  |  | Power on MCU | Send DRCU_CMD(A0870004) |
|  |  | Check MCU power status | SCUDCDCSTAT = 4 MCU+5V = 0xA804 MCU+15V = 0xF810 MCU-15V = 0x07ED MCU+13V = 0cE80E MCU-13V = 0x17EF MCUMACTEMP = 0x1000 MCUSMECTEMP = 0x1000 MCUBSMTEMP = 0x1000 |
|  |  | Reset MCU Subsystem Reset on Wait 5 seconds Reset off Wait 5 seconds Check Status | Send DRCU_CMD(90010005) Send DRCU_CMD(90010007) MCUBOOTSTAT = 0x0001 MCUIFSTAT = 0x0000 |
|  |  | Boot MCU Download Code to RAM Wait 5 seconds Check Boot Status Start Code in RAM | Send DRCU_CMD(9021C000) MCUBOOTSTAT = 0x0001 Send DRCU_CMD(90240001) |
|  |  | Check MCU status | MCUBOOTSTAT = 0x0001 MCUIFSTAT = 0x0000 MCUERR = 0x0000 MCUSCHEDCNTLSW = TBD MCUSCHEDCNTMSW = TBD |
| Success/Failure Criteria: | Procedure completed with no errors |

Comment/Open Issue:

## MCU-02, MCU High-Speed Interface Nominal Data Test

| ID: | MCU-02 |
| --- | --- |
| Test name: | MCU High-Speed Interface Nominal DataTest |
| Purpose | Checking transfer of MCU Nominal Science data frames |
| Description of test: | Request science frames at frequencies associated with nominal operations and in various quantities and check correct receipt. Number of frames and frequencies are: SMEC: ~1000 and continuous frames at 253Hz BSM: ~250 and continuous at 63Hz SMEC+BSM (Scanning mode): continuous at 253+16Hz |
| Test Type: | Interface Check |
| Instrument Models: | AVM/CQM/PFM/FS |
| Redundancy: | This test can be applied to both Prime and Redundant systems |
| Instrument Configuration: | SPIRE in ‘REDY’ mode: DPU and DRCU Powered on |
| EGSE Configuration: | SCOS 2000 required QLA required |
| Level | ILT/PLT/IST/FLT |
| Test Conditions: | FPU Warm or Cold, or FPU Simulator |
| Constraints: |  |
| Outline procedure and analysis: |  | Setup EGSE | Set SCOS Display (DPU and OBS_PARAMETERS) Set QLA Scrolling display of SMEC and BSM Science packet headers |
|  |  | Setup Data contents | TBD |
|  |  | Setup SMEC Nominal data Uplink SMEC Selection Table Set Selection Stop Data generation Reset Time Stamp | Execute Load_SMEC_Selection _Table Send ENABLE_SELECTION(1, 0x1001, 0x0A, 0x0A) Send DRCU_CMD(91C00000) Send SYNCHRONIZE_DRCU() |
|  |  | Request ~1000 frames Start data generation at 253Hz Wait 4 sec Stop data generation Flush MCU FIFO Check ~1000 frames received, with correct contents, and time interval | Send DRCU_CMD(91C0000B) Send DRCU_CMD(91C00000) Send FLUSH(0x2000) TBD |
|  |  | Request continuous frames Start data generation at 253Hz Wait 15 mins, TBC Stop data generation Flush MCU FIFO Check frames received OK | Send DRCU_CMD(91C0000B) Send DRCU_CMD(91C00000) Send FLUSH(0x2000) TBD |
|  |  | Setup BSM Nominal data Stop Data generation Reset Time Stamp | Send DRCU_CMD(91C20000) Send SYNCHRONIZE_DRCU() |
|  |  | Request ~250 frames Start data generation at 63Hz Wait 4 sec Stop data generation Flush MCU FIFO Check ~250 frames received, with correct contents, and time interval | Send DRCU_CMD(91C2002C) Send DRCU_CMD(91C20000) Send FLUSH(0x2000) TBD |
|  |  | Request continuous frames Start data generation at 63Hz Wait 15 mins, TBC Stop data generation Flush MCU FIFO Check frames received OK | Send DRCU_CMD(91C2002C) Send DRCU_CMD(91C20000) Send FLUSH(0x2000) TBD |
|  |  | Request Scanning nominal data Stop data generation Reset Time Stamp Start SMEC frames at 253Hz Start BSM frames at 16Hz Wait 15 mins Stop data generation Check both types of frames received with correct contents, and time interval | Send DRCU_CMD(91C00000) Send DRCU_CMD(91C20000) Send SYNCHRONIZE_DRCU() Send DRCU_CMD(91C0000B) Send DRCU_CMD(91C200AD) Send DRCU_CMD(91C00000) Send DRCU_CMD(91C20000) TBD |
| Success/Failure Criteria: | Procedure completed with no errors |

Comments/Open issues:

## MCU-03, MCU High-Speed Interface Data Performance Test

| ID: | MCU-03 |
| --- | --- |
| Test name: | MCU High-Speed Interface Data PerformanceTest |
| Purpose | Checking the performance and timing of MCU science frame generation. |
| Description of test: | The following tests are made Generation of SMEC packets at 320Hz Generation of BSM packets at 80Hz Generation of Test Packets at 400Hz Generation of Engineering packets at 400Hz For each frame type the reset of the Time Stamp word in data frames is checked and the frame rate accuracy |
| Test Type: | Interface Test |
| Instrument Models: | AVM/CQM/PFM/FS |
| Redundancy: | This test can be applied to both Prime and Redundant systems |
| Instrument Configuration: | SPIRE in ‘READY’ mode: DPU and DRCU Powered on |
| EGSE Configuration: | SCOS 2000 required QLA required |
| Level | ILT/PLT/IST/FLT |
| Test Conditions: | FPU Warm or Cold, or FPU Simulator |
| Constraints: |  |
| Outline procedure and analysis: |  | Setup EGSE | Set SCOS Display (DPU and OBS_PARAMETERS) Set QLA Scrolling display of MCU Science packet headers |
|  |  | Setup Data contents | TBD |
|  |  | Setup SMEC data Uplink SMEC Selection Table Set Selection Stop Data generation Reset Time Stamp Wait 30 secs | Execute Load_SMEC_Selection _Table Send ENABLE_SELECTION(1, 0x1001, 0x0A, 0x0A) Send DRCU_CMD(91C00000) c |
|  |  | Request SMEC frames Reset Time Stamp Start data generation at 400Hz Wait 4 sec Stop data generation Flush MCU FIFO Check frames received, with correct contents, time interval, and time stamp has been reset | Send SYNCHRONIZE_DRCU() Send DRCU_CMD(91C00004) Send DRCU_CMD(91C00000) Send FLUSH(0x2000) TBD |
|  |  | Request BSM frames Reset Time Stamp Start data generation at 80Hz Wait 4 sec Stop data generation Flush MCU FIFO Check frames received, with correct contents, time interval, and time stamp has been reset | Send SYNCHRONIZE_DRCU() Send DRCU_CMD(91C20023) Send DRCU_CMD(91C20000) Send FLUSH(0x2000) TBD |
|  |  | Request Test frames Reset Time Stamp Start data generation at 400Hz Wait 4 sec Stop data generation Flush MCU FIFO Check frames received, with correct contents, time interval, and time stamp has been reset | Send SYNCHRONIZE_DRCU() Send DRCU_CMD(91C40004) Send DRCU_CMD(91C40000) Send FLUSH(0x2000) TBD |
|  |  | Request Engineering frames Reset Time Stamp Start data generation at 400Hz Wait 4 sec Stop data generation Flush MCU FIFO Check frames received, with correct contents, time interval, and time stamp has been reset | Send SYNCHRONIZE_DRCU() Send DRCU_CMD(91C50004) Send DRCU_CMD(91C50000) Send FLUSH(0x2000) TBD |
| Success/Failure Criteria: | Procedure completed with no errors |

Comments/Open issues:

## MCU-04, MCU Low-Speed Interface Test

| ID: | MCU-04 |
| --- | --- |
| Test name: | MCU Low-Speed Interface Test |
| Purpose | Checking the operation of the interface registers and their commands |
| Description of test: | The test sends commands to the subsystem interface, which passes them on to the subsystem. The time between the command being passed to the subsystem and the response from the subsystem being returned to the interface is termed the Subsystem Delay When reading a register in the subsystem the delay should be ~ 3 steps When reading from a component (e.g. an ADC) the delay is ~ 16-23 steps If a time out occurs a delay of 255 steps is returned This test sets the interface into various states and checks the response |
| Test Type: | AVM/CQM/PFM/FS |
| Instrument Models: | This test can be applied to both Prime and Redundant systems |
| Redundancy: | SPIRE in ‘READY’ mode: DPU and DRCU Powered on |
| Instrument Configuration: | SCOS 2000 required QLA required |
| EGSE Configuration: | ILT/PLT/IST/FLT |
| Level | FPU Warm or Cold, or FPU Simulator |
| Test Conditions: | AVM/CQM/PFM/FS |
| Constraints: |  |
| Outline procedure and analysis: |  | Setup EGSE | Set SCOS Display (SCU PARAMETERS) |
|  |  | TBD |  |
| Success/Failure Criteria: | Procedure completed with no errors |

Comments/Open issues:

This test requires a Command List which send a given DRCU command and returns the response, and the I/F status words