SUBJECT:	VIBRATION TEST SPECIFICATION

STM QUALIFICATION

PREPARED BY:	 B. Winter

distribution list

B. Winter	MSSL

C. Brockley-Blat	MSSL

T. Dibbens	MSSL

E. Sawyer	RAL

D. Rippington	RAL

G Toplis	RAL

T. van der Laan	ESTEC

CHANGE RECORD

ISSUE           SECTIONS	REASON FOR CHANGE

1.0	all	New draft issue

Table of Contents

1.	SCOPE	1

2.	documents	1

3.	deFINITIONS	1

3.1.	ABBREVIATIONS	1

4.	TEST PHILOSOPHY	1

5.	build standard	2

6.	TEST OBJECTIVES	2

7.	Fixture	2

8.	TEST REQUIREMENTS	2

8.1.	SUMMARY	2

8.2.	Fixture qualification runs	2

8.3.	Resonance search	2

8.4.	Sine vibration test	3

8.5.	Random vibration test	3

8.6.	Measurement of subsystem levels	4

8.7.	TEST SEQUENCE	4

9.	REJECTION AND REtest	6

10.	DOCUMENTATION	6

11.	PRODUCT ASSURANCE	6

# SCOPE

This document specifies the qualification vibration test for the Herschel SPIRE instrument structural thermal model (STM).

The notching philosophy is outlined in Technote AD (2).

# documents

| AD (1) | Instrument Interface Document, part A | IID-A, issue 4 (?) |
| --- | --- | --- |
| AD (2) | Technote 9 Random Vibration SPIRE February 2003 issue 3.doc |  |
| AD (3) | Drawing of interface fixture for head expander | A1-5264-404-30 |
| AD (4) | Drawing of interface ficutre for slip table | A1-5264-404-31 |

# deFINITIONS

## ABBREVIATIONS

| AD | Applicable Document |
| --- | --- |
| BSM | Beam steering mirror |
| EM | Engineering Model |
| FM | Flight Model |
| ICD | Interface Control Document |
| PFM | Proto-Flight Model |
| QFM | Quartz Filter Mechanism |
| STM | Structural Thermal Model |
| S/C | Spacecraft |
| TBC | To be confirmed |
| TBD | To be defined |
| TRB | Test Revieuw Board |
| TRR | Test Readiness Review |
| TML | Total Material Loss |
| VCD | Verification Control Document |
| VCM | Volatile Condensable Material |

# TEST PHILOSOPHY

The design of the STM of the SPIRE instrument is identical to the flight model except as stated in section 5. This model will be used to qualify the structural design of the SPIRE instrument.

# build standard

The STM of the SPIRE instrument is identical to the PFM with the following exceptions:-

- Mass thermal dummies of the following subsystem are fitted in place of the Flight units:-

- Beam Steering Mirror (and support)

Spectrometer calibration source

- Spectrometer Mechanism (full structure but no electronics and dummy flex-pivots)

- Detectors (mass representative and internally suspended mass representative of the flight hardware with thermal interface for thermal busbar)

- Helium-3 cooler (mass dummy for the heater/evaporator, rest structure representative including suspention)

Filters are optical dummies

The interface to the spacecraft is identical the flight unit. see fig 1

The mass of the SPIRE instrument is 12,345,678.9 kg

# TEST OBJECTIVES

- To Qualify the structural design of the SPIRE instrument and to recover response spectra at critical internal interfaces between system structure and subsystem structures.

- To measure the input levels of the subsystems.

- The test sequence is such that a proper response signature of the instrument is identified both in sine and in random vibration. This will lead to extra reconfigurations of the test set-up and extra runs. In effect all the responses are measured for all excitation directions at levels lower than flight levels before the structure is subjected to qualification levels.

# Fixture

For the X axis vibration ( on the nose of the shaker) fixture to drawing AD (3)-A shall be used.

For the Y and Z axis vibration (on the slip table) fixture to drawing AD (4) shall be used.

# TEST REQUIREMENTS

## SUMMARY

Resonance search, sine vibration test and random vibration tests shall be carried out in three axis. Resonance searches and intermediate random tests shall be performed in all three axes before the instrument is subjected to qualification runs.

## Fixture qualification runs

Runs on just the bare fixture will be carried out as necessary to prove that the fixture behaviour is suitable for the test. This can be carried out before the instrument is available for test.

## Resonance search

A resonance search shall be conducted at approximately 0.5 g input between 5 and 2000 Hz to identify any changes in the primary resonance’s. The will serve as the structure's health check.

The sweep rate shall be 1 Oct/min The monitor accelerometers shall be located on the SPIRE vibration fixture near the mounting locations of the instrument. The resonance search will be performed prior and after a qualification run. No nuts or bolts should be tightened or loosend between these verification runs.

## Sine vibration test

As stated in IID-A, AD (1) the qualification levels are:

X axis

| Frequency Range Hz | Qualification level |
| --- | --- |
| 5 - 20.1 | +/- 11mm |
| 20.1 - 100 | 18 g |

Test sweep rate 2 Oct/min, the input will be limited to equivalent quasi static interface force.

Y and Z axis

| Frequency Range Hz | Qualification level |
| --- | --- |
| 5 - 13.5 | +/- 11mm |
| 13.5 - 100 | 8 g |

Test sweep rate 2 Oct/min, the input will be limited to equivalent quasi static interface force.

## Random vibration test

As stated in IID-A, AD (1) the qualification levels are:

Y and Z axis

| Frequency Range Hz | Qualification level |
| --- | --- |
| 20-100 | +3dB/Oct |
| 100-150 | 0.02 g2/Hz |
| 150-300 | 0.0125g2/Hz |
| 300-2000 | -7 dB/Oct |
| Global | …. gRMS |

Test duration 2 minutes in each axis

X axis

| Frequency Range Hz | Qualification level |
| --- | --- |
| 20-100 | +3dB/Oct |
| 100-150 | 0.05 g2/Hz |
| 150-300 | 0.02g2/Hz |
| 300-2000 | -7 dB/Oct |
| Global | …. gRMS |

Test duration 2 minutes

## Measurement of subsystem levels

The instrumentation of the instrument should be sufficient to characterise the responses at critical locations and allow for the characterisation of the responses at the various subsystem interfaces. If needed runs will be repeated to cover all locations if the data acquisition doesn't allow for simultaneous measurement of all accelerometers at these locations.

Input levels at the following subsystems are required:-

Detectors (detector boxes)

Spectrometer mechanism

Helium cooler

Beam steering mirror (at base of the support structure)

## TEST SEQUENCE

X Axis (on the nose of the shaker)

- Fixture qualification runs as required by the facility.

- Mount instrument on vibration fixture

- Visual inspection

- Resonance search

- Low level random

- Intermediate level random

- Resonance search

- Visual inspection

Change to Y axis.

Y axis  (on the slip table)

- Fixture qualification runs as required by the facility.

- Mount instrument on vibration fixture

- Visual inspection

- Resonance search

- Low level random

- Intermediate level random

- Resonance search

- Visual inspection

Change to Z axis.

Z axis  (on the slip table)

- Mount instrument on vibration fixture

- Visual inspection

- Resonance search

- Low level random

- Intermediate level random

- Resonance search

- Visual inspection

- Intermediate level sine

- Visual inspection

- Full level sine

- Resonance search

- Visual inspection

- Full level random (stepping up from -9dB to full level 30 seconds for each step before full level, retain measurement data for each step.

- Resonance search

- Visual inspection

Change to Y axis

- Mount instrument on vibration fixture

- Visual inspection

- Resonance search

- Intermediate level sine

- Visual inspection

- Full level sine

- Resonance search

- Visual inspection

- Full level random (stepping up from -9dB to full level 30 seconds for each step before full level, retain measurement data for each step.

- Resonance search

- Visual inspection

Change to X axis

- Fixture qualification runs as required by the facility.

- Mount instrument on vibration fixture

- Visual inspection

- Resonance search

- Intermediate level sine

- Visual inspection

- Full level sine

- Resonance search

- Visual inspection

- Full level random (stepping up from -9dB to full level 30 seconds for each step before full level, retain measurement data for each step.

- Resonance search

- Visual inspection

# REJECTION AND REtest

If a failure, malfunction or out of tolerance performance occurs during or after test as appropriate the test shall be discontinued.  This also includes test equipment qualification.  the deficiency, including any design defect, shall be corrected and the applicable procedures repeated until successfully completed.  If the corrective action subsequently affects the significance of results of previously completed test in the sequence, such test shall be repeated.

# DOCUMENTATION

A test report shall be produced logging all events and the results of the visual inspections. Also all main resonances shall be reported and the worst case responses at the subsystem interfaces. The rest report shall also contain the environmental measurement data (taken during the test) and the calibration/qualification certificates of the test facility.

# PRODUCT ASSURANCE

Before a test can proceed a Test Readiness Review (TRR) shall be convened by the SPIRE project manager.  All the relevant test and facility documentation will be made available.  The TRR must give approval before the test can commence. The TRB will convene between each reconfiguration of the test set-up. The test set up can be dismanteled after the TRB convened and agrees.

The test review board will consist of the project manager, quality control manager, mechanical engineer responsible for the test and the test facility manager or their representatives.

Appenix A - INSTRUMENTATION SPECIFICATION

The instrumentation will consists, as a minimum of:

- At the monuting point of the instrument (interface with vibration fixture) tri axial for one, excitation direction for all (4 channels)

- Top of the optical bench in instrument coordinates: +X,+Z tri-axial or near that location. (3 channels)

- +X,-Z,-Y corner of the instrument, tri-axial (3 channels)

- Spectrometer detector box tri-axial (any suitable location) (3 channels)

- Photometer detectorbox 2 on extreme oposite ends measuring in Z direction (2 channels)

- Photometer detectorbox 2 on extreme oposite ends measuring in Y direction (2 channels)

- Photometer detectorbox 1 on any suitable location measuring in X direction (1 channel)

- At the foot of He3 cooler in Y direction (1 channel)

- At the foot of the SMec in Y direction (1 channel)

- At the foot of the BSM in Y direction (1 channel)

- Force in three axes (interface force) (3 channels)