SPIRE-LAM-REP-001881

MCU / BSM DM Mechanism

Integration and Test Report

| Document Prepared by | D.FERRAND | 20/10/2003 |
| --- | --- | --- |
| Document Approved by | B. STOBIE |  |
| Document Released by | P.BARR-BURMAN D.POULIQUEN |  |

Record of issues

| Date | Issue | Remarks |
| --- | --- | --- |
| 20/10/2003 | 1.0 | First issue |

Distribution List

| SPIRE-PROJECT | Matt Griffin | X |
| --- | --- | --- |
|  | Bruce M.Swinyard | X |
|  | Ken J.King | X |
|  | Doug Griffin | X |
| UK-ATC | Colin Cunningham | X |
|  | Phillip Parr-Burman | X |
|  | Brian Stobie | X |
| CEA-Sap | Jean-Louis Auguères | X |
|  | Christohe Cara | X |
|  | Jean Fontignie | X |
| LAM | Dominique Pouliquen | X |
|  | Patrick Levacher | X |

Table of contents

1	Introduction	4

2	Goals of integration	4

3	General experiment set up	4

4	Measured performances vs. requirements	5

5	Detailed results	6

5.1	Chopper Axis Measurements	6

5.1.1	Open loop measurements	6

5.1.2	Open loop scaling	7

5.1.3	Scaling the back emf	8

5.1.4	Chopper closed loop step response	9

5.1.5	Position stability/ noise in closed loop	10

5.2	Jiggle axis measurements	11

5.2.1	Open loop	11

5.2.2	Jiggle sensor scaling	11

5.2.3	Step response in closed loop	12

6	Conclusion	13

# Introduction

This document aims to report about the MCU QM0 electronics and the BSM Development Model integration which was performed at ATC premises during October 14th and 15th 2003.

# Goals of integration

The integration aimed to verify that MCU was running in open and closed loop on both chopper and jiggle axis with the same performances than the dSpace control system used by ATC during lifetime tests and to validate the control scheme and parameters on both side (MCU and dSpace).

The integration did not aim to fine calibrate the absolute position since this step shall be necessary only on the Flight model.

For DM integration, the absolute position was roughly measured using a laser beam hitting the BSM mirror cold down at around 4K and reflected on a wall at a distance of about 6.7 meters.

# General experiment set up

The experiment set-up consisted in :

- a 233 MHz PC equipped with Labview program to send commands to MCU Mac board and to receive telemetry bsm packets,

- a MCU assembly including a MAC board QM1 model, a BSM 40mA QM0 model and a QM1 model backplane,

- a harness compliant with configured  SPIRE pin-out definition and including 10 Ohm resistors on motor lines to be representative with flight model cold harness resistance,

- the BSM DM model put in a cryostat equipped with a window

- a laser beam projected on BSM mirror through the window and reflected on a distant wall.

# Measured performances vs. requirements

This is a recall of main performances to be achieved. The measured values during MCU/BSM integration do not differ significantly as compared with the results of performances tests presented during Instrument hardware Design Review by ATC on July 9th and 10th 2003.

| Requirement item | Specified value | Measured value on DM(peak) | Conformance |
| --- | --- | --- | --- |
| Angular Travel Chop Jiggle | +/-2.53° (+/-130 arcsec sky) +/- 0.573° | +/- 2.51° With 40mA analogue board. +/-0.6° | Shall be compliant with 50mA analogue board QM1 model |
| Minimum chop throw | +/- 0.1° | TBD | TBD |
| Minimum step size Chop Jiggle | 2 arcsec sky (=0.038 °) 0.039° | 0.0002° (ADC accuracy) 0.0001° (ADC accuracy) | Ok Ok |
| Position accuracy | 0.004° | 0.0002° (ADC accuracy) | Ok after linearisation process to be done on FM |
| Position resolution | 0.0005° | 0.0001° (ADC resolution) | ok |
| Stability | 0.2 arcsec sky (=0.004°) | 0.0006° (short term) | ok |
| Settling time Chop Jiggle | 20ms 100ms | ~ 20ms ~ 60ms | Ok Ok |
| Frequency Chop Jiggle | Up to 2Hz Up to 0.5 Hz | Max frequency: 40Hz but power dissipation not measured Max Frequency 10 Hz | Ok |

# Detailed results

## Chopper Axis Measurements

### Open loop measurements

The following table gives the relationship between chopper target position, motor current sent to DAC and estimated position in open loop. This table  implies that the chopper position scale factor parameter (see SetCPositionScaleFactor in command list) is set to default value of 3051. With this setting there is the same digital value sent to DAC as the target position reference parameter.

| motor current and dac output = f(openloop reference) with default position scale factor parameter |
| --- |
|  |  | after inner scale factor |  |  |  |  |
| MCU position scale parameter= | 3051 | 3,05176E-05 |  |  |  |  |  |
|  |  |  | open loop reference (32768=0) | dac value | dac volt output | motor current(mA) | estimated position(°) |
|  |  |  | 0 | 0 | -10 | -40 | -2,51159794 |
|  |  |  | 20000 | 20000 | -3,8964844 | -15,586 | -0,97864021 |
|  |  |  | 32768 | 32768 | 0 | 0 | 0 |
|  |  |  | 35000 | 35000 | 0,6811523 | 2,7246 | 0,17107808 |
|  |  |  | 40000 | 40000 | 2,2070313 | 8,8281 | 0,55431751 |
|  |  |  | 45000 | 45000 | 3,7329102 | 14,932 | 0,93755694 |
|  |  |  | 46000 | 46000 | 4,0380859 | 16,152 | 1,01420483 |
|  |  |  | 47000 | 47000 | 4,3432617 | 17,373 | 1,09085272 |
| flex stiffness: | 0,073 | Nm/rad | 48000 | 48000 | 4,6484375 | 18,594 | 1,1675006 |
| motor cst | 0,08 | Nm/A | 49000 | 49000 | 4,9536133 | 19,814 | 1,24414849 |
| pwr amp max current | 0,04 | A/10V | 50000 | 50000 | 5,2587891 | 21,035 | 1,32079638 |
|  |  |  | 60000 | 60000 | 8,3105469 | 33,242 | 2,08727524 |
|  |  |  | 65532 | 65532 | 9,9987793 | 39,995 | 2,51129134 |

Table 1 : correpondance between motor current, dac output and target position with default position scale factor

To calibrate the chopper we first send an open loop current on DAC. The chosen value is 20000 corresponding to  -1° displacement with a –15.5 mA motor current in the analogue board (see table 1). For this, we perform the following commanding scenario (after the power  switch on and the boot on RAM program):

| Wait between commands | Commanding scenario | Command sent by DPU | Action |
| --- | --- | --- | --- |
| 1ms | SetCSensorPwr,on | 90C00001 | Switch on the 1mA current to be sent to sensor |
| 1ms | SetCPositionScaleFactor,3051 | 90D60BEB | Set the open loop constant between target position and DAC value =1/32768 in order to control in open loop with DAC units (see table 1). |
| 1ms | SetCRateLimit,1000 | 90D103E8 | Apply the slew rate limit to avoid too fast step response in open loop and too much oscillations. |
| 1ms | SetChopLoopMode,3 | 90C20003 | Set the loop mode in open loop mode (no sensor) |
| 1ms | SetChopTargetPosition,20000 | 90C34E20 | Perform a step to 20000,ie –15,5mA or –1° |
| 1ms | SetTelemetryPacket12Sample,8 | 91C20008 | Start BSM Packet telemetry at 8*400us rate. |

The open loop step position is captured on oscilloscope. To be able to operate in open loop, some damping must be added by mean of backemf provided by the motor coil.

### Open loop scaling

The measurements taken by BSM telemetry packet are:

- Sensor ADC value: 21276, ie 3.51 volts; (at 0 position: 29741, ie –0.92 volts). The sensor sensibility is therefore around 3.51-0.92= 2.58 V/deg.

| expected position(°) =f(sensor ADC) =f(target position) |  |
| --- | --- |
|  | target position | sensor volts | position(°) |
| mr sensitivity(V/deg) | 55000 | 6,78466797 | 2,65216717 |
|  | 50000 | 5,25878906 | 2,055692006 |
| 0,06 | 40000 | 2,20703125 | 0,862741678 |
| bsm gain 1 | 30000 | -0,84472656 | -0,330208651 |
|  | 20000 | -3,89648438 | -1,52315898 |
| 19,38 | 15000 | -5,42236328 | -2,119634144 |
| bsm gain 2 | 11000 | -6,64306641 | -2,596814275 |
| 2,2 |  |  |  |
| difference |  |  |  |
| 1 |  |  |  |
| MR ADC scale (V/deg) |  |  |
| 2,55816 |  |  |  |

This value is compliant with the magneto resistance  measured sensibility of 60,4 mV/° amplified by a factor of 2.2*19.38= 42.63 by the analogue BSM board (0.0604*42.63= 2.575 V/°).

- Motor current ADC value: 19973 (there is so a difference with 20000 demanded at DAC level)

- Motor voltage ADC value: 6892

Now we have to calibrate the backemf feedback to allow open loop with some damping.

### Scaling the back emf

The goal of the back emf is to apply speed feedback control by mean of the motor voltage measurement. This feedback shall damp the axis natural oscillation. The useful information is the motor backemf voltage which is proportional of the motion speed. The undesired information is the R*I voltage which is the voltage drop in both coil and harness. The following procedure aims to remove the useless information RI:

- Determine the ratio between motor current and motor voltage as measured on telemetry:

( Motor Voltage-32768)/(Motor current-32768)= -25876 / -12795= 2.02

| backemf |  |  |
| --- | --- | --- |
|  |  | at 0 |
| max current measured | 19973 | 32768 |
| max voltage mesured | 6892 | 32768 |
| ratio V/I | 2,02235248 |  |
| parameter (Rmot) | 20224 |  |

- Send the command corresponding to SetCMotor resistance,20224: 90D34F00

- Now apply some gain of the feedback: SetCMotorbackEmfGain,500:90D201F4

Going to a new target position, the result is an open loop damped as shown next figure.

### Chopper closed loop step response

The closed loop operation need to adjust PID parameters according to dSpace preliminary control results. The following table gives the correspondance between dSpace and MCU 16 bit integer parameter due to necessary scale factor conversion :

| PID Parameter | ATC parameter | ADC/volts | mr deg/volts | ADC/deg | conversion dSPACE->MCU | parameter fixed scale factor | parameter in MCU |
| --- | --- | --- | --- | --- | --- | --- | --- |
| PROPORT | 4,17 | 3276,8 | 0,39090596 | 8382,58 | 0,000497 | 1E-08 | 19898 |
| DERIVATIVE | 0,014 | 3276,8 | 0,39090596 | 8382,58 | 1,67E-06 | 1E-10 | 6681 |
| INTEGRAL | 275 | 3276,8 | 0,39090596 | 8382,58 | 0,032806 | 1E-06 | 13122 |
| INTEGRAL LIMIT | 0,04 | 3276,8 | 0,39090596 | 8382,58 | 4,77E-06 | 1E-06 | 12407 |

In addition, the feedforward gain must be adjusted according to the open loop results.

To operate closed loop control we first send the following commanding scenario from the present open loop configuration.

| Wait between commands | Commanding scenario | Command sent by DPU | Action |
| --- | --- | --- | --- |
| 1sec | SetChopTargetPosition,32768 | 90C38000 | Go to the 0 position to send 0 on dac (safety) |
| 1ms | SetCKp,19898 | 90C84DBA | Set the PID proportional gain |
| 1ms | SetCKd,6681 | 90C91A19 | Set the PID derivative gain |
| 1ms | SetCKi,13122 | 90CA3342 | Set the PID integral gain |
| 1ms | SetChopLoopMode,1 | 90C20001 | Close the loop on the sensor |
| 1ms | SetCRateLimit,800 | 90D10320 | Decrease the slew rate limiter of the step |
| 1ms | SetChopTargetPosition,20000 | 90C34E20 | Go to the target position in step mode |

The dynamics taken by oscilloscope on sensor signal shows a settling time of about 20ms.

Remark: noise level is not representative due to oscilloscope probe measurement. See position stability and noise chapter for actual data as read out by ADC converters.

### Position stability/ noise in closed loop

During a steady position of chopper axis in closed loop, the position noise is +/- 5 ADC unit, ie +/- 1.54 mV. The chop sensor signal has a sensibility of 2.55V/deg. The chop position noise is therefore +/- 0.0006°.

Note: the Y axis unit is the ADC digital value obtained from telemetry.

Figure 1: Chopper sensor ADC signal at steady position

## Jiggle axis measurements

### Open loop

The following table gives the relationship between jiggle target position, motor current sent to DAC and estimated position in open loop. This table  implies that the jiggle position scale factor parameter (see SetJPositionScaleFactor in command list) is set to default value of 3051.

With this setting there is the same digital value sent to DAC as the target position reference parameter.

| motor current and dac output = f(openloop reference) |  |  |  |  |
| --- | --- | --- | --- | --- |
| MCU position scale factor parameter | 3051 |  | open loop reference (32768=0) | dac value | dac out | motor current(mA) | estimated position(°) |
| after scale factor | 3,05176E-05 |  | 0 | 0 | -1 | -40 | -0,65480946 |
|  |  |  | 20000 | 20000 | -0,3896484 | -15,586 | -0,25514548 |
|  |  |  | 32768 | 32768 | 0 | 0 | 0 |
|  |  |  | 35000 | 35000 | 0,0681152 | 2,7246 | 0,0446025 |
|  |  |  | 40000 | 40000 | 0,2207031 | 8,8281 | 0,14451849 |
|  |  |  | 45000 | 45000 | 0,373291 | 14,932 | 0,24443449 |
|  |  |  | 46000 | 46000 | 0,4038086 | 16,152 | 0,26441769 |
|  |  |  | 47000 | 47000 | 0,4343262 | 17,373 | 0,28440089 |
| flex stiffness: | 0,56 | Nm/rad | 48000 | 48000 | 0,4648438 | 18,594 | 0,30438409 |
| motor cst | 0,16 | Nm/A | 49000 | 49000 | 0,4953613 | 19,814 | 0,32436728 |
| pwr amp max current | 0,04 | A/10V | 50000 | 50000 | 0,5258789 | 21,035 | 0,34435048 |
|  |  |  | 60000 | 60000 | 0,8310547 | 33,242 | 0,54418247 |
|  |  |  | 65532 | 65532 | 0,9998779 | 39,995 | 0,65472953 |

### Jiggle sensor scaling

Before closing the loop, the magnetoresistor sensor scale factor must be known. This scale factor shall be used to adjust the necessary feed forward gain and to have a relationship between desired position (°) and sensor signal 16 bit parameters (which, in closed loop without static error, shall be the same as the target position). At cold, the magneto resistors have a sensibility of 130mV/°. After amplification in the BSM analogue board of 2.2*19.195, the overall sensitivity as seen by ADC is 5.48 V/°.

| position(°) =f(sensor ADC) or f(target position in closed loop) |
| --- |
|  | Target position | volts | position(°) |
| mr sensitivity(V/deg) | 20000 | -3,32641602 | -0,605929942 |
| 0,13 | 22500 | -2,56347656 | -0,466955184 |
|  | 25000 | -1,80053711 | -0,327980427 |
| bsm gain 1 | 27500 | -1,03759766 | -0,18900567 |
| 19,195 | 30000 | -0,2746582 | -0,050030913 |
|  | 32500 | 0,48828125 | 0,088943845 |
|  | 35000 | 1,2512207 | 0,227918602 |
|  | 37500 | 2,01416016 | 0,366893359 |
|  | 40000 | 2,77709961 | 0,505868116 |
| bsm gain 2 | 42500 | 3,54003906 | 0,644842874 |
| 2,2 | 30900 | 0 | 0 |
| 1 |  |  |  |
| MR ADC scale (V/deg) |  |  |  |
| 5,48977 |  |  |  |

### Step response in closed loop

The same procedure of tuning has been applied on jiggle axis as chopper axis. Crude tuning of the PID allow to perform a settling within 60ms instead of 100ms required. However some additional time to fine tune this axis should improve the dynamics but at the price of the motor current solicitation. The commanding scenario is identical as the chopper one.

# Conclusion

The MCU/BSM DM integration did not show difference in the dynamics of the control between ATC lifetime operation using dSpace, and PID+Feedforward algorithm implemented in the MCU DSP.

This integration confirms the system performances achieved during lifetime tests using dSpace instead of MCU as presented during Instrument Hardware Design Review held July 9thand 10th 2003 (see ATC BSM Viewgraphs).

Final performances and position calibration shall be done on FM (and Spare) during another integration process.