Total Pages : 8

|  | CDMU DFE TM/TC Services Product Code: 3A2200 |  |
| --- | --- | --- |

| Rédigé par/Written by | Responsabilité-Service-Société Responsibility-Office –Company | Date | Signature |
| --- | --- | --- | --- |
| L. FADE | Planck Platform/Electrical Tests Responsible | 28/10/03 |  |
| Vérifié par/Verified by |  |  |  |
| J. P. HAYET | Planck AIT System Responsible | 13/11/03 |  |
| Approbation/Approved |  |  |  |
| J. Y. CHARNIER | Planck AIT Responsible | 14/11/03 |  |
| D. MONTET | H/P AIV Responsible |  |  |
| C. MASSE | Product Assurance Manager |  |  |
| J. J. JUILLET | Project Manager |  |  |

Entité Emettrice : Alcatel Space - Cannes

(détentrice de l’original) :

|  | DISTRIBUTION RECORD |
| --- | --- |
|  | Issue DRAFT/ Rev. : 1.0 |
| DOCUMENT NUMBER : H-P-1-ASP-TN-0591 | Date: 12/11/03 |
| EXTERNAL DISTRIBUTION |  | INTERNAL DISTRIBUTION |  |
| ESA | X | HP team | X |
| ASTRIUM | X |  |  |
| ALENIA | X |  |  |
| CONTRAVES |  |  |  |
| TICRA |  |  |  |
| TECNOLOGICA |  |  |  |
| HFI | X |  |  |
| LFI | X |  |  |
| HIFI | X |  |  |
| PACS | X |  |  |
| SPIRE | X |  |  |
|  |  | Clt Documentation | Orig. |

ENREGISTREMENT DES EVOLUTIONS / CHANGE RECORDS

| ISSUE | DATE | § : DESCRIPTION DES EVOLUTIONS § : CHANGE RECORD | REDACTEUR AUTHOR |
| --- | --- | --- | --- |
| 1 | 24/09/2003 | Creation | L. FADE |

TABLE OF CONTENTS

1.	INTRODUCTION	5

2.	APPLICABLE AND REFERENCE DOCuMENTS	5

2.1	Applicable Documents	5

2.2	Reference Documents	5

3.	TM/TC Services available	6

3.1	TM/TC Services Table	6

3.2	TM/TC Services covered by the CDMU DFE	7

# INTRODUCTION

This document describes the TM/TC Services available for the warm units during the H/P PLM Tests.

The Test Set up is the following:

As the CDMU DFE does not completely simulate the CDMU Behaviour, the goal of this document is to summarize what TM/TC Services will be available during the tests.

# APPLICABLE AND REFERENCE DOCuMENTS

## Applicable Documents

[AD1]	H-P-1-ASPI-SP-0045	EGSE General Requirement Specification

[AD2]	H-P-1-ASPI-IS-0121	EGSE INTERFACE Requirements Specification

## Reference Documents

[RD1]	SCI-PT-ICD-07527	Packet Structure Interface Control Document

[RD2]	H-P-ASP-MN-2708	Questions/Open Points for CDMU DFE

[RD3]	H-P-SAT-DD-1002	CDMU DFE System Design Description

[RD3]	H-P-MI-AI-225		SSBV Progress Meeting 2

# TM/TC Services available

## TM/TC Services Table

Here are the available Services available in the CDMU DFE:

| Service Number | Description | Available for TC | Available for TM | Covered Sub Services or CCS |
| --- | --- | --- | --- | --- |
| 1 | TC verification | N/A | OK | 1-1, 1-2 |
| 2 | Device Command Distribution Service | Not Supplied | N/A |  |
| 3 | Housekeeping and Diagnostic Data Reporting | Not Supplied * | Not Supplied * |  |
| 4 | Not Used | N/A | N/A |  |
| 5 | Event Reporting | Not Supplied | Not Supplied | CCS Receives TM packet |
| 6 | Memory Management | Not Supplied | OK (like 1) | 1-1, 1-2 CCS Receives TM packets and routes them to I-EGSE |
| 7 | Not Used | N/A | N/A |  |
| 8 | Function Management | Not Supplied | Not Supplied |  |
| 9 | Time Management Service | OK | Not Supplied | 9-3, 9-4, 9-5 |
| 10 | Not Used | N/A | N/A |  |
| 11 | On-board Operations Scheduling Service | Not Supplied | Not Supplied | Covered by CCS TCL Test Sequences |
| 12 | On-board Monitoring Service | Not Supplied | Not Supplied |  |
| 13 | Not Used | N/A | N/A |  |
| 14 | Packet Transmission Control Service | Not Supplied | Not Supplied |  |
| 15 | On-board Storage and Retrieval Service | Not Supplied | Not Supplied |  |
| 16 | On-board Traffic Management | Not Supplied | Not Supplied |  |
| 17 | Test Service | OK | OK | (17-1, 17-2) default |
| 18 | On-board Control Procedure Service | Not Supplied | Not Supplied | Covered by CCS TCL Test Sequences |
| 19 | Event/Action Service | Not Supplied | Not Supplied | Covered by CCS TCL Test Sequences |
| 20 | Information Distribution CDMS | Not Supplied | Not Supplied | CCS Receives TM packet and routes it to I-EGSE |
| 21 | Science Data Transfer Service | N/A | Not Supplied | CCS Receives TM packet and routes it to I-EGSE |
| 22 | Not Used | N/A | N/A |  |

* Note: Service 3 can be sent to CDMU DFE for Instruments Packet update but not for CDMU DFE’s packet update.

NB: “Not Supplied” means: not supplied by CDMU DFE but supplied by CCS (CDMU DFE acts like a mail box transferring messages)

## TM/TC Services covered by the CDMU DFE

- Any TM message received by CDMU DFE (i.e. any TM service) is put into a PIPE message (PIPE trailer + PIPE Body Message). Then it is sent to CCS and to Instruments EGSE Connected onto the CCS LAN.

- The only TC service explicitly simulated by CDMU DFE are services:

- 1,

- 9 (supplied services are 9.3, 9.4, 9.5 ; Services 9.6, 9.7 and 9.9 are NOT supplied),

- 17.

- Other services are NOT implemented in the CDMU DFE Software.

- TC Services that are not available on CDMU DFE might be covered by CCS Functions. (for instance time tagged TC are generated via a CCS dedicated test sequence)

END OF DOCUMENT

# Text boxes

HERSCHEL / PLANCK

CCS

PLM SCOE /CDMU DFE

Warm Units

I-EGSE