| SUBJECT: | SPIRE Data Products SpecificationSPIRE Data Products Specification |
| --- | --- |
| PREPARED BY: | K.J. KingK.J. King |
| DOCUMENT No: | SPIRE-RAL-DOC-002005SPIRE-RAL-DOC-002005 |
| ISSUE: | Issue 0.2Issue 0.2 | Date: | 7th September 20047th September 2004 |
| APPROVED BY: |  | Date: |  |

# Distribution

# Change Record

| ISSUE | DATE | Changes |
| --- | --- | --- |
| Draft 1 | 6th May 2004 | Initial draft containing detector timeline definitions |
| Issue 0.2 | 7th September 2004 | Updated to include SDT, SMECT and SDS product definitions |

Table of Contents

Distribution	3

Change Record	4

Glossary	6

1.	Introduction	7

1.1	Scope	7

1.2	Structure of Document	7

1.3	Documents	7

1.3.1	Applicable Documents	7

1.3.2	Reference Documents	7

2.	Scientific Data Products	8

2.1	Common Data Products	8

2.1.1	Attitude Timeline	8

2.1.2	Beam Steering Mirror Timeline	8

2.1.3	Spectrometer Mechanism Timeline (SMECT)	9

2.1.3.1	Product Format	9

2.1.3.2	Product Contents	10

2.1.4	SCU Timeline	11

2.1.5	Spacecraft Housekeeping Timeline	11

2.1.6	Events Timeline	11

2.1.7	Orbit Timeline	11

2.2	Photometer Specific Products	12

2.2.1	Photometer Detector Timeline (PDT)	12

2.2.1.1	PDT Product Format	13

2.2.1.2	Product Contents	14

2.2.2	Demodulated Detector Timeline	15

2.2.3	Time Averaged Detector Timeline	15

2.2.4	Pointed Photometer Product	15

2.3	Spectrometer Specific Products	16

2.3.1	Spectrometer Detector Timeline (SDT)	16

2.3.1.1	Product Format	17

2.3.1.2	Product Contents	18

2.3.2	Spectrometer Detector Spectrum Product (SDS)	20

2.3.2.2	Product Format	21

2.3.2.3	Product Contents	22

3.	Calibration Data Products	24

Tables

Table 2-1	12

Table 2-2	16

Table 2-3	20

# Glossary

# Introduction

This note specifies the content and structure of the SPIRE data products. These are produced as calibration products created from information provided by instrument manufacturers, calibration products produced from calibration tests and observations after processing through IA and scientific data products generated by the datat processing steps of IA and the SPIRE pipelines.

## Scope

This note is intended to provide the complete definition of the format and contents of all SPIRE data products. The processing that goes into creating the content of the products is described elsewhere (in the individual data processing specification for each processing step - for use by software developers, and in the SPIRE Data Processing Description Document – for use by users of the data products).

## Structure of Document

Section 2 describes the scientific data products produced at various stages of the data processing pipelines.

Section 3 describes the calibration data products used by the scientific data processing steps

## Documents

### Applicable Documents

### Reference Documents

| RD01 | Engineering Data Processing Specification |
| --- | --- |

# Scientific Data Products

## Common Data Products

### Attitude Timeline

TBW

### Beam Steering Mirror Timeline

TBW

### Spectrometer Mechanism Timeline (SMECT)

This spectrometer product is presented as a generic data product. It contains data samples from the spectrometer stage mechanism including the times at which the stage was sampled. A single timeline will contain the data from at most one observation. Normally each building block in an observation will only generate one type of SMEC science data frame but in the event that more than one type is generated multiple data products will be produced.

The data are extracted directly from a single type of science data frame from a single BB generated by the instrument MCU and subsequently stored in the HCSS. The data may have been processed. It is expected that MCU science frames with an invalid checksum, or FrameID will be rejected during the creation of the Data Frames and therefore the SMEC data product will not contain these.

This data product is produced when SMEC data is generated with the instrument in a spectrometer configuration.

#### SMECT Product Format

| product (type=”SMECT”, description=” Spectrometer Mechanism Timeline”) |
| --- |
| Metadata: |  |
| string | Creator | (description=”Creator”, quantity=””) |
| date | creationDate | (description=”Creation Date”, quantity=”UTC”) |
| string | instrument | (description=”Instrument”, quantity=””) |
| string | modelName | (description=”Instrument Model Name”, quantity=””) |
| date | StartDate | (description=”Start Date”, quantity=”UTC”) |
| date | EndDate | (description=”End Date”, quantity=”UTC”) |
| long | Obsid | (description=”Observation Identifier”, quantity=””) |
| long | Bbtype | (description=”Building Block type”, quantity=””) |
| long | Bbcount | (description=”Building Block execution counter”, quantity=””) |
| string | AOT | (description=”AOT Identifier”, quantity=””) |
| composite dataset | (description=”Mechanism Timeline”) |
| table dataset | (description=”Mechanism Scan Timeline”) |
| metadata: |  |
| long | SCANNR | (description=”Current Scan Number”, quantity=””) |
| boolean | SCANDIRECTION | (description=”Scan direction”, quantity=””) |
| integer-1d[] | FrameTime | (description=”SMEC Frame Time”, quantity=”1/312500 Secs”) |
| double-1d[] | SMECSEL_ENCPOSN | signal (description=”SMEC Scan Optical Encoder Position timeline”, quantity=”μm”) |
| double-1d[] | SMECSEL_ENCFINEPOSN | signal (description=”SMEC Scan Optical Encoder Fine Position timeline”, quantity=”nm”) |
| double-1d[] | SMECLVDTPOSN | (description=”LVDT Position”, quantity=”μm”) |
| integer-1d[] | Mask | (description=”Data Mask”, quantity=””) |
| ….. |  |
| history |  |
| ….. |  |

#### SMECT Product Contents

| Data Item | Description |
| --- | --- |
| Creator | Name of the module which created the product. This should indicate the version also. Is set by the creator task, e.g. to “EngineeringDataModule Version_n.m” |
| creationDate | UTC of the date and time of creation of the product. Is set by the creator task. |
| instrument | Set to “SPIRE” Can be derived from the first two bits of OBSID. |
| modelName | Name of the instrument model from which the data came e.g. “CQM”, “PFM1”, “FM”, “FS” Can be derived from the first four bits of the BBID. |
| startDate | UTC of the date and time of the start of the observation to which this product relates. Can be derived from the contents of this product. |
| endDate | UTC of the date and time of the end of the observation to which this product relates. Can be derived from the contents of this product. |
| Obsid | The OBSID parameter from the first Normal Housekeeping TM packet with a time belonging to this building block Since OBSID serves as the overall index of all observations I would assume that it is specified by the requestor of a product. |
| Bbtype | The BBID’s type parameter (14 bits) from the first Normal Housekeeping TM packet with a time belonging to this building block. |
| Bbcount | The BBID execution count parameter (16 bits) from the first Normal Housekeeping TM packet with a time belonging to this building block. |
| AOT | SOFn with n=1..4, depending on the operating mode used. SOF0 can be used when no template is used, e.g. in the case of a non-standard observation. (TBC) How could this be derived? |
| SCANNR | Number of the current scan. One scan is defined as data collected from initial to final position at stabilized speed in the same direction. Can be derived from the contents of this product if information is not available in hk packets (TBC). |
| SCANDIRECTION | Direction of the current scan. Can be derived as follows: 0 or false if scanned<scanstart else 1 or true. |
| FrameTime | Frame time in clock ticks since the last clock reset. The clock runs at a rate of 312500Hz. Pulses get counted by 32 bit counters. Integer is a signed 32 bit variable. We should check that the 32-bit signed format will convert properly into the unsigned format, i.e. negative values must turn into high positive clock counts. Taken from the science report. |
| SMECSEL_ENCPOSN | The coarse position given by the optical encoder at the respective time (resolution of the encoder position is 1μm). Taken from the science report. |
| SMECSEL_ENCFINEPOSN | The fine position given by the optical encoder at the respective time (resolution of the encoder position is 1nm with a maximum distance of 65μm). Taken from the science report. |
| SMECLVDTPOSN | The position given by the LVDT at the respective time (resolution of the encoder position is 0.3μm). TBC how information is calculated from SMECLVDTDCSIG. |
| Mask | Bit mask indicating whether the value failed to meet certain criteria (first bit = 1 indicates failure): |

### SCU Timeline

TBW

### Spacecraft Housekeeping Timeline

TBW

### Events Timeline

TBW

### Orbit Timeline

TBW

## Photometer Specific Products

### Photometer Detector Timeline (PDT)

This product contains data samples from a set of detector channels (containing data from detector pixels, temperature sensors and fixed reference resistors) along with a time at which the channels were sampled. A single timeline will contain the data from at most one observation building block. Normally each building block in an observation will only generate one type of detector science data frame but in the event that more than one type is generated multiple data products will be produced.

The data is extracted directly from a single type of science data frame generated by the instrument DCU and subsequently stored in the HCSS. The data may have been processed. It is expected that DCU science frames with an invalid checksum, or FrameID will be rejected during the creation of the Data Frames and therefore the detector data product will not contain these.

This product is produced when detector data is generated with the instrument in a photometer configuration. In these configurations several different science data frames can be generated

The different photometer science data frame types are:

| Frame Type | Number of Channels | DCU Frame ID (hex) | TM Packet APID (hex) | TM Packet SID (hex) | Subsystem | ArrayName |
| --- | --- | --- | --- | --- | --- | --- |
| Photometer Full Array | 288 | 00 | 3 | 0200 | “PHOTOMETER” | “PSW” “PMW” “PLW” |
| PSW Array | 144 | 02 | 3 | 0102 | “PHOTOMETER” | “PSW” |
| PMW Array | 96 | 03 | 3 | 0103 | “PHOTOMETER” | “PMW” |
| PLW Array | 48 | 04 | 3 | 0104 | “PHOTOMETER” | “PLW” |
| Photometer Test Pattern | 288 | 09 | 3 | 0309 | “PHOTOMETER” | “PSW” “PMW” “PLW” |
| PSW Test Pattern | 144 | 0A | 3 | 030A | “PHOTOMETER” | “PSW” |
| PMW Test Pattern | 96 | 0B | 3 | 030B | “PHOTOMETER” | “PMW” |
| PLW Test Pattern | 48 | 0C | 3 | 030C | “PHOTOMETER” | “PLW” |
| Parallel Mode Data | TBD |  | 5 | 0F01 | “PHOTOMETER” | TBD |
| Transparent Data | TBD |  | 5 | FF00 | TBD | TBD |

Table 2-1

#### PDT Product Format

| product (type=”PDT”, description=” Photometer Detector Timeline”) |
| --- |
| metadata: |  |
| string | creator | (description=”Creator”, quantity=””) |
| date | creationDate | (description=”Creation Date”, quantity=”UTC”) |
| string | instrument | (description=”Instrument”, quantity=””) |
| string | modelName | (description=”Instrument Model Name”, quantity=””) |
| date | startDate | (description=”Start Date”, quantity=”UTC”) |
| date | endDate | (description=”End Date”, quantity=”UTC”) |
| long | obsid | (description=”Observation Identifier”, quantity=””) |
| long | bbid | (description=”Building Block Identifier”, quantity=””) |
| long | bbtype | (description=”Building Block Type”, quantity=””) |
| composite dataset | (description=”Detector Timeline”) |
| metadata: |  |
| string | subsystem | (description=”Instrument Subsystem”, quantity=””) |
| composite dataset | (description=”Array Timeline”) |
| metadata: |  |
| string | arrayName | (description=”Detector Array Name”, quantity=””) |
| string | modelName | (description=”Model Name”, quantity=””) |
| table dataset | (description=”Pixel Timeline”) |
| metadata: |  |
| string | pixelName | (description=” Pixel Name”, quantity=””) |
| string | source | (description=”Source packet”, quantity=””) |
| integer | pixelId | (description=”Pixel Identifier”, quantity=””) |
| double-1d[] | obt | (description=”On Board Time”, quantity=”Secs”) |
| double -1d [] | signal | signal (description=”Detector Signal”, quantity=”Volts”) |
| double -1d [] | error | (description=”Error on signal”, quantity=”Volts”) |
| integer-1d[] | mask | (description=”Data Mask”, quantity=””) |
| table dataset | (description=”Pixel Timeline”) |
| ……. |  |
| table dataset | (description=”Pixel Timeline”) |
| ……. |  |
| composite dataset | (description=”Array Timeline”) |
| ….. |  |
| history |  |
| ….. |  |

#### PDT Product Contents

| Data Item | Description |
| --- | --- |
| creator | Name of the module which created the product. This should indicate the version also. Normally is expected to be “EngineeringData Version_n.m” |
| creationDate | UTC of the date and time of creation of the product |
| instrument | Set to “SPIRE” |
| modelName | Name of the instrument model from which the data came e.g. “CQM”, “PFM1”, “FM”, “FS” |
| startDate | UTC of the date and time of the start of the Building Block to which this product relates |
| endDate | UTC of the date and time of the end of the Building Block to which this product relates |
| obsid | The OBSID parameter from the first Normal Housekeeping TM packet with a time belonging to this building block |
| bbid | The BBID parameter from the first Normal Housekeeping TM packet with a time belonging to this building block |
| bbtype | The BBTYPE parameter from the first Normal Housekeeping TM packet with a time belonging to this building block |
| subsystem | Name of the subsystem generating the data As defined in Table 2-1 |
| arrayName | Name of the detector array to which the data relates As defined in Table 2-1 |
| modelName | Name of the model of the array from which the data came e.g. “CQM”, “PFM1”, “FM”, “FS” |
| pixelName | Unique Name for the pixel For example pixel C5 on the PLW array = “PLWC5” This name identifies the physical pixel from which the data has come irrespective of the type of data frame in which the data was transmitted |
| pixelSource | Identifies the source packet from which the pixel data has been extracted. For example “PHOTLW” |
| pixelID | Identifies the channel in the source packet from which the data comes. For example pixel “PLWC5” may be found in packet “PHOTLW” at location 035 Note: Channel numbers start from 001 |
| obt | The on board time of each sample of the pixel. The value is represented as a Double representing the seconds since a fixed date (nominally Jan 1st 1958) |
| signal | The signal from the detector. This may be represented in raw or engineering units |
| error | Error in the measured signal value. |
| mask | Bit mask indicating whether the pixel failed to meet certain criteria (bit = 1 indicates failure): Bit 0 (lsb) the master bit, is set whenever any of the other bits is set to allow easy detection of a bad sample Bit 1 when set indicates invalid data sample time (see Engineering Data Specification) Bit 2 when set indicates a possible ADC latch up error occurred for this sample (see Engineering Data Specification) Other bits are TBS |

### Demodulated Detector Timeline

TBW

### Time Averaged Detector Timeline

TBW

### Pointed Photometer Product

TBW

## Spectrometer Specific Products

### Spectrometer Detector Timeline (SDT)

This product contains data samples from a set of detector channels (containing data from detector pixels, temperature sensors and fixed reference resistors) along with a time at which the channels were sampled. A single timeline will contain the data from at most one observation building block. Normally each building block in an observation will only generate one type of detector science data frame but in the event that more than one type is generated multiple data products will be produced.

The data is extracted directly from a single type of science data frame generated by the instrument DCU and subsequently stored in the HCSS. The data may have been processed. It is expected that DCU science frames with an invalid checksum, or FrameID will be rejected during the creation of the Data Frames and therefore the detector data product will not contain these.

This product is produced when detector data is generated with the instrument in a spectrometer configuration. In these configurations several different science data frames can be generated

The different spectrometer science data frame types are:

| Frame Type | Number of Channels | DCU Frame ID (hex) | TM Packet APID (hex) | TM Packet SID (hex) | Subsystem | ArrayName |
| --- | --- | --- | --- | --- | --- | --- |
| Spectrometer Full Array | 72 | 01 | 4 | 0201 | “SPECTROMETER” | “SSW” “SLW” |
| SSW Array | 48 | 05 | 4 | 0105 | “SPECTROMETER” | “SSW” |
| SLW Array | 24 | 06 | 4 | 0106 | “SPECTROMETER” | “SLW” |
| Spectrometer Test Pattern | 72 | 0D | 4 | 030D | “SPECTROMETER” | “SSW” “SLW” |
| SSW Test Pattern | 48 | 0E | 4 | 030E | “SPECTROMETER” | “SSW” |
| SLW Test Pattern | 24 | 0F | 4 | 030F | “SPECTROMETER” | “SLW” |
| Transparent Data | TBD |  | 5 | FF00 | TBD | TBD |

Table 2-2

#### SDT Product Format

| product (type=”SDT”, description=” Spectrometer Detector Timeline”) |
| --- |
| metadata: |  |
| string | Creator | (description=”Creator”, quantity=””) |
| date | creationDate | (description=”Creation Date”, quantity=”UTC”) |
| string | instrument | (description=”Instrument”, quantity=””) |
| string | modelName | (description=”Instrument Model Name”, quantity=””) |
| date | StartDate | (description=”Start Date”, quantity=”UTC”) |
| date | EndDate | (description=”End Date”, quantity=”UTC”) |
| long | Obsid | (description=”Observation Identifier”, quantity=””) |
| long | Bbtype | (description=”Building Block type”, quantity=””) |
| long | Bbcount | (description=”Building Block execution counter”, quantity=””) |
| string | AOT | (description=”AOT Identifier”, quantity=””) |
| string | Subsystem | (description=”Instrument Subsystem”, quantity=””) |
| composite dataset | (description=”Array Timeline”) |
| Metadata: |  |
| string | arrayName | (description=”Detector Array Name”, quantity=””) |
| table dataset | (description=”Pixel Timeline”) |
| metadata: |  |
| string | pixelName | (description=”Pixel Name”, quantity=””) |
| string | pixelSource | (description=”Source packet”, quantity=””) |
| integer | pixelId | (description=”Pixel Identifier”, quantity=””) |
| integer-1d[] | FrameTime | (description=”Detector frame time”, quantity=”1/312500 s”) |
| double–1d [] | signal | signal (description=”Detector Signal”, quantity=”Volts”) |
| double–1d [] | error | (description=”Error on signal”, quantity=”Volts”) |
| integer-1d[] | mask | (description=”Data Mask”, quantity=””) |
| table dataset | (description=”Pixel Timeline”) |
| ……. |  |
| table dataset | (description=”Pixel Timeline”) |
| ……. |  |
| history |  |
| ….. |  |

#### SDT Product Contents

| Data Item | Description |
| --- | --- |
| Creator | Name of the module which created the product. This should indicate the version also. Is set by the creator task, e.g. to “EngineeringDataModule Version_n.m” |
| CreationDate | UTC of the date and time of creation of the product Is set by the creator task. |
| Instrument | Set to “SPIRE” Can be derived from the first two bits of OBSID. |
| ModelName | Name of the instrument model from which the data came e.g. “CQM”, “PFM1”, “FM”, “FS” Can be derived from the first four bits of the BBID. |
| StartDate | UTC of the date and time of the start of the Building Block to which this product relates. Can be derived from the contents of this product. |
| EndDate | UTC of the date and time of the end of the Building Block to which this product relates. Can be derived from the contents of this product. |
| Obsid | The OBSID parameter from the first Normal Housekeeping TM packet with a time belonging to this building block Since OBSID serves as the overall index of all observations I would assume that it is specified by the requestor of a product. |
| Bbtype | The BBID’s type parameter (14 bits) from the first Normal Housekeeping TM packet with a time belonging to this building block. |
| Bbcount | The BBID execution count parameter (16 bits) from the first Normal Housekeeping TM packet with a time belonging to this building block. |
| AOT | SOFn with n=1..4, depending on the operating mode used. SOF0 can be used when no template is used, e.g. in the case of a non-standard observation. (TBC) How could this be derived? |
| Subsystem | Name of the subsystem generating the data As defined in Table 2-2: “Spectrometer” Can be derived from the APID in the science telemetry. |
| ArrayName | Name of the detector array to which the data relates As defined in Table 2-2, either “SLW”, “SSW”, or “Full” Can be derived from the APID in the science reports. |
| pixelName | Unique Name for the pixel For example pixel C5 on the PLW array = “PLWC5” This name identifies the physical pixel from which the data has come irrespective of the type of data frame in which the data was transmitted Can be taken from the science reports. |
| pixelSource | Identifies the source packet from which the pixel data has been extracted. “SPECSW”, “SPECLW”, or “SPECF” Can be derived from the APID in the science reports. |
| pixelId | Identifies the channel in the source packet from which the data comes. For example pixel “SLWC5” may be found in packet “SPECLW” at location 021. Note: Channel numbers start from 001 Can be taken from the science reports. |
| FrameTime | The number of clock ticks since the last clock reset. The clock runs at a rate of 312500Hz. Pulses get counted by 32 bit counters. Integer is a signed 32 bit variable. We should check that the 32-bit signed format will convert properly into the unsigned format, i.e. negative values must turn into high positive clock counts. Can be taken from the science reports. |
| Signal | The signal from the detector which has been converted into Volts, taking into account biases and gains from the instrument electronics. Can be taken from the science reports and hk data on the electronics. |
| Error | Error in the measured signal value. |
| Mask | Bit mask indicating whether the pixel failed to meet certain criteria (bit = 1 indicates failure): Bit 0 (lsb) the master bit, is set whenever any of the other bits is set to allow easy detection of a bad sample Bit 1 when set indicates invalid data sample time (see Engineering Data Specification) Bit 2 when set indicates a possible ADC latch up error occurred for this sample (see Engineering Data Specification) Other bits are TBS |

### Spectrometer Detector Spectrum Product (SDS)

This product contains spectral data for a set of detector channels that contain data from detector pixels along with a wavenumber array. A single product will contain all spectra taken within one observation/building block, i.e. it will contain spectra from one or more scans or from an observation in step & integrate mode. Normally each building block in an observation will only generate one type of detector science data frame but in the event that more than one type is generated multiple data products will be produced.

The data has been processed from spectrometer science data frames (SDT and SMECT) or it can be extracted from the HCSS database.

This product is the output of the data processing step Fourier Transformation that operates on spectrometer data SDT and SMECT.

This product may be used by secondary software tools for scientific analysis. The different spectrometer science data frame types are:

| Frame Type | Number of Channels | DCU Frame ID (hex) | TM Packet APID (hex) | TM Packet SID (hex) | Subsystem | Array Name |
| --- | --- | --- | --- | --- | --- | --- |
| Spectrometer Full Array | 72 | 01 | 4 | 0201 | “SPECTROMETER” | “SSW” “SLW” |
| SSW Array | 48 | 05 | 4 | 0105 | “SPECTROMETER” | “SSW” |
| SLW Array | 24 | 06 | 4 | 0106 | “SPECTROMETER” | “SLW” |
| Spectrometer Test Pattern | 72 | 0D | 4 | 030D | “SPECTROMETER” | “SSW” “SLW” |
| SSW Test Pattern | 48 | 0E | 4 | 030E | “SPECTROMETER” | “SSW” |
| SLW Test Pattern | 24 | 0F | 4 | 030F | “SPECTROMETER” | “SLW” |
| Transparent Data | TBD |  | 5 | FF00 | TBD | TBD |

Table 2-3

#### SDS Product Format

| product (type=”SDS”, description=” Spectrometer Detector Spectrum”) |
| --- |
| Metadata: |  |
| String | Creator | (description=”Creator”, quantity=””) |
| Date | creationDate | (description=”Creation Date”, quantity=”UTC”) |
| String | instrument | (description=”Instrument”, quantity=””) |
| String | modelName | (description=”Instrument Model Name”, quantity=””) |
| date | StartDate | (description=”Start Date”, quantity=”UTC”) |
| date | EndDate | (description=”End Date”, quantity=”UTC”) |
| long | Obsid | (description=”Observation Identifier”, quantity=””) |
| long | Bbtype | (description=”Building Block type”, quantity=””) |
| long | Bbcount | (description=”Building Block execution counter”, quantity=””) |
| integer | numSpectra | (description=”Number of spectra”, quantity=””) |
| string | Subsystem | (description=”Instrument Subsystem”, quantity=””) |
| composite dataset | (description=”Detector Spectrum”) |
| metadata: |  |
| String | ArrayName | (description=”Detector Array Name”, quantity=””) |
| table dataset | (description=”Pixel Spectrum”) |
| metadata: |  |
| string | PixelName | (description=” Pixel Name”, quantity=””) |
| string | pixelSource | (description=”Source packet”, quantity=””) |
| integer | PixelId | (description=”Pixel Identifier”, quantity=””) |
| double | LowEdge | (description=”Lower edge of band”, quantity=”cm-1”) |
| double | HighEdge | (description=”Higher edge of band”, quantity=”cm-1”) |
| double | Resolution | (description=”Resolution element”, quantity=”cm-1”) |
| complex –1d [] | flux | (description=”Intensity”, quantity=”mJy”) |
| double –1d [] | frequency | (description=”Wavenumber Array”, quantity=”cm-1”) |
| complex –1d [] | weight | (description=”Error on intensity”, quantity=”mJy”) |
| long-1d [] | specId | (description=”Spectrum Identifier”, quantity=””) |
| integer-1d[] | flag | (description=”Data Mask”, quantity=””) |
| table dataset | (description=”Pixel Spectrum”) |
| ……. |  |
| table dataset | (description=”Pixel Spectrum”) |
| ……. |  |
| history |  |
| ….. | Must identify all measurements/processing steps that went into the calculation of the SDS and include the complete histories of these data sets. |

#### SDS Product Contents

| Data Item | Description |
| --- | --- |
| Creator | Name of the module which created the product. This should indicate the version also. Is set by the creator task, e.g. to “EngineeringDataModule Version_n.m” |
| CreationDate | UTC of the date and time of creation of the product Is set by the creator task. |
| Instrument | Set to “SPIRE” Can be derived from the first two bits of OBSID. |
| ModelName | Name of the instrument model from which the data came e.g. “CQM”, “PFM1”, “FM”, “FS” Can be derived from the first four bits of the BBID. |
| StartDate | UTC of the date and time of the start of the Building Block to which this product relates. Is set by the constructor of this product. |
| EndDate | UTC of the date and time of the end of the Building Block to which this product relates. Is set by the constructor of this product. |
| Obsid | The OBSID parameter from the first Normal Housekeeping TM packet with a time belonging to this building block Since OBSID serves as the overall index of all observations I would assume that it is specified by the requestor of a product. |
| Bbtype | The BBID’s type parameter (14 bits) from the first Normal Housekeeping TM packet with a time belonging to this building block. |
| Bbcount | The BBID execution count parameter (16 bits) from the first Normal Housekeeping TM packet with a time belonging to this building block. |
| numSpectra | Number of spectra in this product. Is equal to the number of scans. |
| Subsystem | Name of the subsystem generating the data As defined in Table 2-2: “Spectrometer” Can be derived from the APID in the science reports. |
| ArrayName | Name of the detector array to which the data relates As defined in Table 2-2: Either “SSW”, “SLW”, or “Full” |
| PixelName | Unique Name for the pixel For example pixel C5 on the PLW array = “PLWC5” This name identifies the physical pixel from which the data has come irrespective of the type of data frame in which the data was transmitted Can be taken from the science reports. |
| pixelSource | Identifies the source packet from which the pixel data has been extracted. “SPECSW”, “SPECLW”, or “SPECF” Can be derived from the APID in the science reports. |
| PixelID | Identifies the channel in the source packet from which the data comes. For example pixel “SLWC5” may be found in packet “SPECLW” at location 021. Note: Channel numbers start from 001 Can be taken from the science reports. |
| lowEdge | The smallest element in the wavenumber array. Can be taken from the product contents. |
| highEdge | The largest element in the wavenumber array. Can be taken from the product contents. |
| resolution | The resolution element Δσ of the wavenumber array. Can be taken from the product contents. |
| flux | The complex spectrum as a function of wavenumber |
| frequency | The uniformly sampled wavenumber array. It is still TBD how the three instruments on Herschel will deal with different x-axes such as wavelength, frequency, and wavenumber. |
| weight | Error in the spectrum as a weight which is proportional to 1 / (error ^2) |
| specId | Counter for the spectra in the dataset. |
| flag | Bit mask indicating whether the pixel failed to meet certain criteria (bit = 1 indicates failure): Bit 0 (lsb) the master bit, is set whenever any of the other bits is set to allow easy detection of a bad sample Bit 1 when set indicates invalid data sample time (see Engineering Data Specification) Bit 2 when set indicates a possible ADC latch up error occurred for this sample (see Engineering Data Specification) Other bits are TBS I assume this is the quality control bitmask and no other quality control feature will have to be handled. |

# Calibration Data Products

TBW