SPIRE CRYOGENIC THERMAL DESIGN REQUIREMENTS

| THERMAL ENGINEERING SECTION |
| --- |
| PREPARED BY: | A.S. GOIZEL | (RAL) | 22-06-04 |  |
| CHECKED BY: | B. SHAUGHNESSY | (RAL) | 29-06-04 |  |

| SPIRE PROJECT TEAM |
| --- |
| CHECKED BY: | J. DELDERFIELD | (RAL) | 29-06-04 |  |
|  | B.WINTER | (MSSL) |  |  |
|  | P. HARGRAVE | (Cardiff) |  |  |
|  | D. POULIQUEN | (LAM) |  |  |
|  | P. PARR-BURMAN | (ATC) |  |  |
|  | L.DUBAND | (CEA) |  |  |
|  | J. BOCK | (JPL) |  |  |
| APPROVED BY: | E. SAWYER | (RAL) | 23-06-04 |  |

“Page intentionally left blank”

CHANGE RECORD

| Issue | Date | Section | Change |
| --- | --- | --- | --- |
| Draft A | 19-06-04 | - | New Document formalising parts of RD9 |
| Draft B | 13-07-04 | Acronym List | Few missing acronyms added |
|  |  | 7/8/9/10 | Section titles changed to “Thermal Design Requirements” for consistency |
|  |  | 3.1 | Figure 3.1.1 corrected |
|  |  | 3.2.1 | Added footnote |
|  |  | 3.2.2 | Added note for DD2 |
|  |  | 4 | Section removed |
|  |  | 5.2 | Added explanatory note describing the difference between Herschel requirements and goals |
|  |  | 6.2.1 | Note reworded |
|  |  | 6.2.2 | “Maximum Power” in Table 6.2.2 replaced by “Maximum Energy” |
|  |  | 7.1 | Added figure 7.1.1. |
|  |  | 8.3 | Note added on mechanism power dissipation requirement. Housekeeping harness heat leak still TBC. |
|  |  | 9 | Added maximum allowable JFET cryo-harness heat leak, still TBC |
|  |  | 11 | Section removed as an identical section is already in the Thermal Configuration Control Document |

ACRONYM LIST

| BDA | Bolometer Detector Array |
| --- | --- |
| 2He | Helium 2 |
| 3He | Helium 3 |
| BSM | Beam Steering Mechanism |
| CQM | Cryogenic Qualification Model |
| DD | Design Driver |
| DTMM | Detailed Thermal Mathematical Model |
| ECR | Engineering Change Request |
| FPU | Focal Plane Unit |
| GMM | Geometrical Mathematical Model |
| HOB | Herschel Optical Bench |
| ITMM | Interface Thermal Mathematical Model |
| JFET | Junction Field Effect Transistor |
| L0 | Temperature Level 0 (~1.7K) |
| L1 | Temperature Level 1 (~4K) |
| L2 | Temperature Level 2 (~12K) |
| L3 | Temperature Level 3 (~15K) |
| PCAL | Photometer Calibration Source |
| PFM | Proto-Flight Model |
| PJFET | Photometer JFET |
| PTC | Photometer Thermal Control |
| RTMM | Reduced Thermal Mathematical Model |
| SCAL | Spectrometer Calibration Source |
| SJFET | Spectrometer JFET |
| SMEC | Spectrometer Mechanism |
| SOB | SPIRE Optical Bench |
| SPIRE | Spectral and Photometric Imaging Receiver |
| SST | Stainless-steel |
| STP | Screened Twisted Pairs |
| TBC | To Be Confirmed |
| TBD | To Be Defined |
| TMM | Thermal Mathematical Model |

CONTENT

1.	Scope	1

2.	Documentation	2

2.1	Applicable Documents	2

2.2	Reference Documents	2

3.	SPIRE Environment and Thermal Design Overview	3

3.1	Herschel Thermal Environment Overview	3

3.2	SPIRE Thermal Design Overview	5

3.2.1	SPIRE Requirements Overview	5

3.2.2	Cooler Recycling Performance Design Drivers	6

3.2.3	Cooler Operation Performance Design Drivers	7

4.	SPIRE Thermal Requirement Organisation	9

5.	SPIRE Interfaces with HERSCHEL Thermal Requirements	10

5.1	Overview	10

5.2	HERSCHEL Interfaces Thermal Requirements	11

6.	SPIRE 300-mK Level Thermal Design Requirements	12

6.1	Overview	12

6.2	BDA Detectors and PTC Control Hardware	13

6.2.1	High Level Thermal Requirements	13

6.2.2	Derived Thermal Requirements	14

6.3	300-mK Busbar System	15

6.3.1	High Level Thermal Requirement	15

6.3.2	Derived Thermal Requirement	15

6.4	3He Sorption Cooler	18

6.4.1	High Level Thermal Requirement	18

6.4.2	Derived Thermal Requirement	18

7.	SPIRE Level-0 Thermal Design Requirements	20

7.1	Overview	20

7.2	Level-0 Evaporator Strap	22

7.2.1	High Level Thermal Requirement	22

7.2.2	Derived Thermal Requirement	22

7.3	Level-0 Pump Strap	24

7.3.1	High Level Thermal Requirement	24

7.3.2	Derived Thermal Requirement	24

7.4	Level-0 Enclosures Strap Sub-system	26

7.4.1	High Level Thermal Requirement	26

7.4.2	Derived Thermal Requirement	26

8.	SPIRE Level-1 Thermal Design Requirements	28

8.1	Overview	28

8.2	High Level Thermal Requirement	29

8.3	Derived Thermal Requirement	29

9.	SPIRE Level-2 / Level-3 Thermal Design Requirements	31

9.1	Overview	31

9.2	High Level Thermal Requirement	31

9.3	Derived Thermal Requirement	31

LIST OF FIGURES

Figure 3.1-1 – SPIRE Thermal Design and Environment	4

Figure 3.2-1 - Typical profile of condensation efficiency versus evaporator temperature [AD1].	6

Figure 3.2-2 - Typical profile of cryo-pumping efficiency versus evaporator temperature [AD1].	6

Figure 3.2-3 – Cooler hold time versus overall recycling efficiency and evaporator gross load [AD1].	7

Figure 3.2-4 – Cooler Cold Tip Temperature versus External Load [AD2]	7

Figure 5.1-1 - HERSCHEL Cryostat / SPIRE Instrument Interfaces Definition	10

Figure 6.1-1 - SPIRE 300-mK Assembly Overview	12

Figure 6.3-1 – Applicable load for given sections of the 300-mK Busbar	17

Figure 7.1-1 – SPIRE and Herschel Level-0 Straps/Pods interface Description	20

Figure 7.1-2 – Level-0 Spectrometer and Photometer Enclosures Strap Assembly	21

Figure 7.4-1 – Level-0 Enclosure Temperature versus Cooler Hold Time [AD3]	26

LIST OF TABLES

Table 2.1-1 – Applicable Documents	2

Table 2.2-1 – Reference Documents	2

Table 3.1-1 – SPIRE Thermal Interfaces with the different Herschel cryostat temperature stages	3

Table 3.2-1 – Cooler Performances Design Drivers	5

Table 5.2-1 - HERSCHEL Interfaces Thermal Requirements [RD8]	11

Table 6.2-1 – BDA Detectors and PTC High Level Requirements [RD1]	13

Table 6.2-2 - PTC Derived Thermal Requirement	14

Table 6.3-1 – 300-mK Busbar High Level Thermal Requirements [RD2]	15

Table 6.3-2 – 300-mK Busbar Derived Thermal Requirement	15

Table 6.3-3 - BDA strap interface temperatures Analysis	15

Table 6.3-4 – Nominal Load for various 300-mK subsystems	16

Table 6.3-5 - Nominal Loads seen on the various section of the 300-mK Photometer Busbar	16

Table 6.3-6 - Nominal Loads seen on the various section of the 300-mK Spectrometer Busbar	16

Table 6.4-1 – Sorption Cooler High Level Requirements [RD3]	18

Table 6.4-2 – Sorption Cooler Derived Thermal Requirements	18

Table 6.4-3 - 300-mK Sub-system Parasitic Load Breakdown	18

Table 7.2-1 – Level-0 Evaporator Strap High-Level Requirement	22

Table 7.2-2 – Level-0 Evaporator Strap Derived Thermal Requirements	23

Table 7.3-1 - Level-0 Pump strap High-Level Requirements	24

Table 7.3-2 - Level-0 Pump Strap Derived Requirement	24

Table 7.4-1 - Level-0 Enclosures Straps High-Level Requirement	26

Table 7.4-2 - Level-0 Enclosures Straps Derived Requirements	27

Table 8.2-1 - Level-1 FPU High-Level Requirement	29

Table 8.3-1 - Level-1 FPU Derived Requirements	29

Table 8.3-2 – Level-1 Mechanisms Power Dissipation during Photometer Mode [AD7]	30

Table 8.3-3 – Level-1 Mechanisms Power Dissipation during Spectrometer Mode [AD7]	30

Table 9.2-1 – Photometer and Spectrometer JFET High-Level Requirements	31

Table 9.3-1 - Photometer and Spectrometer JFET Derived Requirements	31

# Scope

SPIRE is an infrared instrument aiming to operate detectors at a cryogenic temperature of 300mK for observation periods of at least 46 hours. This performance is possible thanks to a cryo-cooler mounted inside the instrument to which the detectors are connected. In order to achieve this performance however, stringent thermal requirements are applicable to the various sub-systems of the instrument in the common goal to minimise heat leak into and dissipated within the instrument.

This document summarises the high-level thermal requirements applicable to each instrument subsystem. Most of these requirements have been design drivers for lower sub-systems for which “derived requirements” have been defined. Moreover, as the cooler performance has been more fully understood and for others reasons, requirements have been evolved by “Engineering Change Request” (ECR) and are now all also summarised here as “derived requirements”.

Section 2 of this document provides the references for additional supporting material while section 3 gives a short description of the SPIRE instrument thermal environment and thermal.

Section 4 introduces the sections 5 to 9, where a detailed statement of the high-level and derived thermal requirements applicable to the SPIRE sub-systems is given for the various temperature stages.

The Flight Detailed Thermal Mathematical Model (DTMM) [AD5] uses values given herein to predict SPIRE thermal performances. A description of the predicted instrument flight performances and how they compare with the requirements defined in this document is given in the “Thermal Configuration Control Document” [RD9].

# Documentation

## Applicable Documents

| ID | Title | Number |
| --- | --- | --- |
| AD1 | SPIRE Cooler Performance Spreadsheet | Cooler_Performances.xls |
| AD2 | SPIRE CQM Cooler test results | HSO-SBT-TN-091 15-Dec-03 Issue: 1.1 |
| AD3 | SPIRE Thermal Report | To be compiled. |
| AD4 | Document / Engineering Change Request | HR-SP-RAL-ECR-054 13-May-03 |
| AD5 | SPIRE Flight Model - Esatan DTMM Logfile | SPIRE Models Log 21 DTMM.xls |
| AD6 | Draft Minute Notes from Visit to CEA-SBT | 19-Jun-03 |
| AD7 | SPIRE Instrument Timeline Definition v2 - reviewed.doc | 19-Nov-02 |

Table 2.1-1 – Applicable Documents

## Reference Documents

| ID | Title | Number |
| --- | --- | --- |
| RD1 | Herschel Spire Detector Subsystem Specification Document | SPIRE-JPL-PRJ-000456 07-Jan-03 Issue 3.2 |
| RD2 | Herschel/SPIRE 300-mK Strap System Requirements | SPIRE-RAL-PRJ-001323 04-Jun-02 Draft 0.1 |
| RD3 | SPIRE & PACS sorption Cooler Specifications | HSO-SBT-SP-001 18-Mar-04 Issue 3.6 |
| RD4 | Photometer Calibrator – Subsystem Specification Document | SPIRE-QMW-PRJ-001101 07-Sep-01 Issue 1.0 |
| RD5 | Spectrometer Calibrator – Subsystem Specification Document | SPIRE-QMW-PRJ-001105 07-Sep-01 Issue 1.0 |
| RD6 | SPIRE Beam Steering Mirror Subsystem Specification Document | SPIRE-ATC-PRJ-000460 11-Sep-03 Issue 3.7 |
| RD7 | Herschel Spire Spectrometer Mirror Mechanism Subsystem Specification Document | SPIRE-LAM-PRJ-000459 12-Oct-01 |
| RD8 | Instrument Interface Document Part B SPIRE Instrument | SPIRE-ESA-DOC-000275 01-Mar-04 Issue 3.2 |
| RD9 | SPIRE Thermal Configuration Control Document | SPIRE-RAL-PRJ-000560 16-Jul-04 Draft 12 |

Table 2.2-1 – Reference Documents

# SPIRE Environment and Thermal Design Overview

## Herschel Thermal Environment Overview

The SPIRE instrument will be launched onboard Herschel Space Observatory in 2007, along with the PACS and the HIFI instruments. SPIRE consists of five bolometer arrays, which will be cooled and controlled to an absolute temperature of 310-mK for nominal observation periods of 46 hours. To achieve such a low temperature, SPIRE will interface with four temperature stages of the Herschel cryostat nominally operating at 15K, 12K, 4K and 1.7K. The final 300-mK temperature stage is provided by a Helium 3 (3He) sorption cooler onboard SPIRE itself.

The SPIRE Focal Plane Unit (FPU) is mounted off the Herschel Optical Bench (HOB) at 12K on isolating supports to limit the parasitic loads into the instrument. Two JFET electronic boxes also mounted off the HOB are thermally coupled to the 15K stage of the Herschel cryostat to heat sink most of their internal power dissipation during operation. The JFET electronic boxes connect to SPIRE FPU through low conductance harnesses to reduce their heat leak into the instrument. The SPIRE FPU is thermally coupled to the 4K stage of the Herschel cryostat to heat sink most of the parasitic loads from the 12K stage as well as the additional heat dissipated by the various mechanisms mounted inside the FPU. The 300-mK detectors are bolted on internal enclosures. These enclosures are mounted off the SPIRE Optical Bench (SOB) on isolation supports and are thermally coupled to the 1.7K stage of the Herschel cryostat. The last 300-mK temperature stage is provided by a 3He sorption cooler mounted off the SOB, with its cold tip connected to each detector through an arrangement of thermal straps. This cooler operates a 48-hour cycle, which consists of 2-hour of recycling, during which the cooler 3He is being regenerated, followed by a nominal 46-hour operation period during which the detectors are cooler to an absolute temperature of 310mK. A thermal control has also been implemented on the 300-mK photometer strap to maintain the detector temperatures as stable as possible.

The table 3.1-1 below and figure 3.1-1 on next page, briefly describe how the different SPIRE subsystems interconnect with the various Hershel cryostat temperature stages.

| Temperature Stages | SPIRE Sub-systems | Herschel Thermal Interfaces |
| --- | --- | --- |
| Level-3 | ~ 15K | Photometer and Spectrometer JFET Electronic Boxes | Each JFET electronic box is coupled to the Herschel Level-3 ventline via a thermal strap. |
| Level-2 | ~ 12K | FPU | Mounted off the HOB on 3 isolating supports. |
|  |  | Photometer JFET | Mounted off the HOB on 5 isolating supports. |
|  |  | Spectrometer JFET | Mounted off the HOB on 4 isolating supports. |
| Level-1 | ~ 4K | SOB | Coupled to the Herschel Level-1 ventline via two thermal straps. |
| Level-0 | ~ 1.7K | Cooler Evaporator | Coupled to the Herschel Level-0 2He tank via a thermal strap. |
|  |  | Cooler Pump | Coupled to the Herschel Level-0 2He tank via a thermal strap. |
|  |  | L0 Spectrometer Enclosure | Coupled to the Herschel Level-0 2He tank via a thermal strap. |

Table 3.1-1 – SPIRE Thermal Interfaces with the different Herschel cryostat temperature stages

Figure 3.1-1 – SPIRE Thermal Design and Environment

## SPIRE Thermal Design Overview

### SPIRE Requirements Overview

To achieve its scientific goals, the SPIRE instrument must be able to run its bolometer arrays for a minimum period of 46 hours at a maximum absolute temperature of 310mK.

To achieve the above requirement, the instrument will be using a 6-litre 3He sorption cooler mounted inside the SPIRE FPU on the optical bench which, when operated in an optimised thermal environment, can provide a “cold tip” temperature as low as 265mK for operation periods exceeding 60 hours.

The cooler hold time and cold tip temperature are both highly dependent on the thermal environment in which the cooler is being operated and it is important to have a clear understanding of how the SPIRE thermal design can affect the cooler performances:

- The cooler hold time is dependent on the total amount of 3He gathered in the evaporator at the beginning of the “low temperature” cooler phase (when the cold tip is at ~300mK) as well as on the rate at which the 3He is subsequently being evaporated.

- The cooler cold tip temperature is dependent on the gross load seen by the evaporator during the “low temperature” phase. This gross load consists of the cooler own internal parasitic load as well as the external load from the 300-mK detector assembly.

The table 3.2.1 below provides an overview of the main design drivers for the SPIRE instrument thermal architecture.

| ID | Design Drivers | Description | Applicable |
| --- | --- | --- | --- |
| DD1 | Maximise the cooler condensation efficiency | Allow to optimise the amount of 3He available for the detector operation. | During recycling |
| DD2 | Maximise the cooler cryo-pumping efficiency | Allow to optimise the amount of 3He available for the detector operation. | During recycling |
| DD3 | Minimise the cooler total evaporator load | Allow the limit the rate at which the 3He is being evaporated following the recycling phase. | During operation |
|  |  | The lower the load on the evaporator, the cooler the cold tip temperature. | During operation |

Table 3.2-1 – Cooler Performances Design Drivers

The following paragraphs provide an overview of the cooler performances for each of the design drivers described in the above table.

### Cooler Recycling Performance Design Drivers

The overall cooler recycling efficiency is driven by:

- The condensation efficiency [DD1], which is dependent on the evaporator temperature at the end of the condensation phase (for a given pump temperature).

Figure 3.2-1 - Typical profile of condensation efficiency versus evaporator temperature [AD1].

- The cryo-pumping efficiency [DD2], which depends on the evaporator temperature at the end of the condensation phase. This takes into account the helium used to cooldown from recycling temperature to cold operation.

Figure 3.2-2 - Typical profile of cryo-pumping efficiency versus evaporator temperature [AD1].

### Cooler Operation Performance Design Drivers

During operation, the cooler hold time and cold tip temperature is driven by:

- Its evaporator’s gross load [DD3], which depends on cooler internal parasitic load as well as the external load from the 300-mK detector assembly.

Figure 3.2-3 – Cooler hold time versus overall recycling efficiency and evaporator gross load [AD1].

Figure 3.2-4 – Cooler Cold Tip Temperature versus External Load [AD2]

The figure 3.2.3 describes the cooler hold time performances for a given gross load on the evaporator as well as the overall recycling efficiency (the latest given in the graph as a function of the evaporator temperature at the end of the condensation period). A red line has been drawn to indicate the region in which the cooler should be operated in order to achieve the required 46-hour hold time.

The figure 3.2.4 describes recent test results measured by CEA [AD2] with the SPIRE CQM cooler. For this test, an external known load was applied to the evaporator cold tip and its temperature measured. It can be observed that the temperature of the cooler’s evaporator cold tip varies as a function of the external applied load. Note 1 and 2 below provide additional information about the interpretation of the results presented in figure 3.2.4.

Note 1: When no external load is applied, the evaporator only sees its internal parasitic load. The temperature of the cold tip can in that case, be used as an indication of how much parasitic the evaporator sees.

Note 2: Care must be taken when using these results to evaluate the SPIRE cooler performances. For these cases, a Level-0 temperature of ~1.6K and a level-1 temperature of ~2K were used, indicating a cooler internal parasitic load of ~8uW. In flight, the interface temperatures are more likely to be around 1.7K and 4K for the Level-0 and Level-1 respectively.

# SPIRE Thermal Requirement Organisation

In the following sections 6 to 10, a detailed statement of the thermal requirements applicable to the various SPIRE subsystems is given. All requirements are defined either as:

- A High-Level Thermal Requirement: requirements originally coming from a specification document.

- A Derived Thermal Requirement: new or updated high-level requirements necessary to ensure that the instrument will be performing as required. Those evolving requirements results from detailed sensitivity analyses or thermal testing performed on the instrument hardware and can be traced via thermal analysis or test reports.

The interface temperature and load requirements with the Herschel cryostat are described first as top-level requirements. Then all SPIRE thermal requirements are described subsequently, organised by temperature levels first, and then gathered in the subsystem group they apply to. An overview of the report architecture is given below:

- SPIRE Interface temperature and load requirements with the Herschel cryostat

- SPIRE 300-mK Level Thermal Requirements

  - BDA and PTC Subsystem

  - 300-mK strap assembly Subsystem

  - Sorption Cooler subsystem

- SPIRE Level-0 Thermal Requirements

  - Level-0 Evaporator Strap Subsystem

  - Level-0 Pump Strap Subsystem

  - Level-0 Enclosure Strap Subsystem

- SPIRE Level-1 Thermal Requirements

  - Mechanism Internal Power Dissipation

  - FPU feet

- SPIRE Level-2/3 Thermal Requirements

  - JFET Isolation Supports

  - JFET internal Power Dissipation

Figure 5 - SPIRE Thermal Requirement Organisation

# SPIRE Interfaces with HERSCHEL Thermal Requirements

## Overview

The picture 5.1.1 below provides a description of the thermal interface locations of SPIRE with the Herschel cryostat.

Figure 5.1-1 - HERSCHEL Cryostat / SPIRE Instrument Interfaces Definition

Stringent specifications are placed on the allowable heat loads at the various Herschel interfaces, for two reasons:

- To maximize the Herschel cryostat mission life,

- To guarantee SPIRE with the interface temperatures as described in Table 5.2.1 on next page.

## HERSCHEL Interfaces Thermal Requirements

| In-Orbit Thermal Requirements |
| --- |
| SPIRE FPU thermal IF | Maximum I/F Temperature at Max Heat Load | Cooler State |
|  | Requirements | Goals |  |
| Level 0 – Detector Box | 2 K @ 4 mW | 1.71K @ 1 mW | Operating |
| Level 0 – Cooler Pump | 2 K @ 2 mW | 2 K @ 2 mW | Operating |
|  | 10 K @ 500 mW peak | 10 K @ 500 mW | Recycling |
| Level 0 – Cooler Evaporator | 1.85 K @ 15 mW | 1.75 K @ 15 mW | Recycling |
| Level 1 | 5.5 K @ 15 mK | 3.7 K @ 13 mW | Operating |
| Level 2 | 12 K @ no load | 8 K @ no load | Operating |
| Level 3 – Photometer | 15 K @ 50 mW | 15 K @ 50 mW | Operating |
| Level 3 – Spectrometer | 15 K @ 25 mW | 15 K @ 25 mW | Operating |
| Instrument Shield | 16 K | 16 K | Operating |

Table 5.2-1 - HERSCHEL Interfaces Thermal Requirements [RD8]

In table 5.2.1, the “Requirements” column describes the agreed temperatures that the Herschel cryostat shall provide at the various SPIRE interfaces for the stated maximum heat loads.

Please note that although those requirements have been agreed by both parties, only the interface temperatures described in the “goals” section would allow SPIRE to meet its 46-hour hold time requirement. With interface temperatures as described in the “requirements” section, the estimated cooler hold time would only reach around 27 hours [AD3].

Therefore, in addition to those requirements, it has been agreed by both parties that Astrium should demonstrated by analysis that the Herschel cryostat will also be able to provide interface temperatures as those described in the “Goals” column.

# SPIRE 300-mK Level Thermal Design Requirements

## Overview

The 300mK Level of the SPIRE instrument consists of the following components:

- Five Bolometers Detector Arrays, also called BDAs, mounted off two Level-0 photometer and spectrometer enclosures at ~1.7K,

- Two high conductance copper strap assembly, also called 300-mK Busbar, which connect the cooler cold tip to each BDA thermal interface,

- The sorption cooler which provide a cold tip heat sink operating at ~290mK for ~46 hours.

Figure 6.1-1 - SPIRE 300-mK Assembly Overview

## BDA Detectors and PTC Control Hardware

### High Level Thermal Requirements

| Requirement | Description | Value | Comments |
| --- | --- | --- | --- |
| BDA-TEC-01 | The BDA shall accommodate a defined mechanical interface to the 2K structure. | - | - |
| BDA-TEC-02 | The BDA shall provide an attachment point and/or a thermal interconnect to a 300 mK thermal strap. | - | - |
| BDA-TEC-06 | Total power load on the 300 mK cooler from the BDAs (from Kevlar cords and Kapton harnesses). | Min performance <15 (W Design value < 8 (W | This assumes the focal plane mount is held at 1.7 K. () |
| BDA-TEC-07 | Power allocated for temperature control of the 3He stage (PTC) | Reqt < 2 (W | - |
| BDA-HCO-01 | Design values of detector performance requires a temperature at the point of contact to the BDA | Reqt < 290mK | - |
|  | Design value sensitivities assume 300 mK at the detector. | - | The BDA Internal temperature drop is < 10mK. |
| BDA-HCO-02 | Design values of detector performance require temperature stability at the point of thermal control (near the evaporator). | 10 µK/√Hz from 0.1-10Hz | This assumes that the BDA acts as a 100-s thermal low-pass filter. |
| BDA-HCO-03 | Maximum allowed thermal drift at the point of thermal control (near the evaporator) | < 1 mK/hr | This assumes that the BDA acts as a 100 s thermal low-pass filter. |

Table 6.2-1 – BDA Detectors and PTC High Level Requirements [RD1]

Note: The performance of the 3He cooler will be measured with the detectors during CQM-level testing.  If the thermal performances are not satisfactory, temperature control of the evaporator stage must be implemented on the PFM and FS instrument models [RD1]. The hardware to do this will be implemented on the Proto-Flight Model (PFM).

### Derived Thermal Requirements

Following a sensitivity analysis described in [AD3], a new goal has been set for the maximum allowable PTC power dissipation (in the form of an energy requirement) to ensure the cooler will achieve its 46-hour hold time.

| Requirement | Description | Value | Comments | Reference |
| --- | --- | --- | --- | --- |
| Reqt-SP-01 | Maximum Energy available for PTC and active control of BDAs temperature | Goal < 0.16J | Goal based on a maximum continuous power dissipation of 1uW for 46 hrs | AD3 |

Table 6.2-2 - PTC Derived Thermal Requirement

Note 1: The definition of maximum power dissipation requirement for the PTC has been expressed in terms of an energy requirement, as it appears to be more appropriate. This means that larger peaks of power dissipation could be used if necessary for a shorter period of time as long as the total energy going into the cooler evaporator doesn’t exceed 0.16 J per 46 hr operation period.

Note 2: The PTC is only used in photometer mode.

## 300-mK Busbar System

### High Level Thermal Requirement

| Requirement | Description | Value | Comments |
| --- | --- | --- | --- |
| STRAP-Req-01 | Maximum Temperature drop along 300mK Busbar System – from the cooler cold tip to each BDA Thermal Interface. | 20mK | No temperature boundaries specified |
| STRAP-Req-02 | Maximum heat leak through 300mK system Kevlar supports | 2 (W | No temperature boundaries specified |
| STRAP-Req-03 | Maximum heat leak through PTC Harness | Reqt <0.2 (W | No temperature boundaries specified |

Table 6.3-1 – 300-mK Busbar High Level Thermal Requirements [RD2]

### Derived Thermal Requirement

| Requirement | Description | Value | Comments | Reference |
| --- | --- | --- | --- | --- |
| Reqt-SP-02 | Maximum Temperature at each of the Busbar BDA thermal interfaces | Reqt < 290mK | - | BDA-HCO-01 |
| Reqt-SP-03 | New maximum Temperature drop along 300-mK Busbar – from cooler cold tip to each BDA thermal interface | Reqt < 10mK Goal < 5mK | With cooler tip at 280-285mK for a gross load of 30(W. | Reqt-Cooler |

Table 6.3-2 – 300-mK Busbar Derived Thermal Requirement

It can be seen that if the high-level requirement for the Busbar maximum temperature drop were to be used, it would not allow the design to meet the derived requirement for the BDA interface temperatures (see table 6.3.3). Instead, a new derived requirement “Reqt-SP-02” had to be set for the 300-mK Busbar system, in order to achieve the required BDA strap interface temperatures.

| Cooler cold Tip temperature | BDA strap interface temperatures |
| --- | --- |
|  | With 20-mK Busbar Requirement | BDA Requirement |
| Cooler tip at 280-285mK (For gross load of 30uW) | 300-305mK | Reqt < 290 mK |

Table 6.3-3 - BDA strap interface temperatures Analysis

The 300-mK Busbar shall be designed to meet the most demanding requirement, which is to achieve a maximum of 5-mK temperature drop from the cooler cold tip to each BDA thermal interface, and this, for the maximum load expected to flow along the Busbar. However, the different sections of the Busbar see different amounts of parasitic load.

In the following tables and illustration, a description of the heat load applicable to each section of the 300-mK Busbar is given and should be used as reference when designing each section to meet the 5-mK maximum temperature drop required.

These numbers have been predicted based on the maximum parasitic load allocated for all five detectors and assume that the Kevlar parasitic load is identical for all detectors.

| Subsystem Components | Maximum Load ((W) |
| --- | --- |
| Load / BDA Kevlar Support | 1.5 |
| Load / BDA Kapton Harness | 0.5 |
| PLW 2 Kapton Harness | 1 |
| PMW 4 Kapton Harness | 2 |
| PSW 6 Kapton Harness | 3 |
| SLW 1 Kapton Harness | 0.5 |
| SSW 2 Kapton Harness | 1 |
| PTC Harness | 0.2 |
| PTC Power Dissipation | 2 |
| Load / Busbar Kevlar Supports | 0.5 |

Table 6.3-4 – Nominal Load for various 300-mK subsystems

| Busbar Section | Description | PLW | Busbar Supports | PMW | PSW | Feedthru Support | PTC Harness | PTC Heater | Total Load ((W) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| P1 | Strap from cooler cold tip to photometer Feedthru | x | x | x | x | x | x | x | x | 14.2 |
| P2 | Photometer Feedthru | x | x | x | x | x | x |  |  | 12 |
| PC1 | PSW Compliant Link |  |  |  | x |  |  |  | 4.5 |
| P3 | Busbar Section 1 | x | x | x | x |  |  |  |  | 7 |
| PC2 | PMW Compliant Link |  |  | x |  |  |  |  | 3.5 |
| P4 | Busbar Section 2 | x | x | x |  |  |  |  |  | 3.5 |
| P5 | Busbar Section 2 | x |  |  |  |  |  |  | 2.5 |
| PC3 | PLW Compliant Link | x |  |  |  |  |  |  | 2.5 |

Table 6.3-5 - Nominal Loads seen on the various section of the 300-mK Photometer Busbar

| Busbar Section | Description | SLW | SSW | Feedthru Support | Total Load ((W) |
| --- | --- | --- | --- | --- | --- |
| S1 | Strap from cooler cold tip to spectrometer Feedthru | x | x | x | 5 |
| S2 | Spectrometer Feedthru | x | x | x | 5 |
| SC1 | SSW Compliant Link |  | x |  | 2.5 |
| SC2 | SLW Compliant Link | x |  |  | 2 |

Table 6.3-6 - Nominal Loads seen on the various section of the 300-mK Spectrometer Busbar

Figure 6.3-1 – Applicable load for given sections of the 300-mK Busbar

## 3He Sorption Cooler

### High Level Thermal Requirement

| Requirement | Description | Value | Comments |
| --- | --- | --- | --- |
| Reqt-Cooler | Nominal Cooler operation conditions | 1.7K Heat Sink 4K Environment | - |
|  | Net heat lift at 290mK | 10 (W | In nominal conditions |
|  | Minimum total amount of cold joules produced by cooler | 5 J | - |
|  | Maximum time allocated for recycling | 2 hrs | - |
|  | Maximum Energy dissipated by cycle due to cooler operation | 860 J | - |
|  | Additional contribution from the 1.7-4K environment | < 0.6 mW | - |

Table 6.4-1 – Sorption Cooler High Level Requirements [RD3]

Note: Based on a 46-hour hold time, 5 J of cooler energy would represent an average nominal load on the cooler evaporator of ~ 30uW.

### Derived Thermal Requirement

| Requirement | Description | Value | Comments | Reference |
| --- | --- | --- | --- | --- |
| Reqt-SP-04 | Maximum cooler internal parasitic Load Use 0.29mm Kevlar cords at evaporator. | 12 (W | As an objective | AD4 |
| Reqt-SP-05 | Maximum Load at Herschel L0 Evaporator Pod during recycling | 15mW | To ensure a 1.75 K pod interface Temperature | RD8 |

Table 6.4-2 – Sorption Cooler Derived Thermal Requirements

As described before, the maximum allowable load on the cooler evaporator during operation must not exceed 30uW to achieve the required cooler hold time. As the evaporator gross load is driven by the parasitic loads from the cooler and from the 300-mK Strap Assembly, it is important to define what is the maximum load allocation for each of these subsystems.

Table 6.4.3 below describes the maximum load for which the 300-mK sub-system is being designed.

| 300-mK Sub-System Parasitic Load Breakdown | References |
| --- | --- |
| BDAs [x5] | 15 (W | BDA-TEC-06 |
| PTC Power Dissipation | 1 (W | Reqt-SP-01 |
| 300-mK Busbar | 2 (W | STRAP-Req-02 |
| PTC Harness | < 0.2 (W | STRAP-Req-03 |
| Total | 18.2 (W | - |

Table 6.4-3 - 300-mK Sub-system Parasitic Load Breakdown

From the table above, it can be deduced that the maximum parasitic load internal to the cooler shall not exceed ~12 (W. This statement has been summarised as the derived requirement “Reqt-SP-04” in table 6.4.2 on previous page.

Note: Action has already been taken in the past to reduce the cooler internal parasitic loads by reducing the Kevlar cords diameter from 0.5mm to 0.29mm.

A final derived requirement for the cooler is coming the high-level requirements agreed between the Herschel cryostat and the SPIRE instrument, to have a maximum load of 15mW flowing on the evaporator strap during the cooler recycling, in order to obtain the required 1.75K interface temperature at the evaporator pod. This high-level requirement has been repeated here as a cooler derived requirement “Reqt-SP-05” as it mainly depends on the cooler internal construction.

# SPIRE Level-0 Thermal Design Requirements

## Overview

The SPIRE Level-0 operates nominally at 1.7K and consists of the following sub-systems:

- A set of two thermal straps connecting the cooler pump and evaporator heat switches interfaces to dedicated pods of the Herschel cryostat:

  - The Level-0 Evaporator Strap,

  - The Level-0 Pump Strap.

Figure 7.1-1 – SPIRE and Herschel Level-0 Straps/Pods interface Description

- The photometer and spectrometer enclosures,

  - Both enclosures are mounted on the SOB on low conductance supports,

  - A low conductance F-harness connects the FPU to each L0 enclosures,

  - An interbox strap thermally couples the photometer enclosure to the spectrometer enclosure (internal to the SPIRE FPU),

  - An external strap thermally couples the spectrometer enclosure to a dedicated Level-0 pod of the Herschel cryostat.

Figure 7.1-2 – Level-0 Spectrometer and Photometer Enclosures Strap Assembly

The following sections describe in more details the thermal requirements applicable to the various Level-0 sub-systems.

## Level-0 Evaporator Strap

### High Level Thermal Requirement

| Requirement | Description | Value | Comments |
| --- | --- | --- | --- |
| RD8 | Maximum Load at Herschel L0 Evaporator Pod during recycling | 15mW | For a 1.75 K pod interface Temperature |

Table 7.2-1 – Level-0 Evaporator Strap High-Level Requirement

The only main high-level requirement is coming from the instrument interface specification document RD8. Although this requirement is applicable to the Level-0 evaporator strap itself, the cooler internal construction will be the main driver for this load.

This evaporator strap however is driving the cooler recycling performances, as the evaporator temperature at the end of the condensation phase is directly dependent on how well this strap performs. It has been advised by CEA that the overall conductance of the thermal link connecting the evaporator heat switch interface to the Level-0 Helium heat sink should be no less than 0.1 W/K during recycling.

In reality, this link includes the following components (please see figure 7.1.1 for corresponding details):

- Section 1: SPIRE Level-0 evaporator strap interface with the cooler evaporator heat switch,

- Section 2: SPIRE Level-0 evaporator strap,

- Section 3: The Level-0 strap interfaces (two of them) with the Herschel Level-0 pod,

- Section 4: The Evaporator Level-0 pods (one nominal and one open pod),

- Section 5: The Evaporator Level-0 pod interfaces (two of them) with the 2He Herschel cryostat.

Note: According to the requirement described above, it can be concluded that the calculated Herschel cryostat pod overall conductance (which includes the sections 3, 4 and 5) will be ~ 0.3 W/K .

### Derived Thermal Requirement

According to Figure 3.2.3, it can be seen that to achieve a 46-hour hold time with a nominal evaporator gross load of 30 uW (or 5J over 46 hours), the evaporator temperature at the end of the condensation phase during the cooler recycling must be less than 2K. This statement has been summarised as the derived requirement “Reqt-SP-06” in table 7.2.2.

The following thermal conditions must be taken into account when designing the Level-0 evaporator strap:

- A 1.75K interface temperature shall be provided at the Herschel evaporator pod, assuming a maximum heat load of 15mW is flowing along the Level-0 evaporator strap [RD8],

- A 0.15K internal temperature drop has been assumed to take place inside the cooler (from the evaporator heat switch to the evaporator wall [AD6]).

In order to achieve 2K at the evaporator, the Level-0 Evaporator Strap shall be sized so that the maximum temperature drop during recycling along the strap shall be no more than 0.1 K for 15 mW (“Reqt-SP-07”).

| Requirement | Description | Value | Comments | Reference |
| --- | --- | --- | --- | --- |
| Reqt-SP-06 | Maximum Evaporator Temperature at end of condensation phase | 2K | During recycling | Figure 3.2.3 |
| Reqt-SP-07 | Maximum Evaporator Temperature drop from Herschel Interface to cooler Interface | 0.1K for 15mW Or 0.15 W/K at 1.7K | During recycling Assuming a 0.15K drop internal to the cooler | RD8 [Goals] |

Table 7.2-2 – Level-0 Evaporator Strap Derived Thermal Requirements

Note 1: The 0.15W/K stated conductance for the L0 evaporator strap:

- Must include the interface at the cooler heat switch (section 1),

- Does not include the interface at the Herschel Pod (section 3).

Note 2: A Herschel pod overall conductance of 0.3 W/K in series with the Level-0 evaporator strap overall conductance of 0.15 W/K provide a thermal link of 0.1W/K, as suggested by CEA.

No specific requirement regarding the maximum load has been defined to date on the evaporator strap during nominal instrument operation. However, the following points should be kept in mind:

- The cooler internal parasitic loads introduced via the evaporator heat switch and the shunt strap are dependent on the temperature at the evaporator heat switch – the lower this temperature, the lower the parasitic.

- To keep the temperature at the Herschel Evaporator Pod interface as close as possible to 1.7K during operation, the load on the Level 0 evaporator strap must be kept to a minimum during operation.

## Level-0 Pump Strap

### High Level Thermal Requirement

| Requirement | Description | Value | Comments |
| --- | --- | --- | --- |
| RD8 | Maximum Load at Herschel L0 Pump Pod during operation | 2mW | For a pod interface Temperature of 2K |
|  | Maximum Load at Herschel L0 Pump Pod during recycling | 500mW | For a pod interface Temperature of 10K |

Table 7.3-1 - Level-0 Pump strap High-Level Requirements

The only main high-level requirements are coming from the instrument interface specification document RD8.

It has been advised by CEA that the overall conductance of the thermal link connecting the pump heat switch interface to the Level-0 Helium heat sink should be around 0.05 W/K during recycling.

In reality, this link includes the following components (please see figure 7.1.1 for corresponding details):

- Section 1: SPIRE Level-0 pump strap interface with the cooler pump heat switch,

- Section 2: SPIRE Level-0 pump strap,

- Section 3: The Level-0 strap interface with the Herschel Level-0 pod,

- Section 4: The pump Level-0 pod,

- Section 5: The pump Level-0 pod interface with the 2He Herschel cryostat.

Note: According to the requirement described above for recycling, it can be concluded that the Herschel cryostat pod overall conductance (which includes the sections 3, 4 and 5) will be ~ 0.06 W/K .

### Derived Thermal Requirement

| Requirement | Description | Value | Comments | Reference |
| --- | --- | --- | --- | --- |
| Reqt-SP-08 | Minimum Level 0 Pump Strap Conductance | 0.15 W/K | At 1.7K. | RD8 |

Table 7.3-2 - Level-0 Pump Strap Derived Requirement

To achieve the 0.05 W/K conductance suggested by CEA, the Level 0 Pump Strap Conductance should be no less than 0.15 W/K as defined by the derived requirement “Reqt-SP-08”.

Note 1: Please note that the 0.15 W/K conductance stated for the L0 pump strap:

- Must include the interface at the cooler heat switch (section 1),

- Does not include the interface at the Herschel Pod (section 3).

Note 2: A Herschel pod overall conductance of 0.06 W/K in series with the Level-0 pump strap overall conductance of 0.15 W/K provide a thermal link of 0.043 W/K, close enough to the 0.05 W/K suggested by CEA.

Although the temperature of the pump heat switch interface doesn’t affect the cooler parasitic or hold time directly, it is important to maintain the load along the Level-0 strap within the 2mW requirement as to maximise the Herschel cryostat mission lifetime.

The load observed on the L0 Pump strap consists of:

- Cooler heat of adsorption which ranges within 48 to 50 x evaporator gross load according SPIRE Cooler CQM test results,

- Pump Heat Switch Heater Power dissipation,

- Heat leak from the pump Heat Switch titanium supports off the cooler Level-1 enclosure,

- Heat leak from the Level-0 Pump strap standoffs off the FPU.

## Level-0 Enclosures Strap Sub-system

### High Level Thermal Requirement

| Requirement | Description | Value | Comments |
| --- | --- | --- | --- |
| RD8 [Goal] | Maximum Load at Herschel L0 Enclosures Pod | 1 mW | For a pod interface Temperature of 1.71 K |

Table 7.4-1 - Level-0 Enclosures Straps High-Level Requirement

The photometer and the spectrometer Level-0 enclosures provide a conductive and radiative interface to the five detector BDAs at approximately 1.7K. The temperature of these two enclosures is of up most importance as it drives the amount of parasitic load going into the 300mK system (via the five BDAs and the Busbar assembly), and therefore participates to the gross load of the cooler. This effectively has a direct impact on the cooler hold time and the evaporator cold tip temperature.

### Derived Thermal Requirement

There is a need for these two enclosures to run at temperatures as close to 1.7K as possible to minimise the parasitic loads into the 300-mK system. To do so, the photometer and spectrometer enclosures are connected to the Herschel Cryostat Level-0 pod interface (running at 1.71K) via an arrangement of straps designed to minimise the temperature drop from the to the enclosures.

The figure 7.4.1 resulting from a sensitivity analysis presented in AD3 has shown that in order to achieve a 46-hour hold time, the Level-0 enclosures temperatures should not exceed 1.74K. This has been defined as a derived requirement “Reqt-SP-09” applicable to both Level-0 enclosures, as described in table 7.4.2.

Figure 7.4-1 – Level-0 Enclosure Temperature versus Cooler Hold Time [AD3]

Although the spectrometer enclosure is directly connected to the Herschel Level-0 pod via the external strap, the photometer enclosure must first be connected to the spectrometer enclosure through the interbox strap. In order to achieve 1.74K at the photometer enclosure with an Herschel interface temperature of 1.71K, both the internal interbox and external Level-0 enclosure straps shall be sized to provide a maximum temperature drop during operation of no more than 0.03 K for a maximum load of 1 mW as defined in the derived requirement “Reqt-SP-10”.

Note: Please note that thermal gradient within the Level-0 enclosures should also be kept to a minimum value.

| Requirement | Description | Value | Comments | Reference |
| --- | --- | --- | --- | --- |
| Reqt-SP-09 | Maximum L0 Enclosures Temperature | 1.74 K | During operation | AD3 |
| Reqt-SP-10 | Maximum Temperature drop along detector enclosure thermal path | 0.03 K | For a maximum load of 1mW during operation | AD3 / RD8 |
| Reqt-SP-11 | Minimum Level 0 Enclosure Strap Conductance | 0.15 W/K | During operation at 1.7K | AD4 |
| Reqt-SP-12 | Minimum Internal interbox Strap Conductance | 0.05 W/K | During operation at 1.7K | AD4 |
| Reqt-SP-13 | Gradient within the photometer Enclosure | < 0.01K | As objective, during operation at 1.7K. | - |
| Reqt-SP-14 | Maximum Level-0 spectrometer A-Frames conductance | 1.6x10 -5 W/K | Between 1.73K and 5K Per A-frame [3] | AD4 |
| Reqt-SP-15 | Maximum Level-0 photometer A-Frames conductance | 3.7x10 –5 W/K | Between 1.8K and 5K Per A-frame [2] | AD4 |
| Reqt-SP-16 | Maximum Level-0 photometer cone conductance | 7.2x10 –5 W/K | Between 1.85K and 5.1K Per Cone [1] | AD4 |

Table 7.4-2 - Level-0 Enclosures Straps Derived Requirements

As described in the high-level requirement, the maximum load on the Level-0 Enclosures strap shall not exceed 1mW. The load observed on the Level-0 Enclosures strap consists of:

- Parasitic Load from the Level-0 Enclosures Strap Standoffs off the FPU,

- Parasitic Load from the Level-0 Enclosure supports off the SOB,

- Parasitic Load from the F-Harness connecting the Level-0 enclosures to the FPU.

Note 1: Please note that the 0.15 W/K conductance stated for the L0 Enclosure strap:

- Must include the interface at the spectrometer enclosure interface,

- Does not include the interface at the Herschel Pod.

Note 2: The previous Level-0 enclosure support design used to be major contribution in heat leaks into the Level-0 stage. Derived requirements have therefore been defined to limit the maximum allowable conductance of each support and thus minimise the heat leaks into the Level-0 stage.

# SPIRE Level-1 Thermal Design Requirements

## Overview

The SPIRE FPU Level-1 structure consists of an Aluminium Alloy 6082 Spire Optical Bench (SOB) with the spectrometer and photometer assemblies mounted on opposite sides.  Aluminium covers surround each assembly and are hard bolted to the SOB to form the Focal Plane Unit (FPU). The SOB forms the mechanical interface for the mirrors, mechanisms and the sorption cooler frame. These components are hard bolted to the SOB. The SOB is then connected to the Level-1 ventline of the Herschel cryostat to be cooled down at temperatures around 4-5K.

The key thermal design features of the SPIRE Level-1 stage are as follows:

- Reduced parasitic load from the Level-2 HOB by using three isolating supports for the FPU,

- Low mechanisms internal power dissipation,

- Low conductance F-harnesses connect the FPU to both JFET enclosures,

- Low conductance housekeeping harnesses connect the FPU to the Level-2 HOB,

- The SOB is thermally coupled to the Herschel Level-1 Ventline (at approximately 4K) via two straps provided by the Hershel cryostat.

## High Level Thermal Requirement

| Requirement | Description | Value | Comments |
| --- | --- | --- | --- |
| RD8 | Maximum Load at Herschel L1 Ventline | 13 mW | Goal during operation, for a Level-1 Ventline interface Temperature of 3.7 K |
| IRD-BSMP-R12 [RD6] | Maximum average power dissipation of the BSM Cryogenic Mechanism (BSMm) and the BSM Support Structure (BSMs) | < 4mW | In any operating mode. |
| SMECm_Tm8 [RD7] | SMECm Maximum Power consumption | <= 2.4 mW | Required mean power consumption over the mission. |
| IRD-CALP-R12 [RD4] | Photometer Calibrator maximum power dissipation in the FPU when operating continuously at nominal radiant output | 4 mW (requirement) 2 mW (goal) | PCAL will be in the ON condition for only about 5 seconds every hour. Allowing for the maximum dissipation of 4 mW, during this period, the time-averaged dissipation of PCAL will be less than 6 W. |
| TBC | Maximum Housekeeping Harness Load from Herschel Cryostat | TBC | - |

Table 8.2-1 - Level-1 FPU High-Level Requirement

The temperature of the Level-1 FPU is the one of the main driver for the instrument overall performances as most of the load into the Level-0 and 300-mK (for the cooler evaporator) and therefore their performances are highly dependent on the SOB/FPU temperature.

The main requirement applicable to the SPIRE Level-1 is therefore to have the SOB/FPU running as cold as possible and a nominal temperature interface of 3.7K as been agreed as a goal with the Herschel cryostat as described in table 8.2.1.

Note: The larger the load going into the Herschel Level-1 ventline, the warmer the cryostat Level-1 interface will run. The total instrument heat load to the Level-1 ventline must therefore be kept at a minimum as below 13mW.

## Derived Thermal Requirement

| Requirement | Description | Value | Comments | Reference |
| --- | --- | --- | --- | --- |
| Reqt-SP-17 | Maximum Level-1 A-Frame Supports Conductance | 1.14 x 10 –4 W/K | Between 10.7K and 5.2K Per A-frame [2] | AD4 |
| Reqt-SP-18 | Maximum Level-1 Cone Supports Conductance | 2.12 x 10 –4 W/K | Between 10.7K and 5.2K Per Cone [1] | AD4 |
| Reqt-SP-19 | SCAL Maximum Power Dissipation | 2 mW | Mean Power | AD4 |

Table 8.3-1 - Level-1 FPU Derived Requirements

The previous Level-1 FPU support design used to be one of the major contributions in heat leaks into the Level-1 Ventline. Derived requirements have therefore been defined to limit the maximum allowable conductance of each support and thus minimise the heat leaks into the Level-1 Ventline stage.

Note: The implementation of these new support designs also greatly reduces the sensitivity of the Level-1 FPU load to the HOB temperature, as the FPU is now more isolated.

Similarly, every effort is currently undertaken to limit the SCAL internal power dissipation to 2 mW as described by the derived requirement “Reqt-SP-19”.

Table 8.3.2 and 8.3.3 on next page describes the average internal power dissipation currently allocated to each SPIRE mechanisms during the Spectrometer and Photometer operation modes.  Please note that only the mean power dissipations are used when assessing the SPIRE thermal performances in steady state and that the highest power dissipations are used as the worse case for the BSM and SMEC mechanisms. Although those values are indicative only, every effort should be made to keep the actual mechanism performances close to those values.

| SPIRE in Photometer Mode |
| --- |
| PCAL | Peak power of 4mW used for only 30 sec every hour = 0.833 % of SPIRE time in photometer mode Mean power = 33 (W [4mW x 0.833%] |
| BSM Shopping Mode | Mean power 1.9 mW [(3mW + 0.8mW) /2] |
| BSM Scanning Mode | Peak Power 3 mW |

Table 8.3-2 – Level-1 Mechanisms Power Dissipation during Photometer Mode [AD7]

| SPIRE in Spectrometer Mode |
| --- |
| PCAL | Peak power of 4mW used for 30 sec every hour = 0.833 % of SPIRE time in spectrometer mode Mean power = 33 (W [4mW x 0.833%] |
| SCAL | Mean Power 2 mW |
| BSM | Q nominal mean power = 0.2 mW |
| SMECm (R=1000) | Q peak = 7.4 mW Q mean = 3.2 mW |
| SMECm (R=10) | Q peak = 0.9 mW Q mean = 0.9 mW |

Table 8.3-3 – Level-1 Mechanisms Power Dissipation during Spectrometer Mode [AD7]

# SPIRE Level-2 / Level-3 Thermal Design Requirements

## Overview

The Level-2 consists of the Herschel Optical Bench (HOB) on which the SPIRE FPU and two JFETs enclosures are mounted. The temperature of the HOB has an important impact on the SPIRE Level-1 parasitic loads and every effort must be made to keep the HOB temperature as low as possible.

To do so, the Level-3 ventline has been implemented as a part of the cryostat design and is thermally coupled to both JFET enclosures to heat sink most of the load they will dissipate during operation. This allows lower HOB temperature to be achieved.

## High Level Thermal Requirement

| Requirement | Description | Value | Comments |
| --- | --- | --- | --- |
| JFET-FUN-01 | The JFET module will mount to the Herschel optical bench, dissipating power at the Level-2 stage of the cryostat. | - | - |
| JFET-TEC-05 | Maximum allowed total JFET power dissipation for photometer mode (all three arrays operating). | 42 mW | - |
|  | Design value for JFET module dissipation per 48-channel module. | 7 mW | - |
|  | Thermal dissipation of fully functional CQM JFET units may be as large as 11 mW per module to meet minimum noise performance specification. | - | - |
| RD8 | Maximum Photometer Load into the L3 ventline | 50mW | For a 15K interface temperature |
|  | Maximum Spectrometer Load into the L3 ventline | 25mW | For a 15K interface temperature |
| TBC | Maximum Cryo-Harness Load from Herschel Cryostat | TBC | - |

Table 9.2-1 – Photometer and Spectrometer JFET High-Level Requirements

## Derived Thermal Requirement

| Requirement | Description | Value | Comments | Reference |
| --- | --- | --- | --- | --- |
| Reqt-SP-20 | Maximum JFET Support Overall Conductance | 0.002 W/K | Per JFET unit | AD4 |

Table 9.3-1 - Photometer and Spectrometer JFET Derived Requirements

To obtain optimal performances with the Level-3 ventline implementation, both JFET enclosures had now to be isolated as much as possible from the HOB. A derived requirement has therefore been defined for the new support design in the forms of a maximum allowable conductance per JFET enclosure as described in table 9.3.1 with the requirement “Reqt-SP-20”.

# Footnotes

This fits in with Herschel ground commanding periods.

The “6-litre” description defines the amount of 3He it contains as being at least 6 litres at STP/NTP (tbc).

Assuming a 2He tank temperature of 1.7 K.

Minimum value not compliant at the moment but the design value is [RD1].

Based on a Herschel 2He temperature of 1.7K.

Based on a Herschel 2He temperature of 1.7K.

# Text boxes

SPIRE SOB

S1

P4

Herschel Evaporator Pod Interfaces

P5

FPU

P3

P2

P1

Herschel Evaporator Pod Interfaces

Herschel Optical Bench

SPIRE FPU Enclosure

S2

~15K

Pipe

He Vent

Level 3

Herschel

PC3

SC2

SC1

SPIRE Level 3 - JFET Enclosures

FPU Structure

PC2

SPIRE Level 1

~12K

Pipe

He Vent

Level 2

Herschel

~12K

Optical Bench/Shield

Herschel Level 2

~4 K

Pipe

He Vent

Level 1

Herschel

Detectors

SPIRE 300-mK

KEYS:

Harness		Radiation		SPIRE Components

Thermal		Isolation		Herschel Cryostat

Straps		Supports		Components

Electrical Isolation			Gas Gap Heat Switch

Cooler Pump

SPIRE Level 0

Cooler Evaporator

SPIRE 290-mK

Detector Enclosures

PC1

SPIRE Level 0

~1.7K

He Tank

Level 0

Herschel

Herschel Instrument Shield

Shunt

ShuntShunt

Hershel Enclosure

Pod Interface at ~1.7K

External Level-0

Enclosure Strap

Internal Interbox Strap

Spectrometer

Enclosure

Photometer

Enclosure

Herschel Detector Box Pod Interfaces

Level-1 Interface to SOB

Herschel Thermal Interface with SPIRE

Herschel Harness Interface with SPIRE

Level-3 Interface to Photometer JFET

Level-3 Interface to Spectrometer JFET

Level-0 Interfaces to SPIRE Level-0 thermal straps

Harness Interface to Spectrometer JFET

Harness Interface to Photometer JFET

Harness Interface to SPIRE FPU

# Cooler

Section 1 - Evaporator L0 strap interface with Heat Switch

Section 1 - Pump L0 strap interface with Heat Switch

Section 2 - Evaporator L0 strap

Section 2 - Pump L0 strap

Section 3 - Evaporator L0 strap interface with Herschel Pods

Section 3 - Pump L0 strap interface with Herschel Pods

Section 4 - Evaporator L0 Herschel Pods

Section 4 - Pump L0 Herschel Pod

Section 5 – Herschel Evaporator Pod Interfaces with Herschel Helium Tank

Section 5 – Herschel Pump Pod Interface with Herschel Helium Tank