# Introduction

This document gives a summary of the CQM functional test results from the first campaign conducted during Jan/Feb 2004. These tests also included the warm functional tests before and after the test cryostat was pumped down and cooled to 4K, as well as the cold functional tests.

The full functionality of the Herschel Common Science System (HCSS) was not used in these tests for the following reasons:

- All the test scripts had already been written in TCL and tested with the warm electronics and the FPU simulator.

- The Common Uplink System (CUS) functionality needed to run all the tests from the HCSS was not available at the time.

- The HCSS CUS command language scripts were not written at this stage.

- Full associations between the telecommands sent and the telemetry generated could not be made with the available version of the HCSS

The entire emphasis was therefore placed on performing the tests and monitoring the progress in real time using SCOS 2000. It was ensured that all the housekeeping and science telemetry, as well as the telecommand information, was safely ingested inside the HCSS database for subsequent retrieval, playback and analysis with QLA.

## Scope

This report judges the success or failure of a functional test by checking that

- the commands were correctly received and executed by the instrument subsystem

- no error or exception reports were generated

- the appropriate telemetry parameters changed in an expected manner

No detailed analyses of the test data has been performed at this stage.

## Reference Documents

RD01    Functional Test Specifications, SPIRE-RAL-DOC-001652, Issue 1.0 (draft 2), 5th Dec 2003

RD02    SPIRE Data ICD (SPIRE-RAL-PRJ-001078), Issue 1.1 (Draft 3), 30th Aug 2003

RD03    SPIRE CQM Thermal Balance Test Specification, SPIRE-RAL-DOC-00????, Issue D1, 2nd Dec 2003.

RD04     SPIRE EGSE-ILT Startup Procedures, SPIRE-RAL-DOC-001630, Issue 0.7, 24th June 2003

RD05     DRCU Switch On Procedure, SPIRE-RAL-NOT-001899, Issue D1, 10th Dec 2003

## Functional Test Configuration

### SPIRE EGSE Setup

- CDMS Simulator version 2.4

- SCOS 2000 2.3e Patch Level 3 + TOPE - running on a Linux SuSE 7.3 system

- OBS v1.3G

- HCSS v0.1.4 ((Build #263 plus patches) – includes the EGSE router and gateway

- SPIRE CQM MIB: MIBDATA_SPIRE_0_6 (stored in the HCSS on 04-11-2003)

- Test Facility Control System Server v1.0

- Test Fourier Transform Spectrometer Server (TFTS v1.0)

- QLA (2.0 Release Candidate 2) – running on a Linux SuSE 7.3 system

- EGSE Test Tool PacketDisplay to display TC and TM packet contents

# pre-test preparations

Dry runs with the functional test scripts revealed an OBS problem which had not been seen earlier (SPIRE SPR-0288). The OBS was found to reject telecommands in a random manner. The result of this serious problem was that some of the pre-defined TCL test scripts could not be run automatically, except in the simplest test cases, without the risk of leaving the instrument in an unpredictable state. As the TOPE debugger environment was not available with SCOS 2.3e P3, it was decided to conduct the tests using the SCOS 2000 Command Manual Stack. One negative consequence of this approach was that these tests lasted longer but, on the positive side, they were fairly easy to control and coordinate.

## Assumptions

Before the start of functional tests the SPIRE EGSE was set up and configured using RD03 and RD04. For each set of tests the following minimum steps were also executed beforehand if they were not already activated.

| Step # | Description | Status Parameter Values Before/After | Test Step Status/ Success/Fail |
| --- | --- | --- | --- |
| 1 | Start TM ingestion | TM ingestion process running | Success |
| 2 | Run Procedure PROC_OPER_DPU_ON | OBS running | Success |
| 3 | Run Procedure PROC_OPER_DRCU_ON | DCU and SCU on. Parameter MONSTAT=0/5 | Success |

# short warm functional tests – inside cryostat (20/01/04)

| Test Name | Description | Key Parameter Values Before/After or ranges | Test Status/ Success/Fail |
| --- | --- | --- | --- |
| FUNC-SCU-03 | SCU DC Thermometry Check | SCUTEMPSTAT=0/0xFFFF SCU temperature channel values changed: SCU Temperature Raw Values PUMPHTRTEMP 1203 / 32768 PUMPHSTEMP 1522 / 32768 EVAPHSTEMP 1620 / 32768 SHUNTTEMP 60484 / 32768 SOBTEMP 139 / 45451 SL0TEMP 1664 / 32768 PL0TEMP 62021 / 32768 OPTTEMP 65400 / 32768 BAFTEMP 65012 / 32768 BSMIFTEMP 65007 / 32768 SCAL2TEMP 65170 / 32768 SCAL4TEMP 64718 / 32768 SCALTEMP 65229 / 32768 SMECIFTEMP 0 / 63217 SMECTEMP 65437 / 58402 BSMTEMP 7 / 32768 |  |
| FUNC-SCU-06 | SCU AC Thermometry Check | SUBKSTAT=0/1 The SUBKTEMP channel value remained unchanged at 31911-31924. | Success |
| FUNC-SCU-07 | Cooler Heaters Check | SPHSV = 0 / 12713 EVHSV = 2 / 12715 SPHTRV = 0 / 14391 | Success |
| FUNC-SCU-04 | PCAL Check | PCALV = 0 / 11017 PCALCURR = 0 / 9061 | Success |
| FUNC-SCU-05 | SCAL Check | SCAL2V = 1 / 12521 SCAL4V = / 12510 SCAL2CURR = 1 / 14076 SCAL4CURR = 0 / 14071 | Success |
| FUNC-MCU-01 | MCU Boot Procedure | MCUIFSTAT = 0 / 0x0038 MCUIFCTRL = 0 / 7 MCUSSDEL = 0 / 3 MCUMACTEMP, MCUSMECTEMP and MCUBSMTEMP parameter values changed. MCUP15V = 0 / 0x9A8E MCUM15V = 0 / 0x6574 MCUP13V = 0 / 0x94C4 MCUM13V = 0 / 0x7FFF MCUP5V = 0 / 0x96FE | Partial Success. Sometimes the Over Current Limiter was triggered preventing the MCU from switching on. NCR_MCU_123 already raised by CEA. To be fixed for MCU QM1. |
| Test Name | Description | Key Parameter Values Before/After or ranges | Test Status/ Success/Fail |
| FUNC-DCU-11: Photometer LW array | Put the Photometer into Standby mode and generate PLW science data. Commanded values: PHOTSAMPFREQ = 0xc PHOTBIASMODE = 0xFF PHOTBIASFREQ = 0x62 PLWBIAS = 3.92V PLWPHASE = 0xA0 PMLWJFERSTAT = 0x30 PLWJFET1V = 0x80 PLWJFET2V = 0x80 | PLW science data frames successfully generated. QLA displayed the PLW science data. | Success |
| PROC-OPER-PDO: | Procedure to switch off Photometer detectors and JFETs |  | Success |
| PROC-OPER-LIO: | Procedure to switch Photometer LIAs off |  | Success |

# warm functional tests – after pump down (23/01/04)

It was ensured that the vacuum chamber pressure was at ~ 10-5 mbar before the commencement of these tests.

| Test Name | Description | Key Parameter Values Before/After or ranges | Test Status/ Success/Fail |
| --- | --- | --- | --- |
| FUNC-SCU-03 | SCU DC Thermometry Check | SCUTEMPSTAT=0/0xFFFF SCU temperature channel values changed: SCU Temperature Raw Values PUMPHTRTEMP 1201 / 32768 PUMPHSTEMP 1524 / 32768 EVAPHSTEMP 1650 / 32768 SHUNTTEMP 60509 / 32768 SOBTEMP 142 / 45526 SL0TEMP 1602 / 32768 PL0TEMP 62105 / 32768 OPTTEMP 65403 / 32768 BAFTEMP 65025 / 32768 BSMIFTEMP 65037 / 32768 SCAL2TEMP 65173 / 32768 SCAL4TEMP 64718 / 32768 SCALTEMP 65230 / 32768 SMECIFTEMP 65534 / 63215 SMECTEMP 65439 / 58411 BSMTEMP 17 / 32768 | Success |
| FUNC-SCU-06 | SCU AC Thermometry Check | SUBKSTAT=0/1 The SUBKTEMP channel value remained unchanged at 31908-31924. | Success |
| FUNC-SCU-07 | Cooler Heaters Check | SPHSV = 65534 / 12713 EVHSV = 65534 / 12715 SPHTRV = 1 / 14391 | Success |
| FUNC-SCU-04 | PCAL Check | PCALV = 1 / 11010 PCALCURR = 0 / 9061 | Success |
| FUNC-SCU-05 | SCAL Check | SCAL2V = 1 / 12518 SCAL4V = / 12512 SCAL2CURR = 1 / 14074 SCAL4CURR = 0 / 14072 | Success |
| FUNC-MCU-01 | MCU Boot Procedure | MCUIFSTAT = 0 / 0x0038 MCUIFCTRL = 0 / 7 MCUSSDEL = 0 / 3 MCUMACTEMP, MCUSMECTEMP and MCUBSMTEMP parameter values changed. MCUP15V = 0 / 0x9A8E MCUM15V = 0 / 0x6574 MCUP13V = 0 / 0x94C4 MCUM13V = 0 / 0x7FFF MCUP5V = 0 / 0x96FE | Partial Success. Sometimes the Over Current Limiter was triggered preventing the MCU from switching on. NCR_MCU_123 already raised by CEA. To be fixed for MCU QM1. |
| Test Name | Description | Key Parameter Values Before/After or ranges | Test Status/ Success/Fail |
| FUNC-DCU-11: Photometer LW array | Put the Photometer into Standby mode and generate PLW science data. Commanded values: PHOTSAMPFREQ = 0xc PHOTBIASMODE = 0xFF PHOTBIASFREQ = 0x62 PLWBIAS = 3.92V PLWPHASE = 0xA0 PMLWJFERSTAT = 0x30 PLWJFET1V = 0x80 PLWJFET2V = 0x80 | PLW science data frames successfully generated. QLA displayed the PLW science data. | Success |
| PROC-OPER-PDO: | Procedure to switch off Photometer detectors and JFETs |  | Success |
| PROC-OPER-LIO: | Procedure to switch Photometer LIAs off |  | Success |

# functional tests with T ~ 90 K (27/01/04)

| Test Name | Description | Key Parameter Values Before/After or ranges | Test Status/ Success/Fail |
| --- | --- | --- | --- |
| FUNC-SCU-03 | SCU DC Thermometry Check | SCUTEMPSTAT=0/0xFFFF SCU temperature channel values changed to: SCU Temperature Raw Values PUMPHTRTEMP 37729 PUMPHSTEMP 32768 EVAPHSTEMP 32768 SHUNTTEMP 32768 SOBTEMP 57509 SL0TEMP 32768 PL0TEMP 32768 OPTTEMP 42013 BAFTEMP 40602 BSMIFTEMP 32768 SCAL2TEMP 53155 SCAL4TEMP 52849 SCALTEMP 32768 SMECIFTEMP 63801 SMECTEMP 60233 BSMTEMP 32768 | Success |
| FUNC-SCU-06 | SCU AC Thermometry Check | SUBKSTAT=0/1 The SUBKTEMP channel value remained essentially unchanged at 31891-31917. | Success |
| FUNC-SCU-07 | Cooler Heaters Check | SPHSV = 0 / 12727 EVHSV = 65534 / 12736 SPHTRV = 1 / 14393 | Success |
| FUNC-SCU-04 | PCAL Check | PCALV = 2 / 11050 PCALCURR = 65535 / 9062 | Success |
| FUNC-SCU-05 | SCAL Check | SCAL2V = 0 / 12547 SCAL4V = 1 / 12541 SCAL2CURR = 1 / 14075 SCAL4CURR = 1 / 14072 | Success |
| FUNC-MCU-01 | MCU Boot Procedure | MCUIFSTAT = 0 / 0x0038 MCUIFCTRL = 0 / 7 MCUSSDEL = 0 / 3 MCUMACTEMP, MCUSMECTEMP and MCUBSMTEMP parameter values changed. MCUP15V = 0 / 0x9A8E MCUM15V = 0 / 0x6574 MCUP13V = 0 / 0x94C4 MCUM13V = 0 / 0x7FFF MCUP5V = 0 / 0x96FE | Partial Success. Sometimes the Over Current Limiter was triggered preventing the MCU from switching on. NCR_MCU_123 already raised by CEA. To be fixed for MCU QM1. |
| Test Name | Description | Key Parameter Values Before/After or ranges | Test Status/ Success/Fail |
| FUNC-DCU-11: Photometer LW array | Put the Photometer into Standby mode and generate PLW science data. Commanded values: PHOTSAMPFREQ = 0xc PHOTBIASMODE = 0xFF PHOTBIASFREQ = 0x62 PLWBIAS = 3.92V PLWPHASE = 0xA0 PMLWJFETSTAT = 0x30 PLWJFET1V = 0x80 PLWJFET2V = 0x80 | PLW science data frames successfully generated. QLA displayed the PLW science data. | Success |
| PROC-OPER-PDO: | Procedure to switch off Photometer detectors and JFETs |  | Success |
| PROC-OPER-LIO: | Procedure to switch Photometer LIAs off |  | Success |

# cold functional tests with the fpu < 10k (29/01/04)

| Test Name /OBSID | Description | Key Parameter Values Before/After or ranges | Test Status/ Success/Fail |
| --- | --- | --- | --- |
| FUNC-SCU-03 / | SCU DC Thermometry Check | Not performed as the DC Thermometry was already on. SCU Temperature Raw Values PUMPHTRTEMP 62286-62310 PUMPHSTEMP 61707-61728 EVAPHSTEMP 61331-61355 SHUNTTEMP 59220-59448 SOBTEMP 64065-64071 SL0TEMP 55451-55545 PL0TEMP 52139-52181 OPTTEMP 60602-60609 BAFTEMP 59842-59848 BSMIFTEMP 55978-55986 SCAL2TEMP 64967-64974 SCAL4TEMP 64958-64964 SCALTEMP 59507-59515 SMECIFTEMP 64953-64958 SMECTEMP 63801-63808 BSMTEMP 47249-47259 | Success |
| FUNC-SCU-06 / 0x203 | SCU AC Thermometry Check | SUBKSTAT=0/1 SUBKTEMP = 14 / 2.2 K (Raw: 31921 / 31708) | Success |
| Test Name /OBSID | Description | Key Parameter Values Before/After or ranges | Test Status/ Success/Fail |
| FUNC-SCU-02 / 0x204 | SCU Science Data Check | 31 SCU science frames generated | Success |
| FUNC-SCU-07 / 0x205 | Cooler Heaters Check | SPHSV = 65534 / 12775 EVHSV = 65533 / 12779 SPHTRV = 65535 / 14391 SUBKTEMP = 2.0 / 2.2 K (Raw value: 31693 / 31693) | Success |
| FUNC-SCU-08 / 0x206 | SCU Test Pattern Test | One SCU science packet with 10 SCU science frames. | Success |
| FUNC-SCU-04 / 0x207 | PCAL Check | PCALV = 2 / 11100 PCALCURR = 65535 / 9062 | Success |
| FUNC-PCAL-01 / 0x208 | PCAL Characterisation Test | PCALV and PCALCURR values changed in response to the commands sent. QLA displayed the PCAL data. | Success |
| FUNC-SCU-05 / 0x209 | SCAL Check | SCAL2V = 1 / 12553 SCAL4V = 65461 / 69 SCAL2CURR = 2 / 14075 SCAL4CURR =- 65534 / 4058 | Partial Success (SCAL4 voltages and currents do not change in accordance to commanded values). NCR HR-SP-RAL-NCR-64 raised. |
| FUNC-SCAL-01 / 0x20A | SCAL Characterisation Test | SCAL2V and SCAL2CURR values changed in response to the commands sent. Voltage drop across SCAL 4% (SCAL4V) was very small and not in proportion to the applied current (SCAL4CURR) QLA displayed the SCAL data. | Partial Success (SCAL4 voltages and currents do not change in accordance to commanded values). Same NCR as above. |
| FUNC-MCU-01 / 0x20B | MCU Boot Procedure | MCUIFSTAT = 0 / 0x0038 MCUIFCTRL = 0 / 7 MCUSSDEL = 0 / 3 MCUMACTEMP, MCUSMECTEMP and MCUBSMTEMP parameter values changed. MCUP15V = 0 / 0x9A8E MCUM15V = 0 / 0x6574 MCUP13V = 0 / 0x94C4 MCUM13V = 0 / 0x7FFF MCUP5V = 0 / 0x96FE | Fail Sometimes the Over Current Limiter was triggered preventing the MCU from switching on. NCR_MCU_123 already raised by CEA. To be fixed for MCU QM1. |
| FUNC-MCU-02 / 0x20C | MCU Science Packet Generation Check | MCUFRAMECNT parameter increased as expected | Success |
| Test Name /OBSID | Description | Key Parameter Values Before/After or ranges | Test Status/ Success/Fail |
| FUNC-MCU-03 / 0x20D | MCU Science Data Check |  | Success |
| FUNC-MCU-04 / 0x20E | MCU Test Pattern Test | 10 seconds of MCU Test Pattern data generated | Success |
| PROC-OPER-MCO / | MCU Switch Off Procedure |  | Success |
| FUNC-DCU-11: Photometer LW array / 0x213 | Put the Photometer into Standby mode and generate PLW science data. Commanded values: PHOTSAMPFREQ = 0xc PHOTBIASMODE = 0xFF PHOTBIASFREQ = 0x62 PLWBIAS = 3.92V PLWPHASE = 0xA0 PMLWJFETSTAT = 0x30 PLWJFET1V = 0x80 PLWJFET2V = 0x80 | PLW science data frames successfully generated. QLA displayed the PLW science data. | Success |
| PROC-OPER-PDO: | Procedure to switch off Photometer detectors and JFETs |  | Success |
| PROC-OPER-LIO: | Procedure to switch Photometer LIAs off |  | Success |

# warm functional tests – following fpu warmup (13/02/04)

| Test Name /OBSID | Description | Key Parameter Values Before/After or ranges | Test Status/ Success/Fail |
| --- | --- | --- | --- |
| FUNC-SCU-01 / 0x237 | SCU Science Packet Generation Check | 31 frames received as expected | Success |
| FUNC-SCU-03 / | SCU DC Thermometry Check | Not performed as the DC Thermometry was already on. | Success |
| FUNC-SCU-06 / 0x238 | SCU AC Thermometry Check | Not Applicable as FPU warm. Performed regardless | Success |
| FUNC-SCU-02 / | SCU Science Data Check | Not necessary as QLA test only |  |
| FUNC-SCU-07 / 0x239 | Cooler Heaters Check | Not necessary as FPU warm | Success |
| FUNC-SCU-08 / 0x23A | SCU Test Pattern Test | One SCU science packet with 10 SCU science frames. | Success |
| FUNC-SCU-04 / 0x23B | PCAL Check |  | Success |
| FUNC-PCAL-01 / 0x23D | PCAL Characterisation Test | PCALV and PCALCURR values changed in response to the commands sent | Success |
| FUNC-SCU-05 / 0x23E | SCAL Check |  | Success |
| FUNC-SCAL-01 / 0x23F | SCAL Characterisation Test | SCAL2V and SCAL2CURR values changed in response to the commands sent. SCAL4V and SCAL4CURR values changed in response to the commands sent. | Success |
| FUNC-MCU-01 / | MCU Boot Procedure | MCU already on |  |
| FUNC-MCU-02 / | MCU Science Packet Generation Check | Not performed as it is the same as the next test |  |
| FUNC-MCU-03 / 0x240 | MCU Science Data Check |  | Success |
| FUNC-MCU-04 / 0x241 | MCU Test Pattern Test | 10 seconds of MCU Test Pattern data generated. | Success |
| Test Name /OBSID | Description | Key Parameter Values Before/After or ranges | Test Status/ Success/Fail |
| PROC-OPER-MCO / | MCU Switch Off Procedure |  | Success |
| FUNC-DCU-01 / 0x242 | DCU Science Packet Generation Check |  | Success |
| FUNC-DCU-02 / 0x244 | DCU Science Data Check |  | Success |
| FUNC-DCU-03 / 0x245?? | DCU Test Pattern Test |  | Success |
| PROC-OPER-LIO: | Procedure to switch Photometer LIAs off |  | Success |
| PROC-OPER-THO: | Procedure to switch off both SCU DC and AC Thermometry | SCUTEMPSTAT = 0xFFFF / 0 SUBKSTAT = 1 / 0 | Success |
| PROC-OPER-DRO: | Procedure to switch off DRCU | MONSTAT = 5 / 0 | Success |
| PROC-OPER-DPO: | Procedure to switch off DPU |  | Success |

# conclusions

The warm and cold functional tests conducted during the first CQM test campaign were largely successful, with the exception of cold functional test of the SCAL 4% source. The experience gained by the AIV team during the first CQM test campaign will be invaluable for the forthcoming second CQM test campaign.