This note contains a report from the SPIRE CQM Verification Matrix covering those requirements tested by the CQM Performance tests; the CQM Warm Functional test and the CQM Cold Functional tests as carried out during the CQM1 test campaign.

This is a draft for information a further update will complete the matrix and include those requirements addressed by the Vibration and thermal tests

| VERIFIED BY PERFORMANCE TEST |
| --- |
| Requirement Name | Description | Procedure(s) In SPIRE-RAL-NOT-1850 | Test Report Section | NCRs | Status/comment |
| IRD-VER-R03 | The CQM verification testing shall demonstrate that the following conditions are met or are likely to be met on the PFM: Correct operation of all FPU sub-systems at cryogenic temperatures for all instrument operation modes for both prime and redundant systems. The instrument cold FPU and JFET box thermal dissipation is within requirements for all instrument operation modes. The warm electronics thermal dissipation at room temperature is within requirements. Correct operation of all on-board software. The instrument straylight environment is within requirements The instrument optics performance is within requirements The performance of the instrument meets the scientific requirements expected for the CQM for all instrument observing modes Development and test of all functional test sequences required for Integrated Systems Testing (IST) at satellite level. The correct functioning of the instrument for all observing modes and calibration sequences. Development and test of all in-flight functional and performance test sequences | All |  |  | Only photometer fitted to CQM – no spectrometer or BSM tests JFET supplied is not flight performance wrt dissipation DPU o.k. DRCU not flight build OBS testing as part of development Tested for photometer Tested for photometer Tested for photometer without BSM All functional tests carried out see functional test report No mode tests for CQM1 Testing carried out as part of OBS and procedure development |
| IRD-PHOT-R01 | Nominal passband | Spectral Response |  |  | CQM1 test inconclusive – to be repeated. Facility level test also required |
| IRD-PHOT-R02 | Field of View | Pixel Centre Pupil Test |  |  | CQM1 test inconclusive – to be repeated. Facility level test also required |
| IRD-PHOT-R03 | Beam FWHM (Arcsec) | PSF Test |  |  | Tested |
| IRD-PHOT-R04 | Point source sensitivity | Optical Efficiency |  |  | Tested |
| IRD-PHOT-R05 | Mapping sensitivity for one FOV | Optical Efficiency Pixel Centre |  |  | Tested |
| IRD-PHOT-R10 | Field distortion must be <10% across the FOV | Pixel Centre |  |  | Tested |
| IRD-PHOT-R11 | Electrical crosstalk should be <1% (goal 0.5%) between nearest-neighbour pixels and <0.1 % (gaol 0.05%) between all other pixels in the same array. | Optical Cross Talk Test |  |  | CQM1 test inconclusive – to be repeated. |
| IRD-PHOT-R12 | NEP variation should be < 20% across each array. | Optical Efficiency |  |  | CQM PLW array does not meet requirement. Instrument throughput tested. |
| IRD-PHOT-R16 | The three arrays need to be co-aligned to within 1 arcsecond. | Pixel Centre |  |  | No test really possible. |
| IRD-PHOT-R18 | SPIRE Photometric measurements shall be linear to 5% over a dynamic range of 4000 for astronomical signals | Linearity Test |  |  |  |
| IRD-STRC-R01 | Alignment of the instrument w.r.t. the FIRST optical axis | Pupil Test |  |  | CQM1 test inconclusive – to be repeated. Facility level test also required |
| IRD-STRC-R04 | Optics and associated sub-system alignment | Pupil Test |  |  | CQM1 test inconclusive – to be repeated. Facility level test also required |
| IRD-STRC-R08 | Attenuation of radiation from cryostat environment | Dark Noise Loadcurve |  |  | Tested |
| IRD-STRP-R02 | Optics and filters alignment | Optical Cross Talk Test PSF Test Pupil Test |  |  | Tested except Pupil Test where CQM1 test inconclusive – to be repeated. Facility level test also required |
| IRD-STRP-R03 | Array module alignment | Pixel Centre |  |  | Tested |
| IRD-STRP-R06 | Attenuation of radiation from common structure environment | Loadcurve Laser Straylight Test Pupil Test |  |  | Tested except Pupil Test where CQM1 test inconclusive – to be repeated. Facility level test also required |
| IRD-STRS-R06 | Attenuation of radiation from 4-K environment | Loadcurve |  |  | Tested |
| IRD-FPHR-R01 | Detector harness capacitance | Loadcurve Harness Test |  |  | Tested |
| IRD-FPHR-R02 | Detector harness mechanical support | Microphonics Test |  |  | Tested |
| IRD-OPTP-R00 | Compatibility with Herschel telescope | Focus Test |  |  | Tested |
| IRD-OPTP-R02 | Variation in focal ratio | PSF Test |  |  | Tested on one pixel only – to be repeated |
| IRD-OPTP-R03 | Distortion | Pixel Centre |  |  | Tested |
| IRD-OPTP-R04 | Anamorphism | PSF Test |  |  | Tested |
| IRD-OPTP-R05 | Throughput | Optical Efficiency Spectral Response |  |  | CQM1 test inconclusive – to be repeated. Facility level test also required |
| IRD-OPTP-R06 | Image quality | PSF Test |  |  | Tested |
| IRD-OPTP-R07 | Out of band radiation | Spectral Response Out of Band Test |  |  | Not tested |
| IRD-OPTP-R08 | In-band straylight | Loadcurve |  |  | Tested |
| IRD-DETP-R01 | Detective Quantum Efficiency at 2 Hz at nominal incident power levels | Noise Tests Optical Efficiency Frequency Response Test |  |  | Tested |
| IRD-DETP-R02 | Time constant | Frequency Response Test |  |  | Tested |
| IRD-DETP-R03 | Uniformity | Optical Efficiency |  |  | CQM PLW array does not meet requirement. |
| IRD-DETP-R05 | Electrical crosstalk for near neighbour pixels. | Optical Cross Talk Test |  |  | CQM1 test inconclusive – to be repeated. |
| IRD-DETP-R06 | Electrical crosstalk any pair of pixels | Optical Cross Talk Test |  |  | CQM1 test inconclusive – to be repeated. |
| IRD-DETP-R08 | Spectral response | Spectral Response |  |  | CQM1 test inconclusive – to be repeated. Facility level test also required |
| IRD-DETP-R09 | Microphonic susceptibility | Microphonics Test |  |  | Tested |
| IRD-DETP-R10 | EMI susceptibility | Noise Tests |  |  | Tested as much as possible QM1 electronics not flight quality. Further tests to be carried out during CQM2 |
| IRD-CALP-R01 | Nominal operating output | PCAL Level Response |  |  | Tested |
| IRD-CALP-R02 | Operating range | PCAL Level Response |  |  | Tested |
| IRD-CALP-R03 | Equivalent obscuration of aperture through BSM mirror |  |  |  | By analysis? |
| IRD-CALP-R04 | Speed of response | PCAL Frequency Response |  |  | CQM PCAL does not meet flight requirement. |
| IRD-CALP-R05 | Repeatability | PCAL Level Response |  |  | ? |
| IRD-FTB-R01 | Amplifier noise | Noise Tests |  |  | Tested |
| IRD-FTB-R02 | RF rejection | Noise Tests |  |  | Tested |
| IRD-FTB-R06 | Operating temperature range | Noise Tests |  |  | Tested |
| IRD-RFM-R04 | Operating temperature range | Noise Tests |  |  | Tested |
| IRD-WE-R08 | Photometer detector readout | ? |  |  | ? |
| VRD-06 | Optical design | Optical Tests |  |  | Tested |
| VRD-07 | Optical interface to FIRST system | Optical Tests |  |  | Tested |
| VRD-08 | Straylight | Straylight Test |  |  | Tested |
| VRD-09 | Instrument optical performance | Optical Tests |  |  | Tested |
| VRD-11 | Sub-system optical interfaces | PSF Tests Pupil Scan Test Pixel Centre |  |  | Tested for photometer LW channel only |
| VRD-12 | Thermal performance | Loadcurve |  |  | CQM1 build standard non-flight – to be repeated. |
| VRD-15 | Micro-vibration environment | Microphonics Test |  |  | Partly tested – to be repeated with higher fidelity test |
| VRD-17 | Harness mechanical frequency response and routing | Microphonics Test |  |  | Partly tested – to be repeated with higher fidelity test |
| VRD-18 | Detector performance versus environment | Noise Tests |  |  | Tested |
| VRD-19 | JFET Amplifier performance versus environment | Noise Tests |  |  | Tested |
| VRD-20 | Detector Harness performance | Noise Tests |  |  | Tested |
| VRD-22 | End-to-end system performance | Noise Tests Optical Efficiency |  |  | Tested |
| VRD-24 | Electrical grounding | Noise Tests |  |  | Tested |
| VRD-25 | Faraday cage integrity and performance | Noise Tests |  |  | Tested |
| VRD-27 | Non-detector Harness performance | PCAL Level |  |  | Not tested for SMEC or BSM |
| VRD-28 | Power supply cleanliness | Noise Tests |  |  | Not tested for flight configuration – GSE power supply. |
| VRD-29 | Digital/analogue separation | Noise Tests |  |  | Tested |
| VRD-30 | Electrical interface to Herschel system | Noise Tests |  |  | Tested for DPU only |
| VRD-39 | On board software definition | All |  |  | Tested as part of OBS development |

| Verified by cold functional test |
| --- |
| Requirement Name | Description | Procedure In | Test Report Section | NCRs | Status/Comments |
| IRD-VER-R03 | The CQM verification testing shall demonstrate that the following conditions are met or are likely to be met on the PFM: Correct operation of all FPU sub-systems at cryogenic temperatures for all instrument operation modes for both prime and redundant systems. The instrument cold FPU and JFET box thermal dissipation is within requirements for all instrument operation modes. The warm electronics thermal dissipation at room temperature is within requirements. Correct operation of all on-board software. The instrument straylight environment is within requirements The instrument optics performance is within requirements The performance of the instrument meets the scientific requirements expected for the CQM for all instrument observing modes Development and test of all functional test sequences required for Integrated Systems Testing (IST) at satellite level. The correct functioning of the instrument for all observing modes and calibration sequences. Development and test of all in-flight functional and performance test sequences | SPIRE-RAL-DOC-001888 SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Warm electronics units used for CQM model have not been thermally cycled and do not have full functional capability. CQM has only verified performance of photometer optics and PLW detector. |
| IRD-FPHR-R01 | Detector harness capacitance |  |  |  | Covered by performance tests |
| IRD-DETP-R05 | Electrical crosstalk for near neighbour pixels. |  |  |  | Covered by performance tests |
| IRD-DETP-R06 | Electrical crosstalk any pair of pixels |  |  |  | Covered by performance tests |
| IRD-CALP-R10 | Thermal isolation | SPIRE-RAL-DOC-001652 FUNC-SCU-03 FUNC-SCU-06 | SPIRE-RAL-REP-002084 |  | Instrument reached operating temperatures and remained stable. |
| IRD-CALP-R11 | Operating temperature | SPIRE-RAL-DOC-001652 FUNC-SCU-03 FUNC-SCU-06 | SPIRE-RAL-REP-002084 |  | Calibrated temperatures showing sensible values except BSM thermometer. |
| IRD-CALP-R12 | Cold power dissipation | SPIRE-RAL-DOC-001652 FUNC-SCU-07 | SPIRE-RAL-REP-002084 | HR-SP-RAL-NCR-62 | Cooler recycling OK Heat switch took too long to close |
| IRD-CALS-R12 | Thermal Isolation | SPIRE-RAL-DOC-001652 FUNC-SCU-03 FUNC-SCU-06 | SPIRE-RAL-REP-002084 |  | Instrument reached operating temperatures and remained stable. |
| IRD-CALS-R13 | Operating Temperature | SPIRE-RAL-DOC-001652 FUNC-SCU-03 FUNC-SCU-06 | SPIRE-RAL-REP-002084 |  | Instrument reached operating temperatures and remained stable. |
| IRD-FTB-R01 | Amplifier noise | SPIRE-RAL-DOC-001652 FUNC-DCU-11 | SPIRE-RAL-DOC-002084 |  | Noise not measured directly? |
| IRD-FTB-R05 | Dissipation | SPIRE-RAL-DOC-001652 FUNC-DCU-11 | SPIRE-RAL-REP-002084 |  | PLW array only Temperatures measured by TFCS were sensible and stable when powered on. |
| IRD-FTB-R08 | Nominal operating temperature | SPIRE-RAL-DOC-001652 FUNC-DCU-11 | SPIRE-RAL-REP-002084 |  | PLW array only Temperatures measured by TFCS were sensible and stable when powered on. |
| IRD-RFM-R03 | Dissipation | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Temperatures measured during test were sensible |
| IRD-RFM-R05 | Nominal operating temperature | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Temperatures measured during test were sensible |
| IRD-WE-R08 | Photometer detector readout | SPIRE-RAL-DOC-001652 FUNC-DCU-11 | SPIRE-RAL-REP-002084 |  | PLW Array only |
| IRD-WE-R13 | PCAL Control | SPIRE-RAL-DOC-001652 FUNC-SCU-04 FUNC-PCAL-01 | SPIRE-RAL-REP-002084 |  |  |
| IRD-WE-R14 | SCAL Control | SPIRE-RAL-DOC-001652 FUNC-SCU-05 FUNC-SCAL-01 | SPIRE-RAL-REP-002084 | HR-SP-RAL-NCR-64 | SCAL 4% failed at operating temperatures |
| IRD-WE-R15 | Cooler Control | SPIRE-RAL-DOC-001652 FUNC-SCU-07 Cooler Recycling | SPIRE-RAL-REP-002084 | HR-SP-RAL-NCR-62 HR-SP-RAL-NCR-63 | Heat switch took too long to close Pump and evaporator heat switch commands were in wrong order |
| IRD-WE-R17 | Housekeeping | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Telemetry acquisition as expected |
| IRD-WE-R20 | Subsystem Control Loops | N/A | N/A |  | Not tested |
| IRD-WE-R21 | Subsystem Data Acquisition | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Telemetry acquisition as expected |
| IRD-WE-R22 | Data Processing | N/A | N/A |  | No on-board data processing |
| IRD-WE-R23 | Communication | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Telecommand, Telemetry, Housekeeping and Science packets being sent/received |
| IRD-WE-R24 | WE anomalies | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 | NCR-MCU-123 NCR- SPIRE-OBS SPR-0288 | Over current limited triggered preventing MCU from switching on – to be fixed for MCU-QM1 MCU went into oscillation when powered on causing instrument temperatures to escalate – should be fixed for MCU-QM1 Occasional Tele-Command drop-out. |
| IRD-WE-R25 | Subsystem anomalies | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 | HR-SP-RAL-NCR-64 | SCAL 4% failed at operating temperatures |
| IRD-WE-R26 | Anomaly Management | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 | HR-SP-RAL-NCR-61 | Illegal command not rejected by DRCU and not sending an exception report. |
| IRD-WE-R35 | Power | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 | NCR-MCU-123 NCR- | Over current limited triggered preventing MCU from switching on – to be fixed for MCU-QM1 MCU went into oscillation when powered on causing instrument temperatures to escalate – should be fixed for MCU-QM1 |
| VRD-12 | Thermal performance | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Temperatures measured during test were sensible |
| VRD-17 | Harness mechanical frequency response and routing | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  |  |
| VRD-21 | Detector sub-system interface compatibility - thermal electrical mechanical | SPIRE-RAL-DOC-001652 |  |  | Electrical checkout during integration Functional tests showed that there were no problems due to electrical interfaces |
| VRD-24 | Electrical grounding | SPIRE-RAL-DOC-001652 |  |  | Checked during integration Functional tests showed that there were no problems due to grounding loops |
| VRD-27 | Non-detector Harness performance | SPIRE-RAL-DOC-001652 |  | HR-SP-RAL-NCR-63 | Pump and evaporator heat switch commands were in wrong order – solution was to update the harness definition and the DRCU/DPU ICD. |
| VRD-28 | Power supply cleanliness | SPIRE-RAL-DOC-001652 |  |  | Noise within acceptable levels |
| VRD-29 | Digital/analogue separation | ? | ? |  |  |
| VRD-30 | Electrical interface to Herschel system | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Tested using SPIRE EGSE |
| VRD-32 | Sub-system electrical interfaces |  |  |  | Tested using SPIRE EGSE |
| VRD-33 | Wiring tables | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 | HR-SP-RAL-NCR-63 | Pump and evaporator heat switch commands were in wrong order – solution was to update the harness definition and the DRCU/DPU ICD. |
| VRD-34 | Analogue to digital interfaces | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Test results show that A2D circuits were OK |
| VRD-37 | Operating mode definition | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | SPIRE in DRCU ON, REDY, PHOT STANDBY |
| VRD-38 | Instrument commanding definition | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | All commands that did execute produced the expected response |
| VRD-39 | On board software definition | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 | SPIRE-OBS SPR-0288 | OBS rejecting some commands at random Otherwise on board software behaved as expected |
| VRD-40 | Sub-system operational and control interfaces | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Commands executed as expected |
| VRD-41 | Sub-system data interfaces | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Telemetry as expected |
| VRD-48 | Ground commissioning and calibration plan | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Functional tests performed will be used for all ground testing, in-flight verification and ISTs |
| VRD-49 | Flight commissioning and calibration plan | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Functional tests performed will be used for in-flight verification and ISTs |
| VRD-50 | Instrument to ground facility interfaces | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Instrument tested with full EGSE system including storage of telemetry inside HCSS database, SCOS, QLA |

| VERIFIED BY WARM FUNCTIONAL TEST |
| --- |
| Requirement Name | Description | Procedure In | Test Report Section | NCRs | Status/Comments |
| IRD-VER-R03 | The CQM verification testing shall demonstrate that the following conditions are met or are likely to be met on the PFM: Correct operation of all FPU sub-systems at cryogenic temperatures for all instrument operation modes for both prime and redundant systems. The instrument cold FPU and JFET box thermal dissipation is within requirements for all instrument operation modes. The warm electronics thermal dissipation at room temperature is within requirements. Correct operation of all on-board software. The instrument straylight environment is within requirements The instrument optics performance is within requirements The performance of the instrument meets the scientific requirements expected for the CQM for all instrument observing modes Development and test of all functional test sequences required for Integrated Systems Testing (IST) at satellite level. The correct functioning of the instrument for all observing modes and calibration sequences. Development and test of all in-flight functional and performance test sequences | SPIRE-RAL-DOC-001888 SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Warm electronics units used for CQM model have not been thermally cycled and do not have full functional capability. CQM has only verified performance of photometer optics and PLW detector. |
| IRD-PHOT-R11 | Electrical crosstalk should be <1% (goal 0.5%) between nearest-neighbour pixels and <0.1 % (gaol 0.05%) between all other pixels in the same array. | Electrical Crosstalk Test Procedure – ref ? |  |  | Covered by performance tests |
| IRD-PHOT-R13 | The photometer dynamic range for astronomical signals shall be > 12 bits. | SPIRE-RAL-DOC-001652 FUNC-DCU-03 | SPIRE-RAL-REP-002084 |  |  |
| IRD-WE-R01 | Packet Services | SPIRE-RAL-DOC-001652 FUNC-DCU-11 FUNC-SCU-01 FUNC-MCU-02 | SPIRE-RAL-REP-002084 §4, 7 §7 §7 |  | Science data generation ok |
| IRD-WE-R02 | Telecommands | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 | SPIRE-OBS SPR-0288 | Some commands failed to execute All commands that did execute produced the expected response |
| IRD-WE-R03 | Telemetry | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Telemetry as expected |
| IRD-WE-R04 | Housekeeping | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Telemetry as expected |
| IRD-WE-R05 | Operating Modes | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | SPIRE into DRCU ON, INIT, REDY & STANDBY |
| IRD-WE-R06 | Command Services | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 | SPIRE-OBS SPR-0288 | Occasional loss of commands |
| IRD-WE-R07 | Data Handling | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Telemetry and housekeeping as expected |
| IRD-WE-R18 | S/C Interface | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Tested using SPIRE EGSE (CDMS Simulator) |
| IRD-WE-R19 | Subsystem Interface | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Commands executed as expected |
| IRD-WE-R20 | Subsystem Control Loops | N/A | N/A |  | Not tested at room temperature |
| IRD-WE-R21 | Subsystem Data Acquisition | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | All subsystems functioned as expected at room temperature |
| IRD-WE-R22 | Data Processing | N/A | N/A |  | No on-board data processing |
| IRD-WE-R23 | Communication | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Telecommand, Telemetry, Housekeeping and Science packets being sent/received |
| IRD-WE-R24 | WE anomalies | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 | NCR-MCU-123 SPIRE-OBS SPR-0288 | Over current limited triggered preventing MCU from switching on – to be fixed for MCU-QM1 Occasional Tele-Command drop-out. |
| IRD-WE-R25 | Subsystem anomalies | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | None |
| IRD-WE-R26 | Anomaly Management | Not Tested | Not Tested |  | Not tested at room temperature |
| IRD-WE-R35 | Power | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 | NCR-MCU-123 | Over current limited triggered preventing MCU from switching on – to be fixed for MCU-QM1 |
| IRD-FSIM-R01 | Function | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | All subsystems functioned as expected during WFT |
| IRD-FSIM-R02 | Analogue Outputs | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | All subsystems functioned as expected during WFT Limited test |
| IRD-FSIM-R03 | Control loops | N/A | N/A |  | Not Tested during WFT |
| VRD-21 | Detector sub-system interface compatibility - thermal electrical mechanical | SPIRE-RAL-DOC-001652 |  |  | Electrical checkout during integration Functional tests showed that there were no problems due to electrical interfaces |
| VRD-24 | Electrical grounding | SPIRE-RAL-DOC-001652 |  |  | Checked during integration Functional tests showed that there were no problems due to grounding loops |
| VRD-27 | Non-detector Harness performance | SPIRE-RAL-DOC-001652 |  |  |  |
| VRD-28 | Power supply cleanliness | SPIRE-RAL-DOC-001652 |  |  | Noise within acceptable levels |
| VRD-29 | Digital/analogue separation | ? | ? |  |  |
| VRD-30 | Electrical interface to Herschel system | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Tested using SPIRE EGSE |
| VRD-31 | Power supply distribution and control |  |  |  | Tested using SPIRE EGSE |
| VRD-32 | Sub-system electrical interfaces | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Functional tests demonstrate that internal interfaces were ok |
| VRD-33 | Wiring tables | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Limited test at warm temperatures show indirectly that subsystems were wired as per harness definition. |
| VRD-34 | Analogue to digital interfaces | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Limited tests at warm temperatures show that all A2D circuits were ok. |
| VRD-35 | Digital to digital interfaces | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Some problems with assignment of parameters as signed or unsigned integers – otherwise numbers coming out as expected |
| VRD-36 | Data interface to Herschel system | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Tested using SPIRE EGSE (CDMS Simulator) |
| VRD-37 | Operating mode definition | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | SPIRE into DRCU ON, INIT, REDY & STANDBY |
| VRD-38 | Instrument commanding definition | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | All commands that did execute produced the expected response |
| VRD-39 | On board software definition | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 | SPIRE-OBS SPR-0288 | OBS rejecting some commands at random Otherwise on board software behaved as expected |
| VRD-40 | Sub-system operational and control interfaces | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Commands executed as expected |
| VRD-41 | Sub-system data interfaces | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Telemetry as expected |
| VRD-48 | Ground commissioning and calibration plan | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Functional tests performed will be used for in-flight verification and ISTs |
| VRD-50 | Instrument to ground facility interfaces | SPIRE-RAL-DOC-001652 | SPIRE-RAL-REP-002084 |  | Instrument tested with full EGSE system including storage of telemetry inside HCSS database, SCOS, QLA |