Procedure for connecting CQM FPU to Warm Electronics in Cryolab

| Prepared by: |  |  |
| --- | --- | --- |
|  | D.L. Smith (RAL) | Date |
| Checked: |  |  |
|  | D. Griffin (RAL) | Date |
| Approval: |  |  |
|  | E. Sawyer (RAL) | Date |

| Host system | Windows 2000 SP2 |
| --- | --- |
| Word Processor | Microsoft Word 2000 SR1 |
| File | Cryoharness Integration Procedure Draft 0.4.Doc |

# Document Change Record

| Date | Index | Affected Pages | Changes |
| --- | --- | --- | --- |
|  | 0.1 | All | First Draft |
| Jan 2004 | 0.2 | All | Revised for CQM 1 Tests |
| August 2004 | 0.3 | All | Updated following review of CQM 1 Cold Testing |
| December 2004 | 0.4 | All | Updated for PFM1 Tests |

# Scope of Document

This document describes the correct sequence to connect and disconnect the SPIRE FPU to the warm electronics.

NOTE: This version of the procedure applies only to the PFM1 build which only has spectrometer detectors mounted.

# Applicable Document

|  | Title | Author | Reference | Date |
| --- | --- | --- | --- | --- |
| AD 1 | Making SPIRE ESD Safe | Doug Griffin | SPIRE-RAL-NOT-002028 Issue 2 | 28-Oct-2004 |

# Constraints

ESD Protective straps must be worn at all times while working on the SPIRE FPU. Failure to do this could result in damage to the detectors and JFETS.

# Measure shorts to ground of installed harness.

The harness will be pre-installed in the cryostat with the external shields isolated from the tank. Disconnect the grounding plugs from the air side harness and connect a DVM between the tank wall and the inner flying lead. Set the DVM to read resistance and set the alarm. If a reading of < 10M is detected then there is a short to tank wall.

# Connect FPU and Electronics to Harness

## Connect Cold Harness to FPU and JFETS.

Once the instrument has been moved into the chamber and locked into position, the cold harness will be connected to the JFETS first with the bias connector blanked off.  Make sure that shorting plugs are fitted to the warm tails of before connecting the live JFETS.  After all JFETS have been connected at the cold end, the bias harness will be connected to the bias connectors before connecting the JFET tails to the DCU.

Connect the harness in this sequence and record the connection in the mate/de-mate log.

| Harness | Cryoharness Connector | FPU/JFET Connector | Comments | Done |
| --- | --- | --- | --- | --- |
| FPU |  |  |  |  |
| C10 | P19 | HSFPU - J19 |  |  |
|  | P21 | HSFPU - J21 |  |  |
|  | P23 | HSFPU - J23 |  |  |
| C12 | P20 | HSFPU - J28 |  |  |
|  | P22 | HSFPU - J22 |  |  |
|  | P24 | HSFPU - J24 |  |  |
| C11 | P25 | HSFPU - J25 |  |  |
|  | P29 | HSFPU - J29 |  |  |
|  | P27 | HSFPU - J27 |  |  |
| C13 | P26 | HSFPU - J26 |  |  |
|  | P30 | HSFPU - J30 |  |  |
|  | P28 | HSFPU - J20 |  |  |
| JFS |  |  |  |  |
| C2 | P1 | HSJFS-J1 |  |  |
|  | P2 | HSJFS-J2 |  |  |
|  | P3 | HSJFS-J3 |  |  |
|  | P4 | HSJFS-J4 |  |  |
|  | P7 | HSJFS-J7 |  |  |
| C1 | P5 | HSJFS-J5 |  |  |
|  | P6 | HSJFS-J6 |  |  |
|  | P8 | HSJFS-J8 |  |  |
|  | P9 | HSJFS-J9 |  |  |
|  | P10 | HSJFS-J10 |  |  |
| JFP |  |  |  |  |
| C4 | P24 | HSJFPJ24 |  |  |
|  | P23 | HSJFPJ23 |  |  |
|  | P22 | HSJFPJ22 |  |  |
|  | P21 | HSJFPJ21 |  |  |
| C5 | P20 | HSJFPJ20 |  |  |
|  | P19 | HSJFPJ19 |  |  |
|  | P18 | HSJFPJ18 |  |  |
|  | P17 | HSJFPJ17 |  |  |
| Fit Shorting plugs to Warm Electronics end of S6 J14, J15 & J16 |
| C6 | P16 | HSJFPJ16 |  |  |
|  | P15 | HSJFPJ15 |  |  |
|  | P14 | HSJFPJ14 |  |  |
|  | P13 | HSJFPJ13 |  |  |
| C7 | P12 | HSJFPJ12 |  |  |
|  | P11 | HSJFPJ11 |  |  |
|  | P10 | HSJFPJ10 |  |  |
|  | P09 | HSJFPJ09 |  |  |
| C8 | P08 | HSJFPJ08 |  |  |
|  | P07 | HSJFPJ07 |  |  |
|  | P06 | HSJFPJ06 |  |  |
|  | P05 | HSJFPJ05 |  |  |
| C9 | P04 | HSJFPJ04 |  |  |
|  | P03 | HSJFPJ03 |  |  |
|  | P02 | HSJFPJ02 |  |  |
|  | P01 | HSJFPJ01 |  |  |
| C3 | P25 | HSJFPJ25 |  |  |
|  | P26 | HSJFPJ26 |  |  |
|  | P27 | HSJFPJ27 |  |  |
|  | P28 | HSJFPJ28 |  |  |

## Connect Warm harness to DRCU and DPU

Connect the harness in this sequence and record in the mate/de-mate log

| Harness | Warm harness Connector | DRCU Connector | Comments | Done |
| --- | --- | --- | --- | --- |
| FCU |  |  |  |  |
| S10 | P11 | HSFCU-J11 |  |  |
|  | P23 | HSFCU-J23 |  |  |
|  | P25 | HSFCU-J25 |  |  |
| S11 | P13 | HSFCU-J13 |  |  |
|  | P17 | HSFCU-J17 |  |  |
|  | P19 | HSFCU-J19 |  |  |
|  | P21 | HSFCU-J21 |  |  |
|  | P29 | HSFCU-J29 |  |  |
| S12 | P12 | Lakeshore Harness |  |  |
|  | P24 | Lakeshore Harness |  |  |
|  | P26 | N/C? |  |  |
| DCU |  |  |  |  |
| Connect JFET Bias First |
| S1 | P31 | HSDCU-J31 |  |  |
| S3 | P29 | HSDCU-J29 |  |  |
| Spectrometer Detectors |
| S1 | P27 | HSDCU-J33 |  |  |
| S1 | P28 | HSDCU-J34 |  |  |
| S2 | P25 | HSDCU-J25 |  |  |
| S2 | P26 | HSDCU-J26 |  |  |
| S2 | P23 | HSDCU-J23 |  |  |
| S2 | P24 | HSDCU-J24 |  |  |
| S6 | P15 | HSDCU-J15 |  |  |
| S6 | P16 | HSDCU-J16 |  |  |
| S6 | P14 | HSDCU-J14 |  |  |

# Disconnect FPU from Harnesses

## Disconnect Warm harness from DRCU and DPU

Disconnect the harness in this sequence and record in the mate/de-mate log

| Harness | Warm harness Connector | DRCU Connector | Comments | Done |
| --- | --- | --- | --- | --- |
| DCU |  |  |  |  |
| Spectrometer Detectors |
| S1 | P27 | HSDCU-J33 |  |  |
| S1 | P28 | HSDCU-J34 |  |  |
| S2 | P25 | HSDCU-J25 |  |  |
| S2 | P26 | HSDCU-J26 |  |  |
| S2 | P23 | HSDCU-J23 |  |  |
| S2 | P24 | HSDCU-J24 |  |  |
| PLW |
| S6 | P15 | HSDCU-J15 |  |  |
| S6 | P16 | HSDCU-J16 |  |  |
| S6 | P14 | HSDCU-J14 |  |  |
| Connect shorting plugs to P14, P15 and P16 before disconnecting bias |
| Disconnect Bias |
| S3 | P29 | HSDCU-J29 |  |  |
| S1 | P31 | HSDCU-J31 |  |  |
| FCU |  |  |  |  |
| S10 | P11 | HSFCU-J11 |  |  |
|  | P23 | HSFCU-J23 |  |  |
|  | P25 | HSFCU-J25 |  |  |
| S11 | P13 | HSFCU-J13 |  |  |
|  | P17 | HSFCU-J17 |  |  |
|  | P19 | HSFCU-J19 |  |  |
|  | P21 | HSFCU-J21 |  |  |
|  | P29 | HSFCU-J29 |  |  |
| S12 | P12 | Lakeshore Harness |  |  |
|  | P24 | Lakeshore Harness |  |  |
|  | P26 | N/C? |  |  |

## Disconnect Cold Harness from FPU and JFETS.

Disconnect the harness in this sequence and record the connection in the mate/de-mate log.

| Harness | Cryoharness Connector | FPU/JFET Connector | Comments | Done |
| --- | --- | --- | --- | --- |
| JFP |  |  |  |  |
| C4 | P24 | HSJFPJ24 |  |  |
|  | P23 | HSJFPJ23 |  |  |
|  | P22 | HSJFPJ22 |  |  |
|  | P21 | HSJFPJ21 |  |  |
| C5 | P20 | HSJFPJ20 |  |  |
|  | P19 | HSJFPJ19 |  |  |
|  | P18 | HSJFPJ18 |  |  |
|  | P17 | HSJFPJ17 |  |  |
| C6 | P16 | HSJFPJ16 |  |  |
|  | P15 | HSJFPJ15 |  |  |
|  | P14 | HSJFPJ14 |  |  |
|  | P13 | HSJFPJ13 |  |  |
| Shorting plugs at Warm Electronics end of S6 J14, J15 & J16 can now be removed. |
| C7 | P12 | HSJFPJ12 |  |  |
|  | P11 | HSJFPJ11 |  |  |
|  | P10 | HSJFPJ10 |  |  |
|  | P09 | HSJFPJ09 |  |  |
| C8 | P08 | HSJFPJ08 |  |  |
|  | P07 | HSJFPJ07 |  |  |
|  | P06 | HSJFPJ06 |  |  |
|  | P05 | HSJFPJ05 |  |  |
| C9 | P04 | HSJFPJ04 |  |  |
|  | P03 | HSJFPJ03 |  |  |
|  | P02 | HSJFPJ02 |  |  |
|  | P01 | HSJFPJ01 |  |  |
| C3 | P25 | HSJFPJ25 |  |  |
|  | P26 | HSJFPJ26 |  |  |
|  | P27 | HSJFPJ27 |  |  |
|  | P28 | HSJFPJ28 |  |  |
| JFS |  |  |  |  |
| C2 | P1 | HSJFS-J1 |  |  |
|  | P2 | HSJFS-J2 |  |  |
|  | P3 | HSJFS-J3 |  |  |
|  | P4 | HSJFS-J4 |  |  |
|  | P7 | HSJFS-J7 |  |  |
| C1 | P5 | HSJFS-J5 |  |  |
|  | P6 | HSJFS-J6 |  |  |
|  | P8 | HSJFS-J8 |  |  |
|  | P9 | HSJFS-J9 |  |  |
|  | P10 | HSJFS-J10 |  |  |
| FPU |  |  |  |  |
| C10 | P19 | HSFPU - J19 |  |  |
|  | P21 | HSFPU - J21 |  |  |
|  | P23 | HSFPU - J23 |  |  |
| C12 | P20 | HSFPU - J28 |  |  |
|  | P22 | HSFPU - J22 |  |  |
|  | P24 | HSFPU - J24 |  |  |
| C11 | P25 | HSFPU - J25 |  |  |
|  | P29 | HSFPU - J29 |  |  |
|  | P27 | HSFPU - J27 |  |  |
| C13 | P26 | HSFPU - J26 |  |  |
|  | P30 | HSFPU - J30 |  |  |
|  | P28 | HSFPU - J20 |  |  |