| Tipo Doc.: Doc.Type: | REPORT SPIRE-IFS-REP-002196 | N° DRD: DRD N°: | N.A. |
| --- | --- | --- | --- |
| N° Doc.: Doc. N°: | DPU-RP-CGS-030 | Ediz.: Issue: | 1 | Data: Date: | 5/04/2002 | Pagina Page | 1 | Di Of | 95 |
| Titolo : Title : | HSO/FIRST DPU BASIC S/W TEST REPORT |

|  | Nome & Funzione Name & Function | Firma Signature | Data Date |  | LISTA DI DISTRIBUZIONE DISTRIBUTION LIST | N | A | I |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Preparato da: Prepared by: | FIRST-DPU TEAM |  |  |  | Interna / Internal |  |  |  |
|  |  |  |  |  | Legramandi S. (PA/QA) Bertoli A. (DT/SW) Longoni A. (DP/PL) | 1 1 1 | X X X |  |
| Approvato da: Approved by: | Legramandi (PA/QA) Di Gioia L. (PC/CC) Bertoli A. (DT/SW) |  |  |  |  |  |  |  |
| Applicazione autorizzata da: Application authorized by: | Longoni A. (DP/PL) |  |  |  | Esterna / External |  |  |  |
|  |  |  |  |  | Orfei R. (CNR-IFSI) | 1 | X |  |
| Customer / Higher Level Contractor |  |  |  |  |  |
| Accettato da: Accepted by: |  |  |  |  |  |  |  |  |
| Approvato da: Approved by: |  |  |  |  |  |  |  |  |
|  |  |  |  |  | N=Numero di copie A=Applicazione I=Informazione N=Number of copy A=Application I=Information |

| Gestione documenti: Data Management: |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | Firma / Signature Data / Date |  | File: | DPU-RP-CGS-030 is 1.doc |

| REGISTRAZIONE DELLE MODIFICHE / CHANGE RECORD |
| --- |
| EDIZIONE ISSUE | DATA DATE | AUTORIZZAZIONE CHANGE AUTHORITY | OGGETTO DELLA MODIFICA E SEZIONI AFFETTE REASON FOR CHANGE AND AFFECTED SECTIONS |
| 1 | 5/04/2002 |  |  |

| LISTA DELLE PAGINE VALIDE / LIST OF VALID PAGES |
| --- |
| PAGINA PAGE | EDIZIONE ISSUE | PAGINA PAGE | EDIZIONE ISSUE | PAGINA PAGE | EDIZIONE ISSUE | PAGINA PAGE | EDIZIONE ISSUE | PAGINA PAGE | EDIZIONE ISSUE |
| 1 - 92 | 1 |  |  |  |  |  |  |  |  |

TABLE OF CONTENT

1.	SCOPE	8

2.	documents	9

2.1	applicable documents	9

2.2	reference documents	9

3.	acronyms	10

4.	participants required	11

4.1	general	11

4.2	responsibility	11

4.3	qa witness of test and sign-off	11

5.	test article	12

5.1	ITEMS description	12

6.	test configuration	13

6.1	cross reference MATRIX	14

7.	INSTRUMENTATION AND TEST EQUIPMENT	18

8.	test procedures.	19

8.1	dpu boot sw TEST PROCEDURES.	19

8.1.1	BOOT SW Test Procedure.	19

8.1.2	DM Test Procedure.	21

8.1.3	PM Test Procedure.	22

8.1.4	EEPROM Test Procedure.	23

8.1.5	EEPROM to PM LOAD Test Procedure.	26

8.1.6	DM to PM LOAD Test Procedure.	27

8.2	1355 DRIVER TEST PROCEDURE.	29

8.2.1	1355 Power On Test Procedure.	29

8.2.2	1355 Reset Link Test Procedure.	30

8.2.3	1355 Time-out Test Procedure.	31

8.2.4	1355 Open Link Test Procedure.	32

8.2.5	1355 Close Link Test Procedure.	33

8.2.6	1355 Start Link As Master Test Procedure.	34

8.2.7	1355 Start Link as Slave Test Procedure.	35

8.2.8	1355 Stop Link Test Procedure.	36

8.2.9	1355 Get Status Register Test Procedure.	37

8.2.10	1355 Write Link Test Procedure.	38

8.2.11	1355 Read Link Test Procedure.	39

8.2.12	1355 Get Link Status Test Procedure.	40

8.2.13	1355 Read Packet Test Procedure.	41

8.2.14	1355 Get Last Read Size Test Procedure.	42

8.2.15	1355 Get Last Read Write Size Test Procedure.	43

8.2.16	1355 Get Last Packet Number Test Procedure.	44

8.2.17	1355 Write to Board Memory Test Procedure.	45

8.2.18	1355 Read From Board Memory Test Procedure.	46

8.2.19	1355 Write Register Test Procedure.	47

8.2.20	1355 Read Register Test Procedure.	48

8.3	watchdog TEST PROCEDURE.	49

8.3.1	Delay Setting Test Procedure.	49

8.3.2	Delay programming Test Procedure.	50

8.3.3	Watchdog Refresh Test Procedure.	51

8.3.4	Watchdog Status Test Procedure.	52

8.4	MIL-STD 1553 SW DRIVER TEST PROCEDURE	53

8.4.1	OPen MIL-STD 1553 CHANNEL	53

8.4.2	TX MIL-STD 1553 MESSAGE	55

8.4.3	RX MIL-STD 1553 MESSAGE	56

8.4.4	CLOSE MIL-STD CHANNEL	57

8.5	EEPROM DRIVER TEST PROCEDURE	58

8.5.1	DELETE EEPROM SEGMENT	58

8.5.2	WRITE EEPROM CELL	59

8.5.3	DELETE EEPROM CELL	61

8.5.4	WRITE EEPROM SEGMENT	63

8.5.5	ENABLE/DISABLE EEPROM PROTECTION	65

8.5.6	COPY PROGRAM IN EEPROM	66

ANNEX A :	1553 RETURNED PACKETS FORMAT AFTER 1355 COMMAND.	69

:	LEGENDA.	69

ANNEX A2 :	POWER-ON, OPEN LINK AND CLOSE LINK RETURNED PACKET.	69

ANNEX A3 :	WRITE REGISTERS RETURNED PACKET.	70

ANNEX A4 :	READ REGISTERS RETURNED PACKET.	70

ANNEX A5 :	START LINK MASTER AND SLAVE, STOP LINK AND RESET LINK RETURNED PACKETS.	71

ANNEX A6 :	WRITE LINK RETURNED PACKET.	73

ANNEX A7 :	READ LINK RETURNED PACKET.	76

ANNEX A8 :	READ PACKET RETURNED PACKET.	79

ANNEX A9 : PACKET NUM, GET_W_SIZE AND GET_R_SIZE RETURNED PACKETS.	83

ANNEX A10 : GET STATUS RETURNED PACKET.	83

ANNEX A11 : GET_IDSTATE AND GET_IDSTATUS RETURNED PACKET.	83

ANNEX A12 : SET TIMEOUT RETURNED PACKET.	85

ANNEX A13 : EXIT STUB RETURNED PACKET.	85

ANNEX A14 : ERROR ON SELECT NUMBER OF FUCTION RETURNED PACKET.	85

ANNEX A15 : WRITE TO BOARD MEMORY RETURNED PACKET.	86

ANNEX A16 : READ FROM BOARD MEMORY RETURNED PACKET.	88

ANNEX A17 : WATCHDOG DELAY RETURNED PACKET.	89

ANNEX A18 : WATCHDOG DELAY FAILED RETURNED PACKET.	90

ANNEX A19 : WATCHDOG REFRESH RETURNED PACKET.	90

ANNEX A20 : WATCHDOG STATUS RETURNED PACKET.	90

ANNEX A21 : ERROR CODE RETURNED PACKET.	90

ANNEX A22 : EXIT STUB RETURNED PACKET.	90

ANNEX A1 : RETURNED MIL-STD-1553 PACKETS FORMAT AFTER A EEPROM COMMAND	91

ANNEX C : 1355 DRIVERS RETURNED ERRORS CODE	91

LIST OF FIGURES

figure 6-1:Test Configuration Environment	13

LIST OF TABLES

table 6-1: Cross reference table	17

table 7-1: Instrumentation and Test Equipment Table	18

# SCOPE

The aim of the present document is to provide a detailed test report of HSO/First-DPU BASIC S/W to be installed on the Data Processing Units developed in the framework of the HSO/FIRST program.

The test to be performed according to the Test Procedure as defined in [AD 6] are to demonstrate the compliance of the above item to the requirements specified in the applicable document [AD 7] as part of the overall verification program.

# documents

## applicable documents

[AD1]:	CNR.IFSI.2000TR01 "Documento di Specifiche Tecniche per il Contratto delle Data Processing Uniste del Satellite First dell'ESA"    IFSI (Issue: 1 - 15/09/2000)

[AD2]:	Technical proposal CGS (Ref. S9-030 November 99)

[AD3]:	“Allegato Tecnico al Contratto ASI"

[AD4]:	 Product Assurance Plan for the FIRST DPU (DPU-PL-CGS-001 Issue 1 Jan. 2001)

[AD5]:	DPU-PL-CGS-002 Dpu-Sw Verification And Validation Plan/Acceptance TEST (issue 1)

[AD6]:	SCI-PT-ICD-07527 Packet Structure Interface Control Document (Issue 1, 1 September 2000)

[AD7]:	DPU-SQ-CGS-001 Dpu-Bsw Software Requirements Document (July 12, 2001).

[AD8]:	CNR.IFSI.2001 TR01 DPU/ICU issue Draft 3 Switch On Procedure DPU SWITCH ON Procedure

## reference documents

[RD 1]:	 ACE/Mini ACE Series BC/RT/MT DDC user’s guide

[RD 2]:	 SMCS 332 user’s guide

# acronyms

| AD | Applicable Document Number |
| --- | --- |
| BB | Broadband |
| CE | Conducted Emission |
| C.I. | Configuration Item. Also called Part Number (P/N) |
| CGS | Carlo Gavazzi Space |
| CS | Conducted Susceptibility |
| DPU | Data Processing Unit |
| DM | Data Memory |
| FIRST | Far Infra-Red and Sub-millimeter Telescope |
| FPU | Focal Plane Unit |
| FCS | Frame Check Sequence |
| GND | Ground |
| HIFI | Heterodyne Instrument for First |
| HK | House Keeping |
| ICD | Interface Control Document |
| ICU | Instrument Control Unit |
| IID | Instrument Interface Document |
| I/F | Interface |
| LCL | Latching Current Limiter |
| NA | Not Applicable |
| NB | Narrowband |
| OCP | Over-Current Protection |
| OVP | Over-Voltage Protection |
| P/N | Part Number. Also called Configuration Item C.I. |
| PA | Product Assurance |
| PACS | Photoconductor Array Camera and Spectrometer |
| PM | Program Memory |
| PL | Payload |
| PVS | Procedure Variation Sheet |
| QA | Quality Assurance |
| RD# | Reference Document Number |
| RE | Radiated Emission |
| RS | Radiated Susceptibility |
| RTN | Return Line |
| S/C | Spacecraft |
| S/W | Software |
| SPIRE | Spectral and Photometric Imaging receiver |
| TBC | To Be Confirmed |
| TBD | To Be Determined |
| TM/TC | Telemetry & Tele-command |
| uut | Unit Under Test |

# participants required

## general

All test will be performed under QA surveillance in accordance with, and following detailed procedure of applicable PA Plan. Start of the Test shall be notified to Prime Contractor and/or Customer as applicable.

## responsibility

The technical responsibility for testing and test results is up to the Software department.

QA is responsible for ensuring that all the agreed procedures are carefully observed, that test equipment and instrumentation used during testing is calibrated and within validity date: that the test data sheets are recorded in the Test Report and signed by the operators and QA witnesses, that all non conforming condition and test results are properly documented and notified to the Prime Contractor, and that all requirements of applicable PA Plan, specification and Statement of Work pertaining to the acceptance tests, are fully satisfied.

## qa witness of test and sign-off

QA inspector, or its delegate, shall witness the tests described in this procedure for the EM model in accordance to the requirement specified in the applicable PA Plans. For the EM QA or its delegate will check the test report sheets only.

# test article

The test article consists of the HSO/DPU FIRST BASIC SW. It is composed of the following items

- BOOT SW

- DRIVERS SW

- 1355 Drivers

- 1553 Drivers

- Watchdog Drivers

- EEPROM Drivers

## ITEMS description

The BOOT SW is that will be resident in the PROM memory and it will allow the copy of the EEPROM program in Program Memory for the execution. The program is able to detect Data memory errors, Program memory errors, EEPROM memory errors, Application Program instruction errors by means of the Frame Check sequence checking. The Program signals the errors by means of the MIL-STD-1553 sending a Telemetry Packet to Computer Data management System according to the [AD 6] document. The BOOT SW program allows to upload a new version of the “Application Program” from Computer Data Management System via MIL-STD-1553. The CMDS will send adequate TC in order to upload the Data Memory of the Board and then it will move all the page in Program memory adjusting the Instruction parallelism.

The 1355 Drivers allow to command the Spacewire interface. A suite of the basic (Data Link layer)  and High level (Transport Layer) functions are provided in order to allow an easy interface to the Application Software.

The 1553 Drivers allow to program and command the DDC chip for the MIL-STD-1553 management. A suite of elementary and High level function is provided in order to allow an easy interface to the Application Software.

The users can choose the level more adequate interfacing the Application Software.

The Watchdog Drivers allow to command the Watchdog. Essential functions are provided in order to program the watchdog board.

The EEPROM Drivers allow to read and write the EEPROM. High level functions are provided for programming the EEPROM. The EEPROM is shared in page and the first 7 words of each page are reserved for page Header. Each page contains the PM check sequence and DM check sequence. When a cell  of the page is written the FCS are automatically computed. The EEPROM Drives includes a high level function which allows to transfer a program in Program memory in EEPROM specifying the start address and the end address. The Interrupt vectors table is automatically included.

# test configuration

The following picture shows the Test environment configuration (figure 6-1).

figure 6-1:Test Configuration Environment

## cross reference MATRIX

Cross reference among requirements and procedure steps is provided in the following table (table 6-1).

| Requirements | Procedure Step |
| --- | --- |
| SRD-3.1.1.0-000 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-010 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-020 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-040 | SEL-R |
| SRD-3.1.1.0-050 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-060 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-070 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-080 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-090 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-100 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-110 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-120 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-130 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-140 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-150 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-160 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-170 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-180 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-190 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-200 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-210 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-220 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-230 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-240 | SEL-R |
| SRD-3.1.1.0-250 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-260 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-270 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-280 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-290 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-300 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-310 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-320 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-330 | SEL-R |
| SRD-3.1.1.0-340 | SEL-R |
| SRD-3.1.1.0-350 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-360 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.1.0-370 | TR-BOOTSW –010, -20, -25, -30, -40, -50 |
| SRD-3.1.2.0-000 | SEL-R |
| SRD-3.1.2.0-005 | SEL-R |
| SRD-3.1.2.0-010 | SEL-R |
| SRD-3.1.2.0-020 | SEL-R |
| SRD-3.1.3.0-000 | SEL-R |
| SRD-3.1.4.0-000 | TR-BOOTSW -20 |
| SRD-3.1.4.0-010 | TR-BOOTSW -20 |
| SRD-3.1.4.0-020 | TR-BOOTSW -20 |
| SRD-3.1.4.0-030 | TR-BOOTSW -20 |
| SRD-3.1.4.0-040 | TR-BOOTSW -20 |
| SRD-3.1.5.0-000 | TR-BOOTSW -25 |
| SRD-3.1.5.0-010 | TR-BOOTSW -25 |
| SRD-3.1.5.0-020 | TR-BOOTSW -25 |
| SRD-3.1.5.0-030 | TR-BOOTSW -25 |
| SRD-3.1.5.0-040 | TR-BOOTSW -25 |
| SRD-3.1.6.0-000 | TR-BOOTSW -30 |
| SRD-3.1.6.0-010 | TR-BOOTSW -30 |
| SRD-3.1.6.0-020 | TR-BOOTSW -30 |
| SRD-3.1.6.0-030 | TR-BOOTSW -30 |
| SRD-3.1.6.0-040 | TR-BOOTSW -30 |
| SRD-3.1.6.0-050 | TR-BOOTSW -30 |
| SRD-3.1.6.0-060 | TR-BOOTSW -30 |
| SRD-3.1.6.0-070 | TR-BOOTSW -30 |
| SRD-3.1.7.0-000 | TR-BOOTSW –40 |
| SRD-3.1.7.0-010 | TR-BOOTSW –40 |
| SRD-3.1.7.0-020 | TR-BOOTSW -40 |
| SRD-3.1.7.0-030 | TR-BOOTSW -40 |
| SRD-3.1.7.0-040 | TR-BOOTSW -40 |
| SRD-3.1.8.0-000 | TR-BOOTSW -50 |
| SRD-3.1.8.0-010 | TR-BOOTSW, -50 |
| SRD-3.1.8.0-020 | TR-BOOTSW, -50 |
| SRD-3.1.8.0-030 | TR-BOOTSW, -50 |
| SRD-3.1.8.0-040 | TR-BOOTS, -50 |
| SRD-3.2.0.0-000 | TR-DRV1355 –010 |
| SRD-3.2.0.0-010 | TR-DRV1355 –010 |
| SRD-3.2.0.0-020 | TR-DRV1355 –020 |
| SRD-3.2.0.0-025 | TR-DRV1355 –030 |
| SRD-3.2.0.0-030 | TR-DRV1355 –040 |
| SRD-3.2.0.0-040 | TR-DRV1355 –050 |
| SRD-3.2.0.0-050 | TR-DRV1355 –060 |
| SRD-3.2.0.0-060 | TR-DRV1355 –070 |
| SRD-3.2.0.0-070 | TR-DRV1355 –080 |
| SRD-3.2.0.0-080 | TR-DRV1355 –090 |
| SRD-3.2.0.0-090 | TR-DRV1355 –100 |
| SRD-3.2.0.0-100 | TR-DRV1355 –100 |
| SRD-3.2.0.0-110 | TR-DRV1355 –010 |
| SRD-3.2.0.0-120 | TR-DRV1355 –110 |
| SRD-3.2.0.0-130 | TR-DRV1355 –110 |
| SRD-3.2.0.0-140 | TR-DRV1355 –120 |
| SRD-3.2.0.0-150 | TR-DRV1355 –120 |
| SRD-3.2.0.0-160 | TR-DRV1355 –140, -130 |
| SRD-3.2.0.0-170 | TR-DRV1355 –140 |
| SRD-3.2.0.0-180 | TR-DRV1355 –160 |
| SRD-3.2.0.0-190 | TR-DRV1355 –150 |
| SRD-3.2.0.0-200 | TR-DRV1355 –200, -190 |
| SRD-3.2.0.0-210 | TR-DRV1355 –180, 170 |
| SRD-3.3.2.0-000 | TR-DRV1553 –010 |
| SRD-3.3.2.0-010 | TR-DRV1553 –010 |
| SRD-3.3.3.1-000 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.1-010 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.1-020 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.1-030 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.1-040 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.1-050 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.1-060 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.2-000 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.2-010 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.2-020 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.2-030 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.2-040 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.2-050 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.2-060 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.3-000 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.3-010 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.3-020 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.3-030 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.3-040 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.3-050 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.3-060 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.3-070 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.3-080 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.3-090 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.3-100 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.3-110 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.3-120 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.3-130 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.3-140 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.3-150 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.3.3.3-160 | TR-DRV1553 –010, -20, -30, -40 |
| SRD-3.5.0.0-000 | TR-DRVEPRM –10, -50 |
| SRD-3.5.0.0-010 | TR-DRVEPRM –10, -50 |
| SRD-3.5.0.0-020 | TR-DRVEPRM –20, -50 |
| SRD-3.5.0.0-030 | TR-DRVEPRM –30, -50 |
| SRD-3.5.0.0-040 | TR-DRVEPRM –40, -50 |
| SRD-3.6.0.0-000 | TR-DRVWD-10 |
| SRD-3.6.0.0-010 | TR-DRVWD –20 |
| SRD-3.6.0.0-020 | TR-DRVWD -30 |
| SRD-4.1.1.0-000 | SEL-R |
| SRD-4.1.2.0-000 | SEL-R |
| SRD-4.1.2.0-010 | SEL-R |
| SRD-4.1.2.0-020 | SEL-R |
| SRD-4.1.2.0-030 | SEL-R |
| SRD-5.1.0.0-000 | SEL-R |
| SRD-5.1.0.0-010 | SEL-R |
| SRD-5.1.0.0-020 | SEL-R |
| SRD-5.1.0.0-030 | SEL-R |
| SRD-5.1.0.0-040 | SEL-R |
| SRD-5.1.0.0-050 | SEL-R |
| SRD-5.1.0.0-060 | SEL-R |
| SRD-5.1.0.0-070 | SEL-R |
| SRD-5.1.0.0-080 | SEL-R |
| SRD-5.1.0.0-090 | SEL-R |
| SRD-5.2.0.0-000 | SEL-R |
| SRD-5.2.0.0-010 | SEL-R |
| SRD-5.3.0.0-000 | SEL-R |
| SRD-5.3.0.0-010 | SEL-R |
| SRD-5.3.0.0-020 | SEL-R |
| SRD-6.1.0.0-000 | SEL-R |
| SRD-6.2.0.0-000 | SEL-R |
| SRD-6.3.0.0-000 | SEL-R |
| SRD-6.4.0.0-000 | SEL-R |
| SRD-7.0.0.0-000 | SEL-R |
| SRD-7.0.0.0-010 | SEL-R |
| SRD-8.0.0.0-000 | SEL-R |
| SRD-9.0.0.0-000 | SEL-R |

table 6-1: Cross reference table

# INSTRUMENTATION AND TEST EQUIPMENT

The complete list of the instrumentation used during the test shall be recorded in table (table 7-1).

| N. | EQUIPMENT |
| --- | --- |
| 1 | Power Supply 2 outputs (5V, 2,5V) |
| 2 | Power Supply 2 outputs (15V, -15V) |
| 3 | ADSP Emulator |
| 4 | Personal Computer with ADSP 21020 SDE tool |
| 5 | Personal Computer with 1355 PCI board, 1553 PCI board and Test equipment tools |
| 6 | Cable connecting Mil-Std-1553 |
| 7 | Cable connecting Spacewire interface |

table 7-1: Instrumentation and Test Equipment Table

# test procedures.

## dpu boot sw TEST PROCEDURES.

### BOOT SW Test Procedure.

| Step | Test Procedure Identifier | TR-BOOTSW –010 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the uploading of an Application Program from EEPROM. |  |  |
|  | Special Requirement | For this operation is requested an Open Box condition to connect the DSP emulator. |  |  |
|  | Procedure steps |
| 1 | Program the EEPROM mezzanine using the SW Test drivers. Dump the EEPROM contained from 0x80000000 to 0x800017ff. Insert a programmed EPROM (FIRST DPU BOOT SW ver 2.0.) on the HSO/FIRST DPU board. Power On. Connect the ADSP Emulator Reset the Board. Open the Program Window. Verify that the BOOTSW program has been uploaded in the first 1555 cells in program memory. | OK |  |
| 2 | Perform a chip reset by emulator Start program Set breakpoint before of jumping to “Application Program” Verify that the program has been uploaded dumping the PM area from 0 to 0x100 cells and from 0x4000 to 0x4acc cell and comparing it with the instruction inside the EXE file. | OK |  |

| 3 | Set a new breakpoint before of reprogramming the EEPROM Start the program Verify that the EEPROM has been cleaned and the first six pages are blanks. | OK |  |
| --- | --- | --- | --- |
| 4 | Start the program Wait until the end of program Verify that the program has been correctly performed comparing the new programmed EEPROM with the values previously dumped | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### DM Test Procedure.

| Step | Test Procedure Identifier | TR-BOOTSW –020 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify DM errors detection during initialization |  |  |
|  | Special Requirement | For this operation is requested an Open Box condition to connect the DSP emulator. |  |  |
|  | Procedure steps |
| 1 | Insert a programmed EPROM (FIRST DPU BOOT SW ver 2.0.) on the HSO/FIRST DPU board. Power On. Connect the ADSP Emulator Reset the Board. Open the Program Window and Data Window Verify that the BOOTSW program has been uploaded in the first 1555 cells in program memory. | OK |  |
| 2 | Perform a chip reset by emulator Start program Set breakpoint before of reading the data from Data memory Write the 0xFFFFFFFF data in the DM cell Start program Verify that the Boot SW detects the DM error verifying that a TM error message is sent to the FIRST TE containing the incorrect DM page address. | OK |  |
| 3 | Verify that the BOOT SW is waiting a TC from FIRST TE checking that the “Application Program” has not been also uploaded ( from 0x4000 to 0x4acc the PM contains spurious data) | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### PM Test Procedure.

| Step | Test Procedure Identifier | TR-BOOTSW –025 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify possible PM error detection during initialization |  |  |
|  | Special Requirement | For this operation is requested an Open Box condition to connect the DSP emulator. |  |  |
|  | Procedure steps |
| 1 | Insert a programmed EPROM (FIRST DPU BOOT SW ver 2.0.) on the HSO/FIRST DPU board. Detach the Emulator and reconnect in order to erase previous value in PM. Power On. Connect the ADSP Emulator Reset the Board. Open the Program Window and Data Window Verify that the BOOTSW program has been uploaded in the first 1555 cells in program memory. | OK |  |
| 2 | Perform a chip reset by emulator Start program Set breakpoint before of reading the data from Program memory Write the 0xFFFFFFFFFFFF data in the PM cell Start program Verify that the Boot SW detects the PM error verifying that a TM error message is sent to the FIRST TE containing the incorrect PM page address. | OK |  |
| 3 | Verify that the BOOT SW is waiting a TC from FIRST TE checking that the “Application Program” has not been also uploaded ( from 0x4000 to 0x4acc the PM contains spurious data) | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### EEPROM Test Procedure.

| Step | Test Procedure Identifier | TR-BOOTSW –030 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify that the “Application Software” is uploaded when an error in the first partition is found. |  |  |
|  | Special Requirement | For this operation is requested an Open Box condition to connect the DSP emulator. |  |  |
|  | Procedure steps |
| 1 | Program the EEPROM mezzanine using the SW Test drivers. Dump the EEPROM contained from 0x80000000 to 0x800017ff. Insert a programmed EPROM (FIRST DPU BOOT SW ver 2.0.) on the HSO/FIRST DPU board. Detach the Emulator and reconnect in order to erase previous value in PM. Power On. Connect the ADSP Emulator Reset the Board. Open the Program Window and Data Window Verify that the BOOTSW program has been uploaded in the first 1555 cells in program memory. | OK |  |
| 2 | Perform a chip reset by emulator Read the value at the EEPROM address 0x80000020 Write a different value (i.e 0xFFFFAAAA) at the EEPROM address 0x80000020 Set a break point before of jumping to the “Application Program” execution. Start program Verify that the program has been uploaded, dumping the PM area from 0 to 0x100 cells and from 0x4000 to 0x4acc cell and comparing it with the instruction inside the EXE file. | OK |  |

| 3 | Set a new breakpoint before of reprogramming the EEPROM Start the program Verify that the EEPROM has been cleaned and the first six pages are blanks. | OK |  |
| --- | --- | --- | --- |
| 4 | Start the program Wait until the end of program Verify that the program has been correctly performed comparing the new programmed EEPROM with the values previously dumped Verify that the values 0xFFFFAAAA at the 0x80000020 is equal to the value read at step 2 | OK |  |
| 5 | Restart the system (power off) Insert a programmed EPROM (FIRST DPU BOOT SW ver 2.0.) on the HSO/FIRST DPU board. Detach the Emulator and reconnect in order to erase previous value in PM. Power On. Connect the ADSP Emulator Reset the Board. Open the Program Window and Data Window Verify that the BOOTSW program has been uploaded in the first 1555 cells in program memory. | OK |  |
| 6 | Perform a chip reset by emulator Read the value at the EEPROM address 0x8003fc20 Write a different value (i.e 0xFFFFAAAA) at the EEPROM address 0x8003fc20 Set a break point before of jumping to the “Application Program” execution. Start program Verify that the program has been uploaded, dumping the PM area from 0 to 0x100 cells and from 0x4000 to 0x4acc cell and comparing it with the instruction inside the EXE file. | OK |  |

| 7 | Set a new breakpoint before of reprogramming the EEPROM Start the program Verify that the EEPROM has been cleaned and the first six pages are blanks. | OK |  |
| --- | --- | --- | --- |
| 8 | Start the program Wait until the end of program Verify that the program has been correctly performed comparing the new programmed EEPROM with the values previously dumped Verify that the values 0xFFFFAAAA at the 0x8003fc20 is equal to the value read at step 5 | OK |  |
| 9 | Restart the test procedure (Power off) Detach the Emulator and reconnect in order to erase previous value in PM. Power On. Connect the ADSP Emulator Reset the Board. Open the Program Window and Data Window Verify that the BOOTSW program has been uploaded in the first 1555 cells in program memory. | OK |  |
| 10 | Perform a chip reset by emulator Read the value at the EEPROM address 0x80000060 and 0x8003fcAA Write a different value (i.e 0xFFFFAAAA) at the EEPROM address 0x80000060 and 0x8003fcAA Set a break point before of jumping to the “Application Program” execution. Start program Verify that the program has not been uploaded, and the “Application Program” has not been copied in the 0x4000 to 0x4acc cells. Verify that a TM error message is generated indicating the EEPROM page address failed And the Checksum expected and computed.. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### EEPROM to PM LOAD Test Procedure.

| Step | Test Procedure Identifier | TR-BOOTSW –040 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify an error is detected during the uploading of an Application Program from EEPROM to PM. |  |  |
|  | Special Requirement | For this operation is requested an Open Box condition to connect the DSP emulator. |  |  |
|  | Procedure steps |
| 1 | Program the EEPROM mezzanine using the SW Test drivers Insert a programmed EPROM (FIRST DPU BOOT SW ver 2.0.) on the HSO/FIRST DPU board. Power On. Connect the ADSP Emulator Reset the Board. Open the Program Window. Verify that the BOOTSW program has been uploaded in the first 1555 cells in program memory. | OK |  |
| 2 | Perform a chip reset by emulator Set breakpoint before of starting the EEPROM to PM upload Start program No checks is requested | OK |  |
| 3 | Write at the EEPROM address 0x80000820 the value 0xFFFFFFFF Stat program Stop program and Verify that a TM error message is sent by means of MIL1553 to FIRST TE indicating the failed PM page upload. Verify that the “Application Program” has been partially uploaded: page 1,2 are ok page 3 is failed checking the PM content. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### DM to PM LOAD Test Procedure.

| Step | Test Procedure Identifier | TR-BOOTSW –050 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify an error is detected during the uploading of an Application Program from DM to PM. |  |  |
|  | Special Requirement | For this operation is requested an Open Box condition to connect the DSP emulator. |  |  |
|  | Procedure steps |
| 1 | Reset the EEPROM content Generate using Tcgen program the DM pages that will be uploaded Insert a programmed EPROM (FIRST DPU BOOT SW ver 2.0.) on the HSO/FIRST DPU board. Power On. Connect the ADSP Emulator Reset the Board. Open the Program Window and Data Window. Verify that the BOOTSW program has been uploaded in the first 1555 cells in program memory. | OK |  |
| 2 | Perform a chip reset by emulator Upload the DM pages in Data Memory starting from 0x00004000 Set breakpoint before of the DM test Start program No check is required | OK |  |

| 3 | Change the value in the memory cell in order to fail the DM test Start the program Verify that a TM message is sent to FIRST TE | OK |  |
| --- | --- | --- | --- |
| 4 | Send a TC in order to force the DM to PM program copy Set a breakpoint before of jumping to “Application Program” execution Verify that the “Application Program” is correctly copied at the following address: Pm 0x0 to 0x100 Pm 0x4000 to 0x4acc Dumping the PM content and comparing it with the Application program exe file | OK |  |
| 5 | Start Program Verify that the EEPROM has been reprogrammed by means of the “Application Program” uploaded | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

## 1355 DRIVER TEST PROCEDURE.

### 1355 Power On Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –010 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the correct functioning of 1355 Power On. |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On. Load on Bus Tools Software the file Power-On.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal. Off-line verification: Check in the log file Power-On-log.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A2. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### 1355 Reset Link Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –020 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the possibility to reset the SMCS332 link. |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Load on Bus Tools Software the file Reset-link.btd Run on Bus Tools the network Wait to receive the last packet from remote terminal Off-line verification: Check in the log file Reset-link.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A5. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### 1355 Time-out Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –030 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the possibility to set time-out value for the SMCS332 |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On Load on Bus Tools Software the file Time-out.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal. Off-line verification: Check in the log file Time-out.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A12. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### 1355 Open Link Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –040 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the correct functioning of 1355 Power On. |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On Load on Bus Tools Software the file Open-link.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal. Off-line verification: Check in the log file Open-link.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A2. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### 1355 Close Link Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –050 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the possibility to close each of the three SMCS links |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On Load on Bus Tools Software the file Close-link.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal Off-line verification: Check in the log file Close-link.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A2. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### 1355 Start Link As Master Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –060 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the possibility to start, as master, each of the three SMCS links using different speed values. |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On Load on Bus Tools Software the file Start-Link-as Master.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal. Off-line verification: Check in the log file Start-Link-as Master.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A5. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### 1355 Start Link as Slave Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –070 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the possibility to start, as slave, each of the three SMCS links using different speed values. |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On. Load on Bus Tools Software the file Start-Link-as-slave.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal Off-line verification: Check in the log file Start-Link-as-slave.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A5 | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### 1355 Stop Link Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –080 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the possibility to start, as slave, each of the three SMCS links using different speed values. |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On. Load on Bus Tools Software the file Start-Link-as-slave.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal Off-line verification: Check in the log file Start-Link-as-slave.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A5. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### 1355 Get Status Register Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –090 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the possibility to get the status of register for each of the three SMCS links. |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On Load on Bus Tools Software the file Get-Status-Register.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal Off-line verification: Check in the log file file Get-Status-Register.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A10. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### 1355 Write Link Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –100 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the possibility to transmit data over each of the three SMCS links |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On. Load on Bus Tools Software the file Write-Link.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal Off-line verification: Check in the log file Write-Link.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A6. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### 1355 Read Link Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –110 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the possibility to receive data over each of the three SMCS links |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On. Load on Bus Tools Software the file Read-Link.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal. Off-line verification: Check in the log file Read-Link.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A7. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### 1355 Get Link Status Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –120 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the possibility to return the current transmit/receive link status for each of the three SMCS links. |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On. Load on Bus Tools Software the file Get-Link-Status.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal. Off-line verification: Check in the log file Get-Link-Status.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A11. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### 1355 Read Packet Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –130 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the possibility to receive data over each of the three SMCS links |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On. Load on Bus Tools Software the file Read-packet.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal. Off-line verification: Check in the log file Read-packet.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A8 | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### 1355 Get Last Read Size Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –140 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the possibility to get the number of received data over each of the three SMCS links. |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On. Load on Bus Tools Software the file Get-Last-Read-Size.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal. Off-line verification: Check in the log file Get-Last-Read-Size.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A9. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### 1355 Get Last Read Write Size Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –150 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the possibility to get the number of transmitted data over each of the three SMCS links. |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On. Load on Bus Tools Software the file Get-Last-Write-Size.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal. Off-line verification: Check in the log file Get-Last-Write-Size.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A9. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### 1355 Get Last Packet Number Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –160 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the possibility to get the number of received packet over each of the three SMCS links |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On. Load on Bus Tools Software the file Get-Last-Packet-Num.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal. Off-line verification: Check in the log file Get-Last-Packet-Num.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A9 | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### 1355 Write to Board Memory Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –170 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the possibility to write in DPRAM for each of the three SMCS links. |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On. Load on Bus Tools Software the file Write-to-board Mem.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal. Off-line verification: Check in the log file Write-to-board Mem.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A15. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### 1355 Read From Board Memory Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –180 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the possibility to read from DPRAM of SMCS device |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On. Load on Bus Tools Software the file Write-to-board Mem.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal. Off-line verification: Check in the log file Write-to-board Mem.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A16 | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### 1355 Write Register Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –190 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the possibility to write in a generic register of SMCS device |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On. Load on Bus Tools Software the file Write-to-board Mem.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal. Off-line verification: Check in the log file Write-to-board Mem.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A3. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### 1355 Read Register Test Procedure.

| Step | Test Procedure Identifier | TR-DRV1355 –200 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the possibility to read the value contained in a generic register of SMCS device |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On. Load on Bus Tools Software the file Read-Reg.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal. Off-line verification: Check in the log file Read-Reg.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A4. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

## watchdog TEST PROCEDURE.

### Delay Setting Test Procedure.

| Step | Test Procedure Identifier | TR-DRVWD –010 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the correct functioning of Watchdog Delay Setting. |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment |  |  |
|  | Procedure steps |
| 1 | Power On. Load on Bus Tools Software the file WD-Delay.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal. Off-line verification: Check in the log file WD-Delay.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A17. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### Delay programming Test Procedure.

| Step | Test Procedure Identifier | TR-DRVWD –020 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the correct functioning of Watchdog Delay Programming. |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment. |  |  |
|  | Procedure steps |
| 1 | Power On. Load on Bus Tools Software the file WD-Delay-fail.btd Run on Bus Tools the network. Wait to receive the last packet from remote terminal. Off-line verification: Check in the log file WD-Delay-fail.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A18. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### Watchdog Refresh Test Procedure.

| Step | Test Procedure Identifier | TR-DRVWD –030 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the correct functioning of Watchdog refresh |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment. |  |  |
|  | Procedure steps |
| 1 | Power On Load on Bus Tools Software the file WD-Refresh.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal. Off-line verification: Check in the log file WD-Refresh.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A19 | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### Watchdog Status Test Procedure.

| Step | Test Procedure Identifier | TR-DRVWD –040 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the correct functioning of Watchdog status |  |  |
|  | Special Requirement | For this operation is requested the use of S/W Stub and Test Equipment. |  |  |
|  | Procedure steps |
| 1 | Power On. Load on Bus Tools Software the file WD-Status.btd. Run on Bus Tools the network. Wait to receive the last packet from remote terminal. Off-line verification: Check in the log file WD-Status.bmd the following: 1) at what function the packet answer are shown in ID field. 2) the success are shown in Error Code field. If Error Code is different from zero, the function is failed. To find error condition see Annex C. 3) the packet size is shown in third word of packet. For several information about the other packet’s word see Annex A20. | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

## MIL-STD 1553 SW DRIVER TEST PROCEDURE

### OPen MIL-STD 1553 CHANNEL

| Step | Test Procedure Identifier | TR-DRV1553 –010 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the configuration of the MIL register and look up table |  |  |
|  | Special Requirement | . |  |  |
|  | Procedure steps |
| 1 | Upload the MIL-STD-1553 SW test using the ADSP emulator Connect the MIL1553 between board and Test Equipment and start the CONDOR BUS TOOL Program Set Remote terminal = 7 Set breakpoint after the Open procedure Start the program Verify that the Mil registers are configured as defined in the specification The DDC chip is configured as Remote Terminal | OK |  |

| 2 | Set a new breakpoint after the mil configuration procedure Verify that the Mil registers are configured as defined in the specification The Look Up Table as the following configuration The SA 10, 11-14, 27 Rx message has been configured pointing to Mil1553 memory free The SA 10,11-26,27 Tx message has been configured pointing to Mil1553 memory free The related SACW has been configured the message are configured in buffer message mode/or single buffer mode Verify that the pointed memory space are not overlapped but they are correctly allocated Verify that the Interrupt on Broadcast synchronize message mode code with data is enabled Verify that the memory configuration of the MIL follows the Mil DDC specification. | OK |  |
| --- | --- | --- | --- |
| 3 | Set breakpoint after the Rtrun procedure Verify that the Mil Stack memory is cleared 0x8F000000 0x80000100 | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### TX MIL-STD 1553 MESSAGE

| Step | Test Procedure Identifier | TR-DRV1553 –020 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the Tx messages transmission |  |  |
|  | Special Requirement | . |  |  |
|  | Procedure steps |
| 1 | Upload the MIL-STD-1553 SW test using the ADSP emulator Connect the MIL1553 between board and Test Equipment and start the CONDOR BUS TOOL Program Set Remote terminal = 7 Set breakpoint after the Open procedure Start the program Set the CONDOR BUS TOOL Tx messages in order to acquire the SA 10, 11-26, 27 message Verify that the messages are correctly received (no random value are acquired) Verify that the messages in the SA 11- 26 are composed of 32 words Verify that the messages in the SA 10, 27 are composed of 2 words | OK |  |
| 2 | Acquire Tx messages by means of the CONDOR BUS TOOLS Verify that the messages are correctly received (the value are incremented with respect to the Previous acquisition) Verify that the messages in the SA 11- 26 are composed of 32 words Verify that the messages in the SA 10, 27 are composed of 2 words Verify stopping the emulator that MIL1553 Stack memory contains the block message words | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### RX MIL-STD 1553 MESSAGE

| Step | Test Procedure Identifier | TR-DRV1553 –030 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the Rx messages reception |  |  |
|  | Special Requirement | . |  |  |
|  | Procedure steps |
| 1 | Upload the MIL-STD-1553 SW test using the ADSP emulator Connect the MIL1553 between board and Test Equipment and start the CONDOR BUS TOOL Program Set Remote terminal = 7 Set breakpoint after the Open procedure Start the program Set the CONDOR BUS TOOL Rx messages in order to acquire the SA 10, 11-24, 27 message Verify that the messages are correctly transmitted to the ADSP Board checking the MIL DDC memory Verify that the messages in the SA 11- 26 are composed of 32 words Verify that the messages in the SA 10, 27 are composed of 2 words | OK |  |
| 2 | Transmit Rx messages by means of the CONDOR BUS TOOLS Verify that the messages are correctly transmitted to the ADSP Board checking the MIL DDC memory Verify that the messages in the SA 11- 26 are composed of 32 words Verify that the messages in the SA 10, 27 are composed of 2 words Verify stopping the emulator that MIL1553 Stack memory contains the block message words | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### CLOSE MIL-STD CHANNEL

| Step | Test Procedure Identifier | TR-DRV1553 –040 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the Rx messages reception |  |  |
|  | Special Requirement | . |  |  |
|  | Procedure steps |
| 1 | Upload the MIL-STD-1553 SW test using the ADSP emulator Connect the MIL1553 between board and Test Equipment and start the CONDOR BUS TOOL Program Set Remote terminal = 7 Set breakpoint after the Open procedure Start the program Send and Acquire Rx and Tx MIL messages Verify that all the messages are received SA Rx 10,11-14,27 SA Tx 10,11,26,27 | OK |  |
| 2 | Exit the program Verify that the Mil register are reset | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

## EEPROM DRIVER TEST PROCEDURE

### DELETE EEPROM SEGMENT

| Step | Test Procedure Identifier | TR-DRVEPRM –010 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Deleting of EEPROM segment |  |  |
|  | Special Requirement | . |  |  |
|  | Procedure steps |
| 1 | Upload the EEPROM test program using the ADSP emulator Set a breakpoint after a Delete Segment function call Write 10 times the 0xFFFFFFFF value beginning from the 0x80000000 address Start the program Verify (when the breakpoint is stricken ) that the segment beginning at 0x80000000 until 0x800003FF address is cleaned | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### WRITE EEPROM CELL

| Step | Test Procedure Identifier | TR-DRVEPRM –020 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Write EEPROM single cell inside the segment |  |  |
|  | Special Requirement | . |  |  |
|  | Procedure steps |
| 1 | Upload the EEPROM test program using the ADSP emulator Set a breakpoint after a write segment cell function call Start the program Verify (when the breakpoint is stricken ) that the segment beginning at 0x80000C00 until 0x80000FFF address is written register the frame check sequence at the 0x80000C06 address and the value at 0x8000C17 | OK |  |
| 2 | Set a breakpoint after the “write eeprom cell” function call Start program Verify that the 0xFFFFFFFF value is written at 0x80000C17 address and the DM Frame Check Sequence and PM Frame Check Sequence are changed with respect to the previous value | OK |  |
| 3 | Set a Breakpoint after the “write eeprom cell” function call The original value of the segment is written at 0x80000c17 address Start program Verify that the 0x00000010 value is written at 0x80000C17 Verify the DM Frame Check sequence and PM Frame sequence are the same of the step 1 | OK |  |

| 4 | Set a breakpoint before the “write eeprom cell” function call which writes the value 0xFFFFFFFF at the 0x80000C06 Read the value in 0x80000c06 Start Program No check is required | OK |  |
| --- | --- | --- | --- |
| 5 | Set breakpoint after the “write eeprom cell” function call Verify that the 0xFFFFFFFF is written at 0x80000c06 address; Verify that the DM frame check sequence is changed with respect to value reported in step 4 Verify that the PM check sequence is equal to the value reported in Step 4 | OK |  |
| 6 | Write the original value at the 0x80000C06 Verify that DM FCS is equal to value reported in step 4 Verify that PM FCS is equal to the value reported in step 4 | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### DELETE EEPROM CELL

| Step | Test Procedure Identifier | TR-DRVEPRM –020 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Deleting of EEPROM single cell inside a segment |  |  |
|  | Special Requirement | . |  |  |
|  | Procedure steps |
| 1 | Upload the EEPROM test program using the ADSP emulator Set a breakpoint after a write segment cell function call Start the program Verify that the segment beginning at 0x80000C00 until 0x80000FFF address is written register the frame check sequence at the 0x80000C06 address and the value at 0x8000C17 | OK |  |
| 2 | Set a breakpoint after the “delete eeprom cell” function call Start program Verify that the 0x000000000 value is written at 0x80000C17 address and the DM Frame Check Sequence and PM Frame Check Sequence are changed with respect to the previous value | OK |  |
| 3 | Set a Breakpoint after the “write eeprom cell” function call The original value of the segment is written at 0x80000c17 address Start program Verify that the 0x00000010 value is written at 0x80000C17 Verify the DM Frame Check sequence and PM Frame sequence are the same of the step 1 | OK |  |

| 4 | Set a breakpoint before the “delete eeprom cell” function call which writes the value 0x00000000 at the 0x80000C06 Read the value in 0x80000c06 Start Program No check is required | OK |  |
| --- | --- | --- | --- |
| 5 | Set breakpoint after the “delete eeprom cell” function call Verify that the 0x00000000 is written at 0x80000c06 address; Verify that the DM frame check sequence is changed with respect to value reported in step 4 Verify that the PM check sequence is equal to the value reported in Step 4 | OK |  |
| 6 | Write the original value at the 0x80000C06 Verify that DM FCS is equal to value reported in step 4 Verify that PM FCS is equal to the value reported in step 4 | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### WRITE EEPROM SEGMENT

| Step | Test Procedure Identifier | TR-DRVEPRM –030 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify the EEPROM segment write |  |  |
|  | Special Requirement | . |  |  |
|  | Procedure steps |
| 1 | Upload the EEPROM test program using the ADSP emulator Set a breakpoint after a Delete Segment function call Start the program Verify that the segment beginning at 0x80000C00 until 0x80000FFF address is cleaned | OK |  |
| 2 | Set breakpoint after “write segment function” Start Program Verify that a EEPROM segment is written at 0x80000C00 until xù0x80000FFF Verify that value of the segment are incremented by one starting from 0x8000C07 Verify that the first six word are the same defined inside the header | OK |  |

|  | Verify that in the header are included the field as follow current page Total Page NextPage in EEPROM Application S/W start address Application S/W Frame Check Sequence PM start address PM length DM FCS PM FCS Boot Option Verify that the word at 0x80000C05 address is the PM FCS (MSB 16 bits) and DM FCS (LSB 16 bits) | OK |  |
| --- | --- | --- | --- |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### ENABLE/DISABLE EEPROM PROTECTION

| Step | Test Procedure Identifier | TR-DRVEPRM –040 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Verify Enable/Disable EEPROM protection |  |  |
|  | Special Requirement | . |  |  |
|  | Procedure steps |
| 1 | Upload the EEPROM test program using the ADSP emulator Set a breakpoint after the “Enable Protection EEPROM” function call Verify that is possible to write a random data in EEPROM using the emulator Start the program Verify that is no more possible to write a data in EEPROM (EEPROM is protected) | OK |  |
| 2 | Set breakpoint after the “Disable Protection” function call Verify that is possible to write in EEPROM the data | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

### COPY PROGRAM IN EEPROM

| Step | Test Procedure Identifier | TR-DRVEPRM –050 | Results | Remarks |
| --- | --- | --- | --- | --- |
|  | Purpose | Uploading in EEPROM of a generic program in Program Memory |  |  |
|  | Special Requirement | . |  |  |
|  | Procedure steps |
| 1 | Upload the EEPROM test program using the ADSP emulator Start the program Wait the end of program | OK |  |
| 2 | Verify that the first EEPROM page is written starting from 0x80000000 address Verify that the header has the following values PM address = 0000 PM length = 0x100 Current Eeprom page = 1 Total Eeprom pages = 6 Next Eeprom page = 0x80000400 Verify that in the segment are recorded the first 256 instructions (interrupt table) (Primary boot) | OK |  |
| 3 | Verify that the Last EEPROM page is written starting from 0x8003FC00 address and the content is the same of the page in step 2 Verify that the header has the following values PM address = 0000 PM length = 0x100 Current Eeprom page = 1 Total Eeprom pages = 6 Next Eeprom page = 0x80000400 Verify that in the segment are recorded the first 256 instructions (interrupt table) (secondary Boot) | OK |  |

| 4 | Verify that the EEPROM page is written starting from 0x8003FC00 address Verify that the header has the following values PM address = 4000 PM length = 0x2A6 Current Eeprom page = 2 Total Eeprom pages = 6 Next Eeprom page = 0x80000800 Verify that in the segment are recorded 0x2A6 instruction starting from PM address 0x4000 | OK |  |
| --- | --- | --- | --- |
| 5 | Verify that the EEPROM page is written starting from 0x8003FC00 address Verify that the header has the following values PM address = 42A6 PM length = 0x2A6 Current Eeprom page = 3 Total Eeprom pages = 6 Next Eeprom page = 0x80000C00 Verify that in the segment are recorded 0x2A6 instruction starting from PM address 0x42A6 | OK |  |

| 6 | Verify that the EEPROM page is written starting from 0x8003FC00 address Verify that the header has the following values PM address = 454C PM length = 0x2A6 Current Eeprom page = 4 Total Eeprom pages = 6 Next Eeprom page = 0x80001000 Verify that in the segment are recorded 0x2A6 instruction starting from PM address 0x454C | OK |  |
| --- | --- | --- | --- |
| 7 | Verify that the EEPROM page is written starting from 0x8003FC00 address Verify that the header has the following values PM address = 47F2 PM length = 0x2A6 Current Eeprom page = 5 Total Eeprom pages = 6 Next Eeprom page = 0x80000C00 Verify that in the segment are recorded 0x2A6 instruction starting from PM address 0x47F2 | OK |  |
| Date 28/04/2002 | Test Conductor A. Bertoli | P. Assurance S. Legramandi |

# :	1553 RETURNED PACKETS FORMAT AFTER 1355 COMMAND.

## :	LEGENDA.

## :	POWER-ON, OPEN LINK AND CLOSE LINK RETURNED PACKET.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| Power-on | 1 | ID |  |
| Open | 2 | Error Code |  |
| Close | 3 | Packet_Size |  |
|  | 4 | Start Addr High |  |
|  | 5 | Start Addr Low |  |
|  | 6 | End Addr High |  |
|  | 7 | End Addr Low |  |
|  | 8 | i_status | Start SW_Architecture |
|  | 9 | i_state |  |
|  | 10 | li_ByteSize_TX H |  |
|  | 11 | li_ByteSize_TX L |  |
|  | 12 | li_ByteSize_RX H |  |
|  | 13 | li_ByteSize_RX L |  |
|  | 14 | li_packets H |  |
|  | 15 | li_packets L |  |
|  | 16 | d_Flag |  |
|  | 17 | j_Timeout |  |
|  | 18 | None | End SW_Architecture |
|  | 19 | Start Addr High |  |
|  | 20 | Start Addr Low |  |
|  | 21 | End Addr High |  |
|  | 22 | End Addr Low |  |
|  | 23 | SICR high | Start: General Registers |
|  | 24 | SICR Low |  |
|  | 25 | TRS_CTRL H |  |
|  | 26 | TRS_CTRL L |  |
|  | 27 | RT_CTRL H |  |
|  | 28 | RT_CTRL L |  |
|  | 29 | ISR H |  |
|  | 30 | ISR L |  |
|  | 31 | IMR H |  |
|  | 32 | IMR L |  |
|  | 33 | COMI_CS0R H |  |
|  | 34 | COMI_CS0R L |  |
|  | 35 | COMI_ACR H |  |
|  | 36 | COMI_ACR L |  |
|  | 37 | PRCIR H |  |
|  | 38 | PRCIR L | End: General Registers |

## :	WRITE REGISTERS RETURNED PACKET.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| WriteReg | 1 | ID |  |
|  | 2 | Error Code |  |
|  | 3 | Packet_Size |  |
|  | 4 | Start Addr High |  |
|  | 5 | Start Addr Low |  |
|  | 6 | End Addr High |  |
|  | 7 | End Addr Low |  |
|  | 8 | CH1_COMICFG H | Start: Registers |
|  | 9 | CH1_COMICFG L | End: Registers |

## :	READ REGISTERS RETURNED PACKET.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| ReadReg | 1 | ID |  |
|  | 2 | Error Code |  |
|  | 3 | Packet_Size |  |
|  | 4 | Value Read H | Start: read |
|  | 5 | Value Read L | End: read |
|  | 6 | Start Addr High |  |
|  | 7 | Start Addr Low |  |
|  | 8 | End Addr High |  |
|  | 9 | End Addr Low |  |
|  | 10 | CH1_COMICFG H | Start: Registers |
|  | 11 | CH1_COMICFG L | End: Registers |

:	START LINK MASTER AND SLAVE, STOP LINK AND RESET LINK RETURNED PACKETS.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| Start link | 1 | ID |  |
| Master | 2 | Error Code |  |
| Start link | 3 | Packet_Size |  |
| Slave | 4 | Start Addr High |  |
| Stop link | 5 | Start Addr Low |  |
| Reset link | 6 | End Addr High |  |
|  | 7 | End Addr Low |  |
|  | 8 | i_status | Start SW_Architecture |
|  | 9 | i_state |  |
|  | 10 | li_ByteSize_TX H |  |
|  | 11 | li_ByteSize_TX L |  |
|  | 12 | li_ByteSize_RX H |  |
|  | 13 | li_ByteSize_RX L |  |
|  | 14 | li_packets H |  |
|  | 15 | li_packets L |  |
|  | 16 | d_Flag |  |
|  | 17 | j_Timeout |  |
|  | 18 | None | End SW_Architecture |
|  | 19 | Start Addr High |  |
|  | 20 | Start Addr Low |  |
|  | 21 | End Addr High |  |
|  | 22 | End Addr Low |  |
|  | 23 | SICR high | Start: Registers |
|  | 24 | SICR Low |  |
|  | 25 | TRS_CTRL H |  |
|  | 26 | TRS_CTRL L |  |
|  | 27 | RT_CTRL H |  |
|  | 28 | RT_CTRL L |  |
|  | 29 | ISR H |  |
|  | 30 | ISR L |  |
|  | 31 | IMR H |  |
|  | 32 | IMR L |  |
|  | 33 | COMI_CS0R H |  |
|  | 34 | COMI_CS0R L |  |
|  | 35 | COMI_ACR H |  |
|  | 36 | COMI_ACR L |  |
|  | 37 | PRCIR H |  |
|  | 38 | PRCIR L | End: Registers |
|  | 39 | Start Addr High |  |
|  | 40 | Start Addr Low |  |
|  | 41 | End Addr High |  |
|  | 42 | End Addr Low |  |
|  | 43 | CHx_DSM_MODR H | Start Link Registers |
|  | 44 | CHx_DSM_MODR L |  |
|  | 45 | CHx_DSM_CMDR H |  |
|  | 46 | CHx_DSM_CMDR L |  |
|  | 47 | CHx_DSM_STAR H |  |
|  | 48 | CHx_DSM_STAR L |  |
|  | 49 | CHx_DSM_TSTR H |  |
|  | 50 | CHx_DSM_TSTR L |  |
|  | 51 | CHx_ADDR H |  |
|  | 52 | CHx_ADDR L |  |

|  | 53 | CHx_RT_ADDR H |  |
| --- | --- | --- | --- |
|  | 54 | CHx_RT_ADDR L |  |
|  | 55 | CHx_PR_STAR H |  |
|  | 56 | CHx_PR_STAR L |  |
|  | 57 | CHx_CNTRL1 H |  |
|  | 58 | CHx_CNTRL1 L |  |
|  | 59 | CHx_CNTRL2 H |  |
|  | 60 | CHx_CNTRL2 L |  |
|  | 61 | CHx_HTID H |  |
|  | 62 | CHx_HTID L |  |
|  | 63 | CHx_HCNTRL H |  |
|  | 64 | CHx_HCNTRL L |  |
|  | 65 | CHx_ESR1 H |  |
|  | 66 | CHx_ESR1 L |  |
|  | 67 | CHx_ESR2 H |  |
|  | 68 | CHx_ESR2 L |  |
|  | 69 | CHx_COMICFG H |  |
|  | 70 | CHx_COMICFG L |  |
|  | 71 | CHx_TX_SAR H |  |
|  | 72 | CHx_TX_SAR L |  |
|  | 73 | CHx_TX_EAR H |  |
|  | 74 | CHx_TX_EAR L |  |
|  | 75 | CHx_TX_CAR H |  |
|  | 76 | CHx_TX_CAR L |  |
|  | 77 | CHx_TX_FIFO H |  |
|  | 78 | CHx_TX_FIFO L |  |
|  | 79 | CHx_TX_EOPB H |  |
|  | 80 | CHx_TX_EOPB L |  |
|  | 81 | CHx_RX_SAR H |  |
|  | 82 | CHx_RX_SAR L |  |
|  | 83 | CHx_RX_EAR H |  |
|  | 84 | CHx_RX_EAR L |  |
|  | 85 | CHx_RX_CAR H |  |
|  | 86 | CHx_RX_CAR L |  |
|  | 87 | CHx_RX_FIFO H |  |
|  | 88 | CHx_RX_FIFO L |  |
|  | 89 | CHx_STAR H |  |
|  | 90 | CHx_STAR L | End Link Registers |

## :	WRITE LINK RETURNED PACKET.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| Write link | 1 | ID |  |
|  | 2 | Error Code |  |
|  | 3 | Packets_Size |  |
|  | 4 | Start Addr High |  |
|  | 5 | Start Addr Low |  |
|  | 6 | End Addr High |  |
|  | 7 | End Addr Low |  |
|  | 8 | i_status | Start SW_Architecture |
|  | 9 | i_state |  |
|  | 10 | li_ByteSize_TX H |  |
|  | 11 | li_ByteSize_TX L |  |
|  | 12 | li_ByteSize_RX H |  |
|  | 13 | li_ByteSize_RX L |  |
|  | 14 | li_packets H |  |
|  | 15 | li_packets L |  |
|  | 16 | d_Flag |  |
|  | 17 | j_Timeout |  |
|  | 18 | None | End SW_Architecture |
|  | 19 | Start Addr High |  |
|  | 20 | Start Addr Low |  |
|  | 21 | End Addr High |  |
|  | 22 | End Addr Low |  |
|  | 23 | SICR high | Start: General Registers |
|  | 24 | SICR Low |  |
|  | 25 | TRS_CTRL H |  |
|  | 26 | TRS_CTRL L |  |
|  | 27 | RT_CTRL H |  |
|  | 28 | RT_CTRL L |  |
|  | 29 | ISR H |  |
|  | 30 | ISR L |  |
|  | 31 | IMR H |  |
|  | 32 | IMR L |  |
|  | 33 | COMI_CS0R H |  |
|  | 34 | COMI_CS0R L |  |
|  | 35 | COMI_ACR H |  |
|  | 36 | COMI_ACR L |  |
|  | 37 | PRCIR H |  |
|  | 38 | PRCIR L | End: General Registers |
|  | 39 | Start Addr High |  |
|  | 40 | Start Addr Low |  |
|  | 41 | End Addr High |  |
|  | 42 | End Addr Low |  |
|  | 43 | CHx_DSM_MODR H | Start: Link Registers |
|  | 44 | CHx_DSM_MODR L |  |
|  | 45 | CHx_DSM_CMDR H |  |
|  | 46 | CHx_DSM_CMDR L |  |
|  | 47 | CHx_DSM_STAR H |  |
|  | 48 | CHx_DSM_STAR L |  |
|  | 49 | CHx_DSM_TSTR H |  |
|  | 50 | CHx_DSM_TSTR L |  |
|  | 51 | CHx_ADDR H |  |
|  | 52 | CHx_ADDR L |  |
|  | 53 | CHx_RT_ADDR H |  |
|  | 54 | CHx_RT_ADDR L |  |
|  | 55 | CHx_PR_STAR H |  |
|  | 56 | CHx_PR_STAR L |  |
|  | 57 | CHx_CNTRL1 H |  |
|  | 58 | CHx_CNTRL1 L |  |
|  | 59 | CHx_CNTRL2 H |  |
|  | 60 | CHx_CNTRL2 L |  |
|  | 61 | CHx_HTID H |  |
|  | 62 | CHx_HTID L |  |
|  | 63 | CHx_HCNTRL H |  |
|  | 64 | CHx_HCNTRL L |  |
|  | 65 | CHx_ESR1 H |  |
|  | 66 | CHx_ESR1 L |  |
|  | 67 | CHx_ESR2 H |  |
|  | 68 | CHx_ESR2 L |  |
|  | 69 | CHx_COMICFG H |  |
|  | 70 | CHx_COMICFG L |  |
|  | 71 | CHx_TX_SAR H |  |
|  | 72 | CHx_TX_SAR L |  |
|  | 73 | CHx_TX_EAR H |  |
|  | 74 | CHx_TX_EAR L |  |
|  | 75 | CHx_TX_CAR H |  |
|  | 76 | CHx_TX_CAR L |  |
|  | 77 | CHx_TX_FIFO H |  |
|  | 78 | CHx_TX_FIFO L |  |
|  | 79 | CHx_TX_EOPB H |  |
|  | 80 | CHx_TX_EOPB L |  |
|  | 81 | CHx_RX_SAR H |  |
|  | 82 | CHx_RX_SAR L |  |
|  | 83 | CHx_RX_EAR H |  |
|  | 84 | CHx_RX_EAR L |  |
|  | 85 | CHx_RX_CAR H |  |
|  | 86 | CHx_RX_CAR L |  |
|  | 87 | CHx_RX_FIFO H |  |
|  | 88 | CHx_RX_FIFO L |  |
|  | 89 | CHx_STAR H |  |
|  | 90 | CHx_STAR L | End: Link Registers |
|  | 91 | Start Addr High |  |
|  | 92 | Start Addr Low |  |
|  | 93 | End Addr High |  |
|  | 94 | End Addr Low |  |
|  | 95 | DPRAM | Start DPRAM channel |
|  | ………………. | DPRAM |  |
|  | 132 | DPRAM | End DPRAM channel |

## :	READ LINK RETURNED PACKET.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| Read link | 1 | ID |  |
|  | 2 | Error Code |  |
|  | 3 | Packets_Size |  |
|  | 4 | Start Addr High |  |
|  | 5 | Start Addr Low |  |
|  | 6 | End Addr High |  |
|  | 7 | End Addr Low |  |
|  | 8 | i_status | Start SW_Architecture |
|  | 9 | i_state |  |
|  | 10 | li_ByteSize_TX H |  |
|  | 11 | li_ByteSize_TX L |  |
|  | 12 | li_ByteSize_RX H |  |
|  | 13 | li_ByteSize_RX L |  |
|  | 14 | li_packets H |  |
|  | 15 | li_packets L |  |
|  | 16 | d_Flag |  |
|  | 17 | j_Timeout |  |
|  | 18 | None | End SW_Architecture |
|  | 19 | Start Addr High |  |
|  | 20 | Start Addr Low |  |
|  | 21 | End Addr High |  |
|  | 22 | End Addr Low |  |
|  | 23 | SICR high | Start: Registers |
|  | 24 | SICR Low |  |
|  | 25 | TRS_CTRL H |  |
|  | 26 | TRS_CTRL L |  |
|  | 27 | RT_CTRL H |  |
|  | 28 | RT_CTRL L |  |
|  | 29 | ISR H |  |
|  | 30 | ISR L |  |
|  | 31 | IMR H |  |
|  | 32 | IMR L |  |
|  | 33 | COMI_CS0R H |  |
|  | 34 | COMI_CS0R L |  |
|  | 35 | COMI_ACR H |  |
|  | 36 | COMI_ACR L |  |
|  | 37 | PRCIR H |  |
|  | 38 | PRCIR L | End: Registers |
|  | 39 | Start Addr High |  |
|  | 40 | Start Addr Low |  |
|  | 41 | End Addr High |  |
|  | 42 | End Addr Low |  |
|  | 43 | CHx_DSM_MODR H | Start Link Registers |
|  | 44 | CHx_DSM_MODR L |  |
|  | 45 | CHx_DSM_CMDR H |  |
|  | 46 | CHx_DSM_CMDR L |  |
|  | 47 | CHx_DSM_STAR H |  |
|  | 48 | CHx_DSM_STAR L |  |
|  | 49 | CHx_DSM_TSTR H |  |
|  | 50 | CHx_DSM_TSTR L |  |
|  | 51 | CHx_ADDR H |  |
|  | 52 | CHx_ADDR L |  |
|  | 53 | CHx_RT_ADDR H |  |
|  | 54 | CHx_RT_ADDR L |  |
|  | 55 | CHx_PR_STAR H |  |
|  | 56 | CHx_PR_STAR L |  |
|  | 57 | CHx_CNTRL1 H |  |
|  | 58 | CHx_CNTRL1 L |  |
|  | 59 | CHx_CNTRL2 H |  |
|  | 60 | CHx_CNTRL2 L |  |
|  | 61 | CHx_HTID H |  |
|  | 62 | CHx_HTID L |  |
|  | 63 | CHx_HCNTRL H |  |
|  | 64 | CHx_HCNTRL L |  |
|  | 65 | CHx_ESR1 H |  |
|  | 66 | CHx_ESR1 L |  |
|  | 67 | CHx_ESR2 H |  |
|  | 68 | CHx_ESR2 L |  |
|  | 69 | CHx_COMICFG H |  |
|  | 70 | CHx_COMICFG L |  |
|  | 71 | CHx_TX_SAR H |  |
|  | 72 | CHx_TX_SAR L |  |
|  | 73 | CHx_TX_EAR H |  |
|  | 74 | CHx_TX_EAR L |  |
|  | 75 | CHx_TX_CAR H |  |
|  | 76 | CHx_TX_CAR L |  |
|  | 77 | CHx_TX_FIFO H |  |
|  | 78 | CHx_TX_FIFO L |  |
|  | 79 | CHx_TX_EOPB H |  |
|  | 80 | CHx_TX_EOPB L |  |
|  | 81 | CHx_RX_SAR H |  |
|  | 82 | CHx_RX_SAR L |  |
|  | 83 | CHx_RX_EAR H |  |
|  | 84 | CHx_RX_EAR L |  |
|  | 85 | CHx_RX_CAR H |  |
|  | 86 | CHx_RX_CAR L |  |
|  | 87 | CHx_RX_FIFO H |  |
|  | 88 | CHx_RX_FIFO L |  |
|  | 89 | CHx_STAR H |  |
|  | 90 | CHx_STAR L | End Link Registers |
|  | 91 | Start Addr High |  |
|  | 92 | Start Addr Low |  |
|  | 93 | End Addr High |  |
|  | 94 | End Addr Low |  |
|  | 95 | DPRAM | Start DPRAM channel |
|  | ……………. | DPRAM |  |
|  | 132 | DPRAM | End DPRAM channel |

## :	READ PACKET RETURNED PACKET.

| Functions | Word | Packets format | Memdump Zone | Note |
| --- | --- | --- | --- | --- |
| Read packets | 1 | ID |  | Packets number = 3 |
|  | 2 | Error Code |  |  |
|  | 3 | Packets_Size |  |  |
|  | 4 | Start Addr High |  |  |
|  | 5 | Start Addr Low |  |  |
|  | 6 | End Addr High |  |  |
|  | 7 | End Addr Low |  |  |
|  | 8 | i_status | Start SW_Architecture |  |
|  | 9 | i_state |  |  |
|  | 10 | li_ByteSize_TX H |  |  |
|  | 11 | li_ByteSize_TX L |  |  |
|  | 12 | li_ByteSize_RX H |  |  |
|  | 13 | li_ByteSize_RX L |  |  |
|  | 14 | li_packets H |  |  |
|  | 15 | li_packets L |  |  |
|  | 16 | d_Flag |  |  |
|  | 17 | j_Timeout |  |  |
|  | 18 | None | End SW_Architecture |  |
|  | 19 | Start Addr High |  |  |
|  | 20 | Start Addr Low |  |  |
|  | 21 | End Addr High |  |  |
|  | 22 | End Addr Low |  |  |
|  | 23 | SICR high | Start: Registers |  |
|  | 24 | SICR Low |  |  |
|  | 25 | TRS_CTRL H |  |  |
|  | 26 | TRS_CTRL L |  |  |
|  | 27 | RT_CTRL H |  |  |
|  | 28 | RT_CTRL L |  |  |
|  | 29 | ISR H |  |  |
|  | 30 | ISR L |  |  |
|  | 31 | IMR H |  |  |
|  | 32 | IMR L |  |  |
|  | 33 | COMI_CS0R H |  |  |
|  | 34 | COMI_CS0R L |  |  |
|  | 35 | COMI_ACR H |  |  |
|  | 36 | COMI_ACR L |  |  |
|  | 37 | PRCIR H |  |  |
|  | 38 | PRCIR L | End: Registers |  |
|  | 39 | Start Addr High |  |  |
|  | 40 | Start Addr Low |  |  |
|  | 41 | End Addr High |  |  |
|  | 42 | End Addr Low |  |  |
|  | 43 | CHx_DSM_MODR H | Start Link Registers |  |
|  | 44 | CHx_DSM_MODR L |  |  |
|  | 45 | CHx_DSM_CMDR H |  |  |
|  | 46 | CHx_DSM_CMDR L |  |  |
|  | 47 | CHx_DSM_STAR H |  |  |
|  | 48 | CHx_DSM_STAR L |  |  |
|  | 49 | CHx_DSM_TSTR H |  |  |
|  | 50 | CHx_DSM_TSTR L |  |  |
|  | 51 | CHx_ADDR H |  |  |
|  | 52 | CHx_ADDR L |  |  |
|  | 53 | CHx_RT_ADDR H |  |  |
|  | 54 | CHx_RT_ADDR L |  |  |
|  | 55 | CHx_PR_STAR H |  |  |
|  | 56 | CHx_PR_STAR L |  |  |
|  | 57 | CHx_CNTRL1 H |  |  |
|  | 58 | CHx_CNTRL1 L |  |  |
|  | 59 | CHx_CNTRL2 H |  |  |
|  | 60 | CHx_CNTRL2 L |  |  |
|  | 61 | CHx_HTID H |  |  |
|  | 62 | CHx_HTID L |  |  |
|  | 63 | CHx_HCNTRL H |  |  |
|  | 64 | CHx_HCNTRL L |  |  |
|  | 65 | CHx_ESR1 H |  |  |
|  | 66 | CHx_ESR1 L |  |  |
|  | 67 | CHx_ESR2 H |  |  |
|  | 68 | CHx_ESR2 L |  |  |
|  | 69 | CHx_COMICFG H |  |  |
|  | 70 | CHx_COMICFG L |  |  |
|  | 71 | CHx_TX_SAR H |  |  |
|  | 72 | CHx_TX_SAR L |  |  |
|  | 73 | CHx_TX_EAR H |  |  |
|  | 74 | CHx_TX_EAR L |  |  |
|  | 75 | CHx_TX_CAR H |  |  |
|  | 76 | CHx_TX_CAR L |  |  |
|  | 77 | CHx_TX_FIFO H |  |  |
|  | 78 | CHx_TX_FIFO L |  |  |
|  | 79 | CHx_TX_EOPB H |  |  |
|  | 80 | CHx_TX_EOPB L |  |  |
|  | 81 | CHx_RX_SAR H |  |  |
|  | 82 | CHx_RX_SAR L |  |  |
|  | 83 | CHx_RX_EAR H |  |  |
|  | 84 | CHx_RX_EAR L |  |  |
|  | 85 | CHx_RX_CAR H |  |  |
|  | 86 | CHx_RX_CAR L |  |  |
|  | 87 | CHx_RX_FIFO H |  |  |
|  | 88 | CHx_RX_FIFO L |  |  |
|  | 89 | CHx_STAR H |  |  |
|  | 90 | CHx_STAR L | End Link Registers |  |
|  | 91 | Start Addr High |  |  |
|  | 92 | Start Addr Low |  |  |
|  | 93 | End Addr High |  |  |
|  | 94 | End Addr Low |  |  |
|  | 95 | rx_pbuffer | Start rx_pbuffer |  |
|  | 96 | rx_pbuffer |  |  |
|  | 97 | rx_pbuffer |  |  |
|  | 98 | rx_pbuffer |  |  |
|  | 99 | rx_pbuffer |  |  |
|  | 100 | rx_pbuffer |  |  |
|  | 101 | rx_pbuffer |  |  |
|  | 102 | rx_pbuffer |  |  |
|  | 103 | rx_pbuffer |  |  |
|  | 104 | rx_pbuffer |  |  |
|  | 105 | rx_pbuffer |  |  |
|  | 106 | rx_pbuffer |  |  |
|  | 107 | rx_pbuffer |  |  |
|  | 108 | rx_pbuffer |  |  |
|  | 109 | rx_pbuffer |  |  |
|  | 110 | rx_pbuffer |  |  |
|  | 111 | rx_pbuffer |  |  |
|  | 112 | rx_pbuffer |  |  |
|  | 113 | rx_pbuffer |  |  |
|  | 114 | rx_pbuffer |  |  |
|  | 115 | rx_pbuffer |  |  |
|  | 116 | rx_pbuffer |  |  |
|  | 117 | rx_pbuffer |  |  |
|  | 118 | rx_pbuffer |  |  |
|  | 119 | rx_pbuffer |  |  |
|  | 120 | rx_pbuffer |  |  |
|  | 121 | rx_pbuffer |  |  |
|  | 122 | rx_pbuffer |  |  |
|  | 123 | rx_pbuffer |  |  |
|  | 124 | rx_pbuffer |  |  |
|  | 125 | rx_pbuffer |  |  |
|  | 126 | rx_pbuffer |  |  |
|  | 127 | rx_pbuffer |  |  |
|  | 128 | rx_pbuffer |  |  |
|  | 129 | rx_pbuffer |  |  |
|  | 130 | rx_pbuffer |  |  |
|  | 131 | rx_pbuffer |  |  |
|  | 132 | rx_pbuffer |  |  |
|  | 133 | rx_pbuffer |  |  |
|  | 134 | rx_pbuffer |  |  |
|  | 135 | rx_pbuffer |  |  |
|  | 136 | rx_pbuffer |  |  |
|  | 137 | rx_pbuffer |  |  |
|  | 138 | rx_pbuffer |  |  |
|  | 139 | rx_pbuffer |  |  |
|  | 140 | rx_pbuffer |  |  |
|  | 141 | rx_pbuffer |  |  |
|  | 142 | rx_pbuffer |  |  |
|  | 143 | rx_pbuffer |  |  |
|  | 144 | rx_pbuffer |  |  |
|  | 145 | rx_pbuffer |  |  |
|  | 146 | rx_pbuffer |  |  |
|  | 147 | rx_pbuffer |  |  |
|  | 148 | rx_pbuffer |  |  |
|  | 149 | rx_pbuffer |  |  |
|  | 150 | rx_pbuffer |  |  |
|  | 151 | rx_pbuffer |  |  |
|  | 152 | rx_pbuffer |  |  |
|  | 153 | rx_pbuffer |  |  |
|  | 154 | rx_pbuffer |  |  |
|  | 155 | rx_pbuffer |  |  |
|  | 156 | rx_pbuffer |  |  |
|  | 157 | rx_pbuffer |  |  |
|  | 158 | rx_pbuffer |  |  |
|  | 159 | rx_pbuffer |  |  |
|  | 160 | rx_pbuffer |  |  |
|  | 161 | rx_pbuffer |  |  |
|  | 162 | rx_pbuffer |  |  |
|  | 163 | rx_pbuffer |  |  |
|  | 164 | rx_pbuffer |  |  |
|  | 165 | rx_pbuffer |  |  |
|  | 166 | rx_pbuffer |  |  |
|  | 167 | rx_pbuffer |  |  |
|  | 168 | rx_pbuffer |  |  |
|  | 169 | rx_pbuffer |  |  |
|  | 170 | rx_pbuffer |  |  |
|  | 171 | rx_pbuffer |  |  |
|  | 172 | rx_pbuffer |  |  |
|  | 173 | rx_pbuffer |  |  |
|  | 174 | rx_pbuffer |  |  |
|  | 175 | rx_pbuffer |  |  |
|  | 176 | rx_pbuffer |  |  |
|  | 177 | rx_pbuffer |  |  |
|  | 178 | rx_pbuffer |  |  |
|  | 179 | rx_pbuffer |  |  |
|  | 180 | rx_pbuffer |  |  |
|  | 181 | rx_pbuffer |  |  |
|  | 182 | rx_pbuffer |  |  |
|  | 183 | rx_pbuffer |  |  |
|  | 184 | rx_pbuffer |  |  |
|  | 185 | rx_pbuffer |  |  |
|  | 186 | rx_pbuffer |  |  |
|  | 187 | rx_pbuffer |  |  |
|  | 188 | rx_pbuffer |  |  |
|  | 189 | rx_pbuffer |  |  |
|  | 190 | rx_pbuffer |  |  |
|  | 191 | rx_pbuffer |  |  |
|  | 192 | rx_pbuffer |  |  |
|  | 193 | rx_pbuffer |  |  |
|  | 194 | rx_pbuffer |  |  |
|  | 195 | rx_pbuffer |  |  |
|  | 196 | rx_pbuffer |  |  |
|  | 197 | rx_pbuffer |  |  |
|  | 198 | rx_pbuffer | End rx_pbuffer |  |

## : PACKET NUM, GET_W_SIZE AND GET_R_SIZE RETURNED PACKETS.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| Get_W_SIZE | 1 | ID |  |
| Get_R_SIZE | 2 | Error Code |  |
| Packet Num | 3 | Packets_Size |  |
|  | 4 | li_value high | Start data read |
|  | 5 | li_value low | End data read |
|  | 6 | Start Addr High |  |
|  | 7 | Start Addr Low |  |
|  | 8 | End Addr High |  |
|  | 9 | End Addr Low |  |
|  | 10 | byte H SW arch | Start SW_Architecture |
|  | 11 | byte L SW arch | End SW_Architecture |

## : GET STATUS RETURNED PACKET.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| Status | 1 | ID |  |
|  | 2 | Error Code |  |
|  | 3 | Packet_Size |  |
|  | 4 | Li_value read H | Start data read |
|  | 5 | Li_value read L | End data read |
|  | 6 | Start Addr High |  |
|  | 7 | Start Addr Low |  |
|  | 8 | End Addr High |  |
|  | 9 | End Addr Low |  |
|  | 10 | byte H register | Start: Status Register |
|  | 11 | byte L register | End: Status Register |

## : GET_IDSTATE AND GET_IDSTATUS RETURNED PACKET.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| IDStatus | 1 | ID |  |
| IDState | 2 | Error Code |  |
|  | 3 | Packet_Size |  |
|  | 4 | li_value_read | Data read |
|  | 5 | Start Addr High |  |
|  | 6 | Start Addr Low |  |
|  | 7 | End Addr High |  |
|  | 8 | End Addr Low |  |
|  | 9 | byte SW arch | SW_Architecture |

## : SET TIMEOUT RETURNED PACKET.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| Set Timeout | 1 | ID |  |
|  | 2 | Error Code |  |
|  | 3 | Packet_Size |  |
|  | 4 | Start Addr High |  |
|  | 5 | Start Addr Low |  |
|  | 6 | End Addr High |  |
|  | 7 | End Addr Low |  |
|  | 8 | byte SW arch | Start SW_Architecture |
|  | 9 | Start Addr High |  |
|  | 10 | Start Addr Low |  |
|  | 11 | End Addr High |  |
|  | 12 | End Addr Low |  |
|  | 13 | SICR high | Start: Registers |
|  | 14 | SICR Low |  |
|  | 15 | TRS_CTRL H |  |
|  | 16 | TRS_CTRL L |  |
|  | 17 | RT_CTRL H |  |
|  | 18 | RT_CTRL L |  |
|  | 19 | ISR H |  |
|  | 20 | ISR L |  |
|  | 21 | IMR H |  |
|  | 22 | IMR L |  |
|  | 23 | COMI_CS0R H |  |
|  | 24 | COMI_CS0R L |  |
|  | 25 | COMI_ACR H |  |
|  | 26 | COMI_ACR L |  |
|  | 27 | PRCIR H |  |
|  | 28 | PRCIR L | End: Registers |

## : EXIT STUB RETURNED PACKET.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| Exit_Stub | 1 | ID |  |
|  | 2 | Error Code |  |
|  | 3 | Packet_Size |  |

## : ERROR ON SELECT NUMBER OF FUCTION RETURNED PACKET.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| None | 1 | ID |  |
|  | 2 | Error Code |  |
|  | 3 | Packet_Size |  |

## : WRITE TO BOARD MEMORY RETURNED PACKET.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| Write to | 1 | ID |  |
| Board | 2 | Error Code |  |
| Memory | 3 | Packet_size |  |
|  | 4 | Buffer size |  |
|  | 5 | Tx_pbuffer | Start tx_pbuffer |
|  | 6 | Tx_pbuffer |  |
|  | 7 | Tx_pbuffer |  |
|  | 8 | Tx_pbuffer |  |
|  | 9 | Tx_pbuffer |  |
|  | 10 | Tx_pbuffer |  |
|  | 11 | Tx_pbuffer |  |
|  | 12 | Tx_pbuffer |  |
|  | 13 | Tx_pbuffer |  |
|  | 14 | Tx_pbuffer |  |
|  | 15 | Tx_pbuffer |  |
|  | 16 | Tx_pbuffer |  |
|  | 17 | Tx_pbuffer |  |
|  | 18 | Tx_pbuffer |  |
|  | 19 | Tx_pbuffer |  |
|  | 20 | Tx_pbuffer |  |
|  | 21 | Tx_pbuffer |  |
|  | 22 | Tx_pbuffer |  |
|  | 23 | Tx_pbuffer |  |
|  | 24 | Tx_pbuffer |  |
|  | 25 | Tx_pbuffer |  |
|  | 26 | Tx_pbuffer |  |
|  | 27 | Tx_pbuffer |  |
|  | 28 | Tx_pbuffer |  |
|  | 29 | Tx_pbuffer |  |
|  | 30 | Tx_pbuffer |  |
|  | 31 | Tx_pbuffer |  |
|  | 32 | Tx_pbuffer |  |
|  | 33 | Tx_pbuffer |  |
|  | 34 | Tx_pbuffer |  |
|  | 35 | Tx_pbuffer |  |
|  | 36 | Tx_pbuffer |  |
|  | 37 | Tx_pbuffer |  |
|  | 38 | Tx_pbuffer |  |
|  | 39 | Tx_pbuffer | End tx_pbuffer |
|  | 40 | Start Addr High |  |
|  | 41 | Start Addr Low |  |
|  | 42 | End Addr High |  |
|  | 43 | End Addr Low |  |
|  | 44 | DPRAM | Start DPRAM channel |
|  | 45 | DPRAM |  |
|  | 46 | DPRAM |  |
|  | 47 | DPRAM |  |
|  | 48 | DPRAM |  |
|  | 49 | DPRAM |  |
|  | 50 | DPRAM |  |
|  | 51 | DPRAM |  |
|  | 52 | DPRAM |  |
|  | 53 | DPRAM |  |
|  | 54 | DPRAM |  |
|  | 55 | DPRAM |  |
|  | 56 | DPRAM |  |
|  | 57 | DPRAM |  |
|  | 58 | DPRAM |  |
|  | 59 | DPRAM |  |
|  | 60 | DPRAM |  |
|  | 61 | DPRAM |  |
|  | 62 | DPRAM |  |
|  | 63 | DPRAM |  |
|  | 64 | DPRAM |  |
|  | 65 | DPRAM |  |
|  | 66 | DPRAM |  |
|  | 67 | DPRAM |  |
|  | 68 | DPRAM |  |
|  | 69 | DPRAM |  |
|  | 70 | DPRAM |  |
|  | 71 | DPRAM |  |
|  | 72 | DPRAM |  |
|  | 73 | DPRAM |  |
|  | 74 | DPRAM |  |
|  | 75 | DPRAM |  |
|  | 76 | DPRAM |  |
|  | 77 | DPRAM |  |
|  | 78 | DPRAM |  |
|  | 79 | DPRAM |  |
|  | 80 | DPRAM |  |
|  | 81 | DPRAM |  |
|  | 82 | DPRAM | End DPRAM channel |

## : READ FROM BOARD MEMORY RETURNED PACKET.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| Read from | 1 | ID |  |
| Board | 2 | Error Code |  |
| Memory | 3 | Packet_size |  |
|  | 4 | Buffer size |  |
|  | 5 | Rx_pbuffer | Start rx_pbuffer |
|  | 6 | Rx_pbuffer |  |
|  | 7 | Rx_pbuffer |  |
|  | 8 | Rx_pbuffer |  |
|  | 9 | Rx_pbuffer |  |
|  | 10 | Rx_pbuffer |  |
|  | 11 | Rx_pbuffer |  |
|  | 12 | Rx_pbuffer |  |
|  | 13 | Rx_pbuffer |  |
|  | 14 | Rx_pbuffer |  |
|  | 15 | Rx_pbuffer |  |
|  | 16 | Rx_pbuffer |  |
|  | 17 | Rx_pbuffer |  |
|  | 18 | Rx_pbuffer |  |
|  | 19 | Rx_pbuffer |  |
|  | 20 | Rx_pbuffer |  |
|  | 21 | Rx_pbuffer |  |
|  | 22 | Rx_pbuffer |  |
|  | 23 | Rx_pbuffer |  |
|  | 24 | Rx_pbuffer |  |
|  | 25 | Rx_pbuffer |  |
|  | 26 | Rx_pbuffer |  |
|  | 27 | Rx_pbuffer |  |
|  | 28 | Rx_pbuffer |  |
|  | 29 | Rx_pbuffer |  |
|  | 30 | Rx_pbuffer |  |
|  | 31 | Rx_pbuffer |  |
|  | 32 | Rx_pbuffer |  |
|  | 33 | Rx_pbuffer |  |
|  | 34 | Rx_pbuffer |  |
|  | 35 | Rx_pbuffer |  |
|  | 36 | Rx_pbuffer |  |
|  | 37 | Rx_pbuffer |  |
|  | 38 | Rx_pbuffer |  |
|  | 39 | Rx_pbuffer | End rx_pbuffer |
|  | 40 | Start Addr High |  |
|  | 41 | Start Addr Low |  |
|  | 42 | End Addr High |  |
|  | 43 | End Addr Low |  |
|  | 44 | DPRAM | Start DPRAM channel |
|  | 45 | DPRAM |  |
|  | 46 | DPRAM |  |
|  | 47 | DPRAM |  |
|  | 48 | DPRAM |  |
|  | 49 | DPRAM |  |
|  | 50 | DPRAM |  |
|  | 51 | DPRAM |  |
|  | 52 | DPRAM |  |
|  | 53 | DPRAM |  |
|  | 54 | DPRAM |  |
|  | 55 | DPRAM |  |
|  | 56 | DPRAM |  |
|  | 57 | DPRAM |  |
|  | 58 | DPRAM |  |
|  | 59 | DPRAM |  |
|  | 60 | DPRAM |  |
|  | 61 | DPRAM |  |
|  | 62 | DPRAM |  |
|  | 63 | DPRAM |  |
|  | 64 | DPRAM |  |
|  | 65 | DPRAM |  |
|  | 66 | DPRAM |  |
|  | 67 | DPRAM |  |
|  | 68 | DPRAM |  |
|  | 69 | DPRAM |  |
|  | 70 | DPRAM |  |
|  | 71 | DPRAM |  |
|  | 72 | DPRAM |  |
|  | 73 | DPRAM |  |
|  | 74 | DPRAM |  |
|  | 75 | DPRAM |  |
|  | 76 | DPRAM |  |
|  | 77 | DPRAM |  |
|  | 78 | DPRAM |  |
|  | 79 | DPRAM |  |
|  | 80 | DPRAM |  |
|  | 81 | DPRAM |  |
|  | 82 | DPRAM | End DPRAM channel |

## : WATCHDOG DELAY RETURNED PACKET.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| WD_Delay | 1 | ID |  |
|  | 2 | Error Code |  |
|  | 3 | Packet_Size |  |
|  | 4 | Watchdog Timer |  |

## : WATCHDOG DELAY FAILED RETURNED PACKET.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| WD_Delay_Fail | 1 | ID |  |
|  | 2 | Error Code |  |
|  | 3 | Packet_Size |  |
|  | 4 | Watchdog Timer |  |

## : WATCHDOG REFRESH RETURNED PACKET.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| WD_Refresh | 1 | ID |  |
|  | 2 | Error Code |  |
|  | 3 | Packet_Size |  |

## : WATCHDOG STATUS RETURNED PACKET.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| WD_Status | 1 | ID |  |
|  | 2 | Error Code |  |
|  | 3 | Packet_Size |  |
|  | 4 | Watchdog Status |  |

## : ERROR CODE RETURNED PACKET.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| None | 1 | ID |  |
|  | 2 | Error Code |  |
|  | 3 | Packet_Size |  |

## : EXIT STUB RETURNED PACKET.

| Functions | Word | Packets format | Memdump Zone |
| --- | --- | --- | --- |
| Exit_Stub | 1 | ID |  |
|  | 2 | Error Code |  |
|  | 3 | Packet_Size |  |

# : RETURNED MIL-STD-1553 PACKETS FORMAT AFTER A EEPROM COMMAND

N/A

# : 1355 DRIVERS RETURNED ERRORS CODE

| Flag | Function | Type of error |
| --- | --- | --- |
| 0 | FOR ALL | OK |
| 1 | FOR ALL | NOT-OK |
| 2 | WRITE TO BOARD MEMORY | OVERFLOW ON TRANSMISSION ON DPRAM |
| 3 | WRITE TO BOARD MEMORY | UNDERFLOW ON TRANSMISSION ON DPRAM |
| 4 |  |  |
| 9 |  |  |
| 10 | READ FROM BOARD MEMORY | OVERFLOW ON RECEPTION ON DPRAM |
| 11 | READ FROM BOARD MEMORY | UNDERFLOW ON RECEPTION ON DPRAM |
| 12 |  |  |
| 19 |  |  |
| 20 | OPEN LINK | ERROR: NUM OF LINK > MAX NUM OF LINK |
| 21 | OPEN LINK | LINK CH1 ALREADY OPEN |
| 22 | OPEN LINK | LINK CH2 ALREADY OPEN |
| 23 | OPEN LINK | LINK CH3 ALREADY OPEN |
| 24 |  |  |
| 29 |  |  |
| 30 | CLOSE LINK | ERROR: NUM OF LINK > MAX NUM OF LINK |
| 31 | CLOSE LINK | LINK CH1 ALREADY CLOSE |
| 32 | CLOSE LINK | LINK CH2 ALREADY CLOSE |
| 33 | CLOSE LINK | LINK CH3 ALREADY CLOSE |
| 34 |  |  |
| 39 |  |  |
| 40 | START LINK MASTER | ERROR: NUM OF LINK > MAX NUM OF LINK |
| 41 | START LINK MASTER | LINK CH1 CLOSE |
| 42 | START LINK MASTER | LINK CH2 CLOSE |
| 43 | START LINK MASTER | LINK CH3 CLOSE |
| 44 | START LINK MASTER | SPEED NOT AUTORIZED ON LINK CH1 |
| 45 | START LINK MASTER | SPEED NOT AUTORIZED ON LINK CH2 |
| 46 | START LINK MASTER | SPEED NOT AUTORIZED ON LINK CH3 |
| 47 | START LINK MASTER | ERROR ON WRITE REGISTER CH1_DSM_MODR |
| 48 | START LINK MASTER | ERROR ON WRITE REGISTER CH2_DSM_MODR |
| 49 | START LINK MASTER | ERROR ON WRITE REGISTER CH3_DSM_MODR |
| 50 | START LINK MASTER | ERROR ON WRITE REGISTER CH1_COMICFG |
| 51 | START LINK MASTER | ERROR ON WRITE REGISTER CH2_COMICFG |
| 52 | START LINK MASTER | ERROR ON WRITE REGISTER CH3_COMICFG |
| 53 | START LINK MASTER | ERROR ON WRITE REGISTER CH1_CNTRL1 |
| 54 | START LINK MASTER | ERROR ON WRITE REGISTER CH2_CNTRL1 |
| 55 | START LINK MASTER | ERROR ON WRITE REGISTER CH3_CNTRL1 |
| 56 | START LINK MASTER | ERROR ON WRITE REGISTER CH1_DSM_CMDR |
| 57 | START LINK MASTER | ERROR ON WRITE REGISTER CH2_DSM_CMDR |
| 58 | START LINK MASTER | ERROR ON WRITE REGISTER CH3_DSM_CMDR |
| 59 | START LINK MASTER | STARTING ERROR: LINK CH1 IS BLOCKED |
| 60 | START LINK MASTER | STARTING ERROR: LINK CH1 IS BLOCKED |
| 61 | START LINK MASTER | STARTING ERROR: LINK CH1 IS BLOCKED |
| 62 |  |  |
| 63 |  |  |
| 64 |  |  |
| 65 | SET TIMEOUT | ERROR TIMEOUT ISN'T AUTORIZED ON LINK CH1 |
| 66 | SET TIMEOUT | ERROR TIMEOUT ISN'T AUTORIZED ON LINK CH2 |
| 67 | SET TIMEOUT | ERROR TIMEOUT ISN'T AUTORIZED ON LINK CH3 |
| 68 |  |  |
| 69 |  |  |
| 70 | STOP LINK | ERROR: NUM OF LINK > MAX NUM OF LINK |
| 71 | STOP LINK | LINK CH1 ALREADY CLOSE |
| 72 | STOP LINK | LINK CH2 ALREADY CLOSE |
| 73 | STOP LINK | LINK CH3 ALREADY CLOSE |
| 74 | STOP LINK | ERROR ON WRITE REGISTER CH1_DSM_CMDR |
| 75 | STOP LINK | ERROR ON WRITE REGISTER CH2_DSM_CMDR |
| 76 | STOP LINK | ERROR ON WRITE REGISTER CH3_DSM_CMDR |
| 77 |  |  |
| 89 |  |  |
| 90 | READ PACKET | ERROR: NUM OF LINK > MAX NUM OF LINK |
| 91 | READ PACKET | ERROR OVERFLOW ON DPRAM ON LINK CH1 |
| 92 | READ PACKET | ERROR OVERFLOW ON DPRAM ON LINK CH2 |
| 93 | READ PACKET | ERROR OVERFLOW ON DPRAM ON LINK CH3 |
| 94 | READ PACKET | LINK CH1 CLOSE |
| 95 | READ PACKET | LINK CH2 CLOSE |
| 96 | READ PACKET | LINK CH3 CLOSE |
| 97 | READ PACKET | LINK CH1 PARITY OR DISCONNECT ERROR DETECTED |
| 98 | READ PACKET | LINK CH2 PARITY OR DISCONNECT ERROR DETECTED |
| 99 | READ PACKET | LINK CH3 PARITY OR DISCONNECT ERROR DETECTED |
| 100 | READ PACKET | LINK CH1 NOT STARTED OR NOT DONE |
| 101 | READ PACKET | LINK CH2 NOT STARTED OR NOT DONE |
| 102 | READ PACKET | LINK CH3 NOT STARTED OR NOT DONE |
| 103 |  |  |
| 109 |  |  |
| 110 | RESET LINK | ERROR: NUM OF LINK > MAX NUM OF LINK |
| 111 | RESET LINK | LINK CH1 CLOSE: RESET IMPOSSIBLE |
| 112 | RESET LINK | LINK CH2 CLOSE: RESET IMPOSSIBLE |
| 113 | RESET LINK | LINK CH3 CLOSE: RESET IMPOSSIBLE |
| 114 | RESET LINK | ERROR ON WRITE REGISTER CH1_DSM_CMDR |
| 115 | RESET LINK | ERROR ON WRITE REGISTER CH2_DSM_CMDR |
| 116 | RESET LINK | ERROR ON WRITE REGISTER CH3_DSM_CMDR |
| 117 |  |  |
| 129 |  |  |
| 130 | READ LINK | ERROR: NUM OF LINK > MAX NUM OF LINK |
| 131 | READ LINK | READ BYTE OVERFLOW ON LINK CH1 |
| 132 | READ LINK | READ BYTE OVERFLOW ON LINK CH2 |
| 133 | READ LINK | READ BYTE OVERFLOW ON LINK CH3 |
| 134 | READ LINK | LINK CH1 CLOSE |
| 135 | READ LINK | LINK CH2 CLOSE |
| 136 | READ LINK | LINK CH3 CLOSE |
| 137 | READ LINK | LINK CH1 PARITY OR DISCONNECT ERROR DETECTED |
| 138 | READ LINK | LINK CH2 PARITY OR DISCONNECT ERROR DETECTED |
| 139 | READ LINK | LINK CH3 PARITY OR DISCONNECT ERROR DETECTED |
| 140 | READ LINK | READ ERROR ON CH1_DSM_STAR |
| 141 | READ LINK | READ ERROR ON CH2_DSM_STAR |
| 142 | READ LINK | READ ERROR ON CH3_DSM_STAR |
| 143 | READ LINK | ERROR WRITE ON CH1_RX_SAR |
| 144 | READ LINK | ERROR WRITE ON CH2_RX_SAR |
| 145 | READ LINK | ERROR WRITE ON CH3_RX_SAR |
| 146 | READ LINK | ERROR WRITE ON CH1_RX_EAR |
| 147 | READ LINK | ERROR WRITE ON CH2_RX_EAR |
| 148 | READ LINK | ERROR WRITE ON CH3_RX_EAR |
| 149 | READ LINK | TIMEOUT ERROR: LINK CH1 NOT STARTED |
| 150 | READ LINK | TIMEOUT ERROR: LINK CH2 NOT STARTED |
| 151 | READ LINK | TIMEOUT ERROR: LINK CH3 NOT STARTED |
| 152 | READ LINK | TRANSFER IN PROGRESS ON LINK CH1 |
| 153 | READ LINK | TRANSFER IN PROGRESS ON LINK CH2 |
| 154 | READ LINK | TRANSFER IN PROGRESS ON LINK CH3 |
| 155 | READ LINK | NULL NOT FOUND ON LINK CH1 |
| 156 | READ LINK | NULL NOT FOUND ON LINK CH2 |
| 157 | READ LINK | NULL NOT FOUND ON LINK CH3 |
| 158 | READ LINK | ERROR PARITY ON LINK CH1 |
| 159 | READ LINK | ERROR PARITY ON LINK CH2 |
| 160 | READ LINK | ERROR PARITY ON LINK CH3 |
| 161 | READ LINK | ERROR DISCONNECT ON LINK CH1 |
| 162 | READ LINK | ERROR DISCONNECT ON LINK CH2 |
| 163 | READ LINK | ERROR DISCONNECT ON LINK CH3 |
| 164 |  |  |
| 169 |  |  |
| 170 | WRITE LINK | ERROR: NUM OF LINK > MAX NUM OF LINK |
| 171 | WRITE LINK | OVERFLOW ON WRITE ON CH1 |
| 172 | WRITE LINK | OVERFLOW ON WRITE ON CH2 |
| 173 | WRITE LINK | OVERFLOW ON WRITE ON CH3 |
| 174 | WRITE LINK | LINK CH1 CLOSE |
| 175 | WRITE LINK | LINK CH2 CLOSE |
| 176 | WRITE LINK | LINK CH3 CLOSE |
| 177 | WRITE LINK | LINK CH1 PARITY OR DISCONNECT ERROR DETECTED |
| 178 | WRITE LINK | LINK CH2 PARITY OR DISCONNECT ERROR DETECTED |
| 179 | WRITE LINK | LINK CH3 PARITY OR DISCONNECT ERROR DETECTED |
| 180 | WRITE LINK | ERROR WRITE ON CH1_TX_SAR |
| 181 | WRITE LINK | ERROR WRITE ON CH2_TX_SAR |
| 182 | WRITE LINK | ERROR WRITE ON CH3_TX_SAR |
| 183 | WRITE LINK | ERROR WRITE ON CH1_TX_EAR |
| 184 | WRITE LINK | ERROR WRITE ON CH2_TX_EAR |
| 185 | WRITE LINK | ERROR WRITE ON CH3_TX_EAR |
| 186 | WRITE LINK | TIMEOUT ERROR ON CH1 |
| 187 | WRITE LINK | TIMEOUT ERROR ON CH2 |
| 188 | WRITE LINK | TIMEOUT ERROR ON CH3 |
| 189 | WRITE LINK | TRANSFER IN PROGRESS ON LINK CH1 |
| 190 | WRITE LINK | TRANSFER IN PROGRESS ON LINK CH2 |
| 191 | WRITE LINK | TRANSFER IN PROGRESS ON LINK CH3 |
| 192 | WRITE LINK | NULL NOT FOUND ON LINK CH1 |
| 193 | WRITE LINK | NULL NOT FOUND ON LINK CH2 |
| 194 | WRITE LINK | NULL NOT FOUND ON LINK CH3 |
| 195 |  |  |
| 199 |  |  |
| 200 | START LINK SLAVE | ERROR: NUM OF LINK > MAX NUM OF LINK |
| 201 | START LINK SLAVE | LINK CH1 CLOSE |
| 202 | START LINK SLAVE | LINK CH2 CLOSE |
| 203 | START LINK SLAVE | LINK CH3 CLOSE |
| 204 | START LINK SLAVE | SPEED ERROR ON LINK CH1 |
| 205 | START LINK SLAVE | SPEED ERROR ON LINK CH2 |
| 206 | START LINK SLAVE | SPEED ERROR ON LINK CH3 |
| 207 | START LINK SLAVE | ERROR ON READ REGISTER CH1_DSM_STAR |
| 208 | START LINK SLAVE | ERROR ON READ REGISTER CH2_DSM_STAR |
| 209 | START LINK SLAVE | ERROR ON READ REGISTER CH3_DSM_STAR |
| 210 | START LINK SLAVE | ERROR ON WRITE REGISTER CH1_DSM_MODR |
| 211 | START LINK SLAVE | ERROR ON WRITE REGISTER CH2_DSM_MODR |
| 212 | START LINK SLAVE | ERROR ON WRITE REGISTER CH3_DSM_MODR |
| 213 | START LINK SLAVE | ERROR ON WRITE REGISTER CH1_COMICFG |
| 214 | START LINK SLAVE | ERROR ON WRITE REGISTER CH2_COMICFG |
| 215 | START LINK SLAVE | ERROR ON WRITE REGISTER CH3_COMICFG |
| 216 | START LINK SLAVE | ERROR ON WRITE REGISTER CH1_CNTRL1 |
| 217 | START LINK SLAVE | ERROR ON WRITE REGISTER CH2_CNTRL1 |
| 218 | START LINK SLAVE | ERROR ON WRITE REGISTER CH3_CNTRL1 |
| 219 | START LINK SLAVE | ERROR ON WRITE REGISTER CH1_DSM_CMDR |
| 220 | START LINK SLAVE | ERROR ON WRITE REGISTER CH2_DSM_CMDR |
| 221 | START LINK SLAVE | ERROR ON WRITE REGISTER CH3_DSM_CMDR |
| 222 | START LINK SLAVE | TRANSFER ERROR TIMEOUT CH1 |
| 223 | START LINK SLAVE | TRANSFER ERROR TIMEOUT CH2 |
| 224 | START LINK SLAVE | TRANSFER ERROR TIMEOUT CH3 |
| 225 |  |  |
| 239 |  |  |
| 240 | STUB | VALUE ERROR |
| 241 | STUB | POWER ON FAILED: NO SW ARCHITETTURE PRODUCED |
| 242 | STUB | WRITE REGISTER FAILED |
| 243 | STUB | READ REGISTER FAILED |
| 244 | STUB | WRITE ON WATCHDOG REGISTER FAILED |
| 245 | STUB | ERROR TO ACCESS AT SW ARCHITECTURE |
| 246 | STUB | ERROR TO GET LINK STATUS |

# Text boxes

Mil-std 1553 I/F

EEPROM,1355 Mezzanine

First Test Equipment,

- Condor Bus Tool

- PCI Mil-std 1553

- PCI 4 links spacewire

-Test Program Spacewire

Payload

Interface

CPU Board

Power

Supply 2

Power

Supply 1

Power Bus, Data Bus

Software Development Environment

ADSP Emulator

| Color |  | Memory zone |
| --- | --- | --- |
|  |  | Data memory |
|  |  | General Registers |
|  |  | Link Registers |
|  |  | Software architecture |
|  |  | DPRAM |

Power Supply 15V, -15V

Power Supply 5V, 2,5V