|  | HERSCHEL SPIRE | Ref: SPIRE-RAL-PRC-002222 Author: Asier Abreu Aramburu | Page: 1 Issue: 0.1 Date: 10-June-2004 |
| --- | --- | --- | --- |
| SPIRE DRCU Switch On Procedure |

| Prepared by: | Asier Abreu | Date 10 June 2004 |
| --- | --- | --- |
| Checked: |  | Date |

| Approval: |  | Date |
| --- | --- | --- |

Distribution

| RAL |  |
| --- | --- |

| Host system | Windows 2000 SP2 |
| --- | --- |
| Word Processor | Microsoft Word 2000 SR1 |
| File |  |

# Document Change Record

| Date | Index | Affected Pages | Changes |
| --- | --- | --- | --- |

# Contents

Contents	4

1	Scope of Document	5

2	Applicable Documents	5

3	Constraints	5

4	DRCU switch on procedure	6

4.1	Stop SPIRE housekeeping telemetry generation	6

4.2	Power on DRCU	7

4.3	Restarting the SPIRE Housekeeping	8

5	DRCU Switch Off procedure	10

# Scope of Document

This document describes the procedure for the safe switch on of the SPIRE DRCU.

NOTE: It ONLY applies when the power bench is to be used NOT WHEN THE PSU is used.

# Applicable Documents

|  | Title | Author | Reference | Date |
| --- | --- | --- | --- | --- |
| AD01 | SPIRE EGSE ILT Startup Procedures | Sunil Sidher & Miguel Requena | SPIRE-RAL-DOC-1630 Issue 0.7 | 24th June 2003 |
| AD02 | SPIRE data ICD | Ken King | SPIRE-RAL-PRJ-001078), Issue 1.1 | 25th May 2004 |

# Constraints

- EGSE Router and EGSE Gateway must be running.

- CDMS Simulator must be running.

- SCOS2000 must be running.

- DPU must be powered on.

Refer to document EGSE-ILT-Startup-Procedures (SPIRE-RAL-DOC-001630) for more information on how to reach to this point.

# DRCU switch on procedure

## Stop SPIRE housekeeping telemetry generation

| Objective: | To prevent the DPU from sending housekeeping parameter update requests through the DPU-DRCU interfaces while the DRCU is being powered on. |
| --- | --- |
| Initial Conditions: | DPU power is ON and HK telemetry is being generated. DRCU power is OFF. Telemetry being generated: CDMS Simulator housekeeping packets with APID 0x7F6, type 3, subtype 25. SPIRE Nominal housekeeping packets with APID 0x502, type 3, subtype 25. SPIRE Critical housekeeping packets with APID 0x500, type 3, subtype 25. In the DPU AND OBS PARAMETERS DISPLAY in SCOS check: MONSTAT = 0 |
| Final Conditions: | DPU power is ON and HK telemetry request to the DRCU is halted. DRCU power is OFF. Telemetry being generated: CDMS Simulator housekeeping packets with APID 0x7F6, type 3, subtype 25. In the DPU AND OBS PARAMETERS DISPLAY in SCOS check: MONSTAT = 0 |
| Constraints: | DPU must be powered ON (28 V power supply) and OBS must be running, i.e. HK must be generated. TC HISTORY display MANUAL STACK and EXIF (TOPE) tasks must have been started on SCOS2000. |
| Total Duration: | < 1 minutes |

| Step. | Action |
| --- | --- |
|  | In TOPE window : Run clear_HK_report.tcl procedure by selecting the procedure (single click over the procedure name) in TOPE and pressing run button. Two CLEAR_HK_REPORT commands are sent by this procedure to the OBS. Verify that both commands are successful on the TC history display. Result : Critical and nominal HK report stops. Alternatively : Issue command CLEAR_HK_REPORT from MANUAL STACK Parameters : Mib definition Value HKPCKTID_CLEARHK 0x300 Result : Critical HK report stops Issue command CLEAR_HK_REPORT from MANUAL STACK Parameters : Mib definition Value HKPCKTID_CLEARHK 0x301 Result : Nominal HK report stops NOTE: Only one of these sequences is needed in order to stop housekeeping telemetry generation, you run either one OR the other. |

## Power on DRCU

| Objective: | To power on the DRCU. |
| --- | --- |
| Initial Conditions: | DPU power is ON and HK telemetry request to the DRCU is halted. DRCU power is OFF. Telemetry being generated: CDMS Simulator housekeeping packets with APID 0x7F6, type 3, subtype 25. In the DPU AND OBS PARAMETERS DISPLAY in SCOS check: MONSTAT = 0 |
| Final Conditions: | DPU power is ON and HK telemetry request to the DRCU is halted. DRCU power is ON. Telemetry being generated: CDMS Simulator housekeeping packets with APID 0x7F6, type 3, subtype 25. In the DPU AND OBS PARAMETERS DISPLAY in SCOS check: MONSTAT = 0 |
| Constraints: | DPU must be powered ON (28 V power supply) and HK generation must have been stopped following the previous steps. |
| Total Duration: | < 2 minutes |

| Step. | Action |
| --- | --- |
|  | Check if the DRCU Power bench main power is switch on. The LED in the top-right hand front side with the label Main Power of the DRCU will be on. See Figure1 at the end of the document. If the main power is on skip this step, if it’s not, press the main power switch which is located in the top-right hand rear side of the DRCU power bench To switch the secondary power pull down the spring in the front side of the bench. |

Comments:  A picture taken of the front side of the power bench is shown at the end of the document.

## Restarting the SPIRE Housekeeping

| Objective: | To restart the SPIRE housekeeping generation |
| --- | --- |
| Initial Conditions: | DPU power is ON and HK telemetry request to the DRCU is halted. DRCU power is ON. Telemetry being generated: CDMS Simulator housekeeping packets with APID 0x7F6, type 3, subtype 25. In the DPU AND OBS PARAMETERS DISPLAY in SCOS check: MONSTAT = 0 |
| Final Conditions: | DPU power is ON and HK telemetry is being generated. DRCU power is ON. Telemetry being generated: CDMS Simulator housekeeping packets with APID 0x7F6, type 3, subtype 25. SPIRE Nominal housekeeping packets with APID 0x502, type 3, subtype 25. SPIRE Critical housekeeping packets with APID 0x500, type 3, subtype 25. In the DPU AND OBS PARAMETERS DISPLAY in SCOS check: MONSTAT = 5 |
| Constraints: | DPU power must be ON (28 V power supply) DRCU power must be ON following previous steps |
| Total Duration: | < 1 minute |

| Step. | Action |
| --- | --- |
|  | In TOPE window : Run define_New_HK_report.tcl procedure by selecting the procedure (single click over the procedure name) in TOPE and pressing run button. Two DEFINE_NEW_HK_REPORT commands are sent by this procedure to the OBS. Verify that both commands are successful on the TC history display. Result : Critical and nominal HK report restarts. Alternatively: Issue command DEFINE_NEW_HK_REPORT from MANUAL STACK Parameters : Mib definition Value HKPCKTID_DEFINENEWHK 0x301 HKSID_DEFINENEWHK 0x301 HKINTERVAL_DEFINENEWHK 0x3E8 HKREPEAT_DEFINENEWHK 0x1 MONTABID_DEFINENEWHK 0x1 TABLEID_DEFINENEWHK 0x1 Result : Nominal HK report restarts Issue command DEFINE_NEW_HK_REPORT from MANUAL STACK Parameters : Mib definition Value HKPCKTID_DEFINENEWHK 0x300 HKSID_DEFINENEWHK 0x300 HKINTERVAL_DEFINENEWHK 0x7D0 HKREPEAT_DEFINENEWHK 0x1 MONTABID_DEFINENEWHK 0x0 TABLEID_DEFINENEWHK 0x0 Result : Critical HK report restarts |

# DRCU Switch Off procedure

| Objective: | To switch off the DRCU |
| --- | --- |
| Initial Conditions: | DRCU main and secondary power switches are ON. DRCU power is ON. DPU power is ON and OBS running. Telemetry being generated: CDMS Simulator housekeeping packets with APID 0x7F6, type 3, subtype 25. SPIRE Nominal housekeeping packets with APID 0x502, type 3, subtype 25. CDMS Simulator housekeeping packets with APID 0x7F6, type 3, subtype 25. In the DPU AND OBS PARAMETERS DISPLAY in SCOS check: MONSTAT = 5 |
| Final Conditions: | DRCU main and secondary power switches are OFF. DRCU powered OFF. DPU powered ON and OBS running. Telemetry being generated: CDMS Simulator housekeeping packets with APID 0x7F6, type 3, subtype 25. SPIRE Nominal housekeeping packets with APID 0x502, type 3, subtype 25. SPIRE Critical housekeeping packets with APID 0x500, type 3, subtype 25. In the DPU AND OBS PARAMETERS DISPLAY in SCOS check: MONSTAT = 0 |
| Constraints: | None. |
| Total Duration: | 0 minute |

| Step. | Action |
| --- | --- |
|  | Pull down the spring in the front right-hand side of the power bench. The LED in the top-right hand front side with the label Secondary Power will fade off. Switch off the Main Power on the top-right hand rear side. |

Figure 1. Power bench front image (OFF configuration)