# Total Pages : 89

|  | Generic Data Collection H-P-1-ASP-TN-0543 Product Code : 460000 |  |
| --- | --- | --- |

| Rédigé par/Written by | Responsabilité-Service-Société Responsibility-Office -Company | Date | Signature |
| --- | --- | --- | --- |
| S. Dos Santos | Database Manager |  |  |
| Vérifié par/Verified by |  |  |  |
| F. Chatte | Ground Segment Interface and Operation Manager |  |  |
| F. Sauvage | Command / Control Manager |  |  |
| Approbation/Approved |  |  |  |
| C. Masse | Product Assurance Manager |  |  |
| J-J. Juillet | Project Manager |  |  |

# Data management : G. SERRA

Entité Emettrice : Alcatel Space - Cannes

(détentrice de l’original) :

| HERSCHEL/PLANCK | DISTRIBUTION RECORD |
| --- | --- |
|  | Issue / Rev. : 01/00 |
| DOCUMENT NUMBER : H-P-1-ASP-TN-0543 | Date: 21-10-2004 |
| EXTERNAL DISTRIBUTION |  | INTERNAL DISTRIBUTION |  |
| ESA | Yes | HP team | Yes |
| ASTRIUM | Yes |  |  |
| ALENIA | Yes |  |  |
| GMV | Yes |  |  |
| HFI | Yes |  |  |
| HFI | Yes |  |  |
| LFI | Yes |  |  |
| PACS | Yes |  |  |
| SPIRE | Yes |  |  |
|  |  | Clt Documentation | Orig. |

# ENREGISTREMENT DES EVOLUTIONS / CHANGE RECORDS

| ISSUE | DATE | § : DESCRIPTION DES EVOLUTIONS § : CHANGE RECORD | REDACTEUR AUTHOR |
| --- | --- | --- | --- |
| 1.0 | 8/06/2004 | Generic Data Definition inside HPSDB | S. Dos Santos |
| 1.1 | 21/10/2004 | Add note for explanation of TC packet header GX0001000 | F. Chatte |
|  |  | Chapter 1 : |  |
|  |  | Addition of a note for PSICD template relevant to SID1 and SID2 position and length for each (type, subtype) couple |  |
|  |  | Addition of a paragraph relevant to S2K identifiers for curves, command verification stage and parameter range set. |  |
|  |  | Chapter 3.1.2 |  |
|  |  | Modification of subtitle |  |
|  |  | Chapter 3.4 |  |
|  |  | Note added to explain generic CVS S2K identifier |  |
|  |  | Chapter 3.7.6 |  |
|  |  | Note added to explain generic command parameter range set S2K identifier |  |
|  |  | Chapter 3.8 |  |
|  |  | Note added to explain generic curve S2K identifier |  |
|  |  | Note : the implementation of generic S2K identifier for curve, CVS and parameter range set have been decided during DMWG21 (20/10/04) |  |
|  |  | Chapter 3.1.2 |  |
|  |  | Updated according to PSICD 5.0 and in order to have unique PIC table |  |
|  |  | All chapters |  |
|  |  | Minor corrections |  |
|  |  | Chapter 3.8.1 |  |
|  |  | Addition of digital curves SET / RESET and RESET / SET according to SES request |  |
|  |  | Note : SES request for dummy TM parameters has not been included in this version. It will be in next one. |  |

# TABLE OF CONTENTS

1.	Introduction	8

2.	Applicable and reference documents	9

2.1	Applicable documents	9

2.1.1	Reference documents	9

2.2	Acronyms	9

2.3	Definition	9

3.	Generic items:	9

3.1	Telemetry:	9

3.1.1	TM packet standard	9

3.1.2	TM packet PSICD data	10

TM  TC Acceptance Report- Success (1, 1)	10

TM TC Acceptance Report- Failure (1, 2)	10

TM  TC Execution Report-Started (1, 3)	10

TM TC Execution Report-Progress (1, 5)	11

TM Execution Report-Completed (1, 7)	11

TM TC Execution Report-Failure (1, 8)	11

TM TC Contents Report (1, 9)	12

3.1.2.8	TM HK Parameter Report Definitions Report (3, 10)	12

3.1.2.9	TM Diagnostic Parameter Definition Report (3, 12)	12

3.1.2.10	TM HK Parameter Report (3, 25)	13

3.1.2.11	TM Diagnostic Parameter Report (3, 26)	13

3.1.2.12	TM Event Report (5, 1)	14

3.1.2.13	TM Exception Report (5, 2)	14

3.1.2.14	TM Error/Alarm Report (5,4)	14

3.1.2.15	TM Memory Dump, Absolute Addresses (6, 6)	15

3.1.2.16	TM Memory Check Report , Absolute addresses (6, 10)	15

3.1.2.17	TM Function Status Report (8, 6)	15

3.1.2.18	TM SREM Data Report (8, 7)	16

3.1.2.19	TM VMC Data Report (8, 8)	16

3.1.2.20	TM Mass Memory Dump Report (8, 9)	16

3.1.2.21	TM Central Time Reference (9, 8)	17

3.1.2.22	TM Time Verification Report (9, 9)	17

3.1.2.23	TM Detailed Schedule Report (11, 10)	17

3.1.2.24	TM Summary Schedule Report (11, 13)	18

3.1.2.25	TM Command Schedule Status Report (11, 19)	18

3.1.2.26	TM Current Monitoring List Report (12, 9)	19

3.1.2.27	TM Enabled Telemetry Packets Report (14, 4)	19

3.1.2.28	TM TM Packets Down-linking / Storage Status Report (14, 7)	19

3.1.2.29	TM Storage Selection Definition Report (15, 6)	20

3.1.2.30	TM Packet Stores Catalogue Report (15, 13)	20

3.1.2.31	TM Connection Test Report (17, 2)	20

3.1.2.32	TM On-Board Control Procedures List Report (18, 9)	21

3.1.2.33	TM Active OBCPs List Report (18, 11)	21

3.1.2.34	TM OBCP Status Report (18, 13)	21

3.1.2.35	TM OBCP Contents Report (18, 15)	22

3.1.2.36	TM Event Detection List Report (19, 7)	22

3.1.2.37	TM Nominal Science Data Report (21, 1)	22

3.1.2.38	TM Science Type B Data Report (21, 2)	23

3.1.2.39	TM Diagnostic Science Data Report (21, 3)	23

3.1.2.40	TM Auxiliary Science Data Report (21, 4)	23

3.1.3	TM Packet Data	24

3.1.4	TM Packet SCOS archiving	24

3.1.5	TM structure data	24

3.1.6	TM packet group data	24

3.2	Telecommands	24

3.2.1	TC packet header  data	24

3.2.1.1	TC Packet Header With Data Field Header	24

3.2.1.2	TC Packet Header Without Data Field Header	26

3.2.2	TC packet data	28

3.2.3	TC structure data	28

3.2.4	TC packet group data	28

3.3	Command Sequences	28

3.3.1	Command Sequences	28

3.4	Command verification	28

3.4.1	Command verification	28

3.5	1553 Messages	29

3.5.1	Command word	29

3.5.2	1553 Status word data	29

3.5.3	1553 Message data	29

3.5.4	1553 Acquisition command link	29

3.5.5	1553 Structure	29

3.5.6	1553 Message group data	29

3.6	OBDH	29

3.6.1	OBDH interrogation	29

3.6.2	OBDH acquisition command link	29

3.6.3	OBDH interrogation group data	29

3.7	Parameters	30

3.7.1	Command Header Parameters	30

3.7.1.1	APID	30

3.7.1.2	Sequence Count Source Part	31

3.7.1.3	Sequence Count Sequence Part	32

3.7.1.4	Packet Length	33

3.7.1.5	Acknowledgement flags	35

3.7.1.6	Packet Type	36

3.7.1.7	Packet Subtype	38

3.7.2	Command Parameters	39

3.7.2.1	Spare 1 - Bit	39

3.7.2.2	Spare 2 - Bit	40

3.7.2.3	Spare 3 - Bit	42

3.7.2.4	Spare 4 - Bit	43

3.7.2.5	Spare 5 - Bit	45

3.7.2.6	Spare 6 - Bit	46

3.7.2.7	Spare 7 - Bit	47

3.7.2.8	Spare 8 - Bit	49

3.7.2.9	Spare 9- Bit	50

3.7.2.10	Spare 10 - Bit	52

3.7.2.11	Spare 11- Bit	53

3.7.2.12	Spare 12- Bit	54

3.7.2.13	Spare 13 - Bit	56

3.7.2.14	Spare 14 - Bit	57

3.7.2.15	Spare 15 - Bit	58

3.7.2.16	Spare 16- Bit	60

3.7.3	Parameter group data	61

3.7.4	Parameter set data	61

3.7.5	Parameter value set	61

3.7.6	Parameter range set data	62

3.8	Calibration Curves	62

3.8.1	Digital curve data	62

3.8.1.1	OFF/ON	62

3.8.1.2	ON / OFF	63

3.8.1.3	NOMINAL / REDUNDANT	63

3.8.1.4	REDUNDANT / NOMINAL	64

3.8.1.5	OK / FAULT	65

3.8.1.6	FAULT / OK	65

3.8.1.7	ACTIVE /NOTACTIVE	66

3.8.1.8	NOTACTIVE/ACTIVE	66

3.8.1.9	CLOSE/OPEN	67

3.8.1.10	OPEN/CLOSE	68

3.8.1.11	TRUE/FALSE	68

3.8.1.12	FALSE/TRUE	69

3.8.1.13	BUS_B/BUS_A	70

3.8.1.14	BUS_A/BUS_B	70

3.8.1.15	REMOTE/LOCAL	71

3.8.1.16	LOCAL/REMOTE	72

3.8.1.17	ENABLED/DISABLED	72

3.8.1.18	DISABLED/ ENABLED	73

3.8.1.19	STOP_RUN_PAUSE	73

3.8.1.20	STATUS	74

3.8.1.21	PASSED/FAILED	75

3.8.1.22	FAILED/ PASSED	76

3.8.1.23	ONLINE/OFFLINE	76

3.8.1.24	OFFLINE/ONLINE	77

3.8.1.25	RUNNING/NOT_RUNNING	78

3.8.1.26	NOT_RUNNING/RUNNING	78

3.8.1.27	B/A	79

3.8.1.28	A/B	79

3.8.1.29	Tripped/OK	80

3.8.1.30	GO/NOGO	81

3.8.1.31	NOGO/GO	81

3.8.1.32	SET/RESET	82

3.8.1.33	RESET/SET	83

3.8.2	Discrete Analogue curve	83

3.8.3	Logarithm curve equation data	83

3.8.4	Polynomial Curves	84

3.8.4.1	Thermistor Type GB42	84

3.8.4.2	Thermistor for Platinum Probe 2k 118MF	84

3.9	Displays	85

3.9.1	Alphanumeric display data	85

3.9.2	Graphic display data	85

3.9.3	Scrolling Display	85

3.9.4	Variable SCOS packet display data	85

3.10	Constants	85

3.10.1	Constants	85

4.	Updating Generic Box contents Process	86

5.	Annex 1	86

6.	Annex 2	90

# LIST OF FIGURES AND TABLES

None

# Introduction

This technical note has the objective to identify the generic  items that shall be input on HPSDB central site by the prime company before HPSDB being available to the Users.

Generic items are the items which are not attached to an element, subsystem or model but which can be referenced by any element, subsystem or model. Those items are not instantiated, they are defined in the generic box. HPSDB supports the definition of all items as generic.

All the HPSDB Users have read access to this type of data, but only the HPSDB central site manager has write access. It’s not possible to create/modify/delete generic items on a mirror site.

It is expected that all HPSDB users make use of those generic items in order to avoid unsafe duplication of items ( for instance  several ON / OFF curves with small differences in the way that they are implemented).

In particular, reference must be made to :

- TM PSICD items

One TM PSICD item is present in generic box for each TM service type, and subtype defined on RD1 ( see 3.1.2 TM packet PSICD data). There is no need to create any other TM Packet PSICD or TM Packet Standard.

Note that for TM (8,6),TM(8,7) and TM (8,9) the Function ID and the Activity ID  defined on RD1 as two 8- bit parameters have been merged in an unique 16 bit parameter.

Note : the generic PSICD items contains the structure identifier 1 (SID1) and the structure identifier 2 (SID2) position and length which shall be used by all the Herschel / Planck users (refer to AD1 issue 2.2).

- TC Packet Header items

Two TC packet Header are defined  ( see 3.2.1 TC packet header  data)

- GX000000 has to be refer to by all TC packets defined in RD1 except the standard TC (2,3)

- GX001000 has to be refer to by the standard TC (2,3)

Consequently there is no need to create any other TC packet header nor Command Header parameters items.

An exception to this rule can be envisaged for the testing of TC packet with TC Header rejection. Because a wrong TC packet will not be created on a generic boc.

- Command parameter items

16 Spare command parameters are defined  with value 0 (see 3.7.2 Command Parameters )

- Calibration Curves

35 digital calibration curves are defined (see 3.8.1 Digital curve data )

2 polynomial calibration curves are defined (see 3.8.4 Polynomial Curves )

For the following generic items :

- Calibration curve,

- Command verification stage,

- Parameter range set

This document provides also the S2K identifier which differs from the HPSDB one due to a different format.

In addition due to S2K Command Verification Stage identifier format (integer in the range [0..65535], the HPSDB generic CVS identifier shall be in the range [000-9999], this is not controlled by HPSDB it is the user responsibility to check it.

# Applicable and reference documents

## Applicable documents

| AD1 | H-P-1-ASPI-ID-0141 | Naming convention specification |
| --- | --- | --- |
| AD2 | H-P-1-ASPI-SP-0082 | System Database Specification |

### Reference documents

| RD1 | SCI-PT-ICD-7527 | Packet Structure Interface Control Document |
| --- | --- | --- |
| RD2 | H-P-1-ASPI-SP-0027 | General Design and Interface Requirements |
| RD3 | DSN 3408 02 AA | Thermistor Fenwal N 526-31-bs13-153 with ETFE wire Technical specification supply |
| RD4 | PDS2131 | Product Data Sheet Rev 6/97 |

## Acronyms

| HP | Herschel-Planck |
| --- | --- |
| HPSDB | Herschel / Planck System Data Base |
| TBW | To be write |

## Definition

# Generic items:

## Telemetry:

### TM packet standard

| Field | Value |
| --- | --- |
| TM packet standard | 000TMSD0000000 |
| Short description | TM Packet Standard |
| Long description | TM Standard template Common to Herschel and Planck |

### TM packet PSICD data

#### TM  TC Acceptance Report- Success (1, 1)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS001001000 |
| Short description, | TM_TCAccepSuccess |
| Long description, | Telecommand Acceptance Report – Success (1,1) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 1 |
| Subtype, | 1 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM TC Acceptance Report- Failure (1, 2)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS001002000 |
| Short description, | TM_TCAccepFailure |
| Long description, | Telecommand Acceptance Report – Failure (1,2) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 1 |
| Subtype, | 2 |
| Identifier 1 position, | 20 |
| Identifier 1 width, | 16 |
| Identifier 2 position, | -1 |
| Identifier 2 width, | 0 |

#### TM  TC Execution Report-Started (1, 3)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS001003000 |
| Short description, | TM_TCExeStarted |
| Long description, | Telecommand Execution Report – Started (1,3) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 1 |
| Subtype, | 3 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM TC Execution Report-Progress (1, 5)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS001005000 |
| Short description, | TM_TCExeProgress |
| Long description, | Telecommand Execution Report – Progress (1,5) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 1 |
| Subtype, | 5 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM Execution Report-Completed (1, 7)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS001007000 |
| Short description, | TM_TCExeCompleted |
| Long description, | Telecommand Execution Report – Completed (1,7) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 1 |
| Subtype, | 7 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM TC Execution Report-Failure (1, 8)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS001008000 |
| Short description, | TM_TCExeFailure |
| Long description, | Telecommand Execution Report – Failure (1,8) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 1 |
| Subtype, | 8 |
| Identifier 1 position, | 20 |
| Identifier 1 width, | 16 |
| Identifier 2 position, | -1 |
| Identifier 2 width, | 0 |

#### TM TC Contents Report (1, 9)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS001009000 |
| Short description, | TM_TCContentsReport |
| Long description, | Telecommand Contents Report (1,9) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 1 |
| Subtype, | 9 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM HK Parameter Report Definitions Report (3, 10)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS003010000 |
| Short description, | TM_ HKParameterDefReport |
| Long description, | HK Parameter Report Definitions Report (3,10) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 3 |
| Subtype, | 10 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM Diagnostic Parameter Definition Report (3, 12)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS003012000 |
| Short description, | TM_DiagnosticDefParameter |
| Long description, | Diagnostic Parameter Report Definition Report (3,12) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 3 |
| Subtype, | 12 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM HK Parameter Report (3, 25)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS003025000 |
| Short description, | TM_HKParameterReport |
| Long description, | HK Parameter Report (3,25) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 3 |
| Subtype, | 25 |
| Identifier 1 position, | 16 |
| Identifier 1 width, | 16 |
| Identifier 2 position, | -1 |
| Identifier 2 width, | 0 |

#### TM Diagnostic Parameter Report (3, 26)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS003026000 |
| Short description, | TM_DiagnosticParameter |
| Long description, | Diagnostic Parameter Report (3,26) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 3 |
| Subtype, | 26 |
| Identifier 1 position, | 16 |
| Identifier 1 width, | 16 |
| Identifier 2 position, | -1 |
| Identifier 2 width, | 0 |

#### TM Event Report (5, 1)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS005001000 |
| Short description, | TM_EventReport |
| Long description, | Event Report (5,1) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 5 |
| Subtype, | 1 |
| Identifier 1 position, | 16 |
| Identifier 1 width, | 16 |
| Identifier 2 position, | 18 |
| Identifier 2 width, | 16 |

#### TM Exception Report (5, 2)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS005002000 |
| Short description, | TM_ExceptionReport |
| Long description, | Exception Report (5,2) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 5 |
| Subtype, | 2 |
| Identifier 1 position, | 16 |
| Identifier 1 width, | 16 |
| Identifier 2 position, | 18 |
| Identifier 2 width, | 16 |

#### TM Error/Alarm Report (5,4)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS005004000 |
| Short description, | TM_ErrorAlarmReport |
| Long description, | Error/Alarm Report (5,4) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 5 |
| Subtype, | 4 |
| Identifier 1 position, | 16 |
| Identifier 1 width, | 16 |
| Identifier 2 position, | 18 |
| Identifier 2 width, | 16 |

#### TM Memory Dump, Absolute Addresses (6, 6)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS006006000 |
| Short description, | TM_MemDumpAbsAd |
| Long description, | Memory Dump, Absolute Addresses (6,6) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 6 |
| Subtype, | 6 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM Memory Check Report , Absolute addresses (6, 10)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS006010000 |
| Short description, | TM_MemCheckAbsAd |
| Long description, | Memory Check Report, Absolute addresses (6,10) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 6 |
| Subtype, | 10 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM Function Status Report (8, 6)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS008006000 * |
| Short description, | TM_FunctionStatus |
| Long description, | Function Status Report (8,6) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 8 |
| Subtype, | 6 |
| Identifier 1 position, | 16 |
| Identifier 1 width, | 16 |
| Identifier 2 position, | 18 |
| Identifier 2 width, | 16 |

(*)This generic definition applies if the packet  contains the optional field SID. If the filed SID is not defined inside of the packet a dedicated TM Packet PSICD has to be defined. (This is not compliant with SCOS – PSICD will be modified : TBC)

#### TM SREM Data Report (8, 7)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS008007000 |
| Short description, | TM_SREMDataReport |
| Long description, | SREM Data Report (8,7) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 8 |
| Subtype, | 7 |
| Identifier 1 position, | 16 |
| Identifier 1 width, | 16 |
| Identifier 2 position, | 18 |
| Identifier 2 width, | 16 |

#### TM VMC Data Report (8, 8)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS008008000 |
| Short description, | TM_VMCDataReport |
| Long description, | VMCData Report (8,8) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 8 |
| Subtype, | 8 |
| Identifier 1 position, | 16 |
| Identifier 1 width, | 16 |
| Identifier 2 position, | -1 |
| Identifier 2 width, | 0 |

#### TM Mass Memory Dump Report (8, 9)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS008009000 |
| Short description, | TM_MassMemDump |
| Long description, | Mass Memory Dump Report (8,9) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 8 |
| Subtype, | 9 |
| Identifier 1 position, | 16 |
| Identifier 1 width, | 16 |
| Identifier 2 position, | 18 |
| Identifier 2 width, | 16 |

#### TM Central Time Reference (9, 8)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS009008000 |
| Short description, | TM_CentralTimeReference |
| Long description, | Central Time Reference (9,8) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 9 |
| Subtype, | 8 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM Time Verification Report (9, 9)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS009009000 |
| Short description, | TM_TimeVerification |
| Long description, | Time Verification Report (9,9) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 9 |
| Subtype, | 9 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM Detailed Schedule Report (11, 10)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS011010000 |
| Short description, | TM_DetailedSchedule |
| Long description, | Detailed Schedule Report (11,10) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 11 |
| Subtype, | 10 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM Summary Schedule Report (11, 13)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS011013000 |
| Short description, | TM_SummarySchedule |
| Long description, | Summary Schedule Report (11,13) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 11 |
| Subtype, | 13 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM Command Schedule Status Report (11, 19)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS011019000 |
| Short description, | TM_CmdScheduleStatus |
| Long description, | Command Schedule Status Report (11,19) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 11 |
| Subtype, | 19 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM Current Monitoring List Report (12, 9)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS012009000 |
| Short description, | TM_CurrentMonitorList |
| Long description, | Current Monitoring List Report (12,9) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 12 |
| Subtype, | 9 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM Enabled Telemetry Packets Report (14, 4)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS014004000 |
| Short description, | TM_EnabTMPacket |
| Long description, | Enabled Telemetry Packets Report (14,4) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 14 |
| Subtype, | 4 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM TM Packets Down-linking / Storage Status Report (14, 7)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS014007000 |
| Short description, | TM_DownLink |
| Long description, | TM Packets Down-link. / Stor. Status Report |
| TM packet standard , | 000TMSD0000000 |
| Type, | 14 |
| Subtype, | 7 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM Storage Selection Definition Report (15, 6)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS015006000 |
| Short description, | TM_StorageSelecDef |
| Long description, | Storage Selection Definition Report (15,6) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 15 |
| Subtype, | 6 |
| Identifier 1 position, | 16 |
| Identifier 1 width, | 8 |
| Identifier 2 position, | -1 |
| Identifier 2 width, | 0 |

#### TM Packet Stores Catalogue Report (15, 13)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS015013000 |
| Short description, | TM_PacketStoresCatalogue |
| Long description, | Packet Stores Catalogue Report (15,13) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 15 |
| Subtype, | 13 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM Connection Test Report (17, 2)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS017002000 |
| Short description, | TM_ConnectionTest |
| Long description, | Connection Test Report (17,2) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 17 |
| Subtype, | 2 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM On-Board Control Procedures List Report (18, 9)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS018009000 |
| Short description, | TM_OnBoardCtProc |
| Long description, | On-Board Control Procedures List Report (18,9) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 18 |
| Subtype, | 9 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM Active OBCPs List Report (18, 11)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS018011000 |
| Short description, | TM_ActiveOBCPList |
| Long description, | Active OBCPs List Report (18,11) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 18 |
| Subtype, | 11 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM OBCP Status Report (18, 13)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS018013000 |
| Short description, | TM_OBCPStatus |
| Long description, | OBCP Status Report (18,13) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 18 |
| Subtype, | 13 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM OBCP Contents Report (18, 15)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS018015000 |
| Short description, | TM_OBCPContents |
| Long description, | OBCP Contents Report (18,15) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 18 |
| Subtype, | 15 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM Event Detection List Report (19, 7)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS019007000 |
| Short description, | TM_EventDetecList |
| Long description, | Event Detection List Report (19,7) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 19 |
| Subtype, | 7 |
| Identifier 1 position, | -1 |
| Identifier 1 width, | 0 |
| Identifier 2 position, |  |
| Identifier 2 width, |  |

#### TM Nominal Science Data Report (21, 1)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS021001000 |
| Short description, | TM_NominalScienceData |
| Long description, | Nominal Science Data Report (21,1) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 21 |
| Subtype, | 1 |
| Identifier 1 position, | 16 |
| Identifier 1 width, | 16 |
| Identifier 2 position, | -1 |
| Identifier 2 width, | 0 |

Note: no structure identifier extracted as far as it is science data.

#### TM Science Type B Data Report (21, 2)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS021002000 |
| Short description, | TM_ScienceTypeBData |
| Long description, | Science Type B Data Report (21,2) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 21 |
| Subtype, | 2 |
| Identifier 1 position, | 16 |
| Identifier 1 width, | 16 |
| Identifier 2 position, | -1 |
| Identifier 2 width, | 0 |

Note: no structure identifier extracted as far as it is science data.

#### TM Diagnostic Science Data Report (21, 3)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS021003000 |
| Short description, | TM_DiagScienceData |
| Long description, | Diagnostic Science Data Report (21,3) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 21 |
| Subtype, | 3 |
| Identifier 1 position, | 16 |
| Identifier 1 width, | 16 |
| Identifier 2 position, | -1 |
| Identifier 2 width, | 0 |

Note: no structure identifier extracted as far as it is science data.

#### TM Auxiliary Science Data Report (21, 4)

| Field | Value |
| --- | --- |
| TM packet PSICD identifier, | 000TMPS021004000 |
| Short description, | TM_AuxScienceData |
| Long description, | Auxiliary Science Data Report (21,4) |
| TM packet standard , | 000TMSD0000000 |
| Type, | 21 |
| Subtype, | 4 |
| Identifier 1 position, | 16 |
| Identifier 1 width, | 16 |
| Identifier 2 position, | -1 |
| Identifier 2 width, | 0 |

Note: no structure identifier extracted as far as it is science data.

### TM Packet Data

Not identified

### TM Packet SCOS archiving

TBW. Waiting for clarification  with ALS & Terma

### TM structure data

Not identified

### TM packet group data

Not identified

## Telecommands

### TC packet header  data

Two TC packet headers are defined for the Herschel Planck project :

#### TC Packet Header With Data Field Header

| Field | Value |
| --- | --- |
| TC packet header identifier | GX000000 |
| Short description | TC_PacketHeader_DFHis1 |
| Long description | TC Packet Header with Data field Header (DFH=1) |
| List of parameter : |  |
| TC packet parameter identifier, | Version Number |
| TC packet parameter type, | Fixed Area |
| Bit offset, | 0 |
| Length | 3 |
| Value, | 0 |
| Radix. | Decimal |
| TC packet parameter identifier, | Type |
| TC packet parameter type, | Fixed Area |
| Bit offset, | 3 |
| Length | 1 |
| Value, | 1 |
| Radix. | Decimal |
| TC packet parameter identifier, | DFH |
| TC packet parameter type, | Fixed Area |
| Bit offset, | 4 |
| Length | 1 |
| Value, | 1 |
| Radix. | Decimal |
| TC packet parameter identifier, | GBAPD000 |
| TC packet parameter type, | APID |
| Bit offset, | 5 |
| Length | 11 |
| Value, |  |
| Radix. | Decimal |
| TC packet parameter identifier, | Seq Flag |
| TC packet parameter type, | Fixed Area |
| Bit offset, | 16 |
| Length | 2 |
| Value, | 3 |
| Radix. | Decimal |
| TC packet parameter identifier, | GBSCT000 |
| TC packet parameter type, | Parameter |
| Bit offset, | 18 |
| Length | 3 |
| Value, |  |
| Radix. | Decimal |
| TC packet parameter identifier, | GBSCS000 |
| TC packet parameter type, | Parameter |
| Bit offset, | 21 |
| Length | 11 |
| Value, |  |
| Radix. | Decimal |
| TC packet parameter identifier, | GBLEN000 |
| TC packet parameter type, | Parameter |
| Bit offset, | 32 |
| Length | 16 |
| Value, |  |
| Radix. | Decimal |
| TC packet parameter identifier, | Sec Header |
| TC packet parameter type, | Fixed Aread |
| Bit offset, | 48 |
| Length | 1 |
| Value, | 0 |
| Radix. | Decimal |
| TC packet parameter identifier, | PUS |
| TC packet parameter type, | Fixed Area |
| Bit offset, | 49 |
| Length | 3 |
| Value, | 0 |
| Radix. | Decimal |
| TC packet parameter identifier, | GBACK000 |
| TC packet parameter type, | Acknowledgment |
| Bit offset, | 52 |
| Length | 4 |
| Value, |  |
| Radix. | Decimal |
| TC packet parameter identifier, | GBTYP000 |
| TC packet parameter type, | Type |
| Bit offset, | 56 |
| Length | 8 |
| Value, |  |
| Radix. | Decimal |
| TC packet parameter identifier, | GBSTY000 |
| TC packet parameter type, | Subtype |
| Bit offset, | 64 |
| Length | 8 |
| Value, |  |
| Radix. | Decimal |
| TC packet parameter identifier, | Spare |
| TC packet parameter type, | Fixed Area |
| Bit offset, | 72 |
| Length | 8 |
| Value, | 0 |
| Radix. | Decimal |

#### TC Packet Header Without Data Field Header

| Field | Value |
| --- | --- |
| TC packet header identifier | GX002000 |
| Short description | TC_PacketHeader_DFHis0 |
| Long description | TC Packet Header without Data Field Header (DFH=0) |
| List of parameter : |  |
| TC packet parameter identifier, | Version Number |
| TC packet parameter type, | Fixed Area |
| Bit offset, | 0 |
| Length | 3 |
| Value, | 0 |
| Radix. | Decimal |
| TC packet parameter identifier, | Type |
| TC packet parameter type, | Fixed Area |
| Bit offset, | 3 |
| Length | 1 |
| Value, | 1 |
| Radix. | Decimal |
| TC packet parameter identifier, | NDF |
| TC packet parameter type, | Fixed Area |
| Bit offset, | 4 |
| Length | 1 |
| Value, | 0 |
| Radix. | Decimal |
| TC packet parameter identifier, | GBAPD000 |
| TC packet parameter type, | APID |
| Bit offset, | 5 |
| Length | 11 |
| Value, |  |
| Radix. | Decimal |
| TC packet parameter identifier, | Seq Flag |
| TC packet parameter type, | Fixed Area |
| Bit offset, | 16 |
| Length | 2 |
| Value, | 3 |
| Radix. | Decimal |
| TC packet parameter identifier, | GBSCT000 |
| TC packet parameter type, | Parameter |
| Bit offset, | 18 |
| Length | 3 |
| Value, |  |
| Radix. | Decimal |
| TC packet parameter identifier, | GBSCS000 |
| TC packet parameter type, | Parameter |
| Bit offset, | 21 |
| Length | 11 |
| Value, |  |
| Radix. | Decimal |
| TC packet parameter identifier, | GBLEN000 |
| TC packet parameter type, | Parameter |
| Bit offset, | 32 |
| Length | 16 |
| Value, |  |
| Radix. | Decimal |

Note:

For TC packet  type = 2, subtype = 3 and ,APID=0, and MAPID =0, the TC packet header to be used is

GX0001000 (ie with data field header flag set to 0 : no data field header)

For TC packet  type = 2, subtype = 3 and ,APID=16, and MAPID =1, the TC packet header to be used is

GX0000000 (ie with data field header flag set to 1 : existing data field header)

### TC packet data

Not identified.

### TC structure data

Not identified

### TC packet group data

Not identified

## Command Sequences

### Command Sequences

Not identified

## Command verification

Not identified

Note : in case generic command verification are defined, the S2K identifier shall be provided and shall be equal to the element command verification stagte identifier plus 10000.

### Command verification

Not identified

## 1553 Messages

### Command word

Not identified

### 1553 Status word data

Not identified

### 1553 Message data

Not identified

### 1553 Acquisition command link

Not identified

### 1553 Structure

Not identified

### 1553 Message group data

Not identified

## OBDH

### OBDH interrogation

Not identified

### OBDH acquisition command link

Not identified

### OBDH interrogation group data

Not identified

## Parameters

### Command Header Parameters

#### APID

| Field | Value |
| --- | --- |
| Item name | GBAPD000 |
| Short description | APID |
| Long Description | Packet APID |
| Reason of change | Generic Data |
| Parameter Type | Command Header Parameter |
| Parameter Type -Type | A |
| Parameter Type -Value |  |
| Parameter Type –Raw Radix | D |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 3 |
| PFC | 7 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Sequence Count Source Part

| Field | Value |
| --- | --- |
| Item name | GBSCT000 |
| Short description | Seq Count - Source |
| Long Description | Sequence Count - Source Part |
| Reason of change | Generic Data |
| Parameter Type | Command Header Parameter |
| Parameter Type -Type | P |
| Parameter Type -Value |  |
| Parameter Type –Raw Radix | D |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 2 |
| PFC | 3 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Sequence Count Sequence Part

| Field | Value |
| --- | --- |
| Item name | GBSCF000 |
| Short description | Seq Count - Seq |
| Long Description | Sequence Count – Sequence Part |
| Reason of change | Generic Data |
| Parameter Type | Command Header Parameter |
| Parameter Type -Type | P |
| Parameter Type -Value |  |
| Parameter Type –Raw Radix | D |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 3 |
| PFC | 7 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Packet Length

| Field | Value |
| --- | --- |
| Item name | GBLEN000 |
| Short description | Packet Length |
| Long Description | Packet Length |
| Reason of change | Generic Data |
| Parameter Type | Command Header Parameter |
| Parameter Type -Type | P |
| Parameter Type -Value |  |
| Parameter Type –Raw Radix | D |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 3 |
| PFC | 12 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Acknowledgement flags

| Field | Value |
| --- | --- |
| Item name | GBACK000 |
| Short description | Ack |
| Long Description | Acknowledgement |
| Reason of change | Generic Data |
| Parameter Type | Command Header Parameter |
| Parameter Type -Type | K |
| Parameter Type -Value |  |
| Parameter Type –Raw Radix | D |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 2 |
| PFC | 4 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Packet Type

| Field | Value |
| --- | --- |
| Item name | GBTYP000 |
| Short description | Packet Type |
| Long Description | Packet Type |
| Reason of change | Generic Data |
| Parameter Type | Command Header Parameter |
| Parameter Type -Type | T |
| Parameter Type -Value |  |
| Parameter Type –Raw Radix | D |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 2 |
| PFC | 8 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Packet Subtype

| Field | Value |
| --- | --- |
| Item name | GBSTY000 |
| Short description | Packet Subtype |
| Long Description | Packet Subtype |
| Reason of change | Generic Data |
| Parameter Type | Command Header Parameter |
| Parameter Type -Type | S |
| Parameter Type -Value |  |
| Parameter Type –Raw Radix | D |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 2 |
| PFC | 8 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

### Command Parameters

Note please that on HPSDB is possible to include fixed areas on the TC packets, so a spare can be defined as a fixed area, or can be a reference to the following generic command parameters:

#### Spare 1 - Bit

| Field | Value |
| --- | --- |
| Item name | GPS01000 |
| Short description | SPARE_1_BIT |
| Long Description | Spare 1 bit |
| Reason of change | Generic Data |
| Parameter Type | Command Parameter |
| Parameter Type –Raw Radix | Hexadecimal |
| Parameter Type – Default Value representation | 0 |
| Parameter Type –Constant or value flag | D |
| Parameter Type –Generic or contant identifier |  |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 2 |
| PFC | 1 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Spare 2 - Bit

| Field | Value |
| --- | --- |
| Item name | GPS02000 |
| Short description | SPARE_2_BIT |
| Long Description | Spare 2 bits |
| Reason of change | Generic Data |
| Parameter Type | Command Parameter |
| Parameter Type –Raw Radix | Hexadecimal |
| Parameter Type – Default Value representation | 0 |
| Parameter Type –Constant or value flag | D |
| Parameter Type –Generic or contant identifier |  |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 2 |
| PFC | 2 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Spare 3 - Bit

| Field | Value |
| --- | --- |
| Item name | GPS03000 |
| Short description | SPARE_3_BIT |
| Long Description | Spare 3 bits |
| Reason of change | Generic Data |
| Parameter Type | Command Parameter |
| Parameter Type –Raw Radix | Hexadecimal |
| Parameter Type – Default Value representation | 0 |
| Parameter Type –Constant or value flag | D |
| Parameter Type –Generic or contant identifier |  |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 2 |
| PFC | 3 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Spare 4 - Bit

| Field | Value |
| --- | --- |
| Item name | GPS04000 |
| Short description | SPARE_4_BIT |
| Long Description | Spare 4 bits |
| Reason of change | Generic Data |
| Parameter Type | Command Parameter |
| Parameter Type –Raw Radix | Hexadecimal |
| Parameter Type – Default Value representation | 0 |
| Parameter Type –Constant or value flag | D |
| Parameter Type –Generic or contant identifier |  |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 2 |
| PFC | 4 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Spare 5 - Bit

| Field | Value |
| --- | --- |
| Item name | GPS05000 |
| Short description | SPARE_5_BIT |
| Long Description | Spare 5 bits |
| Reason of change | Generic Data |
| Parameter Type | Command Parameter |
| Parameter Type –Raw Radix | Hexadecimal |
| Parameter Type – Default Value representation | 0 |
| Parameter Type –Constant or value flag | D |
| Parameter Type –Generic or contant identifier |  |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 2 |
| PFC | 5 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Spare 6 - Bit

| Field | Value |
| --- | --- |
| Item name | GPS06000 |
| Short description | SPARE_6_BIT |
| Long Description | Spare 6 bits |
| Reason of change | Generic Data |
| Parameter Type | Command Parameter |
| Parameter Type –Raw Radix | Hexadecimal |
| Parameter Type – Default Value representation | 0 |
| Parameter Type –Constant or value flag | D |
| Parameter Type –Generic or contant identifier |  |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 2 |
| PFC | 6 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Spare 7 - Bit

| Field | Value |
| --- | --- |
| Item name | GPST0700 |
| Short description | SPARE_7_BIT |
| Long Description | Spare 7 bits |
| Reason of change | Generic Data |
| Parameter Type | Command Parameter |
| Parameter Type –Raw Radix | Hexadecimal |
| Parameter Type – Default Value representation | 0 |
| Parameter Type –Constant or value flag | D |
| Parameter Type –Generic or contant identifier |  |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 2 |
| PFC | 7 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Spare 8 - Bit

| Field | Value |
| --- | --- |
| Item name | GPS08000 |
| Short description | SPARE_8_BIT |
| Long Description | Spare 8 bits |
| Reason of change | Generic Data |
| Parameter Type | Command Parameter |
| Parameter Type –Raw Radix | Hexadecimal |
| Parameter Type – Default Value representation | 0 |
| Parameter Type –Constant or value flag | D |
| Parameter Type –Generic or contant identifier |  |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 2 |
| PFC | 8 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Spare 9- Bit

| Field | Value |
| --- | --- |
| Item name | GPS09000 |
| Short description | SPARE_9_BIT |
| Long Description | Spare 9 bits |
| Reason of change | Generic Data |
| Parameter Type | Command Parameter |
| Parameter Type –Raw Radix | Hexadecimal |
| Parameter Type – Default Value representation | 0 |
| Parameter Type –Constant or value flag | D |
| Parameter Type –Generic or contant identifier |  |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 3 |
| PFC | 5 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Spare 10 - Bit

| Field | Value |
| --- | --- |
| Item name | GPS10000 |
| Short description | SPARE_10_BIT |
| Long Description | Spare 10 bits |
| Reason of change | Generic Data |
| Parameter Type | Command Parameter |
| Parameter Type –Raw Radix | Hexadecimal |
| Parameter Type – Default Value representation | 0 |
| Parameter Type –Constant or value flag | D |
| Parameter Type –Generic or contant identifier |  |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 3 |
| PFC | 6 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Spare 11- Bit

| Field | Value |
| --- | --- |
| Item name | GPS11000 |
| Short description | SPARE_11_BIT |
| Long Description | Spare 11 bits |
| Reason of change | Generic Data |
| Parameter Type | Command Parameter |
| Parameter Type –Raw Radix | Hexadecimal |
| Parameter Type – Default Value representation | 0 |
| Parameter Type –Constant or value flag | D |
| Parameter Type –Generic or contant identifier |  |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 3 |
| PFC | 7 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Spare 12- Bit

| Field | Value |
| --- | --- |
| Item name | GPS12000 |
| Short description | SPARE_12_BIT |
| Long Description | Spare 12 bits |
| Reason of change | Generic Data |
| Parameter Type | Command Parameter |
| Parameter Type –Raw Radix | Hexadecimal |
| Parameter Type – Default Value representation | 0 |
| Parameter Type –Constant or value flag | D |
| Parameter Type –Generic or contant identifier |  |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 3 |
| PFC | 8 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Spare 13 - Bit

| Field | Value |
| --- | --- |
| Item name | GPS13000 |
| Short description | SPARE_13_BIT |
| Long Description | Spare 13 bits |
| Reason of change | Generic Data |
| Parameter Type | Command Parameter |
| Parameter Type –Raw Radix | Hexadecimal |
| Parameter Type – Default Value representation | 0 |
| Parameter Type –Constant or value flag | D |
| Parameter Type –Generic or contant identifier |  |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 3 |
| PFC | 9 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Spare 14 - Bit

| Field | Value |
| --- | --- |
| Item name | GPS14000 |
| Short description | SPARE_14_BIT |
| Long Description | Spare 14 bits |
| Reason of change | Generic Data |
| Parameter Type | Command Parameter |
| Parameter Type –Raw Radix | Hexadecimal |
| Parameter Type – Default Value representation | 0 |
| Parameter Type –Constant or value flag | D |
| Parameter Type –Generic or contant identifier |  |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 3 |
| PFC | 10 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Spare 15 - Bit

| Field | Value |
| --- | --- |
| Item name | GPS15000 |
| Short description | SPARE_15_BIT |
| Long Description | Spare 15 bits |
| Reason of change | Generic Data |
| Parameter Type | Command Parameter |
| Parameter Type –Raw Radix | Hexadecimal |
| Parameter Type – Default Value representation | 0 |
| Parameter Type –Constant or value flag | D |
| Parameter Type –Generic or contant identifier |  |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 3 |
| PFC | 11 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

#### Spare 16- Bit

| Field | Value |
| --- | --- |
| Item name | GPS16000 |
| Short description | SPARE_16_BIT |
| Long Description | Spare 16 bits |
| Reason of change | Generic Data |
| Parameter Type | Command Parameter |
| Parameter Type –Raw Radix | Hexadecimal |
| Parameter Type – Default Value representation | 0 |
| Parameter Type –Constant or value flag | D |
| Parameter Type –Generic or contant identifier |  |
| Validity Condition | - |
| Validity Condition -Parameter identifier | - |
| Validity Condition -Raw or engineering value flag | - |
| Validity Condition -Parameter Value | - |
| Binary Conversion | - |
| PTC | 3 |
| PFC | 12 |
| Calibration Category | - |
| Units | - |
| Default Calibration curve-Type | - |
| Calibration curve identifier | - |
| Ordered list of condition for calibration curve selection | - |
| Order | - |
| Condition parameter | - |
| Condition Raw or engineering flag | - |
| Condition Radix | - |
| Condition value | - |
| Curve Subtype | - |
| Calibration curve identifier | - |
| Limit calibration | - |
| Maximum number of over-limit occurrences acceptable | - |
| List of limits | - |
| Order | - |
| Condition Parameter | - |
| Condition Raw or engineering flag | - |
| Condition Parameter value | - |
| Type | - |
| Low Limit | - |
| Hight limit | - |
| Category flag | - |

### Parameter group data

Not identified

### Parameter set data

Not identified

### Parameter value set

Not identified

### Parameter range set data

Not identified

Note : in case generic parameter range set are defined, the S2K identifier shall be provided and shall be equal to the element parameter range set identifier plus 1000.

## Calibration Curves

Wainting for thermostors calibration curves inputs.

Note The S2K identifier is equal to element curve identifier inside the element (from fourth to sixth characters) plus 1000.

### Digital curve data

In case of one bit digital raw value, the short description of the curve is the label associated to the raw value 1.

The identified generic digital curves are:

#### OFF/ON

0 is ON

1 is is OFF

| Field | Value |
| --- | --- |
| Curve identifier | 000001 |
| S2K identifier | 1001 |
| Short description | OFF |
| Long description | 1 is OFF 0 is ON |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | ON |
| Low raw value | 1 |
| High raw value | 1 |
| Status | OFF |

#### ON / OFF

0 is OFF

1 is is ON

| Field | Value |
| --- | --- |
| Curve identifier | 000002 |
| S2K identifier | 1002 |
| Short description | ON |
| Long description | 1 is ON 0 is OFF |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | OFF |
| Low raw value | 1 |
| High raw value | 1 |
| Status | ON |

#### NOMINAL / REDUNDANT

0 is REDUNDANT

1 is is NOMINAL

| Field | Value |
| --- | --- |
| Curve identifier | 000003 |
| S2K identifier | 1003 |
| Short description | NOMINAL |
| Long description | 1 is NOMINAL 0 is REDUNDANT |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | REDUNDANT |
| Low raw value | 1 |
| High raw value | 1 |
| Status | NOMINAL |

#### REDUNDANT / NOMINAL

0 is NOMINAL

1 is is REDUNDANT

| Field | Value |
| --- | --- |
| Curve identifier | 000004 |
| S2K identifier | 1004 |
| Short description | REDUNDANT |
| Long description | 1 is REDUNDANT 0 is NOMINAL |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | NOMINAL |
| Low raw value | 1 |
| High raw value | 1 |
| Status | REDUNDANT |

#### OK / FAULT

0 is FAULT

1 is is OK

| Field | Value |
| --- | --- |
| Curve identifier | 000005 |
| S2K identifier | 1005 |
| Short description | OK |
| Long description | 1 is OK 0 is FAULT |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | FAULT |
| Low raw value | 1 |
| High raw value | 1 |
| Status | OK |

#### FAULT / OK

0 is OK

1 is is FAULT

| Field | Value |
| --- | --- |
| Curve identifier | 000006 |
| S2K identifier | 1006 |
| Short description | FAULT |
| Long description | 1 is FAULT 0 is OK |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | OK |
| Low raw value | 1 |
| High raw value | 1 |
| Status | FAULT |

#### ACTIVE /NOTACTIVE

0 is NOTACTIVE

1 is is ACTIVE

| Field | Value |
| --- | --- |
| Curve identifier | 000007 |
| S2K | 1007 |
| Short description | ACTIVE |
| Long description | 1 is ACTIVE 0 is NOTACTIVE |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | NOTACTIVE |
| Low raw value | 1 |
| High raw value | 1 |
| Status | ACTIVE |

#### NOTACTIVE/ACTIVE

0 is ACTIVE

1 is is NOTACTIVE

| Field | Value |
| --- | --- |
| Curve identifier | 000008 |
| S2K identifier | 1008 |
| Short description | NOTACTIVE |
| Long description | 1 is NOTACTIVE 0 is ACTIVE |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | ACTIVE |
| Low raw value | 1 |
| High raw value | 1 |
| Status | NOTACTIVE |

#### CLOSE/OPEN

0 is OPEN

1 is is CLOSE

| Field | Value |
| --- | --- |
| Curve identifier | 000009 |
| S2K identifier | 1009 |
| Short description | CLOSE |
| Long description | 1 is CLOSE 0 is OPEN |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | OPEN |
| Low raw value | 1 |
| High raw value | 1 |
| Status | CLOSE |

#### OPEN/CLOSE

0 is CLOSE

1 is is OPEN

| Field | Value |
| --- | --- |
| Curve identifier | 000010 |
| S2K identifier | 1010 |
| Short description | OPEN |
| Long description | 1 is OPEN 0 is CLOSE |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | CLOSE |
| Low raw value | 1 |
| High raw value | 1 |
| Status | OPEN |

#### TRUE/FALSE

0 is FALSE

1 is TRUE

| Field | Value |
| --- | --- |
| Curve identifier | 000013 |
| S2K identifier | 1013 |
| Short description | TRUE |
| Long description | 1 is TRUE 0 is FALSE |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | FALSE |
| Low raw value | 1 |
| High raw value | 1 |
| Status | TRUE |

#### FALSE/TRUE

0 is TRUE

1 is FALSE

| Field | Value |
| --- | --- |
| Curve identifier | 000024 |
| S2K identifier | 1024 |
| Short description | FALSE |
| Long description | 1 is FALSE 0 is TRUE |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | TRUE |
| Low raw value | 1 |
| High raw value | 1 |
| Status | FALSE |

#### BUS_B/BUS_A

0 is BUS_A

1 is BUS_B

| Field | Value |
| --- | --- |
| Curve identifier | 000015 |
| S2K identifier | 1015 |
| Short description | BUS_B |
| Long description | 1 is BUS_B 0 is BUS_A |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | BUS_A |
| Low raw value | 1 |
| High raw value | 1 |
| Status | BUS_B |

#### BUS_A/BUS_B

0 is BUS_B

1 is BUS_A

| Field | Value |
| --- | --- |
| Curve identifier | 000025 |
| S2K identifier | 1025 |
| Short description | BUS_A |
| Long description | 1 is BUS_A 0 is BUS_B |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | BUS_B |
| Low raw value | 1 |
| High raw value | 1 |
| Status | BUS_A |

#### REMOTE/LOCAL

0 is REMOTE

1 is LOCAL

| Field | Value |
| --- | --- |
| Curve identifier | 000016 |
| S2K identifier | 1016 |
| Short description | REMOTE |
| Long description | 1 is REMOTE 0 is LOCAL |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | LOCAL |
| Low raw value | 1 |
| High raw value | 1 |
| Status | REMOTE |

#### LOCAL/REMOTE

0 is REMOTE

1 is LOCAL

| Field | Value |
| --- | --- |
| Curve identifier | 000026 |
| S2K identifier | 1026 |
| Short description | LOCAL |
| Long description | 1 is LOCAL 0 is REMOTE |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | REMOTE |
| Low raw value | 1 |
| High raw value | 1 |
| Status | LOCAL |

#### ENABLED/DISABLED

0 is DISABLED

1 is ENABLED

| Field | Value |
| --- | --- |
| Curve identifier | 000017 |
| S2K identifier | 1017 |
| Short description | ENABLED |
| Long description | 1 is ENABLED 0 is DISABLED |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | DISABLED |
| Low raw value | 1 |
| High raw value | 1 |
| Status | ENABLED |

#### DISABLED/ ENABLED

0 is ENABLED

1 is DISABLED

| Field | Value |
| --- | --- |
| Curve identifier | 000027 |
| S2K identifier | 1027 |
| Short description | DISABLED |
| Long description | 1 is DISABLED 0 is ENABLED |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | ENABLED |
| Low raw value | 1 |
| High raw value | 1 |
| Status | DISABLED |

#### STOP_RUN_PAUSE

0 is STOP

1 is RUN

2 IS PAUSE

| Field | Value |
| --- | --- |
| Curve identifier | 000018 |
| S2K identifier | 1018 |
| Short description | STOP_RUN_PAUSE |
| Long description | 0 is STOP 1 is RUN 2 IS PAUSE |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | STOP |
| Low raw value | 1 |
| High raw value | 1 |
| Status | RUN |
| Low raw value | 1 |
| High raw value | 1 |
| Status | PAUSE |

#### STATUS

0 is CONFIG

1 is IDLE

2 is OPERATIONAL

3 is ERROR

| Field | Value |
| --- | --- |
| Curve identifier | 000019 |
| S2K identifier | 1019 |
| Short description | STATUS |
| Long description | 0 is CONFIG 1 is IDLE 2 is OPERATIONAL 3 is ERROR |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | CONFIG |
| Low raw value | 1 |
| High raw value | 1 |
| Status | IDLE |
| Low raw value | 2 |
| High raw value | 2 |
| Status | OPERATIONAL |
| Low raw value | 3 |
| High raw value | 3 |
| Status | ERROR |

#### PASSED/FAILED

0 is PASSED

1 is FAILED

| Field | Value |
| --- | --- |
| Curve identifier | 000020 |
| S2K identifier | 1020 |
| Short description | PASSED |
| Long description | 1 is PASSED 0 is FAILED |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | FAILED |
| Low raw value | 1 |
| High raw value | 1 |
| Status | PASSED |

#### FAILED/ PASSED

0 is FAILED

1 is PASSED

| Field | Value |
| --- | --- |
| Curve identifier | 000028 |
| S2K identifier | 1028 |
| Short description | FAILED |
| Long description | 1 is FAILED 0 is PASSED |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | PASSED |
| Low raw value | 1 |
| High raw value | 1 |
| Status | FAILED |

#### ONLINE/OFFLINE

0 is OFFLINE

1 is ONLINE

| Field | Value |
| --- | --- |
| Curve identifier | 000021 |
| S2K identifier | 1021 |
| Short description | ONLINE |
| Long description | 1 is ONLINE 0 is OFFLINE |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | OFFLINE |
| Low raw value | 1 |
| High raw value | 1 |
| Status | ONLINE |

#### OFFLINE/ONLINE

0 is ONLINE

1 is OFFLINE

| Field | Value |
| --- | --- |
| Curve identifier | 000029 |
| S2K identifier | 1029 |
| Short description | OFFLINE |
| Long description | 1 is OFFLINE 0 is ONLINE |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | ONLINE |
| Low raw value | 1 |
| High raw value | 1 |
| Status | OFFLINE |

#### RUNNING/NOT_RUNNING

0 is NOT_RUNNING

1 is  RUNNING

| Field | Value |
| --- | --- |
| Curve identifier | 000022 |
| S2K identifier | 1022 |
| Short description | RUNNING |
| Long description | 1 is RUNNING 0 is NOT_RUNNING |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | NOT_RUNNING |
| Low raw value | 1 |
| High raw value | 1 |
| Status | RUNNING |

#### NOT_RUNNING/RUNNING

0 is RUNNING

1 is NOT RUNNING

| Field | Value |
| --- | --- |
| Curve identifier | 000030 |
| S2K identifier | 1030 |
| Short description | NOT_RUNNING |
| Long description | 1 is NOT_RUNNING 0 is RUNNING |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | RUNNING |
| Low raw value | 1 |
| High raw value | 1 |
| Status | NOT_RUNNING |

#### B/A

0 is A

1 is B

| Field | Value |
| --- | --- |
| Curve identifier | 000023 |
| S2K identifier | 1023 |
| Short description | B |
| Long description | 1 is B 0 is A |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | A |
| Low raw value | 1 |
| High raw value | 1 |
| Status | B |

#### A/B

0 is B

1 is A

| Field | Value |
| --- | --- |
| Curve identifier | 000031 |
| S2K identifier | 1031 |
| Short description | A |
| Long description | 1 is A 0 is B |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | B |
| Low raw value | 1 |
| High raw value | 1 |
| Status | A |

#### Tripped/OK

0 is OK

1 is Tripped

| Field | Value |
| --- | --- |
| Curve identifier | 000014 |
| S2K identifier | 1014 |
| Short description | Tripped |
| Long description | 1 is tripped 0 is OK |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | OK |
| Low raw value | 1 |
| High raw value | 1 |
| Status | Tripped |

#### GO/NOGO

0 is NOGO

1 is GO

| Field | Value |
| --- | --- |
| Curve identifier | 000032 |
| S2K identifier | 1032 |
| Short description | GO |
| Long description | 1 is GO 0 is NOGO |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | NOGO |
| Low raw value | 1 |
| High raw value | 1 |
| Status | GO |

#### NOGO/GO

0 is GO

1 is NOGO

| Field | Value |
| --- | --- |
| Curve identifier | 000033 |
| S2K identifier | 1033 |
| Short description | NOGO |
| Long description | 1 is NOGO 0 is GO |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | GO |
| Low raw value | 1 |
| High raw value | 1 |
| Status | NOGO |

#### SET/RESET

0 is RESET

1 is SET

| Field | Value |
| --- | --- |
| Curve identifier | 000034 |
| S2K identifier | 1034 |
| Short description | SET |
| Long description | 1 is SET 0 is RESET |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | RESET |
| Low raw value | 1 |
| High raw value | 1 |
| Status | SET |

#### RESET/SET

0 is SET

1 is RESET

| Field | Value |
| --- | --- |
| Curve identifier | 000035 |
| S2K identifier | 1035 |
| Short description | RESET |
| Long description | 1 is RESET 0 is SET |
| Type (analogue or digital) | Digital |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | NULL |
| Unit | NULL |
| TM or TC or both flag | Both flag |
| Raw format | Unsigned integer |

| Field | Value |
| --- | --- |
| Low raw value | 0 |
| High raw value | 0 |
| Status | SET |
| Low raw value | 1 |
| High raw value | 1 |
| Status | RESET |

### Discrete Analogue curve

Not identified

### Logarithm curve equation data

Not identified

### Polynomial Curves

#### Thermistor Type GB42

This curve was been calculated using the Resistance Temperature Relationship Table for Thermistor type GB42 on Annex 1.

| Field | Value |
| --- | --- |
| Curve identifier | 000011 |
| S2K identifier | 1011 |
| Short description | Curve_GB42 |
| Long description | This curve was been calculated using the Resistance Temperature Relationship Table for Thermistor type GB42 see annex, the range [-40,+85ºC] is specify on the GDIR (version 4.1) H-P-1-ASPI-SP-0027 RD2 |
| Type (analogue or digital) | Analogue |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | Polynomial |
| Unit | Celsius degree |
| TM or TC or both flag | Both flag |

| Field | Value |
| --- | --- |
| a0 | 39591.1 |
| a1 | -2075.9885 |
| a2 | 76.196331 |
| a3 | -1.3738253 |
| a4 | 0.0084341711 |

#### Thermistor for Platinum Probe 2k 118MF

This curve was been calculated using the Resistance Temperature Relationship Table for Platinum Probe 2k 118MF on Annex 2.

| Field | Value |
| --- | --- |
| Curve identifier | 000012 |
| S2K identifier | 1012 |
| Short description | Curve_118MF |
| Long description | This curve was been calculated using the Resistance Temperature Relationship Table for Platinum Probe 2k 118MF see annex. |
| Type (analogue or digital) | Analogue |
| Sub-type for analogue type (Discrete or polynomial or logarithm) | Polynomial |
| Unit | Celsius degree |
| TM or TC or both flag | Both flag |

| Field | Value |
| --- | --- |
| a0 | 2006.6819 |
| a1 | 7.6518368 |
| a2 | -0.0038691002 |
| a3 | 2.5054358e-005 |
| a4 | 1.4419967e-007 |

## Displays

### Alphanumeric display data

Not identified

### Graphic display data

Not identified

### Scrolling Display

Not identified

### Variable SCOS packet display data

Not identified

## Constants

### Constants

Not identified

# Updating Generic Box contents Process

The contents of a generic box has been defined taking into accound the present knowledge of spacecraf development.

It is foreseen to keep the contents of generic box in line with the HPSDB users needs. For this purpose, HPSDB users are invited to submit to HPSDB manager approval updates of generic box contents with general purpose scope.

# Annex 1

Annex Table 1 - Resistance Temperature Relationship Table for Thermistor type GB42

(See RD2 and RD3)

# Annex 2

Annex Table 2 - Resistance Temperature Relationship Table for Platinum Probe 2k 118MF

(see RD4)

END OF THE DOCUMENT

# Text boxes

HERSCHEL / PLANCK