Scope

Outline description of the sequence and procedures to be used during the SPIRE CQM Short Performance Test (SPT) once integrated into the Herschel EQM Payload Module at EADS Astrium in Ottobrun.  The pre-requisites for the test are briefly described followed by a table setting out the steps in the test sequence; the names of the procedures to be executed from SCOS and the references to any manual procedures required; and the estimated duration of each part of the test.

Change notes

0.1	7 January 2005	Draft for checking – procedure names to be added/checked

Applicable Documents

AD1	SPIRE Functional Test Specification - SPIRE-RAL-DOC-001652

AD2	 SPIRE COOLER RECYCLING SCOS PROCEDURE - SPIRE-RAL-PRC-002267

Reference Documents

Prerequisites for carry out the Short Performance Test

FPU is integrated onto HOB

WE integrated with CCE

WE integrated with harness and FPU

Warm functional test done

Cold functional test done at “4K” and “1.7K” as per AD1

FP is at nominal temperature and left in REDY mode – see transition diagram in AD1

Prerequisites for data analysis

SCOS is running and display screens are available with conversion curves loaded

QLA sequences ready for display of data and FITS output

IDL present on local machine (laptop if necessary) with access to FITS filestore via FTP or other method

Outline Test sequence:

| Step | Description | Procedure Name | Estimated Duration |
| --- | --- | --- | --- |
| 1 | Check the noise in the PLW JFETs with shorted inputs versus Vss (detectors at ~2K) | FUNC-DCU-07P (AD1) | 30 minutes |
| 2 | Noise versus bias using spectrometer side of instrument and STM JFETS | FUNC-DCU-10S (AD1) | 30 minutes |
| 3 | Analyse data – verify no excess system noise | BMS IDL code |  |
| Thermal case 1 |
| 4 | Recycle cooler | COOLER RECYCLE (AD2) | 2 hours |
| 5 | Switch to Photometer Standby | Procedure name? Requires manual procedure to set equivalent power in BSM coils | 10 minutes |
| 6 | Wait until temperature stabilises | N/A | TBD |
| 6a | During stabilisation we can check noise versus bias level and frequency with reduced number of bias levels and frequencies or it will take all day | DNA-P Procedure name? | 4 hours max |
| 7 | Analyse data – determine noise is o.k. and optimum frequency setting – analysis procedure exists | BMS/TLL IDL code |  |
| Evaporator temperature must have stabilised before next test |
| 8 | Set for clean bias frequency and nominal bias (~15 mV) | By Manual Command | 10 minutes |
| 9 | Phase up to maximise signal | FUNC-DCU-08P_full FUNC-DCU-08P_short (AD1) | 30 minutes (TBC) |
| 10 | Loadcurve at fixed frequency and phase | Mode_ILT_PERF_DAL_P_SinglePhase | 15 minutes (TBC) |
| 11 | Loadcurve at fixed frequency and phase+90 | Mode_ILT_PERF_DAL_P_SinglePhase | 15 minutes (TBC) |
| 12 | Loadcurve at fixed frequency and phase-90 | Mode_ILT_PERF_DAL_P_SinglePhase | 15 minutes (TBC) |
| 13 | Analyse data – determine detector temperature and estimate background loading | BMS IDL code |  |
| 14 | Set detector for optimum bias setting | By Manual Command | 10 minutes |
| 15 | Rephase detector at optimum bias setting | FUNC-DCU-08P_short (AD1) | 10 minutes |
| 16 | Run PCAL static test to check calibration against CBB | Mode_ILT_PERF_CPS_P | 15 minutes (TBC) |
| 17 | - Analyse data – determine absolute signal versus voltage calibration – | Analysis code required |  |
|  | Can now use SPIRE to determine ambient background for (almost) any setting of the cryo-cover | Analysis code required |  |
| Now run other thermal cases |
| 18 | Photometer scan mode | No procedure required |  |
| 19 | Photometer chop mode | Requires procedure to manually apply power to BSM using external (GSE) supply |  |
| 20 | Switch photometer to spectrometer | Procedure required |  |
| 21 | Spectrometer mode | Requires procedure to manually power to SMEC using external (GSE) supply |  |
| Wait for cooler exhaustion approx 30-32 hours after recycle |
| SPIRE/PACS parallel mode test |
| 22 | Second Cooler recycle in conjunction with PACS | COOLER RECYCLE (AD2) See also SPIRE-RAL-NOT-002283 | Start 25 minutes after PACS recycle Then 2 hours |
| 23 | Switch to SPIRE Photometer Standby | Procedure name? Requires manual procedure to set equivalent power in BSM coils | 10 minutes (TBC) |
| 24 | Switch to SPIRE Parallel (scan) | Procedure to request full photometer data at 10 Hz | 1 minute |
| Wait until temperatures have stabilised |
| 25 | Switch to SPIRE Parallel (chop) | Procedure will not be quite flight like – keep 10 Hz continuous sample and manually apply power to BSM coils via external (GSE) supply | 10 minutes |
| Other PACS modes? Wait for cooler exhaustion |
| Then EMC tests – see separate procedure |