# Introduction

This document specifies the necessary steps to execute a set of WARM or COLD SPIRE functional tests. It also assesses on the checks to do to verify the success or failure of these tests.

## Scope

To judge the success or failure of a (warm/cold) functional test by checking that:

- Commands generated by the correspondent CUS script or saved manual stack and sent via SCOS2000 are correctly received and executed by the OBS.

- No error or exception reports were generated during the execution of the commands.

- The appropriate telemetry was generated and the correspondent parameters changed in an expected manner.

- The success criteria specified for each functional test in RD01 is met.

## Reference Documents

RD01   SPIRE Functional Tests Specification (SPIRE-RAL-DOC-001652), Issue 1.3, 14th Dec 2004

RD02   	SPIRE Data ICD (SPIRE-RAL-PRJ-001078), Issue 1.1, 25th May2004

RD03    SPIRE EGSE-ILT Startup Procedures (SPIRE-RAL-DOC-001630), Issue 0.7, 24th June 2003

RD04  	SPIRE DRCU Swith ON Procedure (SPIRE-RAL-PRC-002222), Issue 0.1, 10th June 2004

RD05    DRCU/DPU Interface Control Document (Sap-SPIRE-CCa-076-02 Issue 1.0 14th Feb 2003

RD06    SPIRE DRCU Integration Test specification Issue1 (SPIRE-RAL-DOC-001799 5th Sep 2003

RD07     EGSE TestControl User Guide Draft 5 (PICC-ME-MN-002 16th December 2003)

# Test log

The following table must be filled in when the test is performed

| Date: |  |
| --- | --- |
| Time: |  |
| Test conductor: |  |
| Machine: |  |

# FUNCTIONAL TEST CONFIGURATION

## SPIRE EGSE Setup

The following tasks must be running on SCOS2000.Check if they are already running just by going to the main window and checking that the correspondent buttons are surrounded by a green perimeter. If they are not, follow these steps in order to start them:

| Step # | Action | Comments |
| --- | --- | --- |
| 1 | In SCOS main window: select EXIF task and hit start (then hit continue). A new window appears .In this window select tasks EXIF_TMM, EXIF_CHM, EXIF_TM1, EXIF_CH1 and TOPE1 then hit start and continue after. | After a few seconds the TOPE environment appears. |
| 2 | In SCOS main window: select MSTK1 task and hit start (then hit continue). The manual stack window appears. |  |
| 3 | In a console in Truro (as sg55) type : “tmingestion ¦ tee <dbname>_tmingestion.log “ |  |
| 4 | Open a console in Lincoln (as sop23e) type: “ssh sg55@lincoln” + hit return enter sg55 password In this console type: “setenv DISPLAY 130.246.32.24:0” + hit return Open a console in Lincoln (as sops23e) type : “xauth list” +hit return Select with the mouse the first line of the result In the first console (the one where you logged on as sg55@lincoln) type: “xauth add ” + hit middle button on mouse (this will paste the line) +hit return In the first console type : “tescontrol-server” +hit return |  |
| 5 | In a console in Truro (as sg55) type: “PacketDisplay” + hit return |  |
|  | It is assumed that the EGSE router, gateway, CDMS simulator and SCOS are already started, refer to RD03 for this. |  |

## SPIRE EGSE Setup Checks

Before any functional test is to be executed ,check that the following applications are running in the correspondent machines. Fill the blanks as appropriate when the test is performed:

| SPIRE EGSE | Version | Status | EGSE Machine | Check | Comments |
| --- | --- | --- | --- | --- | --- |
| EGSE router | 515 | Running | Truro |  |  |
| EGSE Gateway | 515 | Running | Truro |  |  |
| CDMS Simulator | 2.5 | Running | Gordon |  |  |
| SCOS2000 | 2.3 patch level 5 | Running | Lincoln |  |  |
| EXIF + TOPE environment | N/A | Running | Lincoln |  |  |
| Packet Display | 515 | Running | Truro |  |  |
| TM Ingestion | 515 | Running | Truro |  |  |
| Test Control Server | 0.4 | Running | Lincoln |  |  |
| Manual Stack | N/A | Running | Lincoln |  |  |

Comments :

# Test procedure

The general steps to follow for a given functional tests are:

| Step # | Action | Comments |
| --- | --- | --- |
| 1 | Check the correct setup for the correspondent functional tests. In document RD01 check for the required initial configuration. |  |
| 2 | Execute the correspondent QLA script on QLA (IF APPLICABLE) |  |
| 4 | Execute a predefined TestControl script FROM THE HCSS PROCEDURES window in TOPE. Alternatively if a manual stack is needed for the test: Start MSTK1 task in SCOS. In the manual stack window change the display mode from the default BRIEF to FULL. In the top left hand corner : File ---> Load Stack |  |
| 4 | Fill in correspondent test report in Annexe1 |  |

.

## Test control scripts and manual stacks.

For the SCU, DCU and MCU functional tests, scripts have been written to invoke the correspondent CUS script from TOPE. This CUS scripts will generate the appropriate commands for the particular test.

For the mechanisms (BSM and SMECm) functional tests, manual stacks have been written which allow a bigger control over the entire command sequence.

Important Note: this is just a list of available scripts and manual stacks. It does NOT reflect the order in which the functional tests must be executed.

FUNC-DCU-01  : procedure FUNC-DCU-01

FUNC-DCU-02  : procedure FUNC-DCU-02

FUNC-DCU-03  : procedure FUNC-DCU-03

FUNC-DCU-04P: procedure FUNC-DCU-04-PHOT

FUNC-DCU-04S: procedure FUNC-DCU-04-SPEC

FUNC-DCU-05P: procedure FUNC-DCU-05-PHOT

FUNC-DCU-05S: procedure FUNC-DCU-05-SPEC

FUNC-DCU-06P: procedure FUNC-DCU-06-PHOT

FUNC-DCU-06S: procedure FUNC-DCU-06-SPEC

FUNC-DCU-07P: procedure FUNC-DCU-07-PHOT

FUNC-DCU-07S: procedure FUNC-DCU-07-SPEC

FUNC-DCU-08P: procedure FUNC-DCU-08-PHOT

FUNC-DCU-08S: procedure FUNC-DCU-08-SPEC

FUNC-DCU-09P: procedure FUNC-DCU-09-PHOT

FUNC-DCU-09S: procedure FUNC-DCU-09-SPEC

FUNC-DCU-10P: procedure FUNC-DCU-10-PHOT

FUNC-DCU-10S: procedure FUNC-DCU-10-SPEC

FUNC-DCU-11P: procedure FUNC-DCU-11-PHOT

FUNC-DCU-11S: procedure FUNC-DCU-11-SPEC

FUNC-DCU-12P: procedure FUNC-DCU-12-PHOT

FUNC-DCU-12S: procedure FUNC-DCU-12-SPEC

FUNC-SCU-01  : procedure FUNC-SCU-01

FUNC-SCU-02  : procedure FUNC-SCU-02

FUNC-SCU-03  : procedure FUNC-SCU-03

FUNC-SCU-04  : procedure FUNC-SCU-04

FUNC-SCU-05  : procedure FUNC-SCU-05

FUNC-SCU-06  : procedure FUNC-SCU-06

FUNC-SCU-07  : procedure FUNC-SCU-07

FUNC-SCU-08  : procedure FUNC-SCU-08

FUNC-MCU-01 : MANUAL STACK MCU_Power_ON_and_Boot.lincoln

FUNC-MCU-02 : procedure FUNC-MCU-02

FUNC-MCU-03 : procedure FUNC-MCU-03

FUNC-MCU-04 : procedure FUNC-MCU-04

FUNC-PCAL-01: procedure FUNC-PCAL-01

FUNC-SCAL-01: procedure FUNC-SCAL-01

FUNC-SCAL-02: procedure FUNC-SCAL-02

FUNC-SMEC-01: MANUAL STACK SMEC-WARM-SWITCH-ON.lincoln or SMEC-COLD-SWITCH-ON.lincoln

FUNC-SMEC-02: MANUAL STACK PFM-FUNC-SMEC-02.lincoln

FUNC-SMEC-03: MANUAL STACK PFM-FUNC-SMEC-03.lincoln

FUNC-SMEC-04: MANUAL STACK PFM-FUNC-SMEC-04.lincoln

FUNC-SMEC-05: MANUAL STACK PFM-FUNC-SMEC-05.lincoln

FUNC-SMEC-06:  MANUAL STACK PFM-FUNC-SMEC-06.lincoln

FUNC-SMEC-07:  MANUAL STACK PFM-FUNC-SMEC-07.lincoln

FUNC-SMEC-08:  MANUAL STACK PFM-FUNC-SMEC-08.lincoln

FUNC-SMEC-09:  MANUAL STACK PFM-FUNC-SMEC-09.lincoln

FUNC-BSM-01c:  MANUAL STACK PFM-FUNC-BSM-01c.lincoln

FUNC-BSM-01j:  MANUAL STACK PFM-FUNC-BSM-01j.lincoln

FUNC-BSM-02c MANUAL STACK PFM-FUNC-BSM-02c.lincoln

FUNC-BSM-02j:  MANUAL STACK PFM-FUNC-BSM-02j.lincoln

FUNC-BSM-03c MANUAL STACK PFM-FUNC-BSM-03c.lincoln

FUNC-BSM-03j:  MANUAL STACK PFM-FUNC-BSM-03j.lincoln

FUNC-BSM-04c:  MANUAL STACK PFM-FUNC-BSM-04c.lincoln

FUNC-BSM-04j:  MANUAL STACK PFM-FUNC-BSM-04j.lincoln

FUNC-BSM-05c:  MANUAL STACK PFM-FUNC-BSM-05c.lincoln

FUNC-BSM-05j:  MANUAL STACK PFM-FUNC-BSM-05j.lincoln

FUNC-BSM-06 :  MANUAL STACK PFM-FUNC-BSM-06.lincoln

# WARM/COLD FUNCTIONAL TESTS DETAILED PROCEDURE

This is a detailed explanation of the steps to follow for each warm/cold functional test.

The test flow must be as follows:

If both DPU and DRCU are OFF:

From TOPE HCSS Test Procedures

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Run PROC-OPER-SPIRE-DPU-ON |  |  |
| 2 | Run PROC-OPER-SPIRE-DRCU-ON |  |  |

If DPU is ON and DRCU is OFF:

From TOPE HCSS Test Procedures

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Run PROC-OPER-SPIRE-DRCU-ON |  |  |

## SCU FUNCTIONAL TESTS

Open the SCU PARAMETERS Alpha Numeric Display on SCOS

FUNC-SCU-01

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Write down in Annexe1 the current value of SCUFRAMECNT located in SCU PARAMETERS AND |  |  |
| 2 | On Lincoln run FUNC-SCU-01 test procedure from the HCSS Test Procedure window on TOPE |  |  |
| 3 | Write down in Annexe1 the current value of SCUFRAMECNT located in SCU PARAMETERS AND. |  |  |
| 4 | Test passed if 2 telemetry packets (type,subtype) (21,1) ,APID 0x0A20, FRAMEID 20, were received in PacketDisplay and SCUFRAMECNT HK parameter incremented from 0 to 31 decimal. |  |  |

FUNC-SCU-03

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Write down in Annexe1 the current value of SCUTEMPSTAT and the values of the 16 FPU temperatures located in SCU PARAMETERS AND |  |  |
| 2 | On Lincoln run FUNC-SCU-03 test procedure from the HCSS Test Procedure window on TOPE |  |  |
| 3 | When the test is finished write down in Annexe1 the current value of SCUTEMPSTAT and the values of the 16 FPU temperatures located in SCU PARAMETERS AND |  |  |
| 4 | Test passed if SCUTEMPSTAT parameter goes from 0 to 0xffff.(IF WARM) If COLD, the SCU active temperature channels should show the same values as the TFCS display. |  |  |

FUNC-SCU-06

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Write down in Annexe1 the current value of SUBKSTAT and SUBKTEMP located in SCU PARAMETERS AND |  |  |
| 2 | On Lincoln run FUNC-SCU-06 test procedure from the HCSS Test Procedure window on TOPE |  |  |
| 3 | When the test is finished write down in Annexe1 the current value of SUBKSTAT located in SCU PARAMETERS AND |  |  |
| 4 | Test passed if SUBKSTAT parameter went from 0 to 1. |  |  |

FUNC-SCU-02

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Write down in Annexe1 the current value of SCUFRAMECNT located in SCU PARAMETERS AND |  |  |
| 2 | On Salisbury run correspondent QLA script |  |  |
| 3 | On Lincoln run FUNC-SCU-02 test procedure from the HCSS Test Procedure window on TOPE |  |  |
| 4 | When the test is finished write down in Annexe1 the current value of SCUFRAMECNT located in SCU PARAMETERS AND |  |  |
| 4 | Test passed if QLA script triggered correctly and SCU HK parameters and nominal science parameters are similar. Check that SCUFRAMECNT went from 31 to 62 decimal. |  |  |

FUNC-SCU-07

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Write down in Annexe1 the current values of SPHSV,EVHSV,SPHTRV located in SCU PARAMETERS AND |  |  |
| 2 | On Lincoln run FUNC-SCU-07 test procedure from the HCSS Test Procedure window on TOPE |  |  |
| 3 | While the test is running write down in Annexe1 the values of current values of SPHSV,EVHSV,SPHTRV located in SCU PARAMETERS AND (RAW and CONVERTED) If COLD also write down the values of EVAPHSTEMP, PUMPHSTEMP and PUMPHRTEMP after each bias setting is finished. |  |  |
| 4 | Test passed if SPHSV, EVHSV, PHTRV showed expected values of ~12715, ~12715, ~14390 RAW respectively. |  |  |

FUNC-SCU-08

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Write down in Annexe1 the current values of SCUFRAMECNT located in SCU PARAMETERS AND |  |  |
| 2 | On Lincoln run FUNC-SCU-08 test procedure from the HCSS Test Procedure window on TOPE |  |  |
| 3 | When the test is finished write down the current value of SCUFRAMCNT and check 2 telemetry packets (type,subtype) (21,1) ,APID 0x1121, FRAMEID 21 were received in PacketDisplay. |  |  |
| 4 | Test passed if test pattern generated by SCU is the same as test pattern from a previous run of this functional test. Check that SCUFRAMECNT goes from 62 to 93 decimal. |  |  |

FUNC-SCU-04

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Write down in Annexe1 the current value of PCALV and PCALCURR located in SCU PARAMETERS AND |  |  |
| 2 | On Lincoln run FUNC-SCU-04 test procedure from the HCSS Test Procedure window on TOPE |  |  |
| 3 | While the test is running write down in Annexe1 the values of PCALV and PCALCURR located in SCU PARAMETERS AND |  |  |
| 4 | Test passed if PCALCURR shows input bias (0.1 mA) |  |  |

FUNC-SCU-05

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Write down in Annexe1 the current value of SCAL2V ,SCAL2CURR,SCAL4V,SCAL4CURR located in SCU PARAMETERS AND If COLD also write down the current values of SCAL2TEMP , SCAL4TEMP |  |  |
| 2 | On Lincoln run FUNC-SCU-05 test procedure from the HCSS Test Procedure window on TOPE |  |  |
| 3 | While the test is running write down in Annexe1 the values of SCAL2V ,SCAL2CURR,SCAL4V,SCAL4CURR located in SCU PARAMETERS AND If COLD also write down the current values of SCAL2TEMP , SCAL4TEMP after each bias setting is finished. |  |  |
| 4 | Test passed if SCAL2CURR and SCAL4CURR show input values 0.1 mA for both. |  |  |

## MCU FUNCTIONAL TESTS

Open MCU PARAMETERS display on SCOS

FUNC-MCU-01

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Load into the MANUAL STACK saved stack MCU_Power_ON_And_Boot.lincoln. File --- > Load Stack --( MCU_Power_ON_and_Boot.lincoln |  |  |
| 2 | After the first command is sent to power ON MCU, the over current limiter might trigger .In this case press the over current limiter reset button RED on the DRCU power bench. Write down the changes in the MCU HK parameters display after each command. |  |  |
| 3 | When procedure is finished write down the values of the MCU voltages. |  |  |
| 4 | Test passed if MCU boots and MCU voltages show expected values. Note: Check what is happening to SMECENCPWR. |  |  |

FUNC-MCU-02

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Write down in Annexe1 the current value of MCUFRAMECNT located in MCU PARAMETERS AND |  |  |
| 2 | On Lincoln run FUNC-MCU-02 test procedure from the HCSS Test Procedure window on TOPE |  |  |
| 3 | When test is finished write down the current value of MCUFRAMECNT. On packet display check that each type of science packets requested (MCU engineering, BSM and SMEC) were received and that they have the correct APID, FRAMEID and block length specified by the SPIRE DATA ICD Issue 2.0.15th Nov 2004 Pages 101 to 115. |  |  |
| 4 | Test passed if MCU produces all types of frames requested and no events were generated. Check that the frames have the correct APID, FRAMEID. |  |  |

FUNC-MCU-03

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Write down in Annexe1 the current value of MCUFRAMECNT located in MCU PARAMETERS AND |  |  |
| 2 | On Salisbury run correspondent QLA script. |  |  |
| 3 | On Lincoln run FUNC-MCU-03 test procedure from the HCSS Test Procedure window on TOPE |  |  |
| 4 | When test is finished write down the current value of MCUFRAMECNT |  |  |
| 5 | Test passed if QLA script works correctly. |  |  |

FUNC-MCU-04

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Write down in Annexe1 the current value of MCUFRAMECNT located in MCU PARAMETERS AND |  |  |
| 2 | On Salisbury run correspondent QLA script. |  |  |
| 3 | On Lincoln run FUNC-MCU-04 test procedure from the HCSS Test Procedure window on TOPE |  |  |
| 4 | When test is finished write down the current value of MCUFRAMECNT |  |  |
| 5 | Test passed if MCU Test pattern produced is the same as the previous time this test was run. |  |  |

Open CHOP PARAMETERS display in SCOS

FUNC-BSM-01c

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | On Lincoln load saved stack PFM-FUNC-BSM01c.lincoln on MANUAL STACK |  |  |
| 2 | Execute the stack writing down the effect of each command sent to the BSM on the BSM HK parameters |  |  |
| 3 | Check for the successfuls criteria specified in Functional Test Specification doc. |  |  |

FUNC-BSM-01j

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | On Lincoln load saved stack PFM-FUNC-BSM01j.lincoln on MANUAL STACK |  |  |
| 2 | Execute the stack writing down the effect of each command sent to the BSM on the BSM HK parameters |  |  |
| 3 | Check for the successful criteria specified in Functional Test Specification doc. |  |  |

From TOPE HCSS Test Procedures

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Run PROC-OPER-SPIRE-BSM-OFF |  |  |

Open SMEC PARAMETERS display on SCOS

FUNC-SMEC-01

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Check the current value of SMECENCPWR |  |  |
| 2 | Load into the MANUAL STACK saved stack SMEC-WARM-SWITCH-ON.lincoln File --- > Load Stack --( SMEC-WARM-SWITCH-ON.lincoln |  |  |
| 3 | After each command is sent from the stack write down any change in the SMEC HK parameters display. |  |  |
| 4 | Write down in Annexe1 all the current values of the SMEC HK page. |  |  |
| 5 | Check for the successful criteria specified in Functional Test Specification doc. |  |  |

FUNC-SMEC-03

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Load into the MANUAL STACK saved stack PFM-FUNC-SMEC-03.lincoln File --- > Load Stack --( PFM-FUNC-SMEC-03.lincoln |  |  |
| 2 | For each LED power level sent from manual stack ,check the SMECENCPWR parameter |  |  |
| 3 | Fill in Annexe1 |  |  |
| 4 | Check for the successful criteria specified in Functional Test Specification doc. |  |  |

FUNC-SMEC-04

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Write down in Annexe1 all the current values of the SMEC HK page |  |  |
| 2 | Load into the MANUAL STACK saved stack PFM-FUNC-SMEC-04.lincoln File --- > Load Stack --( PFM-FUNC-SMEC-04.lincoln |  |  |
| 3 | When test is finished write down in Annexe1 all the current values of the SMEC HK page |  |  |
| 4 | Check for the successful criteria specified in Functional Test Specification doc. |  |  |

From TOPE HCSS Test Procedures

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Run PROC-OPER-SPIRE-MCU-OFF |  |  |

## DCU FUNCTIONAL TESTS

Open DCU PARAMETERS Alpha Numeric Display

FUNC-DCU-01

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Write down in Annexe1 the current value of DCUFRAMECNT located d in DCU PARAMETERS AND |  |  |
| 2 | On Lincoln run FUNC-DCU-01 test procedure from the HCSS Test Procedure window on TOPE |  |  |
| 3 | Write down in Annexe1 the current value of DCUFRAMECNT located d in DCU PARAMETERS AND |  |  |
| 4 | Test passed if DCUFRAMECNT goes from 0 to 700 and all the frames received have the correct APID, FRAMEID and block length specified by the SPIRE DATA ICD Issue 2.0.15th Nov 2004 Pages 101 to 115. |  |  |

FUNC-DCU-02

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Write down in Annexe1 the current value of DCUFRAMECNT located d in DCU PARAMETERS AND |  |  |
| 2 | On Salisbury run QLA script |  |  |
| 3 | On Lincoln run FUNC-DCU-02 test procedure from the HCSS Test Procedure window on TOPE |  |  |
| 4 | Write down in Annexe1 the current value of DCUFRAMECNT located d in DCU PARAMETERS AND |  |  |
| 5 | Wait for QLA analysis to determine if test is passed or not. Check success criteria in Functional Test Specification doc. |  |  |

FUNC-DCU-03

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Write down in Annexe1 the current value of DCUFRAMECNT located d in DCU PARAMETERS AND |  |  |
| 2 | On Salisbury run QLA script |  |  |
| 3 | On Lincoln run FUNC-DCU-03 test procedure from the HCSS Test Procedure window on TOPE |  |  |
| 4 | Write down in Annexe1 the current value of DCUFRAMECNT located d in DCU PARAMETERS AND |  |  |
| 5 | Test passed if QLA analysis shows that test pattern produced with this test is the same as the one produced last time this test was run. |  |  |

FUNC-DCU-04-S

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | Write down in Annexe1 the current values of LIAS_P5,LIAS_P9,LIAS_N9 located d in DCU PARAMETERS AND |  |  |
| 2 | On Lincoln run FUNC-DCU-04-S test procedure from the HCSS Test Procedure window on TOPE |  |  |
| 3 | Write down in Annexe1 the current value of the current values of LIAS_P5,LIAS_P9,LIAS_N9 located d in DCU PARAMETERS AND |  |  |
| 4 | Test passed if SCUDCDCSTAT goes from 0 to 1. |  |  |

# Annexe1

FUNC-SCU-01

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SCU-01 | Refer to RD01 | SCUFRAMECNT | 0/31 |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SCU-03

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SCU-03 | Refer to RD01 | SCUTEMPSTAT | 0/0xFFFF |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SCU-06

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SCU-06 | Refer to RD01 | SUBKSTAT | 0/1 |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SCU-02

| Test Name | Test Description | Key Parameter(s) | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SCU-02 | Refer to RD01 | SCUFRAMECNT | 31/62 |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SCU-07

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SCU-07 | Refer to RD01 | SPHSV EVHSV SPHTRV | 0/ 0/ 0/ |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SCU-08

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SCU-08 | Refer to RD01 | SCUFRAMECNT | 92/133 |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SCU-04

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SCU-04 | Refer to RD01 | PCALV PCALCURR | 0/ 0/0.1mA |  | N/A |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SCU-05

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SCU-05 | Refer to RD01 | SCAL2V SCAL2CURR SCAL4V SCAL4CURR | 0/ 0/0.1 mA 0/ 0/0.1mA |  | N/A |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-MCU-01

| Test Name | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| FUNC-MCU-01 | MCUBOOTSTAT MCUERR MCU5V MCU14V | 0/0 |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-MCU-02

| Test Name | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| FUNC-MCU-02 | MCUFRAMECNT | 0/0 |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-MCU-03

| Test Name | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| FUNC-MCU-03 | MCUFRAMECNT |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-MCU-04

| Test Name | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| FUNC-MCU-04 | MCUFRAMECNT |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

PFM-FUNC-BSM-01c

| Test Name | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| PFM-FUNC-BSM-01c | CHOPENCPWR CHOPPOSN CHOPLOOPMODE CHOPFFGAIN CHOPDACVAL CHOPMOTORCURR | 0/1 |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

PFM-FUNC-BSM-01j

| Test Name | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| PFM-FUNC-BSM-01j | JIGGENCPWR JIGGPOSN JIGGLOOPMODE JIGGFFGAIN JIGGDACVAL JIGGMOTORCURR | 0/1 |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

PFM-FUNC-SMEC-01

| Test Name | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| PFM-FUNC-SMEC-01 | SMECENCPWR | 0/1 |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

PFM-FUNC-SMEC-03

| Test Name | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| PFM-FUNC-SMEC-03 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

PFM-FUNC-SMEC-04

| Test Name | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| PFM-FUNC-SMEC-04 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-01

| Test Name | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-01 | DCUFRAMECNT | 0/700 |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-02

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-02 | Refer to RD01 | DCUFRAMECNT | 700/1400 |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-03

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-03 | Refer to RD01 | DCUFRAMECNT | 1400/2100 |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-04-PHOT

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-04P | Refer to RD01 | SCUDCDCSTAT | 0/1 |  | N/A |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-4-SPEC

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-04S | Refer to RD01 | SCUDCDSTAT | 0/2 |  | N/A |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-PCAL-01

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| FUNC-PCAL01 | Refer to RD01 | PCALV PCALCURR | 0:(1mA) 1:(2.5mA) 2:(4mA) 3:(5.5mA) 4:(7 mA) 5:(0ma) |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SCAL-01

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- |
| FUNC-SCAL-01 | Refer to RD01 | SCAL4V SCAL4CURR SCAL2V SCAL2CURR | 0:(1mA) 1:(2.5mA) 2:(4mA) 3:(5.5mA) 4:(7 mA) 5:(0ma) 0:(1mA) 1:(2.5mA) 2:(4mA) 3:(5.5mA) 4:(7 mA) 5:(0ma) |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SCAL-02

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SCAL-02 | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-05-PHOT

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-05P | Refer to RD01 | N/A |  |  | N/A |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-05-SPEC

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-05S | Refer to RD01 | N/A |  |  | N/A |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-06-PHOT

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-06P | Refer to RD01 | PHOTHTRV | Sequence : 0V,-1V,-2V,-3V,-4V,-5V,0V |  | N/A |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-06-SPEC

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-06S | Refer to RD01 | SPECTHTRV | Sequence : 0V,-1V,-2V,-3V,-4V,-5V,0V |  | N/A |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-07-PHOT

| Test Name | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-07P | PSWJFET1V,PSWJFET2V,PSWJFET3V,PSWJFET4V,PSWJFET5V,PSWJFET6V PMWJFET1V,PMWJFET2V,PMWJFET3V,PMWJEFT4V,PLWJFET1V,PLWJFET2V | Sequence : 0V,-1V,-2V,-3V,-4V,-5V,0V |  | N/A |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-07-SPEC

| Test Name | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-07S | SSWJFET1V,SSWJFET2V,SLWJFET1V | Sequence : 0V,-1V,-2V,-3V,-4V,-5V,0V |  | N/A |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-08-PHOT

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-08.P | Refer to RD01 | PSWPHASE PMWPHASE PLWPHASE | Sequence depending on input parameters to test |  | N/A |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-08-SPEC

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-08S | Refer to RD01 | SSWPHASE SLWPHASE | Sequence depending on input parameters to test. |  | N/A |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-09-PHOT

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-09P | Refer to RD01 | PHOTMCLKDIV PHOTBIASDIV | Sequence 0:(0x163) 1:(0x96) 2:(0x66) Sequence 0:( 0xc) 1:( 0xc) 2:( 0xc) |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-09-SPEC

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-09S | Refer to RD01 | SPECMCLKDIV SPECBIASDIV | Sequence 0:(0x163) 1:(0x96) 2:(0x66) Sequence 0:( 1) 1:( 1) 2:( 1) |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-10-PHOT

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-10P | Refer to RD01 | PSWBIAS PMWBIAS PLWBIAS | 0:(0x33) 1:(0x66) 2:(0x99) 3:(0xcc) 4:(0xff) 5:(0x0) 0:(0x33) 1:(0x66) 2:(0x99) 3:(0xcc) 4:(0xff) 5:(0x0) 0:(0x33) 1:(0x66) 2:(0x99) 3:(0xcc) 4:(0xff) 5:(0x0) |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-10-SPEC

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-10S | Refer to RD01 | SSWBIAS SLWBIAS | 0:(0x33) 1:(0x66) 2:(0x99) 3:(0xcc) 4:(0xff) 5:(0x0) 0:(0x33) 1:(0x66) 2:(0x99) 3:(0xcc) 4:(0xff) 5:(0x0) |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-11-PHOT

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-11P | Refer to RD01 |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-11-SPEC

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-11S | Refer to RD01 |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-12-PHOT

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-12P | Refer to RD01 |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-DCU-12-SPEC

| Test Name | Test Description | Key Parameter(s) | Expected value Before/After | Actual Value Before/After | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-12S | Refer to RD01 |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SCU-01

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SCU-01 | Refer to RD01 | SCUFRAMECNT | 0/31 |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SCU-02

| Test Name | Test Description | Key Parameter(s) | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SCU-02 | Refer to RD01 | SCUFRAMECNT | 31/62 |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SCU-03

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SCU-03 | Refer to RD01 | SCUFRAMECNT | 62/93 |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SCU-04

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SCU-04 | Refer to RD01 | PCALV PCALCURR | 0/ 0/2.25mA |  | N/A |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SCU-05

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SCU-05 | Refer to RD01 | SCAL2V SCAL2CURR SCAL4V SCAL4CURR | 0/ 0/2.5 mA 0/ 0/2.5mA |  | N/A |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SCU-06

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SCU-06 | Refer to RD01 | SUBKSTAT | 0/1 |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SCU-07

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SCU-07 | Refer to RD01 | SPHSV EVHSV SPHTRV | 0/ 0/ 0/ |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SCU-08

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SCU-08 | Refer to RD01 | SCUFRAMECNT | 92/133 |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-PCAL-01

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- |
| FUNC-PCAL01 | Refer to RD01 | PCALV PCALCURR | 0:(1mA) 1:(2.5mA) 2:(4mA) 3:(5.5mA) 4:(7 mA) 5:(0ma) |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SCAL-01

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- |
| FUNC-SCAL-01 | Refer to RD01 | SCAL4V SCAL4CURR SCAL2V SCAL2CURR | 0:(1mA) 1:(2.5mA) 2:(4mA) 3:(5.5mA) 4:(7 mA) 5:(0ma) 0:(1mA) 1:(2.5mA) 2:(4mA) 3:(5.5mA) 4:(7 mA) 5:(0ma) |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SCAL-02

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SCAL-02 | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-MCU-01

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-MCU-01 | Refer to RD01 |  |  |  | N/A |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-MCU-02

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-MCU-02 | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-MCU-03

| Test Name | Test Description | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-MCU-03 | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-MCU-04

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-MCU-04 | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SMEC-01

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-04P | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SMEC-02

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-02 | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SMEC-03

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-03 | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SMEC-04

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-04 | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SMEC-05

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-05 | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SMEC-06

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-06 | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SMEC-07

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-08 | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SMEC-08

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-08 | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-SMEC-09

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-09 | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-BSM-01c

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-04P | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-BSM-01j

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-04P | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-BSM-02c

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-04P | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-BSM-02j

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-04P | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-BSM-03c

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-04P | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-BSM-03j

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-04P | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-BSM-04c

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-04P | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-BSM-04j

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-04P | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-BSM-05c

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-04P | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-BSM-05j

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-04P | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

FUNC-BSM-06

| Test Name | Test Description | HK Key Parameter | Number of frames expected | Actual Value Before/After | Number of frames received | Comments | Test Result Success/Fail |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FUNC-DCU-04P | Refer to RD01 |  |  |  |  |  |  |
| Start time @: End time @: OBSID: Commets: |

# Annexe2

The CCS templates are provided separately as they are too long to be included in this document.

# Annexe3

Cus scripts for warm electronics integration tests

mode SPIRE_WEIT01 {

double photbiasfreq = 200.0; //Default Master Clock divisor for PhotBiasFreq 199.9 Hz

double photsampfreq = 15.34; //Default Sampling divisor for PhotSamplingFreq 15.38 Hz

double specbiasfreq = 160.0; //Default Master Clock divisor for SpecBiasFreq  Hz

double specsampfreq = 80.0; //Default Sampling divisor for SpecSamplingFreq 80 Hz

int frames = 0x0; //Number of frames to request

}{

IST_ClearObs();

delay(1);

IST_StartObs();

delay(1);

double phase = 0.0;

//Phase to 0 degrees

int ftime = 60;

//Time for the generation

string[] modes = ["PF_Data","SF_Data","PSW_Data","PMW_Data","PLW_Data","SSW_Data","SLW_Data"];

for(int i = 0 .. length(modes) - 1) {

DCU_PhotSpec_QLA_NEW(modes[i],photbiasfreq,photsampfreq,specbiasfreq,specsampfreq,frames,phase,ftime);

delay(1);

}

IST_EndObs();

}

mode SPIRE_WEIT02 {

double photbiasfreq = 200.0; //Default Master Clock divisor for PhotBiasFreq 199.9 Hz

double photsampfreq = 15.34; //Default Sampling divisor for PhotSamplingFreq 15.38 Hz

double specbiasfreq = 160.0; //Default Master Clock divisor for SpecBiasFreq  Hz

double specsampfreq = 80.0; //Default Sampling divisor for SpecSamplingFreq 80 Hz

int frames = 0x0; //Number of frames to request

}{

IST_ClearObs();

delay(1);

IST_StartObs();

delay(1);

double phase = 0.0;

//Phase to 0 degrees

int ftime = 60;

//Time for the generation

string[] modes = ["PFTest_Data","SFTest_Data","PSWTest_Data","PMWTest_Data","PLWTest_Data","SSWTest_Data","SLWTest_Data"];

for(int i = 0 .. length(modes) - 1) {

DCU_PhotSpec_QLA_NEW(modes[i],photbiasfreq,photsampfreq,specbiasfreq,specsampfreq,frames,phase,ftime);

delay(1);

}

IST_EndObs();

}

mode SPIRE_WEIT03 {

double photbiasfreq = 200.0; //Default Master Clock divisor for PhotBiasFreq 199.9 Hz

double photsampfreq = 15.34; //Default Sampling divisor for PhotSamplingFreq 15.38 Hz

double specbiasfreq = 160.0; //Default Master Clock divisor for SpecBiasFreq  Hz

double specsampfreq = 80.0; //Default Sampling divisor for SpecSamplingFreq 80 Hz

int ftime = 60; //Time for the generation

}{

IST_ClearObs();

delay(1);

IST_StartObs();

delay(1);

double phase = 0.0;

//Phase to 0 degrees

int frames = 0x0;

//Number of frames to request

string[] modes = ["PF_Data","SF_Data","PSW_Data","PMW_Data","PLW_Data","SSW_Data","SLW_Data"];

for(int i = 0 .. length(modes) - 1) {

DCU_PhotSpec_QLA_NEW(modes[i],photbiasfreq,photsampfreq,specbiasfreq,specsampfreq,frames,phase,ftime);

delay(1);

}

IST_EndObs();

}

mode SPIRE_WEIT04 {

int scuframes = 0x1f; //Number of scu frames

int framerate = 0; // f(hz)=80/(1+framerate)

}{

int ftime = 1;

//Data generation time If conitnuous

IST_ClearObs();

delay(1);

IST_StartObs();

delay(1);

SCU_Nom_Data(framerate,scuframes,ftime);

delay(1);

IST_EndObs();

}

mode SPIRE_WEIT05 {

int scuframes = 0x1f; //Number of scu frames

int framerate = 0; // f(hz)=80/(1+framerate)

}{

int ftime = 1;

//Data generation time If conitnuous

IST_ClearObs();

delay(1);

IST_StartObs();

delay(1);

SCUTest_Patt(framerate,scuframes,ftime);

delay(1);

IST_EndObs();

}

mode SPIRE_WEIT06 {

int framerate = 0; // f(hz)=80/(1+framerate)

int ftime = 1; //Data generation time If conitnuous

}{

int scuframes = 0;

//Number of scu frames

IST_ClearObs();

delay(1);

IST_StartObs();

delay(1);

SCU_Nom_Data(framerate,scuframes,ftime);

delay(1);

IST_EndObs();

}

mode SPIRE_WEIT07 {

int ftime = 36000; //Time for the generation in sec (10 hours)

}{

//Set Bias frequency

double photbiasfreq = 200.0;

//Default Master Clock divisor for PhotBiasFreq 200.0 Hz

//Convert into RAW Bias frequency

int raw_biasf = iround(1.0E7 / (512.0 * photbiasfreq));

//Set Sampling frequency

double photsampfreq = 25.0;

//Default Sampling divisor for PhotSamplingFreq 25.00 Hz

//Convert to RAW Sampling frequency

int raw_sampf = iround(photbiasfreq / photsampfreq - 1.0);

//Set RAW Bias amplitude

int biasamplitude = 0;

//Set RAW Phase to 0 degrees

int phase = 0;

//START TEST

IST_ClearObs();

delay(1);

IST_StartObs();

delay(1);

Setup_PF_Data(raw_biasf,raw_sampf,biasamplitude,phase);

delay(1);

PF_Data_QLA(ftime);

delay(1);

IST_EndObs();

}

mode SPIRE_WEIT08 {

int ftime = 1800; //Time for the generation in sec (1/2 hours)

}{

//Set Bias frequency

double photbiasfreq = 200.0;

//Default Master Clock divisor for PhotBiasFreq 200.0 Hz

//Convert into RAW Bias frequency

int raw_biasf = iround(1.0E7 / (512.0 * photbiasfreq));

//Set Sampling frequency

double photsampfreq = 25.0;

//Default Sampling divisor for PhotSamplingFreq 25.00 Hz

//Convert to RAW Sampling frequency

int raw_sampf = iround(photbiasfreq / photsampfreq - 1.0);

//Set RAW Bias amplitude

int biasamplitude = 0;

//Set RAW Phase to 0 degrees

int phase = 0;

//START TEST

IST_ClearObs();

delay(1);

IST_StartObs();

delay(1);

Setup_PF_Data(raw_biasf,raw_sampf,biasamplitude,phase);

delay(1);

PF_Data_QLA(ftime);

delay(1);

IST_EndObs();

}

mode SPIRE_WEIT09 {

int ftime = 1800; //Time for the generation in sec (1/2 hours)

}{

//Set Bias frequency

double specbiasfreq = 280.0;

//Default Master Clock divisor for SpecBiasFreq 280.0 Hz

//Convert into RAW Bias frequency

int raw_biasf = iround(1.0E7 / (512.0 * specbiasfreq));

//Set Sampling frequency

double specsampfreq = 140.0;

//Default Sampling divisor for SpecSamplingFreq 140.0 Hz

//Convert to RAW Sampling frequency

int raw_sampf = iround(specbiasfreq / specsampfreq - 1.0);

//Set RAW Bias amplitude

int biasamplitude = 0;

//Set RAW Phase to 0 degrees

int phase = 0;

//START TEST

IST_ClearObs();

delay(1);

IST_StartObs();

delay(1);

Setup_SF_Data(raw_biasf,raw_sampf,biasamplitude,phase);

delay(1);

SF_Data_QLA(ftime);

delay(1);

IST_EndObs();

}