# Introduction

This note describes the tests to be carried out with the PFM1 instrument in order to simulate the operation of the SPIRE instrument during normal observing modes and generate data in a form able to be processed through the available data processing steps.

The goals of these tests are to:

- verify that the instrument can perform representative example observations

- provide example data (both with and without a simulated source) for use in testing and developing data reduction methods

The following observation types are executed:

- Point Source, high resolution, spectroscopy using continuous scanning (SOF1)

- Field mapping, medium resolution, spectroscopy, using continuous scanning  (and raster) (SOF2)

- Point Source, low resolution, spectroscopy, using step and integrate scanning (SOF3)

- Point source photometry using chopping  (and nodding) (POF1)

- Point source photometry using Jiggle Mapping (ie. 7 point Jiggle-map) (POF2)

- Photometric mapping with a fully sampled jiggle map (using a raster) (POF3)

- Mapping using scanning without chopping (POF5)

In all cases satellite pointing modes will be simulated as appropriate. For some of these tests (e.g. scanning) arranging a true simulated source might be rather difficult. Additionally, since only the spectrometer array is in place at this time, photometric observations will use the spectrometer detector arrays rather than the photometer array with the SMEC  held at an appropriate position.

## Reference Documents

| RD01 | Operation of the SPIRE FTS (SPIRE-RAl-NOT-002213) |
| --- | --- |
| RD02 | Instrument User Manual |

# Test Setup

## Prerequisites

### Spectrometer mechanism positions

The start and end positions for FTS scans have to be determined from the measurement of the Zero Path Difference (ZPD) position before executing these tests.

Given the nominal position of the ZPD of 8000, the following positions are assumed for the FTS operations. Any change to ZPD should be reflected in an identical change to these values.

| Position | Value | Description |
| --- | --- | --- |
| ZPD | 8000 (nominal) | Zero path difference |
| HOME | 5000 (Nominal) | Home position |

The nominal scan speed will be set to 0.5mm per second

| Resolution | Scan range (mm) | Start Position | End Position | Scan Time (secs) |
| --- | --- | --- | --- | --- |
| High | -3.4 mm to +34mm | HRSTART (4600) | HREND (42000) | 74.8 |
| Medium | -3.4 mm to +3.4 mm | MRSTART (4600) | MREND (11400) | 13.6 |
| Low | -1.0 mm to +1.0 mm | LRSTART (7000) | LREND (9000) | 4.0 |

### Pixel positions

The value of the chop and jiggle positions corresponding to the pixels used for chopping need to be determined

| Pixel _ID | Chop Posn | Jiggle Posn | Description |
| --- | --- | --- | --- |
| On-source Position |
| SSW-D4 |  |  | SSW Central Pixel (on-source) |
| SLW-C3 |  |  | SLW Central Pixel (on-source) |
| On-source position |  |  | Actual on-source position to be used |
| Off-source Position |
| SLW-C4 |  |  | SLW off-source |
| SSW-B3 |  |  | SSW off-source |
| Off source Position |  |  | Actual off-source position to be used |
| Nod Position |
| SSW-F3 |  |  | SSW nod position |
| SLW-C2 |  |  | SLW nod position |
| Nod Position |  |  | Actual nod position to be used |

### Raster positions

Rasters will be implemented by moving the telescope simulator to a set of positions corresponding to the raster positions. The raster array will be a 3 x 3 array at the following positions

| Raster_ID | Pixel_ID | Chop Posn | Jiggle Posn | STEP |
| --- | --- | --- | --- | --- |
| (0,0) | SSW-F1 |  |  | 0x0000 |
| (0,1) | SSW-F1 |  |  | 0x0001 |
| (0,2) | SSW-F1 |  |  | 0x0002 |
| (1,2) | SSW-F1 |  |  | 0x0022 |
| (1,1) | SSW-F1 |  |  | 0x0021 |
| (1,0) | SSW-F1 |  |  | 0x0020 |
| (2,0) | SSW-F1 |  |  | 0x0040 |
| (2,1) | SSW-F1 |  |  | 0x0041 |
| (2,2) | SSW-F1 |  |  | 0x0042 |

## Configuration

In all cases the test will start, and end, with the instrument and test facility in the following configuration:

Instrument:  In the SPEC_STBY mode (see RD02)

- SMEC is initialised, all trajectory parameters are set to their required values, the scan speed is set to its nominal value and the SMEC is held at the ‘HOME’ position

- The spectrometer JFETS are powered on, the detector bias set and sampling frequency set

- The BSM is powered on, and held in the ‘HOME’ position.

- MODE = 0x0400

- STEP = 0x0000

- Nominal Housekeeping sampling at 0.25 Hz

Facility:

- Cryostat window open

- Hot BB powered on (Temp TBD)

- Telescope simulator set to place the Hot BB on the central Spectrometer Pixels (SSW-D4, SLW-C3)

- Facility chopper out of beam

# Spectrometer Tests

## Point Source Observation (SOF1)

This test will execute a set of 10 high resolution scans of the spectrometer.

### Summary

| Step | Building Block | Procedure | Description |
| --- | --- | --- | --- |
| 1 | A401-0000 | SCAN_CONF Set OBSID Set BBID to 0xA401 Set MODE to 0x1400 Set Nominal Hsk packets to 1 per second Execute FTS_MOVE(HRSTART) Switch on SCAL at required temperature Wait for SMEC to reach HRSTART position and SCAL to settle Set MODE to 0x0410 | Set up the spectrometer for continuous scanning Indicate Start of Observation BBID -> 0 Indicate mode changing Normal speed when SPIRE Prime Move SMEC to start position ready to scan Currently no thermal control of SCAL is envisaged Indicate now in SOF1 mode |
| 2 | A410-0000 | SCAN Set BBID to 0xA410 Execute FTS_SCAN(HRSTART, HREND, 4) | Execute 4 scans Perform 4 FTS scans SMEC ends up back at START |
| 3 | A410-0001 | SCAN Set BBID to 0xA410 Execute FTS_SCAN (HRSTART, HREND, 4) | Execute 4 scans Perform 4 FTS scans SMEC ends up back at START |
| 4 | A410-0002 | SCAN Set BBID to 0xA410 Execute FTS_SCAN (HRSTART, HREND, 2) | Execute 2 scans Perform 2 FTS scans SMEC ends up back at START |
| 5 | A402-0000 | SCAN_END Set BBID to 0xA402 Set MODE to 0x1410 Execute FTS_MOVE(HOME) Switch off SCAL Set Nominal Hsk packets to 0.25 per second Set MODE to 0x0400 Set OBSID=0x00000000 | Return Spectrometer to SPEC_STBY mode Indicate mode changing Move SMEC to ‘home’ position Normal speed when SPIRE in standby Indicate now in SPEC_STBY Indicate end of observation BBID->0 |

### Test Duration

Approximately 20 mins

## Field Mapping Spectroscopy (SOF2)

This test will execute a set of 4 medium resolution scans of the spectrometer at a set of 9 ‘positions on the sky’ (simulated by moving the telscope simulator)

### Summary

| Step | Building Block | Procedure | Description |
| --- | --- | --- | --- |
| 1 | A401-0000 | SCAN_CONF Set OBSID Set BBID to 0xA401 Set MODE to 0x1400 Set Nominal Hsk packets to 1 per second Execute FTS_MOVE(MRSTART) Switch on SCAL at required temperature Wait for SMEC to reach START position and SCAL to settle Set MODE to 0x0410 | Set up the spectrometer for continuous scanning Indicate Start of Observation BBID -> 0 Indicate mode changing Normal speed when SPIRE Prime Move SMEC to start position ready to scan Currently no thermal control of SCAL is envisaged Indicate now in SOF1 mode |
| 2 | A380-0000 | PCAL_FLASH Set BBID to 0xA380 Execute PCAL_Flash | Execute PCAL calibration flash |
| 3 | A702-nnnn | RASTER Set BBID to 0xA702 Move telescope simulator to raster position (see table 2.1.3) Set STEP to value in table 2.1.3 | Move to raster position |
| 4 | A420-nnnn | SCAN Set BBID to 0xA420 Execute Scan_FTS(MRSTART, MREND, 4) | Execute 4 scans Perform 4 FTS scans SMEC ends up back at START |
| 5 |  | Repeat steps 3 and 4 for all raster positions in table 2.1.3 |  |
| 6 | A380-0001 | PCAL_FLASH Set BBID to 0xA380 Execute PCAL_Flash | Execute PCAL calibration flash |
| 7 | A402-0000 | SCAN_END Set BBID to 0xA402 Set MODE to 0x1420 Execute FTS_MOVE(HOME) Switch off SCAL Set STEP to 0 Set Nominal Hsk packets to 0.25 per second Set MODE to 0x0400 Set OBSID=0x00000000 | Return Spectrometer to SPEC_STBY mode Indicate mode changing Move SMEC to ‘home’position Normal speed when SPIRE in standby Indicate now in SPEC_STBY Indicate end of observation BBID->0 |
| 8 |  | Move telescope simulator to central pixel position |  |

### Test Duration

Approximately 60 mins, assuming 5 mins to peak up on each new raster position.

## Point Source, low resolution, spectroscopy, using step and integrate scanning (SOF3)

This test will execute a medium resolution scan of the spectrometer.

### Summary

| Step | Building Block | Procedure | Description |
| --- | --- | --- | --- |
| 1 | A403-0000 | STEP_CONF Set OBSID Set BBID to 0xA403 Set MODE to 0x1400 Set Nominal Hsk packets to 1 per second Execute FTS_MOVE(HRSTART) Switch on SCAL at required temperature Wait for SMEC to reach HRSTART position and SCAL to settle Set MODE to 0x0430 | Set up the spectrometer for step-and-look scanning Indicate Start of Observation BBID -> 0 Indicate mode changing Normal speed when SPIRE Prime Move SMEC to start position ready to scan Currently no thermal control of SCAL is envisaged Indicate now in SOF1 mode |
| 2 | A380-0000 | PCAL_FLASH Set BBID to 0xA380 Execute PCAL_Flash | Execute PCAL calibration flash |
| 3 | A430-nnnn | CHOP Set BBID to 0xA430 Chop for 2 seconds | Chop between on and off source pixels. |
| 4 | A431-nnnn | MOVE Set BBID to 0xA431 Execute FTS_MOVE (posn) | Move to next scan position |
| 5 |  | Repeat steps 3 and 4 for positions MRSTART to MREND in steps of 10 (1600 steps) |  |
| 6 | A404-0000 | STEP_END Set BBID to 0xA404 Set MODE to 0x1430 Execute FTS_MOVE(HOME) Switch off SCAL Set Nominal Hsk packets to 0.25 per second Set MODE to 0x0400 Set OBSID=0x00000000 | Return Spectrometer to SPEC_STBY mode Indicate mode changing Move SMEC to ‘home’position Normal speed when SPIRE in standby Indicate now in SPEC_STBY Indicate end of observation BBID->0 |

### Test Duration

Approximately 90 mins

# Photometer Tests

## POF1: Point Source with Chop and no Nod

### Summary

| Step | Building Block | Procedure | Description |
| --- | --- | --- | --- |
| 1 | A301-0000 | CHOP_CONF Set OBSID Set BBID to 0xA301 Set MODE to 0x1400 Set Nominal Hsk packets to 1 per second Set MODE to 0x0310 | Set up instrument for photometer observations Indicate Start of Observation BBID -> 0 Indicate mode changing Normal speed when SPIRE Prime Indicate now in POF1 mode |
| 2 | A380-0000 | PCAL_FLASH Set BBID to 0xA380 Execute PCAL_Flash | Execute PCAL calibration flash |
| 3 | A310-0000 | CHOP Set BBID to 0xA310 Chop for 120 seconds | Chopping observation Chop between on and off source pixels. |
| 4 | A380-0001 | PCAL_FLASH Set BBID to 0xA380 Execute PCAL_Flash | Execute PCAL calibration flash |
| 5 | A302-0000 | CHOP_END Set BBID to 0xA302 Set MODE to 0x1310 Move BSM to HOLD position Set STEP to 0 Set Nominal Hsk packets to 0.25 per second Set MODE to 0x0400 Set OBSID=0x00000000 | Return Spectrometer to SPEC_STBY mode Indicate mode changing Normal speed when SPIRE in standby Indicate now in SPEC_STBY Indicate end of observation BBID->0 |

### Test Duration

Approximately 8 mins

## POF1: Point Source with Chop and Nodding

### Summary

| Step | Building Block | Procedure | Description |
| --- | --- | --- | --- |
| 1 | A301-0000 | CHOP_CONF Set OBSID Set BBID to 0xA301 Set MODE to 0x1400 Set Nominal Hsk packets to 1 per second Set MODE to 0x0310 | Set up instrument for photometer observations Indicate Start of Observation BBID -> 0 Indicate mode changing Normal speed when SPIRE Prime Indicate now in POF1 mode |
| 2 | A380-0000 | PCAL_FLASH Set BBID to 0xA380 Execute PCAL_Flash | Execute PCAL calibration flash |
| 3 | A310-0000 | CHOP Set BBID to 0xA310 Chop for 120 seconds | Chopping observation Chop between on and off source pixels. |
| 4 | A701-0000 | NOD Set BBID to 0xA701 Move telescope simulator to NOD position Set STEP = 0x0001 | Move to nod position |
| 5 | A310-0001 | CHOP Set BBID to 0xA310 Chop for 120 seconds | Chopping observation Chop between on and off source pixels. |
| 6 | A700-0000 | POINT Set BBID to 0xA700 Move telescope simulator to central pixel position Set STEP = 0x0000 | Move to central position |
| 7 | A310-0002 | CHOP Set BBID to 0xA310 Chop for 120 seconds | Chopping observation Chop between on and off source pixels. |
| 8 | A701-0001 | NOD Set BBID to 0xA701 Move telescope simulator to NOD position Set STEP = 0x0001 | Move to nod position |
| 9 | A310-0003 | CHOP Set BBID to 0xA310 Chop for 120 seconds | Chopping observation Chop between on and off source pixels. |
| 10 | A700-0001 | POINT Set BBID to 0xA700 Move telescope simulator to central pixel position Set STEP = 0x0000 | Move to central position |
| 11 | A380-0001 | PCAL_FLASH Set BBID to 0xA380 Execute PCAL_Flash | Execute PCAL calibration flash |
| 12 | A302-0000 | CHOP_END Set BBID to 0xA302 Set MODE to 0x1310 Move BSM to HOLD position Set STEP to 0 Set Nominal Hsk packets to 0.25 per second Set MODE to 0x0400 Set OBSID=0x00000000 | Return Spectrometer to SPEC_STBY mode Indicate mode changing Normal speed when SPIRE in standby Indicate now in SPEC_STBY Indicate end of observation BBID->0 |

### Test Duration

Approximately 35 mins

## POF2: Point Source with 7-point Jiggle with nodding

### Summary

| Step | Building Block | Procedure | Description |
| --- | --- | --- | --- |
| 1 | A303-0000 | J7_CONF Set OBSID Set BBID to 0xA303 Set MODE to 0x1400 Set Nominal Hsk packets to 1 per second Set MODE to 0x032#0 | Set up instrument for photometer observations Indicate Start of Observation BBID -> 0 Indicate mode changing Normal speed when SPIRE Prime Indicate now in POF1 mode |
| 2 | A380-0000 | PCAL_FLASH Set BBID to 0xA380 Execute PCAL_Flash | Execute PCAL calibration flash |
| 3 | A320-0000 | JIGGLE_7 Set BBID to 0xA320 Execute 7-point jiggle map | 7-point jiggle operation |
| 4 | A701-0000 | NOD Set BBID to 0xA701 Move telescope simulator to NOD position Set STEP = 0x0001 | Move to nod position |
| 5 | A320-0001 | JIGGLE_7 Set BBID to 0xA320 Execute 7-point jiggle map | 7-point jiggle operation |
| 6 | A700-0000 | POINT Set BBID to 0xA700 Move telescope simulator to central pixel position Set STEP = 0x0000 | Move to central position |
| 7 | A320-0002 | JIGGLE_7 Set BBID to 0xA320 Execute 7-point jiggle map | 7-point jiggle operation |
| 8 | A701-0001 | NOD Set BBID to 0xA701 Move telescope simulator to NOD position Set STEP = 0x0001 | Move to nod position |
| 7 | A320-0003 | JIGGLE_7 Set BBID to 0xA320 Execute 7-point jiggle map | 7-point jiggle operation |
| 10 | A700-0001 | POINT Set BBID to 0xA700 Move telescope simulator to central pixel position Set STEP = 0x0000 | Move to central position |
| 11 | A380-0001 | PCAL_FLASH Set BBID to 0xA380 Execute PCAL_Flash | Execute PCAL calibration flash |
| 12 | A304-0000 | J7_END Set BBID to 0xA304 Set MODE to 0x1320 Move BSM to HOLD position Set STEP to 0 Set Nominal Hsk packets to 0.25 per second Set MODE to 0x0400 Set OBSID=0x00000000 | Return Spectrometer to SPEC_STBY mode Indicate mode changing Normal speed when SPIRE in standby Indicate now in SPEC_STBY Indicate end of observation BBID->0 |

### Test Duration

Approximately 30 mins

## POF3: Point Source in Full Jiggle Map no Raster

### Summary

| Step | Building Block | Procedure | Description |
| --- | --- | --- | --- |
| 1 | A305-0000 | J64_CONF Set OBSID Set BBID to 0xA305 Set MODE to 0x1400 Set Nominal Hsk packets to 1 per second Set MODE to 0x0330 | Set up instrument for photometer observations Indicate Start of Observation BBID -> 0 Indicate mode changing Normal speed when SPIRE Prime Indicate now in POF1 mode |
| 2 | A380-0000 | PCAL_FLASH Set BBID to 0xA380 Execute PCAL_Flash | Execute PCAL calibration flash |
| 3 | A330-0000 | JIGGLE_64 Set BBID to 0xA330 Execute 64-point jiggle map | 64-point jiggle operation |
| 4 | A380-0001 | PCAL_FLASH Set BBID to 0xA380 Execute PCAL_Flash | Execute PCAL calibration flash |
| 5 | A306-0000 | J64_END Set BBID to 0xA306 Set MODE to 0x1330 Move BSM to HOLD position Set STEP to 0 Set Nominal Hsk packets to 0.25 per second Set MODE to 0x0400 Set OBSID=0x00000000 | Return Spectrometer to SPEC_STBY mode Indicate mode changing Normal speed when SPIRE in standby Indicate now in SPEC_STBY Indicate end of observation BBID->0 |

### Test Duration

Approximately 10 mins

## POF3: Point Source in Full Jiggle Map with Raster

### Summary

| Step | Building Block | Procedure | Description |
| --- | --- | --- | --- |
| 1 | A305-0000 | J64_CONF Set OBSID Set BBID to 0xA305 Set MODE to 0x1400 Set Nominal Hsk packets to 1 per second Set MODE to 0x0330 | Set up instrument for photometer observations Indicate Start of Observation BBID -> 0 Indicate mode changing Normal speed when SPIRE Prime Indicate now in POF1 mode |
| 2 | A380-0000 | PCAL_FLASH Set BBID to 0xA380 Execute PCAL_Flash | Execute PCAL calibration flash |
| 3 | A702-nnnn | RASTER Set BBID to 0xA702 Move telescope simulator to raster position (see table 2.1.3) Set STEP to value in table 2.1.3 | Move to raster position |
| 4 | A330-nnnn | JIGGLE_64 Set BBID to 0xA330 Execute 64-point jiggle map | 64-point jiggle operation |
| 5 |  | Repeat steps 3 and 4 for each raster position in table 2.1.3 |  |
| 6 | A380-0001 | PCAL_FLASH Set BBID to 0xA380 Execute PCAL_Flash | Execute PCAL calibration flash |
| 7 | A306-0000 | J64_END Set BBID to 0xA306 Set MODE to 0x1330 Move BSM to HOLD position Set STEP to 0 Set Nominal Hsk packets to 0.25 per second Set MODE to 0x0400 Set OBSID=0x00000000 | Return Spectrometer to SPEC_STBY mode Indicate mode changing Normal speed when SPIRE in standby Indicate now in SPEC_STBY Indicate end of observation BBID->0 |

### Test Duration

Approximately 65 mins

## POF5: Scanning without chopping

### Summary

| Step | Building Block | Procedure | Description |
| --- | --- | --- | --- |
| 1 | A307-0000 | PSCAN_CONF Set OBSID Set BBID to 0xA307 Set MODE to 0x1400 Set Nominal Hsk packets to 1 per second Set MODE to 0x0350 | Set up instrument for photometer scanning observations Indicate Start of Observation BBID -> 0 Indicate mode changing Normal speed when SPIRE Prime Indicate now in POF1 mode |
| 2 |  | Insert signal attenuator into beam | Effectively gives no signal for most of the observation |
| 3 | A380-0000 | PCAL_FLASH Set BBID to 0xA380 Execute PCAL_Flash | Execute PCAL calibration flash |
| 4 | A350-nnnn | PSCAN Set BBID to 0xA350 Collect data for 60 seconds | Photometric scan |
| 5 |  | Increment STEP | Set new scan number |
| 6 |  | Repeat steps 3-4 for 10 scans During scan 5 after 30 seconds remove signal attenuator for ~ 0.5 seconds | Puts a ‘source’ at the centre of the map |
| 7 | A380-0001 | PCAL_FLASH Set BBID to 0xA380 Execute PCAL_Flash | Execute PCAL calibration flash |
| 8 | A308-0000 | PSCAN_END Set BBID to 0xA308 Set MODE to 0x1350 Move BSM to HOLD position Set STEP to 0 Set Nominal Hsk packets to 0.25 per second Set MODE to 0x0400 Set OBSID=0x00000000 | Return Spectrometer to SPEC_STBY mode Indicate mode changing Normal speed when SPIRE in standby Indicate now in SPEC_STBY Indicate end of observation BBID->0 |

### Test Duration

Approximately 15 mins