# Scope

Outline description of the sequence and procedures to be used during the SPIRE CQM EMC Test once integrated into the Herschel EQM Payload Module at EADS Astrium in Ottobrun.  The pre-requisites for the test are briefly described followed by a table setting out the steps in the test sequence; the names of the procedures to be executed from CCS and the references to any manual procedures required for, for instance, switching on the DRCU; and the estimated duration of each part of the test.

# Change notes

1.0	15 April 2005		First issue

# Applicable Documents

AD1	SPIRE Functional Test Specification - SPIRE-RAL-DOC-001652

AD2	 SPIRE COOLER RECYCLING SCOS PROCEDURE - SPIRE-RAL-PRC-002267

Reference Documents

# Prerequisites for carry out the Short Performance Test

# FPU is integrated onto HOB

WE integrated with CCE

WE integrated with harness and FPU

Warm functional test done

Cold functional test done at “4K” and “1.7K” as per AD1

FP is at nominal temperature and left in REDY mode – see transition diagram in AD1

# Prerequisites for data analysis

SCOS is running and display screens are available with conversion curves loaded

# QLA sequences ready for display of data and FITS output

IDL V 6.0 or later present on local machine (laptop if necessary) with access to FITS filestore via FTP or other method

# Outline Test sequence:

| Step | Description | Procedure Name | Estimated Duration |
| --- | --- | --- | --- |
| EMC test set up |
| E0 | Start from REDY mode |  |  |
| E1 | Recycle cooler | CCS-SPT-CREC | 2 hours |
| E2 | Switch to Photometer Standby | CCS-SPT-PDET-ON CCS-SPT-RESET-OFFSETS-P Requires manual procedure to set equivalent power in BSM coils | 10 minutes |
| E3 | Wait until temperature stabilises | N/A | TBD |
| E4 | Set up for nominal bias and sampling | CCS-SPT-NOMSETTINGS-P | 10 sec |
| Instrument ready for EMC Testing Standard test procedure as follows |
| S1 | Set OBSID for this test EMC set up | CCS-SPT-STARTTEST | 10 sec |
| S2 | Set STEP number for this frequency/power/polarisation etc setting | CCS-SPT-SETSTEPNO At present we pass parameters through the SCOS system – this may not be possible with CCS and we need to discuss how to implement ths. | 10 sec |
| S3 | Dwell for required amount of time at given setting | N/A | TBD |
| S4 | Set EMC equipment to next setting – if not last step go to S2 Else continue | N/A | TBD |
| S5 | Stop test - unset OBSID | CCS-SPT-ENDTEST | 10 sec |