# SPIRE

| SUBJECT: | Cold vibration test procedure PFM |
| --- | --- |
| PREPARED BY: | E Sawyer |
| DOCUMENT No: | SPIRE-RAL-PRC-002539 |
| ISSUE: | 2.2 | Date: | 23/11/05 |
| CHECKED BY: | …………………………………. | Date: | …………………………. |
| APPROVED BY: | …………………………………. | Date: | …………………………. |

Distribution

# Change Record

| ISSUE | DATE |  |
| --- | --- | --- |
| 1 | 10/11/05 | New issue |
| 2 | 17/11/05 | Reference to JFET removed |
|  |  | Levels added to procedure |
|  |  | Temperature sensor data updated |
|  |  | Accelerometer table completed All the SMEC moving carriage accelerometers coded as SMECLX, instead of SMECLX, SMECLY, SMELZ The serial number of the SMECUY is 26087 instead of 26089 The type cell for the SMECBX : it is 2272. |
| 2.1 | 22/11/05 | Title on front page from CQM to PFM. Order of lateral axis changed Title qualification levels changed to acceptance levels Section 2 column added to indicate feed through number |
| 2.2 | 23/11/05 | Sine test in X axis levels changed Intermediate level above 66Hz was 5.7 g now 3.2 g Full level above 66Hz was 11.5 g now 6.4 g |

# Table of Contents

1.	SCOPE	7

2.	Accelerometer allocation	7

3.	Temperature sensor locations	7

4.	Step by step test sequence record	8

# Glossary

| SPIRE | Spectral and Photometric Imaging REceiver |
| --- | --- |

# References

# Applicable Documents

| No | Document | Ref |
| --- | --- | --- |
| AD1 | SPIRE PFM cold vibration test plan | SPIRE-RAL-PRC-002524 |

Reference Documents

# SCOPE

This document describes the detailed procedure to be followed during the cold vibration testing on the FPU to be carried out at CSL, Liege.

It should be used in conjunction with AD1

# Accelerometer allocation

| Channel No | Location | Type | Serial no | Code | Axis | Feed thro’ |
| --- | --- | --- | --- | --- | --- | --- |
| F65 | Photometer detector box | 7724 |  | PHOTX | X | 1 |
| F71 | Photometer detector box | 7724 |  | PHOTY | Y | 2 |
| F53 | Photometer detector box | 7724 |  | PHOTZ | Z | 3 |
| F66 | FPU top of optics bench over cone | 7724 |  | FPUX | X | 4 |
| F69 | FPU top | 7724 |  | FPUY | Y | 5 |
| F52 | FPU top | 7724 |  | FPUZ | Z | 6 |
| F68 | Spectrometer detector box | 7724 |  | SPECX | X | 7 |
| F73 | Spectrometer detector box | 7724 |  | SPECY | Y | 8 |
| F54 | Spectrometer detector box | 7724 |  | SPECZ | Z | 9 |
|  | SMEC moving carriage 1.284pC/g | 2222C | 32974 | SMECLX | X | 10 |
|  | SMEC moving carriage 1.606pC/g | 2222C | 32977 | SMECLY | Y | 11 |
|  | SMEC moving carriage 1.627pC/g | 2222C | 32976 | SMECLZ | Z | 12 |
|  | SMEC top 1.262pC/g | 2222C | 32975 | SMECUX | X | 13 |
|  | SMEC top 1.692pC/g | 2222C | 26087 | SMECUY | Y | 14 |
|  | SMEC top 1.373pC/g | 2222C | AJC49 | SMECUZ | Z | 15 |
|  | SMEC base plate 14.02 pC/g | 2272 | YG32 | SMECBX | X | 16 |
|  | SMEC base plate 1.618pC/g | 2222C | AADN7 | SMECBY | Y | 17 |
|  | SMEC base plate 1.306pC/g | 2222C | 32978 | SMECBZ | Z | 18 |

# Temperature sensor locations

| Sensor No | Location | CODE | Calibration Curve Prime | Calibration curve Redundant |
| --- | --- | --- | --- | --- |
| 1 | RF filter | RF | X30977 | X31056 |
| 2 | Spectrometer 2K | SPEC | X29606 | X29592 |
| 3 | Photometer 2K | PHOT | X29601 | X29603 |
| 4 | Optical sub bench | OPSB | X30981 | X29602 |
| 5 | Input baffle | BAF | X29604 | X31033 |
| 6 | BSM/SOB interface | BSM | X29597 | X31036 |

NB the redundant set will be used for this test as one of the prime set is faulty

# Step by step test sequence record

| No | Activity | Time | Date | Run number | Comments | Resp. |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Test preparation |  |  |  |  |  |
| 1.1 | Unpacking from container: As per AD1 Store container until the end of the test | 3 hrs | 21/11/05 |  |  |  |
| 1.2 | Visual inspection of the FPU Cover with cover provided while awaiting integration Accelerometers and temperature sensors will be fitted before delivery. | 2 hrs | 21/11/05 |  | Record any anomalies |  |
| 2 | Vibration Test in lateral axis |  |  |  |  |  |
| 2.1 | Test preparation Assuming test adaptor is fitted to the shaker Fit FPU to test adaptor in accordance with AD1 Check torque of mounting feet 8.1 Nm plus running torque for M6 8.25 plus running torque or M8 Kaylock nut. 2.1 Nm for the JFET bolts. Remove MGSE Fit temporary thermal straps between FPU and fixture, 4 straps at each end of the SOB. Cover detector harness connectors with copper tape to provide ESD protection Check isolation and record results L1 to FPU FPU to fixture Spectrometer L0 to FPU Pump L0 to FPU Evaporator L0 to FPU Note JFET supports to be lifted from the fixture for this test Connect accelerometers carry out continuity check. Carry out very low level test in ambient 0.25g 5 to 2000Hz Note The Kevlar suspended detectors will not tolerate significant levels when warm. This test is to verify the instrumentation only. Connect temperature sensors Note These sensors do not record accurate temperatures at room temperature. Accurate only below 40K. Individual calibration curves will be supplied by SPIRE | 3 hrs ½ hrs ½ hrs 2 hrs ½ hrs | 22/11/05 |  |  |  |
| 3 | TRR | 4 hrs | 23/11/05 |  |  |  |
| 4 | Shrouds installation, connection of pumps and fluid lines | 2 days | 24/11/05 25/11/05 |  |  |  |
| 5 | Evacuation Monitor pressure during evacuation and check for consistence with evacuation rate requirement in AD1 Re-pressurisation to be in accordance with AD1, max rate 50mb/min Note pressure values or attach record |  | 26/11/05 |  |  |  |
| 6 | Cool down Monitor temperature sensor during cool down and check for consistence with cool down requirements in AD1 5K/hour, between room temperature and 200K, 10K/hour, between 200K and 100K. 50K/hour below 100K Note Temperature or attach temperature record of temperature sensors |  | 26/11/05 27/11/05 28/11/05 |  |  |  |
| 7 | Y axis test |  |  |  |  |  |
| 7.1 | Resonance search O.25 g 5 to 2000Hz 4 octaves per minute Check results against those expected Confirm levels for next test | 1/2hr 2hrs 1hr | 29/11/05 |  |  |  |
| 7.2 | Intermediate sine test Check results Confirm go-ahead for next test | 1/2h 1hrsr 1/2hr | 29/11/05 |  | Test sweep rate 4 Oct/min, the input will be limited to equivalent quasi static interface force. Y axis Frequency Range Hz Acceptance level 5 - 13.5 +/- 2mm 13.5 – 100 for 1000 cycles * Up to 66Hz 3.2 g 13.5 – 100 for remaining cycles 2.4 g TBC |  |
| 7.3 | Full level sine test As per requirements in AD1 Check results | 1/2hr 2hrs |  |  | Test sweep rate 4 Oct/min, the input will be limited to equivalent quasi static interface force. Y axis Frequency Range Hz Acceptance level 5 - 13.5 +/- 2mm 13.5 – 100 for 1000 cycles * Up to 66Hz 6.4 g 13.5 – 100 for remaining cycles 4.8 g TBC |  |
| 7.4 | Resonance search Carry out resonance search as before Compare with previous results | 1/2hr 1hrs | 29/11/05 |  | 0.25g 5 to 2000Hz |  |
| 7.5 | Low level Random test test to AD1 at –12dB Check results | 1hr 2hr | 30/11/05 |  | -12dB Frequency Range Hz Acceptance levels 20-100 +3dB/Oct 100-150 0.0128 g2/Hz 150-300 0.008 g2/Hz 300-2000 -12 dB/Oct Global 2.0 g RMS |  |
| 7.5 | Intermediate level Random test test to AD1 at –6dB Check results | 1/2hr 1hr |  |  | -6dB Frequency Range Hz Acceptance levels 20-100 +3dB/Oct 100-150 0.0128 g2/Hz 150-300 0.008 g2/Hz 300-2000 -12 dB/Oct Global 2.0 g RMS |  |
| 7.7 | Acceptance level random test Carry out test to AD1 Check results | 1/2hr 2hr |  |  | Frequency Range Hz Acceptance levels 20-100 +3dB/Oct 100-150 0.0128 g2/Hz 150-300 0.008 g2/Hz 300-2000 -12 dB/Oct Global 2.0 g RMS |  |
| 7.8 | Resonance search Carry out resonance search as before Compare with previous results | 1/2hr 1/2hr |  |  | 0.25g 5 to 2000Hz |  |
| 7.9 | Post test analysis Check completeness of data Carry out initial assessment | 2hr |  |  |  |  |

| No | Activity | Time | Date | Run number | Comments | Resp. |
| --- | --- | --- | --- | --- | --- | --- |
| 8 | Test in Z axis |  |  |  |  |  |
| 8.1 | Reconfigure to Z axis | 4hrs | 1/12/05 |  |  |  |
| 8.2 | Intermediate test readiness review, in parallel with 8.1 | 1hr | 1/12/05 |  |  |  |
| 8.3 | Z axis test |  |  |  |  |  |
| 8.4 | Resonance search Check results against those expected. Confirm levels for next test | 1/2hr 1hr 1hr |  |  | 0.25g 5 to 2000Hz |  |
| 8.5 | Intermediate sine test Check results against those expected. Confirm levels for next test | 1/2h 1/2hr 1/2hrr |  |  | Test sweep rate 4 Oct/min, the input will be limited to equivalent quasi static interface force. Z axis Frequency Range Hz Acceptance level 5 - 13.5 +/- 2mm 13.5 – 100 for 1000 cycles * Up to 66Hz 3.2 g 13.5 – 100 for remaining cycles 2.4 g TBC |  |
| 8.6 | Full level sine test As per requirements in AD1 Check results | 1/2hr 1/2hr |  |  | Test sweep rate 4 Oct/min, the input will be limited to equivalent quasi static interface force. Z axis Frequency Range Hz Acceptance level 5 - 13.5 +/- 2mm 13.5 – 100 for 1000 cycles * Up to 66Hz 6.4 g 13.5 – 100 for remaining cycles 4.8 g TBC |  |
| 8.7 | Resonance search Carry out resonance search as before Compare with previous results | 1/2hr 1/2hr |  |  | 0.25g 5 to 2000Hz |  |
| 8.8 | Low level Random test test to AD1 at –12dB Check results | 1/2hr 1/2hr | 2/12/05 |  | -12dB Frequency Range Hz Acceptance levels 20-100 +3dB/Oct 100-150 0.0128 g2/Hz 150-300 0.008 g2/Hz 300-2000 -12 dB/Oct Global 2.0 g RMS |  |
| 8.9 | Intermediate level Random test test to AD1 at –6dB Check results | 1/2hr 1/2hr |  |  | -6 dB Frequency Range Hz Acceptance levels 20-100 +3dB/Oct 100-150 0.0128 g2/Hz 150-300 0.008 g2/Hz 300-2000 -12 dB/Oct Global 2.0 g RMS |  |
| 8.10 | Acceptance level random test Carry out test to AD1 Check results | 1/2hr 1/2hr |  |  | Frequency Range Hz Acceptance levels 20-100 +3dB/Oct 100-150 0.0128 g2/Hz 150-300 0.008 g2/Hz 300-2000 -12 dB/Oct Global 2.0 g RMS |  |
| 8.11 | Resonance search Carry out resonance search as before Compare with previous results | 1/2hr 1/2hr |  |  | 0.25g 5 to 2000Hz |  |
| 8.12 | Post test analysis Check completeness of data Carry out initial assessment | 1/2hr 2hrs |  |  |  |  |

| No | Activity | Time | Date | Run number | Comments | Resp. |
| --- | --- | --- | --- | --- | --- | --- |
| 9 | Warm up Heating rate to be in accordance with AD1 Note 5K/hour, between room temperature and 200K, 10K/hour, between 200K and 100K. 50K/hour below 100K Record any anomalies during warm up |  | 3/12/05 4/12/05 5/12/05 |  |  |  |
| 10 | Return to ambient pressure Re-pressurisation to be in accordance with AD1, max rate 50mb/min | 2hrs | 6/12/05 |  |  |  |
| 11 | Remove vacuum vessel and shrouds In preparation for instrument removal | 1.5day | 6/12/05 7/12/05 |  |  |  |
| 12 | Instrument removal Remove instrument and store temporarily in its container in accordance with AD1 | 1/2day | 7/12/05 |  |  |  |
| 13 | Reconfigure vibration facility | 1day | 8/12/05 |  |  |  |
| 15 | Test preparation Assuming test adaptor is fitted to the shaker Fit FPU to test adaptor in accordance with AD1 Check torque of mounting feet 8.1 Nm plus running torque for M6 8.25 plus running torque or M8 Kaylock nut. 2.1 Nm for the JFET bolts. 2.5 nm for the L3 straps to JFETS Remove MGSE Fit temporary thermal straps between FPU and fixture, 4 straps at each end of the SOB. Cover detector harness connectors with copper tape to provide ESD protection Check isolation and record results L1 to FPU FPU to fixture Spectrometer L0 to FPU Pump L0 to FPU Evaporator L0 to FPU Note JFET supports to be lifted from the fixture for this test Connect accelerometers carry out continuity check. Connect temperature sensors Note These sensors do not record accurate temperatures at room temperature. Accurate only below 40K. Individual calibration curves will be supplied by SPIRE Carry out very low level test in ambient 0.25g 5 to 2000Hz Note The Kevlar suspended detectors will not tolerate significant levels when warm. This test is to verify the instrumentation only. | 3 hrs ½ hrs ½ hrs ½ hrs 2 hrs | 9/12/05 9/12/05 |  |  |  |
| 16 | Installation of shrouds, connections of pumps and fluid lines | 1day | 10/12/05 |  |  |  |
| 17 | Evacuation Monitor pressure during evacuation and check for consistence with evacuation rate requirement in AD1 Not to exceed 50mb/min Note pressure values or attach record | 1/2day | 11/12/05 |  |  |  |
| 18 | Cool down Monitor temperature sensor during cool down and check for consistence with cool down requirements in AD1 5K/hour, between room temperature and 200K, 10K/hour, between 200K and 100K. 50K/hour below 100K Note Temperature or attach temperature record of temperature sensors | 2.5days | 11/12/05 12/12/05 13/12/05 |  |  |  |
| 19 | Intermediate Test readiness review | 1hr | 14/12/05 |  |  |  |
| 20 | X axis test |  |  |  |  |  |
| 20.1 | Resonance search Check results against those expected. Confirm levels for next test | 1/2hr 1hr 1hr | 14/12/05 |  | 0.25g 5 to 2000Hz |  |
| 20.2 | Intermediate sine test Check results against those expected. Confirm levels for next test | 1/2h 1/2hr 1/2hrr |  |  | Test sweep rate 4 Oct/min, the input will be limited to equivalent quasi static interface force. X axis Frequency Range Hz Acceptance level 5 - 20.1 +/- 2mm 20.1 – 100 for 1000 cycles * Up to 66Hz 7.2 g 20.1 – 100 for remaining cycles 3.2 g |  |
| 20.3 | Full level sine test As per requirements in AD1 Check results | 1/2hr 1/2hr |  |  | Test sweep rate 4 Oct/min, the input will be limited to equivalent quasi static interface force. X axis Frequency Range Hz Acceptance level 5 - 20.1 +/- 2mm 20.1 – 100 for 1000 cycles * Up to 66Hz 14.4 g 20.1 – 100 for remaining cycles 6.4 g |  |
| 20.4 | Resonance search Carry out resonance search as before Compare with previous results | 1/2hr 1/2hr |  |  | 0.25g 5 to 2000Hz |  |
| 20.5 | Low level Random test test to AD1 at –12dB Check results | 1/2hr 1/2hr |  |  | -12dB Frequency Range Hz Acceptance levels 20-100 +3dB/Oct 100-150 0.032 g2/Hz 150-300 0.0128 g2/Hz 300-2000 -12 dB/Oct Global 2.77 g RMS |  |
| 20.6 | Intermediate level Random test test to AD1 at –6dB Check results | 1/2hr 1/2hr | 15/12/05 |  | -6 dB Frequency Range Hz Acceptance levels 20-100 +3dB/Oct 100-150 0.032 g2/Hz 150-300 0.0128 g2/Hz 300-2000 -12 dB/Oct Global 2.77 g RMS |  |
| 20.7 | Acceptance level random test Carry out test to AD1 Check results | 1/2hr 1/2hr | 15/12/05 |  | Frequency Range Hz Acceptance levels 20-100 +3dB/Oct 100-150 0.032 g2/Hz 150-300 0.0128 g2/Hz 300-2000 -12 dB/Oct Global 2.77 g RMS |  |
| 20.8 | Resonance search Carry out resonance search as before Compare with previous results | 1/2hr 1/2hr | 15/12/05 |  | 0.25g 5 to 2000Hz |  |
| 20.9 | Post test analysis Check completeness of data Carry out initial assessment | 1/2hr 2hrs |  |  |  |  |
| 21 | TRR |  |  |  |  |  |
| 22 | Post Test Activities • check completeness of test data • Warm up Monitor temperature sensor during warm up and check for consistence with cool down requirements in AD1 Note Temperature or attach temperature record of temperature sensors 5K/hour, between room temperature and 200K, 10K/hour, between 200K and 100K. 50K/hour below 100K Venting Monitor pressure during venting and check for consistence with evacuation rate requirement in AD1 Note pressure values or attach record Max rate 50mb/min | 4hrs | 16/12/05 17/12/05 18/12/05 19/12/05 |  |  |  |
| 23 | Dismount dismounting of shrouds • Visual inspection of test specimen • Removal of instrument (TBC) and cleanliness inspection with UV light • Installation of the instrument inside its own container in accordance with AD1 | 4hrs 1hr 2hr 2hr | 19/12/05 20/12/05 20/12/05 20/12/05 |  |  |  |
| 24 | Transport |  | 21/12/05 |  |  |  |

Annex 1   PFM build standard