# Introduction

This document reports on the acceptance tests performed on the OBS version 2.1.G_02032006 (non official delivery) on DPU CFM to be used for PFM3 cold testing.

Note:

The official delivery for PFM3 test campaign was 2.1.E delivered on Dec 2005. Integration tests with the QM2 DRCU electronics on February 2006 showed that the implementation of the FDIR protocol in v2.1.E was incompatible with the nominal operations of the DRCU and would affect the nominal instrument operations. (c.f   HR-SP-RAL-NCR-0142)

## Scope

This report judges the success or failure of a functional test by checking that

- the commands were correctly received and executed by the instrument subsystem

- no error or exception reports were generated

- the appropriate telemetry parameters changed in an expected manner

No detailed analyses of the test data has been performed at this stage.

## Reference Documents

RD01    SPIRE On-Board Software Verification and Validation Plan/Acceptance Test Plan

RD02    SPIRE Data ICD (SPIRE-RAL-PRJ-001078), Issue 1.1, 25th May2004

RD03    SPIRE OBS URD

RD04    SPIRE EGSE-ILT Startup Procedures (SPIRE-RAL-DOC-001630), Issue 0.7, 24th June 2003

RD05    SPIRE OBS Acceptance Test Plan SPIRE-RAL-DOC-002552 Issue 1.0 19th Dec 2005

RD06	 Switch ON Procedure and Telemetry Packets User Manual Draft 2 20 Mar 2003

## Acceptance Test Configuration

### SPIRE EGSE Setup/Configuration

- CDMS Simulator  v.2.5

- SCOS 2000 2.3e Patch Level 5 + TOPE - running on a Linux SuSE 7.3

- OBS 2.1.G to be acceptance tested

- HCSS v0.3.3 (build #812) – includes the EGSE router and gateway running on Lichfiled

- SPIRE MIB 2.1.E1

- EGSE Test Tool PacketDisplay (build #812) running on Truro to display TC and TM packet contents

- Test control server (build #812)  running on Lichfiled with  TclBlend 1.3.2 .Tcl/Tk 8.4.12. Tcl Thread 2.6.2

# pre-test preparations

- The latest version of the OBS should be installed on the Q drive. A folder with the OBS version number (e.g. 1.2J) should normally be created in Q:\OBS\OBS_Source. Because of access restrictions the OBS test team has found it appropriate to install the latest version under Q:\ICC\OBS.

- Ensure that the pcss.jar file containing the PACS supplied OBS loader program is present in directory /home/sops23e/SPIRE/OBS/OBSLoader.

- To load the OBS using the Load Memory telecommands (service 6,2), the zipped file containing the commands will need to be placed in the SCOS 2000 account in a directory under /home/sops23e/SPIRE/OBS/OBSLoader. For example, the telecommands to be loaded for installing 1.2J would be placed in directory

/home/sops23e/SPIRE/OBS/OBSLoader/OBSTCs_1.2J.

- The shell script to load the OBS may need to be modified to point to the location of the Load Memory  telecommands.

## Assumptions

Before the start of the OBS acceptance tests the remainder of the SPIRE EGSE is to be set up and configured using RD03 and RD04. For each set of tests the following minimum steps were also executed beforehand if they were not already activated.

| Step # | Description | Status Parameter Values Before/After | Test Step Status/ Success/Fail |
| --- | --- | --- | --- |
| 1 | Start TM ingestion | 09/03/06 TM ingestion process stopped and restated on Lichfiled. Telemetry will be ingested into drcu_qm2_at@lichfiled database. NO NEW DB WILL BE CREATED FOR THIS AT. | Success Comment: TM_Ingest_ DPU_CFM_OBS_2.1.G_AT_09032006.log is the telemetry ingestion log for this test. |
| 2 | Start Test Control Server running on Lincoln | 09/03/06 Already running on Lichfiled | Success |
| 3 | The DPU is switched on | Power recycled the CFM DPU. When the Boot Software perform checks , generates a (5,1) event packet with the following contents: ID: 0D00 Seq: C000 Len: 0019 0000: 0D00 C000 0019 0005 0100 8000 0000 0000 8008 0003 ABAB CDCD 0051 AAAA 0000 AE6C This is the expected behaviour; no errors are reported in the penultimate 16 bit word. | Success |

# obs acceptance tests

Note:

After several failed attempts to boot the OBS via FORCE_BOOT_PRIMARY command decided to reload OBS 2.1.G_02032006 using the ObsLoader Program located in

## Loading of the new OBS

### Loading the new OBS using Load Memory Service (6,2)

- Execute the script to issue the Load Memory commands. For version 1.2J the script is called ObsLoader_1.2J. Typically four telecommands are sent per second; For version 1.2J it takes about 6 minutes to finish loading the new OBS.

Note: (09/03/06 @ 15:55)

Action :

Used the ObsLoader program ObsLoader_Issue2.1.G_02032006 in directory ~sops23e/SPIRE/OBS/OBSLoader in Lincoln just after the DPU has been switched ON.

Using the SPIRE_Nominal.txt bus list.

Result:

Events (5,1) are received for each telecommand LOAD_MEMORY(6,2) state = 0xBBBB event = 0x11 as expected.

- Once the script has stopped execution the LOAD_TC_AND_BOOT command can be sent from the SCOS 2000 Manual Stack to start running the new OBS.

Action:

Sent LOAD_TC_AND_BOOT command from manual stack

Result:

HK reports start as expected (Nominal and Critical)

SeveraleEvents (5,1) are also received:

1.  1 event (5,1).

Contents:

ID:  0D00

Seq:  C8AB

Len:  0019

0000: 0D00 C8AB 0019 0005 0100 8000 0000 0000 8008 0003 1D00 C6FB 0011 D0D0 08AB     310A

2.  3  events are to report the non response of the DCU,SCU,MCU codes 0x520,0x521,0x522

3.  1 event with code 0x512

Action:

Cleared HK reports

Power UP DRCU

Restarted HK reports

Result:

2 clearing events are received notifying the response from the SCU and DCU.

### Loading of the OBS using the JTAG probe

This should only be attempted if

- DPU and the Warm Electronics are not in the Cryo Lab

- JTAG probe is available and connected between the CPU board of the DPU and ISOPC1 computer

- All attempts to load the new OBS via the OBSLoader program and the LOAD_TC_AND_BOOT command have failed

The load procedure is described in RD04.

Note: (09/03/06 @ 16:20)

N/A

## Housekeeping Generation and OBS Parameter Monitoring

Once the OBS is running HK reports should be generated automatically. The Telemetry Display page DPU AND OBS PARAMETERS on SCOS 2000 displays all the DPU and OBS specific parameters from the nominal HK report. The Telemetry Display page CRITICAL HK PARAMETERS displays the entire contents of the critical HK report.

Note: (09/03/06 @ 16:30 performed the following checks

### HK Generation Rate

- On the DPU AND OBS PARAMETERS display page, is the nominal HK packet generation time, THSK, incrementing once every second?

YES (Success) / NO (Failure)

- On the DPU AND OBS PARAMETERS display page, is the nominal HK packet source sequence count, TM2N, incrementing once every second?

YES (Success) / NO (Failure)

- Is the time on the CRITICAL HK PARAMETERS display page (top right corner) updating once every two seconds?

YES (Success) / NO (Failure)

### DPU and OBS Parameter Monitoring

The following table lists some of the OBS parameters to be monitored from the DPU AND OBS PARAMETERS display page while the nominal HK reports are being generated.

| Nominal HK parameter Name | Expected Value | Actual Value | Success/Failure | Comments |
| --- | --- | --- | --- | --- |
| OBSVER | OBS version 2 1 G | 2.1G (0x2107) | ( |  |  |
| TMMODE | 0 – Normal TM Mode | 0 | ( |  |  |
| DPUP5V | ~5.0 V | 5.13V | ( |  |  |
| DPUP15V | ~14.70 V | 15.42 | ( | A bit higher than before |  |
| DPUM15V | ~-14.98 V | -15.52V | ( | A bit more negative than before |  |
| DPUTEMP | ~304.68K | 300.17 K | ( | A bit higher than before |  |
| DPUP2_5V | ~2.48V | 2.48V | ( |  |  |
| CPULOAD | ?? | 0x27/0x28 | ( |  |  |
| LSLOAD | ?? | Switching between 0x89B20 and 0x84530 | ( |  |  |

## Command Execution

| Command (Parameters) | HK parameter name | Value before | Value after | Result Success/Failure | Comments |
| --- | --- | --- | --- | --- | --- |
| RESET_DRCU_ COUNTERS() | TRESET | 2094.037.06.28.16 (undefined value) | Current Time 2006.068.16.37.45 | Success | Tm packet 1.1, 1,3 1,7 received as expected |  |
| SET_OBSID( OBSERVATION_ID=0x30000000) | OBSID BBID | 0xd05 0 | 0x30000000 0 | Success | The SET_OBSID command also sets the BBID to 0 Tm packet 1.1, 1,3 1,7 received as expected |  |
| SET_OBSID( OBSERVATION_ID=0) | OBSID | 0x30000000 0 | 0 0 | Success | The SET_OBSID command also sets the BBID to 0 Tm packet 1.1, 1,3 1,7 received as expected |  |
| SET_BBID( BUILDING_BLOCK_ID=0x80000000) | BBID | 0 | 0x80000000 | Success | Tm packet 1.1, 1,3 1,7 received as expected |  |
| SET_OBSID( OBSERVATION_ID=0x30000000) | OBSID BBID | 0 0x80000000 | 0x30000000 0 | Success | The SET_OBSID command also sets the BBID to 0 Tm packet 1.1, 1,3 1,7 received as expected |  |
| SET_BBID( BUILDING_BLOCK_ID=0x8000000) | BBID | 0 | 0x80000000 | Success | Tm packet 1.1, 1,3 1,7 received as expected |  |
| SET_OBS_STEP( OBSERVATION_ STEP=0xffff) | STEP | 0 | 0xffff | Success Step Report also checked - OK | A (5,1) New Step Report should be generated Tm packet 1.1, 1,3 1,7 and (5,1) received as expected |  |
| SET_OBS_STEP( OBSERVATION_ STEP=0) | STEP | 0xffff | 0 | Success | A (5,1) New Step Report should be generated Tm packet 1.1, 1,3 1,7 and (5,1) received as expected |  |
| SET_OBS_MODE( OBSERVING_ MODE=1) | MODE | 0 | 1 | Success | Tm packet 1.1, 1,3 1,7 and (5,1) received as expected |  |
| SET_OBS_MODE( OBSERVING_ MODE=0) | MODE | 1 | 0 | Success | Tm packet 1.1, 1,3 1,7 and (5,1) received as expected |  |
| SET_OBS_MODE( OBSERVING_ MODE=0xffff) | MODE | 0 | 0xffff | Success | Tm packet 1.1, 1,3 1,7 and (5,1) received as expected |  |
| SET_OBS_MODE( OBSERVING_ MODE=0) | MODE | 0xffff | 0 | Success | Tm packet 1.1, 1,3 1,7 and (5,1) received as expected |  |
| clear_HK_report.tcl | Packet Ids 0x300 & 0x301 |  |  | Success | Critical and nominal and HK reports should be cleared TM stops as expected. |  |
| define_new_HK_report.tcl | Packet Ids 0x300 & 0x301 |  |  | Success | Default critical and nominal reports should start to be generated TM restarts as expected. |  |

## Virtual Machine

| Command (Parameters) | Action | Result Success/Failure |
| --- | --- | --- |
| SET_TABLE( TABLEID=0x67, TABLESIZE=0x100) | Check for successful command execution on the SCOS 2000 TC History Display | Success Received (1,1) (1,3) (1,7) command completion reports. |  |
| Execute TCL script UpdateTable3.1.tcl Input VM Table File: PTC_TC0.txt SCOS 2000 directory: tcl/TC/VMTables directory | Check for successful script execution on the TOPE command window and monitor command execution on the SCOS 2000 TC History Display | Success Received (1,1) (1,3) (1,7) command completion reports. Command list is updated successfully |  |
| REPORT_TABLE( TABLEID=0x67, INDEX=0, COUNT=0x0) | Use PacketDisplay and/or QLA to examine the contents of the (21,4) Report Table Report. Do the packet contents agree with the contents of the VM Table file? | Success Sent command REPORT_TABLE(0x100,0,0) Command successful and two packets (21,4) packet are produced of lengths: 1018 and 66 as displayed by packet display. Examined contents of packets and the contents agree with the updated table command. |  |
| SET_TABLE( TABLEID=0x64, TABLESIZE=0x300) | Check for successful command execution on the SCOS 2000 TC History Display | Success |  |
| Execute TCL script UpdateTable3.1.tcl twice Input VM Table File: TC0.txt TC1.txt TC2.txt TC3.txt TC4.txt TC5.txt TC6.txt TC7.txt TC8.txt TC9.txt From VMTables/Table100-Functions/TC/ SCOS 2000 directory: tcl/TC/VMTables directory | Check for successful script execution on the TOPE command window and monitor command execution on the SCOS 2000 TC History Display | Success Command list is updated successfully |  |
| SET_TABLE( TABLEID=0x44, TABLESIZE=0x100) | Check for successful command execution on the SCOS 2000 TC History Display | Success |  |
| Execute TCL script UpdateTable3.1.tcl twice Input VM Table File: TC0.txt TC1.txt TC2.txt TC3.txt From VMTables/Table070-Flash/TC/ SCOS 2000 directory: tcl/TC/VMTables directory | Check for successful script execution on the TOPE command window and monitor command execution on the SCOS 2000 TC History Display | Success |  |
|  | Verified that PCAL flash VM is working. Sent manual commands SEND_DRCU_COMMAND(0x84190095,0) SEND_DRCU_COMMAND(0x84180006,0) To setup DCU frame generation @ ~ 18Hz | Success |  |
| RUN_VM(0x46,0,9,4,2748,15,4000000,0,32,33920,0,0) |  | Success PCAL flash command list working NO EVENTS RECEIVED |  |
| RUN_VM(0x46,0,9,4,2748,15,4000000,0,32,33920,0,0) | A second repeat | Success PCAL flash command list working NO EVENTS RECEIVED |  |

## TC Verification Reports

| Command (Parameters) | Action | Result Success/Failure |
| --- | --- | --- |
| REPORT_TABLE(TABLEID=0x99, INDEX=0, COUNT=0x25) | Sent command | Failed as expected. Failure code 0x811 – table not defined. |
| REPORT_TABLE(TABLEID=0x500, INDEX=0, COUNT=0x100) | Sent command | Failed as expected. Failure code 0x805 – Illegal_Table_ID. |
| REPORT_TABLE(TABLEID=0x67, INDEX=0x100, COUNT=0x100) | Sent command | Failed as expected. Failure code 0x806 – Illegal_Table_index. |
| HALT_VM | Sent command while no VM is actually running | Failed as expected. Failure code 0x80A – VM Inactive. |
| FLUSH_FIFO(FIFO_FLAGS=0) |  | Failed as expected .Failure code 0x80F- Illegal_FIFOFlags |
| CLEAR_HK_REPORT(0x300) CLEAR_HK_REPORT(0x301) | Sent this commands after the reports had been already cleared | Failed as expected .Failure code 0x829.- Unallocated HK packet ID |

## 3.6 OBS 2.1.G_02032206 burning into EEPROM

## This extra section has been added to the report to have a record of the actions taken towards having a persistent OBS 2.1.G_02032006 image in EEPROM which would allow the use of the FORCE_BOOT_PRIMARY to start up the OBS application in PM (program memory) without the need of loading the OBS image via LOAD_MEMORY commands.

Important Note:

Lacking a memory map of the OBS 2.1.G_02032006 which is used to extract the start and end address as the input parameters to the WRITETOEEPROM command, these have been copied from the input parameters for the same command for OBS v2.1.E.

Action:

Sent Manual Stack command:

WRITE2EEPROM(0,x4000,x16000,0,0) Used repeater value 0 for the command parameters

Partition flag 0

WITHOUT STOPPING THE HK

Result:

Command successful AFTER SEVERAL SECONDS

Note:

PROBABLY JUST COINCIDENCE BUT JUST AFERT ISSUING THE WRITETOEEPROM COMMAND received a (5,1) event packet Event code  =0x512 NO TIME_SYNC

## 3.7 Conclusions

The acceptance cannot be declared successful unless a power recycle of the DPU + FORCE_BOOT_PRIMARY command results in the start of the generation of both the Nominal and Critical HK reports.

This would confirm (if it occurs) the correct operation of the OBS 2.1.G_02032006 basic functionality tested through the OBS AT procedure.

If this process fails, (as it was the case previously See section 3.1.1), the overall test result is FAILED.

# Text boxes

| Ref: | SPIRE-RAL-REP-002591 |
| --- | --- |
| Issue: | Draft 1 |
| Date: | 9th March 2006 |
| Page: | 1 of 6 |

SPIRE Document

OBS 2.1.G_02032006 AT Report on DPU CFM

Asier Abreu Aramburu