# Introduction

This document reports on the acceptance tests performed on the 9th August 2006 on the OBS v2.2.D installed on the HSDPU FM model.

## Scope

The coverage of this test is limited to basic OBS functionality.

- commanding reception acknowledgement and execution.

- error condition identification and reporting.

This report judges the success or failure of a DPU functional test by checking that

- the commands were correctly received and executed by the DPU.

- no unexpected error or exception reports were generated.

- the appropriate telemetry parameters changed in an expected manner.

## Reference Documents

RD01    SPIRE On-Board Software Verification and Validation Plan/Acceptance Test Plan

RD02    SPIRE Data ICD (SPIRE-RAL-PRJ-001078), Issue 1.1, 25th May2004

RD03    SPIRE OBS URD

RD04    SPIRE EGSE-ILT Startup Procedures (SPIRE-RAL-DOC-001630), Issue 0.7,  24th June 2003

RD05    SPIRE On-Board Software User Manual (SPIRE-IFS-PRJ-001391 Issue 2.2 12th June 2006

## Acceptance Test Configuration

### SPIRE EGSE Setup

- CDMS Simulator  v2.5.

- SCOS 2000 2.3e Patch Level 5 + TOPE installed and running on Truro.

- Truro Server running Linux SuSE 7.3 OS.

- OBS 2.2.D installed on FM DPU.

- HCSS v0.3.3.

- EGSE Router and Gateway running on Truro.

- SPIRE MIB 2.2.D.

- EGSE Test Tool PacketDisplay running on Truro to display TC and TM packet contents.

# pre-test preparations

- The latest version of the OBS should be installed on the Q drive. A folder with the OBS version number (e.g. 1.2J) should normally be created in Q:\OBS\OBS_Source. Because of access restrictions the OBS test team has found it appropriate to install the latest version under Q:\ICC\OBS.

- Ensure that the pcss.jar file containing the PACS supplied OBS loader program is present in directory /home/sops23e/SPIRE/OBS/OBSLoader.

- To load the OBS using the Load Memory telecommands (service 6,2), the zipped file containing the commands will need to be placed in the SCOS 2000 account in a directory under /home/sops23e/SPIRE/OBS/OBSLoader. For example, the telecommands to be loaded for installing 1.2J would be placed in directory

/home/sops23e/SPIRE/OBS/OBSLoader/OBSTCs_1.2J.

- The shell script to load the OBS may need to be modified to point to the location of the Load Memory  telecommands.

## Assumptions

Before the start of the OBS acceptance tests the remainder of the SPIRE EGSE is to be set up and configured using RD03 and RD04. For each set of tests the following minimum steps were also executed beforehand if they were not already activated.

| Step # | Description | Status Parameter Values Before/After | Test Step Status/ Success/Fail |
| --- | --- | --- | --- |
| 1 | Start TM ingestion | TM ingestion process running (on Chichester) | Success TM ingestion logs: FM_DPU_AT_TM_Ingestion.log and FM_DPU_AT_TM_Ingestion_after_DPU_errors.log located in: chichester: /home/sg55/logs/tmingest/ |
| 2 | Start Test Control Server running on Lincoln | Test control server process running (on Chichester) | Success |
| 3 | The DPU is switched on |  | See comments bellow. |

Comments:

Several problems found in booting the OBS 2.2.D on DPU FM

Symptoms:

After the DPU is switched ON the Boot SW v2.0 starts sending (5,1) packets as expected:

Event Packet : READY to ACCEPT TCs

EventID         : 0x8008

SID                 :0x3 as expected.

Then FORCE_BOOT_PRIMARY command is sent to the DPU an a further event (5,1) is received as expected:

Event Packet: TC ACKNOWLEDGE

EventID        : 0x8111

SID                : 0x3 is received as expected.

but,

just afterwards the boot software starts producing events (5,4):

Event Packet:  LOADING EEPROM  to PM

Event ID       : 0x8005

SID                : 0x1

Error Code   : 0xC00

Further attempts to boot DPU are unsuccessful with the same type of events being produced.

When the FORCE_BOOT_SECONDARY command is sent the OBS starts normally.

This acceptance test will be performed with the OBS 2.2.D booted from the secondary partition.

NCR to be raised.

# obs acceptance tests

## Loading of the new OBS

### Loading the new OBS using Load Memory Service (6,2)

- Execute the script to issue the Load Memory commands. For version 1.2J the script is called ObsLoader_1.2J. Typically four telecommands are sent per second; For version 1.2J it takes about 6 minutes to finish loading the new OBS.

- Once the script has stopped execution the LOAD_TC_AND_BOOT command can be sent from the SCOS 2000 Manual Stack to start running the new OBS.

9th August 2006:

- OBS 2.2.D has already been uploaded  using the obsloader program and then saved into EEPROM

### Loading of the OBS using the JTAG probe

This should only be attempted if

- DPU and the Warm Electronics are not in the Cryo Lab

- JTAG probe is available and connected between the CPU board of the DPU and ISOPC1 computer

- All attempts to load the new OBS via the OBSLoader program and the LOAD_TC_AND_BOOT command have failed

The load procedure is described in RD04.

## Housekeeping Generation and OBS Parameter Monitoring

Once the OBS is running HK reports should be generated automatically. The Telemetry Display page DPU AND OBS PARAMETERS on SCOS 2000 displays all the DPU and OBS specific parameters from the nominal HK report. The Telemetry Display page CRITICAL HK PARAMETERS displays the entire contents of the critical HK report.

### HK Generation Rate

- On the DPU AND OBS PARAMETERS display page, is the nominal HK packet generation time, THSK, incrementing once every second?

YES (Success) / NO (Failure)

- On the DPU AND OBS PARAMETERS display page, is the nominal HK packet source sequence count, TM2N, incrementing once every second?

YES (Success) / NO (Failure)

- Is the time on the CRITICAL HK PARAMETERS display page (top right corner) updating once every two seconds?

YES (Success) / NO (Failure)

### DPU and OBS Parameter Monitoring

The following table lists some of the OBS parameters to be monitored from the DPU AND OBS PARAMETERS display page while the nominal HK reports are being generated.

| Nominal HK parameter Name | Expected Value | Actual Value | Success/Failure | Comments |
| --- | --- | --- | --- | --- |
| OBSVER | OBS version as specified in the release note | 2.2.D | Success |  |  |  |
| TMMODE | 0 – Normal TM Mode | 0 | Success |  |  |  |
| DPUP5V | ~5.0 V | 5.04 V | Success |  |  |  |
| DPUP15V | ~14.70 V | 15.43 V | Success | Slightly high?? Floating between 15.9 and 15.4 |  |  |
| DPUM15V | ~-14.98 V | -15.88 V | Success | Slightly high?? Same comments as above |  |  |
| DPUTEMP | ~304.68K | 300.22 | Success |  |  |  |
| DPUP2_5V | ~2.48V | 2.48V | Success |  |  |  |
| CPULOAD | < 300 | Switching between 0x27 and 0x33 | Success |  |  |  |
| LSLOAD | < 700000 | Switching between 542000 and 564000 | Success |  |  |  |
| MONSTAT | Depends on test configuration If DPU is STANDALONE must be 0x222 (RD05) | 0x222 | Success |  |  |  |
| FIFO_DF_FLAG | Refer (RD05) | 7 | Success | No data requested, so this result is correct. |  |  |
| LOSTTCBLOCK | 0 | 0 | Success |  |  |  |
| LOSTEVBLOCK | 0 | 0 | Success |  |  |  |
| LOSTHKBLOCK | 0 | 0 | Success |  |  |  |
| LOSTNTBLOCK | 0 | 0 | Success |  |  |  |

## Command Execution

| Command (Parameters) | HK parameter name | Value before | Value after | Result Success/Failure | Comments |  |
| --- | --- | --- | --- | --- | --- | --- |
| RESET_DRCU_ COUNTERS() | TRESET | 2094.037.06.28.16 (undefined value) | Current Time 2006.221.10.11.10 | Success |  |  |
| SET_OBSID( OBSERVATION_ID=0x30000000) | OBSID BBID | 0xd05 0 | 0x30000000 0 | Success | The SET_OBSID command also sets the BBID to 0 |  |
| SET_OBSID( OBSERVATION_ID=0) | OBSID | 0x30000000 0 | 0 0 | Success | The SET_OBSID command also sets the BBID to 0 |  |
| SET_BBID( BUILDING_BLOCK_ID=0x80000000) | BBID | 0 | 0x80000000 | Success |  |  |
| SET_OBSID( OBSERVATION_ID=0x30000000) | OBSID BBID | 0 0x80000000 | 0x30000000 0 | Success | The SET_OBSID command also sets the BBID to 0 |  |
| SET_BBID( BUILDING_BLOCK_ID=0x8000000) | BBID | 0 | 0x80000000 | Success |  |  |
| SET_OBS_STEP( OBSERVATION_ STEP=0xffff) | STEP | 0 | 0xffff | Success | A (5,1) New Step Report should be generated |  |
| SET_OBS_STEP( OBSERVATION_ STEP=0) | STEP | 0xffff | 0 | Success | A (5,1) New Step Report should be generated |  |
| SET_OBS_MODE( OBSERVING_ MODE=1) | MODE | 0 | 1 | Success | A (5,1) New Obs Mode Report should be generated |  |
| SET_OBS_MODE( OBSERVING_ MODE=0) | MODE | 1 | 0 | Success | A (5,1) New Obs Mode Report should be generated |  |
| SET_OBS_MODE( OBSERVING_ MODE=0xffff) | MODE | 0 | 0xffff | Success | A (5,1) New Obs Mode Report should be generated |  |
| SET_OBS_MODE( OBSERVING_ MODE=0) | MODE | 0xffff | 0 | Success | A (5,1) Obs Mode Report should be generated |  |
| clear_HK_report_1.2J.tcl | Packet Ids 0x300 & 0x301 |  |  | Success | Critical and nominal and HK reports should be cleared |  |
| define_new_HK_report_ 1.2J.tcl | Packet Ids 0x300 & 0x301 |  |  | Success | Default critical and nominal reports should start to be generated |  |

## Virtual Machine

| Command (Parameters) | Action | Result Success/Failure |
| --- | --- | --- |
| SET_TABLE( TABLEID=0x67, TABLESIZE=0x100) | Check for successful command execution on the SCOS 2000 TC History Display | Success |  |  |
| Execute TCL script UpdateTable3.1.tcl Input VM Table File: PTC_TC0.txt SCOS 2000 directory: tcl/TC/VMTables directory | Check for successful script execution on the TOPE command window and monitor command execution on the SCOS 2000 TC History Display | Success |  |  |
| REPORT_TABLE( TABLEID=0x67, INDEX=0, COUNT=0x0) | Use PacketDisplay and/or QLA to examine the contents of the (21,4) Report Table Report. Do the packet contents agree with the contents of the VM Table file? | Success Contents of Reports (21,4) agree with contents of table updated by UPDATE_TABLE command. |  |  |
| RUN_VM | Used PCAL_VM.truro saved stack to verify if table is loaded and if is executed. This executed a PCAL flash VM with parameters: Table ID =0x46 Index = 0 N params= 9 Param 1 = 100 Param 2 = 2000 Param 3 = 40 Param 4 = 250000 Param 5 = 3 Param 6 = 11 Param 7 = 12000 Param 8 = 0 Param 9 = 9 | Success VMSTAT went from 0 to 0x46 as expected. OBS correctly notified a VM exception. These exception are in effect no responses of the DCU and SCU subunits to the commands sent to them by the PCAL flash VM. Event Packets (5,1) with error codes: 0x520 , 0x522 and SID ;0x5113 Nor these units neither the DRCU simulator were used for this acceptance test. FIFO_DF_FLAG went from 7 to 2 accordingly as the DPU was expecting frames on the DCU and SCU FIFOs. |  |  |

## TC Verification Reports

| Command (Parameters) | Action | Result Success/Failure |
| --- | --- | --- |
| REPORT_TABLE(TABLEID=0x27, INDEX=0, COUNT=0x25) |  | Failed as expected. Failure code 0x811 – table not defined. |  |
| REPORT_TABLE(TABLEID=0x500, INDEX=0, COUNT=0x100) |  | Failed as expected. Failure code 0x805 – Illegal_Table_ID. |  |
| REPORT_TABLE(TABLEID=0x67, INDEX=0x100, COUNT=0x100) |  | Failed as expected. Failure code 0x80D – Illegal_Table_index. |  |
| HALT_VM | Sent command while no VM is actually running | Failed as expected. Failure code 0x80A – VM Inactive. |  |
| FLUSH_FIFO(FIFO_FLAGS=0) |  | Failed as expected .Failure code 0x80F- Illegal_FIFOFlags |  |
| CLEAR_HK_REPORT(0x300) CLEAR_HK_REPORT(0x301) | Sent this commands after the reports had been already cleared | Failed as expected .Failure code 0x829.- Unallocated HK packet ID |  |

# Text boxes

| Ref: | SPIRE-RAL-REP-2698 |
| --- | --- |
| Issue: | Draft 1 |
| Date: | 09/08/2006 |
| Page: | 1 of 7 |

SPIRE Document

OBS 2.2.D on DPU FM Acceptance Test Report

A.A.Aramburu & S.D. Sidher