| Spacecraft / Project | HERSCHEL / SPIRE | Meeting Place | Telecon, |
| --- | --- | --- | --- |
| Instrument / Model | SPIRE PFM | Subsystem | FPU |

| Participants | Agenda |
| --- | --- |
| Print Name | Signature | 1. Test specimen - configuration - inspection status - NCR - cleanliness status - open work 2. Test facility - configuration & status - NCR - cleanliness status 3. Test Reports - Test plan and procedure configuration - Test procedure deviations - Evaluation and verification of test results 4. Conclusion - The test was properly executed ? - The test data confirms that the parameters were within the expected required limits ? - No need for further testing - Completeness of data |
| RAL |  |  |
| Eric Sawyer |  |  |
| ESA |  |  |
| Norbert Nikolaizig |  |  |
| ESA |  |  |
| Carsten Scharmberg |  |  |
| CSL |  |  |
| Christophe Grodent |  |  |
|  |  | Additional Distribution |

1. Test specimen - Configuration Full FM standard, as defined in the CIDL. - Inspection status Inspected on delivery, no damage. Standard electrical check performed before test all OK. Inspected on completion of test, no damage. Standard electrical check performed after test NCR raised due to SMEC latch in non latched state. Latch relatched for transit. - NCR NCR 159 raised, SMEC latch unlatched. Attached to minutes. - Cleanliness status Bagged for delivery, covered when being worked on. No sign of contamination visually. - Open work No open work. 2. Test facility - Configuration & status Set up for X axis test. No problems, bellows re-used. All requirements for delta T and cooling rate were observed. 4 days for cool, 3.5 days for warm up. - NCR No NCRs on facility - Cleanliness status Cleanliness status in the test report. Small out of specification on molecular witness. 3. Test Reports - Test plan and procedure configuration SPIRE-RAL-PRC-002597 issue 2 Cold workmanship vibration test plan, PFM SPIRE-RAL-PRC-002598 issue 3 Cold workmanship vibration test procedure, PFM - Test procedure deviations As run procedure will be scanned and made available No deviation from procedure. - Evaluation and verification of test results To be carried out by SPIRE Vibration test report received from CSL. 4. Conclusion - The test was properly carried out as per specification. - The test data confirms that the parameters were within the expected required limits. - Need for further testing This campaign is complete, further tests may be required. - Completeness of data All data has been made available. The test was successfully performed. ESA would like to thank CSL and SPIRE for a successfully run campaign. SPIRE would also like to thank CSL.

| Action | Title & Description |
| --- | --- |
| No | Responsibility | Due Date |  |

List of NCR’s Raised re this Test

| NCR Number | Title | Level | Originator | Date Raised |
| --- | --- | --- | --- | --- |
| HR-SP-RAL-NCR-159 | SMEC unlatched during cryo-vibration test. | Major | E Sawyer RAL | 14/9/06 |