| Date | 11-Oct-2006 |
| --- | --- |
| Time UT | Activity | Signature |
|  | What we are going to do Remove spectrometer bias connector from DCU (J32) |  |
|  | Put copper tape and kapton over open connector on DCU. |  |
|  | Attach connector to breakout box |  |
|  | Using DVM check impedances as laid out in SPIRE-RAL-NOT-001808 (appended) |  |
|  | Attach connector SPIRE photoconductor GSE |  |
|  | Set to test mode and send test signal to JFET |  |
|  | Observe return signal on CRO |  |
|  | Set detector bias and look for ramps. |  |
| 09:22 | What we did Checked all of above – heater clearly present JFET appeared to turn on but with very large AC noise signal Reset pulses can be observed amongst the noise and compensation appears to affect reset Applying bias to detector does something – AC signal disappears but the output flatlines After a while even the noise signal became intermittent. Not at all clear what is going on! Abandoned effort for time being to concentrate on getting the SFT underway | BMS |
|  | Run SPIRE SFT |  |
| Started 09:50 Finished 10:40 | Ran Full procedure except SPIRE-STM2-THO – left thermistors on Switched off LIAs (SPIRE-STM2-DRCU-OFF) SCU and DPU left running Ooops forgot to check the OBSIDs – check with export tool | BMS |
| 15:31 | Shutting instrument down OBSID B000001A SPIRE-STM-FUNC-THO - thermistors off o.k. OBSID B000001B SPIRE-STM-DRCU-OFF – TM2N stopped incrementing THSK stopped incrementing 15:36 Power turned off at SCOE 15:38 DPU power turned off at SCOE | BMS |
|  | SPIRE is OFF |  |
|  | BEFORE LEAVING I STOPPED THE BUS CONTROLLER (BC OFF) |  |