| Spacecraft / Project | Herschel / SPIRE |
| --- | --- |
| Instrument / Model | PFM |
| Sub System / Serial No. | N/A |

| Type of Test | Post Vibration Verification – PFM-4 |
| --- | --- |
| AIV Facility Test No. | N/A |
| Location & Date(s) of Testing | SPIRE Test Facility |
| Applicable Test Specification (Document No. & Issue) | SPIRE-RAL-DOC-002535 – Issue 2.0 |
| Applicable Test Procedure (Document No. & Issue) | SPIRE-RAL-PRC-002748 – Issue 1.0 |
| AIV Facility Test Plan (if applicable?) | N/A |

| Documentation / Inspection Status |
| --- |
| As Built Status? | Currently at issue 2.8 – Numbers of JFET modules to be updated. |
| List of all items /Parts |  |
| Special Instructions |  |
| Inspection Status and Records: |
| Hazards Identified | Ref SPIRE risk assessment ESD precautions to be observed – only trained personnel to access lab. ESD |
| Cleanliness | Inspected in G56 Test facility to be class 6 (old 1000) |
| Unit/Item Bagged | N/A |
| Screws Locked | N/A |
| Connector Savers | Are being used on FPU and Warm Units |
| Other | Adaptors fitted to MCU P17 & P18 to correct error in warm test harness. |

| Assignment of Personnel |
| --- |
| Function | Name | Contact number |
| Test Director | Dave Smith | Ext 5996 |
| Project Manager | Eric Sawyer | Ext 5385 |
| AIV Facility Manager | Dave Smith | Ext 5996 |
| Safety Officer | Dave Smith | Ext 5996 |
| Product Assurance | Eric Clark | Ext 5662 |

CONTINUATION SHEET

| As Built Status (Will the following have an Impact on the test performance / results?) |
| --- |
| Review of all “NCR’s” | To be reviewed offline. |
| Review of all “Waiver’s” | None |
| “Open Work” | See below |
| Other |  |
| MIP’s or KIP’s |  |

ACTIONS / COMMENTS / OBSERVATIONS: Status All work completed on FPU and cryostat. FPU is now in cryostat and cooling down. Action: Dave & Doug to add JFET module numbers to be updated in ABCL SMEC – latching/unlatching has NOT been tested on FPU at low temperatures. This will be tested at the end of the PFM-4 test campaign. IMPORTANT NOTE – current version of OBS might NOT have any of the safety features associated with the latching – or at least they have not been tested. Action: Investigate whether safety features have been implemented in current version of OBS. If not raise an SPR to make sure that this gets into 2.2.E. Action: Update scripts to ensure that latching can only be performed in two stages – i.e. enable unlatching and then send unlatch command. OBS Currently on 2.2.D for functional tests and performance tests. Will need to switch to version 2.2.E for PTC tests (due Friday week). Testing of later versions can be done on AVM1 units. DCRU No open work – acceptance tests were successful. HCSS Acceptance tests of 0.3.6 completed – may need to be updated for AOT tests (to be investigated). Action: Sunil to investigate the need for future update of HCSS for AOTs Scripts Need to give a CVS tag before getting cold – in progress. Update to PTC and recycle VMs required. Current cooler recycle VM can be used for this test campaign. Action: Annso and Doug to define updates to VMs – cooler recycle VM needed by end of this week. Action: Snapshot of current system is needed as soon as test scripts have been updated. QLA V3.2 installed – has tables for redundant side.

Planning Dave to produce test rota. Cool functional test on 3rd November (prime & redundant) Transfer He on 6th November Current plan is to be cold by 7th November Cold functional tests on 7th November - note both heat switches to be closed after functional test. Vss tests before 1st cooler recycle. Will be working a 2 shift system as before. Weekends are maintenance and tests requiring minimum activities (e.g. thermal, AOTs). Sarah here for next 3 weeks Ivan here for end November and start of December Henri and Rene’ will be here to support cold functional tests. Hien and Bernard should be coming over (details TBC) Locke will be coming over from Mid November to February. LAM will be coming 3rd week of November to support SMEC testing. Doug will be leaving UK for 4 weeks from end of November. Mechanism tests will be performed early on during the functional tests. AOB FPGA running times need to be logged Visitor’s PC to be set up in control room.

Test Readiness We are ready to go.

| Decision for test continuation: | YES / NO / REVIEW | Review Date: |  |
| --- | --- | --- | --- |
| Company | Name |  |
| RAL | Eric Sawyer Dave Smith Ken King Bruce Swinyard | Tanya Lim Doug Griffin Sunil Sider Asier Aramburu Eric Clark |
| Cardiff | Matt Griffin |  |