STM2 Grounding Violation Investigation

Doug Griffin

Table of Contents

Background	1

Appendix 1 – SPIRE NCR-163 Proposal	2

Appendix 2 – Nominal PFM Grounding Diagram	3

Appendix 3 – Nominal STM2 Grounding Diagram	4

Appendix 4 – Nominal STM2 Grounding Diagram during Grounding Verification	5

Appendix 5 – Nominal STM2 Grounding Diagram for NCR-163 Investigation (Stage 2)	6

Appendix 6 – Nominal STM2 Grounding Diagram for NCR-163 Investigation (Stage 3)	7

Appendix 7 – Nominal STM2 Grounding Diagram for NCR-163 Investigation (Stage 4)	8

# Background

Problem

- FPU Faraday Shield should have galvanic isolation from S/C except at DCU/FCU

- Detector Analogue Ground should be isolated from FPU and S/C except at DCU/FCU

Verifications made prior to test

- Isolation of SPIRE FPU from OBA verified during during electrical integration of the instrument at FN (Ref; HP-2-ASED-SD-XX)

- Isolation of SIH-CS Faraday shield wires from OBA verified prior to mating with SPIRE

- CQM Electrical IF Checkout 2216 Issue 8 (23/05/06) indicated that the PLW Grounding and FPU Isolation was OK

Review of SPIRE NCRs

- HR-SP-RAL-NCR-082 - Electrical Short on Cooler Strap

  - Closed with the improved gluing procedure – but CQM has old procedure

- HR-SP-RAL-NCR-083 - Electrical Short on Photometer Detector Box Feet

  - Closed. No longer use Kapton

- HR-SP-RAL-NCR-125 – Heat shrink cracks during thermal cycling.

- HR-SP-RAL-NCR-096 - L1 electrical short

  - Opened during incoming inspection for EQM tests

  - Intermittent fault – not properly resolved

- HR-SP-RAL-NCR-092v2 - SPIRE EQM Electrical Interface Bench Test Anomalies

  - Closed

Drawings Comments

- RED indicates S/C (i.e. CVV, OBA, SVM, cryoharness Outer Overall Shield etc.)

- PINK indicates the FPU Faraday Shield Pins.

- GREEN indicates analogue detector ground. The Photometer and the Spectrometer grounds are separated in the cold end and are commoned to a star point in the DCU

- Configurations shown include the nominal PFM, the nominal STM2 and proposed tests

# Appendix 1 – SPIRE NCR-163 Proposal

# Appendix 2 – Nominal PFM Grounding Diagram

# Appendix 3 – Nominal STM2 Grounding Diagram

# Appendix 4 – Nominal STM2 Grounding Diagram during Grounding Verification

# Appendix 5 – Nominal STM2 Grounding Diagram for NCR-163 Investigation (Stage 2)

# Appendix 6 – Nominal STM2 Grounding Diagram for NCR-163 Investigation (Stage 3)

# Appendix 7 – Nominal STM2 Grounding Diagram for NCR-163 Investigation (Stage 4)