Change Log

| Date | Issue | Change |
| --- | --- | --- |
| Thursday 16 November 2006 | 0 | Email summary circulated for comment prior to drafting |
| Monday, 20 November 2006 | 1.0 | Initial drafting of document |
| Tuesday, 30 January 2007 | 1.1 | Corrected several typos |

Scope

This procedure outlines a series of tests to:

- Investigate the cause of some channels on the PFM instrument show anomalous behaviour.

- Measure the dissipation in each of the individual JFET membranes (half modules)

General ESD Precautions

1. Personnel carrying out operations on the cryoharness are to be grounded to the laboratory ground via a wrist strap

2. When mating or demating a connector, an air ionizer is to be used to discharge the area around the connector for > 60 sec prior to carrying out the operation

3. Only the two people directly involved in the test are to be in the cryolab when carrying out the mate-demate procedures or a breakout box is mated to the instrument

4. Immediately prior to connecting a DVM or Scope probe to a Breakout Box contact, it is to be shorted to chassis to remove any stray charge

JFET Power and Vdd / Vss Measurement

## Iss and Idd measurement

Note: Normal text is for the measurements on the Photometer, italics in blue are the procedure variations for the spectrometer

- Prepare a 78-Way (37-way) breakout box with 20 Ohm inline resistors (40 Ohm for SLW measurements, 20 Ohm for SSW and PTC) as indicated in Table 1 (Table 2). Note: 20 Ohms gives about 24mV voltage drop for a nominal bias current.

- Cover exposed contacts on the breakout box not listed in Table 1 (Table 2) with static dissipative and electrostatic shielding material (e.g. Lumealloy).

- Measure and record the resistance of each resistor.

- Check instrument telemetry that the temperature of the detectors is above 1.7K. Close the evaporator heat switch if necessary.

- Switch off the DRCU and DPU

- Check that DCU J30 (DCU J32Table 2) is mated with DCU P30 (DCU P32Table 2) (it should of course be mated, but it is better to check).

- Demate DCU P29 (DCU P31Table 2) from the DCU

- Place the exposed DCU P29 (DCU P31Table 2) connector in a dissipative ESD bag.

- Short the contacts of the plug connector of the breakout box to chassis with conductive foil

- Mate the 78-way Breakout Box to DCU J29 (DCU J31Table 2)

- Remove DCU P29 (DCU P31Table 2) from the bag and mate to the Breakout Box

- Secure the Breakout Box in a location where there is no risk of ESD events or the box falling and the resistors coming out of the contacts.

- Switch on the DPU and DRCU in Prime mode

- Set up the instrument in Photometer (SpectrometerTable 2) mode with the nominal Vss settings.

- Measure the voltage drop across the resistors and record the values in Table 1 (Table 2).

- Measure Vdd and Vss at the output of the DCU with respect to chassis and record the values in Table 1 (Table 2).

- Switch the instrument off

- Demate DCU P29 (DCU P31Table 2) from the breakout box and place the exposed connector in an ESD dissipative bag.

- Demate the breakout box from DCU J29 (DCU J31Table 2)

- Mate DCU P29 to DCU J29 (DCU P31 to DCU J31).

## Vss and Vdd measurement

- Remove the inline resistors from the 78-Way (37-way) breakout box and reinstall the bridges

- Demate DCU P30 from DCU J30 (DCU P32 from DCU J32).

- Place the exposed DCU P30 (DCU P32Table 2) connector in a dissipative ESD bag.

- Short the contacts of the plug connector of the breakout box to chassis with conductive foil

- Mate the 78-way Breakout Box to DCU J30 (DCU J32Table 2)

- Remove DCU P30 (DCU P32Table 2) from the bag and mate to the Breakout Box

- Secure the Breakout Box in a location where there is no risk of ESD events or the box falling and the resistors coming out of the contacts.

- Switch on the DPU and DRCU in Prime mode

- Set up the instrument in Photometer (SpectrometerTable 2) mode with the nominal Vss settings.

- Measure Vss and Vdd and record the values in Table 1 (Table 2).

- Switch the instrument off

- Demate DCU P30 (DCU P32Table 2) from the breakout box and place the exposed connector in an ESD dissipative bag.

- Demate the breakout box from DCU J30 (DCU J32Table 2)

- Mate DCU P30 to DCU J30 (DCU P32 to DCU J32)

Table 1 – 78-Way Breakout box for photometer Idd/Iss measurement

|  | (a) Vdd Contact | (b) Measured resistance | (c) dV | (d) Idd | (e) Vdd J29 | (f) Vdd J30 | (g) Vss Contact | (h) Measured resistance | (i) dV | (j) Iss | (k) Vss J29 | (l) Vss J30 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| PSW_JFET_V1 | 1 |  |  |  |  |  | 2 |  |  |  |  |  |
| PSW_JFET_V2 | 3 |  |  |  |  |  | 23 |  |  |  |  |  |
| PSW_JFET_V3 | 4 |  |  |  |  |  | 5 |  |  |  |  |  |
| PSW_JFET_V4 | 41 |  |  |  |  |  | 60 |  |  |  |  |  |
| PSW_JFET_V5 | 61 |  |  |  |  |  | 62 |  |  |  |  |  |
| PSW_JFET_V6 | 63 |  |  |  |  |  | 44 |  |  |  |  |  |
| PMW_JFET_V1 | 10 |  |  |  |  |  | 11 |  |  |  |  |  |
| PMW_JFET_V2 | 12 |  |  |  |  |  | 31 |  |  |  |  |  |
| PMW_JFET_V3 | 69 |  |  |  |  |  | 70 |  |  |  |  |  |
| PMW_JFET_V4 | 71 |  |  |  |  |  | 52 |  |  |  |  |  |
| PLW_JFET_V1 | 36 |  |  |  |  |  | 17 |  |  |  |  |  |
| PLW_JFET_V2 | 18 |  |  |  |  |  | 19 |  |  |  |  |  |

Table 2 – 37-Way Breakout box for spectrometer Idd/Iss measurement

|  | (a) Vdd Contact | (b) Measured resistance | (c) dV | (d) Idd | (e) Vdd J31 | (f) Vdd J32 | (g) Vss Contact | (h) Measured resistance | (i) dV | (j) Iss | (k) Vss J31 | (l) Vss J32 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SLW_JFET_V1 | 25 |  |  |  |  |  | 7 |  |  |  |  |  |
| SLW_JFET_V2 | 8 |  |  |  |  |  | 27 |  |  |  |  |  |
| SSW_JFET_V1 | 11 |  |  |  |  |  | 30 |  |  |  |  |  |
| SSW_JFET_V2 | 33 |  |  |  |  |  | 15 |  |  |  |  |  |
| PTC_JFET_V | 21 |  |  |  |  |  | 3 |  |  |  |  |  |

Pixel Check

Similar approach as the JFET power measurement.

- Detectors at > 1.7K

- Switch the instrument off

- Put a breakout box inline

- Switch the instrument on in PDET_STBY (or SDET_STBY)

- Measure Vs (Sig+ and Sig-) for the suspect channel + at least one good detector on the same connector

  - Unmate the harness from the DCU

  - Put the exposed connector in a ESD bag

  - Mate the breakout box to the DCU (shorting contacts prior to mating so that charge is removed)

  - Mate the cryoharness to the Breakout box

  - Make the measurements

  - Remove the cryoharness from the break out box and put in ESD bag

  - Remove the breakout form the DCU

  - Mate the cryoharness to the DCU

- Repeat for any questionable channel on that connector

- Switch off and repeat for any other suspect channels on different connectors