Table of Contents

Change Log	1

1.	Scope	2

2.	Reference Documents	2

3.	Channels monitored during testing	2

4.	Injection calibration	3

5.	Test results	4

5.1	8-20MHz Band	4

5.1.1	Test conditions	4

5.1.2	Channel susceptibilities	5

5.2	20-120MHz Band: 1.2V/m + 6dB	9

5.2.1	Test conditions	9

5.3	20-120MHz Band: 1.2V/m + 0dB	9

5.3.1	Test conditions	9

5.3.2	Manual search for Peak Susceptibilities	14

5.4	Test conditions	21

5.5	Susceptibility Threshold at 30.9 MHz	22

5.5.1	Channels 1-12	22

5.5.2	Channels 13-24	24

5.5.3	Channels 25-36	26

5.5.4	Channels 37-48	28

6.	Comparison STM2 and EQM susceptibility thresholds	30

7.	Load curve analysis	30

8.	Appendix 1 – Susceptibility threshold during EQM Test Campaign	32

9.	Appendix 2: Length of cryoharness and /2 resonance	33

Change Log

| Date | Issue | Change |
| --- | --- | --- |
| 18 November 2006 | 0.1 | Initial drafting of document |
| 27 November 2006 | 0.11 | Circulate for comment |
| 12 Jan 2007 | 0.2 | Some changes |
| 16 March 2007 | 0.3 | More updates for PFM DRB summary |

Scope

This document reports and documents the RS susceptibility tests carried out at ESTEC on the SPIRE CQM instrument in the PFM Cryostat within the scope of the satellite STM2 test campaign during the period 16-Oct-2006 to 21-Oct-2006.

Reference Documents

RD1: ‘’PLM EQM EMC Test Procedure, HP-2-ASED-PR-0033, dated 21.09.05

RD2:  “SPIRE EQM EMC Test Procedure” SPIRE-RAL-PRC-002545, Issue: 2.0 pre-release

Channels monitored during testing

Figure 1 - PLW Array pixel map – bad channels are identified by black colouring.

Figure 1 shows the physical mapping of the various detector channels onto the array. The channels prefixed by the letters A-E are normal optical pixels. Channel R1 is designated as a resistor channel which is intended to have a similar impedance to a normal working pixel, but with a static impedance independent of the bias current or temperature. Channels T1 and T2 are mounted on the 300-mK bath and are intended to monitor the base temperature of the bolometers. They have a strong thermal coupling to the 300-mK bath and should therefore show a weak correlation between thermal loading and temperature rise. Channels DP1 and DP2 are physically similar to the normal optical pixels except that they are enclosed inside a dark cavity and should show no optical response.

The channel yield for the CQM array is 38/48 (79.2%) and the following channels are listed as being out of specification and are therefore excluded from the EMC analysis.

R1

B5

B6

A1

E1

E3

D5

D8

DP2

E9

Table 1 – Bad channels in the SPIRE CQM array

It was noted that the response (V) of pixel C5 to P-Cal flashes was approximately 5 times higher than comparable neighbouring pixels.

Injection calibration

The E-Field generated by the combination of the antenna, RF amplifier and signal synthesizer was calibrated in the ESTEC Maxwell anechoic facility. The E-Field was measured with a calibrated probe, 1 m from the radiating antenna. A calibration file was generated which was stored in the signal synthesizer to achieve the correct field strength in the clean room.

# Test results

8-20MHz Band

Test conditions

| Test type | Frequency Sweep |
| --- | --- |
| Signal | Sinusoidal |
| Amplitude Modulation | 100% Amplitude 1 Hz 80% duty cycle (800ms on: 200ms off) |
| ObsID | 0xB000003E |
| Injection Amplitude | 1.2V/m + 6dB = 2.4V/m |
| Start Frequency | 8MHz |
| End Frequency | 20MHz |
| Frequency Step | 1% (Log-linear) |
| Step Dwell | 5 sec |
| EMI Countermeasures | None |
| Antenna | Monopole, ~ 1m from cryostat |
| Time and date | 17-Oct-2006 12:03 to 12:37 |
| Counter measures | None |

Channel susceptibilities

Figure 2 - 8-20MHz sweep channel 1-12 response

Figure 3 - 8-20MHz sweep channel 13-24 response

Figure 4 - 8-20MHz sweep channel 25-36 response

Figure 5 - 8-20MHz sweep channel 25-36 response

## 20-120MHz Band: 1.2V/m + 6dB

Test conditions

| Test type | Frequency Sweep |
| --- | --- |
| Signal | Sinusoidal |
| Amplitude Modulation | 100% Amplitude 1 Hz 80% duty cycle (800ms on: 200ms off) |
| ObsID | 0xB0000040 |
| Injection Amplitude | 1.2V/m + 6dB = 2.4V/m |
| Start Frequency | 20MHz |
| End Frequency | 120MHz |
| Frequency Step | 1% (Log-linear) |
| Step Dwell | 5 sec |
| EMI Countermeasures | None |
| Antenna | Biconic, ~ 1m from cryostat |
| Time | 17-10-2006 12:38 |

Susceptibilities were on QLA during this test, so it was decided to repeat this portion of the spectrum at 1.2V/m.

20-120MHz Band: 1.2V/m + 0dB

Test conditions

| Test type | Frequency Sweep |
| --- | --- |
| Signal | Sinusoidal |
| Amplitude Modulation | 100% Amplitude 1 Hz 80% duty cycle (800ms on: 200ms off) |
| ObsID | 0xB0000042 |
| Injection Amplitude | 1.2V/m + 6dB = 2.4V/m |
| Start Frequency | 20MHz |
| End Frequency | 120MHz |
| Frequency Step | 1% (Log-linear) |
| Step Dwell | 5 sec |
| EMI Countermeasures | None |
| Antenna | Biconic, ~ 1m from cryostat |

Figure 6

Figure 7

Figure 8

Figure 9

### Manual search for Peak Susceptibilities

Test carried out by setting the function generator to an initial frequency known to be lower than the peak susceptibility and manually stepping the frequency up in small increments. At each step, the magnitude of the EMI is recoded as being better or worse. The assumption is that there is only one global peak susceptibility in the range of frequencies selected.

| 32.56697 |  |
| --- | --- |
| 32.89264 | Worse |
| 33.22156 | Worst |
| 33.55378 | Better |

| 22.5365 |  |
| --- | --- |
| 22.76187 | Worse |
| 22.98948 | Worst |
| 23.21938 | Better |
| 23.45157 | Better |

Figure 10

Figure 11

Figure 12

Figure 13

Figure 14 – Normalised susceptibilities (wrt E4 which showed highest susceptibility in this sweep)

Figure 15 - Schematic view of contact arrangement/allocation on PLW vacuum feedthru. The seven most susceptible channels are cross hatched in black ink.

Figure 16 - Detector channel system table. Yellow highlighted rows correspond to nominally functional channels with large susceptibility

## Test conditions

| Test type | Frequency Sweep |
| --- | --- |
| Signal | Sinusoidal |
| Amplitude Modulation | 100% Amplitude 1 Hz 80% duty cycle (800ms on: 200ms off) |
| ObsID | 0xB000007E |
| Injection Amplitude | 1.2V/m + 6dB = 2.4V/m |
| Start Frequency | 20MHz |
| End Frequency | 80MHz |
| Frequency Step | 2% (Log-linear) |
| Step Dwell | 10 sec |
| EMI Countermeasures | 6 Ferrites on each harness |
| Antenna | Biconic, ~ 3m from cryostat |

Figure 17 - Comparison between peak susceptibility in the 20-80MHz range with Ferrite to the peak without a Ferrite

Figure 18

Susceptibility Threshold at 30.9 MHz

Channels 1-12

Figure 19

Figure 20

Channels 13-24

Figure 21

Figure 22

Channels 25-36

Figure 23 – Channels E1

Figure 24

Channels 37-48

Figure 25

Figure 26

Comparison STM2 and EQM susceptibility thresholds

Figure 27 - Comparison between susceptibility threshold found during EQM and STM2 tests. Plots indicate the field which induces a peak noise PSD of 100nV/rt(Hz)

Load curve analysis

Estimated power and noise for 30 MHz EMC test during STM2 testing.

Upper plot is estimated absorbed power measured two different ways – comparison to dark loadcurve (red) and comparison to internal thermistor (purple)

Lower plot is estimated voltage noise for dark loadcurve (black) and during EMC irradiation (purple)

Figure 28 - Load curve analysis

# Appendix 1 – Susceptibility threshold during EQM Test Campaign

# Appendix 2: Length of cryoharness and /2 resonance

| Function | Harness | CS | IS | SS | Total | Half wave resonant frequency |
| --- | --- | --- | --- | --- | --- | --- |
| Spect Bias | SIH-01 | 1350 mm | 2455 mm | 1245 mm | 5.05 m | 29.7 MHz |
| SSW | SIH-02 | 1315 mm | 2816 mm | 1206 mm | 5.34 m | 28.1 MHz |
| Phot Bias | SIH-03 | 1270 mm | 2136 mm | 1547 mm | 4.95 m | 30.3 MHz |
| PMW | SIH-04 | 1280 mm | 2816 mm | 1556 mm | 5.65 m | 26.5 MHz |
| PMW | SIH-05 | 1200 mm | 2816 mm | 1728 mm | 5.74 m | 26.1 MHz |
| PLW | SIH-06 | 1165 mm | 2816 mm | 1265 mm | 5.25 m | 28.6 MHz |
| PSW | SIH-07 | 1035 mm | 2365 mm | 1242 mm | 4.64 m | 32.3 MHz |
| PSW | SIH-08 | 1245 mm | 1905 mm | 1279 mm | 4.43 m | 33.8 MHz |
| PSW | SIH-09 | 1295 mm | 2816 mm | 1252 mm | 5.36 m | 28.0 MHz |
| S/S Prime | SIH-10 | 1790 mm | 2024 mm | 1784 mm | 5.60 m | 26.8 MHz |
| S/S Prime | SIH-11 | 1710 mm | 1843 mm | 1858 mm | 5.41 m | 27.7 MHz |
| S/S Red. | SIH-12 | 1630 mm | 1896 mm | 1717 mm | 5.24 m | 28.6 MHz |
| S/S Red. | SIH-13 | 1790 mm | 1748 mm | 2015 mm | 5.55 m | 27.0 MHz |

Table 2

Figure 29