# Introduction

This document reports on the WARM FUNCTIONAL TESTS carried out on the SPIRE Flight Instrument Model at the start of the PFM5 ILT tests campaign to verify the correct functioning of each of its subsystems prior to cool down. The test cryostat chamber was fully pumped down.

## Scope

To judge the success or failure of a warm functional test by checking that:

- The telecommand sequence generated for a particular functional test is correctly received and executed on board by the SPIRE DPU.

- No error/event reports or command failures are generated during the execution of these commands.

- Telemetry is generated by the instrument as a result of telemetry requests to its different subunits.

- Particular telemetry parameters for each functional test change in an expected manner.

- A particular success criterion/criteria (specified in this document) is/are met.

## Reference Documents

| Ref | Document | Name | Version/Issue Nb. |
| --- | --- | --- | --- |
| RD01 | SPIRE-RAL-DOC-001652 | SPIRE Functional Tests Specification | Issue 1.4 |
| RD02 | SPIRE-RAL-DOC-001630 | SPIRE EGSE-ILT Start-Up Procedures | Issue 0.7 |
| RD03 | SPIRE-RAL-PRC-002222 | DRCU Switch ON Procedure | Issue 1.0 |
| RD04 | SPIRE-RAL-PRJ-001078 | SPIRE Data ICD | Issue 2.0 |
| RD05 | Sap-SPIRE-CCa-076-02 | DRCU/DPU Interface Control Document | Issue 1.2 |
| RD06 | LAM.PJT.SPI.NOT.011011 | MCU/DPU Command List ICD | Issue 5.0 |
| RD07 | SPIRE-IFS-PRJ-001391 | SPIRE OBS User Manual | Issue 2.2 |
| RD08 | SPIRE-IFS-PRJ-000650 | SPIRE DPU Interface Control Document | Issue 1.1 |

## Change Record

| Document | Change date | Changes |
| --- | --- | --- |
| Issue 1.0 | 3rd January 2007 | First version of the document created. |

# Table of Contents

1.	Introduction	1

1.1	Scope	1

1.2	Reference Documents	1

1.3	Change Record	1

2.	Functional Tests Configuration	4

2.1	SPIRE Instrument Configuration (REDUNDANT)	4

2.2	Software Configuration (REDUNDANT)	4

2.3	EGSE Configuration Checks	5

3.	Test procedure	7

3.1	General Pass/Fail Criteria	7

3.2	General Test Sequence	7

4.	Detailed Test Results on REDUNDANT instrument.	9

4.1	FUNC-SCU-01	9

4.2	FUNC-SCU-03	11

4.3	FUNC-SCU-06	13

4.4	FUNC-SCU-02	15

4.5	FUNC-SCU-08	17

4.6	FUNC-SCU-04	19

4.7	FUNC-SCU-05	20

4.8	FUNC-SCU-07	21

4.9	FUNC-MCU-01	22

4.10	FUNC-MCU-02	24

4.11	FUNC-MCU-03	26

4.12	FUNC-MCU-04	28

4.13	FUNC-BSM-01	30

4.14	FUNC-BSM-02c	32

4.15	FUNC-BSM-02j	32

4.16	FUNC-BSM-03	34

4.17	FUNC-BSM-06	36

4.18	36

4.19	FUNC-SMEC-03	39

4.20	FUNC-SMEC-01	41

4.21	FUNC-SMEC-04a	43

4.22	FUNC-SMEC-02A/B	45

4.23	FUNC-SMEC-09	46

4.24	FUNC-SMEC-07	48

4.25	FUNC-SMEC-04B	50

4.26	FUNC-DCU-01	52

4.27	FUNC-DCU-02	55

4.28	FUNC-DCU-03	56

4.29	FUNC-DCU-04P	57

4.30	FUNC-DCU-11P	59

4.31	FUNC-DCU-13P	61

4.32	ILT_PERF_DNA_P	63

4.33	FUNC-DCU-04S	65

4.34	FUNC-DCU-11S	67

4.35	FUNC-DCU-13S	69

4.36	ILT_PERF_DNA_S	71

5.	Annexe1 (Instrument nominal configuration/modes)	72

6.	Annexe 2 (Results of Load Curves)	73

# Functional Tests Configuration

## SPIRE Instrument Configuration (REDUNDANT)

SPIRE FPU:

- FPU In Tank.

- DRCU to Cryostat harnesses connected (Grounding pins not connected)

- Cryostat open

- Cryo-harness connected to FPU

SPIRE FM DPU:

- DPU Power supply connected on DPU Power REDUNDANT (J01) connector (DPU side).

- 1553 Mil Bus connected on REDUNDANT Connector Bus A (J03) connector (DPU side).

- DPU-DRCU REDUDANT  interfaces connected:

SPIRE FM DRCU:

- DRCU Power supply connected on DRCU Power REDUNDA NT (J05) connector (DRCU side on FCU) via the external DRCU switch box.

- FCU to DCU REDUNDAN T power connector J7 (FCU) to J03 (DCU) via the external DPU switch box.

## Software Configuration (REDUNDANT)

The current EGSE software configuration for the REDUNDANT side tests:

| EGSE component | Version/Build number | Comment |
| --- | --- | --- |
| SCOS2000 | SCOS2.3e Patch 5 | SCOS archives PFM4_TEST3_PRIME under /spired/hfiles and /spired/TMD SCOS MIB is PFM4_Issue2.2.D1_Redundant |
| CDMS Simulator | v2.5 |  |
| HCSS | v0.3.6 Build #1043 |  |
| QLA | 3.2.3 Build #438 |  |
| QLA scripts | ? |  |
| Test Control scripts | Create TAGS |  |
| CUS Scripts | Create TAGS |  |
| Versant | 7.0.0.1 |  |
| TFCS | MIB v1.9 Code |  |
| TFTS | MIB v1.6 Server code v1.6 |  |

## EGSE Configuration Checks

To check for the success of failure of a functional test, the real time telemetry of the instrument has to be monitored. The following applications must be running to do so. Before the test sequence starts, make the following checks:

| Workstation | EGSE component | Status | Check | Comments |
| --- | --- | --- | --- | --- |
| Lichfield | EGSE router | Started | ( | Running in the background – no dedicated console on lichfield |
| Lichfield | EGSE Gateway | Started | ( | Running in the background – no dedicated console on lichfield |
| Lichfield | Telemetry Ingestion | Started | ( | Running |
| Lichfield | Packet Display | Started | ( | Running |
| Lincoln | SCOS2000 | Started | ( | Running |
| Lincoln | EXIF + TOPE | Started | ( | Running |
| Lincoln | Manual Stack | Started | ( | Running |
| Gordon | CDMS Simulator | Started | ( | Running |
| Lichfield | Test Control Server | Started | ( | Running |

The following checks were performed to verify the correct initial instrument configuration for the tests.

| Step# | Action | Comments | Check |
| --- | --- | --- | --- |
| 1 | In SCOS open DPU_AND_OBS_PARAMETERS display Check if : TM2N is incrementing by one @1Hz. TM1N is incrementing by one @0.5Hz. - If they are, go to step 5. - If they are not, go to step 2. | Both TM1N and TM2N are incrementing at their nominal rates. Will go to step 5. | ( |
| 2 | Check if the DPU is powered ON: - If ON, the DPU power supply LCD will show ~ 28V and 0.40A, go to step 4. - If not ON, power ON DPU see comments on the right, then go to step 3. |  |  |
| 3 | In SCOS open Boot_ROM_Memory_Check display and check no errors are reported: - If no errors are reported, execute DPU_ON from HCSS Test Procedures. Then repeat step 1. - If the (5,1) contains errors: Check the error code in RD07. Then switch OFF the DPU and repeat step 2 |  |  |
| 4 | Execute define_new_HK_report.tcl HCSS Test procedure. |  |  |
| 5 | In SCOS open SCU_PARAMETERS display - If SCUP5V/P9V/M9V are jittering and BIAS_PARAMETERS display - If BIASTEMP show ambient temperature, the DRCU is ON.Go to step 6. - If DRCU is not ON, refer to RD03 on how to start up the DRCU. | ALL SCU VOLTAGES LOOKING GOOD. SCUP5V = 5.22V SCUP9V =9.09V SCUM9V = -9.10V ALL BIAS VOLTAGES LOOKING GOOD. BIASP5V = 5.10V BIASP9V = 9.00V BIASM9V= -9.06V | ( |
| 6 | In SCOS open DPU_AND_OBS_PARAMETERS display and check that the MODE housekeeping parameter is DRCU_ON. | MODE (RAW)= 0x100 MODE (ENG) = DRCU_ON | ( |

Table 1. Initial configuration check

# Test procedure

The following two sections describe general pass/fail criteria (Section 3.1), the general test procedure layout (Section 3.1) and the detailed procedure for each functional test (Section 3.2).

## General Pass/Fail Criteria

The general criterion for declaring a single test failed is the repeated failure of 2 consecutive runs of this test. In that case the functional test procedure should be aborted and the overall functional testing declared FAILED.

In the case of a ‘first run’ failure followed by a successful execution a third run of the same test should be performed and in the unlikely event of this third run being a failure the test procedure should be also aborted and the overall functional testing declared FAILED, as this would imply a not reliable operability of the instrument.

As a general remark ANY failure should be closely analyzed.

Note:  If the functional test is declared FAILED refer to section 4.1 for instrument switch OFF.

## General Test Sequence

The table below shows the general WFT as it was performed.

| Step | Subsystem tested | Test Id | Test Purpose |
| --- | --- | --- | --- |
| 1 | SCU | FUNC-SCU-01 | SCU Nominal Science Generation Check |
| 2 |  | FUNC-SCU-03 | FPU DC Thermometry Check |
| 3 |  | FUNC-SCU-06 | FPU AC Thermometry Check |
| 4 |  | FUNC-SCU-02 | SCU Nominal Science Contents Check |
| 5 |  | FUNC-SCU-08 | SCU Test Pattern Check |
| 6 |  | FUNC-SCU-07 | Sorption Cooler Check |
| 7 |  | FUNC-SCU-04 | Photometer Calibrator Check |
| 8 |  | FUNC-SCU-05 | Spectrometer Calibrators Check |
| 9 | MCU | FUNC-MCU-01 | MCU Boot Check |
| 10 |  | FUNC-MCU-02 | MCU Nominal Science Generation Check |
| 11 |  | FUNC-MCU-03 | MCU Nominal Science Contents Check |
| 12 |  | FUNC-MCU-04 | MCU Test Pattern Check |
| 13 | BSMm | FUNC-BSM-01 | BSM Switch ON Check |
| 14 |  | FUNC-BSM-02c | BSM Chop Sensor Polarity Check |
| 15 |  | FUNC-BSM-02j | BSM Jiggle Sensor Polarity Check |
| 16 |  | FUNC-BSM-03 | BSM Open Loop dynamics Check |
| 17 |  | BSM_INIT | Close loop on chop/jiggle axis. |
| 18 |  | FUNC-BSM-06 | BSM Operational Mode Check |
| 19 | DCU | FUNC-DCU-01 | DCU Nominal Science Generation Check |
| 20 |  | FUNC-DCU-02 | DCU Nominal Science Contents Check |
| 21 |  | FUNC-DCU-03 | DCU Test Pattern Check |
| 22 | Photometer LIAs | FUNC-DCU-04P | Photometer LIAs Check |
| 23 |  | FUNC-DCU-05P | Photometer Manual Offset Setting Check |
| 24 |  | FUNC-DCU-11P | Photometer Detectors Switch ON Check |
| 25 | Photometer BDAs | FUNC-DCU-013P | Photometer Detectors Check |
| 26 | Spectrometer LIAs | FUNC-DCU-04S | Spectrometer LIAs Check |
| 27 |  | FUNC-DCU-05S | Spectrometer Manual Offset Setting Check |
| 28 |  | FUNC-DCU-11S | Spectrometer Detectors Switch ON Check |
| 29 | Spectrometer BDAs | FUNC-DCU-013S | Spectrometer Detectors Check |
| 18 | SMECm | FUNC-SMEC-02A | SMEC Launch Latch Open/Close Check |
| 19 |  | FUNC-SMEC-01 | SMECm Switch ON Check |
| 20 |  | FUNC-SMEC-03 | SMEC LED Optical Encoder LED Check |
| 21 |  | FUNC-SMEC-04 | SMEC Positioning Test (Open Loop) |

Table 2. General WFT sequence

# Detailed Test Results on REDUNDANT instrument.

The following is a detailed (test by test) procedure including the steps performed on each test and the results obtained.

| Step# | Action | Comments |
| --- | --- | --- |
| 0 | Open SCU_PARAMETERS display on SCOS Alpha Numeric Displays. |  |

## FUNC-SCU-01

| Test Id: | FUNC-SCU-01 |
| --- | --- |
| Initial Configuration: | DRCU_ON |
| Final Configuration: | DRCU_ON |
| Success Criteria: | Test passed if : Two SCU Nominal Science Report telemetry packets are received on QLA with the following characteristics: APID Type Subtype SID FrameID Frame length 0x509 21 1 0xA20 0x20 0x1E The frame time difference between consecutive SCU frames within these packets corresponds to the sampling rate. Nominal SCU sampling rate is 80Hz ( Δt = 12.5 ms The SPIRE HK parameter SCUFRAMECNT increments by 31. No events are generated during the frame generation. QLA to give go ahead. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Write the initial value of SCUFRAMECNT parameter located in SCU_PARAMETERS display and the initial value of TM1N located in DPU_AND-OBS_PARAMETERS display. | SCUFRAMCNT = 0 |
| 2 | Run QLA script FUNC-SCU-01.py on QLA console. |  |
| 3 | Run FUNC-SCU-01 test procedure from the HCSS Test Procedure window on TOPE |  |
| 4 | Write the final value of SCUFRAMECNT and TM1N. | SCUFRAMCNT = 31 |
| 5 | Contingency: If test fails repeat steps 1 to 4. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SCU-01 | SCUFRAMECNT TM5N | n/ n+ 31 0x3FFF/1 | 0/ 31 0x3FFF/1 | 31 | Success |
| Start time @: 12:29 End time @: 12: 29 OBSID: 0x30011A8D Comments: QLA script was run in playback: ************************************************************************* SCU: OBSID = 30011A8D, BBTYPE = 0x8000, APID = 0x509, SID = 0xa20 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. SCUFRAMECNT 0 31 31 31 Packet type = 0x15 TM5N 16383 1 49153 2 subtype = 0x1 FrameTime 12.4960 12.4960 Frame ID = 0x20 Frame Len = 0x1E STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 12.49792 ms sigma = 0.00160 ms |

## FUNC-SCU-03

| Test Id: | FUNC-SCU-03 |
| --- | --- |
| Initial Configuration: | DRCU_ON |
| Final Configuration: | DRCU_ON + DC thermometry ON |
| Success Criteria: | Test passed if all FPU DC thermometry sensors show temperature values indicating a correct functioning of the sensor, not open/short-circuited. If ANY reading is anomalous check RAW sensor reading. Open Circuit Criterion: RAW reading in the range [0, -100] Short Circuit Criterion: RAW reading of -32768 Note: For some parameters the calibration curve above 75K has only 2 points, thus the linearly interpolated temperature reading given by SCOS is usually not correct at T > 75K. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Run FUNC-SCU-03 test procedure from the HCSS Test Procedure window on TOPE |  |
| 2 | When the test is finished Write the current value of SCUTEMPSTAT and the RAW/converted values of the 16 FPU temperatures located in SCU_PARAMETERS display. |  |
| 3 | Contingency: If test fails execute SCU_OFF procedure from HCSS Test Procedure window on TOPE and then repeat steps 1 and 2. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SCU-03 | SCUTEMPSTAT | 0/0xFFFF | 0/0xffff | N/A | Success |
| Start time @: 12:31 End time @: 12: 31 OBSID:0x30011A8E Comments: SCU-03 Thermometry Check OBSID = 0x30011a8e PUMPHTRTEMP 50.09 32768 PUMPHSTEMP 36.42 32768 EVAPHSTMP 39.25 32768 SHUNTTEMP 18.05 32768 EMCFILTMP 284.27 35977 SL0TEMP 19.89 32768 PL0TEMP 22.52 32768 OPTTEMP 141.72 32768 BAFTEMP 160.50 32768 BSMIFTEMP 110.81 32768 SCAL2TEMP 166.07 32768 SCAL4TEMP 141.47 32768 SCALTEMP 83.15 32768 SMECIFTEMP 133.33 32768 SMECTEMP 27.28 32768 BSMTEMP 13.13 32768 The actual SCOS display readings are -32768. Error on QLA script? |

## FUNC-SCU-06

| Test Id: | FUNC-SCU-06 |
| --- | --- |
| Initial Configuration: | DRCU_ON + DC thermometry ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON |
| Success Criteria: | Test passed if SUBKSTAT parameter went from 0 to 1. Open Circuit Criterion: RAW reading in the range 0 -100 Short Circuit Criterion: RAW reading of -32768 |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Run FUNC-SCU-06 test procedure from the HCSS Test Procedure window on TOPE. |  |
| 2 | When the test is finished Write the current value of SUBKSTAT located in SCU_PARAMETERS display. Also write down the RAW value of the SUBKTEMP parameter. |  |
| 3 | Contingency: If test fails : Send manual command: SEND_DRCU_COMMAND Parameter1 = 0xA0860000 Parameter2 = 0 Then repeat steps 1 and 2. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SCU-06 | SUBKSTAT | 0/1 | 0/1 | N/A | Success |
| Start time @: 12:43 End time @: 12:43 OBSID:0x30011A8F Comments: SUBKTEMP: Before: RAW = 32767 After : RAW = 32767 No change (as it happened) on PFM4 but the channel is actually working. |

## FUNC-SCU-02

| Test Id: | FUNC-SCU-02 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON |
| Success Criteria: | Test passed if : Parameters in the SCU Nominal science packets and the same parameters in the Nominal HK packet have similar RAW/converted values to within 10%. The SPIRE HK parameter SCUFRAMECNT located in SCU_PARAMETERS display increments by 31. No events are generated during the frame generation. QLA to give the go ahead. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Write the current value of SCUFRAMECNT located in SCU_PARAMETERS display. |  |
| 2 | Run QLA script FUNC-SCU-02.py on QLA console. |  |
| 3 | Run FUNC-SCU-02 test procedure from the HCSS Test Procedure window on TOPE |  |
| 4 | When the test is finished Write the current value of SCUFRAMCNT. |  |
| 5 | Contingency: If test fails repeat steps 1 to 4. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SCU-02 | SCUFRAMECNT TM5N | n+31/n+62 1/3 | 31/62 1/3 | 31 | Success |
| Start time @: 12:45 End time @: 12: 46 OBSID: 0x30011A90 Comments: QLA script was run in playback: FUNC-SCU-02 version: 1.4 Housekeeping @ Fri Jan 26 12:45:41 GMT 2007 SCU Science @ Fri Jan 26 12:45:35 GMT 2007 Name HSK value SCU value Equal (within 10%)? TCHTRV 18.0 20.0 False PCALCURR 9.0 10.0 False SCAL4CURR 10.0 11.0 True SCAL2CURR 10.0 10.0 True PCALV 13.0 13.0 True SCAL4V 11.0 10.0 True SCAL2V 10.0 10.0 True PUMPHTRTEMP 32768.0 32768.0 True PUMPHSTEMP 32768.0 32768.0 True EVAPHSTEMP 32768.0 32768.0 True SHUNTTEMP 32768.0 32768.0 True EMCFILTEMP 35978.0 35974.0 True SL0TEMP 32768.0 32768.0 True PL0TEMP 32768.0 32768.0 True OPTTEMP 32768.0 32768.0 True BAFTEMP 32768.0 32768.0 True BSMIFTEMP 32768.0 32768.0 True SCAL2TEMP 32768.0 32768.0 True SCAL4TEMP 32768.0 32768.0 True SCALTEMP 32768.0 32768.0 True SMECIFTEMP 32768.0 32768.0 True SMECTEMP 32768.0 32768.0 True BSMTEMP 32768.0 32768.0 True SUBKTEMP 32767.0 32767.0 True |

## FUNC-SCU-08

| Test Id: | FUNC-SCU-08 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON |
| Success Criteria: | Test passed if : Two SCU Diagnostic Science Report telemetry packets are received with the following characteristics: APID Type Subtype SID FrameID Frame length 0x509 21 3 0x1121 0x21 0x1E The SCU Test Pattern agrees with the reference test pattern. QLA to give go ahead. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Write the current values of SCUFRAMECNT located in SCU_PARAMETERS display. |  |
| 2 | Run QLA script FUNC-SCU-08.py on QLA console. |  |
| 3 | Run FUNC-SCU-08 test procedure from the HCSS Test Procedure window on TOPE |  |
| 4 | When the test is finished Write the current value of SCUFRAMCNT. |  |
| 5 | Contingency: If test fails repeat steps 1 to 4. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SCU-08 | SCUFRAMECNT and SCU test pattern frame parameters | n+62/n+93 | 62/93 93/124 | 31 31 | Success |
| Start time @: 12:47 End time @: 12:48 OBSID:0x30011A91 Comments: QLA produced the following file: SCU Test Pattern @ Fri Jan 26 12:47:15 GMT 2007 ..compared with data from SCU Test Pattern @ Thu Jan 25 13:59:59 GMT 2007, OBSID=0x30011A58 Name New Value[0] New Value[20] Comp Value[0] Comp Value[20] SCUTSTOBSID 8.05378705E8 0.0 8.05378648E8 <--BAD 0.0 --> OK SCUTSTBBID 2.315714561E9 0.0 2.315714561E9 --> OK 0.0 --> OK SCUTSTBLKLEN 30.0 30.0 30.0 --> OK 30.0 --> OK SCUTSTFRAMEID 33.0 33.0 33.0 --> OK 33.0 --> OK SCUTST001 43690.0 31181.0 43690.0 --> OK 31181.0 --> OK SCUTST002 21844.0 62363.0 21844.0 --> OK 62363.0 --> OK SCUTST003 43688.0 59190.0 43688.0 --> OK 59190.0 --> OK SCUTST004 21840.0 52844.0 21840.0 --> OK 52844.0 --> OK SCUTST005 43680.0 40153.0 43680.0 --> OK 40153.0 --> OK SCUTST006 21825.0 14771.0 21825.0 --> OK 14771.0 --> OK SCUTST007 43650.0 29543.0 43650.0 --> OK 29543.0 --> OK SCUTST008 21765.0 59086.0 21765.0 --> OK 59086.0 --> OK SCUTST009 43530.0 52637.0 43530.0 --> OK 52637.0 --> OK SCUTST010 21524.0 39739.0 21524.0 --> OK 39739.0 --> OK SCUTST011 43048.0 13943.0 43048.0 --> OK 13943.0 --> OK SCUTST012 20560.0 27887.0 20560.0 --> OK 27887.0 --> OK SCUTST013 41120.0 55774.0 41120.0 --> OK 55774.0 --> OK SCUTST014 16705.0 46012.0 16705.0 --> OK 46012.0 --> OK SCUTST015 33411.0 26489.0 33411.0 --> OK 26489.0 --> OK SCUTST016 1287.0 52978.0 1287.0 --> OK 52978.0 --> OK SCUTST017 2574.0 40420.0 2574.0 --> OK 40420.0 --> OK SCUTST018 5149.0 15304.0 5149.0 --> OK 15304.0 --> OK SCUTST019 10298.0 30608.0 10298.0 --> OK 30608.0 --> OK SCUTST020 20597.0 61216.0 20597.0 --> OK 61216.0 --> OK SCUTST021 41194.0 56896.0 41194.0 --> OK 56896.0 --> OK SCUTST022 16852.0 48257.0 16852.0 --> OK 48257.0 --> OK SCUTST023 33705.0 30978.0 33705.0 --> OK 30978.0 --> OK SCUTST024 1874.0 61956.0 1874.0 --> OK 61956.0 --> OK SCUTSTADCFLGS 0.0 0.0 0.0 --> OK 0.0 --> OK SCUTSTFRAMETIME 4228657.0 4306769.0 4228894.0 <--BAD 4307006.0 <--BAD SCUTSTCHECKWORD 58804.0 15468.0 58523.0 <--BAD 13059.0 <--BAD |

## FUNC-SCU-04

| Test Id: | FUNC-SCU-04 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON |
| Success Criteria: | Test passed if PCALCURR/PCALV SCU HK parameters show the following values: PCALCURR HK parameter which shows the measured PCAL current is ~ 0.1 mA. PCALV HK parameter which shows the measured PCAL voltage is ~ 0.02V |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Write the current value of PCALV and PCALCURR located in SCU_PARAMETERS display. |  |
| 2 | Run FUNC-SCU-04 test procedure from the HCSS Test Procedure window on TOPE |  |
| 3 | While the test is running Write the values of PCALV and PCALCURR. |  |
| 4 | Contingency: If test fails repeat steps 1 to 3. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/During test | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SCU-04 | PCALCURR PCALV | 0/0.1mA 0/0.02V | 0 / 0.101 mA 0 / 0.0200 V | N/A | Success |
| Start time @: 12:48 End time @: 12: 48 OBSID: 0x30011A92 Comments: Test Successful |

## FUNC-SCU-05

| Test Id: | FUNC-SCU-05 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON |
| Success Criteria: | Test passed if : SCAL2CURR ,SCAL4CURR HK parameters which show the measured current read ~ 0.1 mA SCAL2V,SCAL4V parameters which show the measured voltage read ~ 0.05V. |

Test Procedure

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Write the current value of SCAL2V ,SCAL2CURR,SCAL4V,SCAL4CURR located in SCU_PARAMETERS display. |  |
| 2 | Run FUNC-SCU-05 test procedure from the HCSS Test Procedure window on TOPE |  |
| 3 | While the test is running write the values of SCAL2V ,SCAL2CURR,SCAL4V,SCAL4CURR. |  |
| 4 | Contingency: If test fails repeat steps 1 to 3. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/During test | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SCU-05 | SCAL4CURR SCAL4V SCAL2CURR SCAL2V | 0/0.1mA 0/0.05V 0/0.1mA 0/0.05V | 0 / 0.1017 mA 0 / 0.0508 V 0 / 0.1000 mA 0 / 0.0498 V | N/A | Success |
| Start time @: 12:49 End time @: 12: 52 OBSID:0x30011A93 Comments: The same command (parameter 0x4e) should be sent to both SCAL2/4 Test Successful |

## FUNC-SCU-07

| Test Id: | FUNC-SCU-07 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON |
| Success Criteria: | Test passed if during the execution of the test the following SCU HK parameters give correspondent readings of: SCU HK parameter RAW Converted SPHSV ~12715 ~323mV EVHSV ~12715 ~323mV SPHTRV ~14390 ~ 8 V |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Run FUNC-SCU-07 test procedure from the HCSS Test Procedure window on TOPE. | Pending |
| 2 | While the test is running Write the values of current values of SPHSV, EVHSV, SPHTRV located in SCU_PARAMETERS display. (RAW and CONVERTED) |  |
| 3 | Contingency: If test fails repeat steps 1 and 2. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/During test | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SCU-07 | SPHSV EVHSV SPHTRV | 0/ ~ 323 mV 0/ ~ 323 mV 0/ ~ 8 V | ~ 0 mV / 324.21 mV ~ 0 mV / 325.27 mV ~ 0 V / 8.85 V | N/A | Success |
| Start time @: 12:53 End time @: 12:56 OBSID:0x30011A94 Comments: Test Successful |

| Step# | Action | Comments |
| --- | --- | --- |
| 0 | Open MCU_PARAMETERS display on SCOS Alpha Numeric Displays. |  |

## FUNC-MCU-01

| Test Id: | FUNC-MCU-01 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON |
| Success Criteria: | Test passed if: MCU boots. MCU voltages show expected values. MAC, SMEC and BSM board temperatures shows ambient temperature. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Run FUNC-MCU-01 test procedure from the HCSS Test Procedure window on TOPE |  |
| 2 | When procedure is finished Write the values of the MCU voltages. |  |
| 3 | Contingency: If test fails repeat steps 1 and 2. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-MCU-01 | MCUP5V MCUP15V MCUP14V MCUM14V MCUM15V MCUMACTEMP MCUSMECTEMP MCUBSMTEMP | N/A/ ~ 5V N/A / ~15V N/A / ~ 14V N/A / ~ -14V N/A / ~ -15V N/A / ~ 300K N/A / ~ 300K N/A / ~ 300K | - / 5.00V - / 15.50V - / 14.12V - / -14.49 V - / -15.60 V - / 291.32K - / 295.60K - / 295.00K | N/A | Success |
| Start time @: 12:56 End time @: 14:35 OBSID:0x30011A95 Comments: SCUDCDCSTAT went from 0 to 4 as expected DRCU Power Supply LCD reading = ( I = 0.87 A ) Test Successful |

## FUNC-MCU-02

| Test Id: | FUNC-MCU-02 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON |
| Success Criteria: | Test passed if : MCU produces each type of the frames requested and with the following characteristics. Frame APID Type Subtype SID FrameID Frame length Eng. 0x509 21 3 0x814 0x14 0x15 BSM 0x509 21 1 0x612 0x12 0xD SMEC 0x509 21 1 0x410 0x10 0xC BSM +SMEC No events are generated during the different frames generation. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Write the current value of MCUFRAMECNT located in MCU_PARAMETERS display |  |
| 2 | Run QLA script FUNC-MCU-02.py on QLA console. |  |
| 3 | Run FUNC-MCU-02 test procedure from the HCSS Test Procedure window on TOPE |  |
| 4 | When test is finished Write the current value of MCUFRAMECNT. |  |
| 5 | Contingency: If test fails repeat steps 1 to 4. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-MCU-02 | MCUFRAMECNT | 0/ ~ 6600 | 0 / 6493 |  | Success |
| Start time @: 12:58 End time @: 13:01 OBSID:0x30011A96 Comments: QLA produced the following file: ************************************************************************* MCUENG: OBSID = 30011A96, BBTYPE = 0x8901, APID = 0x509, SID = 0x814 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. MCUFRAMECNT 0 609 609 609 Packet type = 0x15 TM5N 5 32 27 27 subtype = 0x3 FrameTime 16.4223 16.4225 Frame ID = 0x14 Frame Len = 0x15 STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 16.42260 ms sigma = 0.00115 ms ************************************************************************* BSM: OBSID = 30011A96, BBTYPE = 0x8903, APID = 0x509, SID = 0x612 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. MCUFRAMECNT 609 1250 641 609 Packet type = 0x15 TM5N 32 49 17 17 subtype = 0x1 FrameTime 15.5809 15.5809 Frame ID = 0x12 Frame Len = 0xD STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 15.58042 ms sigma = 0.00104 ms ************************************************************************* SMEC: OBSID = 30011A96, BBTYPE = 0x8902, APID = 0x509, SID = 0x410 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. MCUFRAMECNT 1250 3624 2374 2375 Packet type = 0x15 TM5N 49 107 58 58 subtype = 0x1 FrameTime 4.2112 4.2114 Frame ID = 0x10 Frame Len = 0xC STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 4.21092 ms sigma = 0.00090 ms ************************************************************************* SMEC+BSM: OBSID = 30011A96, BBTYPE = 0x8904, APID = 0x509, SID = 0x612 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. MCUFRAMECNT 3624 6493 2869 2850 Packet type = 0x15 TM5N 107 178 71 71 subtype = 0x1 FrameTime SMEC 4.2112 4.2112 Frame ID = 0x10, Len = 0xC FrameTime BSM 20.2143 20.2143 Frame ID = 0x12, Len = 0xD STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 4.21093 ms (SMEC), 20.21245 ms (BSM) sigma = 0.00090 ms (SMEC), 0.00157 ms (BSM) |

## FUNC-MCU-03

| Test Id: | FUNC-MCU-03 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON |
| Success Criteria: | Test passed if : MCU produces 99 frames of each type of frames requested with the following characteristics: Frame APID Type Subtype SID FrameID Frame length Eng. 0x508 21 3 0x814 0x14 0x15 BSM 0x508 21 1 0x612 0x12 0xD SMEC 0x508 21 1 0x410 0x10 0xC BSM +SMEC No events are generated during the different frames generation. QLA analysis results are correct. QLA to give go ahead. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Write the current value of MCUFRAMECNT located MCU_PARAMETERS display. |  |
| 2 | Run QLA script FUNC-MCU-03.py on QLA console. |  |
| 3 | Run FUNC-MCU-03 test procedure from the HCSS Test Procedure window on TOPE |  |
| 4 | When test is finished Write the current value of MCUFRAMECNT |  |
| 5 | Contingency: If test fails repeat steps 1 to 4. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-MCU-03 | MCUFRAMECNT | n/ n+297 n~6600 | 6493 / 6790 |  | Success |
| Start time @: 13:01 End time @: 13:03 OBSID:0x30011A97 |

## FUNC-MCU-04

| Test Id: | FUNC-MCU-04 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON |
| Success Criteria: | Test passed if: MCU produces 100 frames of Test Pattern with the following characteristics: Frame APID Type Subtype SID FrameID Frame length Test 0x509 21 3 0x915 0x15 0x15 MCU Test pattern produced is the same as the previous time this test was run. QLA to give go ahead. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Write the current value of MCUFRAMECNT located in MCU_PARAMETERS display. |  |
| 2 | Run QLA script FUNC-MCU-04.py on QLA console. |  |
| 3 | On Lincoln run FUNC-MCU-04 test procedure from the HCSS Test Procedure window on TOPE |  |
| 4 | When test is finished Write the current value of MCUFRAMECNT |  |
| 5 | Contingency: If test fails repeat steps 1 to 4. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-MCU-04 | MCUFRAMECNT | m/ m+99 m~6600 | 6790/ 6889 |  | Success |
| Start time @: 13:03 End time @: 13:04 OBSID: 0x30011A98 Comments: QLA produced the following file: MCU Test Pattern @ Fri Jan 26 13:03:37 GMT 2007 ..compared with data from MCU Test Pattern @ Thu Jan 25 14:47:41 GMT 2007, OBSID=0x30011A5F Name New Value[0] New Value[20] Comp Value[0] Comp Value[20] MCUTSTBBID 2.298806273E9 0.0 2.298806273E9 --> OK 0.0 --> OK MCUTSTBLKLEN 21.0 21.0 21.0 --> OK 21.0 --> OK MCUTSTFRAMEID 21.0 21.0 21.0 --> OK 21.0 --> OK MCUTST001 21845.0 21845.0 21845.0 --> OK 21845.0 --> OK MCUTST002 43690.0 43690.0 43690.0 --> OK 43690.0 --> OK MCUTST003 21844.0 21844.0 21844.0 --> OK 21844.0 --> OK MCUTST004 43688.0 43688.0 43688.0 --> OK 43688.0 --> OK MCUTST005 21840.0 21840.0 21840.0 --> OK 21840.0 --> OK MCUTST006 43680.0 43680.0 43680.0 --> OK 43680.0 --> OK MCUTST007 21825.0 21825.0 21825.0 --> OK 21825.0 --> OK MCUTST008 43650.0 43650.0 43650.0 --> OK 43650.0 --> OK MCUTST009 21765.0 21765.0 21765.0 --> OK 21765.0 --> OK MCUTST010 43530.0 43530.0 43530.0 --> OK 43530.0 --> OK MCUTST011 21524.0 21524.0 21524.0 --> OK 21524.0 --> OK MCUTST012 43048.0 43048.0 43048.0 --> OK 43048.0 --> OK MCUTST013 20560.0 20560.0 20560.0 --> OK 20560.0 --> OK MCUTST014 41120.0 41120.0 41120.0 --> OK 41120.0 --> OK |

| Step# | Action | Comments |
| --- | --- | --- |
| 0 | Open CHOP PARAMETERS display on SCOS Alpha Numeric Displays. |  |

## FUNC-BSM-01

| Test Id: | FUNC-BSM-01 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON + BSM ON (open loop) |
| Success Criteria: | Test passed if: CHOPSENSPWR HK parameter goes from 0 to 1 CHOPDACVAL HK parameter goes from 0 to 0x8000 CHOPSENSIG HK parameter shows variation from off to on JIGGSENSPWR HK parameter goes from 0 to 1 JIGGDACVAL parameter goes from 0 to 0x8000 JIGGSENSSIG HK parameter shows variation from off to on |

Test Procedure

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | On QLA bring up a time series display of the following HK parameters: CHOPSENSPWR CHOPDACVAL CHOPSENSIG JIGGSENSPWR JIGGDACVAL JIGGSENSSIG |  |
| 2 | Run FUNC-BSM-01 test procedure from the HCSS Test Procedure window on TOPE |  |
| 3 | When the test is finished record all the Key parameters noted bellow |  |
|  | Contingency: If test fails repeat steps 1 and 2. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-BSM-01 | CHOPSENSPWR CHOPLOOPMODE CHOPDACVAL CHOPFFGAIN CHOPSENSSIG JIGGSENSPWR JIGGLOOPMODE JIGGDACVAL JIGGFFGAIN JIGGSENSSIG | 0/1 3/3 0x8000/0x8000 0xBEB/0xBEB ~0x8000/? 0/1 3/3 0x8000/0x8000 0xBEB/0xBEB ~0x8000/? | 0/1 3/3 0x8000/0x8000 0xBEB/0x770 0x7FFD/0x94B2 0/1 3/3 0x8000/0x8000 0xBEB/0xF6E 0x7FF2/ ~ 0x8CB6 | N/A | Success |
| Start time @: 14:39 End time @: 14:40 OBSID: 0x30011A99 Comments: The BSM was switched ON correctly. The highlighted Chop and Jiggle FF gains are consistent with the latest BSMNominalSettings.txt table in the CUS. |

## FUNC-BSM-02c

| Test Id: | FUNC-BSM-02c |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON + BSM ON (open loop) |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON + BSM ON (open loop) |
| Success Criteria: | Test passed if the chop sensor signal evolves in the same way as the positions set.(i.e if (pos1 > pos2 ( sig1 > sig2) |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | On QLA open up a time series display of HK parameter CHOPDACVAL and CHOPSENSSIG |  |
| 2 | Run FUNC-BSM-02c test procedure from the HCSS Test Procedure window on TOPE |  |
| 3 | Contingency: If test fails repeat steps 1. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-BSM-02c | CHOPDACVAL CHOPSENSSIG |  | See below | N/A | Success |
| Start time @: 14:42 End time @: 14:43 OBSID: 0x30011A9A Comments: The BSM moved along the chop axis in the same direction as expected. Insert QLA picture |

## FUNC-BSM-02j

| Test Id: | FUNC-BSM-02j |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON + BSM ON (open loop) |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON + BSM ON (open loop) |
| Success Criteria: | Test passed if the jiggle sensor signal evolves in the same way as the positions set.(i.e if (pos1 > pos2 ( sig1 > sig2) |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | On QLA open up a time series display of HK parameter JIGGDACVAL and JIGGSENSSIG |  |
| 2 | Run FUNC-BSM-02j test procedure from the HCSS Test Procedure window on TOPE |  |
| 3 | Contingency: If test fails repeat steps 1. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-BSM-02j | JIGGDACVAL JIGGSENSSIG |  | See below | N/A | Success |
| Start time @: 14:44 End time @: 14:46 OBSID: 0x30011A9B Comments: The BSM moved along the jiggle axis in the same direction as expected. Insert QLA picture |

## FUNC-BSM-03

| Test Id: | FUNC-BSM-03 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON + BSM ON (open loop) |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON + BSM ON (open loop) |
| Success Criteria: | Test passed if the chop sensor signal evolves in the same way as the positions set.(i.e if (pos1 > pos2 ( sig1 > sig2) for each jiggle position. Note: During warm tests the voltages on both chop and jiggle motors are likely to be saturated (CHOP/JIGGMOTORVOLT RAW values of ~ 0xFFFF) due to the high resistance of the motor coil at ambient temperature. |

Test Procedure

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | On QLA open up a time series display of HK parameters: CHOPPOSN CHOPDACVAL CHOPMOTORCURR CHOPSENSSIG CHOPMOTORVOLT JIGGPOSN JIGGDACVAL JIGGMOTORCURR JIGGSENSSIG JIGGMOTORVOLT |  |
| 2 | Run FUNC-BSM-03 test procedure from the HCSS Test Procedure window on TOPE |  |
| 3 | Contingency: If test fails repeat step 2. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-BSM-03 |  |  |  | N/A | Success |

Start time @: 14:48 End time @: 14: 52 OBSID:0x30011A9C Comments: Ran TOPE script with input parameters: Jiggle Start = 0x4000 Jiggle End = 0xC000 Jiggle Step = 0x4000 Chop Start = 0x3000 Chop End = 0xF000 Chop Step = 0x1000 3 seconds per step Insert QLA picture Jiggle position as given by senssig shows going to position then coming back as the chop position is stepped. This is due to the coupling between the axis. Insert QLA picture

## FUNC-BSM-06

| Step# | Action | Comments |
| --- | --- | --- |
| 0 | Execute BSM_INIT from HCSS Test Procedures | Started at 16:52 OBSID: 0x30011A9D |

| Test Id: | FUNC-BSM-06 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON + BSM ON (open loop) |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON + BSM ON (open loop) |
| Success Criteria: | Note: The purpose of this test is to check the correctness of the BSM close loop initialisation procedure and the default PID parameters If the dynamical behaviour of the BSM during chopping with these PID parameters is close or within requirements this indicates that the PID parameters used can be applied to cold testing with certain adjustment. If NOT these indicates that the PID parameters need further tuning BUT NOT TO BE DONE DURING THESE TEST. In any case the success/fail criteria are NOT applicable for this test. |

Test Procedure

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | On QLA open up a time series display of HK parameters: BSMCHOPSENSSIG BSMCHOPMOTORCURR BSMCHOPMOTORVOLT BSMJIGGSENSSIG BSMJIGGMOTORCURR BSMJIGGMOTORVOLT |  |
| 2 | Run FUNC-BSM-06 test procedure from the HCSS Test Procedure window on TOPE |  |
| 3 | Contingency: None contemplated. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-BSM-06 | CHOPSENSSIG CHOPMOTORCURR CHOPDACVAL | ?/? ?/? ?/? |  | N/A | N/A |
| Start time @: 14:56 End time @: 15:02 OBSID:0x30011AA0 Comments: Ran TOPE script with default values that the input parameters have: Input Parameter Value Frame rate 125 Hz On source chop 0x5279 On source jiggle 0x8D00 Off source chop 0xAD87 Off source chop 0x8D00 Number of cycles 50 Chop cycle period 500000 (us) DCU frame type 0 Number of DCU frame per half cycle 4 DCU delay to start sampling 34959 (us) Number of BSM samples 65535 = continuous sampling Had to run LoadCommandList procedure from TOPE as apparently the BSM CHOP command list had not been uploaded correctly due to the initial CDMS Sim Bus problem. Repeated the functional test then the BSM chopped. Second Attempt behaviour: Note: Although both sensor signals show clear signs of not correct PID settings and the jiggle motor current is very irregular the purpose of this test is to prove that we can operate the BSM in its nominal operational mode PID chopping. |

| Step# | Action | Comments |
| --- | --- | --- |
| 4 | Execute BSM_OFF from HCSS Test Procedures | Switched OFF the BSM @ 15:08 Obsid: 0x30011AA1 |

Manually set the MODE HK parameter to REDY: SET_OBS_MODE(0x200)

## FUNC-SMEC-03

| Test Id: | FUNC-SMEC-03 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON+ SMEC ON (open loop) |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON+ SMEC ON (open loop) |
| Success Criteria: | Test passed if: SMEC encoder signals 1 and 2 show a variation on their amplitudes from one LED illumination level to another. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | On QLA bring up a time series display of the following Nominal HK parameters: SMECENCSIGAMP1 SMECENCSIGAMP2 |  |
| 2 | Run FUNC-SMEC-03 test procedure from the HCSS Test Procedure window on TOPE |  |
| 3 | Contingency: If test fails repeat steps 1 and 2. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-03 | SMECENCSIG1 SMECENCSIG2 |  |  |  | Success |
| Start time @: 15:12 End time @: 15:13 OBSID: 0x30011AA2 Comments: Using input parameters: Start level = 3 End level = 6 Step level = 1 5 seconds at each Also plotted SMECENCPWR. The level of the encoder signals 1 and 2 changed as the level of the power changed staying in range throughout the sequence. Note: Procedure should be change to plot the QLA MCU ENG frames rather than the HK values which have a much lower resolution. |

## FUNC-SMEC-01

| Test Id: | FUNC-SMEC-01 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON+ SMEC ON (open loop) |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON+ SMEC ON (open loop) |
| Success Criteria: | Test passed if : SMECENCPWR HK parameter changes from 0 to 6. SMEC encoder signals 1 and 2 amplitude show variation when encoder is switched ON. SMEC LVDT is switched ON. SMEC LVDT DC and AC signals show variation when LVDT is switched ON. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 0 | Open SMEC PARAMETERS display on SCOS Alpha Numeric Displays. |  |
| 1 | On QLA bring up a display of the following HK parameters: SMECENCPWR SMECENCSIG1AMP SMECENCSIG2AMP SMECLVDTDCSIG SMECLVDTACSIG |  |
| 2 | Run FUNC-SMEC-01 test procedure from the HCSS Test Procedure window on TOPE |  |
|  | Contingency: If test fails repeat steps 1. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/ After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-01 | SMECENCPWR SMECLVDTPWR SMECENCSIG1 SMECENCSIG1AMP SMECENCSIG1OFF SMECENCSIG2 SMECENCSIG2AMP SMECENCSIG2OFF |  | 0/6 0/1 not relevant/ ~ 0x3C00 0xCE20/0xDEA8 not relevant/~0x5400 0xCE20/0xAFC8 | N/A |  |
| Start time @: 15:17 End time @: 15:18 OBSID: 0x30011AA2 Comments: Procedure still asks from encoder signal amplitudes when it should only ask for encoder signals |

## FUNC-SMEC-04a

| Test Id: | FUNC-SMEC-04a |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ SMEC ON (open loop) UNLATCHED |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ SMEC ON (open loop) UNLATCHED |
| Success Criteria: | Test passed if only the SMECMOTORCURR shows a variation meaning that the mechanism has not moved. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | On QLA bring up a time series display of the following Nominal HK parameters: SMECENCSIG1 SMECENCSIG2 SMECLVDTDCSIG SMECLVDTACSIG SMECMOTORCURR |  |
| 2 | Run FUNC-SMEC-04a test procedure from the HCSS Test Procedure window on TOPE |  |
| 3 | Contingency: If test fails repeat steps 1. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-04a | SMECLVDTDCSIG |  | 13A4/ |  |  |
| Start time @: 15:30 End time @: 15:33 OBSID:0x30011AA3 Comments: Used the following input parameters to the TOPE script: Scan Start = 1000 um Scan End = 15000 um Scan Step = 1000 um Scan F speed = 500 um/s Scan R speed = 1000 um/s Time at each position = 5 s The test procedure specifies HK parameters should be displayed when the SMEC science parameters are needed. |

## FUNC-SMEC-02A/B

| Test Id: | FUNC-SMEC-02A/B |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON + SMEC ON If WFT prior to cooldown : Smec Latched If WFT after warm up : Smec Unlatched |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON + SMEC ON If WFT prior to cooldown : Smec Unlatched If WFT after warm up : Smec Latched |
| Success Criteria: | Test passed if : Prior to un-latching the resistance across pins 7 and 8 of the launch latch is ~ 368 Ohms. After un-latching the resistance is 483 Ohms. Note: These resistance values were recorded for the CQM SMEC model, for the flight SMEC, these values are expected to vary. |

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Measure the resistance across pins 7 and 8 of the launch latch. | This step is not applicable anymore |
| 2 | If WFT prior to cooldown: Run FUNC-SMEC-02A test procedure from the HCSS Test Procedure window on TOPE If WFT after warm up: Run FUNC-SMEC-02B test procedure from the HCSS Test Procedure window on TOPE |  |
| 3 | Measure the resistance across pins 7 and 8 of the launch latch. |  |
| 4 | Contingency: If test fails repeat steps 1. |  |

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-02A/B |  |  |  | N/A | Passed |
| Start time: End time : OBSID: Test not performed as the SMEC is already unlatched and will be left unlatched for the cooldown. |

## FUNC-SMEC-09

| Test Id: | FUNC-SMEC-09 |
| --- | --- |
| Test Purpose: | SMEC Open Loop Scan Test. |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ SMEC ON (open loop) |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ SMEC ON (open loop) |
| Success Criteria: | Test passed if SMECLVDTDCSIG parameter shows a variation according to the different position of the SMEC along the scan. |

Test Procedure:

| Step# | Action |
| --- | --- |
| 1 | On QLA bring up a time series display of the following SMEC nominal science parameters: SMECENCSIG1 SMECENCSIG2 SMECLVDTDCSIG SMECLVDTACSIG SMECMOTORCURR |
| 2 | Run FUNC-SMEC-09 test procedure from the HCSS Test Procedure window on TOPE |
| 3 | Contingency: If test fails repeat steps 1. |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | No. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-09 | All above mentioned in step 2 | N/A | N/A | N/A | Success |
| Start time @: 16:08 End time @: 16;20 OBSID: 0x30011AA5 Comments: ALL SMEC FUNCTIONAL TESTS PRODUCE ENGINEERING FRAMES NOT SMEC SCIENCE AND THIS SHOULD BE NOTED IN THE PROCEDURES Manually set the encoder signal 1/2 offsets to : SMECEMCSIGOFF1 = 14500 (0x38A4) SMECEMCSIGOFF2 = 22500 (0x57E4) as the SMEC_ON script still does not incorporate a PRIME/REDUNDANT switch Start point = 1 mm, End point = 38 mm Forward speed = 0.5 mm/s Reverse speed = 0.5 mm/s Number of scan = 4 Encoder not counting Reset manually SMECEMCSIGOFF1 = 15000 SMECEMCSIGOFF2 = 23000 Repeated SCAN: OBSID: 0x30011AA6 Start point = 1 mm, End point = 15 mm Forward speed = 0.2 mm/s Reverse speed = 0.2 mm/s Number of scan = 2 Encoder now counting See next test for a comparison with the open to close loop performance |

| Step# | Action | Comments |
| --- | --- | --- |
| 0 | Execute SMEC_INIT from HCSS Test Procedures | Obsid: 0x30011AA7 |

## FUNC-SMEC-07

| Test Id: | FUNC-SMEC-07 |
| --- | --- |
| Test Purpose: | SMEC Close Loop Scan Test. |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ SMEC ON (close loop) |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ SMEC ON (close loop) |
| Success Criteria: | Test passed if: SMECENCPOS HK parameter shows identical values as those of the SMECTRAJPOSN HK parameter during the scan. |

Test Procedure:

| Step# | Action |
| --- | --- |
| 1 | On QLA bring up a time series display of the following SMEC nominal science parameters: SMECENCSIG1 SMECENCSIG2 SMECLVDTDCSIG SMECLVDTACSIG SMECMOTORCURR |
| 2 | Run FUNC-SMEC-07 test procedure from the HCSS Test Procedure window on TOPE |
| 3 | Contingency: If test fails repeat steps 1. |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | No. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-07 | All above mentioned in step 1 | N/A | N/A | N/A | Success |
| Start time @: 16:26 End time @: 16:30 OBSID: 0x30011AA8 Comments: Start point = 1 mm, End point = 15 mm Forward speed = 0.2 mm/s Reverse speed = 0.2 mm/s Number of scan = 2 The loop remained closed through out the scan but note the much larger scatter on the SMEC motor current during the close loop scan which most probably indicates a wrong set of PID parameters for redundant SMEC warm operation. Nevertheless this test proves that the redundant SMEC CAN be operated in close loop. |

## FUNC-SMEC-04B

| Test Id: | FUNC-SMEC-04B |
| --- | --- |
| Test Purpose: | SMEC Close Loop Position Test. SMEC close loop operation check. |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ SMEC ON (open loop) |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ SMEC ON (open loop) |
| Success Criteria: | Test passed if : SMECENCPOS HK parameter shows identical values as those of the SMECTRAJPOSN HK parameter for the different commanded SMEC positions.( 1mm to 25mm in steps of 1mm) |

Test Procedure:

| Step# | Action |
| --- | --- |
| 1 | On QLA bring up 2 time series displays: Display 1 of the following MCU Engineering block parameters: MCUENGSMECENCSIG1 MCUENGSMECENCSIG2 MCUENGSMECLVDTDCSIG MCUENGSMECLVDTACSIG MCUENGSMECMOTORCURR Display 1 of the following SMEC HK parameters: SMECENCPOSN SMECTRAJPOSN |
| 2 | Run FUNC-SMEC-04B test procedure from the HCSS Test Procedure window on TOPE |
| 3 | Contingency: If test fails repeat steps 1. |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | No. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-04B | All above mentioned in step 1 | N/A | N/A | N/A | Not done |
| Start time @: 16:37 End time @: 16:41 OBSID: 0x30011AA9 Comments: Start point = 1 mm End point = 15 mm Steps = 1 mm Forward speed = 0.5 mm/s Reverse speed = 1.0 mm/s |

| Step# | Action | Comments |
| --- | --- | --- |
| 4 | Execute SMEC_OFF from HCSS Test Procedures | Done at 16:49; Obsid:0x30011AAA |

| Step# | Action | Comments |
| --- | --- | --- |
| 0 | Open DCU PARAMETERS SCOS Alpha Numeric Display |  |

## FUNC-DCU-01

| Test Id: | FUNC-DCU-01 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON |
| Success Criteria: | Test passed if: DCU produces each type of DCU nominal science frame with the following characteristics. APID Type S.type SID Frame ID Frame type Nb. Of frames Nb. of pkts. 0x505 21 1 0x200 0 PF 100 100 0x507 21 1 0x201 1 SF 100 17 0x505 21 2 0x102 2 PSW 100 34 0x505 21 2 0x103 3 PMW 100 25 0x505 21 2 0x104 4 PLW 100 12 0x507 21 2 0x105 5 SSW 100 12 0x507 21 2 0x106 6 SLW 100 7 The frame time difference between consecutive DCU frames of each type corresponds to the sampling rate. Photometer Sampling rate is 15.3Hz ( Δt ~ 65.5 ms Spectrometer Sampling rate is 80Hz ( Δt = 12.5 ms The SPIRE HK parameter DCUFRAMECNT increments by 700. No events are generated during the frames generation. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Write the current value of DCUFRAMECNT located d in DCU PARAMETERS AND |  |
| 2 | Run FUNC-DCU-01 test procedure from the HCSS Test Procedure window on TOPE |  |
| 3 | Write the current value of DCUFRAMECNT located d in DCU PARAMETERS AND |  |
| 4 | Contingency: If test fails repeat steps 1 to 3. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-DCU-01 | DCUFRAMECNT | n/n+700 n depends on the BSM chop operations on FUNC-BSM-06 | 0 / 700 | 700 |  |
| Start time @: 29/01/2007 - 14:19 End time @: 29/01/2007 - 14:22 OBSID: 0x30011AB9 Comments: Test run out of sequence Ran TOPE script with default values QLA created file QLA-DCU-01_30011AB9.txt: ************************************************************************* PHOTF: OBSID = 30011AB9, BBTYPE = 0x8800, APID = 0x505, SID = 0x200 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. DCUFRAMECNT 0 100 100 100 Packet type = 0x15 TM3N 16383 99 49251 100 subtype = 0x1 FrameTime 53.7568 53.7568 Frame ID = 0x0 Frame Len = 0x126 STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 53.75887 ms sigma = 0.00154 ms ************************************************************************* PHOTSW: OBSID = 30011AB9, BBTYPE = 0x8802, APID = 0x505, SID = 0x102 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. DCUFRAMECNT 100 200 100 100 Packet type = 0x15 TM3N 99 133 34 34 subtype = 0x2 FrameTime 53.7568 53.7600 Frame ID = 0x2 Frame Len = 0x96 STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 53.75890 ms sigma = 0.00154 ms ************************************************************************* PHOTMW: OBSID = 30011AB9, BBTYPE = 0x8803, APID = 0x505, SID = 0x103 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. DCUFRAMECNT 200 300 100 100 Packet type = 0x15 TM3N 133 158 25 25 subtype = 0x2 FrameTime 53.7600 53.7600 Frame ID = 0x3 Frame Len = 0x66 STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 53.75890 ms sigma = 0.00152 ms ************************************************************************* PHOTLW: OBSID = 30011AB9, BBTYPE = 0x8804, APID = 0x505, SID = 0x104 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. DCUFRAMECNT 300 400 100 100 Packet type = 0x15 TM3N 158 170 12 12 subtype = 0x2 FrameTime 53.7600 53.7600 Frame ID = 0x4 Frame Len = 0x36 STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 53.75890 ms sigma = 0.00152 ms ************************************************************************* SPECF: OBSID = 30011AB9, BBTYPE = 0x8801, APID = 0x507, SID = 0x201 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. DCUFRAMECNT 400 500 100 100 Packet type = 0x15 TM4N 16383 16 49168 17 subtype = 0x1 FrameTime 12.4928 12.4928 Frame ID = 0x1 Frame Len = 0x4E STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 12.49254 ms sigma = 0.00089 ms ************************************************************************* SPECSW: OBSID = 30011AB9, BBTYPE = 0x8805, APID = 0x507, SID = 0x105 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. DCUFRAMECNT 500 600 100 100 Packet type = 0x15 TM4N 16 28 12 12 subtype = 0x2 FrameTime 12.4928 12.4896 Frame ID = 0x5 Frame Len = 0x36 STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 12.49254 ms sigma = 0.00089 ms ************************************************************************* SPECLW: OBSID = 30011AB9, BBTYPE = 0x8806, APID = 0x507, SID = 0x106 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. DCUFRAMECNT 600 700 100 100 Packet type = 0x15 TM4N 28 35 7 7 subtype = 0x2 FrameTime 12.4928 12.4928 Frame ID = 0x6 Frame Len = 0x1E STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 12.49254 ms sigma = 0.00088 ms |

## FUNC-DCU-02

| Test Id: | FUNC-DCU-02 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON |
| Success Criteria: | Test passed if DCUFRAMECNT goes from 700 to 1400 and the frametime difference between consecutive frames computed by QLA script is in agreement with the expected differences based on commanded sampling rate: Photometer Sampling rate is 15.3Hz ( Δt ~ 65.5 ms Spectrometer Sampling rate is 80Hz ( Δt = 12.5 ms |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Write the current value of DCUFRAMECNT located d in DCU PARAMETERS AND |  |
| 2 | Run QLA script FUNC-DCU-02.py on QLA console. |  |
| 3 | Run FUNC-DCU-02 test procedure from the HCSS Test Procedure window on TOPE |  |
| 4 | Write the current value of DCUFRAMECNT located d in DCU PARAMETERS AND |  |
| 5 | Contingency: If test fails repeat steps 1 to 4. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-DCU-02 | DCUFRAMECNT | m/m+1400 | 700 / 1400 | 700 | Success |
| Start time @: 29/01/2007 - 14:26 End time @: 29/01/2007 - 14:29 OBSID: 0x30011ABA Comments: Test run out of sequence Contents of QLA created files show sampling times to be consistent with input parameters entered for sampling frequencies of photometer 18Hz (Δt ~ 53.3 ms) and spectrometer 80Hz Δt ~ 12.5 ms. |

## FUNC-DCU-03

| Test Id: | FUNC-DCU-03 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON |
| Success Criteria: | Test passed if : DCU produces 100 frames of Full Photometer Test Pattern and 100 frame of Full Spectrometer Test Pattern test. QLA analysis shows that phot/spec test patterns are the same as the reference phot/spec test patterns. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Write the current value of DCUFRAMECNT located d in DCU PARAMETERS AND |  |
| 2 | Run QLA script FUNC-DCU-03.py on QLA console. |  |
| 3 | Run FUNC-DCU-03 test procedure from the HCSS Test Procedure window on TOPE |  |
| 4 | Write the current value of DCUFRAMECNT located d in DCU PARAMETERS AND |  |
| 5 | Contingency: If test fails repeat steps 1 to 4. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-DCU-03 | DCUFRAMECNT | j/j+200 | 1400 / 1600 | 200 |  |
| Start time @: 29/01/2007 - 14:29 End time @: 29/01/2007 - 14:32 OBSID: 0x30011ABB Comments: Test run out of sequence Files produced by QLA: QLA-DCU-03_30011ABB_8807.txt QLA-DCU-03_30011ABB_8808.txt Test pattern files show agreement with reference DCU test pattern files from OBSID 0x30011A6A (25/01/2007). |

## FUNC-DCU-04P

| Test Id: | FUNC-DCU-04P |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON + Photometer LIAs ON |
| Success Criteria: | Test passed if : SCUDCDCSTAT parameter goes from 4 to 5. Photometer LIA card voltages are showing correct readings of +5V,+9V,-9V. Photometer LIA temperatures show an increase indicating that they are ON. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | On QLA bring up a time series display of the HK parameters: PLIAP5V PLIAP9V PLIAM9V LIAP1/2/3/4/5/6/7/8/9TEMP |  |
| 2 | Run FUNC-DCU-04P test procedure from the HCSS Test Procedure window on TOPE |  |
| 5 | Contingency: If test fails repeat steps 1 and 2. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-DCU-04-P | SCUDCDCSTAT PLIAP5V PLIAP9V PLIAM9V LIAP1TEMP to LIAP9TEMP | 4/5 0/~ +5V 0/~+11V 0/~-11V N/A/ [290-300]K | 4/5 0/+5.18V 0/+11.53V 0/-11.53V ~294/warming up |  | Success |
| Start time @: 16:53 End time @: 16:54 OBSID: 0x30011AAB Comments: |

## FUNC-DCU-11P

| Test Id: | FUNC-DCU-11P |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ Photometer LIAs ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ Photometer LIAs ON + Photometer BIAS ON +Photometer JFETs ON |
| Success Criteria: | Test passed if Photometer JFET source and drain voltages are correct: PSWJFETVSS1/2/3/4/5/6 (RAW: 0x4C CONVERTED ~ -1.5V). PMLWJFETVSS1/2/3/4 (RAW: 0x4C CONVERTED ~ -1.5V). PSWJFETSTAT = 0x3F PMLWJFETSTAT = 0x1F |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Run FUNC-DCU-11P test procedure from the HCSS Test Procedure window on TOPE |  |
| 2 | After the test Write the values RAW and converted values of: PSWJFETSTAT,PMLWJFETSTAT, PSWJFET1/2/3/4/5/6V PMWJFET1/2/3/4V PLWJFET1/2V located in DCU PARAMETERS AND |  |
| 3 | Contingency: If test fails repeat steps 1 and 2. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-DCU-11P | PSWJFETSTAT PMLWJFETSTAT PSWJFET1/2/3/4/5/6V PMWJFET1/2/3/4V PLWJFET1/2V | 0/0x3f 0/0x7f 0V/-1.5V 0V/-1.5V 0V/-1.5V | 0/0x03f 0/0x07f See comments | N/A | Success |
| Start time @: 17:05 End time @: 17: 06 OBSID: 0x30011AAC Comments: The Vss values for the JFETs were the same as for the PFM4 cold test campaign, i.e. PSWJFET1V: -1.68V PSWJFET2V: -1.59V PSWJFET3V: -1.37V PSWJFET4V: -1.59V PSWJFET5V: -1.78V PSWJFET6V: -1.59V PMWJFET1V: -1.68V PMWJFET2V: -1.59V PMWJFET3V: -1.59V PMWJFET4V: -1.88V PLWJFET1V: -1.59V PLWJFET2V: -1.37V PSW: G8 and C12 have a relatively higher output (~ 45000 ADUs against ~ 16500) than the rest G13 appears to be dead (no signal before or after, only during the JFET switch on did it show a spike). PMW: D7, C8 , DP1 , T2 are flat at 0 ADUs PLW: All good |

## FUNC-DCU-13P

| Test Id: | FUNC-DCU-13P |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ Photometer LIAs ON + Photometer BIAS ON +Photometer JFETs ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ Photometer LIAs ON + Photometer BIAS ON +Photometer JFETs ON |
| Success Criteria: | Test passed if : The photometer detectors show a small linear variation on the output voltage when different bias is applied through the load curve. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | On QLA bring up a time series display of a couple of pixels on each of the photometer BDAs |  |
| 2 | Run FUNC-DCU-13P test procedure from the HCSS Test Procedure window on TOPE |  |
| 3 | Contingency: If test fails repeat step 1 and 2. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-DCU-13P |  |  |  | N/A | Success |
| Start time @: 17: 12 End time @: 17: 24 OBSID: 0x30011AAD Comments: Parameter for LC: Array: PF Bias frequency: 130 Hz Sampling frequency: 18 Hz PSW phase: 180.71 deg PMW phase: 180.71 deg PLW phase: 180.71 deg Time at each level: 5 s See Annex 2 for detailed plots for each pixel |

## ILT_PERF_DNA_P

| Test Id: |  |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON + Photometer LIAs ON + Photometer BIAS ON + Photometer JFETs ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON + Photometer LIAs ON + Photometer BIAS ON + Photometer JFETs ON |
| Success Criteria: | Test passed if : The Photometer detectors don’t show excess noise. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Run ILT-PERF-DAN-P test procedure from the HCSS Test Procedure window on TOPE |  |
| 2 | Contingency: If test fails repeat step 1. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| ILT_PERF_DNA_P |  |  |  | N/A |  |
| Start time @: 17: 30 End time @: 17: 35 OBSID: 0x30011AAE Comments: Detectors settings: Bias frequency: 130 Hz Sampling frequency: 18 Hz PSW phase: 180.71 deg PMW phase: 180.71 deg PLW phase: 180.71 deg PSW bias : ~ 31mV PMW bias : ~ 31mV PLW bias : ~ 31mV TC bias : ~ 62 mV Duration of test: 5 minutes |

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | From TOPE HCSS Test Procedures run PDET-OFF | Executed @ 17:36 OBSID 0x30011AAF |

## FUNC-DCU-04S

| Test Id: | FUNC-DCU-04S |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON + Spectrometer LIAs ON |
| Success Criteria: | Test passed if : SCUDCDCSTAT parameter goes from 4 to 6. Spectrometer LIA card voltages are showing correct readings of +5V,+9V,-9V. Spectrometer LIA temperatures show an increase indicating that they are ON. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | On QLA bring up a time series display of the HK parameters: SLIAP5V SLIAP9V SLIAM9V LIAS1/2/3TEMP |  |
| 2 | Run FUNC-DCU-04S test procedure from the HCSS Test Procedure window on TOPE |  |
| 5 | Contingency: If test fails repeat steps 1 and 2. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-DCU-04S | SCUDCDCSTAT SLIAP5V SLIAP9V SLIAM9V LIA1/2/3TEMP | 4/6 0/~ +5V 0/~+11V 0/~-11V N/A/ [290-300]K | 4/6 0.17 / 5.23 0.003/ 11.57 0.003/-11.55 /~295Kwarming up |  | Success |
| Start time @: 17:43 End time @: 17:44 OBSID: 0x30011AB0 Comments: Spectrometer LIAs switched ON correctly |

## FUNC-DCU-11S

| Test Id: | FUNC-DCU-11S |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON + Spectrometer LIAs ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON + Spectrometer LIAs ON + Spectrometer BIAS ON + Spectrometer JFETs ON |
| Success Criteria: | Test passed if SCUDCDCSTAT goes from 4 to 6, Spectrometer LIAs voltages are correct and SJFET voltages are also correct. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Run FUNC-DCU-11S test procedure from the HCSS Test Procedure window on TOPE |  |
| 2 | After the test Write the values RAW and converted values of: LIASTAT SLIAP5V, SLIAP9V, SLIAN9V, SSWJFETSTAT,SLWJFETSTAT, SSWJFET1V,SLWJFET2V located in DCU PARAMETERS AND |  |
| 3 | Contingency: If test fails repeat steps 1 and 2. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-DCU-11S | SCUDCDCSTAT LIASTAT SLIAP5V SLIAP9V SLIAM9V SPECJFETSTAT SSWJFET1/2V SLWJFET1/2V | 6/6 0/0 0V/ ~ 5V 0V/~11V 0V/-11V 0/7 0V/-1.5V 0V/-1.5V | 6/6 0/0 /5.23 /11.57 /-11.55 0/0x7 See comments below | N/A | Success |
| Start time @: 17:51 End time @: 17:52 OBSID: 0x30011AB1 Comments: The Vss values for the JFETs were the same as for the PFM4 cold test campaign, i.e. SSWJFET1V: -2.07V SSWJFET2V: -1.59V SLWJFET1V: -1.68V SSW: D7 shows a higher output ( ~ 35000 ADUs against ~ 16500 ADUs) then the rest of the array. SLW: DP1, DP2 not responsive after switch on, they jump to zero. T2 remains at zero. C2, C4 and B3 showing previous (PFM4) anomalous behaviour. C4 behaviour corrected itself during cooldown. |

## FUNC-DCU-13S

| Test Id: | FUNC-DCU-13S |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON + Spectrometer LIAs ON + Spectrometer BIAS ON + Spectrometer JFETs ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON + Spectrometer LIAs ON + Spectrometer BIAS ON + Spectrometer JFETs ON |
| Success Criteria: | Test passed if : The spectrometer detectors show a small linear variation on the output voltage when different bias is applied through the load curve. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Run FUNC-DCU-13S test procedure from the HCSS Test Procedure window on TOPE |  |
| 2 | Contingency: If test fails repeat step 1. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-DCU-13S |  |  |  | N/A | Success |
| Start time @: 17:56 End time @: 18:10 OBSID: 0x30011AB2 Comments: Array: SF Bias frequency: 160 Hz Sampling frequency: 80 Hz SSW phase shift: 180.71deg SLW phase shift: 179.295 deg Time at each level: 5 s SSW D5 shows different behaviour than the rest of the pixels as in PFM4. Generally all (SSW/SLW) pixels looking responsive (TBC) except SSW C2,C4,B3 (the three bottom last ones). See Annex 2 for detailed plots for every pixel. |

## ILT_PERF_DNA_S

| Test Id: | FUNC-DCU-13S |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON + Spectrometer LIAs ON + Spectrometer BIAS ON + Spectrometer JFETs ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON + Spectrometer LIAs ON + Spectrometer BIAS ON + Spectrometer JFETs ON |
| Success Criteria: | Test passed if : The spectrometer detectors show a signal with some noise. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Run FUNC-DCU-13S test procedure from the HCSS Test Procedure window on TOPE |  |
| 2 | Contingency: If test fails repeat step 1. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| ILT_PERF_DNA_S |  |  |  | N/A |  |
| Start time @: 18:11 End time @: 18:16 OBSID: 0x30011AB3 Comments: Test run in order to collect noise data at nominal spectrometer settings: Array: SF Bias frequency: 160 Hz Sampling frequency: 80 Hz SSW phase shift: 180.71deg SLW phase shift: 179.29 deg Duration of test: 5 minutes QLA script needed to report the RMS values for all Spectrometer detectors. |
| Step# | Action | Comments |
| 1 | From TOPE HCSS Test Procedures run SDET_OFF | 18:45 OBSID 0x30011A74 |

SWITCH OFF sequence:

Execute MCU_OFF

Execute DRCU_OFF

Power OFF DRCU

Power OFF DPU

# Annexe1 (Instrument nominal configuration/modes)

|  | OFF | INIT | DPU_ON | DRCU_ON | REDY | PHOT STBY | SPEC STBY | CREC | SAFE |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| DPU |  | ON | ON | ON | ON | ON | ON | ON | ON |
| Essential Hsk packets |  |  | 0.5Hz | 0.5Hz | 0.5Hz | 0.5Hz | 0.5Hz | 0.5Hz | 0.5Hz |
| Normal Hsk packets |  |  | 1.0Hz | 1.0Hz | 0.25Hz | 0.25Hz | 0.25Hz | 1.0Hz | 0.25Hz |
| TC Acceptance |  | TBC | Yes | Yes | Yes | Yes | Yes | Yes | Yes |
| Event packets |  | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes |
| Science packets |  |  |  |  |  |  |  |  |  |
| VM |  |  |  |  |  |  |  | Cooler_Recycle |  |
| VM1 |  |  |  |  |  | Det_Temp_Ctrl |  |  |  |
| VM2 |  |  |  |  |  |  |  |  |  |
| VM3 |  |  |  |  |  |  |  |  |  |
| MODE |  |  | 0x0000 | 0x0100 | 0x0200 | 0x0300 | 0x0400 | 0x0600 | 0x0900 |
| DRCU |  |  | ON | ON | ON | ON | ON | ON |  |
| SCU |  |  |  |  |  |  |  |  |  |
| Temp Channels powered |  |  |  |  | Yes | Yes | Yes | Yes |  |
| SubK Channel powered |  |  |  |  | Yes | Yes | Yes | Yes |  |
| PCAL source powered |  |  |  |  |  |  |  |  |  |
| SCAL sources powered |  |  |  |  |  |  | TBD |  |  |
| TC Heater powered |  |  |  |  |  | Yes |  |  |  |
| Cooler SP Heater powered |  |  |  |  |  |  |  | Yes |  |
| Cooler EV HS powered |  |  |  |  |  |  |  | Yes |  |
| Cooler SP HS powered |  |  |  |  | Yes | Yes | Yes | Yes |  |
| DCU |  |  |  |  |  |  |  |  |  |
| Photometer BIAS |  |  |  |  |  | Yes |  |  |  |
| Photometer JFETS |  |  |  |  |  | Yes |  |  |  |
| Photometer LIAs |  |  |  |  |  | Yes |  |  |  |
| TC BIAS |  |  |  |  |  | Yes |  |  |  |
| TC JFETS |  |  |  |  |  | Yes |  |  |  |
| TC LIAs |  |  |  |  |  | Yes |  |  |  |
| Spectrometer BIAS |  |  |  |  |  |  | Yes |  |  |
| Spectrometer JFETS |  |  |  |  |  |  | Yes |  |  |
| Spectrometer LIAs |  |  |  |  |  |  | Yes |  |  |
| MCU |  |  |  |  |  |  |  |  |  |
| DSP |  |  |  |  | On | On | On | On |  |
| BSM |  |  |  |  |  | Hold | Hold |  |  |
| SMEC |  |  |  |  |  |  | Hold |  |  |

# Annexe 2 (Results of Load Curves)

The following graphs (1-12) show the response of the 288 Photometer detectors to the input voltage during the Load Curve (FUNC-DCU-13). The graph (13) shows the response of the 3 PTC channels to the input voltage during the Load Curve. The graphs (14-16) show the spectrometer 78 detectors output voltage during the load curve performed on the spectrometer side. These plots are for OBSIDs 30011AAD (phot) and 30011AB2 (spec).

Figure 1. PSW Detectors (1)

Figure 2. PSW Detectors (2)

Figure 3. PSW Detectors (3)

Figure 4. PSW Detectors (4)

Figure 5. PSW Detectors (5)

Figure 6. PSW Detectors (6)

Figure 7. PMW Detectors (1)

Figure 8. PMW Detectors (2)

Figure 9. PMW Detectors (3)

Figure 10. PMW Detectors (4)

Figure 11. PLW Detectors (1)

Figure 12. PLW Detectors (2)

Figure 13. PTC Detectors (1)

Figure 14. SSW Detectors (1)

Figure 15. SSW Detectors (2)

Figure 16. SLW  Detectors (1)