# Introduction

This document reports on the cool functional tests performed on the SPIRE Flight Instrument on the 2nd  February 2007 during the cooldown of PFM5 ILT Test Campaign.

## Scope

To judge the success or failure of a warm functional test by checking that:

- The telecommand sequence generated for a particular functional test is correctly received and executed on board by the SPIRE DPU.

- No error/event reports or command failures are generated during the execution of these commands.

- Telemetry is generated by the instrument as a result of telemetry requests to its different subunits.

- Particular telemetry parameters for each functional test change in an expected manner.

- A particular success criterion/criteria (specified in this document) is/are met.

## Reference Documents

| Ref | Document | Name | Version/Issue Nb. |
| --- | --- | --- | --- |
| RD01 | SPIRE-RAL-DOC-001652 | SPIRE Functional Tests Specification | Issue 1.4 |
| RD02 | SPIRE-RAL-DOC-001630 | SPIRE EGSE-ILT Start-Up Procedures | Issue 0.7 |
| RD03 | SPIRE-RAL-PRC-002222 | DRCU Switch ON Procedure | Issue 1.0 |
| RD04 | SPIRE-RAL-PRJ-001078 | SPIRE Data ICD | Issue 2.0 |
| RD05 | Sap-SPIRE-CCa-076-02 | DRCU/DPU Interface Control Document | Issue 1.2 |
| RD06 | LAM.PJT.SPI.NOT.011011 | MCU/DPU Command List ICD | Issue 5.0 |
| RD07 | SPIRE-IFS-PRJ-001391 | SPIRE OBS User Manual | Issue 2.1 |
| RD08 |  | SPIRE ILT Functional Testing Overview |  |

## Change Record

| Document | Change date | Changes |
| --- | --- | --- |
| Issue 1.0 | 03/11/06 | Document created |

# Table of Contents

1.	Introduction	1

1.1	Scope	1

1.2	Reference Documents	1

1.3	Change Record	1

2.	Functional Tests Configuration	3

2.1	SPIRE Instrument Configuration (MAIN)	3

2.2	Software Configuration	3

2.3	EGSE Configuration Checks	4

3.	Test procedure	6

3.1	GENERAL PASS/FAIL CRITERIA	6

3.2	GENERAL TEST PROCEDURE LAYOUT	6

4.	Detailed Test Results on MAIN instrument.	7

4.1	FUNC-SCU-01	7

4.2	FUNC-SCU-03	9

4.3	FUNC-SCU-06	11

4.4	FUNC-SCU-07	12

4.5	FUNC-SCU-04	13

4.6	FUNC-SCU-05	14

4.7	FUNC-MCU-01	15

4.8	FUNC-MCU-02	16

4.9	FUNC-BSM-01	17

4.10	FUNC-BSM-03	18

4.11	FUNC-SMEC-03	20

4.12	FUNC-SMEC-01	21

4.13	FUNC-SMEC-04a	23

4.14	FUNC-SMEC-09	25

4.15	FUNC-SMEC-07	27

4.16	FUNC-DCU-01	30

4.17	FUNC-DCU-11P	34

4.18	FUNC-DCU-13P	36

4.19	FUNC-DCU-14P	37

4.20	FUNC-DCU-11S	38

4.21	FUNC-DCU-13S	39

4.22	FUNC-DCU-14S	40

5.	END TEST SEQUENCE	40

6.	Annexe1 (Instrument nominal configuration/modes)	41

7.	Annexe 2 (Results of Load Curves)	42

# Functional Tests Configuration

## SPIRE Instrument Configuration (MAIN)

SPIRE FPU:

- FPU In Tank. ( Highest T is Spectrometer JFET Chassis ~ 110 K, Phot JFET Chassis ~ 104K)

- Cryostat under vacuum:

  - Pump Port Pressure =  ~ 1.3x10-7 bar

  - Tank Top Pressure  =  ~ 4.8x10-7 bar

- DRCU to Cryostat harnesses connected (Grounding pins not connected)

- Cryo-harness connected to FPU

SPIRE FM DPU:

- DPU Power supply connected on DPU Power MAIN (J01) connector (DPU side).

- 1553 Mil Bus connected on MAIN Connector Bus A (J03) connector (DPU side).

- DPU-DRCU warm interconnect harnesses (flight harnesses):

  - DPU J07 to DCU J01 DPU to DCU PRIME

  - DPU J08 to FCU J01 DPU to MCU PRIME

  - DPU J09 to FCU J03 DPU to SCU PRIME

  - DPU J10 to DCU J02 DPU to DCU RED

  - DPU J11 to FCU J02 DPU to MCU RED

  - DPU J12 to FCU J04 DPU to SCU RED

SPIRE FM DRCU:

- DRCU Power supply connected on DRCU Power MAIN (J05) connector (DRCU side on FCU).

- FCU to DCU PRIME power connectors J7 (FCU) to J03 (DCU) and FCU to DCU REDUNDANT power connectors J06 FCU to J04.

## Software Configuration

The current EGSE software configuration for the PRIME instrument tests:

| EGSE component | Version/Build number | Comment |
| --- | --- | --- |
| SCOS2000 | 2.3eP5 | Archive: PFM5_TEST1_PRIME MIB : Prime |
| HCSS | v0.4.1 Build# 1106 |  |
| QLA | v3.2 |  |
| QLA scripts |  |  |
| Test Control scripts |  |  |
| CUS Scripts | PFM5_CUS_DEFINITIONS_V1 |  |
| OBS | 2.2.D | 2.2.G has been acceptance tested but not yet installed on FM DPU |
| Boot Software | 2.0 |  |

## EGSE Configuration Checks

To check for the success of failure of a functional test, the real time telemetry of the instrument has to be monitored. The following applications must be running to do so. Before the test sequence starts, make the following checks:

| Workstation | EGSE component | Status | Check |
| --- | --- | --- | --- |
| Lichfield | EGSE router | Started | ( |
| Lichfield | EGSE Gateway | Started | ( |
| Lichfield | Telemetry Ingestion | Started | ( |
| Lichfield | Packet Display | Started | ( |
| Lincoln | SCOS2000 | Started | ( |
| Lincoln | EXIF + TOPE | Started | ( |
| Lincoln | Manual Stack | Started | ( |
| Gordon | CDMS Simulator | Started | ( |
| Lincoln | Test Control Server | Started | ( |

The following checks were performed to verify the correct initial instrument configuration for the tests.

| Step# | Action | Comments (Write any comments under this tab) | Check |
| --- | --- | --- | --- |
| 1 | In SCOS open DPU_AND_OBS_PARAMETERS display Check if : TM2N is incrementing by one @1Hz. TM1N is incrementing by one @0.5Hz. - If both are incrementing of only TM2N is incrementing , go to step 5. - If they are not, go to step 2. | TM2N is incrementing by 1 @ 1Hz TM1N is incrementing by 1 @ 0.5Hz Will go to step 5 | ( |
| 2 | Check if the DPU is powered ON: - If ON, the DPU power supply LCD will show ~ 28V and 0.40A, go to step 4. - If not ON, power ON DPU see comments on the right, then go to step 3. |  |  |
| 3 | In SCOS open Boot_ROM_Memory_Check display and check no errors are reported: - If no errors are reported, execute DPU_ON from HCSS Test Procedures. Then repeat step 1. - If the (5,2) contains errors: Check the error code in RD07. Then switch OFF the DPU and repeat step 2 |  |  |
| 4 | Execute define_new_HK_report.tcl HCSS Test procedure. Repeat step 1. |  |  |
| 5 | In SCOS open SCU_PARAMETERS display - If SCUP5V/P9V/M9V are jittering and BIAS_PARAMETERS display - If BIASTEMP shows ambient temperature, the DRCU is ON.Go to step 6. - If DRCU is not ON, refer to RD03 on how to start up the DRCU. | Had to power ON DRCU PRIME: SCU VOLTAGES LOOKING GOOD. SCUP5V = 5.23V SCUP9V = 9.08V SCUM9V = -9.08V BIAS VOLTAGES LOOKING GOOD. BIASP5V = 5.12V BIASP9V = 8.98V BIASM9V= -9.05V BIASTEMP LOOKING GOOD. BIASTEMP = 291.81K | ( |
| 6 | In SCOS open DPU_AND_OBS_PARAMETERS display and check that the MODE housekeeping parameter is DRCU_ON. | MODE (RAW)= 0x100 MODE (ENG) = DRCU_ON | ( |

Table 1. Initial configuration check

# Test procedure

The following two sections describe general pass/fail criteria (Section 3.1), the general test procedure layout (Section 3.1) and the detailed procedure for each functional test (Section 3.2).

## GENERAL PASS/FAIL CRITERIA

The general criterion for declaring a single test failed is the repeated failure of 2 consecutive runs of this test. In that case the functional test procedure should be aborted and the overall functional testing declared FAILED.

In the case of a ‘first run’ failure followed by a successful execution a third run of the same test should be performed and in the unlikely event of this third run being a failure the test procedure should be also aborted and the overall functional testing declared FAILED, as this would imply a not reliable operability of the instrument.

As a general remark ANY failure should be closely analyzed.

Note:  If the functional test is declared FAILED refer to section 4.1 for instrument switch OFF.

## GENERAL TEST PROCEDURE LAYOUT

The table below shows the general Short WFT sequence as it should be performed. In each step of this procedure the operator should refer to the detailed procedure in Section 3.2 .Test Control TCL scripts are available to invoke the correspondent CUS script stored in the HCSS database for each functional test. These CUS scripts will generate the appropriate command sequence for the particular functional test.

| Step | Subsystem tested | Test Id | Test Purpose |
| --- | --- | --- | --- |
| 1 | SCU | FUNC-SCU-01 | SCU Nominal Science Generation Check |
| 2 |  | FUNC-SCU-03 | FPU DC Thermometry Check |
| 3 |  | FUNC-SCU-06 | FPU AC Thermometry Check |
| 4 |  | FUNC-SCU-07 | Sorption Cooler Check |
| 5 |  | FUNC-SCU-04 | Photometer Calibrator Check |
| 6 |  | FUNC-SCU-05 | Spectrometer Calibrators Check |
| 9 | MCU | FUNC-MCU-01 | MCU Boot Check |
| 10 |  | FUNC-MCU-02 | MCU Nominal Science Generation Check |
| 11 | BSMm | FUNC-BSM-01 | BSM Switch ON Check |
| 12 |  | FUNC-BSM-03 | BSM Open Loop dynamics Check |
| 13 | SMECm | FUNC-SMEC-02A/B* | SMEC Launch Latch Open/Close Check |
| 14 |  | FUNC-SMEC-01 | SMECm Switch ON Check |
| 15 |  | FUNC-SMEC-03 | SMEC LED Integrity Check |
| 16 |  | FUNC-SMEC-04 | SMEC Positioning Test (Open Loop) |
| 17 | DCU | FUNC-DCU-01 | DCU Nominal Science Generation Check |
| 18 | Photometer LIAs | FUNC-DCU-04P | Photometer LIAs Check |
| 19 | Spectrometer LIAs | FUNC-DCU-04S | Spectrometer LIAs Check |

Table 2. General Short WFT sequence

# Detailed Test Results on MAIN instrument.

The following is a detailed (test by test) procedure including the steps required to perform each functional test individually.

| Step# | Action | Comments |
| --- | --- | --- |
| 0 | Open SCU_PARAMETERS display on SCOS Alpha Numeric Displays. |  |

## FUNC-SCU-01

| Test Id: | FUNC-SCU-01 |
| --- | --- |
| Initial Configuration: | DRCU_ON |
| Final Configuration: | DRCU_ON |
| Success Criteria: | Test passed if : Two SCU Nominal Science Report telemetry packets are received on QLA with the following characteristics: APID Type Subtype SID FrameID Frame length 0x508 21 1 0xA20 0x20 0x1E The frame time difference between consecutive SCU frames within these packets corresponds to the sampling rate. Nominal SCU sampling rate is 80Hz ( Δt = 12.5 ms The SPIRE HK parameter SCUFRAMECNT increments by 31. No events are generated during the frame generation. QLA to give go ahead. |

Test Procedure:

| Step# | Action |
| --- | --- |
| 1 | Write the initial value of SCUFRAMECNT parameter located in SCU_PARAMETERS display. |
| 2 | Run QLA script FUNC-SCU-01.py on QLA console. |
| 3 | Run FUNC-SCU-01 test procedure from the HCSS Test Procedure window on TOPE |
| 4 | Write the final value of SCUFRAMECNT. |
| 5 | Contingency: If test fails repeat steps 1 to 4. |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SCU-01 | SCUFRAMECNT | n/ n+ 31 | 0/ 31 | 31 | Success |
| Start time @: 13:44 End time @: 13:45 OBSID: 0x30012005 Comments: ************************************************************************* SCU: OBSID = 30012005, BBTYPE = 0x8000, APID = 0x508, SID = 0xa20 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. SCUFRAMECNT 0 31 31 31 Packet type = 0x15 TM5N 16383 1 49153 2 subtype = 0x1 FrameTime 12.4960 12.4992 Frame ID = 0x20 Frame Len = 0x1E STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 12.49802 ms sigma = 0.00155 ms |

## FUNC-SCU-03

| Test Id: | FUNC-SCU-03 |
| --- | --- |
| Initial Configuration: | DRCU_ON |
| Final Configuration: | DRCU_ON + DC thermometry ON |
| Success Criteria: | Test passed if all FPU DC thermometry sensors show temperature values indicating a correct functioning of the sensor, not open/short-circuited. If ANY reading is anomalous check RAW sensor reading. Open Circuit Criterion: RAW reading in the range [0, -100] Short Circuit Criterion: RAW reading of -32768 Note: All calibration with an upper limit of T > ~ 80K are likely to show short circuit readings |

Test Procedure:

| Step# | Action |
| --- | --- |
| 1 | Record all 16 FPU temperatures on the log |
| 2 | Contingency: If test fails execute SCU_OFF procedure from HCSS Test Procedure window on TOPE and then repeat steps 1 and 2. |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SCU-03 | SCUTEMPSTAT | 0/0xFFFF | 0xFFFF/0xFFFF | N/A | Success |
| Start time @: 13:45 End time @: 13:46 OBSID: 0x30012006 Comments: SCU-03 Thermometry Check OBSID = 0x30012006 PUMPHTRTEMP 54.11 32768 PUMPHSTEMP 37.26 32768 EVAPHSTMP 36.90 32768 SHUNTTEMP 18.71 32768 EMCFILTMP 89.69 50701 SL0TEMP 19.72 32768 PL0TEMP 20.33 32768 OPTTEMP 89.41 42103 BAFTEMP 90.26 44807 BSMIFTEMP 89.95 34750 SCAL2TEMP 89.59 42625 SCAL4TEMP 89.38 42292 SCALTEMP 83.34 32768 SMECIFTEMP 91.19 39859 SMECTEMP 26.54 32768 BSMTEMP 12.80 32768 |

## FUNC-SCU-06

| Test Id: | FUNC-SCU-06 |
| --- | --- |
| Initial Configuration: | DRCU_ON + DC thermometry ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON |
| Success Criteria: | Test passed if SUBKSTAT parameter went from 0 to 1. Open Circuit Criterion: RAW reading in the range 0 -100 Short Circuit Criterion: RAW reading of -32768 |

Test Procedure:

| Step# | Action |
| --- | --- |
| 1 | Record the current value of SUBKTEMP channel on the log |
| 3 | Contingency: If test fails : Send manual command: SEND_DRCU_COMMAND Parameter1 = 0xA0860000 Parameter2 = 0 Then repeat steps 1 and 2. |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SCU-06 | SUBKSTAT | 0/1 | 1/1 | N/A | Success |
| Start time @: 13:46 End time @: 13:46 OBSID: 0x30012007 Comments: fpu temp temp(K) temp(raw) Subktemp ~ 80K Before:32756 After :32737 |

## FUNC-SCU-07

| Test Id: | FUNC-SCU-07 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON |
| Success Criteria: | Test passed if during the execution of the test the following SCU HK parameters give correspondent readings of: SCU HK parameter RAW Converted SPHSV ~12715 ~323mV EVHSV ~12715 ~323mV SPHTRV ~14390 ~ 8 V |

Test Procedure:

| Step# | Action |
| --- | --- |
| 1 | Run FUNC-SCU-07 test procedure from the HCSS Test Procedure window on TOPE. |
| 2 | While the test is running Write the values of current values of SPHSV, EVHSV, SPHTRV located in SCU_PARAMETERS display. (RAW and CONVERTED) |
| 3 | Contingency: If test fails repeat steps 1 and 2. |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/During test | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SCU-07 | SPHSV EVHSV SPHTRV | 0/ ~ 323 mV 0/ ~ 323 mV 0/ ~ 8 V | 0/323.85mV 0/323.68mV 0/8.85V | N/A | Success |
| Start time @: 13:47 End time @: 14:49 OBSID: 0x30012008 Comments: |

## FUNC-SCU-04

| Test Id: | FUNC-SCU-04 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON |
| Success Criteria: | Test passed if PCALCURR/PCALV SCU HK parameters show the following values: PCALCURR HK parameter which shows the measured PCAL current is ~ 0.1 mA. PCALV HK parameter which shows the measured PCAL voltage is ~ 0.02V |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Write the current value of PCALV and PCALCURR located in SCU_PARAMETERS display. |  |
| 2 | Run FUNC-SCU-04 test procedure from the HCSS Test Procedure window on TOPE |  |
| 3 | While the test is running Write the values of PCALV and PCALCURR. |  |
| 4 | Contingency: If test fails repeat steps 1 to 3. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/During test | Actual Value Before/ During test | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SCU-04 | PCALCURR PCALV | 0/0.1mA 0/0.02V | 0/0.1015mA 0/0.0205V | N/A | Success |
| Start time @: 13:52 End time @: 13:54 OBSID: 0x300120009 Comments: |

## FUNC-SCU-05

| Test Id: | FUNC-SCU-05 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON |
| Success Criteria: | Test passed if : SCAL2CURR ,SCAL4CURR HK parameters which show the measured current read ~ 0.1 mA SCAL2V,SCAL4V parameters which show the measured voltage read ~ 0.05V. |

Test Procedure

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Write the current value of SCAL2V ,SCAL2CURR,SCAL4V,SCAL4CURR located in SCU_PARAMETERS display. |  |
| 2 | Run FUNC-SCU-05 test procedure from the HCSS Test Procedure window on TOPE |  |
| 3 | While the test is running write the values of SCAL2V ,SCAL2CURR,SCAL4V,SCAL4CURR. |  |
| 4 | Contingency: If test fails repeat steps 1 to 3. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/During test | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SCU-05 | SCAL2CURR SCAL2V SCAL4CURR SCAL4V | 0/0.1mA 0/0.05V 0/0.1mA 0/0.05V | 0/0.1003mA 0/0.0504V 0/0.1019mA 0/0.0510V | N/A | Success |
| Start time @: 13:55 End time @: 13:57 OBSID: 0x30012000A Comments: SCAL4 followed by SCAL2 |

| Step# | Action | Comments |
| --- | --- | --- |
| 0 | Open MCU_PARAMETERS display on SCOS Alpha Numeric Displays. |  |

## FUNC-MCU-01

| Test Id: | FUNC-MCU-01 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON |
| Success Criteria: | Test passed if: MCU boots. MCU voltages show expected values. MAC Board Temperature Reading shows ambient temperature. |

Test Procedure:

| Step# | Action |
| --- | --- |
| 1 | Run FUNC-MCU-01 test procedure from the HCSS Test Procedure window on TOPE |
| 2 | When procedure is finished Write the values of the MCU voltages. |
| 3 | Contingency: If test fails repeat steps 1 and 2. |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-MCU-01 | MCUP5V MCUP15V MCUP14V MCUM14V MCUM15V MCUMACTEMP MCUBSMTEMP MCUSMECTEMP | N/A/ ~ 5V N/A / ~15V N/A / ~ 14V N/A / ~ -14V N/A / ~ -15V N/A / ~ 300K | / 5.01V / 15.53V / 14.15V / -14.47V / -15.63V / 288.24 K / 293.48 K / 293.08 K | N/A | Success |
| Start time @: 14:00 End time @: 14:02 OBSID: 0x3001200B Comments: MCU Powered ON I = 0.83 MCU Booted I = 0.87 MCU Booted properly. |

## FUNC-MCU-02

| Test Id: | FUNC-MCU-02 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON |
| Success Criteria: | Test passed if : MCU produces each type of the frames requested and with the following characteristics. Frame APID Type Subtype SID FrameID Frame length Eng. 0x508 21 3 0x814 0x14 0x15 BSM 0x508 21 1 0x612 0x12 0xD SMEC 0x508 21 1 0x410 0x10 0xC BSM +SMEC No events are generated during the different frames generation. |

Test Procedure:

| Step# | Action |
| --- | --- |
| 1 | Write the current value of MCUFRAMECNT located in MCU_PARAMETERS display |
| 2 | Run QLA script FUNC-MCU-02.py on QLA console. |
| 3 | Run FUNC-MCU-02 test procedure from the HCSS Test Procedure window on TOPE |
| 4 | When test is finished Write the current value of MCUFRAMECNT. |
| 5 | Contingency: If test fails repeat steps 1 to 4. |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-MCU-02 | MCUFRAMECNT | 0/ ~ 6600 | 0 / 6493 |  | Success |
| Start time @: 14:03 End time @: 14:06 OBSID: 0x3001200C Comments: |

| Step# | Action | Comments |
| --- | --- | --- |
| 0 | Open CHOP PARAMETERS display on SCOS Alpha Numeric Displays. |  |

## FUNC-BSM-01

| Test Id: | FUNC-BSM-01 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON + BSM ON (open loop) |
| Success Criteria: | Test passed if: CHOPSENSPWR HK parameter goes from 0 to 1 CHOPSENSIG HK parameter shows variation from off to on JIGGSENSPWR HK parameter goes from 0 to 1 JIGGSENSSIG HK parameter shows variation from off to on |

Test Procedure

| Step# | Action |
| --- | --- |
| 1 | Run FUNC-BSM-01.py script on QLA |
| 2 | Run FUNC-BSM-01 test procedure from the HCSS Test Procedure window on TOPE |
| 3 | When the test is finished record all the Key parameters noted bellow |
|  | Contingency: If test fails repeat steps 1 and 2. |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-BSM-01 | CHOPSENSPWR CHOPLOOPMODE CHOPSENSSIG JIGGSENSPWR JIGGLOOPMODE JIGGSENSSIG | 0/1 3/3 0/? 0/1 3/3 0/? | 0/1 3/3 0x7FED/~ 0x9353 0/1 3/3 0x7FE4/0xA100 | N/A | Success |
| Start time @:14:06 End time @:14:07 OBSID:0x3001200D Comments: BSM switched ON normally |

## FUNC-BSM-03

| Test Id: | FUNC-BSM-03 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON + BSM ON (open loop) |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON + BSM ON (open loop) |
| Success Criteria: | Test passed if the chop sensor signal evolves in the same way as the positions set.(i.e if (pos1 > pos2 ( sig1 > sig2) for each jiggle position. Note: During warm tests the voltages on both chop and jiggle motors are likely to be saturated (CHOP/JIGGMOTORVOLT RAW values of ~ 0xFFFF) due to the high resistance of the motor coil at ambient temperature. |

Test Procedure

| Step# | Action |
| --- | --- |
| 1 | Run FUNC-BSM-03.py script on QLA |
| 2 | Run FUNC-BSM-03 test procedure from the HCSS Test Procedure window on TOPE |
| 3 | Contingency: If test fails repeat step 2. |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-BSM-03 |  |  |  | N/A | Success |
| Start time @: 14:10 End time @: 14:14 OBSID: 0x3001200E Comments: Run the test with the following parameters: BSM sampling 64Hz Chop start position = 0x1000 Chop end position = 0xf000 Chop step = 0x1000 Jigg start position = 0x7000 Jigg end position = 0x9000 Jigg step =0x2000 T at each position = 3 sec |

| Step# | Action | Comments |
| --- | --- | --- |
| 4 | Execute BSM_OFF from HCSS Test Procedures | 14:18 Obsid: 0x3001200F |

| Step# | Action | Comments |
| --- | --- | --- |
| 0 | Open SMEC PARAMETERS display on SCOS Alpha Numeric Displays. |  |

## FUNC-SMEC-03

| Test Id: | FUNC-SMEC-03 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON+ SMEC ON (open loop) |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON+ SMEC ON (open loop) |
| Success Criteria: | Test passed if: SMEC encoder signals 1 and 2 show a variation from one LED illumination level to another. |

Test Procedure:

| Step# | Action |
| --- | --- |
| 1 | Run FUNC-SMEC-03.py script on QLA. |
| 2 | Run FUNC-SMEC-03 test procedure from the HCSS Test Procedure window on TOPE |
| 3 | Contingency: If test fails repeat steps 1 and 2. |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-03 | SMECENCPWR SMECENCSIG1 SMECENCSIG2 |  | Values changed from 3 to 5 to 6 as expected | Not relevant | Success |
| Start time @: 14:23 End time @: 14:24 OBSID: 0x30012010 Comments: Input parameters for TOPE script: Start level = 3 End level = 6 Step level =1 T at each level = 5 |

## FUNC-SMEC-01

| Test Id: | FUNC-SMEC-01 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON+ SMEC ON (open loop) |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON +MCU ON+ SMEC ON (open loop) |
| Success Criteria: | Test passed if : SMECENCPWR HK parameter changes from 0 to 6. SMEC encoder signals 1 and 2 level show variation when encoder is switched ON. SMEC LVDT is switched ON. ( SMECLVDTPWR HK parameter goes from 0 to 1) SMEC LVDT DC and AC signals show variation when LVDT is switched ON. |

Test Procedure:

| Step# | Action |
| --- | --- |
| 1 | Run FUNC-SMEC-01.py script on QLA. |
| 2 | Run FUNC-SMEC-01 test procedure from the HCSS Test Procedure window on TOPE |
|  | Contingency: If test fails repeat steps 1. |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-01 | SMECENCPWR SMECLVDTPWR SMECENCSIG1 SMECENCSIG2 |  | 0/ 6 0/ 1 0xFFFF ~ 0xF000 | N/A | Success |
| Start time @: 14:45 End time @: 14:46 OBSID: 0x30012013 Comments: Signal 1 is saturated on prime with encoder level 6 as the previous SMEC tests shows. The encoder level to set is extracted from the SMEC nominal settings caltable. It would be useful to include a third ‘thermal’ status apart from the warm/cold , ‘cool’ with different encoder level. Will manually reduce the encoder level from 6 to 5. (0x90400005) When this is done the encoder signal 1 comes in range. |

## FUNC-SMEC-04a

| Test Id: | FUNC-SMEC-04a |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ SMEC ON (open loop) |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ SMEC ON (open loop) |
| Success Criteria: | Test passed if SMECLVDTDCSIG parameter shows a variation according to the different positions set. |

Test Procedure:

| Step# | Action |
| --- | --- |
| 1 | Run FUNC-SMEC-04a.py script on QLA |
| 2 | Run FUNC-SMEC-04a test procedure from the HCSS Test Procedure window on TOPE |
| 3 | Contingency: If test fails repeat steps 1. |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-04a | SMECLVDTDCSIG |  |  |  | Success |
| Start time @: 15:00 End time @: 15:03 OBSID: 0x30012015 Comments: |

Some extra SMEC functional test added for comparison with the future redundant side tests:

## FUNC-SMEC-09

| Test Id: | FUNC-SMEC-09 |
| --- | --- |
| Test Purpose: | SMEC Open Loop Scan Test. |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ SMEC ON (open loop) |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ SMEC ON (open loop) |
| Success Criteria: | Test passed if SMECLVDTDCSIG parameter shows a variation according to the different position of the SMEC along the scan. |

Test Procedure:

| Step# | Action |
| --- | --- |
| 1 | Run FUNC-SMEC-09.py script on QLA |
| 2 | Run FUNC-SMEC-09 test procedure from the HCSS Test Procedure window on TOPE |
| 3 | Contingency: If test fails repeat steps 1. |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | No. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-09 | All above mentioned in step 2 | N/A | N/A | N/A | Success |
| Start time @: 15:11 End time @: 12: OBSID: 0x30012016 Comments: Manually adjusted offsets: Signal 1 offset = 0x9058BF68 Signal 1 offset = 0x905A9C40 Start point = 1 mm, End point = 25 mm, Speed = 0.5 mm/s (forward/revers) Scans. = 2 Encoder not counting OBSID: 0x30012017 Comments: Manually adjusted offsets: Signal 1 offset = 0x9058C350 Signal 1 offset = 0x905AA410 Start point = 1 mm, End point = 25 mm, Speed = 0.5 mm/s (forward/revers) Scans. = 2 See next test for comparison of MOTORCURRENT |

| Step# | Action | Comments |
| --- | --- | --- |
| 0 | Execute SMEC_INIT from HCSS Test Procedures | 15:14 Obsid: 0x30012018 |

## FUNC-SMEC-07

| Test Id: | FUNC-SMEC-07 |
| --- | --- |
| Test Purpose: | SMEC Close Loop Scan Test. |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ SMEC ON (close loop) |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ SMEC ON (close loop) |
| Success Criteria: | Test passed if: SMECENCPOS HK parameter shows identical values as those of the SMECTRAJPOSN HK parameter during the scan. |

Test Procedure:

| Step# | Action |
| --- | --- |
| 1 | Run FUNC-SMEC-07.py script on QLA |
| 2 | Run FUNC-SMEC-07 test procedure from the HCSS Test Procedure window on TOPE |
| 3 | Contingency: If test fails repeat steps 1. |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | No. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-SMEC-07 | All above mentioned in step 1 | N/A | N/A | N/A | Success |
| Start time @: 15:26 End time @: 15:29 OBSID: 0x30012019 Comments: Start point = 1 mm, End point = 25 mm, Speed = 0.5 mm/s (forward/revers) Scans. = 2 Note: On the left hand side display the two consecutive (open) then (close) loop scans can be seen. Once gain the jitter on motorcurrent on the close loop points to a wrong set of PID parameters. |

| Step# | Action | Comments |
| --- | --- | --- |
| 4 | Execute SMEC_OFF from HCSS Test Procedures | 15:29 Obsid: 0x3001201A |

| Step# | Action | Comments |
| --- | --- | --- |
| 0 | Open DCU PARAMETERS SCOS Alpha Numeric Display |  |

## FUNC-DCU-01

| Test Id: | FUNC-DCU-01 |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON |
| Success Criteria: | Test passed if: DCU produces each type of DCU nominal science frame with the following characteristics. APID Type S.type SID Frame ID Frame type Nb. Of frames Nb. of pkts. 0x504 21 1 0x200 0 PF 100 100 0x506 21 1 0x201 1 SF 100 17 0x504 21 2 0x102 2 PSW 100 34 0x504 21 2 0x103 3 PMW 100 25 0x504 21 2 0x104 4 PLW 100 12 0x506 21 2 0x105 5 SSW 100 12 0x506 21 2 0x106 6 SLW 100 7 The frame time difference between consecutive DCU frames of each type corresponds to the sampling rate. Photometer Sampling rate is 15.3Hz ( Δt ~ 65.5 ms Spectrometer Sampling rate is 80Hz ( Δt = 12.5 ms The SPIRE HK parameter DCUFRAMECNT increments by 700. No events are generated during the frames generation. |

Test Procedure:

| Step# | Action |
| --- | --- |
| 1 | Write the current value of DCUFRAMECNT located d in DCU PARAMETERS AND |
| 2 | Run FUNC-DCU-01.py script on QLA |
| 3 | Run FUNC-DCU-01 test procedure from the HCSS Test Procedure window on TOPE |
| 4 | Write the current value of DCUFRAMECNT located d in DCU PARAMETERS AND |
| 5 | Contingency: If test fails repeat steps 1 to 3. |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-DCU-01 | DCUFRAMECNT | 0/700 | 8351/9051 | 700 | Success |
| Start time @: 15:30 End time @: 15: 33 OBSID: 0x3001201B Comments: ************************************************************************* PHOTF: OBSID = 3001201B, BBTYPE = 0x8800, APID = 0x504, SID = 0x200 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. DCUFRAMECNT 8351 8451 100 100 Packet type = 0x15 TM3N 8350 8450 100 100 subtype = 0x1 FrameTime 53.7600 53.7600 Frame ID = 0x0 Frame Len = 0x126 STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 53.75948 ms sigma = 0.00119 ms ************************************************************************* PHOTSW: OBSID = 3001201B, BBTYPE = 0x8802, APID = 0x504, SID = 0x102 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. DCUFRAMECNT 8451 8551 100 100 Packet type = 0x15 TM3N 8450 8484 34 34 subtype = 0x2 FrameTime 53.7600 53.7600 Frame ID = 0x2 Frame Len = 0x96 STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 53.75945 ms sigma = 0.00121 ms ************************************************************************* PHOTMW: OBSID = 3001201B, BBTYPE = 0x8803, APID = 0x504, SID = 0x103 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. DCUFRAMECNT 8551 8651 100 100 Packet type = 0x15 TM3N 8484 8509 25 25 subtype = 0x2 FrameTime 53.7600 53.7600 Frame ID = 0x3 Frame Len = 0x66 STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 53.75945 ms sigma = 0.00122 ms ************************************************************************* PHOTLW: OBSID = 3001201B, BBTYPE = 0x8804, APID = 0x504, SID = 0x104 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. DCUFRAMECNT 8651 8751 100 100 Packet type = 0x15 TM3N 8509 8521 12 12 subtype = 0x2 FrameTime 53.7568 53.7600 Frame ID = 0x4 Frame Len = 0x36 STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 53.75945 ms sigma = 0.00121 ms ************************************************************************* SPECF: OBSID = 3001201B, BBTYPE = 0x8801, APID = 0x506, SID = 0x201 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. DCUFRAMECNT 8751 8851 100 100 Packet type = 0x15 TM4N 16383 16 49168 17 subtype = 0x1 FrameTime 12.4928 12.4928 Frame ID = 0x1 Frame Len = 0x4E STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 12.49267 ms sigma = 0.00064 ms ************************************************************************* SPECSW: OBSID = 3001201B, BBTYPE = 0x8805, APID = 0x506, SID = 0x105 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. DCUFRAMECNT 8851 8951 100 100 Packet type = 0x15 TM4N 16 28 12 12 subtype = 0x2 FrameTime 12.4928 12.4928 Frame ID = 0x5 Frame Len = 0x36 STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 12.49267 ms sigma = 0.00065 ms ************************************************************************* SPECLW: OBSID = 3001201B, BBTYPE = 0x8806, APID = 0x506, SID = 0x106 _________________________________________________________________________ Parameter Initial Final Increment Expect Incre. Packet Chars. DCUFRAMECNT 8951 9051 100 100 Packet type = 0x15 TM4N 28 35 7 7 subtype = 0x2 FrameTime 12.4896 12.4928 Frame ID = 0x6 Frame Len = 0x1E STATISTICS ON TIME BETWEEN RECEPTION OF 2 CONSECUTIVE FRAMES: mean = 12.49267 ms sigma = 0.00064 ms |

## FUNC-DCU-11P

| Test Id: | FUNC-DCU-11P |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ Photometer LIAs ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ Photometer LIAs ON + Photometer BIAS ON +Photometer JFETs ON |
| Success Criteria: | Test passed if Photometer JFET source and drain voltages are correct: PSWJFETVSS1/2/3/4/5/6 (RAW: 0x4C CONVERTED ~ -1.5V). PMLWJFETVSS1/2/3/4 (RAW: 0x4C CONVERTED ~ -1.5V). PSWJFETSTAT = 0x3F PMLWJFETSTAT = 0x1F |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Run FUNC-DCU-11P test procedure from the HCSS Test Procedure window on TOPE |  |
| 2 | After the test Write the values RAW and converted values of: PSWJFETSTAT,PMLWJFETSTAT, PSWJFET1/2/3/4/5/6V PMWJFET1/2/3/4V PLWJFET1/2V located in DCU PARAMETERS AND |  |
| 3 | Contingency: If test fails repeat steps 1 and 2. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-DCU-11P | PSWJFETSTAT PMLWJFETSTAT PSWJFET1/2/3/4/5/6V PMWJFET1/2/3/4V PLWJFET1/2V | 0/0x3f 0/0x7f 0V/-1.5V 0V/-1.5V 0V/-1.5V | 0/0x03f 0/0x07f 0/-1.49 0/-1.49 0/-1.49 | N/A | Success |
| Start time @: 08:48 05th Feb 2007 End time @: 08:50 OBSID: 0x3001201C Comments: PSW: A10 appear to be dead (no signal before of after, only during the JFET switch on they showed a spike). G8 and C12 have a much higher output ( ~ 50000 ADUs against ~ 16400) than the rest of the array. PMW: C8 started of with signal an when the JFETS were started the signal went bottom of the scale. T2 does not have signal. DP1 has now signal against its behaviour during WFTs. PLW: Seems to be fine. |

## FUNC-DCU-13P

| Test Id: | FUNC-DCU-13P |
| --- | --- |
| Test Purpose: | Photometer Detectors Check |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ Photometer LIAs ON + Photometer BIAS ON +Photometer JFETs ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON+ Photometer LIAs ON + Photometer BIAS ON +Photometer JFETs ON |
| Success Criteria: | Test passed if : The photometer detectors show a small linear variation on the output voltage when different bias is applied through the load curve. |

Test Procedure:

| Step# | Action |
| --- | --- |
| 1 | On QLA bring up a time series display of a couple of pixels on each of the photometer BDAs |
| 2 | Run FUNC-DCU-13P.py script on QLA |
| 3 | Run FUNC-DCU-13P test procedure from the HCSS Test Procedure window on TOPE |
| 4 | Contingency: If test fails repeat step 1 and 2. |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | No. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-DCU-13P |  |  |  | N/A | To Check |
| Ran Proc_Stop_DCU_Data as data still running after DCU-11 Start time @: 08:53 End time @: 09:05 OBSID: 0x3001201D Comments: PSW: F9, B12 and T1 behave differently than the rest of the array with higher response to the increasing bias. PMW: No particularities. PLW: A7 behaves differently than the rest of the array with higher response to the increasing bias. See Annexe 2 for full results from every pixel |

## FUNC-DCU-14P

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | N/A | To Check |
| Start time @: 09:10 End time @: 09:15 OBSID: 0x3001201E Comments: Executed ILT-PERF-DNA-P Input parameters: Array = PF Time = 300 sec |

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | From TOPE HCSS Test Procedures run PDET-OFF | Executed @: 09:16 OBSID 0x3001201F |

## FUNC-DCU-11S

| Test Id: | FUNC-DCU-11S |
| --- | --- |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON + Spectrometer LIAs ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON + Spectrometer LIAs ON + Spectrometer BIAS ON + Spectrometer JFETs ON |
| Success Criteria: | Test passed if SCUDCDCSTAT goes from 4 to 6, Spectrometer LIAs voltages are correct and SJFET voltages are also correct. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | Run FUNC-DCU-11S test procedure from the HCSS Test Procedure window on TOPE |  |
| 2 | After the test Write the values RAW and converted values of: LIASTAT SLIAP5V, SLIAP9V, SLIAN9V, SSWJFETSTAT,SLWJFETSTAT, SSWJFET1V,SLWJFET2V located in DCU PARAMETERS AND |  |
| 3 | Contingency: If test fails repeat steps 1 and 2. |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-DCU-11S | SCUDCDCSTAT LIASTAT SLIAP5V SLIAP9V SLIAN9V SPECJFETSTAT SSWJFET1V SSWJFET2V SLWJFET1V | 6/6 0/0 0V/ ~ 5V 0V/~11V 0V/-11V 0/7 0V/-2.07V 0V/-1.59V 0V/-1.68V | 6/6 0/0 ~0/5.23 ~0/11.57 ~0/-11.53 0/0x7 0V/-2.07V 0V/-1.59V 0V/-1.68V | N/A | Success |
| Start time @: 09:18 End time @: OBSID: 0x30012020 Comments: Generally all pixels looking responsive SSW: D5 seem to show higher RAW ouput (~ 40000 ADUs against ~ 164000 ADUs) then the rest. SLW: C2,B3 seems to show low responsivity DP2 seems dead. |

## FUNC-DCU-13S

| Test Id: | FUNC-DCU-13S |
| --- | --- |
| Test Purpose: | Spectrometer detectors check |
| Initial Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON + Spectrometer LIAs ON + Spectrometer BIAS ON + Spectrometer JFETs ON |
| Final Configuration: | DRCU_ON + AC/DC thermometry ON+MCU ON + Spectrometer LIAs ON + Spectrometer BIAS ON + Spectrometer JFETs ON |
| Success Criteria: | Test passed if : The spectrometer detectors show a small linear variation on the output voltage when different bias is applied through the load curve. |

Test Procedure:

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | On QLA bring up a time series display of a couple of pixels on each of the spectrometer BDAs |  |
| 2 | Run FUNC-DCU-13S test procedure from the HCSS Test Procedure window on TOPE |  |
| 3 | Contingency: If test fails repeat steps 1 and 2 |  |

Test Log:

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | No. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
| FUNC-DCU-13S |  |  |  | N/A | To Check |
| Start time @: 09:22 End time @: 09:33 OBSID: 0x30012021 SSW: A3 and C6 show a higher response to the increasing bias than the rest. D5 behaving as during PFM4. SLW: C1 show a higher response to the increasing bias than the rest. See Annexe 2 for full results from every pixel |

## FUNC-DCU-14S

| Test Id | Key Parameter(s) | Expected Value Before/After | Actual Value Before/After | Nb. of frames received | Test Result |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | N/A | To Check |
| Start time @: 09:37 End time @: 09:42 OBSID: 0x30012022 Comments: Executed ILT-PERF-DNA-S Input parameters: Array = SF Time = 300 sec |

| Step# | Action | Comments |
| --- | --- | --- |
| 1 | From TOPE HCSS Test Procedures run SDET-OFF | Executed @: 09:45 OBSID 0x30012023 |

# END TEST SEQUENCE

The following table shows the necessary steps to be followed to end the warm functional test sequence.

| Step# | Action | HK parameters | Expected Value | Comments | Check |
| --- | --- | --- | --- | --- | --- |
| 1 | Check BSM is OFF | CHOPSENSPWR JIGGSENSPWR | 0 0 | 0 0 | ( ( |
| 2 | Check SMEC is OFF | SMECENCPWR | 0 | 0 | ( |
| 3 | Run MCU-OFF from the HCSS Test Procedure window on TOPE | SCUDCDCSTAT | 0 | 0 | ( |
| 4 | Check Instrument Configuration | MODE | 0x100/ DRCU_ON | DRCU_ON | ( |
| 5 | Run SCU_OFF from the HCSS Test Procedure window on TOPE | SCUTEMPSTAT SUBKSTAT | 0 0 | 0 0 | ( |
| 6 | Run DRCU_OFF from the HCSS Test Procedure window on TOPE | MODE | 0/ DPU_ON | ***** undefined | ( |

# Annexe1 (Instrument nominal configuration/modes)

|  | OFF | INIT | DPU_ON | DRCU_ON | REDY | PHOT STBY | SPEC STBY | CREC | SAFE |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| DPU |  | ON | ON | ON | ON | ON | ON | ON | ON |
| Essential Hsk packets |  |  | 0.5Hz | 0.5Hz | 0.5Hz | 0.5Hz | 0.5Hz | 0.5Hz | 0.5Hz |
| Normal Hsk packets |  |  | 1.0Hz | 1.0Hz | 0.25Hz | 0.25Hz | 0.25Hz | 1.0Hz | 0.25Hz |
| TC Acceptance |  | TBC | Yes | Yes | Yes | Yes | Yes | Yes | Yes |
| Event packets |  | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes |
| Science packets |  |  |  |  |  |  |  |  |  |
| VM |  |  |  |  |  |  |  | Cooler_Recycle |  |
| VM1 |  |  |  |  |  | Det_Temp_Ctrl |  |  |  |
| VM2 |  |  |  |  |  |  |  |  |  |
| VM3 |  |  |  |  |  |  |  |  |  |
| MODE |  |  | 0x0000 | 0x0100 | 0x0200 | 0x0300 | 0x0400 | 0x0600 | 0x0900 |
| DRCU |  |  | ON | ON | ON | ON | ON | ON |  |
| SCU |  |  |  |  |  |  |  |  |  |
| Temp Channels powered |  |  |  |  | Yes | Yes | Yes | Yes |  |
| SubK Channel powered |  |  |  |  | Yes | Yes | Yes | Yes |  |
| PCAL source powered |  |  |  |  |  |  |  |  |  |
| SCAL sources powered |  |  |  |  |  |  | TBD |  |  |
| TC Heater powered |  |  |  |  |  | Yes |  |  |  |
| Cooler SP Heater powered |  |  |  |  |  |  |  | Yes |  |
| Cooler EV HS powered |  |  |  |  |  |  |  | Yes |  |
| Cooler SP HS powered |  |  |  |  | Yes | Yes | Yes | Yes |  |
| DCU |  |  |  |  |  |  |  |  |  |
| Photometer BIAS |  |  |  |  |  | Yes |  |  |  |
| Photometer JFETS |  |  |  |  |  | Yes |  |  |  |
| Photometer LIAs |  |  |  |  |  | Yes |  |  |  |
| TC BIAS |  |  |  |  |  | Yes |  |  |  |
| TC JFETS |  |  |  |  |  | Yes |  |  |  |
| TC LIAs |  |  |  |  |  | Yes |  |  |  |
| Spectrometer BIAS |  |  |  |  |  |  | Yes |  |  |
| Spectrometer JFETS |  |  |  |  |  |  | Yes |  |  |
| Spectrometer LIAs |  |  |  |  |  |  | Yes |  |  |
| MCU |  |  |  |  |  |  |  |  |  |
| DSP |  |  |  |  | On | On | On | On |  |
| BSM |  |  |  |  |  | Hold | Hold |  |  |
| SMEC |  |  |  |  |  |  | Hold |  |  |

# Annexe 2 (Results of Load Curves)

The following graphs (1-12) show the response of the 288 Photometer detectors to the input voltage during the Load Curve (FUNC-DCU-13). The graph (13) shows the response of the 3 PTC channels to the input voltage during the Load Curve. The graphs (14-16) show the spectrometer 78 detectors output voltage during the load curve performed on the spectrometer side. These plots are for OBSIDs 3001201D for phot and 30012021 for spec.

Figure 1. PSW Detectors (1)

Figure 2. PSW Detectors (2)

Figure 3. PSW Detectors (3)

Figure 4. PSW Detectors (4)

Figure 5. PSW Detectors (5)

Figure 6. PSW Detectors (6)

Figure 7. PMW Detectors (1)

Figure 8. PMW Detectors (2)

Figure 9. PMW Detectors (3)

Figure 10. PMW Detectors (4)

Figure 11. PLW Detectors (1)

Figure 12. PLW Detectors (2)

Figure 13. PTC Detectors (1)

Figure 14. SSW Detectors (1)

Figure 15. SSW Detectors (2)

Figure 16. SLW  Detectors (1)