SPIRE Flight Thermal Performance

Predictions

| THERMAL ENGINEERING GROUP |
| --- |
| PREPARED BY | A.S. GOIZEL | (RAL) | 20-03-07 | pp |
| CHECKED BY | B. SHAUGHNESSY | (RAL) |  |  |
| SPIRE PROJECT |
| APPROVED BY | E. SAWYER | (RAL) |  |  |

“Page intentionally left blank”

CHANGE RECORD

| Issue | Date | Section | Change |
| --- | --- | --- | --- |
| Draft A | 14/03/07 | - | New Document. |
| Issue 1 | 20/03/07 | - | First Issue |

Acronyms

| Acronym | Definition |
| --- | --- |
| AD | Applicable Document |
| BDA | Bolometer Detector Arrays |
| BSM | Beam Steering Mechanism |
| CBB | Cold Black Body |
| CQM | Cryogenic Qualification Model |
| DRCU | Digital Readout Control Unit |
| DTMM | Detailed Thermal Mathematical Model |
| EGSE | Electronic Ground Support Equipment |
| FM | Flight Model |
| FPU | Focal Plane Unit |
| FS | Flight Spare |
| HCSS | Herschel Common Science System |
| HeI | Helium I |
| HeII | Helium II |
| HOB | Herschel Optical Bench |
| I/F | Interface |
| IIDB | Instrument Interface Document Part B |
| IRD | Instrument Requirement Document |
| ILT | Instrument Level Testing |
| JFET | Junction Field Effect Transistor |
| L0 | Level-0 |
| L1 | Level-1 |
| L2 | Level-2 |
| L3 | Level-3 |
| LN2 | Liquid Nitrogen |
| MGSE | Mechanical Ground Support Equipment |
| PFM | Proto Flight Model |
| RD | Reference Document |
| SMEC | Spectrometer Mechanism |
| SCU | Subsystem Control Unit |
| SOB | SPIRE Optical Bench |
| SPIRE | Spectral and Photometric Imaging Receiver |
| TBT | Thermal Balance Test |

CONTENTS

1	Introduction	7

1.1	Scope	7

1.2	Documents	7

1.2.1	Applicable Documents	7

1.2.2	Reference Documents	7

2	Analysis	8

2.1	SPIRE High Level Thermal Requirements	8

2.2	SPIRE Thermal Testing and Verification	8

2.3	SPIRE Flight Thermal Model	9

2.4	Instrument Power Dissipations	10

2.4.1	Photometer Mode and Power Budget	10

2.4.2	Spectrometer Mode and Power Budget	11

2.4.3	Power Dissipation References	12

2.5	Cooler Recycling	13

2.6	SPIRE Photometer Mode – Steady-State Analysis	14

2.6.1	Power Dissipation in Worse Case Photometer Mode	14

2.6.2	Heat Loads in Worse Case Photometer Mode	15

2.6.3	Temperatures in Worse Case Photometer Mode	16

2.7	SPIRE Spectrometer Mode – Steady-State Analysis	17

2.7.1	Power Dissipation in Worse Case Spectrometer Mode	17

2.7.2	Heat Loads in Worse Case Spectrometer Mode	18

2.7.3	Temperatures in Worse Case Spectrometer Mode	19

2.8	SPIRE Steady-State Average Performance during Mission	20

2.8.1	Average Power Dissipation during Mission	20

2.8.2	Average Heat Loads during Mission	21

LIST OF TableS

Table 1-1- Applicable Documents	7

Table 1-2 - Reference Documents	7

Table 2-1 –SPIRE High Level Thermal Requirements	8

Table 2-2 – SPIRE Flight Thermal Model Correlation Factors Summary	9

Table 2-3 - Photometer Observatory Functions (SPIRE-RAL-DOC-000320, Issue 3)	10

Table 2-4 – SPIRE Mechanisms and Calibration Sources Dissipations in Photometer Mode	11

Table 2-5 – Spectrometer Observatory Functions (SPIRE-RAL-DOC-000320, Issue 3)	11

Table 2-6 – SPIRE Mechanisms and Calibration Sources Dissipations in Spectrometer Mode	12

Table 2-8 – Worse Case Power Dissipation in Photometer Mode	14

Table 2-9 – SPIRE Heat Load Performance in Worse Case Photometer Mode	15

Table 2-9 – Herschel Interface Temperature in Worse Case Photometer Mode	16

Table 2-10 - SPIRE Temperature in Worse Case Photometer Mode	16

Table 2-12 – Worse Case Power Dissipation in Spectrometer Mode	17

Table 2-13 – SPIRE Heat Load Performance in Worse Case Spectrometer Mode	18

Table 2-13 – Herschel Interface Temperature in Worse Case Spectrometer Mode	19

Table 2-14 - SPIRE Temperature in Worse Case Spectrometer Mode	19

Table 2-16 - Average SPIRE Dissipation during Mission	20

Table 2-17 – Average SPIRE Heat Loads During Mission	21

LIST OF FIGUReS

Figure 3-1 – Cooler Pump Heater Dissipation Profile during Nominal Automated Cooler Recycling	13

# Introduction

## Scope

This report presents the results from the SPIRE flight thermal performance prediction analysis. These predictions have been carried out with the SPIRE detailed thermal mathematical model (correlated against test data gathered during the instrument and its subsystems test campaigns) integrated in the Herschel detailed thermal mathematical model Issue 4.6 delivered by ESA in September 2006 (which has been correlated against test data gathered during the cryostat STM1 test campaign).

## Documents

### Applicable Documents

| ID | Title | Number |
| --- | --- | --- |
| AD1 | SPIRE Thermal Design Requirements | SPIRE-RAL-PJR-002075 |
| AD2 | SPIRE Instrument Interface Document Part B (IIDB) | SPIRE-ESA-DOC-000275 |

Table 1-1- Applicable Documents

### Reference Documents

| ID | Title | Number |
| --- | --- | --- |
| RD1 | SPIRE Flight Thermal Model Correlation Report | SPIRE-RAL-REP-002723 |
| RD2 | SPIRE CQM1/2 Thermal Test Balance Report | SPIRE-RAL-REP-002078 |
| RD3 | SPIRE PFM2 Thermal Balance Test Report | SPIRE-RAL-REP-002534 |
| RD4 | SPIRE PFM3 Thermal Balance Test Report | SPIRE-RAL-REP-002684 |
| RD5 | SPIRE PFM4/PFM5 Thermal Balance Test Report | SPIRE-RAL-REP-002784 |
| RD6 | SPIRE Verification Science Review Thermal Performance | SPIRE-RAL-REP-002557 |

Table 1-2 - Reference Documents

# Analysis

## SPIRE High Level Thermal Requirements

Requirements applicable to the SPIRE thermal design can be found in [AD1] and [AD2]. The main SPIRE high level requirements are summarised in Table 2-1 hereafter.

| Parameter | Reqt | Goal |
| --- | --- | --- |
| Minimum Cooler Hold Time [hr] | 46 | 46 |
| Maximum Detector Absolute Temperature [mK] | 310 | 310 |
| Maximum L0 Enclosure Heat Load [mW] | 4 | 1 |
| Maximum L0 Pump Heat Load [mW] | 2 | 2 |
| Maximum L1 Heat Load [mW] | 15 | 13 |
| Maximum PJFET L3 Heat Load [mW] | 50 | 50 |
| Maximum SJFET L3 Heat Load [mW] | 25 | 25 |

Table 2-1 –SPIRE High Level Thermal Requirements

Important notes:

- The heat load requirements guarantee a maximum interface temperature at the various Herschel temperature stages. These have been defined such that SPIRE meets its 46hr holdtime.

- Should the SPIRE operating loads at one/several of these interfaces be higher than required, the Herschel interface temperatures will increase and this could compromise the instrument overall performance. It is therefore important that the SPIRE thermal design ensures that operating heat loads remain within the requirements at all times.

- The heat load requirements also represent the maximum allowable average operating heat loads for SPIRE over the whole mission lifetime. It is important that the SPIRE average loads do not exceed the requirements in order for the Herschel cryostat to meet its 3.5 years mission lifetime.

## SPIRE Thermal Testing and Verification

The SPIRE instrument underwent a total of 6 thermal balance test campaigns (as part of the instrument level testing) and a number of reports have been produced (RD2 to RD5), each summarising the outcome and results from the tests carried out during each of the test campaign.

The “SPIRE Verification Science Review Thermal Performance” (RD6) summarises the outcome of each test campaign and also contains the Thermal Requirement Verification Matrix.

## SPIRE Flight Thermal Model

The SPIRE detailed thermal model has been correlated against test data gathered at unit and instrument level testing. A summary of the main correlation factors is given in Table 2-2 hereafter. Additional details about the thermal model correlation can be found in RD1.

| Parameter | Correlation Factors |
| --- | --- |
| JFET Isolation Supports Conductance | 1.1 |
| L3 Isolation Interface Conductance | 0.3 |
| JFET Chassis Conductance | 0.333 |
| FPU Isolation Joint | 0.14 |
| Cooler Heat Switches OFF Conductance | 1.3795 |
| Cooler Shunt to Evaporator Titanium Tube Conductance | 0.8 |
| L0 Straps Cu/Cu Bolted Interface Conductance | 0.588 |
| Support CFRP Thermal Conductivity | 2 |
| PLW Feedhorn to Cover Interface Conductance | 1.2 |
| PMW Feedhorn to Cover Interface Conductance | 0.93 |
| PSW Feedhorn to Cover Interface Conductance | 1.83 |
| SLW Feedhorn to Cover Interface Conductance | 1.07 |
| SSW Feedhorn to Cover Interface Conductance | 1.15 |
| PSW Kapton Harness Conductance | 1 |
| PMW Kapton Harness Conductance | 0.55 |
| PLW Kapton Harness Conductance | 0.87 |
| SSW Kapton Harness Conductance | 0.87 |
| SLW Kapton Harness Conductance | 3.51 |
| Cooler Cold tip Absolute Temperature | -10mK |

Table 2-2 – SPIRE Flight Thermal Model Correlation Factors Summary

The SPIRE thermal model which has been used for this analysis can be found on the Thermal_Models network drive at the Rutherford Appleton Laboratory under:

\\Thermal_Models\TD-01-02-SPIRE\DTMM\SPIRE_TMM_FM_3-1\SPIRE_TMM_FM_3-1.d

The thermal model logfile can be found at:

\\Thermal_Models\TD-01-02-SPIRE\DTMM\ SPIRE_TMM_FM_Logfile.xls

Note: Issue 4.6 of the correlated Herschel cryostat detailed thermal model (delivered by ESA in September 2006) has been used in conjunction with SPIRE_TMM_FM_3-1 for this analysis.

## Instrument Power Dissipations

This section summarises all power dissipated in SPIRE at L1 and L3 for the photometer and spectrometer observation modes.

### Photometer Mode and Power Budget

Table 2-3 describes the various operations mode of SPIRE when in photometer observation mode.

Table 2-3 - Photometer Observatory Functions (SPIRE-RAL-DOC-000320, Issue 3)

Observations in photometer mode consist mainly of POF1, POF2, POF3, POF5 and POF8.

Table 2-4 hereafter describes the power dissipated by the SPIRE PCAL, BSM and PJFET when operating in photometer mode. The dissipations represent the “average power” dissipated during a given mode of observation i.e. the power dissipated by the BSM at the various chop/jiggle positions of the 7pt jiggle map varies between 0mW and 0.7mW, the 0.3mW given in the table represents the average dissipation for all positions for a single map. The duty cycle gives an indication of the amount of time which will be allocated to the various operation modes for a nominal observation period of 46hr i.e. the chopping mode is to be used for only a quarter of the overall 46hr period.

| Mechanisms | Ref | Average Dissipation [mW] | Duty Cycle [%] (*) |
| --- | --- | --- | --- |
| BSM – POF8 – Calibration with PCAL | 2 | 0.0243 | 100 |
| BSM Sensors | 1 | 0.8 | 100 |
| BSM Motor - POF1 – Chopping (+/-63”) | 1 | 0.548 | 25 |
| BSM Motor - POF2 – 7pt Jiggle Map | 1 | 0.3 | 25 |
| BSM Motor - POF3 – 64pt Jiggle Map | 1 | 1.55 | 25 |
| BSM Motor – POF5 – Scan | 1 | 0.0 | 25 |
| Extra power component during BSM dynamic switching | 1 | 0.25 | 100 |
| Photometer JFETs | 3 | 56.64 | 100 |

(*) Over a nominal 46hr observation period in photometer mode.

Table 2-4 – SPIRE Mechanisms and Calibration Sources Dissipations in Photometer Mode

Notes:

- It is currently assumed that POF1, POF2, POF3 and POF5 will be equally used. This will depend on the scientific community needs.

- The 64pt Jiggle Map is currently the worse case power dissipation for the steady-state analysis.

- The reference given in the table can be found in section 2.4.3.

### Spectrometer Mode and Power Budget

Table 2-5 describes the various operations mode of SPIRE when in spectrometer observation mode.

Table 2-5 – Spectrometer Observatory Functions (SPIRE-RAL-DOC-000320, Issue 3)

Table 2-6 hereafter describes the power dissipated by the SPIRE SMEC, SCAL, BSM, PCAL and SJFET when operating in spectrometer mode. The dissipations represent the “average power” dissipated during a given mode of observation i.e. the power dissipated by the SMEC actuator during a high resolution scan varies quadratically between 0 and ~17mW. The 3.56mW given in the table represents the integrated power dissipation of the actuator over the full scan range. The duty cycle gives an indication of the amount of time which will be allocated to the various observation modes for a nominal observation period of 46hr i.e. the SMEC HI resolution mode is to be used half the time of the overall 46hr period.

| Mechanisms | Ref | Average Dissipation [mW] | Duty Cycle [mW] (*) |
| --- | --- | --- | --- |
| SCAL2 at 80K | 2 | 2 | 100 |
| Extra power component during SCAL dynamic switching | 2 | 0.87 | 50 |
| SMEC Actuator R1000 (HI Resolution) | 4 | 3.56 | 50 |
| SMEC Actuator R100 (MED Resolution) | 4 | 0.46 | 25 |
| SMEC Actuator R10 (L0 Resolution) | 4 | 0.43 | 25 |
| SMEC Encoder (Level 2) | 4, 5 | 1.2 | 100 |
| SMEC LVDT | 5 | 0.112 | 100 |
| BSM Sensors | 1 | 0.8 | 100 |
| BSM Motor – POF3 – 64pt Jiggle Map | 1,6,7 | 1.55 | 50 |
| Extra power component during BSM dynamic switching | 1, 6 | 0.25 | 50 |
| BSM Calibrator (PCAL) | 2 | 0.0243 | 100 |
| Spectrometer JFETs | 3 | 15.17 | 100 |

(*) Over a nominal 46hr operation period in Spectrometer mode.

Table 2-6 – SPIRE Mechanisms and Calibration Sources Dissipations in Spectrometer Mode

Notes:

- The High Scan Resolution map is currently the worse case power dissipation for the steady-state analysis.

- The reference given in the table can be found in section 2.4.3.

### Power Dissipation References

[1] – Measured at unit level on PFM unit, please refer to Bryan Stobie’s email on 09/02/04.

[2] – Measured as part of instrument PFM3 test campaign, please refer to PFM3 Thermal Test Report, section 4.8.1.

[3] – Measured as part of instrument PFM3 test campaign, please refer to HR-SP-RAL-RFW-005v1.

[4] – Measured as part of instrument PFM4 test campaign, please refer to PFM4 Thermal Test Report (including short section on latest PFM5 test results).

[5] – Measured at unit level on CQM unit, please refer to SMEC CQM Cryogenic Test Results (LAM.ELE.SPI.PRV.040731_01).

[6] – Emails from Bruce Swinyard on 05/12/05.

[7] – SPIRE Operating Modes Document (SPIRE-RAL-DOC-000320, Issue 3).

## Cooler Recycling

Figure 2-1 describes the cooler pump heater power dissipation during a nominal automated cooler recycling.

Figure 2-1 – Cooler Pump Heater Dissipation Profile during Nominal Automated Cooler Recycling

## SPIRE Photometer Mode – Steady-State Analysis

### Power Dissipation in Worse Case Photometer Mode

The table below summarises the power dissipation for the SPIRE mechanisms, calibration source and electronic boxes, including their duty cycle for the worse case operating mode when in photometer mode.

| BSM – POF8 – Calibration with PCAL | [mW] | 0.024 | 100% | 0.024 |
| --- | --- | --- | --- | --- |
| SCAL2 at 80K | [mW] | 2.000 | 0% | 0.000 |
| Extra power component during SCAL dynamic switching | [mW] | 0.870 | 0% | 0.000 |
| SMEC Actuator – R10 | [mW] | 0.430 | 0% | 0.000 |
| SMEC Actuator – R100 | [mW] | 0.460 | 0% | 0.000 |
| SMEC Actuator – R1000 | [mW] | 3.560 | 0% | 0.000 |
| SMEC Encoder (Level 2) | [mW] | 1.200 | 0% | 0.000 |
| SMEC LVDT | [mW] | 0.112 | 0% | 0.000 |
| BSM Sensors | [mW] | 0.800 | 100% | 0.800 |
| BSM Motor – POF1 – Chopping (+/-63”) | [mW] | 0.548 | 0% | 0.000 |
| BSM Motor – POF2 – 7pt Jiggle Map | [mW] | 0.300 | 0% | 0.000 |
| BSM Motor – POF3 – 64pt Jiggle Map | [mW] | 1.550 | 100% | 1.550 |
| BSM Motor – POF5 – Scan | [mW] | 0.000 | 0% | 0.000 |
| Extra power component during BSM dynamic switching | [mW] | 0.250 | 100% | 0.250 |
| Total L1 Dissipation | [mW] | - | - | 2.624 |
| PJFET Dissipation | [mW] | 56.64 | 100.0% | 56.64 |
| SJFET Dissipation | [mW] | 15.17 | 0.0% | 0.000 |

Table 2-7 – Worse Case Power Dissipation in Photometer Mode

### Heat Loads in Worse Case Photometer Mode

The table below summarises the SPIRE heat loads at the various interfaces for the worse case operating mode in photometer mode.

|  |  | Performance | Reqt | Goal |
| --- | --- | --- | --- | --- |
| Cooler Total Load | [uW] | 29.4 (*) | 30 | 30 |
| Cooler Hold Time | [hr] | 49.4 | 46 | 46 |
| L0 Evaporator Heat Load | [mW] | 0.44 | - | - |
| L0 Pump Heat Load | [mW] | 2.3 | 2 | 2 |
| L0 Enclosure Heat Load | [mW] | 0.7 | 4 | 1 |
| L1 PJFET Harness Parasitic | [mW] | 2.17 | - | - |
| L1 SJFET Harness Parasitic | [mW] | 0.29 | - | - |
| L1 Isolation Supports | [mW] | 7.97 | - | - |
| L1 Housekeeping Harness | [mW] | 1.62 | - | - |
| L1 Radiation Load | [mW] | 3.64 | - | - |
| L1 Dissipation | [mW] | 2.64 | - | - |
| Total L1 Heat Load | [mW] | 16.75 | 15 | 13 |
| L3 PJFET Heat Load | [mW] | 41.96 | 50 | 50 |
| L3 SJFET Heat Load | [mW] | -5.34 | 25 | 25 |

Table 2-8 – SPIRE Heat Load Performance in Worse Case Photometer Mode

Notes:

- Please note that the Herschel L0 HeII interface temperature is assumed to be at 1.65K.

- The cooler total heat load includes a 1uW (*) for PTC operation.

- The results presented do not include any margin.

Observations:

- The heat load at the pump L0 interface exceeds the 2mW requirement but the heat loads from the L0 Enclosure is much lower than the requirement.

- The total L1 heat load exceeds the 15mW requirement in this case but the instrument still meets its hold time requirements.

### Temperatures in Worse Case Photometer Mode

Table 2-9 summarises the temperatures experienced at the various Herschel interfaces (for the operating heat loads described in section 2.6.2) while Table 2-10 gives an overview of the instrument temperatures.

| Herschel Interface Temperature [K] | Photometer Mode |
| --- | --- |
| PJFET L3 IF | 15.532 |
| SJFET L3 IF | 14.944 |
| HOB - 371 | 12.098 |
| HOB - 372 | 11.842 |
| HOB - 373 | 12.08 |
| HOB - 374 | 12.1 |
| HOB - 375 | 12.094 |
| HOB - 376 [-> SPIRE Cone] | 12.097 |
| HOB - 377 | 12.177 |
| HOB - 378 | 12.308 |
| HOB - 379 | 12.176 |
| HOB - 380 | 12.193 |
| HOB - 381 [-> SPIRE A-Frames] | 12.173 |
| L1 Strap IF #1 | 4.481 |
| L1 Strap IF #2 | 4.567 |
| HeII Tank | 1.65 |

Table 2-9 – Herschel Interface Temperature in Worse Case Photometer Mode

| SPIRE Temperature [K] (*) | Photometer Mode |
| --- | --- |
| Cold Tip (adjusted for self-heating on sensor) | 0.28 |
| PLW BDA Detector | 296 |
| PMW BDA Detector | 298 |
| PSW BDA Detector | 299 |
| SLW BDA Detector | 301 |
| SSW BDA Detector | 294 |
| Cooler Pump | 1.851 |
| Cooler Shunt | 1.656 |
| L0 Photometer Enclosure | 1.68 |
| L0 Spectrometer Enclosure | 1.67 |
| SOB | 4.8 |
| PJFET Chassis | 16.75 |
| SJFET Chassis | 14.85 |

(*) Mean temperature for enclosures

Table 2-10 - SPIRE Temperature in Worse Case Photometer Mode

Observations:

- All detectors are within the required 310mK absolute temperature.

## SPIRE Spectrometer Mode – Steady-State Analysis

### Power Dissipation in Worse Case Spectrometer Mode

The table below summarises the power dissipation for the SPIRE mechanisms, calibration source and electronic boxes, including their duty cycle for the worse case operating mode when in spectrometer mode.

| BSM – POF8 – Calibration with PCAL | [mW] | 0.024 | 100% | 0.024 |
| --- | --- | --- | --- | --- |
| SCAL2 at 80K | [mW] | 2.000 | 100% | 2.000 |
| Extra power component during SCAL dynamic switching | [mW] | 0.870 | 50% | 0.435 |
| SMEC Actuator – R10 | [mW] | 0.430 | 0% | 0.000 |
| SMEC Actuator – R100 | [mW] | 0.460 | 0% | 0.000 |
| SMEC Actuator – R1000 | [mW] | 3.560 | 100% | 3.560 |
| SMEC Encoder (Level 2) | [mW] | 1.200 | 100% | 1.200 |
| SMEC LVDT | [mW] | 0.112 | 100% | 0.112 |
| BSM Sensors | [mW] | 0.800 | 100% | 0.800 |
| BSM Motor – POF1 – Chopping (+/-63”) | [mW] | 0.548 | 0% | 0.000 |
| BSM Motor – POF2 – 7pt Jiggle Map | [mW] | 0.300 | 0% | 0.000 |
| BSM Motor – POF3 – 64pt Jiggle Map | [mW] | 1.550 | 50% | 0.775 |
| BSM Motor – POF5 – Scan | [mW] | 0.000 | 0% | 0.000 |
| Extra power component during BSM dynamic switching | [mW] | 0.250 | 50% | 0.125 |
| Total L1 Dissipation | [mW] | - | - | 9.031 |
| PJFET Dissipation | [mW] | 56.64 | 0.0% | 0.000 |
| SJFET Dissipation | [mW] | 15.17 | 100.0% | 15.170 |

Table 2-11 – Worse Case Power Dissipation in Spectrometer Mode

### Heat Loads in Worse Case Spectrometer Mode

The table below summarises the SPIRE heat loads at the various interfaces for the worse case operating mode in spectrometer mode.

|  |  | Performance | Reqt | Goal |
| --- | --- | --- | --- | --- |
| Cooler Total Load | [uW] | 29.1 | 30 | 30 |
| Cooler Hold Time | [hr] | 49.9 | 46 | 46 |
| L0 Evaporator Heat Load | [mW] | 0.53 | - | - |
| L0 Pump Heat Load | [mW] | 2.38 | 2 | 2 |
| L0 Enclosure Heat Load | [mW] | 0.86 | 4 | 1 |
| L1 PJFET Harness Parasitic | [mW] | 0.91 | - | - |
| L1 SJFET Harness Parasitic | [mW] | 0.21 | - | - |
| L1 Isolation Supports | [mW] | 6.66 | - | - |
| L1 Housekeeping Harness | [mW] | 2.42 | - | - |
| L1 Radiation Load | [mW] | 3.65 | - | - |
| L1 Dissipation | [mW] | 9.05 | - | - |
| Total L1 Heat Load | [mW] | 20.91 | 15 | 13 |
| L3 PJFET Heat Load | [mW] | 0.48 | 50 | 50 |
| L3 SJFET Heat Load | [mW] | 12.63 | 25 | 25 |

Table 2-12 – SPIRE Heat Load Performance in Worse Case Spectrometer Mode

Notes:

- Please note that the Herschel L0 HeII interface temperature is assumed to be at 1.65K.

- The results presented do not include any margin.

Observations:

- The heat load at the pump L0 interface exceeds the 2mW requirement but the heat loads from the L0 Enclosure is much lower than the requirement.

- The total L1 heat load exceeds the 15mW requirement in this case but the instrument still meets its hold time requirements.

### Temperatures in Worse Case Spectrometer Mode

Table 2-13 summarises the temperatures experienced at the various Herschel interfaces (for the operating heat loads described in section 2.7.2) while Table 2-14 gives an overview of the instrument temperatures.

| Herschel Interface Temperature [K] | Spectrometer Mode |
| --- | --- |
| PJFET_L3 IF | 11.785 |
| SJFET_L3 IF | 12.687 |
| HOB - 371 | 11.492 |
| HOB - 372 | 11.273 |
| HOB - 373 | 11.475 |
| HOB - 374 | 11.494 |
| HOB - 375 | 11.482 |
| HOB - 376 [-> SPIRE Cone] | 11.485 |
| HOB - 377 | 11.565 |
| HOB - 378 | 11.64 |
| HOB - 379 | 11.539 |
| HOB - 380 | 11.581 |
| HOB - 381 [-> SPIRE A-Frames] | 11.535 |
| L1 Strap IF #1 | 4.885 |
| L1 Strap IF #2 | 4.985 |
| HeII Tank | 1.65 |

Table 2-13 – Herschel Interface Temperature in Worse Case Spectrometer Mode

| SPIRE Temperature [K] (*) | Spectrometer Mode |
| --- | --- |
| Cold Tip (adjusted for self-heating on sensor) | 0.28 |
| PLW BDA Detector | 296 |
| PMW BDA Detector | 298 |
| PSW BDA Detector | 300 |
| SLW BDA Detector | 301 |
| SSW BDA Detector | 294 |
| Cooler Pump | 1.86 |
| Cooler Shunt | 1.66 |
| L0 Photometer Enclosure | 1.70 |
| L0 Spectrometer Enclosure | 1.68 |
| SOB | 5.4 |
| PJFET Chassis | 11.8 |
| SJFET Chassis | 13 |

(*) Mean temperature for enclosures

Table 2-14 - SPIRE Temperature in Worse Case Spectrometer Mode

Observations:

- All detectors are within the required 310mK absolute temperature.

## SPIRE Steady-State Average Performance during Mission

### Average Power Dissipation during Mission

The table below summarises the power dissipations for the SPIRE mechanisms, calibration source and electronic boxes, including their duty cycle for all operating modes during the mission lifetime.

| PACS Mode | - | - | ON Spectro | ON Photo | OFF | OFF | OFF | OFF | OFF |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| HIFI Mode | - | - | OFF | OFF | ON | OFF | OFF | OFF | OFF |
| SPIRE Mode | - | - | OFF | OFF | OFF | ON Photo | ON Spectro |
| BSM – POF8 – Calibration with PCAL | [mW] | 0.024 | 0 | 0 | 0 | 100% | 0.024 | 100% | 0.024 |
| SCAL2 at 80K | [mW] | 2.000 | 0 | 0 | 0 | 0% | 0 | 100% | 2.000 |
| Extra power component during SCAL dynamic switching | [mW] | 0.870 | 0 | 0 | 0 | 0% | 0 | 50% | 0.435 |
| SMEC Actuator – R10 | [mW] | 0.430 | 0 | 0 | 0 | 0% | 0 | 25% | 0.108 |
| SMEC Actuator – R100 | [mW] | 0.460 | 0 | 0 | 0 | 0% | 0 | 25% | 0.115 |
| SMEC Actuator – R1000 | [mW] | 3.560 | 0 | 0 | 0 | 0% | 0 | 50% | 1.780 |
| SMEC Encoder (Level 2) | [mW] | 1.200 | 0 | 0 | 0 | 0% | 0 | 100% | 1.200 |
| SMEC LVDT | [mW] | 0.112 | 0 | 0 | 0 | 0% | 0 | 100% | 0.112 |
| BSM Sensors | [mW] | 0.800 | 0 | 0 | 0 | 100% | 0.800 | 100% | 0.800 |
| BSM Motor – POF1 – Chopping (+/-63”) | [mW] | 0.548 | 0 | 0 | 0 | 25% | 0.137 | 0% | 0.000 |
| BSM Motor – POF2 – 7pt Jiggle Map | [mW] | 0.300 | 0 | 0 | 0 | 25% | 0.075 | 0% | 0.000 |
| BSM Motor – POF3 – 64pt Jiggle Map | [mW] | 1.550 | 0 | 0 | 0 | 25% | 0.388 | 50% | 0.775 |
| BSM Motor – POF5 – Scan | [mW] | 0.000 | 0 | 0 | 0 | 25% | 0.000 | 0% | 0.000 |
| Extra power component during BSM dynamic switching | [mW] | 0.250 | 0 | 0 | 0 | 100% | 0.250 | 50% | 0.125 |
| Total L1 Dissipation | [mW] | - | 0 | 0 | 0 | - | 1.674 | - | 7.474 |
| PJFET Dissipation | [mW] | 56.64 | 0 | 0 | 0 | 100% | 56.64 | 0% | 0 |
| SJFET Dissipation | [mW] | 15.17 | 0 | 0 | 0 | 0% | 0 | 100% | 15.17 |

Table 2-15 - Average SPIRE Dissipation during Mission

Observations:

- One can see that in this case the average power dissipation at L1 in photometer mode is 1.67mW versus 2.62mW for the worse case power dissipation.

- One can see that in this case the average power dissipation at L1 in spectrometer mode is 7.47mW versus 9.03mW for the worse case power dissipation.

### Average Heat Loads during Mission

| PACS Mode | - | ON Spectro | ON Photo | OFF | OFF | OFF |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| HIFI Mode | - | OFF | OFF | ON | OFF | OFF |  |  |  |
| SPIRE Mode | - | OFF | OFF | OFF | ON Photo | ON Spectro |  |  |  |
| Mission Duty Cycle | [%] | 16.65 | 16.65 | 33.3 | 16.65 | 16.65 | Mission Average | Reqt | Goal |
| L0 Evaporator Heat Load | [mW] | 0.62 | 0.37 | 0.48 | 0.44 | 0.53 | 0.49 | - | - |
| L0 Pump Heat Load | [mW] | 0.61 | 0.37 | 0.47 | 2.3 | 2.38 | 1.10 | 2 | 2 |
| L0 Enclosure Heat Load | [mW] | 1.00 | 0.59 | 0.78 | 0.7 | 0.86 | 0.79 | 4 | 1 |
| L1 PJFET Harness Parasitic | [mW] | 1.00 | 0.83 | 1.36 | 2.17 | 0.91 | - | - | - |
| L1 SJFET Harness Parasitic | [mW] | 0.18 | 0.15 | 0.24 | 0.29 | 0.21 | - | - | - |
| L1 Isolation Supports | [mW] | 7.89 | 6.3 | 11.01 | 7.97 | 6.66 | - | - | - |
| L1 Housekeeping Harness | [mW] | 1.38 | 1.4 | 1.85 | 1.62 | 2.42 | - | - | - |
| Radiation Load | [mW] | 3.65 | 3.58 | 3.76 | 3.64 | 3.65 | - | - | - |
| Total L1 Dissipation | [mW] | 0.00 | 0.00 | 0.00 | 1.67 | 7.47 | - | - | - |
| Total L1 Heat Load | [mW] | 11.84 | 10.62 | 16.45 | 16.75 | 20.91 | 15.5 | 15 | 13 |
| L3 PJFET Heat Load | [mW] | -0.04 | 0.12 | -0.318 | 41.96 | 0.48 | 6.98 | 50 | 50 |
| L3 SJFET Heat Load | [mW] | 0.06 | 0.08 | 0.033 | -5.34 | 12.63 | 1.25 | 25 | 25 |

Table 2-16 – Average SPIRE Heat Loads During Mission

Notes:

- Please note that the Herschel L0 HeII interface temperature is assumed to be at 1.65K.

- The results presented do not include any margin.

Observations:

- One can see that the SPIRE L1 heat load exceeds the 15mW requirement by 0.5mW.