# Introduction

This document reports the results of the execution of several instantiated AOTs during the PFM4 test campaign.

AOTs define the way in which the different types of SPIRE observations are implemented. They are defined using the Herschel Common Uplink System (CUS), which converts user input into a sequence of satellite and instrument commands with appropriate timing. These command sequences use both simple DRCU commands and Command Lists defined specifically for SPIRE observations. One purpose of these tests was to execute as many different AOT types as possible in order to determine if the command sequence and timing was correct, and to exercise the Command Lists used.

For each AOT tested the user inputs were taken from the relevant section of RD01 and the command sequence generated was executed by the instrument.

## Scope

The purpose of this test was

- To execute as many different instantiated AOT types as possible in order to confirm correct command sequencing and timing, and correct execution of command lists. (This was limited by both the number of AOTs defined at the time and the instrument operational modes previously verified)

- To generate data for testing the latest version of the SPIRE pipeline (version 0.5).

## Reference Documents

| Ref | Document | Name | Version/Issue No. |
| --- | --- | --- | --- |
| RD01 |  | SPIRE AOT Test Plan (SPIRE-RAL-DOC_002720) | Issue 1.0 |
| RD02 |  | SPIRE Instrument User Manual (SPIRE-RAL-PRJ-002395) | Issue 1.0 |

## Change Record

| Document | Change date | Changes |
| --- | --- | --- |
| Issue 1.0 | 01/03/07 | First Version |

# Table of Contents

1.	Introduction	1

1.1	Scope	1

1.2	Reference Documents	1

1.3	Change Record	1

2.	Summary of AOT Tests	3

2.1	Instrument Configuration	3

2.2	AOT Tests Summary	3

2.3	AOT Results	4

3.	Detailed Test Results	5

3.1	7-pnt Jiggle Mapping	5

3.1.1	Configuration	5

3.1.2	Test Case: ILT-OPS-POF2-Ca	5

3.1.3	Test Case: ILT-OPS-POF2-Da	5

3.2	Small Map	5

3.2.1	Configuration	5

3.2.2	Test Case: ILT-OPS-POF3-Aa	5

3.2.3	Test Case: ILT-OPS-POF3-Ab	6

3.2.4	Test Case: ILT-OPS-POF3-Ba	6

3.2.5	Test Case: ILT-OPS-POF3-Ca	6

3.3	Scan Mapping	6

3.3.1	Configuration	6

3.3.2	Test Case: ILT-OPS-POF5-Aa	6

3.3.3	Test Case: ILT-OPS-POF5-Ab	6

3.3.4	Test Case: ILT-OPS-POF5-Ac	7

3.3.5	Test Case: ILT-OPS-POF5-Ad	7

3.4	Spectrometer Point Source	7

3.4.1	Configuration	7

3.4.2	Test Case: ILT-OPS-SOF1-Aa	7

3.4.3	Test Case: ILT-OPS-SOF1-Ab	7

3.4.4	Test Case: ILT-OPS-SOF1-Ad	7

3.4.5	Test Case: ILT-OPS-SOF1-Ae	8

3.5	Spectrometer Map	8

3.5.1	Configuration	8

3.5.2	Test Case: ILT-OPS-SOF2-Ac	8

3.5.3	Test Case: ILT-OPS-SOF2-Bb	8

# Summary of AOT Tests

## Instrument Configuration

- All tests start with the instrument in the appropriate standby mode (PHOT_STBY or SPEC_STBY) see RD02.

- All observations have a PCAL flash at the beginning and end (some also have PCAL flashes within the operations)

## AOT Tests Summary

This table lists the AOTs carried out during POF4.

Highlighted tests have severe problems identified with them and should not be used for pipeline testing.

| OBSID | Test Case | Description |
| --- | --- | --- |
| 30011547 | ILT-OPS-POF2-Ca | Data for the ‘on’ part of the third PCAL flash in each cycle is missing. |
| 3001154A | ILT-OPS-POF3-Aa | COLLECT_GARBAGE cmd failed at start and all subsequent cmds failed |
| 300115AB | ILT-OPS-POF2-Ca | Only half a PCAL flash performed at each end of the test. At the end of the test, the BSM was seen to be along way from the nominal position in the chop direction. |
| 300115AC | ILT-OPS-POF2-Ca | Only half a PCAL flash performed at each end of the test. At the end of the test, the BSM was seen to be along way from the nominal position in the chop direction. |
| 300115B1 | ILT-OPS-POF2-Ca | At the end of the test, the BSM was seen to be along way from the nominal position in the chop direction. |
| 300115B5 | ILT-OPS-POF2-Ca | At the end of the test, the BSM was seen to be along way from the nominal position in the chop direction. Source was being moved during the observation |
| 30011626 | ILT-OPS-POF2-Ca | Jiggle Map with source on central pixel |
| 30011627 | ILT-OPS-POF3-Aa | Didn’t go to correct position s for 64 pnt map |
| 30011628 | ILT-OPS-POF5-Aa | Large Scan Map (7mins) |
| 30011647 | ILT-OPS-POF5-Aa | Large Scan Map (7mins) |
| 30011648 | ILT-OPS-POF5-Ab | Large Scan Map (21mins) |
| 30011649 | ILT-OPS-POF5-Ac | Large Scan Map (53mins) |
| 3001164A | ILT-OPS-POF5-Ad | Large Scan Map (255mins) – not known if successful – unable to read data into DP |
| 300116DC | ILT-OPS-SOF1-Aa | Wrong scan speed (0.0525mm/s instead of 0.525) |
| 300116DD | ILT-OPS-SOF1-Aa | Wrong scan speed (0.0525mm/s instead of 0.525). Scan end out of limit at 42.1 mm |
| 30011701 | ILT-OPS-POF2-Ca | Manual ‘nod’ of telescope position carried out at wrong time External chopper was on |
| 30011702 | ILT-OPS-POF2-Ca | Jiggle Map with source on central pixel |
| 300117FD | ILT-OPS-SOF1-Aa | Possibly no source |
| 300117FE | ILT-OPS-SOF1-Aa | Sparse High Res Spectrum, Laser on SSWD3, SCAL @ 67.90K |
| 300117FF | ILT-OPS-SOF1-Aa | Sparse High Res Spectrum, Laser on SSWD2, SCAL @ 67.90K |
| 30011800 | ILT-OPS-SOF1-Ad | Sparse Medium Res Spectrum No Source (HotBB warming up), SCAL @ 67.90K |
| 30011801 | ILT-OPS-SOF1-Ae | Sparse Low Res Spectrum No Source (HotBB warming up), SCAL @ 67.90K |
| 30011802 | ILT-OPS-SOF1-Ab | Sparse H+L Res Spectrum No Source (HotBB warming up), SCAL @ 67.90K |
| 30011803 | ILT-OPS- SOF2-Ac | BSM did not move during observation |
| 30011804 | ILT-OPS- SOF2-Bb | BSM did not move during observation |
| 3001180D | ILT-OPS-POF3-Aa | Map positions not correct |
| 300118E3 | ILT-OPS-POF2-Ca | Jiggle Map viewing ColdBB at 6.7k |
| 300118E5 | ILT-OPS-POF2-Ca | Viewing lab (HotBB switched on part way through test) |
| 300118E6 | ILT-OPS-POF2-Ca | Jiggle Map with source (HotBB) on central pixel |
| 300118E7 | ILT-OPS-POF2-Da | Jiggle Map with source (HotBB) offset from central pixel (~4” +y, +z) |
| 300118E8 | ILT-OPS-POF3-Aa | Small Map with central source (HotBB) (1’ beam) |
| 300118E9 | ILT-OPS-POF3-Ba | Small Map with offset source (HotBB) (1’ beam) |
| 300118EA | ILT-OPS-POF3-Ca | Small Map, viewing chopper, No source |
| 300118EB | ILT-OPS-POF3-Ab | Small Map with HotBB central source (0.4’ beam) |
| 300118FE | ILT-OPS-SOF1-Aa | Sparse High Res Spectrum, Signal saturated as SCAL not on |
| 30011900 | ILT-OPS-SOF1-Aa | Sparse High Res Spectrum, SCAL @80K |
| 30011901, | ILT-OPS- SOF2-Ac | Done with Sparse sampling |
| 30011902 | ILT-OPS- SOF2-Ac | BSM did not move |
| 30011904 | ILT-OPS- SOF2-Ac | Intermediate Medium Res Spectral Map |
| 30011905 | ILT-OPS- SOF2-Bb | Full Low Res Spectral Map |

## AOT Results

| Test Case | Result | SPRs Raised |
| --- | --- | --- |
| ILT-OPS-POF2-Ca | Completed Successfully |  |
| ILT-OPS-POF2-Da | Completed Successfully |  |
| ILT-OPS-POF3-Aa | Completed Successfully |  |
| ILT-OPS-POF3-Ab | Completed Successfully |  |
| ILT-OPS-POF3-Ba | Completed Successfully |  |
| ILT-OPS-POF3-Ca | Completed Successfully |  |
| ILT-OPS-POF5-Aa | Completed Successfully |  |
| ILT-OPS-POF5-Ab | Completed Successfully |  |
| ILT-OPS-POF5-Ac | Completed Successfully |  |
| ILT-OPS-SOF1-Aa | Completed Successfully |  |
| ILT-OPS-SOF1-Ab | Completed Successfully |  |
| ILT-OPS-SOF1-Ad | Completed Successfully |  |
| ILT-OPS-SOF1-Ae | Completed Successfully |  |
| LT-OPS- SOF2-Ac ILT-OPS- SOF2-Bb | No BSM data sampled during the AOTs. | SPR-0582 |

# Detailed Test Results

## 7-pnt Jiggle Mapping

### Configuration

- The instrument was placed into the PHOT_STBY mode before execution of the AOT

- In order to be able to simulate nodding of the Herschel telescope the movement time between on-source and nodding positions was increased to 3 mins to allow time for the operator to ‘move’ the input beam. This should have no affect on the data.

- For on-source BBs (Nod position A) the beam was centred on pixel PSWE8 and chopped between PSWE6 and PSWE10. For off-source BBs (Nod position B) the beam was centred on pixel PSWE12 and chopped between PSWE10 and PSWE14

### Test Case: ILT-OPS-POF2-Ca

| OBSID: | 30011626, 30011702, 300118E3, 300118E6 |
| --- | --- |
| Description: | 7-pnt jiggle with one complete jiggle cycle on-source and one at the nod position (i.e AB nodding) Source (Hot BB) is at the centre of the beam |
| Results: | Completed successfully |

### Test Case: ILT-OPS-POF2-Da

| OBSID: | 300118E7 |
| --- | --- |
| Description: | 7-pnt jiggle with one complete jiggle cycle on-source and one at the nod position (i.e AB nodding) Source (Hot BB) is offset from the centre of the beam by approximately 0.5 of the PMW beam size |
| Results: | Completed successfully |

## Small Map

### Configuration

- The instrument was placed into the PHOT_STBY mode before execution of the AOT

### Test Case: ILT-OPS-POF3-Aa

| OBSID: | 300118E8 |
| --- | --- |
| Description: | Small Map with 4 nod cycles. Source at centre of map |
| Results: | Completed successfully |

### Test Case: ILT-OPS-POF3-Ab

| OBSID: | 300118EB |
| --- | --- |
| Description: | Small Map with 4 nod cycles. Source at centre of map. Repeated 2 times |
| Results: | Completed successfully |

### Test Case: ILT-OPS-POF3-Ba

| OBSID: | 300118E9 |
| --- | --- |
| Description: | Small Map with 4 nod cycles. Source offset from centre of map |
| Results: | Completed successfully |

### Test Case: ILT-OPS-POF3-Ca

| OBSID: | 300118EA |
| --- | --- |
| Description: | Small Map with 4 nod cycles. No source |
| Results: | Completed successfully |

## Scan Mapping

### Configuration

- The instrument was placed into the PHOT_STBY mode before execution of the AOT

- No movement of the telescope simulator was made so no source is expected to be seen in the map

### Test Case: ILT-OPS-POF5-Aa

| OBSID: | 30011628, 30011647 |
| --- | --- |
| Description: | Scan Map: 10 arcmin x 10 arcmin, no source in beam 4 scan lines of length 10 armin |
| Results: | Completed successfully |

### Test Case: ILT-OPS-POF5-Ab

| OBSID: | 30011648 |
| --- | --- |
| Description: | Scan Map: 30 arcmin x 30 arcmin, no source 9 scan lines of length 30 arcmin |
| Results: | Completed successfully |

### Test Case: ILT-OPS-POF5-Ac

| OBSID: | 30011649 |
| --- | --- |
| Description: | Scan Map: 60 arcmin x 60 arcmin, no source 16 scan lines of length 60 arcmin |
| Results: | Completed successfully |

### Test Case: ILT-OPS-POF5-Ad

| OBSID: | 3001164A |
| --- | --- |
| Description: | Scan Map: 200 arcmin x 120 arcmin, no source 32 scan lines of length 200 arcmin |
| Results: | Completed successfully???? This test was carried out overnight. I have been unable to read the data using DP as the memory used is too great. |

## Spectrometer Point Source

### Configuration

- The instrument was placed into the SPEC_STBY mode before execution of the AOT

### Test Case: ILT-OPS-SOF1-Aa

| OBSID: | 300117FE, 300117FF, 30011900 |
| --- | --- |
| Description: | 4 High Resolution FTS scans of Hot BB |
| Results: | Completed successfully |

### Test Case: ILT-OPS-SOF1-Ab

| OBSID: | 30011802 |
| --- | --- |
| Description: | 4 High Resolution + 10 Low resolution FTS scans |
| Results: | Completed successfully |

### Test Case: ILT-OPS-SOF1-Ad

| OBSID: | 30011800 |
| --- | --- |
| Description: | 10 Medium Resolution FTS scans |
| Results: | Completed successfully |

### Test Case: ILT-OPS-SOF1-Ae

| OBSID: | 30011801 |
| --- | --- |
| Description: | 20 Low resolution FTS scans |
| Results: | Completed successfully |

## Spectrometer Map

### Configuration

- The instrument was placed into the SPEC_STBY mode before execution of the AOT

### Test Case: ILT-OPS-SOF2-Ac

| OBSID: | 30011904 |
| --- | --- |
| Description: | 4 Medium Resolution FTS scans with Intermediate spatial sampling |
| Results: | Completed successfully No BSM data sampled during the AOTs |

### Test Case: ILT-OPS-SOF2-Bb

| OBSID: | 30011905 |
| --- | --- |
| Description: | 4 Low Resolution FTS scans with Full spatial sampling |
| Results: | Completed successfully No BSM data sampled during the AOTs |