| Prepared by: |  |  |
| --- | --- | --- |
|  | Allan Dowell | Date 21-March-2007 |
| Checked: |  |  |
|  | Sunil Sidher | Date 21-March-2007 |

| Approval: |  |  |
| --- | --- | --- |
|  | Sunil Sidher | Date 21-March-2007 |

Distribution

| RAL | Steve Guest |
| --- | --- |
|  | Sunil Sidher |
|  | Eric Sawyer |
| EADS Astrium | Siegmund Idler |
|  | Nico Sonn |
|  | Markus Koelle |
| MPE (PACS) | Erich Wiezorrek |
| TERMA AS | Simon Hamer |
| Alcatel Alenia Space | Felix Chatte |
|  | Bernard Collaudin |
|  | Benoit Gobillot |
| ESA | Carsten Scharmberg |

| Host system | Windows 2000 SP2 |
| --- | --- |
| Word Processor | Microsoft Word 2000 SR1 |
| File |  |

# Document Change Record

| Date | Index | Affected Pages | Changes |
| --- | --- | --- | --- |
| 21-February-2007 | Draft 0.1 |  | First version emailed as word doc attachment without document number during AVM test at Astrium, Friedrichshafen. |
| 22-February-2007 | Draft 0.2 |  | Grounding step and procedure completion comment updated |
| 21-March-2007 | Issue 1.0 |  | Give email attachment a document number. |

# Contents

Contents	4

1	Scope of Document	5

2	Applicable Documents	5

3	ESD Safety	5

4	Set-Up Description	5

# Scope of Document

This procedure is relevant to the EGSE set-up at Astrium, Friedrichshafen on 21.02.07. The set-up of the DRCU Simulator to the AVM DPU is described.

# Applicable Documents

AD1 Astrium test procedure,  HP-2-ASED-TP-0142 Issue 1.0.

# ESD Safety

All relevant Astrium ESD Safety measures are to be taken when touching the DPU and it’s cables to the Spacecraft and later DRCU Simulator.

# Set-Up Description

- The AVM DPU is connected to the Spacecraft. (It has connectors labelled J1, J2, J3, J7, J8 and J9.)

- J1 is connected to the Spacecraft power and is not touched (or changed in any way).

- J2 and J3 are connected to the Spacecraft via Mil bus cables and are not touched (or changed in any way).

- The spacecraft needs to be switched off.

- The keyboard, mouse and monitor is attached to the DRCU Simulator PC whilst it is switched off.

- The DRCU Simulator PC and it’s monitor’s power supply cables are grounded using a MITU 4000 Isolating Transformer to avoid grounding loops.

- When confirmation is given by Astrium staff that the spacecraft is off, the following cables are altered.

- Cables to J7, J8 and J9 on the AVM DPU are removed.

- The connector J7 on the AVM DPU is connected to CH1 on the DRCU Simulator PC with the cable labelled CH1.

- The connector J8 on the AVM DPU is connected to CH2 on the DRCU Simulator PC with the cable labelled CH2.

- The connector J9 on the AVM DPU is connected to CH3 on the DRCU Simulator PC with the cable labelled CH3.

- The DRCU Simulator PC is switched on. The user is administrator and there is no password.

- The Spacecraft is switched on.

Note: The DRCU Simulator PC is left on but the file transmit.exe on the desktop is run only at the applicable step in Astrium test procedure HP-2-ASED-TP-0142 Issue 1 (AD1).

End of Set-up procedure.

Test procedure completed 22.02.2007 at ~10:00.