# Introduction

AOTs define the way in which the different types of SPIRE observations are implemented. They are defined using the Herschel Common Uplink System (CUS), which converts user input into a sequence of satellite and instrument commands with appropriate timing. These command sequences use both simple DRCU commands and Command Lists defined specifically for SPIRE observations. One purpose of these tests was to execute as many different AOT types as possible in order to determine if the command sequence and timing was correct, and to exercise the Command Lists used..

For each AOT tested the user inputs were taken from the relevant section of RD01 and the command sequence generated was executed by the instrument.

## Scope

The purpose of this document is to record the current status of the AOT testing at the conclusion of the FM Instrument-Level Test programme. Subsequent testing will continue with

- Integrated System Tests  - the Reference Mission Scenario will execute a set of nominal observations

- FS Instrument-Level Test Programme

- FS additional cooldowns

- AVM Tests

## Reference Documents

| Ref | Document | Name | Version/Issue No. |
| --- | --- | --- | --- |
| RD01 | SPIRE AOT Test Plan | SPIRE-RAL-DOC-002720 | Issue 1.0 |
| RD02 | PFM3 AOT Test Report | SPIRE-RAL-REP-002719 | Issue 1.0 |
| RD03 | PFM4 AOT Test Report | SPIRE-RAL-REP-002844 | Issue 1.1 |

## Change Record

| Document | Change date | Changes |
| --- | --- | --- |
| Issue 1.0 | 26/09/07 | First Version |

# Summary of AOT Test Status

| AOT | Operating Mode | Status | Outstanding SPRs | Comments |
| --- | --- | --- | --- | --- |
| Point Source Photometry | POF1 (Chopping) | Not Tested |  | Non-baseline mode |
|  | POF2 (7 point Jiggle map No nodding) | Not Tested |  | Non-baseline mode |
|  | POF2 (7 point Jiggle map Nodding) | Successful |  | Multiple integrations not tested |
| Small Map Photometry | POF3 | Successful |  |  |
| Large Map Photometry | POF4 | Not Tested |  | Non-baseline mode |
|  | POF5 | Successful |  | Restricted to no-source observations |
| Spectroscopy Single Pointing | SOF1 (sparse spatial sampling) | Successful |  |  |
|  | SOF2 (int/full spatial sampling) | Successful | SPR-0582 | No BSM data generated |
|  | SOF3 (sparse spatial sampling) | Not Tested |  | Non-baseline mode |
|  | SOF4 (int/full spatial sampling) | Not Tested |  | Non-baseline mode |
| Spectroscopy Raster Map | SOF1 (sparse spatial sampling) | Not Tested |  | Cannot control telescope movement |
|  | SOF2 (int/full spatial sampling) | Not Tested |  | Cannot control telescope movement |
|  | SOF3 (sparse spatial sampling) | Not Tested |  | Non-baseline mode |
|  | SOF4 (int/full spatial sampling) | Not Tested |  | Non-baseline mode |