| Title: | Herschel IST Test Case 'Test of Instrument FDIR OBCP' |
| --- | --- |
| CI-No: |  |  |
| Prepared by: | Functional Team | Date: | 13.12.2007 |
| Checked by: | M. Koelle |  |  |
| Product Assurance: | R. Stritter |  |  |
| Configuration Control: | W. Wietbrock |  |  |
| Project Management: | Dr. Fricke |  |  |
| Distribution: | See Distribution List (last page) |  |
|  | Copying of this document, and giving it to others and the use or communication of the contents there-of, are forbidden without express authority. Offenders are liable to the payment of damages. All rights are reserved in the event of the grant of a patent or the registration of a utility model or design. |  |

| Issue | Date | Sheet | Description of Change | Release |
| --- | --- | --- | --- | --- |
| 1 | 13.12.2007 |  | Initial version |  |

# Table of Content

1	Scope	6

1.1	Objective	6

1.2	Operational Flow	6

2	Documents/Drawings	17

2.1	Applicable Documents	17

2.2	Reference Documents	17

2.3	Other Documents	18

2.4	Acronyms	18

3	Requirements to be verified	19

4	Configuration	20

4.1	Herschel S/C Configuration	20

4.1.1	Hardware Configuration	20

4.1.2	Software Configuration	20

4.1.3	Test Configuration	20

4.1.4	Simulated Equipments	20

4.2	Set-up	20

5	Conditions	21

5.1	Personnel	21

5.2	Environmental	21

5.3	General Precautions and Safety	21

5.3.1	General Safety Requirements, Precautions	21

5.3.2	ESD constraints	21

5.3.3	Special QA Requirements	21

5.4	GSE	21

5.4.1	MGSE	21

5.4.2	CVSE	22

5.4.3	EGSE	22

5.4.4	OGSE	22

5.4.5	Special Equipment	22

6	Verification Requirements and Test Criteria	23

7	Test Execution Step-by-Step Procedure	24

7.1	S/C Initialization	24

7.2	Test Specific Initialization	25

7.3	HIFI	35

7.4	PACS	43

7.5	SPIRE	62

7.6	Specific Post-Test Activities	79

7.7	S/C Power OFF	82

8	ANNEX	83

8.1	Master Tcl script	83

8.2	HIFI Tcl script	92

8.3	PACS Tcl script	99

8.4	SPIRE Tcl script	116

9	Summary Sheets	129

9.1	Procedure Variation Summary	129

9.2	Non Conformance Report (NCR) Summary	130

9.3	Sign-off Sheet	131

# List of Tables

Table 9.1-1: Procedure Variation Sheet	129

Table 9.2-1: Non-Conformance Record Sheet	130

# Scope

## Objective

This Procedure represents the instruments FDIR part of the S/C IST Test in the debugging phase. In the formal run, this simulates the triggering of some specific FDIR actions during the operation day of each of the three instruments after S/C turn ON and initialisation at RMS start date. During debugging it has been decided to keep the date of the CCS to the current UTC and compact the three instruments during only one session.

After successful debugging, this procedure will be integrated into the overall S/C IST Test Procedure.

According to the IST specifications, the following OBCPs will be tested:

| HIFI OBCP (refer to chapter 7.3) | APID | TM | Event ID | type | Comment |
| --- | --- | --- | --- | --- | --- |
| DB_OBCP_H_HIFI_RESET | 16 | 5,x | 151 | DLL FDIR |  |

| PACS OBCPs (refer to chapter 7.4) | APID | TM | Event ID | type | Comment |
| --- | --- | --- | --- | --- | --- |
| DB_OBCP_H_PACS_ SAFE | 1152/1153 | 5,2 | 4 |  | Done in instrument commissioning See PACS-ME-TP-021 §11,1,3 (autonomous SAFE) |
| DB_OBCP_H_PACS_BOLC_OFF | 1152/1153 | 5,2 | 5 |  | To be tested with start command [no TC available to generate TM(5,2)] |
| DB_OBCP_H_PACS_POWER_CYCLE | 1152/1153 | 5,2 | 6 |  | To be tested with start command [no TC available to generate TM(5,2)] |
| DB_OBCP_H_PACS_NORMAL_OFF | 1152/1153 | 5,2 | 25 |  | TFL done in instr. commissioning See TP-021 §11,1.4 (autonomous OFF mode HK loss) |
| DB_OBCP_H_PACS_IMMEDIATE_OFF | 16 | 5,x | 153 ( replaced by 186 | DLL FDIR ( replaced by TFL TM FDIR | TFL done in instr. commissioning See TP-021 §11,1.6 (autonomous OFF modeHK loss) |

| SPIRE OBCPs (refer to chapter 7.5) | APID | TM | Event ID | type | Comment |
| --- | --- | --- | --- | --- | --- |
| DB_OBCP_H_SPIRE_DRCU_OFF | 1280/1281 | 5,2 | xC000 | Test TC allow stimulation | Not before end of Nov 2007 |
| DB_OBCP_H_SPIRE_OPE_STOP | 1280/1281 | 5,2 | xC100 | Test TC allow stimulation | Not before end of Nov 2007 |
| DB_OBCP_H_SPIRE_OPE_RESUME | 1280/1281 | 5,2 | xC110 | Test TC allow stimulation | Not before end of Nov 2007 |
| DB_OBCP_H_SPIRE_OFF | 16 | 5,x | 152 | DLL FDIR |  |
| DB_OBCP_H_SPIRE_OFF_CTRL | 16 | 5,x | 185 | TFL TM FDIR |  |

## Operational Flow

The overall flow of the Instruments FDIR is providedin the schemas of the following pages.

DB_OBCP_H_HIFI_RESET

DB_OBCP_H_PACS_SAFE (script in warm TBC)

DB_OBCP_H_PACS_POWER_CYCLE (OBCP Start TC)

DB_OBCP_H_PACS_BOLC _OFF (OBCP Start TC)

DB_OBCP_H_PACS_NORMAL_OFF (script in warm TBC)

DB_OBCP_H_PACS_IMMEDIATE _OFF (TFL)

DB_OBCP_H_ SPIRE _OPE_STOP (OBCP start TC)

DB_OBCP_H_SPIRE _OPE_RESUME (OBCP Start TC)

DB_OBCP_H_ SPIRE _DRCU_OFF (OBCP Start TC)

DB_OBCP_H_ SPIRE _OFF_CTRL (TFL)

DB_OBCP_H_ SPIRE _OFF (DLL)

Alternatively:

Send TC with

TCID=C3ST

Short description=Obcp_1103_SPI_ST

TC=start(18,3)

Parameters needed:

1(DID_OBCP_32_OFFSET_000):SPIRE_SUBS_ID_CMD (370 by default)

2(DID_OBCP_32_OFFSET_001):SPIRE_SUBS_ID_META (100 by default)

Note:

The detailed step-by-step test procedure is provided in chapter 7.

# Documents/Drawings

This document incorporates, by dated or undated references, provisions from other publications. These normative references are cited at appropriate places in the text and publications are listed hereafter. For dated references, subsequent amendments to or revisions of any of these apply to this document only when incorporated into it by amendment or revision. For undated references, the latest edition of the publication referred to apply.

## Applicable Documents

| AD-1 | Herschel Integrated Satellite Test Specification H-P-2-ASP-SP-0939, Issue 4 |
| --- | --- |
| AD-2 | S/C I.S.T. Routine Mission Scenario – Operation day framework ASP-06-AIT-AVIO-PL-008030, Issue 2 |
| AD-3 | Test Specification for Herschel Instruments AVM and FM Tests performed at Satellite Level HP-2-ASP-TS-1083_1_0 |
| AD-4 | Leading Procedure for Herschel Integrated Satellite Test 'IST' HP-2-ASED-TP-0134 |

## Reference Documents

| RD-1 | Herschel SVM User Manual H-P-MA-AI-0001 |
| --- | --- |
| RD-2 | Reference Mission Scenario, Herschel / Planck project SCI-PT / 12759, Issue 3.1, 06/08/2004 |
| RD-3 | Herschel/Planck List of Acronyms H-P-ASP-LI-0077 |
| RD-4 | Herschel Instruments power ON-OFF and Mode Switching Procedure for functional Testing HP-2-ASED-TP-0206 issue 1. |

## Other Documents

None

## Acronyms

Acronyms are specified in RD-3 and are therefore not listed in this document.

# Requirements to be verified

The requirements of AD-1, chapter 5.8.13 "TEST OF INSTRUMENT FDIR", are to be verified.

# Configuration

## Herschel S/C Configuration

Refer to AD-4

### Hardware Configuration

Refer to AD-4

### Software Configuration

Refer to AD-4

### Test Configuration

Refer to AD-4

### Simulated Equipments

Refer to AD-4

## Set-up

Refer to AD-4

# Conditions

## Personnel

Refer to AD-4

## Environmental

Refer to AD-4

## General Precautions and Safety

Refer to AD-4

### General Safety Requirements, Precautions

Refer to AD-4

### ESD constraints

Refer to AD-4

### Special QA Requirements

Refer to AD-4

## GSE

Refer to AD-4

### MGSE

Refer to AD-4

### CVSE

Refer to AD-4

### EGSE

#### EGSE Hardware Configuration

Refer to AD-4

#### EGSE User Software

Refer to AD-4

#### Grounding Configuration

Refer to AD-4

#### Test Equipment

Refer to AD-4

#### Data Acquisition System

Refer to AD-4

### OGSE

Refer to AD-4

### Special Equipment

Refer to AD-4

# Verification Requirements and Test Criteria

PASS/FAIL CRITERIA

At each test stage completion, the test success is determined comparing the results obtained against the expected values.

If the compliance between obtained and expected values has been met, and authorisation to proceed with the next stage of the test is given, then the actual test stage must be considered satisfactory completed.

The success of the overall testing activities is determined from the satisfactory completion of all test stages.

Successful criteria to be satisfied in each test stage shall be:

- Test conditions according to specification requirement;

- Complete verification of the requirement aspects according to the test specification [AD-1];

- Fulfilment of test results with respect to required data;

- Verification that all the TM parameters used to monitor the SVM do not exceed the limit thresholds loaded in the HPSDB (OOL display);

- Verification that the TM(5,2), TM(5,4) and TM(1,8) received event reports are only those ones expected to fulfil the pass test criteria.

# Test Execution Step-by-Step Procedure

## S/C Initialization

Follow the steps in the power ON procedure of AD-4, selecting the Test Case Instruments FDIR (5.8.13).

If the test case is run after the CDMS management (5.8.7):

- on the master GUI, select Test Case Instruments FDIR (5.8.13)

- SKIP the IST_START

- Call the master Z010999MCVT131_IST_INSTR_FDIR

NOTE: In this sequence, SKIP the step “Configure for Instrument FDIR test”

If the test case is run stand-alone (e.g. during debugging),:

- on the master GUI, select Test Case Instruments FDIR (5.8.13)

- PERFORM the IST_START (during debugging SKIP steps for ACMS on)

- Call the master Z010999MCVT131_IST_INSTR_FDIR

NOTE: In this sequence, PERFORM the step “Configure for Instrument FDIR test”

## Test Specific Initialization

| Step nr. | Test-Step-Description | Nominal Value | Tolerance | Actual Value | Remarks | P | N |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | In the CCS Test Console Callasync Z010999MCVT131_IST_INSTR_FDIR.tcl |  |  |  |  |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR.tcl START HERSCHEL INSTRUMENTS FDIR, SECTION 5.8.13 Click button YES to proceed |  |  |  |  |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR.tcl Configure for Instruments FDIR test? (SKIP if S/C already on and configured by CDMS MGMNT“ Click button YES to proceed |  |  |  |  |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR "CDMS setting for separation" Click the button Confirm to proceed |  |  |  |  |  |  |
|  | During … D103159SCVT138_IST_LAUNCH_SUNACQ Wait, go to script …ACMS_CONFIG25 and enter option 2 |  |  |  | Pending SEPARATION to be executed from … ACMS_CONFIG25 |  |  |
|  | During A102109SPVT103_ACMS_CONFIG25 (1,6,4,5,20,99,88) SEPARATION (open separation straps) Main Menu 3.0: option 2 Click the button OK Click the button Continue |  |  |  |  |  |  |
|  | During Z010999MCVT089_ACMS_SAM_MON Do you want to continue to monitor SAM Sun Pointing mode? Enter your choice: no |  |  |  |  |  |  |
|  | During Z010999MCVT089_IST_LAUNCH_SUNACQ IF TM error occurs Click the button Retry to proceed |  |  |  | error happens only sometimes |  |  |
|  | At end of Z010999MCVT089_IST_LAUNCH_SUNACQ Click the button “End TS!” to proceed |  |  |  |  |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR Transition to Nominal Click the button Confirm to proceed |  |  |  |  |  |  |
|  | During Z010999MCVT089_SUNACQ_NOMINAL Click the button “End TS!” to proceed |  |  |  |  |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR At the prompt "Command ACMS (via OCM/Earth) to SCM/Earth" Press "OK" to proceed |  |  |  | If you wish to keep the ACMS off, send manually the command "XXXX" to open the straps and jump to step xxx. |  |  |
|  | During A102109SPVT103_ACMS_CONFIG25 Select Transition to OCM. Main Menu 4.0 SAM Phase: Option 6 Click the button OK to proceed Click the button Continue to proceed |  |  |  |  |  |  |
|  | During A102109SPVT036_ACMS_STR_ON Do you want to change the current STR in use ?: Answer no Click the button OK to proceed |  |  |  |  |  |  |
|  | During A102109SPVT043_TRANSITION_TO_OCM Only for info: Verify after ca.7 min if ACMS mode is = OCM point fine (Earth pointing) Verify in AND: ZAA00999 if Est Attitude Q1..Q4 is close to Cur Target Q1/Q3 = 0, Q2=0.6 / Q4= 0.79 Verify AESM3002 = OCM point fine or in synoptic SAT – ACMS – ACC – Mode Nominal |  |  |  |  |  |  |
|  | During A102109SPVT043_TRANSITION_TO_OCM SUSPEND click on script name in Test Console Click the button RESUME to proceed |  |  |  | FCV duty cycle fail |  |  |
|  | During A102109SPVT103_ACMS_CONFIG25 Select Transition to SCM (Science mode). Main Menu 7.0: Option 3 Click the button OK to proceed Click the button Continue to proceed |  |  |  |  |  |  |
|  | During A102109SPVT038_RWL_ON "Do you want to change actual on-board wheel set selected in the nominal configuration? RWL 1-2-4 selected, RWL-3 not selected" Click the button NO to proceed ? |  |  |  |  |  |  |
|  | During A102109SPVT042_RWL_SPINUP "Change actual Angular Momentum (initial values)?" Option: no Wait for ca. 10 min |  |  |  |  |  |  |
|  | Only for info: Verify RWL speed in plotting window 1. Select REALTIME => DESKTOP => MONITORING => TM Plotting Tool 2. Select Directory: Home/heracms/plotting 3. Select FILE => LOAD => 15 (RWLs_REAL(cal)&Simul_SPEED.txt) |  |  |  |  |  |  |
|  | Only for info: Verify 4x RWL momentum parameters AEWMA002 = 11.0 (RWL1 momentum) AEWMB002 = - 9.4 (RWL2 momentum) AEWMC002 = 0.0 (RWL3 momentum) AEWMD002 = - 8.5 (RWL4 momentum) Verify in SAT synoptic SAT – ACMS – ACC – Mode Nominal = SCM Point Fine Verify in Telemetry window ZAAF0999 (diagnostic TM) As long as the ACMS is switched On the Menu Box has to be present !!! |  |  |  |  |  |  |
|  | At end of A102109SPVT103_ACMS_CONFIG25 Click the button “End TS!” to proceed |  |  |  |  |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR "Transition from SAS 900W and BS 24V to SAS 1475W and BS full charged" Click the button Confirm to proceed |  |  |  |  |  |  |

During

Z010999MCVT131_IST_INSTR_FDIR

| "Switch on SREM and start acquisition service" Click the YES Confirm |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | During A102109SPVT103_ACMS_CONFIG25 Initial S/C status check (acc. table in 5.8.3.4) except for: SCBP = 5, ACMS mode = SAM, STRs & RWs = OFF !!! Click the button Confirm |  |  |  | Could be done earlier, as asynchronous |  |  |
|  | During A102109SPVT103_ACMS_CONFIG25 Click the YES to Confirm |  |  |  | Could be done earlier, as asynchronous |  |  |
|  | At end of A102109SPVT103_ACMS_CONFIG25 Click the button “End TS!” to proceed |  |  |  | Could be done earlier, as asynchronous |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR "POWER ON HIFI PRIMARY" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR "POWER ON PACS PRIMARY" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR "POWER ON SPIRE PRIMARY" Click the YES Confirm |  |  |  |  |  |  |

During

Z010999MCVT131_IST_INSTR_FDIR

| "SAVING ORIGINAL SCBP" Click the YES Confirm |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | During Z010999MCVT131_IST_INSTR_FDIR "UPLOAD OBCP and EAT for PRIMARY" Click the YES Confirm |  |  |  | Open NCR's for the OBCP and Event Action Table upload: - HP-460000-ASED-NC-3835 |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR "Please upload only the EAT entries for PRIMARY" Click the OK to Confirm | (only primary EAT entries work for now) |  |  |  |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR "Clear MTL and start ON BOARD SCHEDULING?" to proceed Click YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR “Check actual deletion of MTL content” Press OK to continue |  |  |  |  |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR “Check that at subschedules from 1 to 256, plus the 370 are enabled” Press OK to continue |  |  |  |  |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR "Start the instrument specific FDIR sequence”” Callasync the specific instrument FDIR sequence from test console and at the end of it click OK. |  |  |  | For HIFI continue from chapter 7.3 For PACS 7.4 For SPIRE 7.5 Also one after the other. |  |  |
|  | During D102159SCVT192_GET_EAT_REPORT "???????????”” |  |  |  |  |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR "Check that all EATs are enabled” Perform activity and then press OK |  |  |  |  |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR "Start up instrument specific sequence and Select OK to switch off” Call the specific instrument FDIR sequence and at the end of it click OK. |  |  |  |  |  |  |

## HIFI

| Step-No. | Test-Step-Description | Nominal Value | Tolerance | Actual Value | Remarks | P | N |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Callasync Z010999MCVT134_IST_HIFI_FDIR to perform the HIFI related part of the Instruments FDIR IST |  |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "Perform HIFI FDIR PRIMARY?" Click the YES to Confirm |  |  |  | If NO, it exits script |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "Please check that all instruments are in standby. If not put them in standby" Click the YES Confirm |  |  |  | RD-4 for details. |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "INITIAL S/C STATUS CHECK" Click the YES Confirm | 5.8.13 |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "Set SCBP to HIFI Prime (2)" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "upload dummy MTL with HIFI connection test in subschedule 70" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR “Check that the MTL contains one HC176289 (HIFI_connection_test) every 5 minutes for 10 hours in subshcedule 70" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "Check that subschedule 60 (meta-HIFI) is disabled and 70 (HIFI TCs) is ena bled, then press OK" Perform activitythen press OK |  |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "Wait for execution of the first command, then press OK" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "Put HIFI Primary in science mode" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "Insert call to science mode sequence" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "Perform HIFI RESET OBCP (DLL)?" Click the YES Confirm | If skipped goes to 60. |  |  | According to E-mail from Simon Hamer on 5.12.2007 to noam.lebonnois@external.thalesaleniaspace.com the 1 second wait between switching off/on HIFI ICU is too short. SRON requires 4 minutes and 20 seconds. This might be a blocking problem (NCR is not yet raised). |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "HIFI RESET DLL FDIR triggering" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "start the HIFI (RT 16) simulation on the CDMU SCOE to create jamming" Press OK |  |  |  |  |  |  |
|  | On CDMS SCOE Double-click on the link “StartSCOE.bat” on the desktopto start CDMU SCOE application. |  |  |  |  |  |  |
|  | On CDMS SCOE Select Menu: Mode( Local Mode Password: H-P |  |  |  |  |  |  |
|  | On CDMS SCOE Select from menu: Setup(RTSim Configuration |  |  |  |  |  |  |
|  | On CDMS SCOE Select file: R:\(192.168.90.32)\Herschel.rtc And press OK |  |  |  |  |  |  |
|  | On CDMS SCOE Select from menu: Mode( On Line |  |  |  |  |  |  |
|  | On CDMS SCOE Select from menu: Control(TM Generation |  |  |  |  |  |  |
|  | On CDMS SCOE In TM Generation tab press button “Load List” Then browse to: Herschel_PACS_BURST_5_7_2007.pkt |  |  |  |  |  |  |
|  | On CDMS SCOE In window: “RT TM Generation Control” Delete PACS and SPIRE Select “Continuous Run” in Run Specifications frame Select “Sequence Count”, “SCET”,”CRC” in Automatic Packet Updates Confirm the dialog box, to recalculate the packet |  |  |  |  |  |  |
|  | On CDMS SCOE In window: “RT TM Generation Control” Check that the generation time is fixed to 50/30 ms (check 25 with Piero) |  |  |  |  |  |  |
|  | On CDMS SCOE In window: “System Control/RT controls” Press the Enable button for: control TM queue TC queue Burst mode |  |  |  |  |  |  |
|  | On CDMS SCOE In window: “RT TM Generation Control” Press “Run” |  |  |  | Check that in marter log windows there are not too many errors. Otherwise press “Stop” and reconfigure the generation time to a higher value. |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "Please press OK when CDMU SCOE has been configured for jamming" Press OK |  |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "check that OBCP HIFI_RESET has been triggered (e.g. events, commands directed to HIFI are being sent and HIFI is going off)" Perform activity then press OK | Check for TM(5,4) with Event ID = 0x3001, SID = 0 Check for TM(5,4) with Event ID = 0x3002, SID = 0 OR Event ID = 0x3000, SID = 0 |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "Wait until the end of the OBCP, when HIFI is OFF" Click the YES Confirm | Event TM(5,1,107) OBCP Ended with ProcedureID 0x130D |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "RECOVERY ACTION" Click the YES to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "please check that HIFI is OFF and INVALID and no HK is being received" Perform activity and press OK Confirm | WM52K565 = OFF WM52D565 = OFF |  |  | LCL64 1 and 2 |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "please check that the MTL commands of the subschedule 70 have been disabled" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "please check subschedules 60 and 70 have been disabled" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "Stop the simulation on the CDMU scoe and set the scoe OFF LINE" Press OK |  |  |  |  |  |  |
|  | On CDMS SCOE In window: “RT TM Generation Control” Press “Stop” |  |  |  | . |  |  |
|  | On CDMS SCOE Select from menu: Mode( Off Line |  |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "End of HIFI RESET OBCP (DLL)" "check that all EATs are enabled" Perform activity and press OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "RESET starting conditions" Click the YES to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR “Check actual deletion of MTL content” Press OK to continue |  |  |  |  |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR “Check that at subschedules from 1 to 256, plus the 370 are enabled” Press OK to continue |  |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "Please clear the MTL" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT134_IST_HIFI_FDIR "check that all EATs are enabled" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | At end of Z010999MCVT134_IST_HIFI_FDIR Click the button "End TS!" to proceed |  |  |  |  |  |  |

## PACS

| Step-No. | Test-Step-Description | Nominal Value | Tolerance | Actual Value | Remarks | P | N |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Call Z010999MCVT135_IST_PACS_FDIR to perform the PACS related part of the Instruments FDIR IST |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "PERFORM PACS FDIR TEST (PRIMARY)?" Click the YES Confirm | If NO, exits script |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Please check that all instruments are in standby. If not put them in standby" Click the YES Confirm RD-4 for details. |  |  |  | RD-4 for details. |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "INITIAL S/C STATUS CHECK" Click the YES Confirm | 5.8.13 |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Set SCBP to PACS Prime (4)" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "upload dummy MTL with PACS connection test in subschedule 90" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR “Check that the MTL contains one PC023280 (DPU_TEST_CONN) every 5 minutes for 10 hours in subshcedule 90" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Check that subschedule 80 (meta-PACS) is disabled and 90 (PACS TCs) is ena bled, then press OK" Perform activitythen press OK |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Wait for execution of the first command, then press OK" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Insert call to PACS PING MTL upload" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Wait for execution of the first command, then press OK" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Set SCBP to PACS Prime (4)" Click the YES Confirm |  |  |  |  |  |  |
|  | Z010999MCVT135_IST_PACS_FDIR "INITIAL S/C STATUS CHECK" Click the YES Confirm | 5.8.13.7 |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Put PACS in SCIENCE" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "TEST the PACS SAFE FDIR?" Click the YES Confirm | If skipped goes to step 100. |  |  | Open NCR's for the PACS SAFE OBCP: NC-3510 NC-3780 |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Execute PACS SCRIPT FOR AUTONOMY FUNCTION 14?" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Filter a TMPKT history for TM(5,2) and one for TM(5,1)" Check script name and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Executing in parallel script PACS_StartAutonomy_Function_14_OBS_Shell.tcl" Check script name and press OK Confirm | If not correct Abort test sequence |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "check that PACS is sending 3 event packets TM(5,2) -cooler recycling temp expired" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "check that OBCP PACS_SAFE has been triggered – TM(5,1) with SPID 40148170 prodID 0x1208" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "check that CDMU reacts as in SAFE MODE transition" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "check that BOL_T_FPU is disabled again" Perform activity and press OK Confirm | PM165380 (DP_EV_BOL_T_FPU) = Disabled |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Wait until the end of the OBCP TM(5,1) with SPID 40145170 procID 0x1208“ Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "please check that PACS is in SAFE mode and that its MTL commands have been disabled" Perform activity and press OK Confirm | P380402380 (TM RATE) = SAFE |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "RECOVERY ACTION" Press YES to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "If still running, please terminate the sequence that keeps PACS in SCIENCE" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Check that subschedule 80 (meta-PACS) is disabled and 90 (PACS TCs) is ena bled, then press OK" Perform activitythen press OK |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "End of PACS SAFE OBCP TEST" "check that all EATs are enabled" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "TEST the PACS POWER CYCLE OBCP?" Click the YES Confirm | If NO, it jumps to step 99. |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "TRIGGER OBCP WITH START TC" Click the YES Confirm |  |  |  |  |  |  |
|  | Z010999MCVT135_IST_PACS_FDIR "Filter a TMPKT history for TM(5,1)" Check script name and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "sending EGSE_tcsend_CEV DCAST185 { DPV32185 90 } { DPV32185 0}" Perform activity and press OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "check that OBCP PACS_POWER_CYCLE has been triggered– TM(5,1) with SPID 40148170 procID 0x120A" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR " Wait until the end of the OBCP TM(5,1) with SPID 40145170 procID 0x120A" Perform activity and then Press OK (there will be another wait of 5 mins for safety) |  |  |  | Check for TM(5,4) with Event ID = 0x2001, SID = 0 (as a result of the called-up "PACS normal off" OBCP) Check for TM(5,4) with Event ID = 0x2000, SID = 0 (as a result of the called-up "PACS normal off" OBCP) Check for TM(5,4) with Event ID = 0x2002, SID = 0 |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "please check that PACS is in SAFE mode and that its MTL commands have been disabled" Perform activity and press OK Confirm | P380402380 (TM RATE) = SAFE |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "RECOVERY ACTION" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "if still running, please terminate the sequence that keeps PACS in SCIENCE" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Check that subschedule 80 (meta-PACS) is disabled and 90 (PACS TCs) is ena bled, then press OK" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "End of PACS POWER CYCLE TEST. check that all EATs are enabled" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "TEST PACS BOLC OFF OBCP?" Click the YES Confirm | If No, it jumps to step 110. |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "TRIGGER OBCP WITH START TC" Click YES Confirm |  |  |  |  |  |  |
|  | Z010999MCVT135_IST_PACS_FDIR "Filter a TMPKT history for TM(5,1)" Check script name and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Sending EGSE_tcsend_CEV DC9ST185 { DPV32185 90 }" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "check that OBCP PACS BOLC OFF has been triggered– TM(5,1) with SPID 40148170 proID 0x1209 " Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR " Wait until the end of the OBCP TM(5,1) with SPID 40145170 procID 0x1209" Perform activity and then Press OK | DEL54171 (PacsBolc1FunctSt) = OFF P380402380 (TM RATE) = SAFE |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "RECOVERY ACTION" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "please check that PACS is in SAFE mode and that its MTL commands have been disabled" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "if still running, please terminate the sequence that keeps PACS in SCIENCE" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Check that subschedule 80 (meta-PACS) is disabled and 90 (PACS TCs) is ena bled, then press OK" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Please run in parallel the sequence to put PACS in SCIENCE for 1h" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "End of PACS BOLC OFF TEST check that all EATs are enabled" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "PACS NORMAL OFF OBCP" Click the YES Confirm | If NO, it jumps to step 123. |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Execute PACS SCRIPT FOR AUTONOMY FUNCTION 17?" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Calling script PACS_StartAutonomy_Function_17_OBS_Shell.tcl" Perform activity and press OK to Confirm | If script is not correct abort test sequence. |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "check that OBCP PACS_NORMAL_OFF has been triggered" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "check that PACS is sending event packets TM(5,2) - BOLC power violated" Perform activity and press OK Confirm | Check for TM(5,4) with Event ID = 0x2001, SID = 0 Check for TM(5,4) with Event ID = 0x2000, SID = 0 |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "check that CDMU reacts as in OFF MODE transition" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Wait until the end of the OBCP (PACS OFF mode and MTL TCs disabled)" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "RECOVERY ACTION" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Check that PACS is OFF and MTL TCs are disabled" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "If still running, please terminate the sequence to keep PACS in SCIENCE" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Please check that only the PACS TCs Release is enabled!" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Please run in parallel the sequence to put PACS in SCIENCE for 1h" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "End of PACS NORMAL OFF TEST. Check that all EATs are enabled" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "PACS IMMEDIATE OFF OBCP?" Click the YES Confirm | If skipped it jumps to step Error! Reference source not found. |  |  | Open NCR's for the PACS IMMEDIATE OFF OBCP: HP-130000-ASED-NC-3509 |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Execute PACS script for clearing HK (warm TBC)?" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Calling script PACS_Disable_HK_OBS_Shell.tcl" Perform activity and press OK Confirm | If it is not the correct script, abort test sequence |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "check that OBCP PACS IMMEDIATE OFF has been triggered" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "check that PACS is sending no regular packets any more" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "check that CDMU reacts as in OFF MODE transition" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Wait until the end of the OBCP (PACS OFF mode and MTL TCs disabled)" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "RECOVERY ACTION" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Check that PACS is OFF and MTL TCs are disabled" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "If still running, please terminate the sequence to keep PACS in SCIENCE" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "End of PACS IMMEDIATE OFF TEST check that all EATs are enabled" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "End of PACS FDIR TEST (PRIMARY) check that all EATs are enabled" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "RESET the starting condition" Click YES to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT135_IST_PACS_FDIR "Please clear the MTL" Click YES to Confirm |  |  |  |  |  |  |
|  | At end of Z010999MCVT135_IST_PACS_FDIR Click the button "End TS!" to proceed |  |  |  |  |  |  |

## SPIRE

| Step-No. | Test-Step-Description | Nominal Value | Tolerance | Actual Value | Remarks | P | N |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Call Z010999MCVT136_IST_SPIRE_FDIR to perform the SPIRE related part of the Instruments FDIR IST |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "PERFORM SPIRE FDIR TEST (PRIMARY)?" Click the YES Confirm | If NO, exits script |  |  | Open NCR's for the SPIRE FDIR OBCP Tests: HP-460000-ASED-NC-3836 (no packet defined for TMs of SPIRE LCLs current) |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "upload dummy MTL with SPIRE connection test in subschedule 370" Click the YES Confirm | Check that OBQ reflects the content of the MTL. 1 ping to SPIRE every 5 minutes for 10 hours. All enabled and running. |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "Insert call to SPIRE PING MTL upload" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "Please check that SPIRE TCs Release is enabled!" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "Wait for execution of the first command, then press OK" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "Set SCBP to SPIRE Prime (3)" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "INITIAL S/C STATUS CHECK" Click the YES Confirm | 5.8.13.8 |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "Put SPIRE Primary in science mode" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "TEST the SPIRE OPE STOP FDIR?" Click the YES Confirm | If skipped goes to step Error! Reference source not found. |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "TRIGGER OBCP WITH START TC" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "sending EGSE_tcsend_CEV DC4ST185 { DPV32185 370 } { DPV32185 100 }" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "check that OBCP SPIRE OPE STOP has been triggered" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "Wait until the end of the OBCP (SPIRE is in SCIENCE mode and MTL TCs disabled)" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "RECOVERY ACTION" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "please check that SPIRE is in SCIENCE mode and MTL TCs disabled" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "Please run the sequence to put SPIRE in SCIENCE (if science interrupted...) then press OK" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "End of SPIRE OPE STOP TEST" "check that all EATs are enabled" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "TEST the SPIRE OPE RESUME FDIR?" Click the YES Confirm | If skipped goes to step 164. |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "TRIGGER OBCP WITH START TC" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "Sending EGSE_tcsend_CEV DC7ST185 { DPV32185 100 }" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "check that OBCP SPIRE OPE RESUME has been triggered" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "Wait until the end of the OBCP (SPIRE is in SCIENCE mode and MTL TCs enabled)" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "RECOVERY ACTION" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "please check that SPIRE is in SCIENCE mode and MTL TCs enabled" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "Please run the sequence to put SPIRE in SCIENCE (if science interrupted...) then press OK" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "End of SPIRE OPE STOP TEST" "check that all EATs are enabled" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "TEST the SPIRE DRCU OFF OBCP?" Click the YES Confirm | If skipped goes to step 172. |  |  | Open NCR's for the SPIRE DRCU OFF OBCP: HP-460000-ASED-NC-3835 |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "TRIGGER OBCP WITH START TC" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "Sending TC DC2ST185 to start the SPIRE DRCU OFF OBCP" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "check that OBCP SPIRE DRCU OFF has been triggered" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "Wait until the end of the OBCP (SPIRE is in SCIENCE mode, DRCU OFF and MTL TCs disabled)" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "RECOVERY ACTION" Click the YES to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "Please check that the SPIRE TCs Release is enabled" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "End of SPIRE DRCU OFF TEST" "check that all EATs are enabled" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "TEST the SPIRE OFF CONTROLLED OBCP?" Click the YES Confirm | If skipped goes to step 181. |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "TRIGGER OBCP WITH START TC" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "This OBCP is a TFL, but the command to clear the HK is not given yet, so it will be started by the start cmd" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "Sending TC DC4ST185 {DPV32185 370} {DPV32185 100} to start the SPIRE OFF CTRL OBCP" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "check that OBCP SPIRE OFF CONTROLLED has been triggered" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "Wait until the end of the OBCP (SPIRE is OFF and MTL TCs disabled)" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "RECOVERY ACTION" Click the YES to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "Please check that the SPIRE TCs Release is enabled!" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "End of SPIRE OFF CONTROLLED TEST" "check that all EATs are enabled" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "TEST the SPIRE OFF DLL OBCP?" Click the YES Confirm | If skipped goes to step |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "SPIRE OFF DLL FDIR triggering Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "please start the SPIRE (RT XX) simulation on the CDMU SCOE to create jamming" Click the YES Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "check that OBCP SPIRE OFF has been triggered (e.g. events, commands directed to SPIRE are being sent and SPIRE is going off)" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "Wait until the end of the OBCP, when SPIRE is OFF" Perform activity and press OK Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "Wait until the end of the OBCP (SPIRE is OFF and MTL TCs disabled" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "RECOVERY ACTION" Click the YES to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "please check that SPIRE is OFF and INVALID and no HK is being received" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "please check that its MTL commands have been disabled" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "Stop the simulation on the CDMU scoe and set the scoe OFF LINE" Click the OK to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT136_IST_SPIRE_FDIR "End of SPIRE OFF CONTROLLED TEST" "check that all EATs are enabled" Click the OK to Confirm |  |  |  |  |  |  |
|  | At end of Z010999MCVT136_IST_SPIRE_FDIR Click the button "End TS!" to proceed |  |  |  |  |  |  |

## Specific Post-Test Activities

| Step-No. | Test-Step-Description | Nominal Value | Tolerance | Actual Value | Remarks | P | N |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | During Z010999MCVT131_IST_INSTR_FDIR "RESET to the original SCBP?" Click the YES to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR "DUMP CEL CONTENT?" Click the YES to Confirm |  |  |  |  |  |  |
|  | During Z010999MCVT131_IST_INSTR_FDIR "Bring the S/C into a SAFE mode and switch OFF" Click the YES to Confirm | IST_END script is running. This is going to give user dialogs in case services are not properly stopped. Confirm the suggested corrective actions |  |  |  |  |  |
|  | IN PARALLEL: A102109SPVT003_ACMS_CONFIG25 At prompt: HERSCHEL/PLANCK - MAIN MENU 5.0 - SCM PHASE select option 2. Transition to OCM | 2 Continue |  |  |  |  |  |
|  | A102109SPVT003_ACMS_CONFIG25 Click the button “CONTINUE” to proceed | OK |  |  |  |  |  |
|  | A102109SPVT003_ACMS_CONFIG25 At prompt: HERSCHEL/PLANCK - MAIN MENU 7.0 - OCM PHASE select option 5. RWL Spin Down to 0 Nms in OCM (BiasHold) | 5 continue |  |  |  |  |  |
|  | A102109SPVT003_ACMS_CONFIG25 Click the button “CONTINUE” to proceed | OK |  |  |  |  |  |
|  | A102109SPVT003_ACMS_CONFIG25 At prompt: HERSCHEL/PLANCK - MAIN MENU 7.0 - OCM PHASE select option 99 Terminate ACMS_CONFIG | 99 continue |  |  |  |  |  |
|  | A102109SPVT003_ACMS_CONFIG25 Click the button “CONTINUE” to proceed | OK |  |  |  |  |  |
|  | A102109SPVT003_ACMS_CONFIG25 At prompt: HERSCHEL/PLANCK - MAIN MENU 9.0 - ACMS OFF PHASE Select option 1. Switch Off ACMS | 1 continue |  |  |  |  |  |
|  | A102109SPVT003_ACMS_CONFIG25 Click the button “CONTINUE” to proceed | OK |  |  |  |  |  |

## S/C Power OFF

Follow the steps in the power OFF procedure of AD-4.

# ANNEX

## Master Tcl script

##################################################################

# File: $Id: Z010999MCVT131_IST_INSTR_FDIR.tcl,v 1.4 2007/11/26 10:18:41 hercdmu Exp $

#

# Description:

#

# Uwe Klenke on 2007/12/06: Master script for the Instruments FDIR IST

#                           It switches the S/C and instruments ON and OFF

#

#

# Last edited by: $Author: hercdmu $ on $Date: 2007/11/26 10:18:41 $.

#

#

##################################################################

# automatically set the revision. do not edit this

setrevision {$Id: Z010999MCVT131_IST_INSTR_FDIR.tcl,v 1.4 2007/11/26 10:18:41 hercdmu Exp $}

##################################################################

# start of test sequence

##################################################################

EGSE_init

global ambient

global user_gen

global sequence_to_manage

global sequence_success

global sequence_not_found

global sequence_to_manage

set local_script_name "Z010999MCVT131_IST_INSTR_FDIR"

set logfile $env(HPCCSTESTRES)/USER/[gettime]_Z010999MCVT094_IST_DTCP_CDMS_MANAGM

# TCL SEQUENCE DEFINITION...

setup_win

logm "***********************************************************"

yesorno "START HERSCHEL INSTRUMENTS FDIR, SECTION 5.8.13 "

logm "***********************************************************"

waittime 00.00.01.0000

if { $user_gen == 5 } {

} elseif { $user_gen == 4 } {

waittime 00.00.02.0000

exit

}

logm "*******************************************************************************"

logm "* Start of the section 5.8.13 - INSTRUMENTS FDIR"

logm "*******************************************************************************"

newTest_gen "POWER ON S/C and configure for ALL A)? - (SKIP if S/C already on and configured by CMDS MGMNT"

menuTB

if { $user_gen == 8 } {

# *****************************************************************************************

newTest_gen "POWER ON S/C AND BRING THE S/C TO END OF LAUNCH"

menuTB

if { $user_gen == 8 } {

call Z010999MCVT003_IST_START 5.8.13.6

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "CDMS SETTING FOR SEPARATION"

menuTB

if { $user_gen == 8 } {

#commented out only for DEBUG, since ACMS will be off:	callasync A102109SPVT202_ACMS_STATUS_H

call D102159SCVT138_IST_LAUNCH_SUNACQ

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "TRANSITION TO NOMINAL"

menuTB

if { $user_gen == 8 } {

call D102159SCVT137_IST_SUNACQ_NOM

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "TRANSITION FROM SAS 900W AND BS 24V TO SAS 1475W AND BS FULL CHARGED"

menuTB

if { $user_gen == 8 } {

call W102584SPVT101_PCDU_TRANSITION_FDIR 1

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "SWITCH ON SREM AND START ACQUISITION SERVICE"

menuTB

if { $user_gen == 8 } {

call Z102999SCVT001_SREM_ON  60

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

logm "End of SKIPPABLE S/C configuration for the Instruments FDIR test"

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

logm "*****************************************************************"

logm "Start of Instruments FDIR specific configuration"

logm "*****************************************************************"

newTest_gen "SAVING ORIGINAL SCBP"

menuTB

if { $user_gen == 8 } {

set FirstBP [ getrawvalue [fetch DEF5F160 ] ]

logm "Saving current bus profile $FirstBP to variable FirstBP"

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "UPLOAD OBCP and EAT for PRIMARY"

menuTB

if { $user_gen == 8 } {

logm " "

logm " Calling external sequence to Upload OBCP and EAT "

logm " "

call D102159SCVT193_IST_UPLOAD_OBCP

infom "Please upload only the EAT entries for PRIMARY"

call D102159SCVT192_IST_UPLOAD_EAT

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "Clear MTL and start ON BOARD SCHEDULING?"

menuTB

if { $user_gen == 8 } {

infom "If MTL already filled in by previous tests, please clear it, then press OK!!!!!"

logm "Check the following TM : - MtlSts = Stopped "

if { [ getengvalue [ fetch DEH26170] ] == "Stopped" } then {

logm "Sending Telecommand DC90F170 Description: StartOnBoardSched"

EGSE_tcsend_CEV DC90F170 checks { SPTV DPTV CEV }  ack { ACCEPT COMPLETE  }

waittime +00.00.01.000000

} else {

logm "MtlSts is already running"

}

logm " "

logm " Disabling Release of All SubSched TCs"

logm " "

EGSE_tcsend_CEV DC76F170

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "POWER ON HIFI PRIMARY"

menuTB

if { $user_gen == 8 } {

call Z102999SCVT014_ASDGEN_HIFIPWRON_P

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "POWER ON PACS PRIMARY"

menuTB

if { $user_gen == 8 } {

logm " "

call Z102999SCVT010_ASDGEN_PACSPWRON_P

waittime 00.00.02.0000

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "POWER ON SPIRE PRIMARY"

menuTB

if { $user_gen == 8 } {

logm " "

call Z102999SCVT004_ASDGEN_SPIREPWRON_P

waittime 00.00.02.0000

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

logm "*****************************************************************"

logm "End of Instruments FDIR specific configuration"

logm "*****************************************************************"

# *****************************************************************************************

infom "Select OK to switch off when FDIR OBCP activities are complete"

# *****************************************************************************************

logm "************************************************************************************"

logm "End of INSTRUMENTS FDIR TESTS"

infom "check that all EATs are enabled"

logm "************************************************************************************"

waittime 00.00.02.0000

# *****************************************************************************************

newTest_gen "RESET to the original SCBP?"

menuTB

if { $user_gen == 8 } {

logm "Set bus profile back to original setting"

EGSE_trace_TC DC819160

tcsend DC819160 [list DH049160 $FirstBP]

waittime 1

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "DUMP CEL CONTENT?"

menuTB

if { $user_gen == 8 } {

infom "call the CEL downlink sequence"

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "BRING THE S/C INTO A SAFE MODE AND SWITCH OFF"

menuTB

if { $user_gen == 8 } {

call Z010999MCVT004_IST_END

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

finish_TS

EGSE_finish

##################################################################

# end of test sequence

##################################################################

# Changes:

# $Log: Z010999MCVT131_IST_INSTR_FDIR.tcl,v $

# Revision 1.4  2007/11/26 10:18:41  hercdmu

# reorganised the sequence of the test steps

#

# Revision 1.3  2007/10/26 14:05:18  hercdmu

# still to clarify TCs to start obcps and end/final state of instruments in some cases"

#

# Revision 1.2  2007/10/19 11:59:20  hercdmu

# hifi fdir

#

# Revision 1.1  2007/10/15 09:24:52  hercdmu

# initial version

#

#

##################################################################

## HIFI Tcl script

##################################################################

# File: $Id: Z010999MCVT134_IST_HIFI_FDIR.tcl,v 1.1 2007/12/06 02:39:09 hercdmu Exp $

#

# Description:

#

# Uwe Klenke 2007/12/06: performs the HIFI part of the Instruments FDIR IST

#

#

# Last edited by: $Author: hercdmu $ on $Date: 2007/12/06 02:39:09 $.

#

#

##################################################################

# automatically set the revision. do not edit this

setrevision {$Id: Z010999MCVT134_IST_HIFI_FDIR.tcl,v 1.1 2007/12/06 02:39:09 hercdmu Exp $}

##################################################################

# start of test sequence

##################################################################

EGSE_init

global ambient

global user_gen

global sequence_to_manage

global sequence_success

global sequence_not_found

global sequence_to_manage

set local_script_name "Z010999MCVT134_IST_HIFI_FDIR"

set logfile $env(HPCCSTESTRES)/USER/[gettime]_Z010999MCVT094_IST_DTCP_CDMS_MANAGM

# TCL SEQUENCE DEFINITION...

setup_win

# *****************************************************************************************

newTest_gen "Perform HIFI FDIR PRIMARY?"

menuTB

if { $user_gen == 8 } {

# *****************************************************************************************

newTest_gen "upload dummy MTL with HIFI connection test in subschedule 70"

menuTB

if { $user_gen == 8 } {

logm "Uploading MTL for pinging HIFI subschedule ID 70"

infom "Insert call to HIFI PING MTL upload"

logm "Enabling HIFI subchedule ID in MTL"

EGSE_tcsend_CEV DC63F159

infom "Wait for execution of the first command, then press OK"

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "Set SCBP to HIFI Prime (2)"

menuTB

if { $user_gen == 8 } {

logm "Changing SCBP to HIFI prime (2)"

set EGSE_trace_TC DC819160

tcsend DC819160 { DH049160 2 }

ver_send_raw " " "DEF5F160" "2" "2" "FALSE" " "

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "INITIAL S/C STATUS CHECK"

menuTB

if { $user_gen == 8 } {

call Z010999MCVT153_IST_STATUS 5.8.13.6

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "Put HIFI Primary in science mode "

menuTB

if { $user_gen == 8 } {

logm "Putting HIFI in science mode"

infom "Insert call to science mode sequence"

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "Perform HIFI RESET OBCP (DLL)?"

menuTB

if { $user_gen == 8 } {

# *****************************************************************************************

newTest_gen "HIFI RESET DLL FDIR triggering"

menuTB

if { $user_gen == 8 } {

infom "please start the HIFI (RT XX) simulation on the CDMU SCOE to create jamming"

infom "check that OBCP HIFI_RESET has been triggered (e.g. events, commands directed to HIFI are being sent and HIFI is going off)"

infom "Wait until the end of the OBCP, when HIFI is OFF"

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "RECOVERY ACTION"

menuTB

if { $user_gen == 8 } {

infom "please check that HIFI is OFF and INVALID and no HK is being received"

waittime 00.00.02.0000

infom "please check that the MTL commands of the corresponding subschedule have been disabled"

waittime 00.00.02.0000

infom "Stop the simulation on the CDMU scoe and set the scoe OFF LINE"

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *********************************************************************************************

logm "************************************************************************************"

logm "End of HIFI RESET OBCP (DLL)"

infom "check that all EATs are enabled"

logm "************************************************************************************"

# *****************************************************************************************

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

newTest_gen "RESET starting conditions"

menuTB

if { $user_gen == 8 } {

infom "Please clear the MTL"

waittime 00.00.02.0000

logm " "

logm " "

logm " Disabling Release of All SubSched TCs"

logm " "

EGSE_tcsend_CEV DC76F170

logm "HIFI is being turned on again"

call Z102999SCVT014_ASDGEN_HIFIPWRON_P

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

logm "************************************************************************************"

logm "End of HIFI FDIR TEST"

infom "check that all EATs are enabled"

logm "************************************************************************************"

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *********************************************************************************************

# *********************************************************************************************

# ******************************** - END OF HIFI FDIR - ***************************************

# *********************************************************************************************

# *********************************************************************************************

# *********************************************************************************************

finish_TS

EGSE_finish

##################################################################

# end of test sequence

##################################################################

# Changes:

# $Log: Z010999MCVT134_IST_HIFI_FDIR.tcl,v $

# Revision 1.1  2007/12/06 02:39:09  hercdmu

# initial version

#

#

##################################################################

## PACS Tcl script

##################################################################

# File: $Id: Z010999MCVT135_IST_PACS_FDIR.tcl,v 1.1 2007/12/06 02:40:14 hercdmu Exp $

#

# Description:

#

# Uwe Klenke 2007/12/06: performs the PACS part of the Instruments FDIR IST

#

#

# Last edited by: $Author: hercdmu $ on $Date: 2007/12/06 02:40:14 $.

#

#

##################################################################

# automatically set the revision. do not edit this

setrevision {$Id: Z010999MCVT135_IST_PACS_FDIR.tcl,v 1.1 2007/12/06 02:40:14 hercdmu Exp $}

##################################################################

# start of test sequence

##################################################################

EGSE_init

global ambient

global user_gen

global sequence_to_manage

global sequence_success

global sequence_not_found

global sequence_to_manage

set local_script_name "Z010999MCVT135_IST_PACS_FDIR"

set logfile $env(HPCCSTESTRES)/USER/[gettime]_Z010999MCVT094_IST_DTCP_CDMS_MANAGM

# TCL SEQUENCE DEFINITION...

setup_win

# *********************************************************************************************

# *********************************************************************************************

# ******************************** - START OF PACS FDIR - *************************************

# *********************************************************************************************

# *********************************************************************************************

# *********************************************************************************************

# *****************************************************************************************

newTest_gen "PERFORM PACS FDIR TEST (PRIMARY)?"

menuTB

if { $user_gen == 8 } {

# *****************************************************************************************

newTest_gen "upload and enable dummy MTL with PACS connection test in subschedule 90"

menuTB

if { $user_gen == 8 } {

logm "Uploading MTL for pinging PACS subschedule ID 90"

infom "Insert call to PACS PING MTL upload"

logm "Enabling Release of PACS MTL TCs"

EGSE_tcsend_CEV DC65F159

infom "Wait for execution of the first command, then press OK"

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "Set SCBP to PACS Prime (4)"

menuTB

if { $user_gen == 8 } {

logm "Changing SCBP to PACS Prime (4)"

set EGSE_trace_TC DC819160

tcsend DC819160 { DH049160 4 }

ver_send_raw " " "DEF5F160" "4" "4" "FALSE" " "

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "INITIAL S/C STATUS CHECK"

menuTB

if { $user_gen == 8 } {

call Z010999MCVT153_IST_STATUS 5.8.13.7

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "PUT PACS IN SCIENCE"

menuTB

if { $user_gen == 8 } {

logm " "

infom "Please run in parallel the sequence to put PACS in SCIENCE for 1h"

waittime 00.00.02.0000

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "TEST the PACS SAFE FDIR?"

menuTB

if { $user_gen == 8 } {

# *****************************************************************************************

newTest_gen "Execute PACS SCRIPT FOR AUTONOMY FUNCTION 14?"

menuTB

if { $user_gen == 8 } {

infom "Calling script PACS_StartAutonomy_Function_14_OBS_Shell.tcl"

callasync PACS_StartAutonomy_Function_14_OBS_Shell

infom "check that OBCP PACS_SAFE has been triggered"

waittime 00.00.02.0000

infom "check that PACS is sending 3 event packets TM(5,2) -cooler recycling temp expired"

waittime 00.00.02.0000

infom "check that CDMU reacts as in SAFE MODE transition"

waittime 00.00.02.0000

infom "check that BOL_T_FPU is disabled again"

waittime 00.00.02.0000

infom "Wait until the end of the OBCP (PACS is in SAFE mode and MTL TCs disabled)"

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "RECOVERY ACTION"

menuTB

if { $user_gen == 8 } {

infom "please check that PACS is in SAFE mode and that its MTL commands have been disabled"

waittime 00.00.02.0000

infom "If still running, please terminate the sequence to keep PACS in SCIENCE"

logm "Enabling Release of PACS MTL TCs"

EGSE_tcsend_CEV DC65F159

waittime 00.00.02.0000

infom "Please check that PACS TCs Release is enabled!"

waittime 00.02.00

logm " "

logm "Changing SCBP to PACS Prime (4)"

set EGSE_trace_TC DC819160

tcsend DC819160 { DH049160 4 }

ver_send_raw " " "DEF5F160" "4" "4" "FALSE" " "

waittime 00.02.00

infom "Please run in parallel the sequence to put PACS in SCIENCE for 1h"

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

logm "************************************************************************************"

logm "End of PACS SAFE OBCP TEST"

infom "check that all EATs are enabled"

logm "************************************************************************************"

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *********************************************************************************************

# *********************************************************************************************

# ******************************** - END OF PACS SAFE OBCP - **********************************

# *********************************************************************************************

# *********************************************************************************************

# *****************************************************************************************

newTest_gen "TEST the PACS POWER CYCLE OBCP?"

menuTB

if { $user_gen == 8 } {

waittime 00.02.00

# *****************************************************************************************

newTest_gen "TRIGGER OBCP WITH START TC"

menuTB

if { $user_gen == 8 } {

logm "Sending TC DCAST185 to start the PACS_POWER_CYCLE_OBCP"

infom "sending EGSE_tcsend_CEV DCAST185 { DPV32185 90 } { DPV32185 'NOMINAL' ENG}"

EGSE_tcsend_CEV DCAST185 { DPV32185 90 } { DPV32185 "NOMINAL" ENG}

waittime 00.00.02.0000

infom "check that OBCP PACS_POWER_CYCLE has been triggered"

waittime 00.00.02.0000

infom "Wait until the end of the OBCP (PACS is in SAFE mode and MTL TCs disabled)"

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "RECOVERY ACTION"

menuTB

if { $user_gen == 8 } {

infom "please check that PACS is in SAFE mode and that its MTL commands have been disabled"

waittime 00.00.02.0000

infom "if still running, please terminate the sequence to keep PACS in SCIENCE"

logm "Enabling Release of PACS MTL TCs"

waittime 00.00.02.0000

EGSE_tcsend_CEV DC65F159

waittime 00.00.02.0000

infom "Please check that the PACS TCs Release is enabled!"

waittime 00.02.00

logm " "

logm "Changing SCBP to PACS Prime (4)"

set EGSE_trace_TC DC819160

tcsend DC819160 { DH049160 4 }

ver_send_raw " " "DEF5F160" "4" "4" "FALSE" " "

waittime 00.02.00

logm " "

infom "Please run in parallel the sequence to put PACS in SCIENCE for 1h"

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

logm "************************************************************************************"

logm "End of PACS POWER CYCLE TEST"

infom "check that all EATs are enabled"

logm "************************************************************************************"

waittime 00.00.02.0000

# *****************************************************************************************

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *********************************************************************************************

# *********************************************************************************************

# ******************************** - END OF PACS POWER CYCLE OBCP - ***************************

# *********************************************************************************************

# *********************************************************************************************

# *****************************************************************************************

newTest_gen "TEST PACS BOLC OFF OBCP?"

menuTB

if { $user_gen == 8 } {

waittime 00.02.00

# *****************************************************************************************

newTest_gen "TRIGGER OBCP WITH START TC"

menuTB

if { $user_gen == 8 } {

logm "Sending TC DC9ST185 to start the PACS_BOLC_OFF OBCP"

infom "Sending EGSE_tcsend_CEV DC9ST185 { DPV32185 90 }"

EGSE_tcsend_CEV DC9ST185 { DPV32185 90 }

waittime 00.00.02.0000

infom "check that OBCP PACS BOLC OFF has been triggered"

waittime 00.00.02.0000

infom "Wait until the end of the OBCP (PACS is in SAFE mode and MTL TCs disabled)"

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "RECOVERY ACTION"

menuTB

if { $user_gen == 8 } {

infom "please check that PACS is in SAFE mode and that its MTL commands have been disabled"

waittime 00.00.02.0000

infom "If still running, please terminate the sequence to keep PACS in SCIENCE"

logm "Enabling Release of PACS MTL TCs"

logm " "

logm "switching PACS OFF"

call Z102999SCVT011_ASDGEN_PACSPWROFF_P

waittime 00.00.02.0000

logm " "

logm "switching PACS ON"

call Z102999SCVT010_ASDGEN_PACSPWRON_P

logm "Enabling Release of PACS MTL TCs"

EGSE_tcsend_CEV DC65F159

waittime 00.00.02.0000

infom "Please check that only the PACS TCs Release is enabled!"

waittime 00.02.00

logm " "

logm "Changing SCBP to PACS Prime (4)"

set EGSE_trace_TC DC819160

tcsend DC819160 { DH049160 4 }

ver_send_raw " " "DEF5F160" "4" "4" "FALSE" " "

waittime 00.02.00

logm " "

infom "Please run in parallel the sequence to put PACS in SCIENCE for 1h"

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

logm "************************************************************************************"

logm "End of PACS BOLC OFF TEST"

infom "check that all EATs are enabled"

logm "************************************************************************************"

waittime 00.00.02.0000

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *********************************************************************************************

# *********************************************************************************************

# ******************************** - END OF PACS BOLC OFF OBCP - ******************************

# *********************************************************************************************

# *********************************************************************************************

# *****************************************************************************************

newTest_gen "PACS NORMAL OFF OBCP"

menuTB

if { $user_gen == 8 } {

waittime 00.02.00

# *****************************************************************************************

newTest_gen "Execute PACS SCRIPT FOR AUTONOMY FUNCTION 17?"

menuTB

if { $user_gen == 8 } {

infom "Calling script PACS_StartAutonomy_Function_17_OBS_Shell.tcl"

waittime 00.00.02.0000

callasync PACS_StartAutonomy_Function_17_OBS_Shell

waittime 00.00.02.0000

infom "check that OBCP PACS_NORMAL_OFF has been triggered"

waittime 00.00.02.0000

infom "check that PACS is sending event packets TM(5,2) - BOLC power violated"

waittime 00.00.02.0000

infom "check that CDMU reacts as in OFF MODE transition"

waittime 00.00.02.0000

infom "Wait until the end of the OBCP (PACS OFF mode and MTL TCs disabled)"

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "RECOVERY ACTION"

menuTB

if { $user_gen == 8 } {

infom "Check that PACS is OFF and MTL TCs are disabled"

waittime 00.00.02.0000

infom "If still running, please terminate the sequence to keep PACS in SCIENCE"

logm "Enabling Release of PACS MTL TCs"

logm " "

logm "switching PACS ON"

call Z102999SCVT010_ASDGEN_PACSPWRON_P

logm "Enabling Release of PACS MTL TCs"

EGSE_tcsend_CEV DC65F159

waittime 00.00.02.0000

infom "Please check that only the PACS TCs Release is enabled!"

waittime 00.02.00

logm " "

logm "Changing SCBP to PACS Prime (4)"

set EGSE_trace_TC DC819160

tcsend DC819160 { DH049160 4 }

ver_send_raw " " "DEF5F160" "4" "4" "FALSE" " "

waittime 00.02.00

logm " "

infom "Please run in parallel the sequence to put PACS in SCIENCE for 1h"

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

logm "************************************************************************************"

logm "End of PACS NORMAL OFF TEST"

infom "check that all EATs are enabled"

logm "************************************************************************************"

waittime 00.00.02.0000

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *********************************************************************************************

# *********************************************************************************************

# ******************************** - END OF PACS NORMAL OFF OBCP - ****************************

# *********************************************************************************************

# *********************************************************************************************

# *****************************************************************************************

newTest_gen "PACS IMMEDIATE OFF OBCP?"

menuTB

if { $user_gen == 8 } {

waittime 00.02.00

# *****************************************************************************************

newTest_gen "Execute PACS SCRIPT FOR CLEARING HK (WARM TBC)?"

menuTB

if { $user_gen == 8 } {

infom "Calling script PACS_Disable_HK_OBS_Shell.tcl"

callasync PACS_Disable_HK_OBS_Shell

waittime 00.00.02.0000

infom "check that OBCP PACS IMMEDIATE OFF has been triggered"

waittime 00.00.02.0000

infom "check that PACS is sending no regular packets any more"

waittime 00.00.02.0000

infom "check that CDMU reacts as in OFF MODE transition"

waittime 00.00.02.0000

infom "Wait until the end of the OBCP (PACS OFF mode and MTL TCs disabled)"

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "RECOVERY ACTION"

menuTB

if { $user_gen == 8 } {

infom "Check that PACS is OFF and MTL TCs are disabled"

waittime 00.00.02.0000

infom "If still running, please terminate the sequence to keep PACS in SCIENCE"

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

logm "************************************************************************************"

logm "End of PACS IMMEDIATE OFF TEST"

infom "check that all EATs are enabled"

logm "************************************************************************************"

waittime 00.00.02.0000

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *********************************************************************************************

# *********************************************************************************************

# ******************************** - END OF PACS IMMEDIATE OFF OBCP - *************************

# *********************************************************************************************

# *********************************************************************************************

logm "************************************************************************************"

logm "End of PACS FDIR TEST (PRIMARY)"

infom "check that all EATs are enabled"

logm "************************************************************************************"

waittime 00.00.02.0000

# *********************************************************************************************

newTest_gen "RESET the starting condition"

menuTB

if { $user_gen == 8 } {

infom "Please clear the MTL"

waittime 00.00.02.0000

logm " "

logm " Disabling Release of All SubSched TCs"

logm " "

EGSE_tcsend_CEV DC76F170

logm " "

logm "PACS is being turned on again"

call Z102999SCVT010_ASDGEN_PACSPWRON_P

waittime 00.00.02.0000

logm " "

logm "switching PACS ON"

call Z102999SCVT010_ASDGEN_PACSPWRON_P

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *********************************************************************************************

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *********************************************************************************************

# *********************************************************************************************

# ******************************** -        END OF PACS FDIR        - *************************

# *********************************************************************************************

# *********************************************************************************************

# *********************************************************************************************

# *********************************************************************************************

finish_TS

EGSE_finish

##################################################################

# end of test sequence

##################################################################

# Changes:

# $Log: Z010999MCVT135_IST_PACS_FDIR.tcl,v $

# Revision 1.1  2007/12/06 02:40:14  hercdmu

# initial version

#

#

##################################################################

## SPIRE Tcl script

##################################################################

# File: $Id: Z010999MCVT136_IST_SPIRE_FDIR.tcl,v 1.1 2007/12/06 02:41:55 hercdmu Exp $

#

# Description:

#

# Uwe Klenke 2007/12/06: performs the SPIRE part of the Instruments FDIR IST

#

#

# Last edited by: $Author: hercdmu $ on $Date: 2007/12/06 02:41:55 $.

#

#

##################################################################

# automatically set the revision. do not edit this

setrevision {$Id: Z010999MCVT136_IST_SPIRE_FDIR.tcl,v 1.1 2007/12/06 02:41:55 hercdmu Exp $}

##################################################################

# start of test sequence

##################################################################

EGSE_init

global ambient

global user_gen

global sequence_to_manage

global sequence_success

global sequence_not_found

global sequence_to_manage

set local_script_name "Z010999MCVT136_IST_SPIRE_FDIR"

set logfile $env(HPCCSTESTRES)/USER/[gettime]_Z010999MCVT094_IST_DTCP_CDMS_MANAGM

# TCL SEQUENCE DEFINITION...

setup_win

# *********************************************************************************************

# *********************************************************************************************

# ******************************** -       START OF SPIRE FDIR        - ***********************

# *********************************************************************************************

# *********************************************************************************************

# *********************************************************************************************

# *********************************************************************************************

newTest_gen "PERFORM SPIRE FDIR TEST (PRIMARY)?"

menuTB

if { $user_gen == 8 } {

# *****************************************************************************************

newTest_gen "upload and enable dummy MTL with SPIRE connection test in subschedule 370"

menuTB

if { $user_gen == 8 } {

logm "Uploading MTL for pinging SPIRE subschedule ID 370"

infom "Insert call to SPIRE PING MTL upload"

logm "Enabling Release of SPIRE MTL TCs"

EGSE_tcsend_CEV DC67F159

waittime 00.00.02.0000

infom "Please check that SPIRE TCs Release is enabled!"

infom "Wait for execution of the first command, then press OK"

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "Set SCBP to SPIRE Prime (3)"

menuTB

if { $user_gen == 8 } {

logm "Changing SCBP to PACS Prime (3)"

set EGSE_trace_TC DC819160

tcsend DC819160 { DH049160 3 }

ver_send_raw " " "DEF5F160" "3" "3" "FALSE" " "

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "INITIAL S/C STATUS CHECK"

menuTB

if { $user_gen == 8 } {

call Z010999MCVT153_IST_STATUS 5.8.13.8

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "PUT SPIRE IN SCIENCE"

menuTB

if { $user_gen == 8 } {

logm " "

infom "Calling the sequence to put SPIRE in SCIENCE"

call S102999SCVT015_ASDISTSPIR_STBY2PHOT

waittime 00.00.02.0000

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "TEST the SPIRE OPE STOP FDIR?"

menuTB

if { $user_gen == 8 } {

# *****************************************************************************************

newTest_gen "TRIGGER OBCP WITH START TC"

menuTB

if { $user_gen == 8 } {

infom "sending EGSE_tcsend_CEV DC4ST185 { DPV32185 370 } { DPV32185 100 }"

logm "Sending TC DCAST185 to start the SPIRE OPE STOP OBCP"

EGSE_tcsend_CEV DC4ST185 { DPV32185 370 } { DPV32185 100 }

waittime 00.00.02.0000

infom "check that OBCP SPIRE OPE STOP  has been triggered"

waittime 00.00.02.0000

infom "Wait until the end of the OBCP (SPIRE is in SCIENCE mode and MTL TCs disabled)"

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "RECOVERY ACTION"

menuTB

if { $user_gen == 8 } {

infom "please check that SPIRE is in SCIENCE mode and MTL TCs disabled"

waittime 00.00.02.0000

logm " "

infom "Please run the sequence to put SPIRE in SCIENCE (if science interrupted...) then press OK"

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

logm "************************************************************************************"

logm "End of SPIRE OPE STOP TEST"

infom "check that all EATs are enabled"

logm "************************************************************************************"

waittime 00.00.02.0000

# *****************************************************************************************

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *********************************************************************************************

# *********************************************************************************************

# ******************************** - END OF SPIRE OPE STOP OBCP - ***************************

# *********************************************************************************************

# *********************************************************************************************

# *****************************************************************************************

newTest_gen "TEST SPIRE OPE RESUME OBCP?"

menuTB

if { $user_gen == 8 } {

waittime 00.02.00

# *****************************************************************************************

newTest_gen "TRIGGER OBCP WITH START TC"

menuTB

if { $user_gen == 8 } {

infom "Sending EGSE_tcsend_CEV DC7ST185 { DPV32185 100 }"

logm "Sending TC DC7ST185 to start the SPIRE OPE RESUME OBCP"

EGSE_tcsend_CEV DC7ST185 { DPV32185 100 }

waittime 00.00.02.0000

infom "check that OBCP SPIRE OPE RESUME has been triggered"

waittime 00.00.02.0000

infom "Wait until the end of the OBCP (SPIRE is in SCIENCE mode and MTL TCs enabled)"

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "RECOVERY ACTION"

menuTB

if { $user_gen == 8 } {

infom "please check that SPIRE is in SCIENCE mode and MTL TCs enabled"

waittime 00.00.02.0000

logm " "

infom "Please run the sequence to put SPIRE in SCIENCE (if science interrupted) then press OK"

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

logm "************************************************************************************"

logm "End of SPIRE OPE RESUME TEST"

infom "check that all EATs are enabled"

logm "************************************************************************************"

waittime 00.00.02.0000

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *********************************************************************************************

# *********************************************************************************************

# ******************************** - END OF SPIRE OPE RESUME OBCP - ******************************

# *********************************************************************************************

# *********************************************************************************************

# *****************************************************************************************

newTest_gen "SPIRE DRCU OFF OBCP"

menuTB

if { $user_gen == 8 } {

waittime 00.02.00

# *****************************************************************************************

newTest_gen "TRIGGER OBCP WITH START TC"

menuTB

if { $user_gen == 8 } {

infom "Sending TC DC2ST185 to start the SPIRE DRCU OFF OBCP"

EGSE_tcsend_CEV DC2ST185

waittime 00.00.02.0000

infom "check that OBCP SPIRE DRCU OFF has been triggered"

infom "Wait until the end of the OBCP (SPIRE is in SCIENCE mode, DRCU OFF and MTL TCs disabled)"

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "RECOVERY ACTION"

menuTB

if { $user_gen == 8 } {

logm " "

logm " Disabling Release of SPIRE  MTL TCs"

logm " "

EGSE_tcsend_CEV DC68F159

logm " "

logm "switching SPIRE OFF"

call Z102999SCVT005_ASDGEN_SPIREPWROFF_P

waittime 00.00.02.0000

logm " "

logm "switching SPIRE ON"

call Z102999SCVT004_ASDGEN_SPIREPWRON_P

waittime 00.00.02.0000

logm "Enabling Release of SPIRE MTL TCs"

EGSE_tcsend_CEV DC67F159

infom "Please check that the SPIRE TCs Release is enabled"

waittime 00.02.00

logm " "

logm "Calling sequence to put SPIRE in SCIENCE"

call S102999SCVT015_ASDISTSPIR_STBY2PHOT

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

logm "************************************************************************************"

logm "End of SPIRE DRCU OFF TEST"

infom "check that all EATs are enabled"

logm "************************************************************************************"

waittime 00.00.02.0000

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *********************************************************************************************

# *********************************************************************************************

# ******************************** - END OF SPIRE DRCU OFF OBCP - ****************************

# *********************************************************************************************

# *********************************************************************************************

# *****************************************************************************************

newTest_gen "SPIRE OFF CTRL OBCP"

menuTB

if { $user_gen == 8 } {

waittime 00.02.00

# *****************************************************************************************

newTest_gen "TRIGGER OBCP WITH START TC"

menuTB

if { $user_gen == 8 } {

infom "This OBCP is a TFL, but the command to clear the HK is not given yet, so it will be started by the start cmd"

waittime 00.00.02.0000

infom "Sending TC DC4ST185 {DPV32185 370 } {DPV32185 100}to start the SPIRE OFF CTRL OBCP"

waittime 00.00.02.0000

EGSE_tcsend_CEV DC4ST185 {DPV32185 370 } {DPV32185 100}

waittime 00.00.02.0000

infom "check that OBCP SPIRE OFF CONTROLLED  has been triggered"

waittime 00.00.02.0000

infom "Wait until the end of the OBCP (SPIRE is OFF and MTL TCs disabled)"

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "RECOVERY ACTION"

menuTB

if { $user_gen == 8 } {

logm " "

logm "switching SPIRE ON"

call Z102999SCVT004_ASDGEN_SPIREPWRON_P

waittime 00.00.02.0000

logm "Enabling Release of SPIRE MTL TCs"

EGSE_tcsend_CEV DC67F159

infom "Please check that SPIRE TCs Release is enabled!"

waittime 00.02.00

logm " "

logm "Calling sequence to put SPIRE in SCIENCE"

call S102999SCVT015_ASDISTSPIR_STBY2PHOT

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

logm "************************************************************************************"

logm "End of SPIRE OFF CTRL TEST"

infom "check that all EATs are enabled"

logm "************************************************************************************"

waittime 00.00.02.0000

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *********************************************************************************************

# *********************************************************************************************

# ******************************** - END OF SPIRE OFF CTRL  OBCP - ****************************

# *********************************************************************************************

# *********************************************************************************************

# *****************************************************************************************

newTest_gen "SPIRE OFF OBCP"

menuTB

if { $user_gen == 8 } {

waittime 00.02.00

# *****************************************************************************************

newTest_gen "SPIRE OFF DLL FDIR triggering"

menuTB

if { $user_gen == 8 } {

infom "please start the SPIRE (RT XX) simulation on the CDMU SCOE to create jamming"

waittime 00.00.02.0000

infom "check that OBCP SPIRE OFF has been triggered (e.g. events, commands directed to SPIRE are being sent and SPIRE is going off)"

waittime 00.00.02.0000

infom "Wait until the end of the OBCP, when SPIRE is OFF"

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *****************************************************************************************

newTest_gen "RECOVERY ACTION"

menuTB

if { $user_gen == 8 } {

infom "please check that SPIRE is OFF and INVALID and no HK is being received"

waittime 00.00.02.0000

infom "please check that its MTL commands have been disabled"

waittime 00.00.02.0000

infom "Stop the simulation on the CDMU scoe and set the scoe OFF LINE"

waittime 00.00.02.0000

waittime 00.02.00

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

logm "************************************************************************************"

logm "End of SPIRE OFF TEST"

infom "check that all EATs are enabled"

logm "************************************************************************************"

waittime 00.00.02.0000

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

} elseif { $user_gen == 10 } {

waittime 00.00.01.0000

exit

}

# *********************************************************************************************

# *********************************************************************************************

# ******************************** - END OF SPIRE OFF  OBCP - *********************************

# *********************************************************************************************

# *********************************************************************************************

finish_TS

EGSE_finish

##################################################################

# end of test sequence

##################################################################

# Changes:

# $Log: Z010999MCVT136_IST_SPIRE_FDIR.tcl,v $

# Revision 1.1  2007/12/06 02:41:55  hercdmu

# initial version

#

#

##################################################################

# Summary Sheets

## Procedure Variation Summary

|  | Test Change | Curr. No.: Date Page of |
| --- | --- | --- |
| Test designation | Test Procedure | Issue | Rev. |
| Test step changed | Reason for Change |
| Prepared by: | Resp. Test Leader | Project Engineer |
| PA/QA | Prime | Customer |

Table 9.1-1: Procedure Variation Sheet

## Non Conformance Report (NCR) Summary

| NCR - No. | NCR - Title | Date | Open Closed | PA sig. |
| --- | --- | --- | --- | --- |

Table 9.2-1: Non-Conformance Record Sheet

## Sign-off Sheet

|  | Date | Signature |
| --- | --- | --- |
| Test Manager |  |  |
| Operator |  |  |
| PA Responsible |  |  |
| ESA Representative |  |  |

E N D   O F   D O C U M E N T

Distribution List

|  | Name | Dep./Comp. |  | Name | Dep./Comp. |
| --- | --- | --- | --- | --- | --- |
|  | Alberti von Mathias Dr. | ASG23 |  | Reichle Konrad | ASA42 |
|  | Baldock Richard | FAE12 |  | Runge Axel | OTN/ASA44 |
|  | Barlage Bernhard | AED13 |  | Sauer Maximilian Dr. | AED65 |
|  | Bayer Thomas | ASA42 |  | Schink Dietmar | AED32 |
|  | Brune Holger | ASA45 |  | Schmidt Thomas | AED15 |
|  | Edelhoff Dirk | AED2 |  | Schweickert Gunn | ASG23 |
|  | Fehringer Alexander | ASG13 |  | Sonn Nico | ASG51 |
|  | Fricke Wolfgang Dr. | AED 65 |  | Steininger Eric | AED32 |
|  | Geiger Hermann | ASA42 |  | Stritter Rene | AED11 |
|  | Grasl Andreas | OTN/ASA44 |  | Suess Rudi | OTN/ASA44 |
|  | Grasshoff Brigitte | AET12 |  | Theunissen Martijn | DSSA |
|  | Hamer Simon | Terma |  | Vascotto Riccardo | HE Space |
|  | Hanka, Erhard | FI552 |  | Wagner Klaus | ASG23 |
|  | Hendrikse Jeffrey | HE Space |  | Wietbrock Walter | AET12 |
|  | Hendry David | Terma |  | Wöhler Hans | ASG23 |
|  | Hengstler Reinhold | ASA42 |  | Wössner Ulrich | ASE252 |
|  | Hinger Jürgen | ASG23 |  | Zumstein Armin | ASQ42 |
|  | Hohn Rüdiger | AED65 |  |  |  |
|  | Hölzle Edgar Dr. | AED32 |  |  |  |
|  | Hopfgarten Michael | AED32 |  |  |  |
|  | Huber Johann | ASA42 |  |  |  |
|  | Hund Walter | ASE252 |  | Alcatel Alenia Space Cannes | AAS-F |
|  | Idler Siegmund | AED312 |  | Alcatel Alenia Space Torino | AAS-I |
|  | Ivády von András | FAE12 |  | ESA/ESTEC | ESA |
|  | Jahn Gerd Dr. | ASG23 |  |  |  |
|  | Kalde Clemens | ASM2 |  | Instruments: |  |
|  | Kettner Bernhard | AET42 |  | MPE (PACS) | MPE |
|  | Klenke Uwe | ASG72 |  | RAL (SPIRE) | RAL |
|  | Knoblauch August | AET32 |  | SRON (HIFI) | SRON |
|  | Koelle Markus | ASA43 |  |  |  |
|  | Koppe Axel | AED312 |  |  |  |
|  | Kroeker Jürgen | AED65 |  | Subcontractors: |  |
|  | La Gioia Valentina | Terma |  | Alcatel Alenia Space Antwerp | ABSP |
|  | Lang Jürgen | ASE252 |  | Austrian Aerospace | AAE |
|  | Langenstein Rolf | AED15 |  | Austrian Aerospace | AAEM |
|  | Langfermann Michael | ASA41 |  | BOC Edwards | BOCE |
|  | Martin Olivier | ASA43 |  | Dutch Space Solar Arrays | DSSA |
|  | Maukisch Jan | ASA43 |  | EADS Astrium Sub-Subsyst. & Equipment | ASSE |
|  | Much Christoph | ASA43 |  | EADS CASA Espacio | CASA |
|  | Müller Jörg | ASA42 |  | EADS CASA Espacio | ECAS |
|  | Müller Martin | ASA43 |  | European Test Services | ETS |
|  | Pietroboni Karin | AED65 |  | Patria New Technologies Oy | PANT |
|  | Platzer Wilhelm | AED2 |  | SENER Ingenieria SA | SEN |

# Text boxes

Das Ändern der Daten wie Datum, Dokumententyp, Ausgabe und Dokumenten-Nummer erfolgt über die Datenvorgabe in den Properties (Eigenschaften). Vorgehensweise: File (Datei) ( Properties (Eigenschaften) und dann den Rider (Reiter) Custom (Anpassen) wählen. Dort können die Daten geändert werden. Nach der Eingabe oben auf Change (Ändern) klicken, dann wird das Dokument aktualisiert. Achtung: Dieser Text wird nicht mitgedruckt, deshalb bitte NICHT löschen!!!!!

Currently the final status is OFF (PACS_NORMAL_OFFis called instead of entrer SAFE