SPIRE RE Most Emissive Mode EMC Test Procedures for IST

Issue 1.0

Approved by

# Introduction

This document describes the SPIRE procedures to be used for IST Radiative Emissions EMC testing in the most emissive mode. The transition to and from the mode for the measurements is as follows:

- OFF to STBY. Note that the STBY mode is known as REDY mode in SPIRE terminology. In this mode only SPIRE HK is being generated.

- STBY to “PHOTOPS”, where “PHOTOPS” refers to a dummy mode where SPIRE is Prime Instrument and generating both Photometer and MCU science as well as HK data at the nominal data rate. SPIRE should be in this mode for the duration of the EMC RE tests.

- “PHOTOPS” to STBY

- STBY to OFF

Since these procedures use standalone TCL scripts they do not require initiation from the I-EGSE, although the I-EGSE will be used to monitor the progress of the tests and to archive test data.

## Scope

## Applicable Documents

| AD# | Title | Reference | Issue# | Date |
| --- | --- | --- | --- | --- |
| AD01 | SPIRE Functional Test Specification | SPIRE-RAL-DOC-001652 | 1.4 | 22nd July 2005 |

## Reference Documents

| RD# | Title | Reference | Issue# | Date |
| --- | --- | --- | --- | --- |
| RD01 | SPIRE Instrument User Manual | SPIRE-RAL-PRJ-002395 | 1.3 | 9th Nov 2007 |

## Change Record

| Doc | Issue# | Changes | Date of Change |
| --- | --- | --- | --- |
| Issue | 1.0 | First version | 25th March 2008 |

## Open Issues

## Constraints

## List of Acronyms

| AND | Alpha Numeric Display |
| --- | --- |
| AVM | Avionics Model |
| BSM | Beam Steering Mirror |
| CCS | Central Checkout System |
| CDMU | Command and Data Management Unit |
| CE | Conductive Emissions |
| DCU | Detector Control Unit |
| DPU | Digital Processing Unit |
| DRCU | Detector Readout and Control Unit |
| EGSE | Electrical Ground Support Equipment |
| EMC | Electromagnetic Compatibility |
| FM | Flight Model |
| FPU | Focal Plane Unit |
| I-EGSE | Instrument EGSE |
| IST | Integrated Systems Test |
| MCU | Mechanism Control Unit |
| RE | Radiative Emissions |
| SMEC | Spectrometer Mechanism |
| WU | Warm Units |

Table of contents

1.	Introduction	2

1.1	Scope	3

1.2	Applicable Documents	3

1.3	Reference Documents	3

1.4	Change Record	3

1.5	Open Issues	3

1.6	Constraints	3

1.7	List of Acronyms	3

2.	Test Configuration	6

2.1	FM Test Configuration	6

3.	IST EMC Procedures Overview	7

3.1	General instructions for executing the test procedures	7

3.2	Test Sequences	7

3.2.1	EMC Test Sequence	7

4.	Detailed IST EMC RE Procedures	8

4.1	Procedures	8

4.1.1	Procedure SPIRE-IST-EMC-RE-OFF-TO-STBY	8

4.1.2	Procedure SPIRE-IST-EMC-RE-STBY-TO-PHOTOPS	11

4.1.3	Procedure SPIRE-IST-EMC-RE-PHOTOPS-TO-STBY	13

4.1.4	Procedure SPIRE-IST-EMC-RE-STBY-TO-OFF	16

# Test Configuration

The main differences between the AVM and the FM configurations are with respect to the hardware.

On the SPIRE AVM hardware the Warm Units and the FPU are substituted by a DRCU simulator.

## FM Test Configuration

This is the required configuration prior to the start of the test:

SPIRE WU:

- The SPIRE FM DRCU should be interconnected with the SPIRE FM DPU, both PRIME and REDUNDANT interfaces.

- The SPIRE FM DRCU NOMINAL and REDUNDANT power interfaces to the Herschel satellite should be connected.

- The SPIRE FM DPU NOMINAL and REDUNDANT 1553 interfaces to the Herschel satellite should be connected.

- The SPIRE FM DPU NOMINAL and REDUNDANT power interfaces to the Herschel satellite should be connected.

HCDMU:

- The Bus list selected on the HCDMU should be as appropriate for the planned activity. If SPIRE is to put into an “Operations” mode then bus list should be for SPIRE Prime Instrument, (i.e., 27 TM slots allocated for SPIRE telemetry). For the NOMINAL side tests the BUS Configuration should be SPIRE Nominal (i.e, RT=21) and for the REDUNDANT side test the BUS Configuration should be SPIRE Redundant (i.e, RT=22).

- The HCDMU and CCS should be interconnected.

CCS:

- The SPIRE MIB should be imported on the CCS.

# IST EMC Procedures Overview

## General instructions for executing the test procedures

- Section 3.2 of this document specifies the sequence to be executed. Each of the steps in the sequence has a detailed specification in section 4.

- The detailed procedures in section 4 include blank boxes where the actual values of parameters can be noted. Based on the comparison with the expected values the success or failure of a step should be recorded in the final column of the table.

- The last row in a procedure table should be used to record the overall Pass/Fail result of each test.

- In general any text in boldface in the procedural steps indicates an action which may have to be performed manually by the CCS staff.

## Test Sequences

### EMC Test Sequence

This section specifies the sequence to be executed for switching between OFF and PHOTOPS modes. Maximum estimated times for executing a test sequence are also given.

| Procedure Name | Purpose | Duration |
| --- | --- | --- |
| SPIRE-IST-EMC-RE-OFF-TO-STBY | To switch SPIRE from OFF to STBY mode | ~5 min |
| SPIRE-IST-EMC-RE-STBY-TO-PHOTOPS | To switch SPIRE from STBY to “PHOTOPS” mode | ~5 min |
| SPIRE-IST-EMC-RE-PHOTOPS-TO-STBY | To switch SPIRE from “PHOTOPS” to STBY mode | ~5 min |
| SPIRE-IST-EMC-RE-STBY-TO-2OFF | To switch SPIRE from STBY to OFF | ~5 min |

Total: ~ 20 min

# Detailed IST EMC RE Procedures

## Procedures

### Procedure SPIRE-IST-EMC-RE-OFF-TO-STBY

| Version | 1.0 |
| --- | --- |
| Date | 31st July 2007 |
| Purpose | To switch the SPIRE instrument from OFF to STBY mode |
| Initial configuration | SPIRE DPU and DRCU are switched off |
| Final configuration | SPIRE is in STBY mode: SPIRE DPU and DRCU are on Generating Nominal HK reports at 4 second intervals Generating Critical HK reports at 2 second intervals |
| Preconditions | SPIRE FM DPU and DRCU are electrically integrated with the Herschel Satellite SPIRE MIB is imported in the CCS database. CCS is up and running DPU AND OBS PARAMETERS AND is selected on the CCS SFT PARAMETERS AND is selected on the CCS |
| Duration | 5 minutes |
| Pass/Fail criteria | Nominal and Critical HK reports start being generated at their nominal rates of 0.25Hz and 0.5Hz respectively. |

| Step | Description | Parameter | Expected Values Before/After | Actual Values Before/After | Pass/ Fail |
| --- | --- | --- | --- | --- | --- |
| 1 | Power ON the SPIRE DPU NOMINAL unit using the dedicated spacecraft LCL line and configure 1553 Spacecraft bus for SPIRE DPU (RT = 21) | — | — | — |  |
| 2 | Wait for the boot software to produce at least 2 event packets (5,1) | — | — | — |  |
| 3 | Execute TCL script SPIRE-IST-DBG-OFF2DPUON.tcl – Issue 1.2 | — | — | — |  |
| 4 | Nominal and Critical HK packets should arrive at the CCS for 30 seconds: SPIRE Nominal HK: (type ,subtype) : (3,25) APID : 0x502 SPIRE Critical HK: (type ,subtype) : (3,25) APID: 0x500 | — | — | — |  |
| 5 | For this 30 second period check that TM1N and TM2N parameters incremented as indicated | TM1N TM2N | @ 0.5Hz @ 1Hz | — |  |
| 6 | After this 30 second interval check that all HK TM reception has stopped | TM1N TM2N | Not incrementing Not incrementing | — — |  |
| 7 | Power ON the SPIRE DRCU NOMINAL unit using the dedicated spacecraft LCL line. | — | — | — |  |
| 8 | Execute TCL script SPIRE-IST-DBG-DPUON2STBY.tcl – Issue 1.3 | — | — | — |  |
| 9 | Check that the THSK parameter is refreshing every 4 seconds | THSK | Refreshing @ 0.25Hz | — |  |

| Step | Description | Parameter | Expected Values Before/After | Actual Values Before/After | Pass/ Fail |
| --- | --- | --- | --- | --- | --- |
| 10 | Check that TM1N and TM2N parameters are incrementing as indicated | TM1N TM2N | Incrementing by 2 every 4 seconds Incrementing by one every 4 seconds | — — |  |
| 11 | Check that the DRCU parameters show nominal values. | SCUP5V SCUP9V SCUM9V BIASP5V BIASP9V BIASM9V MCUBITSTAT MCUP5V MCUP14V MCUM14V MCUP15V MCUM15V | ~ 5.2 ± 0.5V ~ 9.0 ± 0.2V ~ -9.0 ± 0.2V ~ 5.1 ± 0.5V ~ 9.0 ± 0.2V ~ -9.0 ± 0.2V 0/1 ~ 5.0 ± 0.3V ~ 14.0 ± 0.6V ~ -14..0 ± 0.6V ~ 15.0 ± 0.6V ~ -15.0 ± 0.7V |  |  |
| 12 | Check that SPIRE is in REDY mode | MODE | DRCU_ON/REDY |  |  |
| Test Result (Pass/Fail): |

### Procedure SPIRE-IST-EMC-RE-STBY-TO-PHOTOPS

| Version | 1.0 |
| --- | --- |
| Date | 25th March 2008 |
| Purpose | To switch SPIRE from STBY to “PHOTOPS” mode |
| Initial configuration | SPIRE DPU and DRCU are ON SPIRE is in REDY mode |
| Final configuration | SPIRE is Prime Instrument and in “PHOTOPS” mode: Generating critical and nominal HK at 0.5Hz and 1Hz respectively Photometer LIAs are switched on BSM and SMEC sensors are switched on Generating photometer data at ~ 18 packets/s Generating MCU Eng data at 2 packets/s |
| Preconditions | SPIRE MIB is imported in the CCS database. CCS is up and running DPU AND OBS PARAMETERS and FUNCTIONAL TEST PARAMETERS ANDs are selected on the CCS |
| Duration | 10 minutes |
| Pass/Fail criteria | SPIRE is Prime Instrument and in “PHOTOPS” mode: Generating critical and nominal HK at 0.5Hz and 1Hz respectively Generating Photometer and MCU engineering data at ~ 18 packets/s and 2 packets/s respectively |

| Step | Description | Parameter | Expected Values Before/After | Actual Values Before/ After | Success/ Failure |
| --- | --- | --- | --- | --- | --- |
| 1 | Execute TCL script SPIRE-IST-EMC-RE-STBY2PHOTOPS.tcl – Issue 1.1 | — | — | — |  |
| 2 | Check that THSK parameter is refreshing every second | THSK | Refreshing @ 1Hz | — |  |
| 3 | Check that TM1N and TM2N parameters are incrementing as indicated | TM1N TM2N | @ 0.5Hz @ 1Hz | — |  |
|  | Check that the Photometer LIAs have switched on | PLIABITSTAT | 0/1 |  |  |
|  | Check that the BSM sensors have switched on | CHOPSENSPWR JIGGSENSPWR | 0/1 0/1 |  |  |
|  | Check that the SMEC sensors are switched on | SMECENCPWR SMECLVDTPWR | 0/1 0/1 |  |  |
| 4 | Check that TM3N is incrementing as indicated | TM3N | ~18-20 Hz | — |  |
| 5 | Check that TM5N is incrementing as indicated | TM5N | Incrementing by ~4-5 every 2 seconds | — |  |
| 6 | Check that DCUFRAMECNT and MCUFRAMECNT on the FUNCTIONAL TEST PARAMETERS AND are incrementing as indicated | DCUFRAMECNT MCUFRAMECNT | ~18-20 Hz Incrementing by ~96-100 every 2 seconds | — — |  |
| 7 | Check that the MODE parameter is set to RAW value 0xFFCD for the “PHOTOPS” mode Note that “PHOTOPS” is a dummy value for the EMC RE activities – no converted value is defined. | MODE | REDY (0x200) / 0xFFCD |  |  |
| Test Result (Pass/Fail): |

### Procedure SPIRE-IST-EMC-RE-PHOTOPS-TO-STBY

| Version | 1.0 |
| --- | --- |
| Date | 25th March 2008 |
| Purpose | To switch SPIRE from “PHOTOPS” to STBY mode |
| Initial configuration | SPIRE DPU and DRCU are ON SPIRE is Prime Instrument SPIRE is in “PHOTOPS” mode and generating photometer and MCU test pattern data, as well as HK Photometer LIAs are switched on BSM and SMEC sensors are on |
| Final configuration | SPIRE is in STBY mode: Generating only critical and nominal HK at 0.5Hz and 0.25Hz respectively Photometer LIAs are switched off BSM and SMEC sensors are switched off |
| Preconditions | SPIRE MIB is imported in the CCS database. CCS is up and running DPU AND OBS PARAMETERS and FUNCTIONAL TEST PARAMETERS ANDs are selected on the CCS |
| Duration | 10 minutes |
| Pass/Fail criteria | SPIRE is in STBY mode |

| Step | Description | Parameter | Expected Values Before/After | Actual Values Before/After | Success/ Failure |
| --- | --- | --- | --- | --- | --- |
| 1 | Execute TCL script SPIRE-IST-EMC-RE-PHOTOPS2STBY.tcl – Issue 1.0 | — | — | — |  |
| 2 | Check that the THSK parameter is refreshing every 4 seconds | THSK | Refreshing @ 0.25Hz | — |  |
| 3 | Check that TM1N and TM2N parameters are incrementing as indicated | TM1N TM2N | Incrementing by 2 every 4 seconds Incrementing by one every 4 seconds | — |  |
| 4 | Check that TM3N and TM5N have stopped incrementing | TM3N TM5N | — — | — — |  |
| 5 | Check that DCUFRAMECNT and MCUFRAMECNT on the FUNCTIONAL TEST PARAMETERS AND have stopped incrementing | DCUFRAMECNT MCUFRAMECNT | — — | — — |  |
| 6 | Check that SPIRE is in REDY mode (RAW 0x200) | MODE | 0xFFCD/0x200 (REDY) |  |  |
|  | Check that the Photometer LIAs are switched off | PLIABITSTAT | 1/0 |  |  |
|  | Check that the BSM sensors have switched off | CHOPSENSPWR JIGGSENSPWR | 1/0 1/0 |  |  |
|  | Check that the SMEC sensors are switched off | SMECENCPWR SMECLVDTPWR | 1/0 1/0 |  |  |
| Test Result (Pass/Fail): |

### Procedure SPIRE-IST-EMC-RE-STBY-TO-OFF

| Version | 1.1 |
| --- | --- |
| Date | 25th March 2008 |
| Purpose | To switch SPIRE from STBY mode to OFF |
| Initial configuration | SPIRE DPU and DRCU are ON SPIRE is in STBY mode: Generating only critical and nominal HK at 0.5Hz and 0.25Hz respectively |
| Final configuration | SPIRE is OFF: DPU and DRCU are both OFF |
| Preconditions | SPIRE MIB is imported in the CCS database. CCS is up and running DPU AND OBS PARAMETERS is selected on the CCS SFT PARAMETERS AND is selected on the CCS |
| Duration | 5 minutes |
| Pass/Fail criteria | SPIRE instrument is OFF |

| Step | Description | Parameter | Expected Values Before/After | Actual Values Before/After | Success/ Failure |
| --- | --- | --- | --- | --- | --- |
| 1 | Execute TCL script SPIRE-IST-DBG-STBY2OFF.tcl – Issue 1.2 | — | — | — |  |
| 2 | Check that TM1N and TM2N parameters have both stopped incrementing | TM1N TM2N | — — | — — |  |
| 3 | Check that the MCU has been switched off Expected events: A TM(5,1) event report with Event ID 0x0521 and SID 0x510F will be received to indicate that the DPU is not receiving a response from the MCU. A TM(5,4) event report with Event ID 0x550D and SID 0x5420 will be received to indicate the MCU disconnection from the DPU. | MCUBITSTAT | 1/0 |  |  |
| 4 | Check that SPIRE is in DRCU_ON mode | MODE | DRCU_ON |  |  |
| 5 | Power OFF the SPIRE DRCU NOMINAL unit. | — | — | — |  |
| 6 | Power OFF the SPIRE DPU NOMINAL unit. | — | — | — |  |
| Test Result (Pass/Fail): |

#### NOTE: IF THE DPU IS TO BE POWERED ON AGAIN, PLEASE WAIT ~2 MINUTES AFTER EXECUTION OF SPIRE-IST-EMC-RE-STBY2OFF.

# Text boxes

“PHOTOPS”

REDY (STBY)

OFF