| Location : ESTEC | Title: Instrument Emergency Switch OFF Procedures for SVT1 |
| --- | --- |
| Facility : Class 100000 | Model: FM | System: S/C | Date: 12/03/2008 |
|  | Test Conductor: | S. Hamer | NCR Ref: N/A |
| CI No 125000 | Prepared By: | S. Hamer | CIL No: N/A |

| Scope: This ACS details the activities to be performed in the event of a problem occurring during SVT1 instrument tests and ESOC-MOC/Instrument Responsible request switch-off of the designated instrument Appendices: 1 - Activity Control Sheet: Session Record 2 – PACS Prime Switch OFF 3 – PACS Redundant Switch OFF 4 – SPIRE Prime Switch OFF 5 – SPIRE Redundant Switch OFF 6 – HIFI Prime Switch OFF 7 – HIFI Redundant Switch OFF 8 – Switch of S/C Commanding from ESOC to AIT-ESTEC 9 – Switch of S/C Commanding from AIT-ESTEC to ESOC Ref 1: HP-2-ASED-TP-0216 - Lead Procedure for SVT1 S/C Start Configuration |
| --- |
| EGSE CCS SW version: 2.0-1219 | On-Board S/W: CDMS ASW: 3.1.3 ACMS ASW: 3.7 |
| HPSDB: LI-1441 Issue 8draft1 |  |
| Facilities required: | SCOE cables connection: see Appendix 2 |  |
| Personnel required: | 1 AIT eng, 1 Instrument Responsible 1 QA |  |
| Safety and Hazards: | Emergency switch off designated Instrument on request from ESOC-MOC/Instrument Responsible |  |
| NCR / Constraints: | Safety critical NCRs identified: None Blocking NCRs: None Instruments: PACS, SPIRE, HIFI S/C configuration: Ref 1 |  |

| No: | Activity | Proc/Drg/Result | Responsible & sign off |
| --- | --- | --- | --- |
| EMERGENCY SWITCH OFF CALLS |
| 01 | If not already done so, take back S/C commanding from ESOC-MOC as per Appendix 8 |  |  |
| 02 | IF PACS PRIME is to be switched OFF run, procedure in Appendix 2 |  |  |
| 03 | IF PACS REDUNDANT is to be switched OFF, run procedure in Appendix 3 |  |  |
| 04 | IF SPIRE PRIME is to be switched OFF, run procedure in Appendix 4 |  |  |
| 05 | IF SPIRE REDUNDANT is to be switched OFF, run procedure in Appendix 5 |  |  |
| 06 | IF HIFI PRIME is to be switched OFF, run procedure in Appendix 6 |  |  |
| 07 | IF HIFI REDUNDANT is to be switched OFF, run procedure in Appendix 7 |  |  |
| 08 | Once confirmed instrument concerned is switch OFF and all commanding completed, hand back S/C commanding to ESOC-MOC as per Appendix 9 |  |  |
| 09 | Fill in the session ID according to the sheet (Appendix 1) |  |  |

APPENDIX 1

Activity Control Sheet: Session Record

| Session ID | Start Date/Time | End Date/Time | QA Approval |
| --- | --- | --- | --- |

APPENDIX 2

PACS PRIME EMERGENCY SWITCH OFF

| Step-No. | Test-Step-Description | Nominal Value | Actual Value | Remarks | P | N |
| --- | --- | --- | --- | --- | --- | --- |
|  | From the HPCCS test conductor console start the test script to power OFF PACS Prime from SAFE: P102999SCVT906_ASDISTPACS_PWR_OFF_N |  |  |  |  |  |
|  | On HPCCS when prompted: ”FM PACS Switch OFF in Warm or Cold conditions, FPU connected - Select NO to abort TS if not correct” Select YES | YES |  |  |  |  |
|  | Note: During switch off of PACS (5,2) TM event packets are expected |  |  |  |  |  |
|  | On HPCCS when all autonomous actions have been completed by the power on script P102999SCVT906_ASDISTPACS_PWR_OFF_N it will prompt: “Set Bus Profile Back to Original Setting?” Select NO | NO |  |  |  |  |
|  | At the prompt: “Bus Profile left unchanged” Select OK to continue | OK |  |  |  |  |
|  | Inform ESOC-MOC/PACS Responsible that PACS PRIME is OFF | OK |  |  |  |  |
|  | Return to main ACS step 8 |  |  |  |  |  |

APPENDIX 3

PACS REDUNDANT EMERGENCY SWITCH OFF

| Step-No. | Test-Step-Description | Nominal Value | Actual Value | Remarks | P | N |
| --- | --- | --- | --- | --- | --- | --- |
|  | From the HPCCS test conductor console start the test script to power OFF PACS Redundant from SAFE: P102999SCVT908_ASDISTPACS_PWR_OFF_R |  |  |  |  |  |
|  | On HPCCS when prompted: ”FM PACS Switch OFF in Warm or Cold conditions, FPU connected - Select NO to abort TS if not correct” Select YES | YES |  |  |  |  |
|  | Note: During switch off of PACS (5,2) TM event packets are expected |  |  |  |  |  |
|  | On HPCCS when all autonomous actions have been completed by the power on script P102999SCVT908_ASDISTPACS_PWR_OFF_R it will prompt: “Set Bus Profile Back to Original Setting?” Select NO | NO |  |  |  |  |
|  | At the prompt: “Bus Profile left unchanged” Select OK to continue | OK |  |  |  |  |
|  | Inform ESOC-MOC/PACS Responsible that PACS REDUNDANT is OFF | OK |  |  |  |  |
|  | Return to main ACS step 8 |  |  |  |  |  |

APPENDIX 4

SPIRE PRIME EMERGENCY SWITCH OFF

| Step-No. | Test-Step-Description | Nominal Value | Actual Value | Remarks | P | N |
| --- | --- | --- | --- | --- | --- | --- |
|  | If not already running from the HPCCS start the test script: ALL_SubscribeParams | OK |  |  |  |  |
|  | Confirm that the HPCCS is connected to SPIRE I-EGSE, if not issue the command: connect HSPIREEGSE | CONNECTED |  |  |  |  |
|  | From the HPCCS start the test script and wait for completion: SPIRE-IST-COLD-PDET-OFF-P | OK |  |  |  |  |
|  | Check that the Photometer detectors are switched off: PSWJFETSTAT PMLWJFETSTAT | 0x3F/-/0 0x7F/-/0 |  |  |  |  |
|  | Check that the Photometer LIAs are switched off: PLIABITSTAT | 1/-/0 |  |  |  |  |
|  | Inform ESOC-MOC/SPIRE Responsible that SPIRE-IST-COLD-PDET-OFF-P completed execution, checks nominal and obtain confirmation to execute next step. | OK |  |  |  |  |
|  | From the HPCCS start the test script and wait for completion: SPIRE-IST-COLD-BSM-OFF-P | OK |  |  |  |  |
|  | Inform ESOC-MOC/SPIRE Responsible that SPIRE-IST-COLD-BSM-OFF-P completed execution and obtain confirmation to execute next step | OK |  |  |  |  |
|  | From the HPCCS start the test script and wait for completion: SPIRE-IST-COLD-SDET-OFF-P | OK |  |  |  |  |
|  | Check that the Spectrometer detectors are switched off: SPECJFETSTAT | 7/-/0 |  |  |  |  |
|  | Check that the Spectrometer LIAs are switched off: SLIABITSTAT | 1/-/0 |  |  |  |  |
|  | Inform ESOC-MOC/SPIRE Responsible that SPIRE-IST-COLD-SDET-OFF-P completed execution, checks nominal and obtain confirmation to execute next step | OK |  |  |  |  |
|  | From the HPCCS start the test script and wait for completion: SPIRE-IST-COLD-SMEC-OFF-P | OK |  |  |  |  |
|  | Inform ESOC-MOC/SPIRE Responsible that SPIRE-IST-COLD-SMEC-OFF-P completed execution and obtain confirmation to execute next step | OK |  |  |  |  |
|  | From the HPCCS start the test script and wait for completion: SPIRE-IST-COLD-MCU-OFF-P | OK |  |  |  |  |
|  | Inform ESOC-MOC/SPIRE Responsible that SPIRE-IST-COLD-MCU-OFF-P completed execution and obtain confirmation to execute next step | OK |  |  |  |  |
|  | From the HPCCS start the test script and wait for completion: SPIRE-IST-COLD-SCU-OFF-P | OK |  |  |  |  |
|  | Inform ESOC-MOC/SPIRE Responsible that SPIRE-IST-COLD-SCU-OFF-P completed execution and obtain confirmation to execute next step | OK |  |  |  |  |
|  | From the HPCCS test conductor console start the test script to power OFF SPIRE Prime: S102999SCVT032_ASDCFTSPIR_PWR_OFF_P | OK |  |  |  |  |
|  | On HPCCS when prompted: “SPIRE Switch OFF for CFT related tests in Hel/Hell conditions only - Select NO to abort TS if not correct” Select YES | YES |  |  |  |  |
|  | During Switch OFF of SPIRE the following (5,2) and (5,4) event messages on APID 1280 may be expected and do not indicate a problem: EVID 1313 No_MCU_Response_Error EVID 21773 ALARM_LSMCU_DEAD |  |  |  |  |  |
|  | On HPCCS when prompted: "Check Telemetry No Longer Updating - OK to continue" Check that parameters: |  |  | AND: SA_1_559 |  |  |
|  | THSK | Not refreshing |  |  |  |  |
|  | TM2N | Not incrementing |  |  |  |  |
|  | Select OK to continue | OK |  |  |  |  |
|  | On HPCCS when all autonomous actions have been completed by the power on script S102999SCVT032_ASDCFTSPIR_PWR_OFF_P it will prompt: “Bus profile left as SPIRE PRIME, change manually after if required - OK to continue” |  |  |  |  |  |
|  | Select OK to continue | OK |  |  |  |  |
|  | Inform ESOC-MOC/SPIRE Responsible that SPIRE PRIME is OFF | OK |  |  |  |  |
|  | Return to main ACS step 8 |  |  |  |  |  |

APPENDIX 5

SPIRE REDUNDANT EMERGENCY SWITCH OFF

| Step-No. | Test-Step-Description | Nominal Value | Actual Value | Remarks | P | N |
| --- | --- | --- | --- | --- | --- | --- |
|  | If not already running from the HPCCS start the test script: ALL_SubscribeParams | OK |  |  |  |  |
|  | Confirm that the HPCCS is connected to SPIRE I-EGSE, if not issue the command: connect HSPIREEGSE | CONNECTED |  |  |  |  |
|  | From the HPCCS start the test script: SPIRE-IST-COLD-PDET-OFF-R | OK |  |  |  |  |
|  | Inform ESOC-MOC/SPIRE Responsible that SPIRE-IST-COLD-PDET-OFF-R completed execution and obtain confirmation to execute next step | OK |  |  |  |  |
|  | From the HPCCS start the test script: SPIRE-IST-COLD-BSM-OFF-R | OK |  |  |  |  |
|  | Inform ESOC-MOC/SPIRE Responsible that SPIRE-IST-COLD-BSM-OFF-R completed execution and obtain confirmation to execute next step | OK |  |  |  |  |
|  | From the HPCCS start the test script: SPIRE-IST-COLD-SDET-OFF-R | OK |  |  |  |  |
|  | Inform ESOC-MOC/SPIRE Responsible that SPIRE-IST-COLD-SDET-OFF-R completed execution and obtain confirmation to execute next step | OK |  |  |  |  |
|  | From the HPCCS start the test script: SPIRE-IST-COLD-SMEC-OFF-R | OK |  |  |  |  |
|  | Inform ESOC-MOC/SPIRE Responsible that SPIRE-IST-COLD-SMEC-OFF-R completed execution and obtain confirmation to execute next step | OK |  |  |  |  |
|  | From the HPCCS start the test script: SPIRE-IST-COLD-MCU-OFF-R | OK |  |  |  |  |
|  | Inform ESOC-MOC/SPIRE Responsible that SPIRE-IST-COLD-MCU-OFF-R completed execution and obtain confirmation to execute next step | OK |  |  |  |  |
|  | From the HPCCS start the test script: SPIRE-IST-COLD-SCU-OFF-R | OK |  |  |  |  |
|  | Inform ESOC-MOC/SPIRE Responsible that SPIRE-IST-COLD-SCU-OFF-R completed execution and obtain confirmation to execute next step | OK |  |  |  |  |
|  | From the HPCCS test conductor console start the test script to power OFF SPIRE Redundant: S102999SCVT034_ASDCFTSPIR_PWR_OFF_R | OK |  |  |  |  |
|  | On HPCCS when prompted: “SPIRE Switch OFF for CFT related tests in Hel/Hell conditions only - Select NO to abort TS if not correct” Select YES | YES |  |  |  |  |
|  | During Switch OFF of SPIRE the following (5,2) and (5,4) event messages on APID 1280 may be expected and do not indicate a problem: EVID 1313 No_MCU_Response_Error EVID 21773 ALARM_LSMCU_DEAD |  |  |  |  |  |
|  | On HPCCS when prompted: "Check Telemetry No Longer Updating - OK to continue" Check that parameters: |  |  | AND: SA_1_559 |  |  |
|  | THSK | Not refreshing |  |  |  |  |
|  | TM2N | Not incrementing |  |  |  |  |
|  | Select OK to continue | OK |  |  |  |  |
|  | On HPCCS when all autonomous actions have been completed by the power on script S102999SCVT034_ASDCFTSPIR_PWR_OFF_R it will prompt: “Bus profile left as SPIRE PRIME, change manually after if required - OK to continue” |  |  |  |  |  |
|  | Select OK to continue | OK |  |  |  |  |
|  | Inform ESOC-MOC/SPIRE Responsible that SPIRE REDUNDANT is OFF | OK |  |  |  |  |
|  | Return to main ACS step 8 |  |  |  |  |  |

APPENDIX 6

HIFI PRIME EMERGENCY SWITCH OFF

| Step-No. | Test-Step-Description | Nominal Value | Actual Value | Remarks | P | N |
| --- | --- | --- | --- | --- | --- | --- |
|  | If not already running from the HPCCS start the test script: ALL_SubscribeParams | OK |  |  |  |  |
|  | Confirm that the HPCCS is connected to SPIRE I-EGSE, if not issue the command: connect HHIFIEGSE | CONNECTED |  |  |  |  |
|  | From the HPCCS test conductor console start the test script: HIFIST_SFT_Nominal_off.warm | OK |  |  |  |  |
|  | From the HPCCS test conductor console start the test script: H102999SCVT016_ASDISTHIFI_PWR_OFF_P | OK |  |  |  |  |
|  | On HPCCS when prompted: “FM HIFI Switch OFF for IST or SFT in Hel/Hell conditions with warm LOU - Select NO to abort TS if not correct” Select YES | YES |  |  |  |  |
|  | On HPCCS when all autonomous actions have been completed by the power on script H102999SCVT016_ASDISTHIFI_PWR_OFF_P it will prompt: “Set Bus Profile Back to Original Setting?” Select NO | NO |  |  |  |  |
|  | at the prompt: “Bus Profile left unchanged” Select OK to continue | OK |  |  |  |  |
|  | Inform ESOC-MOC/HIFI Responsible that HIFI PRIME is OFF | OK |  |  |  |  |
|  | Return to main ACS step 8 |  |  |  |  |  |

APPENDIX 7

HIFI REDUNDANT EMERGENCY SWITCH OFF

| Step-No. | Test-Step-Description | Nominal Value | Actual Value | Remarks | P | N |
| --- | --- | --- | --- | --- | --- | --- |
|  | If not already running from the HPCCS start the test script: ALL_SubscribeParams | OK |  |  |  |  |
|  | Confirm that the HPCCS is connected to SPIRE I-EGSE, if not issue the command: connect HHIFIEGSE | CONNECTED |  |  |  |  |
|  | From the HPCCS test conductor console start the test script: HIFIST_SFT_Nominal_off.warm | OK |  |  |  |  |
|  | From the HPCCS test conductor console start the test script: H102999SCVT018_ASDISTHIFI_PWR_OFF_R | OK |  |  |  |  |
|  | On HPCCS when prompted: “FM HIFI Switch OFF for IST or SFT in Hel/Hell conditions with warm LOU - Select NO to abort TS if not correct” Select YES | YES |  |  |  |  |
|  | On HPCCS when all autonomous actions have been completed by the power on script H102999SCVT018_ASDISTHIFI_PWR_OFF_R it will prompt: “Set Bus Profile Back to Original Setting?” Select NO | NO |  |  |  |  |
|  | at the prompt: “Bus Profile left unchanged” Select OK to continue | OK |  |  |  |  |
|  | Inform ESOC-MOC/HIFI Responsible that HIFI REDUNDANT is OFF | OK |  |  |  |  |
|  | Return to main ACS step 8 |  |  |  |  |  |

APPENDIX 8

SWITCH OF S/C TC CONTROL FROM ESOC-MOC TO AIT-ESTEC

|  | When agreed and authorised to do so take TC control from ESOC-MOC by performing the following step. |
| --- | --- |
|  | To switch TC commanding over to ESTEC: GOTO TM/TC- DFE From the pull down menu select ‘Local Control Mode’ Use the Password ‘ H-P ‘ Open system control window In TAB “EIU” apply the setting “TC Generation via Int. ” In TAB “EIU” apply the setting “EIU direct” From the pull down menu select ‘Remote Control Mode’ |
|  | Switch of S/C TC control back to ESTEC-AIT complete, return to main ACS step 2 |

APPENDIX 9

SWITCH OF CONTROL FROM AIT-ESTEC TO ESOC MOC

|  | Contact MOC using the VOICE INTERCOM and inform them as follows MOC / AIV Wait for response and then report: “<INST NAME> Emergency Switch-off Complete, ready to switch TC control back to MOC. Please Confirm when to switch over” Wait for response ..Acknowledge their response.. When MOC Confirms switch over , continue with the next steps |
| --- | --- |
|  | To switch TC commanding over to ESOC: GOTO TM/TC- DFE From the pull down menu select ‘Local Control Mode’ Use the Password ‘ H-P ‘ Open system control window In TAB “EIU” apply the setting “NDIU” In TAB “EIU” apply the setting “NDIU via TC DEMOD” From the pull down menu select ‘Remote Control Mode’ |
|  | Contact MOC and inform them as follows MOC / AIV Wait for response and then report: TC Switchover to MOC Completed, Please verify. When MOC has send the connection test TC successfully, TC commanding for MOC is verified. |
|  | Switch of S/C TC control back to ESOC-MOC complete, return to main ACS step 9 |