| Title: | H-EPLM Thermal Model and Analysis |
| --- | --- |
| CI-No: |  |  |
| Prepared by: | A. Hauser, K. Wagner | Date: |  |
| Checked by: | J. Kroeker |  |  |
| Product Assurance: | R. Stritter |  |  |
| Configuration Control: | A. v. Ivády |  |  |
| Project Management: | W. Rühe |  |  |
| Distribution: | See Distribution List (last page) |  |
|  | Copying of this document, and giving it to others and the use or communication of the contents there-of, are forbidden without express authority. Offenders are liable to the payment of damages. All rights are reserved in the event of the grant of a patent or the registration of a utility model or design. |  |

| Issue | Date | Sheet | Description of Change | Release |
| --- | --- | --- | --- | --- |
| 1 2Draft 2 2.1 3 | 30.11.01 11.06.02 17.06.02 10.12.02 24.07.03 | all all all 30 35, 36 37 41 47 52 53, 55 58-64 74 79 80 86 90 91 Annex 1 Annex 2 all | First Issue Draft Issue for PDR Sect. 5.3: HTT, HOT, HS1 and innermost tank suspension straps implemented in ESARAD Geometry Model, Heat shield Beam entrance baffles merged to a common baffle with 0.8 emissivity and attached to HS2 only, Cryostat Baffle Insert with 500 mm diameter introduced, Telescope opening changed from 360 mm to 560 mm. Sect. 5.4: +Y Radiator rotated by 14° towards Y axis (to avoid collision with filling port), emissivity of CVV main radiator changed from 0.8 to 0.7, emissivity of CVV (Y and –Z Radiator changed from 0.9 to 0.8. Sect. 5.5: Waveguides implemented in ESARAD Geometry Model, LOU harness updated acc. to RD 02, LOU radiator design updated acc. to ECP HP-2-ASED-CP-001, Telescope mechanical fixation on CVV changed from GFRP struts to T300 CFRP struts, BOLA direct mounted on CVV and covered with MLI Sect. 5.6: Scientific harness updated acc. to RD 02, Thermalization of SPIRE JFET harness shifted from HS 1 to HS 2. Sect. 5.7: HSS update acc. to. Drawing Set Status “Begin 2002“. Sect. 5.8: SVM Thermal Shield modified (+Z half deleted), SVM top MLI set to 230 K boundary acc. to AD 07, Cross-section to length ratio of SVM/CVV struts changed from 18.42 mm to 13.05 mm. Sect. 6.1: MLI performance data changed based on RD 08 and RD 09. PDR Issue of document Table 5.2-2 corrected (typo: JFET dissipation in wrong column) Table 5.3-1 corrected (typo: 9 LOU windows instead 7) Explanation of CVV radiator model added as requeseted in PDR RID 8516 Table 5.4-1 corrected (typo: 9 LOU windows instead 7) Table 5.6-2 corrected (typo: JFET harness length) Complete data as requested in PDR RID 8517 Correction of SVM shield skin data acc. to TMM assumptions References for material data plots completed as requested in PDR RID 8517 Table 7.4-1 corrected and completed Table 7.4-3 completed as requested in PDR RID 8519 Figure 7.4-5 exchanged (copy and paste error) Table 7.4-6 corrected (typo: HOB temperature uncertainty) Introduction of Section 7.4.5 to refer to transient analyses described in RD 06 Lifetime of PDR Collocation Status added Temperature listings for in orbit hot and cold case as well as for ground case added as requested in PDR RID 8517 Input Traceability Matrix added Document entirely modified. Major changes: Restructuring of H-EPLM GMM/TMM to allow Submodel structure Refinement of CVV lower bulkhead MLI (HP-2-ASPI-TN-0366) Increase of CVV radiator (upper bulk and Cryostat Baffle). Refinement of Telescope Geometry based on ASEF catia model ICD-DT0018251-02-00-3D-TELESCOPE_28_05_02. Refinement/update of ventline modelling. Implementation of Cryo-Cooled Cover (low emissive cover shield). Update LEOP Calculation (PPS Sample 5). Implementation of HIFI coax cable: Precision Tube JS50141, JN50141. Refinement/update of beam entrance baffles Removal of BOLA Implementation of H-RSVM submodel (ALCATEL delivery) Introduction of L3 interfaces. Update of SVM Thermal Shield material (CFRP panel instead of Al panel). Removal of Instrument Shield MLI Introduction of 100 mm EPLM enlargement Implementation of HSS lower stiffening ribs Introduction fo save Mode introduced Introduction of On-Ground Test Mode (IMT) Implementation of optimized tank suspension straps ISO TMM conductance values between suspension bolts and heat shields replaced by physical values Update/Refinement of LOU HS2 baffle and LOU windows in H-EPLM GMM Refinement (nodal- break-down) of Cryostat Baffle and Cryostat Baffle MLI Update of AL5083 thermal conductivity data (CVV) acc. to NIST data base Implementation of HSS/SVM closure MLI Implementation of overall instrument timeline Update of Lifetime calculation (HP-2-ASED-TN-0065) Implementation of Instrument Submodels, see below Integration of PACS RTMM update (delivery date 09.05.2003) Integration of SPIRE RTMM Issue 2.3 Integration of HIFI RTMM update (delivery date 28.03.2003) |  |

# Table of Content

1	SCOPE	13

2	Applicable and Reference Documents	14

2.1	Applicable Documents	14

2.2	Reference Documents	14

2.3	Abbreviations	15

3	Requirements and Boundary Conditions	17

3.1	Thermal Requirements	17

3.1.1	Lifetime	17

3.1.2	Temperature Requirements of Instruments within Cryostat	18

3.1.3	Temperature Requirements for LOU (outside Cryostat)	20

3.1.4	Temperature Requirements for Telescope	20

3.2	Thermal Environment	21

3.2.1	Ground and Pre-Launch Phase	21

3.2.2	Early Orbit Phase	21

3.2.3	Operation Phase in L2 Orbit	22

4	DTMM Description	23

4.1	General	23

4.2	H-EPLM Model for Lifetime Calculation	23

4.3	H-EPLM Model with Implemented Instrument Models	24

4.4	Pressure Drop Model	24

5	DTMM Nodal Break Down	26

5.1	He Subsystem and Optical Bench Assembly	26

5.2	Instruments	32

5.2.1	PACS	32

5.2.2	SPIRE	34

5.2.3	HIFI	37

5.3	Heat Shields and Tank Suspensions	39

5.4	Cryostat Vacuum Vessel and Radiators	43

5.5	LOU and Telescope	49

5.6	Harness	53

5.7	HERSCHEL Sunshield and Sunshade with Struts	58

5.8	SVM with Struts and SVM Thermal Shield	62

6	Material Properties	65

6.1	MLI Thermo-Optical Properties and Performance Data	65

6.2	Thermal Conductivity Data	67

6.3	Specific Heat Capacity Data	70

6.4	Helium Properties	71

6.5	References for Material Properties	73

7	Thermal Analysis Results	74

7.1	Operation On Ground	74

7.1.1	On-Ground Lifetime	74

7.1.2	On-Ground Autonomy (closed HTT)	77

7.1.3	On-Ground Testing (IMT)	79

7.2	Pre-Launch and Early Orbit Phase	81

7.3	Operation in L2 Orbit	86

7.3.1	Steady State Analysis for Hot and Cold Case Conditions	86

7.3.2	Sensitivity Analysis for Lifetime and EPLM Temperatures	90

7.3.3	Transient Analysis for S/C Operations in Orbit	96

7.4	Transient Analysis with In-Orbit Instrument Timeline	99

7.4.1	PACS Interface Temperatures and Heat Flows	100

7.4.2	SPIRE Interface Temperatures and Heat Flows	104

7.4.3	HIFI Interface Temperatures and Heat Flows	109

7.4.4	Instrument Heat Load on HTT and He Mass Flow	111

7.4.5	Sensitivity Analysis	115

7.5	Lifetime Calculation	119

8	Summary and Conclusions	120

9	ANNEX 1:   Nodal Temperature Listing	121

# Table of Figures

Figure ‎3.2-1:	Solar Aspect Angels on H-EPLM at L2	22

Figure ‎5.1-1:	Nodal Break Down of HTT and SFW	26

Figure ‎5.1-2:	Nodal Break Down of Optical Bench with Instruments	27

Figure ‎5.1-3:	Beam Pattern for the Three Instruments	28

Figure ‎5.1-4:	Nodal Break Down of OB Ventline	29

Figure ‎5.2-1:	Reduced PACS Instrument TMM	32

Figure ‎5.2-2:	Reduced SPIRE Instrument TMM	34

Figure ‎5.2-3: 	Reduced HIFI Instrument TMM	37

Figure ‎5.3-1:	Nodal Break-Down of Tank Suspensions	39

Figure ‎5.3-2:	Nodal Break-Down of Tanks and Heat Shield 1	40

Figure ‎5.4-1:	CVV Nodal Break-Down	44

Figure ‎5.4-2:	Cryostat Baffle and Cover Nodal Break-Down (Cover open & closed View)	45

Figure ‎5.4-3: 	LOU Windows / Baffles	46

Figure ‎5.5-1:	H-EPLM GMM External Overall View including H-SVM RGMM	49

Figure ‎5.5-2:	Telescope GMM	50

Figure ‎5.5-3:	Nodal Break-Down of LOU Waveguides and Harness	51

Figure ‎5.6-1:	Harness Chart used in TMM	53

Figure ‎5.7-1:	HSS Nodal Break-Down (upper: MLI nodes, lower: structural nodes)	59

Figure ‎5.8-1:	H-RSVM, SVM Thermal Shield and SVM/CVV Struts	63

Figure ‎6.2-1:	Thermal Conductivity of S-Glass GFRP Tank Suspensions and GFRP Struts	67

Figure ‎6.2-2:	Thermal Conductivity of T300 CFRP Tank Suspensions and M40A CFRP	67

Figure ‎6.2-3:	Thermal Conductivity of Harness Wires	68

Figure ‎6.2-4:	Thermal Conductivity of Harness Wire Insulation Materials /14/	68

Figure ‎6.2-5:	Thermal Conductivity of Copper Cooling Strap Materials	69

Figure ‎6.3-1:	Specific Heat Capacity of Aluminium and Titanium /14/	70

Figure ‎6.4-1:	Heat of Vapourization of Helium 4	71

Figure ‎6.4-2: 	Vapour Density of Helium (Ref. /5/)	72

Figure ‎6.4-3:	Volume Specific Heat Capacity of Liquid He on Saturation Line	72

Figure ‎7.1-1:	CVV Heat Flow Chart for On-Ground Environment	74

Figure ‎7.1-2:	HTT Heat Flow Sensitivity for Operation on Ground	76

Figure ‎7.1-3:	HOB Temperature Sensitivity for Operation on Ground	76

Figure ‎7.1-4:	Warm-up of HTT for Different HOT Mass Flow Rates	78

Figure ‎7.1-5:	Floating HOT Mass Flow Rate due to Parasitic Heat Load only	78

Figure ‎7.1-6:	Warm-up of Heat Shields for 25 mg/s HOT Mass Flow Rate	79

Figure ‎7.1-7:	CVV Heat Flow Chart for IMT	80

Figure ‎7.1-8:	OBA Heat Flow Chart for IMT (SPIRE Spectrometer Mode)	80

Figure ‎7.2-1:	HTT Temperature Evolution During Nominal Launch Phase	81

Figure ‎7.2-2:	Heat Shield Temperature Evolution During Pre-Launch Phase	82

Figure ‎7.2-3:	H-EPLM Temperatures During In-Orbit Cool-Down (25 h launch delay)	83

Figure ‎7.2-4:	HTT Temperature During In-Orbit Cool-Down	84

Figure ‎7.2-5:	Telescope Cool-Down Rate after Decontamination (Cover still closed)	84

Figure ‎7.2-6:	Helium Mass Flow and Mass Loss During In-Orbit Cool-Down	85

Figure ‎7.3-1:	H-EPLM Temperature Distribution for Hot Case Environment at L2	87

Figure ‎7.3-2: 	CVV Heat Flow Chart for Hot Case Environment at L2	88

Figure ‎7.3-3:	CVV Heat Flow Chart for Cold Case Environment at L2	88

Figure ‎7.3-4: 	HPLM internal Heat Flow Chart for Average Instrument Dissipation and Hot Case Environment at L2	89

Figure ‎7.3-5:	Lifetime Sensitivity for CVV Internal Parameter Variations	93

Figure ‎7.3-6:	Lifetime Sensitivity for CVV External Parameter Variations	93

Figure ‎7.3-7:	Sensitivity of CVV Temperature for Operation at L2	94

Figure ‎7.3-8:	Sensitivity of Sunshade MLI Temperature for Operation at L2	95

Figure ‎7.3-9:	Sensitivity of Sunshield MLI Temperature for Operation at L2	95

Figure ‎7.3-10:	Sensitivity of Telescope Temperature for Operation at L2	96

Figure ‎7.3-11:	Transient Cool-Down of Telescope after S/C Rotation 30° around Y-Axis	97

Figure ‎7.3-12:	Transient Cool-Down of LOU Baseplate after S/C Rotation 30° around Y-Axis	97

Figure ‎7.3-13:	Transient Cool-Down of CVV after S/C Rotation 30° around Y-Axis	98

Figure ‎7.3-14:	Transient Cool-Down of HTT after S/C Rotation 30° around Y-Axis	98

Figure ‎7.4-1:	PACS L0 Interface Temperatures	100

Figure ‎7.4-2:	PACS L0 Interface Heat Flows	100

Figure ‎7.4-3:	PACS L0 Interface Temperatures during Recycling	101

Figure ‎7.4-4:	PACS L0 Interface Heat Flows during Recycling	101

Figure ‎7.4-5:	PACS L1 Interface Temperatures	102

Figure ‎7.4-6:	PACS L1 Interface Heat Flows	102

Figure ‎7.4-7:	PACS L2 Interface Heat Flows	103

Figure ‎7.4-8:	SPIRE L0 Interface Temperatures	104

Figure ‎7.4-9:	SPIRE L0 Interface Heat Flows	104

Figure ‎7.4-10:	SPIRE L0 Interface Temperatures during Recycling	105

Figure ‎7.4-11:	SPIRE L0 Interface Heat Flows during Recycling	105

Figure ‎7.4-12:	SPIRE L1 Interface Temperatures	106

Figure ‎7.4-13:	SPIRE L1 Interface Heat Flows	106

Figure ‎7.4-14:	SPIRE L3 Interface Temperatures	107

Figure ‎7.4-15:	SPIRE L3 Interface Heat Flows	107

Figure ‎7.4-16:	SPIRE L2 Interface Heat Flows	108

Figure ‎7.4-17:	HIFI L0 Interface Temperature	109

Figure ‎7.4-18:	HIFI L0 Interface Heat Flow	109

Figure ‎7.4-19:	HIFI L1 Interface Temperature and Stability	110

Figure ‎7.4-20:	HIFI L1 Interface Heat Flow	110

Figure ‎7.4-21:	HTT Temperature and He Mass Flow	111

Figure ‎7.4-22:	Total Instrument Heat Load on HTT (different scales on Y-axis)	112

Figure ‎7.4-23:	Total Instrument Heat Load on L1 Ventline	113

Figure ‎7.4-24:	Total Instrument Heat Load on L2 (Optical Bench Plate)	113

Figure ‎7.4-25:	Total Instrument Heat Load on L2 (Optical Bench Plate)	114

Figure ‎7.4-26:	HTT Temperature for Different Conditions	115

Figure ‎7.4-27:	Helium Mass Flow for Different Conditions	116

Figure ‎7.4-28:	PACS L0 Temperature for Different Conditions	117

Figure ‎7.4-29:	SPIRE L0 Temperature for Different Conditions	117

Figure ‎7.4-30:	PACS L1 Temperature for Different Conditions	118

Figure ‎7.4-31:	SPIRE L1 Temperature for Different Conditions	118

List of Tables

Table ‎3.1-1:	PACS Temperature Limits	18

Table ‎3.1-2:	SPIRE Temperature Limits	18

Table ‎3.1-3:	HIFI Temperature Limits	19

Table ‎3.1-4:	LOU Temperature Limits	20

Table ‎3.1-5:	Telescope Temperature Limits	20

Table ‎5.1-1:	Item List for Tanks, Ventline and Optical Bench	31

Table ‎5.2-1:	Item List for PACS	33

Table ‎5.2-2:	 Item List for SPIRE	36

Table ‎5.2-3:	Item List for HIFI	38

Table ‎5.3-1:	Item List for Heat Shields	42

Table ‎5.4-1:	Item List for CVV and Cryostat Baffle	48

Table ‎5.5-1:	Item List for LOU and Telescope	52

Table ‎5.6-1:	Modelling of the CVV Internal Harness Branches in the EPLM TMM	53

Table ‎5.6-2:	CVV Internal Harness Data for PACS, SPIRE and HIFI	55

Table ‎5.6-3:	CVV External SIH Data	56

Table ‎5.6-4:	CVV Internal CCH Data, values not yet updated (Issue 2 status)	57

Table ‎5.6-5:	CVV External CCH Data, values not yet updated (Issue 2 status)	57

Table ‎5.7-1:	HSS related Items	61

Table ‎5.8-1:	SVM and SVM Shield related Items	64

Table ‎6.1-1:	Overview on Herschel MLI Performance Data	66

Table ‎7.1-1:	Sensitivities for Operation on Ground	75

Table ‎7.1-2:	Predicted I/F Temperatures for IMT on Ground	79

Table ‎7.3-1:	Analysis Results for Hot and Cold Case Environment	86

Table ‎7.3-2:	In-orbit Sensitivities due to Uncertainties of Physical Parameters inside CVV	90

Table ‎7.3-3:	In-orbit Sensitivities due to Uncertainties of Physical Parameters outside CVV	91

Table ‎7.3-4:	Uncertainties of HSS and Telescope Temperature at L2	92

Table ‎7.4-1:	Average Instrument Dissipation versus IIDA Allocation	111

# SCOPE

This document describes the status of the HERSCHEL EPLM DetailedThermal Mathematical Model (DTMM) and Geometrical Mathematical Model (DGMM) at 30th June 2003 that is used as the actual working baseline. The nodal break down and the corresponding assumptions are described in detail. The DTMM with the data described in this document is referenced “herschel.d, Issue 3, dated 30/06/03”.

Material properties used in the DTMM/DGMM are also reported in this document. Finally, the analysis results obtained from this reference DTMM are reported, too. The results are shown basically in form of temperature distribution and heat flow charts. A comprehensive sensitivity analysis is performed with respect to lifetime and EPLM temperatures. Instrument interface temperatures are calculated using a dedicated instrument timeline of 6 x 48h which includes transient operation of and switching between 5 different instrument modes. Finally lifetime calculations are carried out based on the thermal analysis results including transient in-orbit cool down.

# Applicable and Reference Documents

## Applicable Documents

AD 01	HERSCHEL/PLANCK Instrument Interface Document IID Part A, Doc.No.: SCI-PT-IIDA-04624, Issue 2/0, 31.07.2001

AD 02	HERSCHEL/PLANCK Instrument Interface Document IID Part B for PACS, Doc.No.: SCI-PT-IIDB/HIFI-02126, Issue 2/0, 31.07.2001

AD 03	HERSCHEL/PLANCK Instrument Interface Document IID Part B for SPIRE, Doc.No.: SCI-PT-IIDB/HIFI-02124, Issue 2/0, 31.07.2001

AD 04	HERSCHEL/PLANCK Instrument Interface Document IID Part B for HIFI, Doc.No.: SCI-PT-IIDB/HIFI-02125, Issue 2/0, 31.07.2001

AD 05	H-EPLM Environment & Test Requirements Specification, Doc.No.:  HP-2-ASED-SP-0004,

AD 06	HERSCHEL/PLANCK System Requirements Specification, Doc.No.: SCI-PT-RS-05991, Issue

AD 07	Herschel EPLM Interface Specification; HP-2-ASPI-IS-0039; Issue 3

AD 08	Herschel EPLM Thermal Interfaces; HP-2-ASP-TN-0413; Issue 1

## Reference Documents

RD 01	Hypothesis and Methods for Lifetime Calculations; Doc.No.: HP-2-ASED-TN-0065, Issue 1.1

RD 02	Harness Inputs for Thermal Analysis Doc.No.: HP-2-ASED-TN-0010, Issue 1.1, dated 08.05.02

RD 03	Reduced PACS Instrument TMM provided by PACS on 09.05.2003

RD 04	Reduced SPIRE Instrument TMM, Issue 2.3 provided by SPIRE on 28.03.2003

RD 05	Reduced HIFI Instrument TMM provided by HIFI on 02.04.2003

RD 06	He System Description, HP-2-ASED-RP-0034, Issue 1

RD 07	Thermal Mathematical Modelling Methods of HPLM Ventline on Optical Bench, HP-2-ASED-TN-0056, Draft Issue, dated 10.06.02

RD 08	Evaluation of LINDE/ESTEC-MLI Measurements and Transformation to the ISO Cryostat MLI Design, Doc.No.: ISO.TN-B1430.007, dated 12.07.88

RD 09	J. Doenecke:  Survey and Evaluation of Multilayer Insulation Heat Transfer Measurement, ICES July 1993

RD 10	PACS FPU Drawing No. PACS-KT-ICD-0000W1.22, dated 04.09.01

RD 11	SPIRE Interface Drawing No. 5264 300, dated 30.07.01

RD 12	HIFI-FPU External Configuration Drawing No. 455-3-001-0, dated 29.05.01

RD 13	H-EPLM Pressure Drop Analysis, HP-2-ASED-TN-0071 Iss. 1, 14.11.2002

RD 14	M. Sander: ISO Thermal Mathematical Model, Submodel VENT, Version 3.00, 24.02.1994

RD 15	Test Report of the Additional Pressure Drop Measurements of DASA Valve #990-11 at Different Mass Flows and Temperatures, ISO-TR-BCGI0.008, Issue 1, 02.11.1993

RD 16	Flexible Thermal Link – Test Evaluation Report, ESTEC Contract No.: 11200/94/NL/FG, August 1997

RD 17	Van Sciver et al: Thermal Conductance Values for Metallic Joints, Proc. Space Cryogenic Workshop, Berlin 1984

RD 18	INTELSAT X 02 Feed Assembly Specification, Doc.No.: NIA2.SP.00002.T.ASTR, Issue 2, dated 01.10.01

RD 19	PDR Collocation Handout “Thermal Analysis”; HP-2-ASED-HO-0013, dated 16.09.02

RD 20	TSS Design Justification, HP-2-ASED-TN-0081, dated 12.05.2003

RD 21	Procurement Specification for Herschel Spatial Framework, HP-2-ASED-PS-0016, Issue 2.1, dated 14.02.03

RD 22	Procurement Specification for Tank Support Suspensions, HP-2-ASED-PS-0017

RD 23	OBA Specification, HP-2-ASED-PS-0015, Issue 1.3, dated 17.01.03.

RD 24	Procurement Specification for H-PLM Internal MLI, HP-2-ASED-PS-0028, Issue 2, dated 07.03.03

RD 25	Procurement Specification for Herschel Support Structures, HP-2-ASED-PS-0026

RD 26	Procurement Specification for SVM Thermal Shield, HP-2-ASED-PS-0034

RD 27	Procurement Specification for Herschel Telescope Mounting Structure, HP-2-ASED-PS-0037

RD 28	Procurement Specification for Herschel External MLI, HP-2-ASED-PS-0029, Issue 1, dated 29.07.02

Note: 	Further References concerning material properties are listed in section ‎6.5 separately.

## Abbreviations

ASED	Astrium GmbH

ASP	Alcatel Space

BOL	Begin of Life

CVV	Cryostat Vacuum Vessel

EOL	End of Life

GMM	Geometrical Mathematical Model

HSS	Herschel Sunshield & Sunshade

IR	InfraRed

OBA	Optical Bench Assembly

OSR	Optical Solar Reflector

SFW	Spatial FrameWork

SS	Summer Solstice

SSD	Sunshade

SSH	Sunshield

TMM	Thermal Mathematical Model

TSS	Tank Support Suspensions

WS	Winter Solstice

# Requirements and Boundary Conditions

## Thermal Requirements

### Lifetime

The relevant requirements regarding the H-EPLM lifetime are the following [AD 06]:

SPER-005:	The spacecraft shall have a nominal lifetime of 3.5 years from launch till end of the mission. This duration includes an allocation of 6 months for the transfer to the L2 Lissajous orbit.

SPLM-035:	The cryostat and its internal insulation shall meet the specified nominal lifetime and temperature requirements. The amount of cryogen shall be sized accordingly and shall include a margin of 15%.

The on-ground autonomy shall be 6 days [AD 01].

For lifetime calculations a special thermal-mathematical model (TMM) shall be applied. In this model the instrument TMMs are replaced by the instrument interface nodes of the different temperature levels. Herewith the following maximum instrument dissipations as specified in the IIDA [AD 01] shall be taken into account:

Level 0 :  10 mW

Level 1 :  25 mW

Level 2 :  35 mW

Level 3 :  15 mW

An average thermal environment at L2 orbit to be assumed for lifetime prediction as well as a procedure for lifetime calculation has been agreed with ESA, ASP and ASED. The details are reported in [RD 01].

### Temperature Requirements of Instruments within Cryostat

This section will be updated after agreement on IID-B's, Issue 3.

The temperature limits required at the instrument interfaces are specified in the instrument interface control documents IIDBs for PACS [AD 02], SPIRE [AD 03] and HIFI [AD 04] and are compiled in Table ‎3.1-1 to Table ‎3.1-3.

| Instrument Interface | Temp. Level | TMM Node | Operating | Cooler recycling | Non-operating |
| --- | --- | --- | --- | --- | --- |
| PACS |  |  | Min.[K] | Max.[K] | [K] | Min. | Max. |
| Red Detector | L0 | 721 | 1.6 | 1.75 | 1.75 |  | 60°C *) 85°C **) (TBC) |
| Blue Detector | L0 | 732 | 1.6 | 2.0 | 2.0 |  | 60°C 85°C (TBC) |
| Cooler Pump | L0 | 761 | 1.6 | 2.2 | 10 |  | 60°C 85°C (TBC) |
| Cooler Evaporator | L0 | 762 | 1.6 | 2.0 | 2.0 |  | 60°C 85°C (TBC) |
| Optics/Structure assy. | L1 | 781 782 783 | 2.5 | 5.0 | 5.0 | NA | 60°C *) 85°C **) (TBC) |

*)	Continuous temperature limit

**)	Short-duration temperature limit for bake-out during a maximum of TBD hours

Table ‎3.1-1:	PACS Temperature Limits

| Instrument Interface | Temp. Level | TMM Node | Operating | Cooler recycling | Non-operating |
| --- | --- | --- | --- | --- | --- |
| SPIRE |  |  | Min.[K] | Max.[K] | [K] | Min. | Max. |
| Detector Enclosure | L0 | 814 | 0 | 2.0 | 2.0 | NA | 80°C during 72 h |
| Cooler Pump | L0 | 815 | 0 | 2.0 | 10 | NA | bake-out |
| Cooler Evaporator | L0 | 816 | 0 | 2.0 | 2.0 | NA | 60°C *) |
| SPIRE OB units | L1 | 800 830 | 0 | 6 | 6 | NA |  |
| PM-JFETs | L2 | 831 | TBD | 15 | 15 | NA |  |
| SM-JFET | L2 | 832 | TBD | 15 | 15 | NA |  |

*)	Continuous temperature limit

Table ‎3.1-2:	SPIRE Temperature Limits

| Instrument Interface | Temp. Level | TMM Node | Operating | Switch-off | Non-operating |
| --- | --- | --- | --- | --- | --- |
| HIFI |  |  | Min.(K) | Max.(K) |  | Min. | Max. |
| L0 boundary | L0 | 949 | 0 | 2 | 40°C | 0 K | 60°C *) (TBC) |
| L1 boundary | L1 | 939 | TBD | 6 | 40°C | 0 K | 60°C *) (TBC) |
| FPU structure | L2 | 910 | TBD | 15 | 40°C | 0 K | 60°C *) (TBC) |

*)	Continuous temperature limit

**)	Short-duration temperature limit for bake-out during a maximum of TBD hours

Table ‎3.1-3:	HIFI Temperature Limits

Temperature Stability Requirements of HIFI as specified in AD 04 [not agreed by ASED]:

During operation the following temperature changes shall not be exceeded:

Level 2 parts:  0.015 K per 100 s

Level 1 parts:  0.006 K per 100 s

Level 0 parts:  0.006 K per 100 s

### Temperature Requirements for LOU (outside Cryostat)

As specified in AD 04 the HIFI Local Oscillator Unit (LOU) shall not exceed the temperature limits at the mounting interfaces compiled in following Table ‎3.1-4.

| Instrument Interface | Thermal node No. | Operating | Functional testing | Start-up | Switch-off | Non-operating |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | Min.(K) | Max.(K) | Max.(K) | Max.(K) | Max.(K) | Min.(K) | Max.(K) |
| LOU | 4200 | 90 | 150 | 298 | 80 | 303 | 60 TBC | 328 |

Table ‎3.1-4:	LOU Temperature Limits

### Temperature Requirements for Telescope

For the HERSCHEL Telescope, the following requirements exist [AD 01]:

|  | Thermal node No. | Operating | Contamination Release (3 weeks) | Non-operating |
| --- | --- | --- | --- | --- |
|  |  | Min.(K) | Max.(K) | Min.(K) | Max.(K) | Min.(K) | Max.(K) |
| Telescope | 8000 | 70 | 90 | 313 | 323 | 55 TBC | 328 |

Table ‎3.1-5:	Telescope Temperature Limits

## Thermal Environment

### Ground and Pre-Launch Phase

The He filled PLM is in a temperature controlled environment at 22(3°C [AD 05].

During transport and storage different thermal environment apply, ranging from –10°C to 50°C.

### Early Orbit Phase

The thermal loads to be applied for the H-EPLM during the launch and early orbit phase are defined in detail in [AD 05].

Solar constant:

The applicable values of the solar constant for the early orbit phase (BOL) are:

- 1425 W/m²  during Winter Solstice  (WS)

- 1325  W/m² during Summer Solstice (SS)

Albedo is the fraction of incident solar radiation that is reflected from the earth back into space. A value of 0.3 0.05 shall be used.

Earth Infrared Thermal Radiation

The Earth infrared radiation shall be assumed to be that of a black body with a characteristic temperature of 288 K. The average infrared radiation emitted by Earth is 230 W/m2, with variations between 150 W/m² and 350 W/m².

From the a.m. data following load cases can be derived:

Hot Case:	WS solar constant, max. Earth IR radiation, 0.35 albedo

BOL thermo-optical properties, Solar power generator in shunt mode

Cold Case:	SS solar constant, min. Earth IR radiation, 0.25 albedo

BOL thermo-optical properties, Solar power generator in operating mode

### Operation Phase in L2 Orbit

During on-orbit operation at L2 the extremes of solar constant are [AD 05]:

- 1405 W/m² during Winter Solstice  (WS)

- 1287 W/m² during Summer Solstice (SS)

During HERSCHEL mission phases and operational modes, the solar aspect angle will be maintained at 30 deg around the Y-axis and at 1 deg around the X-axis.

Figure ‎3.2-1:	Solar Aspect Angels on H-EPLM at L2

From the a.m. data the following load cases can be derived:

Hot Case:	WS solar constant with 0° solar aspect angle

EOL thermo-optical properties

Cold Case:	SS solar constant with 30° solar aspect angle around Y-axis

BOL thermo-optical properties

The temperatures of the H-EPLM structure attachment points on the SVM (conductive I/F) and the temperatures of the SVM outer surfaces like top panel MLI (radiative I/F) are considered according to [AD07] and [AD08].

# DTMM Description

## General

The H-EPLM is written in ESATAN format V 8.7, the geometry model is written in ESARAD format V 5.1.

The following main calculation modes can be operated:

G	Operation on Ground (steady state)

X	Instrument Testing on Ground (steady state)

P	Prelaunch: On-Ground Autonomy (SUBCASE=1) and Launch Autonomy (SUBCASE=2), including pre-cooling and HOT refill

L	Launch until fairing jettisoning

T	In-orbit transient cool down with telescope decontamination heating

O	Operation at L2 orbit, including nominal steady state modes (hot, cold), transient orbit timeline, safe mode and a lifetime calculation mode acc. to [RD 01] (adjustable via control variables SUBCASE, IMODE, TRANS)

## H-EPLM Model for Lifetime Calculation

The He mass flow (MHe) is calculated based on the sum of all heat load into the HTT (( QHTT) and the Helium heat of vapourization (hv) for the average environmental conditions at L2. As required in [AD 06], the nominal initial amount of He m0 includes a margin of 15%. The increased Helium consumption (mtrans) during the in orbit cool down period (ttrans) is also considered for the lifetime prediction. In addition the residual He gas (mresidual) after all HeII is evaporated, and that can not be used for vapour cooling, is considered. Furthermore, a lifetime correction (tuncertainty) is introduced reflecting parameter variations. Finally a maximum loss of 1% lifetime is considered due to DLCM. Thus, the nominal (contractual) lifetime is calculated according to following formula:

Lifetime = 0.99*((m n - m trans - m residual) / M He,avg  + t trans   –t uncertainty)

with

mn	nominal amount of He at lift off,			mn = 0.98/1.15 * HeII density * HTT volume

m trans	He consumption during in-orbit cool down,	m trans  = output of Figure ‎7.2-6

m residual	residual He gas in tank at EOL,			m residual = 0.94 * GHe density * HTT volume

MHe	mass flow at L2 (at condition defined in RD01),		MHe = ( QHTT / hv

t trans	duration of transient cool down until HTT@1.65K,	t trans = output of Figure ‎7.2-6

t uncertainty = Lifetime correction due to RSS input variations

The He mass flow MHe is determined by the sum of all heat flow into the tank and is calculated for in orbit steady state condition applying the heat load allocations defined in [AD 01].

## H-EPLM Model with Implemented Instrument Models

The supplied Instrument Interface Models [RD 03, RD 04, RD 05] are implemented as submodels in the overall H-EPLM Model structure.

## Pressure Drop Model

The pressure drop calculation within the ESATAN model uses the detailed numerical pressure drop model as described in [RD 13], with minor updates concerning external tube routing, PPS characteristics and nozzle layout.

The detailed pressure drop model is based on the pressure drop model used in the ISO TMM [RD 14] for the final flight predictions. In the detailed model, the pressure drop of the individual vent line components (e.g. PPS, straight pipes, bends, t-pieces, valves, heater, nozzles…) is calculated by dedicated subroutines. Most of these subroutines are directly inherited from the ISO model, with the exceptions being

- PPS: The Herschel phase separator is different from the ISO PPS. A mini-model-type regression function is used to represent the flight model porous plug which was characterised as Sample 5 in the Herschel PPS Pre-Development test campaign. The regression formula is 
			
with pressure p [mbar], mass flow rate [mg/s], temperature T [K], and fit parameters a=6.039899454, b=1.532479916, and c=0.439538736.

- Electromagnetic valves: The original valve function from ISO results in unrealistically small pressure drop values (below 10-10 Pa per valve) for the Herschel conditions. The function has therefore been replaced by a mini-model type regression which represents the measurements of the external valves (without filters) carried out in the ISO programme [RD 15].

- Filter: In the original ISO TMM, the filter function is not used in the pressure drop calculations. It is therefore also not called in the current detailed pressure drop model.

- CVSE Pump: For the nominal ground steady-state case, a cryo vacuum pump is attached to the V502. The characteristic of this pump is represented by a newly introduced function which calculates the inlet pressure depending on the mass flow rate and the gas temperature. This feature is currently not being used within the TMM.

The pressure drop model is called from ESATAN with the following arguments:

CALL CALCMD (TIMEM, MDOT, T10, T546, T563, T586, T1030, T2030, T3030, T4031, IPPS, INOZZ, SUCCES)

This call calculates the mass flow rates depending on the tank temperature and the temperature distribution along the vent line. Input arguments are

TIMEM:	current time step, used for control output

MDOT:		initial value for mass flow rate calculation, new value after calcmd returns

T10-T4031:	temperatures of the individual elements

IPPS:	integer switch: =1 for flow through PPS, =0 for bypass via V104, <0 for closed HTT

INOZZ:	integer switch: =1 for flow through small nozzles, =2 flow through big and small nozzles, <= 0 for flow via V502

SUCCESS:	integer flag: =0 if iteration was successful (calcmd output)

To calculate the tank temperature depending on a given mass flow rate and temperature distribution along the vent line, the pressure drop model is called with the subroutine

CALL CALCTT (TIMEM, MDOT, T10, T546, T563, T586, T1030, T2030, T3030, T4031, IPPS, INOZZ, SUCCES). This subroutine uses the same arguments as for the mass flow calculation routine calcmd.

CALCMD and CALCTT both call the internal subroutine DPVENT and apply the Regula Falsi to iterate the mass flow rate until the pressure drop along the vent line, together with the nozzle inlet pressure calculated from the choked flow conditions, is equal to the pressure in the tank as defined by the tank temperature (or vice versa for CALCTT). The subroutine DPVENT calculates and sums up the respective pressure drop contributions of the individual vent line components one by one going upstream from the external nozzles to the phase separator. Bends in the pipe routing are modelled using equal or smaller bending radii than defined in the drawings. For the two pairs of parallel redundant valves V103/V106 and V501/V503, it is assumed that the respective valve with the shorter pipe routing does not open. Filling and safety lines as well as the filling port are not represented in the current version of the pressure drop model.

The Fortran code for CALCMD, CALCTT, and all functions and routines which are used internally by the pressure drop model is included in the file calcmd.f, which has to be compiled and transformed to an object library named USRLIB.a. The makefile delivered with the TMM automatically performs these tasks. The Esatan preprocessor requires that the calling names of the subroutines provided in the object library be listed in the file USRLIB.DAT.

The detailed pressure drop model is completely coded in Fortran 77. Thus it can be used either as a stand-alone program with the temperatures of the vent line sections being defined as input, or it can be called from the ESATAN Herschel TMM to perform transient analyses with variable mass flow rate.

The dominating contributions to the overall pressure drop in the orbit cool-down and operation phases are generated by the PPS and the external nozzles. The nozzle throat diameters are adjusted for the combination of desired tank temperature, temperature distribution along the vent line and mass flow rate, and are hard-coded in the pressure drop model. Changes with an impact on the mass flow rate or temperatures will therefore also have an impact on the average tank temperature. The nozzle diameters used in the current version are 0.975 mm for two small and 2.121 mm for one big nozzle. With these settings and the calculated mass flow rates, a nominal HTT temperature of 1.65 K for orbit hot case with average instrument dissipation and a maximum mass flow rate below 20 mg/s (as required by the PPS) during the in-orbit cool-down are achieved.

Detailed information on the calculation fundamentals for each vent line component as well as representative results are given in [RD 13].

# DTMM Nodal Break Down

## He Subsystem and Optical Bench Assembly

The Optical Bench Assembly (OBA) is mounted on top of the HTT via the so called Spatial Framework (SFW). The SFW consists of a frame made of aluminium and struts to the HTT made out of T300 CFRP. The OB is connected to the aluminium frame by means of Titanium blades. The SFW itself is attached to the CVV structure by the tank suspension straps. The nodal break down of the SFW is shown in Figure ‎5.1-1.

Figure ‎5.1-1:	Nodal Break Down of HTT and SFW

The OB with the instruments is covered with the OB heat shield, see Figure ‎5.1-2. The opening for the beam entrance is modelled with cylindrical baffles, thermally (and mechanically) attached to the heat shield 2 (node 2050) and to the OB shield (node 315). The thermal and material properties are compiled in Table ‎5.1-1. The OB shield baffle has rectangular cut-outs reflecting the beam pattern for the three instruments, see Figure ‎5.1-3.

Figure ‎5.1-2:	Nodal Break Down of Optical Bench with Instruments

| Beam Pattern acc. to I/F Drawing | Instrument Shield Baffle in TMM (node 315) |
| --- | --- |

Figure ‎5.1-3:	Beam Pattern for the Three Instruments

A schematic overview of the OB ventline modelling is given in Figure ‎5.1-4.

Figure ‎5.1-4:	Nodal Break Down of OB Ventline

| Item | Node | Material / Components | Mass | Size | IR | Unit Level | Remark |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Emiss. | Requirement |  |
| He II Tank (HTT) | 10 | superfluid Helium (He II) Al tank (Al 5083, 3.3547) | 337 kg 141.8 kg | 2367 l (cold volume) D=1.63 m, h=1.352 m |  |  |  |
| MLI on He II Tank low cyl. upp. | 111 112 113 | 20 layers (tbc) | 1.1 kg 3.2 kg 1.1 kg | A=3.26m² A=2.91 m² (D=1.63m, h=0.569m) A=2.94m² | 0.05 |  |  |
| Aux. He I Tank (HOT) | 20 | *90% HeI (=~8.7 kg He on ground) ellipsoid shaped Al tank (Al 5083) | 13 kg | 78 l (cold volume) D=0.88 m, h=0.252 m |  |  |  |
| MLI on He I Tank low upp. | 121 122 | 10 layers 10 layers | 0.45 kg 0.45 kg | A=0.66m² A=0.66m² | 0.05 |  |  |
| Lower Spatial Framework (Aux. tank) | 201-203 | AL frame (Al 5083) Corner struts T300 to HTT center struts T300 to HTT |  | 4 x 225 mm², l = 80 mm 4 x 160 mm², l = 200 mm |  | R-SFW-290 [RD 22] R-SFW-300 [RD 22] |  |
| Upper Spatial Framework (OB) | 211-213 | AL frame (Al 5083) Corner struts T300 center struts T300 |  | 4 x 225 mm², l = 80 mm 4 x 160 mm², l = 200 mm |  | R-SFW-290 [RD 22] R-SFW-300 [RD 22] |  |
| Optical Bench (OB) | 371- 381 | Aluminium structure 4 Titanium blades to AL frame of SFW | 60 kg | D=1.63m,H=70mm,2.5mm skins A/L = 28.6 mm Ti5Al2.5Sn | 1.0 | R-OBA-330 [RD 23] R-OBA-145 [RD 23] | A) |
| Instrument Shield | 310 311 315 | Al (cylinder) Al (top), see Figure ‎5.1-2 Al baffle with 0.025 m² aperture (cut-out), see Figure ‎5.1-3 | 3.3 kg 4.5 kg 0.12 kg | A=1.70m², s= 0.8mm A=2.18m², s= 0.8mm D=310 mm, s= 0.8mm cylinder part, inside cylinder part, inside | 0.05 0.05 0.05(±X) 0.8 0.05 | R-OBA-326 [RD 23] R-OBA-325 [RD 23] R-OBA-410 [RD 23] for emissivities | A) A) |
| GHe Ventline between HTT and Level 1 | 510-514 | stainless steel tube |  | cross sect. 19.6mm2 (D=13 mm, d=12 mm) |  |  |  |
| GHe Ventline Level 1 | 520-546 | Al tube CFRP T300 brackets to OB |  | cross sect. 39.6mm2 (D=13 mm, d=12 mm), incl. fins A/l = 2.393mm |  | R-OBA-360 [RD 23] | A) |
| GHe Ventline between Level 1 and Level 2 | 550-554 | Al tube (not coupled to OB) |  | cross sect. 19.6mm2 (D=13 mm, d=12 mm) |  | R-OBA-365 [RD 23] | A) |
| GHe Ventline Level 2 | 560-563 | Al tube on OB Al brackets to OB |  | cross sect. 39.6mm2 (D=13 mm, d=12 mm), incl. fins A/l = 19.60mm |  | R-OBA-370 [RD 23] | A) |
| GHe Ventline between Level 2 and Level 3 | 570-571 | Al tube (not coupled to OB) |  | cross sect. 39.6mm2 (D=13 mm, d=12 mm), incl. fins |  | R-OBA-365 [RD 23] | A) |
| GHe Ventline Level 3, SPIRE JFETs | 580-586 | Al tube CFRP T300 brackets to OB |  | cross sect. 39.6mm2 (D=13 mm, d=12 mm), incl. fins A/l = 1.45mm |  |  |  |
| GHe Ventline between Level 3 and HS1 | 590-592 | stainless steel tube |  | cross sect. 19.6mm2 (D=13 mm, d=12 mm) |  |  |  |
| Filling Port / Tubes | 440-452 | stainless steel |  | ISO design |  |  |  |
| MLI on Filling Tubes | 642-652 | 10 layers |  | ISO design |  |  |  |

A) Detailed design not yet finalised, ASED PDR reference design assumed

Table ‎5.1-1:	Item List for Tanks, Ventline and Optical Bench

## Instruments

The Instrument Interface Thermal Mathematical Models (ITMMs) have been supplied by the instrument people [RD 03, RD 04, RD 05] in ESATAN format and are implemented as submodels in the overall H-EPLM TMM structure. SPIRE in addition has delivered an Interface Geometrical Mathematical Model (IGMM) in ESARAD format. Since no IGMMs of PACS and HIFI were available, they had to be established by ASED according to the corresponding FPU drawings in [RD 10] and [RD 12]. The IGMMs are implemented as submodels in the overall H-EPLM GMM.

### PACS

The PACS instrument TMM thermal network is illustrated in Figure ‎5.2-1. All thermal nodes except [743], [744], [753] and [754] are represented in this sketch. The relevant data of each instrument node are compiled in Table ‎5.2-1 together with the design data of the thermal links to the Level 0 and Level 1 interfaces.

Figure ‎5.2-1:	Reduced PACS Instrument TMM

| Item | Node | Material / Components | Mass | Size / Performance | IR | Unit Level | Remark |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | [kg] |  | Emiss. | Requirement |  |
| Red Detector I/F | 721 | Thermal link to HTT (L0) |  | 0.052 W/K @ 1.7K 1) |  | R-OBA-345 [RD 23] |  |
| Feed Through Blue Det. | 722 |  |  |  |  |  |  |
| Blue Detector I/F | 723 | Thermal link to HTT (L0) |  | 0.017 W/K @ 1.7K 1) |  | R-OBA-345 [RD 23] |  |
| Cooler Pump I/F | 761 | Cu, Thermal link to HTT (L0) | 0.15 | 0.044 W/K @ 1.7K 1) |  | R-OBA-345 [RD 23] |  |
| Evaporator I/F | 762 | Cu, Thermal link to HTT (L0) | 0.15 | 0.080 W/K @ 1.7K 1) |  | R-OBA-345 [RD 23] |  |
| Buffer | 763 | Al, PACS cooling strap to Evaporator I/F | 1.45 |  |  |  |  |
| Blue Detector | 751 | Al | 2.9 |  |  |  |  |
| Red Detector | 741 | Al | 2.25 |  |  |  |  |
| Blue Det. CRE | 752 | Al | 0.4 |  |  |  |  |
| Red Det. CRE | 742 | Al | 0.4 |  |  |  |  |
| CFRP strut Blue Det. | 753 |  |  |  |  |  |  |
| CFRP strut Red Det. | 743 |  |  |  |  |  |  |
| Harness Blue Det. Int. | 754 |  |  |  |  |  |  |
| Harness Red Det. Int. | 744 |  |  |  |  |  |  |
| Spectr. Housing | 712 | Al | 14.6 |  |  |  |  |
| Collimator Housing | 713 | Al | 13.5 |  |  |  |  |
| Phot. Housing | 714 | Al, Ti | 15.0 |  |  |  |  |
| Top Optics | 711 | Al | 14.2 | Apertures with filters: 0.002 m² | 0.26 1.0 |  |  |
| Grating | 731 | Al, Cu | 4.0 |  |  |  |  |
| Phot. L1 I/F | 781 | Cu Cooling strap to GHe ventline (L1) 2) |  | cross sect.: (20x1)mm, l=0.3m |  | R-OBA-345 [RD 23] |  |
| Collimator L1 I/F | 782 | Cu Cooling strap to GHe ventline (L1) 2) |  | cross sect.: (20x1)mm, l=0.3m |  | R-OBA-345 [RD 23] |  |
| Spec. L1 I/F | 783 | Cu Cooling strap to GHe ventline (L1) 2) |  | cross sect.: (20x1)mm, l=0.3m |  | R-OBA-345 [RD 23] |  |
| L2 IF (Phot.) | 772 | CFRP bracket to OB (L2) |  | A/L= 7.66 mm |  |  |  |
| L2 IF (Top Opt.) | 773 | CFRP bracket to OB (L2) |  | A/L= 15.3 mm |  |  |  |
| L2 IF (Spec/Coll.) | 771 | CFRP bracket to OB (L2) |  | A/L= 23.0 mm |  |  |  |

1)	Conductance includes R-OBA-345 and tank wall conductance of 0.4 W/K @ 1.7 K

2)	Detailed design not yet finalised, ASED PDR reference design assumed

Table ‎5.2-1:	Item List for PACS

### SPIRE

The SPIRE instrument TMM thermal network is illustrated in Figure ‎5.2-2. All thermal nodes are represented in this sketch and are also compiled in Table ‎5.2-2 together with the design and performance data of the thermal links to the Level 0, Level 1 and Level 3 interfaces.

Figure ‎5.2-2:	Reduced SPIRE Instrument TMM

| Item | Node | Material / Components | Mass | Size / Performance | IR | Unit Level | Remark |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | [kg] |  | Emissivity | Reqirement |  |
| PM Det. enclosure | 809 | Al, St. Steel, Invar, Silicon | 3.91 |  |  |  |  |
| SM Det. enclosure | 810 | Al, St. Steel, Invar, Silicon | 1.70 |  |  |  |  |
| Enclosure Strap | 811 |  | 6.16E-3 |  |  |  |  |
| Pump Strap | 812 |  | 6.16E-3 |  |  |  |  |
| Evap. Strap | 813 |  | 6.16E-3 |  |  |  |  |
| Enclosure Strap I/F | 814 | Thermal link to HTT (L0) | 45.4E-3 | 0.063 W/K @ 1.7K 1) |  | R-OBA-345 [RD 23] |  |
| Pump Strap I/F | 815 | Thermal link to HTT (L0) | 52.3E-3 | 0.044 W/K @ 1.7K 1) |  | R-OBA-345 [RD 23] |  |
| Evap. Strap I/F | 816 | Thermal link to HTT (L0) | 65.3E-3 | 0.080 W/K @ 1.7K 1) |  | R-OBA-345 [RD 23] |  |
| Cooler Pump | 817 | Ti | 0.15 |  |  |  |  |
| Cooler Shunt | 818 | Ti | 0.01 |  |  |  |  |
| Cooler Evaporator | 819 | Ti | 0.084 |  |  |  |  |
| Cooler Evapor. HS | 820 | Ti | 0.074 |  |  |  |  |
| Cooler Pump HS | 821 | Ti | 0.074 |  |  |  |  |
| PM Detector | 822 | Invar, Cu | 1.144 |  |  |  |  |
| SM Detector | 823 | Invar, Cu | 0.535 |  |  |  |  |
| L1 strap I/F1 | 800 | Cooling strap to GHe ventline (L1) 2) |  | cross sect.: (20x1)mm, l=0.220m |  | R-OBA-345 [RD 23] |  |
| L1 strap I/F2 | 830 | Cooling strap to GHe ventline (L1) 2) |  | cross sect.: (20x1)mm, l=0.220m |  | R-OBA-345 [RD 23] |  |
| Optical Bench | 803 | Stainless Steel feet / Vespel to HOB | 26.75 | aperture | 0.20 1.0 |  |  |
| RF Filter box | 804 | Al casing/structure | 1.465 |  |  |  |  |
| BSM | 805 |  | 1.10 |  |  |  |  |
| SMECm | 806 |  | 1.043 |  |  |  |  |
| PM Calibration | 807 |  | 0.03 |  |  |  |  |
| SM Calibration | 808 |  | 2.041E-4 |  |  |  |  |
| PM JFET Encl. | 801 | Al, Thermal coupl. to OB: 0.00504 W/K | 2.348 |  | 0.20 |  |  |
| PM JFET I/F | 831 | Cooling strap to Level 3 2) |  | cross sect.: (20x1)mm, l=0.3m |  |  |  |
| SM JFET Encl. | 802 | Al, Thermal coupl. to OB: 0.00405 W/K | 0.81342 |  | 0.20 |  |  |
| SM JFET I/F | 832 | Cooling strap to Level 3 2) |  | cross sect.: (20x1)mm, l=0.3m |  |  |  |

1)	Conductance includes R-OBA-345 and tank wall conductance of 0.4 W/K @ 1.7 K

2)	Detailed design not yet finalised, ASED PDR reference design assumed

Table ‎5.2-2:	 Item List for SPIRE

### HIFI

The HIFI instrument TMM thermal network is illustrated in Figure ‎5.2-3. All thermal nodes are represented in this sketch and are also compiled in Table ‎5.2-3 together with the design and performance data of the thermal links to the Level 0 and Level 1 interfaces.

Figure ‎5.2-3: 	Reduced HIFI Instrument TMM

| Item | Node | Material / Components | Mass | Size / Performance | IR | Unit Level | Remark |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | [kg] |  | Emiss. | Requirement |  |
| FPU Structure | 910 | Al | 35.72 | Aperture | 0.26 1.0 |  |  |
| Calib. Source Assy | 911 | Al | 1.5 |  |  |  |  |
| Focal Plane Chopper | 912 | Al | 0.40 |  |  |  |  |
| Dipl. Rooftop transl. | 913 | Al | 0.59 |  |  |  |  |
| 2nd stage amplifier | 914 | Al | 2.30 |  |  |  |  |
| L2 boundary | 919 |  |  | thermal coupl. to OB: 1.2 W/K |  |  |  |
| Mixer Sub Assy | 920 | Al | 2 |  |  |  |  |
| 1st stage amplifier | 921 |  |  |  |  |  |  |
| EMC filtering | 922 |  |  |  |  |  |  |
| Magnet current diss. | 925 |  |  |  |  |  |  |
| Console L1 decks | 930 | Al | 0.56 |  |  |  |  |
| Magnet current diss. | 935 |  |  |  |  |  |  |
| L1 boundary | 939 | Al, Cu Cooling strap to GHe ventl. (L1) 2) | 0.40 | cross sect.: (20x1)mm, l=0.3m |  | R-OBA-345 [RD 23] |  |
| Console L0 decks | 940 | Al | 1.68 |  |  |  |  |
| Mixer Unit | 941 | Al | 1.05 |  |  |  |  |
| Heater | 942 |  |  |  |  |  |  |
| LO-power | 943 |  |  |  |  |  |  |
| L0 boundary | 949 | Al, Thermal link to HTT (L0) | 0.40 | 0.04 W/K @ 1.7K 1) |  | R-OBA-345 [RD 23] |  |

1)	Conductance includes R-OBA-345 and tank wall conductance of 0.4 W/K @ 1.7 K

2)	Detailed design not yet finalised, ASED PDR reference design assumed

Table ‎5.2-3:	Item List for HIFI

## Heat Shields and Tank Suspensions

The tank suspension consists of GFRP and T300 CFRP chains with heat interceptions at each heat shield. The two innermost chains are made out of T300 CFRP; the other ones are made out of S-glass. The cross section and material selection of each chain has been optimized w.r.t. thermal and mechanical performance. The details are described in [RD 20]. The nodal break-down of the chains is shown in Figure ‎5.3-1 and the relevant data are compiled in Table ‎5.3-1.

Figure ‎5.3-1:	Nodal Break-Down of Tank Suspensions

Figure ‎5.3-2:	Nodal Break-Down of Tanks and Heat Shield 1

| Item | Node | Material / Components | Mass | Size | IR | Unit Level | Remark |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | [kg] |  | Emiss. | Requirement |  |
| Susp. Bolt HS1 lo Susp. Bolt HS1 up | 1001 1002 | stainless steel stainless steel | 0.15 0.15 |  |  |  |  |
| Susp. Straps lo Susp. Straps up | 250 260 | 8 CFRP T300, between HS1 and SFW 8 CFRP T300, between HS1 and SFW |  | 8x137 mm², l= 306 mm 8x137 mm², l= 306 mm | 0.8 | R-TSS-200 [RD 21] | A) |
| Heat Shld 1 low bulk Heat Shld 1 low cyl. Heat Shld 1 upp cyl. Heat Shld 1 upp bulk | 1010 1020 1030 1040 | Al | 10.0 12.1 10.0 8.2 | A= 3.708 m², s=0.8 mm D=1.69m, h=0.842m, s=0.8 mm D=1.69m, h=0.696m, s=0.8 mm A= 3.021 m², s=0.8 mm | 0.05 |  |  |
| Heat Shield 1 MLI | 1110 1120 1130 1140 | 2 x 5 layers | 1.9 2.0 1.9 1.4 | A= 3.708 m² D=1.69m, h=0.842m D=1.69m, h=0.696m A= 3.021 m² | 0.05 | R-INM-0510 [RD 24] R-INM-0530 [RD 24] | B) |
| Susp. Bolt HS2 lo Susp. Bolt HS2 up | 2001 2002 | stainless steel stainless steel 2x8 CFRP T300, susp. straps to HS1 | 0.15 0.15 | 2x8x131 mm², l= 64.5 mm |  | R-TSS-200 [RD 21] | A) |
| Heat Shld 2 low bulk Heat Shld 2 low cyl. Heat Shld 2 upp cyl. Heat Shld 2 upp bulk | 2010 2020 2030 2040 |  | 11.1 12.6 10.4 9.0 | A= 4.124 m², s=0.8 mm D=1.76m, h=0.842m, s=0.8 mm D=1.76m, h=0.696m, s=0.8 mm A= 3.319 m², s=0.8 mm |  |  |  |
| Heat Shield 2 Baffle | 2050 |  |  | 290 mm diameter | 0.7 |  |  |
| HS 2 LOU Baffle | 2090 |  |  | 9 x 38 mm diameter | 0.7 |  |  |
| Heat Shield 2 MLI | 2110 2120 2130 2140 | 3 x 5 layers (tbc) | 2.1 2.1 1.9 1.7 | A= 4.124 m² D=1.76m, h=0.842m D=1.76m, h=0.696m A= 3.319 m² | 0.05 | R-INM-0610 [RD 24] R-INM-0630 [RD 24] | B) |
| Susp. Bolt HS3 lo Susp. Bolt HS3 up | 3001 3002 | stainless steel stainless steel 2x8 GFRP suspension straps to HS2 2x8 GFRP suspension straps to CVV | 0.15 0.15 | 2x8x168 mm², l= 57.5 mm 2x8x167 mm², l= 57 mm |  | R-TSS-200 [RD 21] | A) |
| Heat Shld 3 low bulk Heat Shld 3 low cyl. Heat Shld 3 upp cyl. Heat Shld 3 upp bulk | 3010 3020 3030 3040 |  | 12.2 kg 13.1 kg 10.8 kg 10.5 kg | A= 4.503 m², s=1mm D=1.83m, h=0.842m, s=1mm D=1.83m, h=0.696m, s=1mm A= 3.886 m², s=1mm | 0.05 |  |  |
| Heat Shield 3 MLI | 3111- 3148 | 4 x 5 layers (tbc) | 2.5 kg 4.6 kg 2.1 kg |  | 0.05 | R-INM-0710 [RD 24] R-INM-0730 [RD 24] | B) |

A) Thermal conductivity of material confirmed by sample tests

B) MLI Performance test at Forschungszentrum Karlsruhe not completed, ASED PDR reference design assumed

Table ‎5.3-1:	Item List for Heat Shields

The thermal property data of the cryostat internal MLI are described in Section ‎6.1.

## Cryostat Vacuum Vessel and Radiators

The nodal break-down of the CVV is shown in Figure ‎5.4-1. About one half of the cylindrical part and a 90° section of the upper bulkhead of the CVV serve as radiator, this area is called the CVV main radiator. The remaining surface of the CVV is covered with MLI. Three additional radiators are located at the –Z, +Y and –Y sides.

The (Y radiators shadow the CVV main radiator from the warm Sunshield MLI and increase further the CVV radiative area to space. The radiator (-Z) side of the (Y radiators (as well as both sides of the –Z radiator) are black anodized with sandblasting pre-treatment. The rear (+Z) sides of the (Y radiators are covered with MLI.

The (Y radiators and the –Z radiator have an area of 350 mm x 1600 mm, respectively. The thermal / mechanical attachment of each radiator to the CVV is provided via 6 interfaces with a contact conductance of 1 W/K each. Three M6 bolt connections are foreseen for each I/F. The contact conductance of 1 W/K between machined aluminium parts has been derived from test data described in RD 16, where >5W/K has been measured for a 6 x M4 connection at 76 K. In RD 17 a heat transfer coefficient of 2000 W/m²K is reported for a bolt torque of 20 Nm (M6 or M8) at 4.2 K. The contact area of one CVV radiator I/F is at least 20 mm x 35 mm leading to a contact conductance of 1.4 W/K (even at 4.2 K). Thus, the assumption of 1 W/K for a 3 x M6 connection at 70 K is rather conservative.

The heat spreading effect on CVV and radiators has been taken into account in the TMM using appropriate formulas in the corresponding “GL” conductance calculations (serial conductances of contact conductance and linear conductance of the corresponding CVV radiator). On the CVV two arithmetic nodes are introduced at the –Z Radiator I/F on the lower (node 4051) and upper part (4052). Thus, node 4051 connects the radiator node 4050 with the CVV nodes 4024 and 4025. Node 4052 connects the radiator node 4050 with the CVV nodes 4034 and 4035.

A cryostat baffle is arranged between the Telescope and the CVV upper bulk. The external surface of this baffle is covered with MLI except a 90° section at the -Z side that serve as radiator area. The internal surface has a low IR emissivity. Inside this cryostat baffle there is an additional internal conical baffle with a low IR surface emissivity.

Figure ‎5.4-1:	CVV Nodal Break-Down

Figure ‎5.4-2:	Cryostat Baffle and Cover Nodal Break-Down (Cover open & closed View)

Figure ‎5.4-3: 	LOU Windows / Baffles

| Item | Node | Material / Components | Mass | Size | Solar | IR | Unit Level | Remark |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | [kg] |  | Absorpt. | Emiss. | Requirement |  |
| CVV lower bulk | 4011-4018 | Al 5083, 3.3547, black anodized | 88.5 | A= 8 x 0.585 m² 7 mm thickness (average) | (=0.95 | 0.7 |  |  |
| CVV lower cylinder | 4021-4028 | Al 5083, 3.3547, black anodized | 95.0 | D = 1.9 m, h=0.842 m 7 mm thickness (average) | (=0.95 | 0.7 |  |  |
| CVV upper cylinder | 4031-4038 | Al 5083, 3.3547, black anodized | 78.5 | D = 1.9 m , h= 0.696 m 7 mm thickness | (=0.95 | 0.7 |  |  |
| CVV upper bulk | 4041-4048 | Al 5083, 3.3547, black anodized | 78.1 | A= 8 x 0.516 m² 7 mm thickness (average) | (=0.95 | 0.7 |  |  |
| CVV lower bulk MLI | 4111-4118 4103-4106 | 25 layers (4x6+1) |  |  | (=0.13 | 0.05 | R-EXM-530 [RD 28] | A) |
| CVV lower cyl. MLI | 4121-4128 | 25 layers (4x6+1) |  |  | (=0.13 | 0.05 | R-EXM-530 [RD 28] | A) |
| CVV upper cyl. MLI | 4131-4138 | 25 layers (4x6+1) |  |  | (=0.13 | 0.05 | R-EXM-530 [RD 28] | A) |
| CVV upper bulk MLI | 4141-4148 | 25 layers (4x6+1) |  |  | (=0.13 | 0.05 | R-EXM-530 [RD 28] | A) |
| CVV –Z Radiator | 4050 | AlMgSi, black paint |  | 0.35 x 1.5 m | (=0.95 | 0.8 |  |  |
| CVV -Y Radiator | 4055 | AlMgSi , black paint |  | 0.35 x 1.5 m | (=0.95 | 0.8 |  |  |
| CVV +Y Radiator | 4057 | AlMgSi , black paint |  | 0.35 x 1.5 m | (=0.95 | 0.8 |  |  |
| CVV -Y Radiat. MLI | 4155 | 25 layers (4x6+1) |  |  | (=0.13 | 0.05 | R-EXM-530 [RD 28] | A) |
| CVV +Y Radiat. MLI | 4157 | 25 layers (4x6+1) |  |  | (=0.13 | 0.05 | R-EXM-530 [RD 28] | A) |
| LOU Windows | 4090 | Glass windows |  | 9 x D=38 mm |  | 0.9 |  |  |
| Cover | 4800 | If opened: -107° rotated around Y axis | 7 |  |  | 0.15 |  |  |
| Cover Heat Shield | 4801 | Heat shield rim/short cone | 0.46 |  |  | 0.05 0.7 |  |  |
| Cryostat Baffle outer | 4070,4071, 4073,4079 4072 | Al 5083 90° radiator section | 5 | D=850mm |  | 0.1 0.7 |  |  |
| Cryostat Baffle inner | 4075 | Al 5083 outer surface | 1 | Conical: D=500, d=300 |  | 0.05 0.1 |  |  |
| Cryostat Baffle MLI | 4170,4171, 4173,4179 | 25 layers (4x6+1) | 0.6 0.3 |  | (=0.13 | 0.05 | R-EXM-830 [RD 28] | A) |
| Pretension 1 - 8 | 4081-4088 | Ti brackets | 8 x 0.15 |  |  |  |  |  |

A)   ASED PDR Reference design assumed

Table ‎5.4-1:	Item List for CVV and Cryostat Baffle

The thermal property data of the CVV MLI are described in Section ‎6.1.

## LOU and Telescope

Figure ‎5.5-1:	H-EPLM GMM External Overall View including H-SVM RGMM

Figure ‎5.5-2:	Telescope GMM

LOU:

This section is still the ASED PDR Reference Design Status

The LOU is modelled as one common box connected to the LOU baseplate with 1 W/K and with a heat dissipation of 7 W [AD 01 and AD 04].

The LOU baseplate has a conductive interface to the CVV via 8 GFRP struts with 3.27 mm cross-section to length ratio in total and an assumed conductive coupling to the LOU radiator of 1 W/K.

In addition to the LOU radiator the +X and –Z side of LOU box serve also as radiator, the other sides of the box are covered with MLI.

The LOU Waveguide bundle is subdivided in 6 nodes, see Figure ‎5.5-3.

Figure ‎5.5-3:	Nodal Break-Down of LOU Waveguides and Harness

| Item | Node | Material / Components | Mass | Size | Solar | Emiss. | Unit Level | Remark |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | [kg] |  | Absorpt |  | Requirement |  |
| LOU Baseplate | 4200 | thermally equivalent to Al 8 GFRP struts on CVV | 35 | Box: (555x492x240)mm A/l = 3.27 mm GFRP |  |  | R-SS-0330 [RD 25] |  |
| LOU box +X side (Rad.) LOU box -X side (MLI) LOU box +Y side (MLI) LOU box -Y side (MLI) LOU box +Z side (MLI) LOU box -Z side (Rad.) | 4201 4202 4203 4204 4205 4206 | specularity = 0.8 (IR) specularity = 0.7 (IR) specularity = 0.8 (IR) specularity = 0.8 (IR) |  |  | (=0.95 (=0.13 (=0.13 (=0.13 (=0.13 (=0.95 | 0.8 0.05 0.15 0.05 0.05 0.8 |  |  |
| LOU Radiator | 4250 | black painted Al |  | 0.5 m² | (=0.95 | 0.8 |  |  |
| LOU Radiator MLI | 4251 | specularity = 0.8 (IR) |  |  | (=0.13 | 0.05 |  |  |
| LOU Waveguides | 4361-4366 | 14 St. Steel WR28 / WR34 WG’s to SVM | 1.917 | A=119.25 mm², l=1.63 m | (=0.8 | 0.8 |  |  |
|  |  | GFRP WG support brackets on CVV |  | A/l = 3.6 mm GFRP |  |  |  |  |
| Telescope | 8000 8100 8200 | Primary Reflector M1 (SiC) M2 Mirror (SiC) Hexapod (SiC) | 210 20 70 | (3.5 m |  | 0.01 0.01 0.02 |  |  |
|  | 8400 | CFRP T300 struts to CVV |  | A/l=6x1.433 mm (l=515 mm) |  |  | R-TMS-0330 [RD 27] |  |
| Telesc. M1 MLI | 8501- 8518, 8550 | ”Two screen” concept |  | D = 3.5 m, d = 0.5 m |  | 0.05 0.02 |  | Decontamin. Orbit |

Table ‎5.5-1:	Item List for LOU and Telescope

## Harness

The harness implementation principle in the H-EPLM TMM is shown in Figure ‎5.6-1. Depending on the harness dissipation, the different harness branches are modelled either by dedicated nodes or via a thermal conductance coupling using thermal conductivity integral functions. For the latter ones, the harness dissipation is distributed to the corresponding interface at the cold end. An overview for the CVV internal harness modelling is given in Table ‎5.6-1.

| Instrument | Branches with dedicated nodes | Branches with (integral) thermal conductance | Remark |
| --- | --- | --- | --- |
| PACS FPU | 4 | 18 |  |
| SPIRE FPU | 1 | 3 |  |
| HIFI FPU | 8 | 2 + 4 coax |  |
| SPIRE JFET Phot. | 0 | 7 |  |
| SPIRE JFET Spec. | 0 | 2 |  |

Table ‎5.6-1:	Modelling of the CVV Internal Harness Branches in the EPLM TMM

Figure ‎5.6-1:	Harness Chart used in TMM

The LOU waveguides are located outside the CVV and are subdivided in 6 nodes in x-direction. The waveguides are also modelled in the GMM. All other external harness is implemented by means of conductive couplings between the corresponding I/F nodes. All CVV external harness dissipation is distributed to 100% to the corresponding cold end.

The cross-section and dissipation values of the scientific harness (SIH) and the cryostat control harness (CCH) have been mostly evaluated based on the data listed in RD 02. The SIH data are summarized in Table ‎5.6-2 and Table ‎5.6-3; the CCH data are listed in Table ‎5.6-4 and Table ‎5.6-5. Values that are not based on RD 02 are written in brackets ( ).

The thermally isolating harness lengths are defined between the following I/F points, see Figure ‎5.6-1:

- at SVM: all harness assumed to have SVM temperature at SVM / CVV strut I/F

- at CVV: all harness assumed to have CVV temperature at the CVV / tank suspension strap I/F. Thermal connection via connector brackets, additional thermal connections at CVV internal wall (if necessary)

- at HS1: thermal connection of SIH (except SPIRE JFET harness) and CCH by means of "Stycast brackets", similar as done on ISO

- at OB: thermal connection of PACS FPU, SPIRE FPU and HIFI FPU harness by means of "Stycast brackets" or connector brackets.

The SIH thermal isolating length between CVV and inner heat shield (HS1) is assumed to 0.3 m. Thermal insulation length means the "free" length between the end of the harness thermal connection section at the CVV and the begin of the thermal connection section at the HS 1. The harness routing length between CVV connector brackets and the tank suspension straps is not taken as thermal isolating length, which is a conservative assumption. Harness conduction across the fixation ties on the tank suspension straps is considered to be negligible and therefore not taken into account in the TMM.

The SPIRE JFET harness is directly routed from the CVV to the JFET units.

The thermal contact conductance across a "Stycast bracket" is estimated to 0.05 W/K per branch.

| Internal Harness (SIH) | Node | from | to | Length * | Average Dissip ** | Spec Mode Dissip ** | Phot Mode Dissip ** | Stainl. St. | Brass | Cu | PTFE |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | m | mW/m | mW/m | mW/m | mm2 | mm2 | mm2 | mm2 |
| PACS FPU | 9101- 9171, 9201 | CVV HS1 OB | HS1 OB FPU | 0.3 0.66-2.9 0.3 | 6.02 | 21.36 | 14.68 | 28.597 | 6.804 | - | 247 |
| SPIRE FPU | 9301- 9311, 9341 | CVV HS1 OB | HS1 OB FPU | 0.3 0.83-1.52 0.3 | 2.501 | 15.009 | 0.754 | 10.31 | 8.052 | - | 103 |
| SPIRE JFET-P |  | CVV | JFET-P | 0.65-1.52 | 0.069 | 0 | 0.415 | 21.5 | 0.847 | - | 170 |
| SPIRE JFET-S |  | CVV | JFET-S | 0.80-0.90 | 0.015 | 0.088 | 0 | 6.146 | 0.594 | - | 52 |
| HIFI FPU (incl. coax) | 9401- 9491, 9521 | CVV HS1 OB | HS1 OB FPU | 0.3 0.5-1.88 0.3 | 8.485 | HIFI on: 25.465 | 20.876 | 5.816 | (0.522) | 134 |

*)   thermally isolating length only

**)  dissipation values are valid for 293 K, dissipation at lower temperature expected to be lower

Table ‎5.6-2:	CVV Internal Harness Data for PACS, SPIRE and HIFI

| External Harness (SIH) | from | to | Length * | Average Dissip ** | Spec Mode Dissip ** | Phot Mode Dissip ** | Stainl. St. | Brass | Cu | Manganin | PTFE |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | m | mW/m | mW/m | mW/m | mm2 | mm2 | mm2 | mm2 | mm2 |
| PACS FPU | SVM | CVV | 2.1 | 5.71 | 20.33 | 13.90 | 29.981 | 6.808 | - | 17.16 | 256 |
| SPIRE FPU | SVM | CVV | 2.1 | 2.576 | 15.459 | 0.987 | 13.426 | 6.656 | - | 6.24 | 104 |
| SPIRE JFET-P | SVM | CVV | 2.1 | 0.411 | 0 | 2.47 | 25.496 | 2.436 | - | 10.92 | 262 |
| SPIRE JFET-S | SVM | CVV | 2.1 | 0.173 | 1.04 | 0 | 7.288 | 0.874 | - | 3.12 | 75 |
| HIFI FPU *** | SVM | CVV | 2.1 | 11.81 | HIFI on: 35.333 | 15.84 | 5.564 | 2.944 | 7.8 | 116 |
| HIFI LOU | SVM | LOU | 2.5 | 52.0 | LOU on: 156.0 | 7.72 | 0.914 | 75.12 | - | 107 |

*) thermally isolating length only

**) dissipation values are valid for 293 K, dissipation at lower temperature expected to be lower

***) in addition: Silver with 0.016mm2 and 2.612 mm2 Copper-Beryllium (Coax harness)

Table ‎5.6-3:	CVV External SIH Data

| Internal Harness (CCH) | from | to | Length * | Dissip | Stainl. St. | Brass | PTFE |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | m | mW/m | mm2 | mm2 | mm2 |
| CCH | CVV | HS1 | 0.25 | 0 | 4.99 | (2.75) | 36 |
| CCH to HOT & HTT | HS1 lo. SFW | lo. SFW HOT | 0.7 0.1 | 0 0 | 1.73 0.42 | 1.73 0.24 | 9.3 2.2 |
|  | lo. SFW | HTT | 0.4 | 0 | 1.31 | 1.49 | 7.1 |
| CCH to OB | HS1 up. SFW | up. SFW OB | 1.5 0.5 | 0 0 | 0.45 0.45 | 1.02 1.02 | 4 4 |

*) thermally isolating length only

Table ‎5.6-4:	CVV Internal CCH Data, values not yet updated (Issue 2 status)

| External Harness (CCH and Telescope) | from | to | Length * | Dissip. at 293 K | Stainl. St. | Brass | Cu | Manganin | PTFE |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | m | mW/m | mm2 | mm2 | mm2 | mm2 | mm2 |
| CCH to CVV lower CB | SVM | CVV low. CB | 1.04 | 0 | 4.99 | (2.75) |  |  | 36 |
| CCH to CVV upper Cylinder | SVM | CVV | 2.1 | 0 | 0.32 | 0.61 | 1.8 | - | 2.78 |
| CCH to Cover | SVM | CVV /Cover | 7.1 |  |  | 2.8 |  |  | 10 |
| Telescope heater via CVV | SVM CVV | CVV Telescope | 4.7 3 | 0 |  |  | 8.1 |  | 10 |

*) thermally isolating length only

values in ( ) are own estimates

Table ‎5.6-5:	CVV External CCH Data, values not yet updated (Issue 2 status)

## HERSCHEL Sunshield and Sunshade with Struts

The HERSCHEL Sunshield and Sunshade (HSS) is split in two parts, the upper part is the Sunshade (SSD), providing the shade mainly for the telescope and the lower part is the Sunshield (SSH), which provides shading for the CVV and the electrical power. The SSH +Z side therefore is covered with solar cells and the SSD +Z side is covered with OSRs. The rear side (-Z side) of the HSS is covered with high efficient MLI. The HSS nodal break-down is shown Figure ‎5.7-1 and the corresponding thermally relevant data are listed in Table ‎5.7-1.

Figure ‎5.7-1:	HSS Nodal Break-Down (upper: MLI nodes, lower: structural nodes)

| Item | Node | Material / Components | Mass | Size | Unit Level | Solar Absorpt. | IR | Remark |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Requirement | Oper. | Non-Op | Emis |  |
| Sunshield Panels | 7000-7022 | Solar Cells with cover glass and harness CFRP skins (M55J) * Adhesive for HC Al Honeycomb (16 kg/m³) | 1.6 kg/m² 0.83 kg/m² 0.3 kg/m² 0.8 kg/m² | 2 x 0.3 mm thick 50 mm thick |  | (=0.72 | (=0.9 [RD 18] | 0.82 [RD 18] |  |
|  |  | GFRP struts to CVV Ti end fittings (Ti6AlV4) M55J CFRP struts to SVM |  | A/L = 2.27 mm GFRP in total | R-SS-0330 [RD 25] R-SS-0330 [RD 25] |  |  |  |  |
| Sunshield Panels MLI | 7100-7132 | 22 layers (4x5+2) | 0.65 kg/m2 |  | R-EXM-430 [RD 28] |  | (=0.13 | 0.05 |  |
| Sunshield Stiffening Frame MLI upper | 7133-7138 | 22 layers (4x5+2) | 0.65 kg/m2 |  | R-EXM-430 [RD 28] |  | (=0.13 | 0.05 |  |
| Sunshield Stiffening Frame MLI lower | 7103-7108 | 22 layers (4x5+2) | 0.65 kg/m2 |  | R-EXM-430 [RD 28] |  | (=0.13 | 0.05 |  |
| Sunshield-SVM Closure MLI | 7203-7208 | 22 layers (4x5+2) | 0.65 kg/m2 |  | R-EXM-430 [RD 28] |  | (=0.13 (=0.8 | 0.05 0.8 | +x side -x side |
| Sunshade Panels | 7050-7082 | OSR inclusive Adhesive CFRP skins (M55J) * Adhesive Al Honeycomb (16 kg/m³) GFRP blades to Sunshield GFRP struts to CVV | 1.0 kg/m2 0.83 kg/m² 0.3 kg/m² 0.8 kg/m² | 2 x 0.3 mm thick 50 mm thick A/L = (10)x16 x 7.86 mm GFRP A/L = 2.34 mm GFRP in total | R-SS-0330 [RD 25] |  | (=0.20 (=0.10 | 0.84 0.84 | EOL BOL |
| Sunshade +Y Stiffen. Rib | 7054 |  |  |  |  |  | (=0.92 | 0.8 |  |
| Sunshade -Y Stiffen. Rib | 7053 |  |  |  |  |  | (=0.92 | 0.8 |  |
| Sunshade Panels MLI | 7140-7142, 7150-7182 | 20 layers (3x6+1) | 0.65 kg/m2 |  | R-EXM-330 [RD 28] |  | (=0.13 | 0.05 |  |
| Sunshade +Y Rib MLI | 7154 | 20 layers (3x6+1) | 0.65 kg/m2 |  | R-EXM-330 [RD 28] |  | (=0.13 | 0.05 |  |
| Sunshade -Y Rib MLI | 7153 | 20 layers (3x6+1) | 0.65 kg/m2 |  | R-EXM-330 [RD 28] |  | (=0.13 | 0.05 |  |
| Sunshade Stiffening Frame MLI | 7143-7148 | 20 layers (3x6+1) | 0.65 kg/m2 |  |  |  | (=0.13 | 0.05 |  |

*) Thermal conductivity of 55 W/mK have been taken acc. to Thoray product information 1989

Table ‎5.7-1:	HSS related Items

## SVM with Struts and SVM Thermal Shield

To calculate the radiative couplings of the HERSCHEL CVV/SVM GFRP struts to their environment all 24 struts have been modelled in the ESARAD geometry model with an IR emissivity of 0.03 (e.g. one or a few layer MLI). Each strut has been subdivided into three nodes. The struts and the obtained radiative couplings have been implemented in the H-EPLM ESATAN TMM. The relevant length for the thermal analysis is the total GFRP strut length minus the length of one half of the parts where GFRP tube and the titanium end fitting overlap. The thermally relevant dimensions of the struts are summarized in Table ‎5.8-1.

The SVM Shield is subdivided into 3 nodes and the MLI on top of the SVM Shield is subdivided accordingly, see Figure ‎5.8-1. The struts supporting the SVM Thermal Shield are implemented by conductive couplings between SVM and SVM Thermal Shield.

Figure ‎5.8-1:	H-RSVM, SVM Thermal Shield and SVM/CVV Struts

| Item | Node | Material / Components | Mass | Size | Unit Level | Solar | IR | Remark |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Requirement | Absor. | Emiss. |  |
| SVM Module | 60XX,61XX | H-RSVM model, Alcatel responsibility |  |  |  |  |  | AD 07/08 |
|  | 6020-6024 | Boundary Nodes (conductive) |  |  |  |  |  |  |
|  | 6101-6106 | SVM top MLI |  |  |  | (=0.15 | 0.05 |  |
| SVM/CVV struts | 6501-6733 | GFRP strut tubes Ti fittings for GFRP tubes |  | A/L = 13.05 mm GFRP (24x D=50x1.4 mm, l=393 mm) | R-SS-0330 [RD 25] |  |  |  |
| SVM Thermal Shield | 6204-6206 | CFRP T300 face sheets, VDA Kapton Foil on -X side (90% specularity) Al Honeycomb (32 kg/m³) |  | 2 x 0.25 mm thick 20 mm thick | R-STS-0180 [RD 26] R-STS-0190 [RD 26] | (=0.3 | 0.05 |  |
|  |  | GFRP strut tubes to SVM structure Ti fittings for GFRP tubes |  | A/L = 2.123 mm GFRP | R-STS-0230 [RD 26] |  | 0.05 |  |
| SVM Thermal Shield MLI | 6304-6306 | 20 layers (3x6+1) |  |  | R-EXM-630 [RD 28] | (=0.13 | 0.05 |  |

Table ‎5.8-1:	SVM and SVM Shield related Items

# Material Properties

Note:	All references mentioned in this chapter are listed in Section ‎6.5 (i.e. not in Section 2).

## MLI Thermo-Optical Properties and Performance Data

The thermal property data of the cryostat internal MLI can be derived from /9/ and /11/. Test data evaluation had been performed within the ISO project and is described in /1/.

The performance data for 10 layers of embossed Mylar foils with 0.2 µm alumization and 9B2A spacers have been measured at mean temperatures between 30 K and 185 K at Linde /9/. The results can be summarized following:

- Radiative component: (rad  = 0.00278  (between structure and external MLI layer)

- Radiative component: (rad  = 0.00295  (MLI blanket only)

- Linear component: H = 3.5 10 –4 W/m²K for “loose” contact to the support structure

- Linear component: H = 6.2 10 –4 W/m²K for full contact with the support structure

The performance data for 10 layers and 20 layers of embossed Mylar foils have been measured at mean temperatures between 188 K and 343 K at ESTEC /11/. The results can be summarized following:

- Radiative component: (rad  = 0.00297 for 10 layers

- Radiative component: (rad  = 0.0024 for 20 layers

- Linear component: H = 1.093 10 –3 W/m²K for 10 layer blanket with round studs

Thus, it can be concluded, that the radiative component (rad is in any case less than 0.003 for a 10 layer MLI. For the CVV internal MLI quasi “free floating” MLI blankets can be assumed with a linear component of 3.5 10 –4 W/m²K. This is valid for temperatures below 185 K. For higher temperatures this approach is not applicable.

To calculate the MLI performance at higher temperature the approach proposed by Doenecke /12/ is used. This approach is valid for a temperature range between 130 K and 410 K and features a calculation procedure for an effective MLI emissivity (eff. No linear component is foreseen in this approach. This calculation procedure has been taken for the HSS MLI and the HS2 and HS3 MLI on ground.

| MLI on | Layers | radiative and effective emissivity ((rad and (eff) | linear conductance H [W/m²K] | emissivity of ext. layer ((ext) | specul. of ext. layer ((ext) | Remark |
| --- | --- | --- | --- | --- | --- | --- |
| HTT | 20 | (rad = 0.0024 | 1.8 E-4 | 0.05 | 0 | Ref. /1,9/ |
| HOT | 10 | (rad = 0.003 | 3.5 E-4 | 0.05 | 0 |  |
| Heat Shield 1, ext. | 10 | (rad = 0.003 | 3.5 E-4 | 0.05 | 0 | Ref. /1,9/ |
| Heat Shield 1, int. | (1) * | n.a. | n.a. | 0.05 | 0.9 | Ref. /10/ |
| Heat Shield 2 Orbit Ground | 15 | (rad = 0.0026 | 2.5 E-4 | 0.05 | 0 | Ref. /1/ |
|  |  | (eff = 0.011 | n.a. | 0.05 | 0 | Ref. /1,12/ |
| Heat Shield 3 Orbit Ground | 20 | (rad = 0.0024 | 1.8 E-4 | 0.05 | 0 | Ref. /1, 9/ |
|  |  | (eff = 0.007 | n.a. | 0.05 | 0 | Ref. /1,12/ |
| CVV | 25 | (rad = 0.0022 | 1.093 E-3 | 0.05 | 0.8 | Ref. /1,11/ |
| Cryostat Baffle | 25 | (rad = 0.0022 | 1.093 E-3 | 0.05 | 0.8 | Ref. /1,11/ |
| LOU | 20 | (eff = 0.02 | n.a. | 0.05 | 0.8 |  |
|  | 20 | (eff = 0.02 | n.a. | 0.15 | 0.7 | baseplate |
| Sunshade | 20 | (eff = 0.015 | n.a. | 0.05 | 0.8 | Ref. /12/ |
| Sunshield | 22 | (eff = 0.012 | n.a. | 0.05 | 0.8 | Ref. /12/ |
| SVM Shield +X | 20 | (eff = 0.015 | n.a. | 0.05 | 0.8 |  |
| SVM Shield -X | (1) |  | n.a. | 0.05 | 0.9 | Ref. /10/ |
| SVM Struts | 1 | n.a. | n.a. | 0.03 | 0 |  |
| SVM Top | n.a. |  | n.a. | 0.05 | 0 | AD 07 & 08 |
| Telescope, Orbit Decontam. | n.a. | (eff = 0.01 | n.a. | 0.02 | 0 |  |
|  | n.a. | (eff = 0.025 | n.a. | 0.05 | 0 |  |

*) one layer goldized Kapton foil or low emissive surface coating

Table ‎6.1-1:	Overview on Herschel MLI Performance Data

## Thermal Conductivity Data

Figure ‎6.2-1:	Thermal Conductivity of S-Glass GFRP Tank Suspensions and GFRP Struts

Figure ‎6.2-2:	Thermal Conductivity of T300 CFRP Tank Suspensions and M40A CFRP

Figure ‎6.2-3:	Thermal Conductivity of Harness Wires

Figure ‎6.2-4:	Thermal Conductivity of Harness Wire Insulation Materials /14/

Figure ‎6.2-5:	Thermal Conductivity of Copper Cooling Strap Materials

## Specific Heat Capacity Data

Figure ‎6.3-1:	Specific Heat Capacity of Aluminium and Titanium /14/

## Helium Properties

For the heat of vapourization of Helium different values are found in literature, see Figure ‎6.4-1. For the TMM calculations the data reported in Ref. /2/ are used.

The specific heat of the gas is 5.1966 kJ/kg/K (almost constant versus temperature).

Figure ‎6.4-1:	Heat of Vapourization of Helium 4

Figure ‎6.4-2: 	Vapour Density of Helium (Ref. /5/)

Figure ‎6.4-3:	Volume Specific Heat Capacity of Liquid He on Saturation Line

## References for Material Properties

/1/	Evaluation of LINDE/ESTEC-MLI Measurements and Transformation to the ISO Cryostat MLI Design, Doc.No.: ISO.TN-B1430.007, dated 12.07.88

/2/	VDI Kryoatlas BW 2407

/3/	Thermophysical Properties of Helium from 2 to 1500K with pressures to 1000 Atm (National Bureau of Standards TN 631)

/4/	W. Blanke: Thermophysikalische Stoffdaten, Springer 1989

/5/	NIST Standard Reference Database 12: NIST Thermophysical Properties of Pure Fluids, Version 3.0.

/6/	ASPI ax AS-FAX SE/SP/IS 2244/89, dated 30.01.89

/7/	Hartwig & Knaak, Cryogenics, Nov. 84, p.645

/8/	Touloukian: Thermophysical Properties of Matter, 1972

/9/	MLI Test Report – Linde, Doc.No.:  ISO-TR-C130.001, dated 19.02.88

/10/	METOP Mechanical and Thermal Design Requirement Specification, Doc.No.; MO.RS.MMT.SY.0004, Issue 3, June 2000

/11/	Comparative Performance Measurements on MLI Test Samples with different Types of Foils and Studs, Test Report: YCV/BA/136, dated 07.03.88

/12/	Doenecke:  Survey and Evaluation of Multilayer Insulation Heat Transfer Measurement, ICES July 1993

/13/ 	Reed and Golda: Cryogenic composite supports, Cryogenics 1997, p.233

/14/	ISO Thermal Mathematical Model, Version 7.12

/15/	NIST Data Base, http://cryogenics.nist.gov/NewFiles/material_properties.html

/16/	Data delivered by Th. Passvogel,  ESA-FAX-PT-01750, dated 23.02.1996

/17/	Guy K. White: Experimental Techniques in Low Temperature Physics, Handbook on Materials for Superconductivity Machinery, 3rd Edition

# Thermal Analysis Results

## Operation On Ground

### On-Ground Lifetime

A heat flow chart based on ground case analysis and showing the CVV internal main paths is shown in Fig. 7.1-1. The calculated temperatures of the different components as well as the GHe mass flow rate are included.

Only main paths are shown. All values are in [mW]

Figure ‎7.1-1:	CVV Heat Flow Chart for On-Ground Environment

In Table ‎7.1-1 the main results of a sensitivity analysis performed for ground case conditions are summarised. The uncertainties for the different items are assumed to be between (20% for mechanical support structures and (50% for MLI conductance. In Figure ‎7.1-2 the heat flow to HTT sensitivity is visualised.

| Item |  | T, HS1 [K] [1020] | T, HS2 [K] [3020] | T, HS3 [K] [3020] | T, OB [K] [375] | M He [mg/s] | Heat to HTT [mW] |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | + | - | + | - | + | - | + | - | + | - | + | - |
| Reference |  | 85.4 | 171 | 233 | 30.34 | 31.503 | 730 |
| HTT MLI conductance | k1 | ±50% | -3.0 | 3.6 | -3 | 3 | -1 | 1 | -1.57 | 2.03 | 0.526 | -0.618 | 12 | -14 |
| Heat Shield MLI conduct. | k2 | ±50% | 5.2 | -6.4 | 11 | -19 | 6 | -13 | 1.70 | -2.45 | 5.259 | -6.513 | 122 | -151 |
| HS 1 MLI cond. | k2a | ±50% | 2.2 | -2.9 | -2 | 3 | -1 | 1 | -0.07 | 0.11 | 0.459 | -0.540 | 11 | -13 |
| HS 2 MLI cond. | k2b | ±50% | 0.9 | -1.9 | 5 | -10 | -4 | 7 | 0.64 | -1.27 | 1.604 | -2.982 | 37 | -69 |
| HS 3 MLI cond. | k2c | ±50% | 1.5 | -3.0 | 7 | -14 | 11 | -21 | 0.95 | -1.70 | 2.586 | -4.296 | 60 | -100 |
| HTT bones (T300) | k3 | ±20% | -0.8 | 1.0 | -1 | 1 | 0 | 0 | -0.45 | 0.55 | 0.138 | -0.167 | 3 | -4 |
| Inner tank susp. (T300) | k4 | ±20% | -1.5 | 1.7 | -1 | 1 | -1 | 1 | -0.58 | 0.68 | 0.272 | -0.302 | 6 | -7 |
| HS1/2 tank susp. (T300) | k5 | ±20% | 0.9 | -1.1 | -2 | 2 | -1 | 1 | -0.16 | 0.21 | 0.335 | -0.405 | 8 | -9 |
| HS2/3 tank susp. (GFRP) | k6 | ±20% | 0.2 | -0.2 | 0 | 0 | 0 | 0 | 0.00 | 0.00 | 0.178 | -0.191 | 4 | -4 |
| Outer tank susp. (GFRP) | k7 | ±20% | 0.1 | -0.1 | 0 | 0 | 1 | -1 | 0.04 | -0.04 | 0.140 | -0.148 | 3 | -3 |
| Int. harness cross-section | k8 | ±15% | 0.8 | -0.8 | 0 | 0 | 0 | 0 | 0.07 | -0.07 | 0.348 | -0.351 | 8 | -8 |
| Int. harness length | k9 | ±15% | -0.8 | 0.8 | 0 | 0 | 0 | 0 | -0.07 | 0.07 | -0.351 | 0.348 | -8 | 8 |
| Int. harness dissipation | k10 | ±20% | 0.0 | 0.0 | 0 | 0 | 0 | 0 | 0.00 | 0.00 | 0.000 | 0.000 | 0 | 0 |
| He II latent heat | k11 | ±1% | 0.3 | -0.3 | 0 | 0 | 0 | 0 | 0.17 | -0.17 | -0.064 | 0.065 | 6 | -6 |

Table ‎7.1-1:	Sensitivities for Operation on Ground

Figure ‎7.1-2:	HTT Heat Flow Sensitivity for Operation on Ground

Figure ‎7.1-3:	HOB Temperature Sensitivity for Operation on Ground

### On-Ground Autonomy (closed HTT)

The parameter determining the length for the on-ground autonomy is the temperature of the He II in the main tank, which shall be below 2.15 K after 6 days.

The on-ground autonomy analysis is based on the following steady state start conditions (time t =0:):

- System Pre-cooling with a He mass flow of 1000 mg/s

- HOT He mass flow: 			25 mg/s

- Start temperature of HTT: 		1.8 K

- Temperature of HOT:  			4.2 K (boundary until HOT is empty)

- CVV temperature:			295 K (boundary)

For the transient HTT warm up two scenarios have been investigated: a constant HOT mass flow rate of 25 mg/s (adjusted by HOT heating) and a free floating mass flow rate determined by the parasitic heat load into the HOT only. The results shown in Figure ‎7.1-4 reveal that for the 25 mg/s scenario the HTT is below 2.15 K after 6 days, for the floating mass flow scenario the HTT exceeds 2.15 K after about 124 hours (5.2 days).

The bend in the 25 mg/s curve indicates that the HOT He reservoir of 8.75 kg is exhausted after 97 hours. In case of the floating mass flow 5.35 kg Helium are consumed after 6 days; i.e. 3.4 kg are still in the tank.

The mass flow evolution for a free floating mass flow due to parasitic heat into the HOT is shown in Figure ‎7.1-5. The HOT mass flow during 6 days launch autonomy is always less than 25 mg/s. This means, that the HOT tank need to be heated in order to achieve a constant HOT mass flow of 25 mg/s.

Figure ‎7.1-4:	Warm-up of HTT for Different HOT Mass Flow Rates

Figure ‎7.1-5:	Floating HOT Mass Flow Rate due to Parasitic Heat Load only

Figure ‎7.1-6:	Warm-up of Heat Shields for 25 mg/s HOT Mass Flow Rate

### On-Ground Testing (IMT)

For the Integrated Module Test (IMT) with the CVV at 20°C the following conditions are assumed:

- HTT closed: 			1.8 K

- HOT He mass flow: 		100 mg/s

- Temperature of HOT:  		4.2 K (boundary)

- CVV temperature:		295 K (boundary)

- Cryo Cover cooled:		80 K

The corresponding I/F temperatures and heat flow charts for the CVV internal and for the OBA with SPIRE in Spectrometer Mode (average dissipation) are shown in Figure ‎7.1-7 and Figure ‎7.1-8.

|  | PACS L0 | SPIRE L0 | Hifi L0 | Pacs L1 | Spire L1 | Hifi L1 | OBP L2 | Spire L3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| TMM Node | [723] | [721] | [761] | [762] | [814] | [815] | [816] | [949] | [814] | [814] | [939] | [376] | [814] |
| PACS Phot. | 1.92 | 1.86 | 1.88 | 1.95 | 2.01 | 1.83 | 1.82 | 2.04 | 6.6 | 6.5 | 4.7 | 7.8 | 8.0 |
| SPIRE Spect. | 1.92 | 1.86 | 1.82 | 1.87 | 2.03 | 1.96 | 1.83 | 2.04 | 6.5 | 6.7 | 4.8 | 7.9 | 8.1 |
| HIFI on | 1.92 | 1.86 | 1.82 | 1.87 | 2.01 | 1.83 | 1.82 | 2.06 | 6.5 | 6.5 | 4.8 | 8.3 | 8.2 |

Table ‎7.1-2:	Predicted I/F Temperatures for IMT on Ground

Figure ‎7.1-7:	CVV Heat Flow Chart for IMT

Figure ‎7.1-8:	OBA Heat Flow Chart for IMT (SPIRE Spectrometer Mode)

## Pre-Launch and Early Orbit Phase

For the pre-launch and early orbit phase two scenarios have been investigated:

- nominal scenario with no launch delay

- launch scenario with 25 hours launch delay

The figures shown in this section represent the nominal scenario (without delay). The helium loss during the in-orbit cool-down phase in this case is 22.1 kg within the first 40 days. This amount of Helium is taken for the lifetime analysis described in section ‎7.5. The HTT temperature increases from 1.844 K at launch to a maximum of 1.941 K during in-orbit cool down.

For the scenario with 25 hours launch delay the corresponding Helium consumption is about 33.5 kg within the first 40 days and the HTT temperature increases from 1.904 K at launch to a maximum of 2.081 K during in-orbit cool down.

Figure ‎7.2-1:	HTT Temperature Evolution During Nominal Launch Phase

Figure ‎7.2-2:	Heat Shield Temperature Evolution During Pre-Launch Phase

Figure ‎7.2-3:	H-EPLM Temperatures During In-Orbit Cool-Down (25 h launch delay)

Figure ‎7.2-4:	HTT Temperature During In-Orbit Cool-Down

Figure ‎7.2-5:	Telescope Cool-Down Rate after Decontamination (Cover still closed)

Figure ‎7.2-6:	Helium Mass Flow and Mass Loss During In-Orbit Cool-Down

## Operation in L2 Orbit

### Steady State Analysis for Hot and Cold Case Conditions

Thermal analysis runs with implemented instrument models have been performed both for the hot and cold case thermal environment at L2.

The results are summarized in Table ‎7.3-1. The corresponding heat flow charts showing the CVV external main paths are shown in Figure ‎7.3-2 for the hot case environment and in Figure ‎7.3-3 for the cold case environment. The calculated temperatures of the relevant components are included. The internal heat flow chart for the hot case environment is shown in Figure ‎7.3-4.

|  | Solar constant | SAA around Y | solar absorpt. of OSR | T CVV | T HOB | He Mass Flow |
| --- | --- | --- | --- | --- | --- | --- |
| Cold case | 1287 W/m² (SS) | 30° | 0.1 (BOL) | 63.8 K | 9.94 K | 1.931 mg/s |
| Hot case | 1405 W/m² (WS) | 0° | 0.2 (EOL) | 67.0 K | 10.07 K | 2.067 mg/s |
| Average * | 1352 W/m² | 17.267° | 0.15 | 65.6 K | 13.11 K | 2.176 mg/s |

*) Instrument TMM's replaced by IID-A heat load allocations

Table ‎7.3-1:	Analysis Results for Hot and Cold Case Environment

Figure ‎7.3-1:	H-EPLM Temperature Distribution for Hot Case Environment at L2

Figure ‎7.3-2: 	CVV Heat Flow Chart for Hot Case Environment at L2

Figure ‎7.3-3:	CVV Heat Flow Chart for Cold Case Environment at L2

Only main paths are shown. All values are in [mW]

Figure ‎7.3-4: 	HPLM internal Heat Flow Chart for Average Instrument Dissipation and Hot Case Environment at L2

### Sensitivity Analysis for Lifetime and EPLM Temperatures

A comprehensive sensitivity analysis has been performed for In-Orbit operations. The results are listed in Table ‎7.3-2 and Table ‎7.3-4. The sensitivities for the lifetime, the CVV and the Optical Bench temperature are visualised in Figure ‎7.3-5 to Figure ‎7.3-8.

| Item | Sensitivity | T, OB [K] | M He [mg/s] | ( Lifetime [days] | Remark |
| --- | --- | --- | --- | --- | --- |
|  |  | + | - | + | - | + | - |  |
| Reference Case: see Figure ‎7.3-4 | 10.07 | 2.067 | - |  |
| HTT MLI conductance | k1 | ( 50% | -0.02 | 0.14 | 0.003 | -0.016 | -2 | 12 | *) |
| Heat Shield MLI cond. | k2 | ( 50% | -0.01 | 0.01 | 0.038 | -0.047 | -27 | 35 |  |
| HS 1 MLI cond. | k2a | ( 50% | -0.01 | 0.01 | 0.012 | -0.020 | (-9) | (15) |  |
| HS 2 MLI cond. | k2b | ( 50% | 0.00 | 0.00 | 0.010 | -0.014 | (-8) | (10) |  |
| HS 3 MLI cond. | k2c | ( 50% | 0.00 | 0.00 | 0.013 | -0.017 | (-10) | (12) |  |
| HTT bones (T300) | k3 | ( 20% | -0.18 | 0.20 | 0.015 | -0.018 | -11 | 13 |  |
| Inner tank susp. (T300) | k4 | ( 20% | -0.03 | 0.04 | 0.024 | -0.025 | -17 | 19 |  |
| HS1/2 tank susp. (T300) | k5 | ( 20% | -0.02 | 0.02 | 0.019 | -0.022 | -14 | 16 |  |
| HS2/3 tank susp. (GFRP) | k6 | ( 20% | 0.00 | 0.00 | 0.019 | -0.023 | -14 | 17 |  |
| Outer tank susp. (GFRP) | k7 | ( 20% | 0.00 | 0.00 | 0.018 | -0.021 | -13 | 16 |  |
| Int. Harness cross-section | k8 | ( 15% | 0.14 | -0.15 | 0.085 | -0.087 | -59 | 66 |  |
| Int. Harness length | k9 | ( 15% | -0.15 | 0.14 | -0.087 | 0.085 | 66 | -59 |  |
| Int. Harness dissipation | k10 | ( 20% | 0.17 | -0.17 | 0.025 | -0.025 | -18 | 18 |  |
| He II latent heat | k11 | ( 1% | 0.04 | -0.04 | -0.007 | 0.007 | 5 | -5 |  |
| CVV conductivity | k12 | +71% |  |  |  |  | + 6 |  | case 177a |
| Sum of mean root square |  |  |  |  | -95 | 108 |  |

*) +50% value extrapolated from +20% calculation run (because of numerical error with +50% run)

Note: Values in ( ) not taken for lifetime uncertainty

Table ‎7.3-2:	In-Orbit Sensitivities due to Uncertainties of Physical Parameters inside CVV

| Item | Sensitivity | T, CVV [K] | M He [mg/s] | ( Lifetime [days] | Remark |
| --- | --- | --- | --- | --- | --- |
|  |  | + | - | + | - | + | - |  |
| Reference Case: see Figure ‎7.3-4 | 67.0 | 2.067 | - |  |
| CVV MLI conductance | k21 | ( 50% | 1.7 | -2.0 | 0.059 | -0.070 | -42 | 52 |  |
| Sunshield MLI conduct. | k22 | ( 50% | 1.4 | -2.0 | 0.053 | -0.072 | -37 | 54 |  |
| Sunshade MLI conduct. | k23 | ( 50% | 0.3 | -0.3 | 0.020 | -0.026 | -14 | 19 |  |
| SVM Shield MLI conduct. | k24 | ( 50% | 0.1 | -0.1 | 0.002 | -0.003 | -2 | 3 |  |
| CVV strut conductance | k25 | ( 20% | 0.8 | -0.8 | 0.026 | -0.026 | -19 | 19 |  |
| HSS strut conductance | k26 | ( 20% | 0.4 | -0.4 | 0.013 | -0.013 | -9 | 10 |  |
| Ext. Harness cross-section | k27 | ( 15% | 0.4 | -0.4 | 0.016 | -0.017 | -12 | 12 |  |
| Ext. Harness length | k28 | ( 15% | -0.4 | 0.4 | -0.017 | 0.016 | 12 | -12 |  |
| Ext. Harness dissipation | k29 | ( 20% | 0.0 | 0.0 | 0.001 | -0.001 | -1 | 1 |  |
| MLI specularity | k30 | ( 20% | -0.4 | 0.4 | -0.012 | 0.016 | 9 | -11 |  |
| Emissivity of radiator surfaces | k31 | ( 20% | -1.5 | 1.9 | -0.052 | 0.069 | 39 | -49 | CVV radiators *) |
| Emissivity of Sunshade (OSR panels) | k32 | ( 0.03 | 0.0 | 0.0 | -0.002 | 0.003 | 2 | -2 | acc. to ECSS-E-30, Part 1A |
| Emissivity of Sunshield (Solar panels) | k33 | ( 0.03 | -0.2 | 0.2 | -0.006 | 0.007 | 4 | -5 | acc. to ECSS-E-30, Part 1A |
| Absorptivity of Sunshade (OSR panels) | k34 | ( 0.03 | 0.2 | -0.2 | 0.011 | -0.011 | -8 | 8 | acc. to ECSS-E-30, Part 1A |
| Absorptivity of Sunshield (Solar panels) | k35 | ( 0.03 | 0.2 | -0.2 | 0.007 | -0.007 | -5 | 5 | acc. to ECSS-E-30, Part 1A |
| Telescope emissivity (M1) | k36 | (0.005 | -0.1 | 0.1 | -0.004 | 0.005 | (2) | (-3) | case 163,164a |
| SVM Thermal Shield strut conductance | k37 | +75% | ~0 |  | ~0 |  | -0.3 |  | Manufacturing reasons (CASA) |
| LOU strut conductance | k38 | ( 20% | 0.1 |  | 0.002 | -0.002 | (-1) | (1) |  |
| Telescope Mounting Structure conductance | k39 | +60% | 0.1 |  | 0.002 |  | (-2) |  | in orbit only, decontam. phase not yet analyzed |
| Sum of mean root square |  |  |  |  | -82 | 92 |  |

*) -20% value extrapolated from -10% calculation run (because of numerical error with -20% run)

Note: Values in ( ) not taken for lifetime uncertainty

Table ‎7.3-3:	In-Orbit Sensitivities due to Uncertainties of Physical Parameters outside CVV

The case of 25 hours launch delay has also to be taken into account as uncertainty. As described in Section ‎7.2 the launch delay leads to 11.4 kg additional loss of Helium during in-orbit cool down which corresponds to about 60 days loss of lifetime.

| Item | Node | T, cold case [K] | T, hot case [K] |
| --- | --- | --- | --- |
| SSH MLI, center panel | [7100] | 245 | +18 / -31 a) | 261 | +20 / -33 |
| SSH MLI side panel | [7101] | 234 | +17 / -29 a) | 248 | +18 / -30 |
| SSD MLI, center panel | [7160] | 157 | +11 / -18 a) | 196 | +15 / -25 |
| SSD MLI side panel | [7161] | 147 | +10 / -16 a) | 184 | +14 / -23 |
| Telescope | [8000] | 72.2 | +4 / -5 a) | 79.3 | +4 / -5 |
| LOU Baseplate | [4200] | 136 | +2 / -2 a) | 140 | +2 / -3 |
| SSH (solar cells), center panel | [7000] | 360 |  | 382 | ( 6 |
| SSH (solar cells), side panel | [7001] | 342 |  | 362 | ( 6 |
| SSD (OSR’s), center panel | [7060] | 219 |  | 276 | ( 11 |
| SSD (OSR’s), side panel | [7061] | 205 |  | 259 | ( 11 |
| SVM Thermal Shield | [6204] | 119 |  | 133 |  |

a) sum of mean root square due to MLI sensitivity analysis (k21, k22, k23)

Table ‎7.3-4:	Uncertainties of HSS and Telescope Temperature at L2

In case the solar cells are in shunt mode and all absorbed solar energy is dumped in the SSH, the temperature of the center panel increases to 409 K (136°C). This has been calculated for LEOP and Winter Solstice. Further cases are listed in Section 6.4 of RD 01.

Figure ‎7.3-5:	Lifetime Sensitivity for CVV Internal Parameter Variations

Figure ‎7.3-6:	Lifetime Sensitivity for CVV External Parameter Variations

Figure ‎7.3-7:	Sensitivity of CVV Temperature for Operation at L2

Figure ‎7.3-8:	Sensitivity of Sunshade MLI Temperature for Operation at L2

Figure ‎7.3-9:	Sensitivity of Sunshield MLI Temperature for Operation at L2

Figure ‎7.3-10:	Sensitivity of Telescope Temperature for Operation at L2

### Transient Analysis for S/C Operations in Orbit

A transient analysis run has been performed for in-orbit rotation of the Herschel S/C by 30° around Y-axis. The transient cool-down curves of Telescope, LOU, CVV and HTT in this case are shown in the following figures.

Figure ‎7.3-11:	Transient Cool-Down of Telescope after S/C Rotation 30° around Y-Axis

Figure ‎7.3-12:	Transient Cool-Down of LOU Baseplate after S/C Rotation 30° around Y-Axis

Figure ‎7.3-13:	Transient Cool-Down of CVV after S/C Rotation 30° around Y-Axis

Figure ‎7.3-14:	Transient Cool-Down of HTT after S/C Rotation 30° around Y-Axis

## Transient Analysis with In-Orbit Instrument Timeline

The transient temperature and heat flow results for the instrument thermal interface nodes shown in this section are based on the following instrument timeline:

- Start conditions (steady state):			Instruments average dissipation

- PACS Photometer Mode (incl.  sorption cooler cycle)		48 h

- SPIRE 								48 h

- HIFI								48 h

- SPIRE 								48 h

- PACS Spectrometer Mode (no sorption cooler cycle)		24 h

- HIFI								48 h

- PACS Spectrometer Mode (no sorption cooler cycle) 		24 h

The analysis is performed with a remaining He II mass of 5  kg at beginning of the simulation.

Please note that the L0 temperatures will have an uncertainty of about 75 mK (50 mK due to the uncertainty of the HTT temperature and 25 mK due to sensitivity analysis results obtained with Issue 2 TMM).

### PACS Interface Temperatures and Heat Flows

Figure ‎7.4-1:	PACS L0 Interface Temperatures

Figure ‎7.4-2:	PACS L0 Interface Heat Flows

Figure ‎7.4-3:	PACS L0 Interface Temperatures during Recycling

Figure ‎7.4-4:	PACS L0 Interface Heat Flows during Recycling

Figure ‎7.4-5:	PACS L1 Interface Temperatures

Figure ‎7.4-6:	PACS L1 Interface Heat Flows

Figure ‎7.4-7:	PACS L2 Interface Heat Flows

### SPIRE Interface Temperatures and Heat Flows

Figure ‎7.4-8:	SPIRE L0 Interface Temperatures

Figure ‎7.4-9:	SPIRE L0 Interface Heat Flows

Figure ‎7.4-10:	SPIRE L0 Interface Temperatures during Recycling

Figure ‎7.4-11:	SPIRE L0 Interface Heat Flows during Recycling

Figure ‎7.4-12:	SPIRE L1 Interface Temperatures

Figure ‎7.4-13:	SPIRE L1 Interface Heat Flows

Figure ‎7.4-14:	SPIRE L3 Interface Temperatures

Figure ‎7.4-15:	SPIRE L3 Interface Heat Flows

Figure ‎7.4-16:	SPIRE L2 Interface Heat Flows

### HIFI Interface Temperatures and Heat Flows

Figure ‎7.4-17:	HIFI L0 Interface Temperature

Figure ‎7.4-18:	HIFI L0 Interface Heat Flow

Figure ‎7.4-19:	HIFI L1 Interface Temperature and Stability

Figure ‎7.4-20:	HIFI L1 Interface Heat Flow

### Instrument Heat Load on HTT and He Mass Flow

Figure ‎7.4-21:	HTT Temperature and He Mass Flow

|  | Average instrument dissipation | Average instrument I/F heat flow | HERS-0530 AD 03 | Remark |
| --- | --- | --- | --- | --- |
| Level 0 | 4.38 mW | 12.2 mW | 10 mW |  |
| Level 1 | 4.98 mW | 34.3 mW | 25 mW |  |
| Level 2 | 16.07 mW | - 1.4 mW | 35 mW | L2 I/F heat flow is ~0 due to cooling via PACS and SPIRE L1 I/F |
| Level 3 | 12.62 mW | 10.6 mW | 15 mW | SPIRE JFET’s |

Table ‎7.4-1:	Average Instrument Dissipation versus IIDA Allocation

Figure ‎7.4-22:	Total Instrument Heat Load on HTT (different scales on Y-axis)

Figure ‎7.4-23:	Total Instrument Heat Load on L1 Ventline

Figure ‎7.4-24:	Total Instrument Heat Load on L2 (Optical Bench Plate)

Figure ‎7.4-25:	Total Instrument Heat Load on L2 (Optical Bench Plate)

### Sensitivity Analysis

Figure ‎7.4-26:	HTT Temperature for Different Conditions

Figure ‎7.4-27:	Helium Mass Flow for Different Conditions

Figure ‎7.4-28:	PACS L0 Temperature for Different Conditions

Figure ‎7.4-29:	SPIRE L0 Temperature for Different Conditions

Figure ‎7.4-30:	PACS L1 Temperature for Different Conditions

Figure ‎7.4-31:	SPIRE L1 Temperature for Different Conditions

## Lifetime Calculation

A thermal analysis run with implemented IID-A heat load allocations have been performed for the average thermal environment at L2 as defined in RD01. This run has been performed to calculate the He mass flow relevant for the “contractual” lifetime.

According to the lifetime calculation formula described in section ‎4.2, the expected lifetime is calculated following:

mn 		= 0.98 /1.15 * 145.338 kg/m³ * 2.367m³ = 293.16 kg

mtrans		= 22.1 kg (output of section ‎7.2)

mresidual		= 0.94 * 0.33 kg/m³ * 2.367m³  = 0.73 kg

MHe		= 2.1762 mg/s

t trans		= 40 days (output of section ‎7.2)

t uncertainty	= -139 days (see section ‎7.3.2)

Thus, the lifetime formula can be written:

Lifetime [days] = 0.99*((293.16 kg – 22.1 kg – 0.73 kg )*1E6 / (MHe [mg/s]*3600*24) + 40 days – 139 days)

with MHe to be inserted in [mg/s]

or

Lifetime [days] = 0.99*(3129.3 / MHe - 99 days) = 1325 days = 3.63 years

On the other hand, the corresponding lifetime using the TMM with implemented instrument models reveal a mass flow MHe of 2.067 mg/s even for hot case environment at L2 (see section ‎7.3), which leads to a lifetime of 3.84 years (including uncertainties).

The uncertainty of the nominal lifetime is evaluated using the sum of the mean root square of the uncertainty of 60 days due to 25 hours launch delay and all sensitivities shown in Table ‎7.3-2 and Table ‎7.3-3. This leads to an overall lifetime uncertainty of

-139 days for the negative sensitivities (already included in the lifetime calculation above)

+142 days for the positive sensitivities

# Summary and Conclusions

The status of the H-EPLM TMM at end of June 2003 is described in detail and the corresponding analysis results are reported.

On-Ground autonomy analyses show that starting from 1.8 K, the HTT tank temperature is less than 2.15 K after six days autonomy. Thus, the on-ground autonomy requirement is fulfilled.

Calculation of the nominal lifetime applying the heat load allocations defined in IID-A [AD 01] lead to 4.0±0.4 years, which is compliant to the requirement of 3.5 years.

The corresponding lifetime prediction with implemented instrument TMMs lead to 4.2±0.4 years lifetime even for hot case environment at L2.

Transient analyses with instrument timeline have been conducted for hot and cold case environment as well as for a nearly full HTT and a nearly empty HTT (EOL).

# ANNEX 1:   Nodal Temperature Listing

|  |  |  | Orbit hot | Orbit cold | Orbit save | Ground | Ground, IMT |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Node |  | LABEL | T [K] | T [K] | T [K] | T [K] | T [K] |
| 10 |  | MAIN TANK He II | 1.65 | 1.63128 | 1.58045 | 1.8 | 1.8 |
| 20 |  | AUXILIARY TANK He I | 16.30049 | 15.64733 | 15.45041 | 58.40089 | 4.2 |
| 111 |  | MLI ON MAIN TANK LOW | 11.33225 | 10.21529 | 9.86063 | 82.17459 | 3.67384 |
| 112 |  | MLI ON MAIN TANK CYL | 11.20946 | 10.12936 | 9.76928 | 78.72209 | 7.98171 |
| 113 |  | MLI ON MAIN TANK UPP | 8.03813 | 7.29724 | 6.9555 | 71.87058 | 31.75451 |
| 121 |  | MLI ON AUX TANK LOW | 20.35442 | 19.31397 | 19.00791 | 83.37301 | 4.92148 |
| 122 |  | MLI ON AUX TANK UPP | 19.67869 | 18.69842 | 18.40961 | 82.96261 | 5.11556 |
| 201 |  | SF strut tank end lo | 1.66223 | 1.64262 | 1.59156 | 2.00941 | 1.80187 |
| 202 |  | SF belt fitting lo | 15.59322 | 14.98454 | 14.80174 | 55.39835 | 5.25504 |
| 203 |  | SF Ti-head lo | 15.59472 | 14.98619 | 14.80346 | 55.42247 | 5.27186 |
| 211 |  | SF strut tank end up | 1.65563 | 1.63679 | 1.58437 | 1.85147 | 1.80343 |
| 212 |  | SF belt fitting up | 10.1439 | 10.00081 | 8.07569 | 30.93268 | 7.56466 |
| 213 |  | SF Ti-head up | 10.15047 | 10.00734 | 8.08145 | 30.95229 | 7.57004 |
| 250 |  | Suspension Straps low | 27.62813 | 26.73275 | 26.48351 | 88.0143 | 13.53601 |
| 260 |  | Suspension Straps upp | 25.50642 | 24.75764 | 24.30328 | 76.90374 | 21.68328 |
| 310 |  | Instr. Shield Cyl. | 10.12165 | 9.97758 | 7.9492 | 33.59487 | 8.87504 |
| 311 |  | Instr. Shield Top | 10.18757 | 10.03136 | 8.01477 | 35.85081 | 9.47833 |
| 315 |  | Instr. Shield Baffle | 10.22861 | 10.06151 | 8.0508 | 37.84016 | 10.0954 |
| 371 |  | Opt. Bench +Z | 9.95527 | 9.83418 | 7.79499 | 27.67615 | 6.52349 |
| 372 |  | Opt. Bench +Z -Y | 9.60583 | 9.50521 | 7.53573 | 26.27158 | 6.69447 |
| 373 |  | Opt. Bench +Z mid | 9.98222 | 9.85966 | 7.80939 | 28.50379 | 6.99456 |
| 374 |  | Opt. Bench +Z +Y | 10.03567 | 9.90904 | 7.86365 | 28.37967 | 6.37825 |
| 375 |  | Opt. Bench -Y | 10.07251 | 9.94602 | 7.85511 | 30.34434 | 8.11441 |
| 376 |  | Opt. Bench centre | 10.11295 | 9.98433 | 7.88395 | 30.32385 | 7.99942 |
| 377 |  | Opt. Bench +Y | 10.10835 | 9.97757 | 7.90289 | 29.73231 | 6.92206 |
| 378 |  | Opt. Bench -Z -Y | 10.15805 | 10.02376 | 7.94092 | 31.65236 | 8.36575 |
| 379 |  | Opt. Bench -Z mid | 10.1334 | 10.00003 | 7.91788 | 31.30473 | 8.14864 |
| 380 |  | Opt. Bench -Z +Y | 10.172 | 10.0377 | 7.95749 | 30.98806 | 7.70476 |
| 381 |  | Opt. Bench -Z | 10.11961 | 9.98476 | 7.91312 | 31.64821 | 8.23876 |
| 440 |  | filling tube 440 | 64.78939 | 61.80272 | 59.58351 | 277.21549 | 271.24919 |
| 441 |  | filling tube 441 | 63.4793 | 60.58563 | 58.44836 | 255.51292 | 246.6585 |
| 442 |  | filling tube 442 | 61.1924 | 58.44685 | 56.44118 | 237.76741 | 227.18606 |
| 443 |  | filling tube 443 | 59.02297 | 56.41413 | 54.53473 | 223.59806 | 210.86762 |
| 447 |  | empty tube 447 | 35.18727 | 34.06762 | 33.65232 | 97.86722 | 41.30944 |
| 452 |  | empty tube 452 | 33.15537 | 31.86119 | 30.94444 | 95.0808 | 86.88191 |
| 510 |  | Vline wall Tank-PACS | 1.65175 | 1.63291 | 1.58236 | 1.8089 | 4.19988 |
| 511 |  | Vline wall Tank-PACS | 1.6533 | 1.63437 | 1.58413 | 1.8141 | 4.19994 |
| 512 |  | Vline wall Tank-PACS | 1.65479 | 1.63579 | 1.58586 | 1.81894 | 4.19994 |
| 513 |  | Vline wall Tank-PACS | 1.6563 | 1.63722 | 1.58761 | 1.82379 | 4.19994 |
| 514 |  | Vline wall Tank-PACS | 1.70007 | 1.68131 | 1.6161 | 1.94448 | 4.20058 |
| 520 |  | Vline wall PACS I/F 1 | 2.36277 | 2.32607 | 1.98979 | 8.61268 | 4.34957 |
| 521 |  | Vline wall PACS I/F 1 | 2.72253 | 2.67399 | 2.2005 | 11.97611 | 5.01283 |
| 522 |  | Vline wall PACS I/F 1 | 2.42213 | 2.3876 | 2.03433 | 8.61879 | 4.37855 |
| 523 |  | Vline wall PACSI/F1/2 | 2.09161 | 2.07558 | 1.86369 | 3.27002 | 4.25129 |
| 524 |  | Vline wall PACSI/F1/2 | 2.10091 | 2.08752 | 1.8773 | 3.04381 | 4.25035 |
| 525 |  | Vline wall PACS I/F 2 | 2.64705 | 2.60934 | 2.17173 | 9.99848 | 4.42905 |
| 526 |  | Vline wall PACS I/F 2 | 2.92222 | 2.87087 | 2.32271 | 13.02714 | 5.19076 |
| 527 |  | Vline wall PACS I/F 2 | 2.6988 | 2.66217 | 2.20564 | 9.88982 | 4.46262 |
| 528 |  | Vline wall PACSI/F2/3 | 2.44226 | 2.42608 | 2.07908 | 4.39327 | 4.3092 |
| 529 |  | Vline wall PACSI/F2/3 | 2.52446 | 2.50525 | 2.12476 | 5.20958 | 4.3139 |
| 530 |  | Vline wall PACS I/F 3 | 2.80067 | 2.76434 | 2.26856 | 9.86782 | 4.48759 |
| 531 |  | Vline wall PACS I/F 3 | 3.04046 | 2.98828 | 2.39455 | 13.2691 | 5.28118 |
| 532 |  | Vline wall PACS I/F 3 | 2.88518 | 2.84624 | 2.31624 | 10.34412 | 4.53042 |
| 533 |  | Vline wall PACS-SPIRE | 2.71835 | 2.69599 | 2.23618 | 5.65649 | 4.37033 |
| 534 |  | Vline wall PACS-SPIRE | 2.72544 | 2.70407 | 2.2438 | 5.4622 | 4.36962 |
| 535 |  | Vline wall PACS-SPIRE | 2.82363 | 2.80282 | 2.31634 | 5.85363 | 4.37152 |
| 536 |  | Vline wall SPIRE I/F1 | 3.76669 | 3.70907 | 2.95898 | 13.72606 | 4.70019 |
| 537 |  | Vline wall SPIRE I/F1 | 4.27643 | 4.19621 | 3.30574 | 17.53912 | 5.98805 |
| 538 |  | Vline wall SPIRE I/F1 | 3.93516 | 3.87906 | 3.08131 | 13.72052 | 4.75091 |
| 539 |  | Vline wall SPIREI/F12 | 3.78937 | 3.7495 | 2.98784 | 10.73331 | 4.50213 |
| 540 |  | Vline wall SPIRE I/F2 | 4.09014 | 4.03034 | 3.18029 | 14.38597 | 4.78341 |
| 541 |  | Vline wall SPIRE I/F2 | 4.4042 | 4.32078 | 3.38173 | 18.20958 | 6.03886 |
| 542 |  | Vline wall SPIRE I/F2 | 4.24587 | 4.17925 | 3.28355 | 15.29277 | 4.86279 |
| 543 |  | Vline wall SPIRE-HIFI | 4.11268 | 4.073 | 3.2163 | 9.42797 | 4.57699 |
| 544 |  | Vline wall HIFI I/F | 4.84677 | 4.80784 | 3.76163 | 11.73652 | 4.60151 |
| 545 |  | Vline wall HIFI I/F | 5.20405 | 5.16122 | 4.03217 | 13.10792 | 4.7113 |
| 546 |  | Vline wall HIFI I/F | 4.96144 | 4.93002 | 3.8591 | 11.59472 | 4.60517 |
| 550 |  | Vline wall L1-L2 | 4.82422 | 4.80225 | 3.76688 | 10.44756 | 4.58622 |
| 551 |  | Vline wall L1-L2 | 4.79514 | 4.77744 | 3.7505 | 10.01311 | 4.58499 |
| 552 |  | Vline wall L1-L2 | 4.82593 | 4.81046 | 3.77584 | 9.97924 | 4.58497 |
| 553 |  | Vline wall L1-L2 | 4.96746 | 4.9558 | 3.88766 | 10.15191 | 4.58509 |
| 554 |  | Vline wall L1-L2 | 5.51539 | 5.50567 | 4.31768 | 11.2072 | 4.58881 |
| 560 |  | Vline wall Lev.2 OB | 9.09323 | 9.02733 | 7.14995 | 20.65267 | 4.86516 |
| 561 |  | Vline wall Lev.2 OB | 9.88794 | 9.77407 | 7.74666 | 24.93561 | 5.04494 |
| 562 |  | Vline wall Lev.2 OB | 10.01071 | 9.88727 | 7.84427 | 26.73621 | 5.14195 |
| 563 |  | Vline wall Lev.2 OB | 10.09607 | 9.9667 | 7.89576 | 28.35678 | 5.30708 |
| 570 |  | Vline wall L2-L3 | 10.10349 | 9.9748 | 7.89956 | 27.81381 | 5.21199 |
| 571 |  | Vline wall L2-L3 | 10.18632 | 10.0606 | 7.94052 | 27.84468 | 5.2131 |
| 580 |  | Vline wall PM JFET | 10.84136 | 10.70643 | 8.256 | 29.30595 | 5.77767 |
| 581 |  | Vline wall PM JFET | 11.07576 | 10.93378 | 8.37216 | 29.86424 | 7.49515 |
| 582 |  | Vline wall PM JFET | 11.00303 | 10.86797 | 8.33867 | 29.39967 | 5.87046 |
| 583 |  | Vline wall PM/SM JFET | 10.93849 | 10.81296 | 8.31302 | 28.32219 | 5.37413 |
| 584 |  | Vline wall SM JFET | 11.04589 | 10.90993 | 8.36297 | 28.93185 | 5.60964 |
| 585 |  | Vline wall SM JFET | 11.08338 | 10.94321 | 8.38098 | 29.1627 | 6.4065 |
| 586 |  | Vline wall SM JFET | 11.07105 | 10.93304 | 8.37558 | 28.93876 | 5.64599 |
| 590 |  | Vline wall L3-HS1 | 11.06165 | 10.92576 | 8.37213 | 28.53608 | 5.44441 |
| 591 |  | Vline wall L3-HS1 | 11.06328 | 10.92746 | 8.37411 | 28.52463 | 5.44373 |
| 592 |  | Vline wall L3-HS1 | 11.52792 | 11.38955 | 8.96762 | 28.85731 | 5.44533 |
| 642 |  | MLI filling tube 642 | 36.41951 | 35.1724 | 34.42064 | 121.89214 | 111.31971 |
| 643 |  | MLI filling tube 643 | 35.70017 | 34.50302 | 33.80217 | 115.93687 | 103.38469 |
| 647 |  | MLI filling tube 647 | 29.56892 | 28.71545 | 28.43597 | 80.60982 | 28.10641 |
| 652 |  | MLI filling tube 652 | 29.33071 | 28.42222 | 28.02061 | 79.90774 | 47.04101 |
| 1001 |  | Susp bolt lo HS 1 | 34.38889 | 33.31592 | 33.02969 | 111.14265 | 16.81375 |
| 1002 |  | Susp bolt up HS 1 | 33.94534 | 32.91425 | 32.62018 | 101.9469 | 14.18785 |
| 1010 |  | HS 1 lower bulk | 33.77745 | 32.76617 | 32.47007 | 88.13908 | 12.31721 |
| 1020 |  | HS 1 lower cyl | 33.73105 | 32.7241 | 32.42614 | 85.40696 | 11.70718 |
| 1030 |  | HS 1 upper cyl | 33.79964 | 32.78643 | 32.4891 | 89.62263 | 14.36283 |
| 1040 |  | HS 1 upper bulk | 33.80249 | 32.78893 | 32.49231 | 90.32259 | 14.65224 |
| 1110 |  | HS 1 lower bulk MLI | 39.68043 | 38.08566 | 37.91179 | 172.64986 | 19.52883 |
| 1120 |  | HS 1 lower cyl MLI | 39.62699 | 38.03483 | 37.86659 | 168.52194 | 16.4966 |
| 1130 |  | HS 1 upper cyl MLI | 39.8651 | 38.24019 | 38.04214 | 178.86032 | 59.25636 |
| 1140 |  | HS 1 upper bulk MLI | 39.76222 | 38.13961 | 37.95767 | 181.8056 | 38.31658 |
| 1210 |  | HS 1 lower strap I/F | 33.77622 | 32.76503 | 32.4685 | 87.79066 | 12.25417 |
| 1220 |  | HS 1 upper strap I/F | 33.78682 | 32.77458 | 32.47743 | 88.82023 | 13.38965 |
| 2001 |  | Susp bolt lo HS 2 | 43.17074 | 41.57596 | 41.40077 | 162.89389 | 48.06274 |
| 2002 |  | Susp bolt up HS 2 | 42.7715 | 41.17459 | 41.05909 | 168.08637 | 43.72177 |
| 2010 |  | HS 2 lower bulk | 42.55222 | 40.97121 | 40.88774 | 175.49915 | 31.95847 |
| 2020 |  | HS 2 lower cyl | 42.50487 | 40.9253 | 40.85031 | 171.3471 | 28.59594 |
| 2030 |  | HS 2 upper cyl | 42.60162 | 41.00133 | 40.91055 | 181.25111 | 45.04451 |
| 2040 |  | HS 2 upper bulk | 42.62793 | 41.01393 | 40.91958 | 184.74509 | 47.71708 |
| 2050 |  | HS 2 baffle | 42.66553 | 41.02991 | 40.93202 | 185.49746 | 49.4777 |
| 2090 |  | HS 2 LO Baffles. | 42.8348 | 41.19305 | 41.06345 | 212.01615 | 123.26874 |
| 2110 |  | HS 2 lower bulk MLI | 50.57562 | 48.363 | 47.75453 | 227.93579 | 126.11454 |
| 2120 |  | HS 2 lower cyl MLI | 50.51578 | 48.30839 | 47.71333 | 224.79731 | 109.21508 |
| 2130 |  | HS 2 upper cyl MLI | 50.66108 | 48.43869 | 47.81652 | 230.28968 | 136.32943 |
| 2140 |  | HS 2 upper bulk MLI | 50.61048 | 48.38941 | 47.77417 | 232.09543 | 143.23221 |
| 2210 |  | HS 2 lower strap I/F | 42.55018 | 40.96927 | 40.88676 | 173.21003 | 31.09245 |
| 2220 |  | HS 2 upper strap I/F | 42.57762 | 40.98632 | 40.89971 | 176.23898 | 38.71192 |
| 3001 |  | Susp bolt lo HS 3 | 52.74046 | 50.52775 | 49.73058 | 234.59251 | 142.01847 |
| 3002 |  | Susp bolt up HS 3 | 52.39196 | 50.20136 | 49.48288 | 235.65185 | 138.47874 |
| 3010 |  | HS 3 lower bulk | 52.19184 | 50.02126 | 49.35006 | 235.66436 | 132.51781 |
| 3020 |  | HS 3 lower cyl | 52.13396 | 49.96912 | 49.31121 | 232.57465 | 114.75731 |
| 3030 |  | HS 3 upper cyl | 52.20487 | 50.03212 | 49.35791 | 237.50975 | 141.54496 |
| 3040 |  | HS 3 upper bulk | 52.21675 | 50.04229 | 49.36561 | 239.38539 | 150.44894 |
| 3111 |  | HS 3 lower bulk MLI 1 | 67.3724 | 63.99137 | 61.46939 | 289.47859 | 285.89924 |
| 3112 |  | HS 3 lower bulk MLI 2 | 67.03228 | 63.70117 | 61.19443 | 289.47859 | 285.89924 |
| 3113 |  | HS 3 lower bulk MLI 3 | 66.28241 | 63.04992 | 60.59513 | 289.47859 | 285.89924 |
| 3114 |  | HS 3 lower bulk MLI 4 | 65.67701 | 62.52309 | 60.11598 | 289.47859 | 285.89924 |
| 3115 |  | HS 3 lower bulk MLI 5 | 65.56919 | 62.4251 | 60.03289 | 289.47859 | 285.89924 |
| 3116 |  | HS 3 lower bulk MLI 6 | 65.99655 | 62.7899 | 60.37417 | 289.47859 | 285.89924 |
| 3117 |  | HS 3 lower bulk MLI 7 | 66.73521 | 63.43232 | 60.96258 | 289.47859 | 285.89924 |
| 3118 |  | HS 3 lower bulk MLI 8 | 67.26048 | 63.89007 | 61.38222 | 289.47859 | 285.89924 |
| 3121 |  | HS 3 lower cyl MLI 1 | 66.91861 | 63.55685 | 61.11814 | 289.27765 | 285.72177 |
| 3122 |  | HS 3 lower cyl MLI 2 | 66.68207 | 63.35977 | 60.93212 | 289.27765 | 285.72177 |
| 3123 |  | HS 3 lower cyl MLI 3 | 65.41439 | 62.24656 | 59.9204 | 289.27765 | 285.72177 |
| 3124 |  | HS 3 lower cyl MLI 4 | 64.488 | 61.44264 | 59.20115 | 289.27765 | 285.72177 |
| 3125 |  | HS 3 lower cyl MLI 5 | 64.32456 | 61.29489 | 59.07777 | 289.27765 | 285.72177 |
| 3126 |  | HS 3 lower cyl MLI 6 | 64.92986 | 61.80813 | 59.55226 | 289.27765 | 285.72177 |
| 3127 |  | HS 3 lower cyl MLI 7 | 66.10781 | 62.84054 | 60.47802 | 289.27765 | 285.72177 |
| 3128 |  | HS 3 lower cyl MLI 8 | 66.74422 | 63.39934 | 60.98232 | 289.27765 | 285.72177 |
| 3131 |  | HS 3 upper cyl MLI 1 | 66.72378 | 63.35637 | 60.95255 | 289.60223 | 286.02136 |
| 3132 |  | HS 3 upper cyl MLI 2 | 66.43798 | 63.11078 | 60.70556 | 289.60223 | 286.02136 |
| 3133 |  | HS 3 upper cyl MLI 3 | 65.49196 | 62.29389 | 59.96818 | 289.60223 | 286.02136 |
| 3134 |  | HS 3 upper cyl MLI 4 | 64.59531 | 61.51303 | 59.28195 | 289.60223 | 286.02136 |
| 3135 |  | HS 3 upper cyl MLI 5 | 64.41986 | 61.3543 | 59.15243 | 289.60223 | 286.02136 |
| 3136 |  | HS 3 upper cyl MLI 6 | 64.98481 | 61.83711 | 59.59678 | 289.60223 | 286.02136 |
| 3137 |  | HS 3 upper cyl MLI 7 | 66.03908 | 62.75141 | 60.41887 | 289.60223 | 286.02136 |
| 3138 |  | HS 3 upper cyl MLI 8 | 66.58413 | 63.23035 | 60.84942 | 289.60223 | 286.02136 |
| 3141 |  | HS 3 upper bulk MLI 1 | 66.73001 | 63.34056 | 60.97452 | 289.73072 | 286.16681 |
| 3142 |  | HS 3 upper bulk MLI 2 | 66.45934 | 63.09826 | 60.7248 | 289.73072 | 286.16681 |
| 3143 |  | HS 3 upper bulk MLI 3 | 65.90505 | 62.61957 | 60.29228 | 289.73072 | 286.16681 |
| 3144 |  | HS 3 upper bulk MLI 4 | 65.09178 | 61.89444 | 59.63969 | 289.73072 | 286.16681 |
| 3145 |  | HS 3 upper bulk MLI 5 | 64.95077 | 61.76589 | 59.54689 | 289.73072 | 286.16681 |
| 3146 |  | HS 3 upper bulk MLI 6 | 65.57783 | 62.31941 | 60.06693 | 289.73072 | 286.16681 |
| 3147 |  | HS 3 upper bulk MLI 7 | 66.16722 | 62.83039 | 60.52506 | 289.73072 | 286.16681 |
| 3148 |  | HS 3 upper bulk MLI 8 | 66.62669 | 63.24853 | 60.90396 | 289.73072 | 286.16681 |
| 3210 |  | HS 3 lower strap I/F | 52.18173 | 50.01248 | 49.34359 | 234.09783 | 124.18971 |
| 3220 |  | HS 3 upper strap I/F | 52.19075 | 50.02006 | 49.34897 | 235.21266 | 129.78345 |
| 4011 |  | @CVV LOW BULK 1 | 68.64138 | 65.27942 | 62.6919 | 295 | 295 |
| 4012 |  | @CVV LOW BULK 2 | 68.28746 | 64.97621 | 62.40238 | 295 | 295 |
| 4013 |  | @CVV LOW BULK 3 | 67.50582 | 64.29456 | 61.77003 | 295 | 295 |
| 4014 |  | @CVV LOW BULK 4 | 66.87334 | 63.74183 | 61.26311 | 295 | 295 |
| 4015 |  | @CVV LOW BULK 5 | 66.76056 | 63.63889 | 61.17508 | 295 | 295 |
| 4016 |  | @CVV LOW BULK 6 | 67.20733 | 64.02191 | 61.53642 | 295 | 295 |
| 4017 |  | @CVV LOW BULK 7 | 67.97803 | 64.69503 | 62.15795 | 295 | 295 |
| 4018 |  | @CVV LOW BULK 8 | 68.52496 | 65.17362 | 62.60015 | 295 | 295 |
| 4021 |  | @CVV LOW CYL 1 | 68.17324 | 64.82949 | 62.32545 | 295 | 295 |
| 4022 |  | @CVV LOW CYL 2 | 67.92684 | 64.62332 | 62.12933 | 295 | 295 |
| 4023 |  | @CVV LOW CYL 3 | 66.603 | 63.45567 | 61.05952 | 295 | 295 |
| 4024 |  | @CVV LOW CYL 4 | 65.63174 | 62.60895 | 60.2955 | 295 | 295 |
| 4025 |  | @CVV LOW CYL 5 | 65.46003 | 62.45299 | 60.16414 | 295 | 295 |
| 4026 |  | @CVV LOW CYL 6 | 66.09542 | 62.99428 | 60.66885 | 295 | 295 |
| 4027 |  | @CVV LOW CYL 7 | 67.32785 | 64.07936 | 61.64983 | 295 | 295 |
| 4028 |  | @CVV LOW CYL 8 | 67.9916 | 64.66473 | 62.18227 | 295 | 295 |
| 4031 |  | @CVV UPP CYL 1 | 67.96518 | 64.61466 | 62.14667 | 295 | 295 |
| 4032 |  | @CVV UPP CYL 2 | 67.66718 | 64.35744 | 61.88598 | 295 | 295 |
| 4033 |  | @CVV UPP CYL 3 | 66.67875 | 63.50005 | 61.10574 | 295 | 295 |
| 4034 |  | @CVV UPP CYL 4 | 65.73876 | 62.67762 | 60.3769 | 295 | 295 |
| 4035 |  | @CVV UPP CYL 5 | 65.55446 | 62.51007 | 60.23902 | 295 | 295 |
| 4036 |  | @CVV UPP CYL 6 | 66.14748 | 63.01931 | 60.71162 | 295 | 295 |
| 4037 |  | @CVV UPP CYL 7 | 67.2508 | 63.98062 | 61.58297 | 295 | 295 |
| 4038 |  | @CVV UPP CYL 8 | 67.8196 | 64.4827 | 62.03785 | 295 | 295 |
| 4041 |  | @CVV UPP BULK 1 | 67.97081 | 64.59728 | 62.16915 | 295 | 295 |
| 4042 |  | @CVV UPP BULK 2 | 67.68859 | 64.34349 | 61.90559 | 295 | 295 |
| 4043 |  | @CVV UPP BULK 3 | 67.10986 | 63.84138 | 61.44832 | 295 | 295 |
| 4044 |  | @CVV UPP BULK 4 | 66.2587 | 63.07881 | 60.75646 | 295 | 295 |
| 4045 |  | @CVV UPP BULK 5 | 66.11085 | 62.94337 | 60.65787 | 295 | 295 |
| 4046 |  | @CVV UPP BULK 6 | 66.7677 | 63.52602 | 61.20967 | 295 | 295 |
| 4047 |  | @CVV UPP BULK 7 | 67.38373 | 64.06264 | 61.69454 | 295 | 295 |
| 4048 |  | @CVV UPP BULK 8 | 67.86311 | 64.50092 | 62.09471 | 295 | 295 |
| 4050 |  | @CVV -Z Radiator | 64.69756 | 61.77705 | 59.562 | 295 | 295 |
| 4051 |  | CVV -Z Rad. arithm. low | 65.25021 | 62.26605 | 59.99364 | 295 | 295 |
| 4052 |  | CVV -Z Rad. arithm. upp | 65.30701 | 62.29935 | 60.03743 | 295 | 295 |
| 4055 |  | @CVV -Y Radiator | 66.35848 | 63.22938 | 60.8616 | 295 | 295 |
| 4057 |  | @CVV +Y Radiator | 65.8727 | 62.78014 | 60.49211 | 295 | 295 |
| 4070 |  | Cryostat baffle pz | 67.56597 | 64.20353 | 61.82661 | 295 | 295 |
| 4071 |  | Cryostat baffle my | 67.27169 | 63.94607 | 61.56883 | 295 | 295 |
| 4072 |  | Cryostat baffle mz | 66.53692 | 63.2783 | 60.96359 | 295 | 295 |
| 4073 |  | Cryostat baffle py | 67.11981 | 63.80505 | 61.46311 | 295 | 295 |
| 4075 |  | Cryostat inner baffle | 67.06876 | 63.69481 | 61.36581 | 295 | 295 |
| 4079 |  | Cryostat baffle top | 67.1137 | 63.77738 | 61.43237 | 295 | 295 |
| 4081 |  | Pretension 1 | 66.88903 | 63.64177 | 61.27936 | 295 | 295 |
| 4082 |  | Pretension 2 | 66.66236 | 63.4521 | 61.099 | 295 | 295 |
| 4083 |  | Pretension 3 | 65.4448 | 62.37812 | 60.11538 | 295 | 295 |
| 4084 |  | Pretension 4 | 64.55181 | 61.59955 | 59.41288 | 295 | 295 |
| 4085 |  | Pretension 5 | 64.39396 | 61.45617 | 59.29194 | 295 | 295 |
| 4086 |  | Pretension 6 | 64.97809 | 61.95384 | 59.75626 | 295 | 295 |
| 4087 |  | Pretension 7 | 66.11139 | 62.95173 | 60.65809 | 295 | 295 |
| 4088 |  | Pretension 8 | 66.72193 | 63.49019 | 61.14768 | 295 | 295 |
| 4090 |  | CVV LO windows | 67.44392 | 64.13828 | 61.67367 | 291.50689 | 291.34108 |
| 4103 |  | CVV MLI LOW BULK top 3 | 91.91746 | 84.72659 | 80.28327 | 295 | 295 |
| 4104 |  | CVV MLI LOW BULK top 4 | 71.76618 | 65.38291 | 58.78955 | 295 | 295 |
| 4105 |  | CVV MLI LOW BULK top 5 | 71.20048 | 64.84938 | 58.3219 | 295 | 295 |
| 4106 |  | CVV MLI LOW BULK top 6 | 82.61432 | 76.16281 | 72.66365 | 295 | 295 |
| 4111 |  | CVV MLI LOW BULK 1 | 161.37921 | 147.69874 | 139.12009 | 295 | 295 |
| 4112 |  | CVV MLI LOW BULK 2 | 149.27454 | 135.71099 | 124.99199 | 295 | 295 |
| 4113 |  | CVV MLI LOW BULK 3 | 149.10046 | 133.41914 | 116.0863 | 295 | 295 |
| 4114 |  | CVV MLI LOW BULK 4 | 144.67215 | 128.38697 | 108.28435 | 295 | 295 |
| 4115 |  | CVV MLI LOW BULK 5 | 144.11437 | 127.77313 | 107.52184 | 295 | 295 |
| 4116 |  | CVV MLI LOW BULK 6 | 146.52113 | 130.65031 | 112.97065 | 295 | 295 |
| 4117 |  | CVV MLI LOW BULK 7 | 146.8644 | 133.2623 | 122.78172 | 295 | 295 |
| 4118 |  | CVV MLI LOW BULK 8 | 161.44051 | 147.73165 | 139.27415 | 295 | 295 |
| 4121 |  | CVV MLI LOW CYL 1 | 151.23333 | 140.38162 | 137.23193 | 295 | 295 |
| 4122 |  | CVV MLI LOW CYL 2 | 123.10136 | 113.98395 | 109.78026 | 295 | 295 |
| 4127 |  | CVV MLI LOW CYL 7 | 124.99096 | 115.49117 | 112.25746 | 295 | 295 |
| 4128 |  | CVV MLI LOW CYL 8 | 151.59809 | 140.68147 | 137.65437 | 295 | 295 |
| 4131 |  | CVV MLI UPP CYL 1 | 148.31303 | 137.2874 | 134.63138 | 295 | 295 |
| 4132 |  | CVV MLI UPP CYL 2 | 123.71524 | 114.59521 | 109.97761 | 295 | 295 |
| 4137 |  | CVV MLI UPP CYL 7 | 120.99589 | 111.53398 | 108.88282 | 295 | 295 |
| 4138 |  | CVV MLI UPP CYL 8 | 148.90051 | 137.79855 | 135.26447 | 295 | 295 |
| 4141 |  | CVV MLI UPP BULK 1 | 131.27505 | 118.82258 | 116.45984 | 295 | 295 |
| 4142 |  | CVV MLI UPP BULK 2 | 114.28331 | 103.81792 | 100.60146 | 295 | 295 |
| 4143 |  | CVV MLI UPP BULK 3 | 85.16444 | 78.41466 | 74.51016 | 295 | 295 |
| 4146 |  | CVV MLI UPP BULK 6 | 81.31295 | 74.26389 | 72.36169 | 295 | 295 |
| 4147 |  | CVV MLI UPP BULK 7 | 112.69132 | 101.95013 | 99.85733 | 295 | 295 |
| 4148 |  | CVV MLI UPP BULK 8 | 131.49224 | 119.00526 | 116.82547 | 295 | 295 |
| 4155 |  | CVV -Y Rad. MLI | 123.76625 | 115.74181 | 108.6238 | 295 | 295 |
| 4156 |  | CVV -Y Rad. MLI2 | 59.3195 | 56.33877 | 54.06221 | 295 | 295 |
| 4157 |  | CVV +Y Rad. MLI | 136.92872 | 126.79044 | 123.88771 | 295 | 295 |
| 4158 |  | CVV +Y Rad. MLI2 | 58.76422 | 55.68495 | 53.7102 | 295 | 295 |
| 4170 |  | Cryos. baf. MLI pz | 132.21411 | 120.43367 | 118.22266 | 295 | 295 |
| 4171 |  | Cryos. baf. MLI my | 104.27003 | 95.55746 | 92.1534 | 295 | 295 |
| 4173 |  | Cryos. baf. MLI py | 102.49075 | 93.45198 | 91.43169 | 295 | 295 |
| 4179 |  | Cryos. baf. MLI top | 82.72161 | 74.98847 | 72.2548 | 295 | 295 |
| 4200 |  | LOU baseplate | 139.75844 | 136.39697 | 101.59142 | 163.55112 | 177.77024 |
| 4201 |  | LOU Rad +X | 138.47233 | 135.083 | 101.43768 | 164.87452 | 177.73331 |
| 4202 |  | LOU MLI -X | 135.95655 | 128.39539 | 115.16353 | 222.94869 | 224.79556 |
| 4203 |  | LOU MLI +Y | 129.37835 | 121.37929 | 112.77043 | 219.88201 | 220.92021 |
| 4204 |  | LOU MLI -Y | 136.70041 | 130.98712 | 110.42704 | 192.99187 | 198.10584 |
| 4205 |  | LOU MLI +Z | 146.30089 | 137.3977 | 127.80768 | 198.04652 | 200.69351 |
| 4206 |  | LOU Rad -Z | 138.59503 | 135.21853 | 101.5119 | 166.05009 | 178.92843 |
| 4250 |  | LOU Radiator | 133.41453 | 130.43809 | 99.9119 | 155.18619 | 165.5097 |
| 4251 |  | LOU Rad. MLI | 134.67618 | 128.37909 | 112.07108 | 203.21666 | 206.11883 |
| 4361 |  | LOUA Waveguid 1 | 125.61267 | 118.10335 | 108.89447 | 295 | 295 |
| 4362 |  | LOUA Waveguid 2 | 117.2016 | 109.14225 | 104.58414 | 295 | 295 |
| 4363 |  | LOUA Waveguid 3 | 113.5459 | 105.48724 | 101.73405 | 295 | 295 |
| 4364 |  | LOUA Waveguid 4 | 113.34166 | 105.15292 | 101.19373 | 295 | 295 |
| 4365 |  | LOUA Waveguid 5 | 119.56236 | 110.89174 | 105.60001 | 295 | 295 |
| 4366 |  | LOUA Waveguid 6 | 157.41755 | 145.34862 | 134.09304 | 295 | 295 |
| 5000 |  | GHe tank outlet | 1.65 | 1.63128 | 1.58045 | 1.8 | 4.2 |
| 5010 |  | GHe Tank-PACS | 1.65149 | 1.63269 | 1.58218 | 1.80484 | 4.19993 |
| 5011 |  | GHe Tank-PACS | 1.65298 | 1.6341 | 1.58392 | 1.80969 | 4.19994 |
| 5012 |  | GHe Tank-PACS | 1.65448 | 1.63552 | 1.58565 | 1.81453 | 4.19994 |
| 5013 |  | GHe Tank-PACS | 1.65598 | 1.63695 | 1.5874 | 1.81938 | 4.19994 |
| 5014 |  | GHe PACS I/F 1 | 1.69259 | 1.67445 | 1.61305 | 1.88455 | 4.20028 |
| 5020 |  | GHe PACS I/F 1 | 1.8314 | 1.81545 | 1.70338 | 2.27721 | 4.21216 |
| 5021 |  | GHe PACS I/F 1 | 1.91882 | 1.90369 | 1.75855 | 2.53037 | 4.23822 |
| 5022 |  | GHe PACS I/F 1 | 2.02898 | 2.01452 | 1.8273 | 2.87929 | 4.24938 |
| 5023 |  | GHe PACS I/F 1/2 | 2.06914 | 2.05491 | 1.85298 | 2.98355 | 4.24997 |
| 5024 |  | GHe PACS I/F 2 | 2.10063 | 2.08729 | 1.87721 | 3.0293 | 4.25028 |
| 5025 |  | GHe PACS I/F 2 | 2.2299 | 2.21658 | 1.95474 | 3.44996 | 4.2645 |
| 5026 |  | GHe PACS I/F 2 | 2.30592 | 2.29196 | 1.99913 | 3.72773 | 4.29463 |
| 5027 |  | GHe PACS I/F 2 | 2.40282 | 2.38757 | 2.05514 | 4.11086 | 4.30799 |
| 5028 |  | GHe PACS I/F 2/3 | 2.43608 | 2.42067 | 2.07617 | 4.21035 | 4.30852 |
| 5029 |  | GHe PACS I/F 3 | 2.48405 | 2.46829 | 2.10465 | 4.3701 | 4.30963 |
| 5030 |  | GHe PACS I/F 3 | 2.56569 | 2.54823 | 2.15056 | 4.72243 | 4.32378 |
| 5031 |  | GHe PACS I/F 3 | 2.62194 | 2.60294 | 2.18167 | 4.98678 | 4.35492 |
| 5032 |  | GHe PACS I/F 3 | 2.69214 | 2.67083 | 2.22024 | 5.34851 | 4.36887 |
| 5033 |  | GHe PACS-SPIRE | 2.71436 | 2.69255 | 2.23417 | 5.44351 | 4.36947 |
| 5034 |  | GHe PACS-SPIRE | 2.72453 | 2.70325 | 2.24318 | 5.45073 | 4.36955 |
| 5035 |  | GHe SPIRE I/F 1 | 2.81602 | 2.79623 | 2.31196 | 5.60507 | 4.37053 |
| 5036 |  | GHe SPIRE I/F 1 | 3.11592 | 3.09687 | 2.52632 | 6.25614 | 4.39672 |
| 5037 |  | GHe SPIRE I/F 1 | 3.29489 | 3.27518 | 2.65246 | 6.65527 | 4.4484 |
| 5038 |  | GHe SPIRE I/F 1 | 3.51137 | 3.48896 | 2.8037 | 7.23477 | 4.47243 |
| 5039 |  | GHe SPIRE I/F 2 | 3.668 | 3.6413 | 2.91109 | 7.74535 | 4.47696 |
| 5040 |  | GHe SPIRE I/F 2 | 3.81649 | 3.78444 | 3.01046 | 8.30427 | 4.5013 |
| 5041 |  | GHe SPIRE I/F 2 | 3.91368 | 3.87763 | 3.07577 | 8.66843 | 4.55123 |
| 5042 |  | GHe SPIRE I/F 2 | 4.03401 | 3.99177 | 3.15519 | 9.24087 | 4.57596 |
| 5043 |  | GHe HIFI I/F | 4.1125 | 4.07281 | 3.21616 | 9.36737 | 4.57667 |
| 5044 |  | GHe HIFI I/F | 4.39556 | 4.36946 | 3.44307 | 9.56324 | 4.57865 |
| 5045 |  | GHe HIFI I/F | 4.54507 | 4.52403 | 3.56241 | 9.68631 | 4.58297 |
| 5046 |  | GHe HIFI I/F | 4.7108 | 4.69339 | 3.69014 | 9.84446 | 4.58474 |
| 5050 |  | GHe L1-L2 | 4.77379 | 4.75632 | 3.7357 | 9.92124 | 4.58493 |
| 5051 |  | GHe L1-L2 | 4.78565 | 4.76854 | 3.74449 | 9.93283 | 4.58495 |
| 5052 |  | GHe L1-L2 | 4.80809 | 4.79285 | 3.76316 | 9.93868 | 4.58496 |
| 5053 |  | GHe L1-L2 | 4.89781 | 4.88837 | 3.83802 | 9.96572 | 4.58498 |
| 5054 |  | GHe L1-L2 | 5.26067 | 5.2658 | 4.137 | 10.12594 | 4.58546 |
| 5060 |  | GHe Lev.2 OB | 9.08449 | 9.01875 | 7.14308 | 17.99507 | 4.77124 |
| 5061 |  | GHe Lev.2 OB | 9.8861 | 9.77235 | 7.74528 | 24.21466 | 4.98794 |
| 5062 |  | GHe Lev.2 OB | 10.01042 | 9.887 | 7.84404 | 25.74829 | 5.05834 |
| 5063 |  | GHe Lev.2 OB | 10.09587 | 9.96652 | 7.89564 | 27.78657 | 5.21159 |
| 5070 |  | GHe L2-L3 | 10.10347 | 9.97478 | 7.89955 | 27.80268 | 5.21177 |
| 5071 |  | GHe PM JFET I/F | 10.18613 | 10.0604 | 7.94042 | 27.84166 | 5.21286 |
| 5080 |  | GHe PM JFET I/F | 10.60802 | 10.49117 | 8.1533 | 28.02508 | 5.25757 |
| 5081 |  | GHe PM JFET I/F | 10.76757 | 10.64988 | 8.23343 | 28.12158 | 5.32987 |
| 5082 |  | GHe PM JFET I/F | 10.92019 | 10.79624 | 8.30511 | 28.28221 | 5.37266 |
| 5083 |  | GHe SM JFET I/F | 10.93845 | 10.81293 | 8.313 | 28.32054 | 5.37394 |
| 5084 |  | GHe SM JFET I/F | 11.00822 | 10.87814 | 8.34712 | 28.39714 | 5.3926 |
| 5085 |  | GHe SM JFET I/F | 11.03399 | 10.90159 | 8.35961 | 28.43717 | 5.42546 |
| 5086 |  | GHe SM JFET I/F | 11.05808 | 10.92275 | 8.37053 | 28.50009 | 5.44293 |
| 5090 |  | GHe L3-HS1 | 11.06164 | 10.92575 | 8.37212 | 28.52371 | 5.44365 |
| 5091 |  | GHe L3-HS1 | 11.06328 | 10.92745 | 8.3741 | 28.5243 | 5.4437 |
| 5092 |  | GHe L3-HS1 | 11.52686 | 11.3885 | 8.96627 | 28.74346 | 5.4445 |
| 5100 |  | Heat Shield 1 out GHe | 33.73105 | 32.7241 | 32.42614 | 85.40698 | 11.70719 |
| 5200 |  | Heat Shield 2 out GHe | 42.50487 | 40.9253 | 40.85031 | 171.34713 | 28.59595 |
| 5300 |  | Heat Shield 3 out GHe | 52.13396 | 49.96912 | 49.31121 | 232.57467 | 114.75733 |
| 5900 |  | Mass Flow Rate [mg/s] | 2.06897 | 1.93223 | 1.52008 | 31.50322 | 100 |
| 5901 |  | Helium: Init Mass [kg] | 337 | 337 | 337 | 337 | 337 |
| 5950 |  | Lifetime [days] | 1537 | 1666 | 2108 | 139 | 71 |
| 5951 |  | Heat to Tank [mW] | 47.2552 | 44.03796 | 34.42882 | 730.24457 | 66.22489 |
| 6204 |  | SVM SHIELD C. +Y-Z | 132.61103 | 119.32916 | 104.98791 | 295 | 295 |
| 6205 |  | SVM SHIELD C. -Y-Z | 133.49733 | 120.22756 | 105.87464 | 295 | 295 |
| 6206 |  | SVM SHIELD -Z | 128.90372 | 116.51778 | 102.69224 | 295 | 295 |
| 6304 |  | SVM SHLD MLI C. +Y-Z | 109.45733 | 99.91816 | 93.23849 | 295 | 295 |
| 6305 |  | SVM SHLD MLI C. -Y-Z | 113.91356 | 104.26087 | 97.2875 | 295 | 295 |
| 6306 |  | SVM SHLD MLI -Z | 92.00973 | 83.50899 | 74.73981 | 295 | 295 |
| 6501 |  | STRUT1_CVVSVM | 229.5441 | 226.96036 | 199.47733 | 295 | 295 |
| 6502 |  | STRUT1_CVVSVM | 173.97657 | 168.35697 | 152.2728 | 295 | 295 |
| 6503 |  | STRUT1_CVVSVM | 117.42577 | 110.7701 | 102.3398 | 295 | 295 |
| 6511 |  | STRUT2_CVVSVM | 228.47981 | 226.13892 | 198.49971 | 295 | 295 |
| 6512 |  | STRUT2_CVVSVM | 172.29861 | 167.01237 | 150.72771 | 295 | 295 |
| 6513 |  | STRUT2_CVVSVM | 116.50946 | 110.01133 | 101.46838 | 295 | 295 |
| 6521 |  | STRUT3_CVVSVM | 228.1181 | 225.85298 | 198.1336 | 295 | 295 |
| 6522 |  | STRUT3_CVVSVM | 170.63373 | 165.68413 | 149.25137 | 295 | 295 |
| 6523 |  | STRUT3_CVVSVM | 113.2682 | 107.44249 | 98.87426 | 295 | 295 |
| 6531 |  | STRUT4_CVVSVM | 226.95932 | 224.93866 | 196.96763 | 295 | 295 |
| 6532 |  | STRUT4_CVVSVM | 168.5668 | 164.03483 | 147.31917 | 295 | 295 |
| 6533 |  | STRUT4_CVVSVM | 112.21537 | 106.58289 | 97.87937 | 295 | 295 |
| 6541 |  | STRUT5_CVVSVM | 227.00229 | 224.95855 | 196.90095 | 295 | 295 |
| 6542 |  | STRUT5_CVVSVM | 167.01749 | 162.94381 | 146.29833 | 295 | 295 |
| 6543 |  | STRUT5_CVVSVM | 109.06247 | 104.30603 | 95.9099 | 295 | 295 |
| 6551 |  | STRUT6_CVVSVM | 226.64843 | 224.55636 | 196.05894 | 295 | 295 |
| 6552 |  | STRUT6_CVVSVM | 166.16826 | 162.08979 | 144.84237 | 295 | 295 |
| 6553 |  | STRUT6_CVVSVM | 107.43523 | 102.95963 | 94.45526 | 295 | 295 |
| 6561 |  | STRUT7_CVVSVM | 225.76689 | 223.85403 | 195.25899 | 295 | 295 |
| 6562 |  | STRUT7_CVVSVM | 163.14054 | 159.65651 | 142.26383 | 295 | 295 |
| 6563 |  | STRUT7_CVVSVM | 102.47334 | 99.15276 | 90.93393 | 295 | 295 |
| 6571 |  | STRUT8_CVVSVM | 225.18947 | 223.38917 | 194.71842 | 295 | 295 |
| 6572 |  | STRUT8_CVVSVM | 163.29411 | 159.62327 | 141.89338 | 295 | 295 |
| 6573 |  | STRUT8_CVVSVM | 102.32044 | 98.97155 | 90.62126 | 295 | 295 |
| 6581 |  | STRUT9_CVVSVM | 225.02985 | 223.26384 | 194.56869 | 295 | 295 |
| 6582 |  | STRUT9_CVVSVM | 162.78417 | 159.1944 | 141.39373 | 295 | 295 |
| 6583 |  | STRUT9_CVVSVM | 101.57912 | 98.33484 | 89.95493 | 295 | 295 |
| 6591 |  | STRUT10_CVVSVM | 224.6256 | 222.97792 | 194.30116 | 295 | 295 |
| 6592 |  | STRUT10_CVVSVM | 162.47747 | 158.95962 | 141.13103 | 295 | 295 |
| 6593 |  | STRUT10_CVVSVM | 102.1766 | 98.70825 | 90.11032 | 295 | 295 |
| 6601 |  | STRUT11_CVVSVM | 224.52911 | 222.91054 | 194.24274 | 295 | 295 |
| 6602 |  | STRUT11_CVVSVM | 162.05404 | 158.66085 | 140.89568 | 295 | 295 |
| 6603 |  | STRUT11_CVVSVM | 101.8569 | 98.48125 | 89.93413 | 295 | 295 |
| 6611 |  | STRUT12_CVVSVM | 224.54974 | 222.91914 | 194.2419 | 295 | 295 |
| 6612 |  | STRUT12_CVVSVM | 162.21574 | 158.75107 | 140.92945 | 295 | 295 |
| 6613 |  | STRUT12_CVVSVM | 102.28444 | 98.73457 | 90.04392 | 295 | 295 |
| 6621 |  | STRUT13_CVVSVM | 224.55128 | 222.92302 | 194.25742 | 295 | 295 |
| 6622 |  | STRUT13_CVVSVM | 162.16907 | 158.73499 | 140.96943 | 295 | 295 |
| 6623 |  | STRUT13_CVVSVM | 101.53711 | 98.26124 | 89.82235 | 295 | 295 |
| 6631 |  | STRUT14_CVVSVM | 224.96583 | 223.20698 | 194.51388 | 295 | 295 |
| 6632 |  | STRUT14_CVVSVM | 162.84712 | 159.20237 | 141.35748 | 295 | 295 |
| 6633 |  | STRUT14_CVVSVM | 101.94984 | 98.54328 | 90.03369 | 295 | 295 |
| 6641 |  | STRUT15_CVVSVM | 224.97518 | 223.22481 | 194.57033 | 295 | 295 |
| 6642 |  | STRUT15_CVVSVM | 162.5083 | 159.04293 | 141.44027 | 295 | 295 |
| 6643 |  | STRUT15_CVVSVM | 101.67816 | 98.4709 | 90.22924 | 295 | 295 |
| 6651 |  | STRUT16_CVVSVM | 225.56255 | 223.66685 | 195.06383 | 295 | 295 |
| 6652 |  | STRUT16_CVVSVM | 163.26341 | 159.63812 | 142.12224 | 295 | 295 |
| 6653 |  | STRUT16_CVVSVM | 102.23487 | 98.90055 | 90.66892 | 295 | 295 |
| 6661 |  | STRUT17_CVVSVM | 225.75693 | 223.84785 | 195.37449 | 295 | 295 |
| 6662 |  | STRUT17_CVVSVM | 163.38485 | 159.92372 | 142.93998 | 295 | 295 |
| 6663 |  | STRUT17_CVVSVM | 104.3421 | 100.5575 | 92.43057 | 295 | 295 |
| 6671 |  | STRUT18_CVVSVM | 226.1882 | 224.30328 | 196.2527 | 295 | 295 |
| 6672 |  | STRUT18_CVVSVM | 164.75931 | 161.12965 | 144.59932 | 295 | 295 |
| 6673 |  | STRUT18_CVVSVM | 106.24372 | 102.08048 | 93.99271 | 295 | 295 |
| 6681 |  | STRUT19_CVVSVM | 226.64283 | 224.67808 | 196.75226 | 295 | 295 |
| 6682 |  | STRUT19_CVVSVM | 167.90128 | 163.49271 | 146.91147 | 295 | 295 |
| 6683 |  | STRUT19_CVVSVM | 111.41099 | 105.92636 | 97.40643 | 295 | 295 |
| 6691 |  | STRUT20_CVVSVM | 228.01178 | 225.75544 | 198.06518 | 295 | 295 |
| 6692 |  | STRUT20_CVVSVM | 170.26847 | 165.36314 | 149.00724 | 295 | 295 |
| 6693 |  | STRUT20_CVVSVM | 112.9136 | 107.09531 | 98.59858 | 295 | 295 |
| 6701 |  | STRUT21_CVVSVM | 228.33633 | 226.02395 | 198.41822 | 295 | 295 |
| 6702 |  | STRUT21_CVVSVM | 172.08766 | 166.84394 | 150.64576 | 295 | 295 |
| 6703 |  | STRUT21_CVVSVM | 116.26762 | 109.81741 | 101.3761 | 295 | 295 |
| 6711 |  | STRUT22_CVVSVM | 229.54973 | 226.962 | 199.49071 | 295 | 295 |
| 6712 |  | STRUT22_CVVSVM | 173.97405 | 168.3327 | 152.26702 | 295 | 295 |
| 6713 |  | STRUT22_CVVSVM | 117.42434 | 110.72781 | 102.30178 | 295 | 295 |
| 6721 |  | STRUT23_CVVSVM | 229.77213 | 227.13855 | 199.69247 | 295 | 295 |
| 6722 |  | STRUT23_CVVSVM | 174.70551 | 168.93123 | 152.92709 | 295 | 295 |
| 6723 |  | STRUT23_CVVSVM | 118.37262 | 111.5193 | 103.14627 | 295 | 295 |
| 6731 |  | STRUT24_CVVSVM | 229.80159 | 227.16056 | 199.70142 | 295 | 295 |
| 6732 |  | STRUT24_CVVSVM | 174.74922 | 168.96484 | 152.92318 | 295 | 295 |
| 6733 |  | STRUT24_CVVSVM | 118.54058 | 111.64435 | 103.22293 | 295 | 295 |
| 7000 |  | SOLGEN CELLS Mid low | 381.82653 | 360.33302 | 360.32246 | 295 | 295 |
| 7001 |  | SOLGEN CELLS -Y low | 361.95318 | 341.59303 | 341.58203 | 295 | 295 |
| 7002 |  | SOLGEN CELLS +Y low | 361.95315 | 341.59292 | 341.58227 | 295 | 295 |
| 7010 |  | SOLGEN CELLS Mid cent | 382.86869 | 361.30516 | 361.30318 | 295 | 295 |
| 7011 |  | SOLGEN CELLS -Y cent | 362.61659 | 342.20518 | 342.20206 | 295 | 295 |
| 7012 |  | SOLGEN CELLS +Y cent | 362.61731 | 342.20576 | 342.20289 | 295 | 295 |
| 7020 |  | SOLGEN CELLS Mid up | 380.91516 | 358.95919 | 358.95584 | 295 | 295 |
| 7021 |  | SOLGEN CELLS -Y up | 360.76633 | 339.85723 | 339.81595 | 295 | 295 |
| 7022 |  | SOLGEN CELLS +Y up | 360.76696 | 339.85767 | 339.81671 | 295 | 295 |
| 7050 |  | SUNSHADE OSR Mid low | 277.61257 | 224.06695 | 224.05918 | 295 | 295 |
| 7051 |  | SUNSHADE OSR -Y low | 260.5874 | 210.23722 | 210.22642 | 295 | 295 |
| 7052 |  | SUNSHADE OSR +Y low | 260.58749 | 210.23652 | 210.2274 | 295 | 295 |
| 7053 |  | SUNSHADE flap -Y | 218.9484 | 185.81792 | 185.80544 | 295 | 295 |
| 7054 |  | SUNSHADE flap +Y | 218.94638 | 185.81454 | 185.8058 | 295 | 295 |
| 7060 |  | SUNSHADE OSR Mid lcen | 276.15811 | 219.34537 | 219.34327 | 295 | 295 |
| 7061 |  | SUNSHADE OSR -Y lcen | 258.48474 | 205.00167 | 204.99727 | 295 | 295 |
| 7062 |  | SUNSHADE OSR +Y lcen | 258.48434 | 205.00073 | 204.99739 | 295 | 295 |
| 7070 |  | SUNSHADE OSR Mid ucen | 276.0888 | 219.02174 | 219.02149 | 295 | 295 |
| 7071 |  | SUNSHADE OSR -Y ucen | 258.49842 | 204.80369 | 204.80161 | 295 | 295 |
| 7072 |  | SUNSHADE OSR +Y ucen | 258.49835 | 204.80322 | 204.80171 | 295 | 295 |
| 7080 |  | SUNSHADE OSR Mid up | 276.13382 | 219.07741 | 219.07736 | 295 | 295 |
| 7081 |  | SUNSHADE OSR -Y up | 261.47744 | 207.42801 | 207.42772 | 295 | 295 |
| 7082 |  | SUNSHADE OSR +Y up | 261.47745 | 207.428 | 207.42776 | 295 | 295 |
| 7100 |  | SOLGEN MLI Mid low | 260.5525 | 245.40014 | 244.60288 | 295 | 295 |
| 7101 |  | SOLGEN MLI -Y low | 248.19516 | 233.6231 | 232.47586 | 295 | 295 |
| 7102 |  | SOLGEN MLI +Y low | 248.2976 | 233.70221 | 232.59126 | 295 | 295 |
| 7103 |  | SOLGEN -x rib MLI +Z low | 271.75573 | 255.13339 | 252.78127 | 295 | 295 |
| 7104 |  | SOLGEN -x rib MLI -Y low | 258.43252 | 242.42 | 239.47638 | 295 | 295 |
| 7105 |  | SOLGEN -x rib MLI +Y low | 258.19788 | 242.21071 | 239.33459 | 295 | 295 |
| 7106 |  | SOLGEN -x rib MLI +Z up | 259.06713 | 244.19262 | 243.85259 | 295 | 295 |
| 7107 |  | SOLGEN -x rib MLI -Y up | 245.85139 | 231.73755 | 231.37767 | 295 | 295 |
| 7108 |  | SOLGEN -x rib MLI +Y up | 245.87843 | 231.74631 | 231.4327 | 295 | 295 |
| 7110 |  | SOLGEN MLI Mid cent | 258.48533 | 243.64399 | 243.23625 | 295 | 295 |
| 7111 |  | SOLGEN MLI -Y cent | 245.40103 | 231.27551 | 230.75816 | 295 | 295 |
| 7112 |  | SOLGEN MLI +Y cent | 245.56592 | 231.41025 | 230.9482 | 295 | 295 |
| 7120 |  | SOLGEN MLI Mid up | 257.58953 | 242.51539 | 242.15492 | 295 | 295 |
| 7121 |  | SOLGEN MLI -Y up | 244.3426 | 229.95189 | 229.46785 | 295 | 295 |
| 7122 |  | SOLGEN MLI +Y up | 244.57254 | 230.13954 | 229.70649 | 295 | 295 |
| 7130 |  | SOLGEN MLI Mid up2 | 256.97022 | 241.76876 | 241.58356 | 295 | 295 |
| 7131 |  | SOLGEN MLI -Y up2 | 243.72013 | 229.20819 | 228.94943 | 295 | 295 |
| 7132 |  | SOLGEN MLI +Y up2 | 243.62682 | 229.11152 | 228.9009 | 295 | 295 |
| 7133 |  | SOLGEN +x rib MLI +Z low | 259.45653 | 244.18141 | 243.64336 | 295 | 295 |
| 7134 |  | SOLGEN +x rib MLI -Y low | 246.11178 | 231.53578 | 230.90268 | 295 | 295 |
| 7135 |  | SOLGEN +x rib MLI +Y low | 246.18592 | 231.58328 | 230.97879 | 295 | 295 |
| 7136 |  | SOLGEN +x rib MLI +Z up | 258.33425 | 242.75809 | 242.51609 | 295 | 295 |
| 7137 |  | SOLGEN +x rib MLI -Y up | 244.79311 | 229.97614 | 229.68795 | 295 | 295 |
| 7138 |  | SOLGEN +x rib MLI +Y up | 244.71785 | 229.89802 | 229.63915 | 295 | 295 |
| 7140 |  | SUNSHADE MLI Mid low2 | 200.42852 | 165.53234 | 164.93149 | 295 | 295 |
| 7141 |  | SUNSHADE MLI -Y low2 | 189.5353 | 157.12713 | 156.23898 | 295 | 295 |
| 7142 |  | SUNSHADE MLI +Y low2 | 189.58044 | 157.11275 | 156.40411 | 295 | 295 |
| 7143 |  | SSHADE rib MLI +Z low | 198.27739 | 166.28556 | 165.41968 | 295 | 295 |
| 7144 |  | SSHADE rib MLI -Y low | 187.27683 | 157.52784 | 156.381 | 295 | 295 |
| 7145 |  | SSHADE rib MLI +Y low | 187.36256 | 157.55586 | 156.56583 | 295 | 295 |
| 7146 |  | SSHADE rib MLI +Z up | 193.22472 | 158.32457 | 157.82487 | 295 | 295 |
| 7147 |  | SSHADE rib MLI -Y up | 181.24519 | 148.60447 | 148.0479 | 295 | 295 |
| 7148 |  | SSHADE rib MLI +Y up | 181.2053 | 148.51946 | 148.04278 | 295 | 295 |
| 7150 |  | SUNSHADE MLI Mid low | 200.22642 | 163.94416 | 163.47734 | 295 | 295 |
| 7151 |  | SUNSHADE MLI -Y low | 188.36471 | 154.54864 | 153.98198 | 295 | 295 |
| 7152 |  | SUNSHADE MLI +Y low | 188.36279 | 154.49162 | 154.0015 | 295 | 295 |
| 7153 |  | SUNSHADE flap MLI -Y | 162.77955 | 139.43088 | 138.83388 | 295 | 295 |
| 7154 |  | SUNSHADE flap MLI +Y | 162.6684 | 139.27568 | 138.75602 | 295 | 295 |
| 7160 |  | SUNSHADE MLI Mid lcen | 195.57239 | 156.74227 | 156.46292 | 295 | 295 |
| 7161 |  | SUNSHADE MLI -Y lcen | 183.67941 | 147.4955 | 147.08076 | 295 | 295 |
| 7162 |  | SUNSHADE MLI +Y lcen | 183.63037 | 147.40446 | 147.08144 | 295 | 295 |
| 7170 |  | SUNSHADE MLI Mid ucen | 191.87461 | 152.30847 | 152.29221 | 295 | 295 |
| 7171 |  | SUNSHADE MLI -Y ucen | 179.90304 | 142.72993 | 142.67797 | 295 | 295 |
| 7172 |  | SUNSHADE MLI +Y ucen | 179.92073 | 142.73202 | 142.68948 | 295 | 295 |
| 7180 |  | SUNSHADE MLI Mid up | 191.63506 | 152.07889 | 152.07209 | 295 | 295 |
| 7181 |  | SUNSHADE MLI -Y up | 181.66617 | 144.17551 | 144.16446 | 295 | 295 |
| 7182 |  | SUNSHADE MLI +Y up | 181.66846 | 144.18446 | 144.16945 | 295 | 295 |
| 7203 |  | SShld SVM gapMLI mX | 256.05306 | 234.26133 | 213.29161 | 295 | 295 |
| 7204 |  | SShld SVM gapMLI mY mX | 253.41118 | 231.90701 | 211.24512 | 295 | 295 |
| 7205 |  | SShld SVM gapMLI pY mX | 253.48914 | 231.9689 | 211.28463 | 295 | 295 |
| 7206 |  | SShld SVM gapMLI pX | 225.00244 | 207.35407 | 195.5246 | 295 | 295 |
| 7207 |  | SShld SVM gapMLI mY pX | 212.24568 | 195.29954 | 182.82559 | 295 | 295 |
| 7208 |  | SShld SVM gapMLI pY pX | 212.16472 | 195.21809 | 182.8197 | 295 | 295 |
| 8000 |  | TELESCOPE M1 Mirror | 85.74693 | 76.39013 | 74.54078 | 295 | 295 |
| 8100 |  | TELESCOPE M2 Mirror | 85.4255 | 76.16269 | 74.3383 | 257.23357 | 257.2338 |
| 8200 |  | TELESCOPE Hexapod | 85.46494 | 76.18873 | 74.36176 | 260.95001 | 260.95021 |
| 8400 |  | TEL-CVV I/F node | 81.16134 | 73.5589 | 71.69291 | 295 | 295 |
| 8501 |  | TEL M1 MLI inner ring | 127.88906 | 117.56189 | 115.05904 | 295 | 295 |
| 8502 |  | TEL M1 MLI inner ring | 118.3197 | 108.98172 | 105.60828 | 295 | 295 |
| 8503 |  | TEL M1 MLI inner ring | 98.03715 | 90.37495 | 86.65768 | 295 | 295 |
| 8504 |  | TEL M1 MLI inner ring | 78.24009 | 71.65791 | 68.77319 | 295 | 295 |
| 8505 |  | TEL M1 MLI inner ring | 76.56749 | 69.74131 | 67.94127 | 295 | 295 |
| 8506 |  | TEL M1 MLI inner ring | 95.43667 | 87.38426 | 85.45205 | 295 | 295 |
| 8507 |  | TEL M1 MLI inner ring | 116.56218 | 107.0241 | 104.72957 | 295 | 295 |
| 8508 |  | TEL M1 MLI inner ring | 127.32746 | 116.92119 | 114.64261 | 295 | 295 |
| 8511 |  | TEL M1 MLI outer ring | 127.18592 | 112.78195 | 110.83545 | 295 | 295 |
| 8512 |  | TEL M1 MLI outer ring | 112.99252 | 101.89569 | 99.3056 | 295 | 295 |
| 8513 |  | TEL M1 MLI outer ring | 82.52307 | 75.32883 | 72.36303 | 295 | 295 |
| 8514 |  | TEL M1 MLI outer ring | 67.5233 | 60.62208 | 58.70453 | 295 | 295 |
| 8515 |  | TEL M1 MLI outer ring | 67.21838 | 60.19867 | 58.65618 | 295 | 295 |
| 8516 |  | TEL M1 MLI outer ring | 81.56664 | 74.0565 | 72.24529 | 295 | 295 |
| 8517 |  | TEL M1 MLI outer ring | 112.20848 | 100.91921 | 98.96191 | 295 | 295 |
| 8518 |  | TEL M1 MLI outer ring | 127.16282 | 112.68787 | 110.90127 | 295 | 295 |
| 8550 |  | TEL M1 MLI on cryo baf | 86.21056 | 77.7887 | 75.44192 | 295 | 295 |
| 9000 |  | CVV conn. brackets | 67.50145 | 64.21034 | 61.69228 | 292.32363 | 291.95464 |
| 9101 |  | PACS int. harn. 15 | 5.60067 | 5.52437 | 4.13509 | 20.78131 | 7.37278 |
| 9102 |  | PACS int. harn. 15 | 7.96774 | 7.87002 | 6.01219 | 25.02745 | 7.80581 |
| 9103 |  | PACS int. harn. 15 | 9.52407 | 9.40547 | 7.32806 | 28.66906 | 8.00973 |
| 9104 |  | PACS int. harn. 15 | 10.12294 | 9.99402 | 7.8877 | 30.33081 | 8.00764 |
| 9105 |  | PACS int. harn. 15 | 21.29169 | 20.97237 | 14.98232 | 44.12182 | 16.2796 |
| 9106 |  | PACS int. harn. 15 | 30.43239 | 29.84359 | 23.58459 | 64.39555 | 20.82929 |
| 9107 |  | PACS int. harn. 15 | 34.01482 | 33.15899 | 29.86542 | 80.42149 | 19.02946 |
| 9108 |  | PACS int. harn. 15 | 33.91141 | 32.88701 | 32.56602 | 87.65924 | 14.38516 |
| 9109 |  | PACS int. harn. 15 | 41.07148 | 39.55374 | 38.68638 | 131.19751 | 95.20332 |
| 9110 |  | PACS int. harn. 15 | 52.93147 | 50.58128 | 48.90598 | 203.13737 | 186.08764 |
| 9111 |  | PACS int. harn. 15 | 62.96092 | 59.9564 | 57.68332 | 264.42238 | 259.27526 |
| 9121 |  | PACS int. harn. 18 | 6.58392 | 6.5216 | 4.10199 | 20.78659 | 8.13757 |
| 9122 |  | PACS int. harn. 18 | 9.08779 | 9.00392 | 5.98566 | 25.04305 | 8.97099 |
| 9123 |  | PACS int. harn. 18 | 10.10686 | 9.99578 | 7.32183 | 28.69433 | 8.71401 |
| 9124 |  | PACS int. harn. 18 | 10.13234 | 10.00317 | 7.89183 | 30.36067 | 8.01233 |
| 9125 |  | PACS int. harn. 18 | 20.8557 | 20.53264 | 14.94198 | 43.68442 | 15.55838 |
| 9126 |  | PACS int. harn. 18 | 29.90617 | 29.31293 | 23.52687 | 63.5745 | 19.69991 |
| 9127 |  | PACS int. harn. 18 | 33.69351 | 32.83816 | 29.80096 | 79.46221 | 17.80485 |
| 9128 |  | PACS int. harn. 18 | 33.83443 | 32.81812 | 32.4994 | 86.61985 | 13.19593 |
| 9129 |  | PACS int. harn. 18 | 41.10484 | 39.60908 | 38.5968 | 130.23783 | 94.36427 |
| 9130 |  | PACS int. harn. 18 | 53.02468 | 50.69403 | 48.81275 | 202.4204 | 185.43711 |
| 9131 |  | PACS int. harn. 18 | 63.02477 | 60.02862 | 57.64517 | 264.15874 | 259.03682 |
| 9141 |  | PACS int. harn. 19 | 10.38077 | 10.34283 | 4.06265 | 20.79578 | 11.42953 |
| 9142 |  | PACS int. harn. 19 | 13.7717 | 13.71599 | 5.94995 | 25.05317 | 13.71251 |
| 9143 |  | PACS int. harn. 19 | 12.91434 | 12.82643 | 7.30866 | 28.69561 | 11.85538 |
| 9144 |  | PACS int. harn. 19 | 10.15596 | 10.02688 | 7.89057 | 30.35587 | 8.03667 |
| 9145 |  | PACS int. harn. 19 | 29.1524 | 28.92061 | 15.01049 | 43.38336 | 25.54812 |
| 9146 |  | PACS int. harn. 19 | 39.82213 | 39.37812 | 23.56868 | 63.08347 | 32.72369 |
| 9147 |  | PACS int. harn. 19 | 39.35821 | 38.62985 | 29.79656 | 78.99104 | 26.79819 |
| 9148 |  | PACS int. harn. 19 | 33.82479 | 32.81201 | 32.47186 | 86.16348 | 12.6767 |
| 9149 |  | PACS int. harn. 19 | 41.83633 | 40.37863 | 38.53718 | 129.73327 | 94.13386 |
| 9150 |  | PACS int. harn. 19 | 54.04945 | 51.76798 | 48.72697 | 201.89537 | 185.35926 |
| 9151 |  | PACS int. harn. 19 | 63.57949 | 60.60976 | 57.60714 | 263.94153 | 259.05848 |
| 9161 |  | PACS int. harn. 21 | 7.33227 | 7.27749 | 4.10199 | 20.79276 | 8.7351 |
| 9162 |  | PACS int. harn. 21 | 9.95665 | 9.88104 | 5.98641 | 25.05462 | 9.85055 |
| 9163 |  | PACS int. harn. 21 | 10.58743 | 10.48091 | 7.32344 | 28.70717 | 9.27102 |
| 9164 |  | PACS int. harn. 21 | 10.1371 | 10.00781 | 7.89385 | 30.37336 | 8.01506 |
| 9165 |  | PACS int. harn. 21 | 20.62892 | 20.30242 | 14.96373 | 43.65267 | 15.23303 |
| 9166 |  | PACS int. harn. 21 | 29.61978 | 29.0216 | 23.53837 | 63.48405 | 19.22749 |
| 9167 |  | PACS int. harn. 21 | 33.53094 | 32.67281 | 29.79724 | 79.33161 | 17.42688 |
| 9168 |  | PACS int. harn. 21 | 33.82357 | 32.80851 | 32.48819 | 86.4668 | 13.03148 |
| 9169 |  | PACS int. harn. 21 | 41.22428 | 39.73357 | 38.59071 | 130.15115 | 94.46751 |
| 9170 |  | PACS int. harn. 21 | 53.19552 | 50.87155 | 48.80952 | 202.38152 | 185.55327 |
| 9171 |  | PACS int. harn. 21 | 63.11534 | 60.12295 | 57.64417 | 264.14798 | 259.09065 |
| 9201 |  | PACS int. harn. res. | 3.35401 | 3.2803 | 2.55789 | 18.31533 | 7.02541 |
| 9301 |  | SPIRE int. harn. 11 | 7.27891 | 7.20006 | 4.63157 | 27.78593 | 8.74901 |
| 9302 |  | SPIRE int. harn. 11 | 9.51543 | 9.4248 | 6.19793 | 28.87329 | 9.43096 |
| 9303 |  | SPIRE int. harn. 11 | 10.30037 | 10.18737 | 7.38473 | 29.92206 | 8.94182 |
| 9304 |  | SPIRE int. harn. 11 | 10.16351 | 10.0337 | 7.90079 | 30.43321 | 8.0378 |
| 9305 |  | SPIRE int. harn. 11 | 22.40318 | 22.09692 | 15.0275 | 44.18474 | 17.77898 |
| 9306 |  | SPIRE int. harn. 11 | 31.73128 | 31.16262 | 23.63228 | 64.6134 | 22.89579 |
| 9307 |  | SPIRE int. harn. 11 | 34.75158 | 33.90851 | 29.9047 | 80.8837 | 20.72418 |
| 9308 |  | SPIRE int. harn. 11 | 33.98242 | 32.95338 | 32.60043 | 88.26285 | 15.22311 |
| 9309 |  | SPIRE int. harn. 11 | 41.23365 | 39.73037 | 38.67211 | 131.43564 | 94.83989 |
| 9310 |  | SPIRE int. harn. 11 | 53.10984 | 50.77642 | 48.85124 | 203.02356 | 185.69138 |
| 9311 |  | SPIRE int. harn. 11 | 63.05716 | 60.06059 | 57.65662 | 264.33719 | 259.11567 |
| 9341 |  | SPIRE int. harn. res. | 4.62733 | 4.52746 | 3.50319 | 27.22844 | 7.70705 |
| 9361 |  | PM JFET int. hn. res. | 11.22576 | 11.0746 | 8.43317 | 31.36027 | 8.99639 |
| 9381 |  | SM JFET int. hn. res. | 11.10954 | 10.96584 | 8.39203 | 29.79908 | 7.08816 |
| 9401 |  | HIFI int. harn. 2+7 | 13.64984 | 13.5534 | 7.86454 | 30.70247 | 12.27911 |
| 9402 |  | HIFI int. harn. 2+7 | 15.60426 | 15.51896 | 7.87282 | 30.55447 | 14.36467 |
| 9403 |  | HIFI int. harn. 2+7 | 13.67107 | 13.57399 | 7.88109 | 30.40579 | 12.1982 |
| 9404 |  | HIFI int. harn. 2+7 | 10.14059 | 10.01189 | 7.88522 | 30.33121 | 8.02588 |
| 9405 |  | HIFI int. harn. 2+7 | 57.85018 | 57.71942 | 14.92304 | 43.27746 | 55.87274 |
| 9406 |  | HIFI int. harn. 2+7 | 77.85309 | 77.58305 | 23.4915 | 62.83154 | 73.72481 |
| 9407 |  | HIFI int. harn. 2+7 | 64.37503 | 63.86895 | 29.75159 | 78.59331 | 56.43605 |
| 9408 |  | HIFI int. harn. 2+7 | 33.77906 | 32.76994 | 32.44377 | 85.68428 | 12.06455 |
| 9409 |  | HIFI int. harn. 2+7 | 41.91517 | 40.45761 | 38.52344 | 129.39534 | 94.11919 |
| 9410 |  | HIFI int. harn. 2+7 | 54.18791 | 51.90853 | 48.7345 | 201.78972 | 185.4536 |
| 9411 |  | HIFI int. harn. 2+7 | 63.65368 | 60.6858 | 57.61272 | 263.92555 | 259.12151 |
| 9421 |  | HIFI int. harn. 3+8 | 10.33842 | 10.21323 | 7.86566 | 30.7092 | 8.47248 |
| 9422 |  | HIFI int. harn. 3+8 | 10.50244 | 10.37849 | 7.87617 | 30.57474 | 8.6006 |
| 9423 |  | HIFI int. harn. 3+8 | 10.35943 | 10.23327 | 7.88666 | 30.43973 | 8.34438 |
| 9424 |  | HIFI int. harn. 3+8 | 10.13071 | 10.00158 | 7.8919 | 30.37203 | 8.01008 |
| 9425 |  | HIFI int. harn. 3+8 | 20.97086 | 20.64786 | 14.97203 | 43.85685 | 15.78682 |
| 9426 |  | HIFI int. harn. 3+8 | 30.0424 | 29.44858 | 23.56522 | 63.93677 | 20.09417 |
| 9427 |  | HIFI int. harn. 3+8 | 33.78664 | 32.92893 | 29.83925 | 79.95062 | 18.32511 |
| 9428 |  | HIFI int. harn. 3+8 | 33.87711 | 32.85638 | 32.53692 | 87.18063 | 13.83891 |
| 9429 |  | HIFI int. harn. 3+8 | 41.02032 | 39.51757 | 38.62708 | 130.66008 | 94.48537 |
| 9430 |  | HIFI int. harn. 3+8 | 52.88065 | 50.54244 | 48.83094 | 202.64707 | 185.46879 |
| 9431 |  | HIFI int. harn. 3+8 | 62.94506 | 59.94499 | 57.65118 | 264.22892 | 259.03256 |
| 9441 |  | HIFI int. harn. 4+9 | 10.31136 | 10.18581 | 7.86579 | 30.71004 | 8.43943 |
| 9442 |  | HIFI int. harn. 4+9 | 10.45814 | 10.33359 | 7.87656 | 30.57728 | 8.54637 |
| 9443 |  | HIFI int. harn. 4+9 | 10.33283 | 10.20627 | 7.88731 | 30.44398 | 8.31082 |
| 9444 |  | HIFI int. harn. 4+9 | 10.13132 | 10.00214 | 7.89268 | 30.37714 | 8.01006 |
| 9445 |  | HIFI int. harn. 4+9 | 20.50759 | 20.17749 | 14.94053 | 44.00568 | 15.21203 |
| 9446 |  | HIFI int. harn. 4+9 | 29.52416 | 28.91915 | 23.54484 | 64.16342 | 19.38757 |
| 9447 |  | HIFI int. harn. 4+9 | 33.52346 | 32.65741 | 29.83953 | 80.15518 | 17.96162 |
| 9448 |  | HIFI int. harn. 4+9 | 33.89032 | 32.86812 | 32.54762 | 87.37419 | 14.06874 |
| 9449 |  | HIFI int. harn. 4+9 | 41.05755 | 39.54568 | 38.65577 | 130.89095 | 94.8359 |
| 9450 |  | HIFI int. harn. 4+9 | 52.9265 | 50.58132 | 48.87351 | 202.89579 | 185.79699 |
| 9451 |  | HIFI int. harn. 4+9 | 62.96325 | 59.96073 | 57.67001 | 264.33213 | 259.16845 |
| 9461 |  | HIFI int. harn. 5 | 13.71917 | 13.62486 | 7.86468 | 30.70326 | 12.3699 |
| 9462 |  | HIFI int. harn. 5 | 15.68759 | 15.60467 | 7.87323 | 30.55684 | 14.47547 |
| 9463 |  | HIFI int. harn. 5 | 13.74577 | 13.65076 | 7.88178 | 30.40974 | 12.29427 |
| 9464 |  | HIFI int. harn. 5 | 10.15239 | 10.02363 | 7.88605 | 30.33594 | 8.03689 |
| 9465 |  | HIFI int. harn. 5 | 53.05073 | 52.91009 | 15.05231 | 43.04812 | 50.94571 |
| 9466 |  | HIFI int. harn. 5 | 71.78174 | 71.48391 | 23.59437 | 62.58152 | 67.28133 |
| 9467 |  | HIFI int. harn. 5 | 60.03336 | 59.48646 | 29.79254 | 78.58009 | 51.55917 |
| 9468 |  | HIFI int. harn. 5 | 33.80111 | 32.79095 | 32.45292 | 85.81411 | 12.23386 |
| 9469 |  | HIFI int. harn. 5 | 41.81079 | 40.37438 | 38.4679 | 129.18661 | 93.14285 |
| 9470 |  | HIFI int. harn. 5 | 54.03992 | 51.77639 | 48.61808 | 201.22708 | 184.44995 |
| 9471 |  | HIFI int. harn. 5 | 63.59476 | 60.63207 | 57.55755 | 263.65235 | 258.68861 |
| 9481 |  | HIFI int. harn. 10 | 13.94281 | 13.85 | 7.86463 | 30.70297 | 12.61696 |
| 9482 |  | HIFI int. harn. 10 | 16.0145 | 15.93323 | 7.87308 | 30.55597 | 14.82829 |
| 9483 |  | HIFI int. harn. 10 | 13.97298 | 13.87946 | 7.88152 | 30.40828 | 12.54641 |
| 9484 |  | HIFI int. harn. 10 | 10.1606 | 10.03186 | 7.88574 | 30.33419 | 8.0454 |
| 9485 |  | HIFI int. harn. 10 | 64.63197 | 64.50897 | 15.05229 | 43.04751 | 62.79619 |
| 9486 |  | HIFI int. harn. 10 | 87.47885 | 87.21269 | 23.59453 | 62.58209 | 83.51049 |
| 9487 |  | HIFI int. harn. 10 | 70.79857 | 70.31168 | 29.79281 | 78.58146 | 63.3302 |
| 9488 |  | HIFI int. harn. 10 | 33.80997 | 32.79979 | 32.45323 | 85.81586 | 12.24243 |
| 9489 |  | HIFI int. harn. 10 | 41.89238 | 40.45749 | 38.46812 | 129.18784 | 93.19023 |
| 9490 |  | HIFI int. harn. 10 | 54.15002 | 51.88952 | 48.61819 | 201.2277 | 184.50806 |
| 9491 |  | HIFI int. harn. 10 | 63.65317 | 60.69241 | 57.55758 | 263.65253 | 258.71855 |
| 9521 |  | HIFI int. harn. res. | 10.09853 | 9.97088 | 7.86042 | 30.77601 | 8.21026 |
|  |  | PACS LABEL |  |  |  |  |  |
| 711 |  | Top Optic Housing | 3.35325 | 3.27925 | 2.55833 | 18.35252 | 7.04339 |
| 712 |  | Spectrometer Housing | 3.35298 | 3.27929 | 2.55729 | 18.30875 | 7.02506 |
| 713 |  | Collimator Housing | 3.34919 | 3.27564 | 2.55501 | 18.28407 | 7.01487 |
| 714 |  | Photometer Housing | 3.24341 | 3.17478 | 2.50249 | 17.17372 | 6.60514 |
| 721 |  | 2K Feed-Through Red D | 1.65851 | 1.63944 | 1.58492 | 2.05764 | 1.85708 |
| 722 |  | 2K Feed-Through Blue D | 1.84056 | 1.81631 | 1.65361 | 5.82226 | 2.46433 |
| 723 |  | 2K StSt I/F Blue Det. | 1.68294 | 1.66326 | 1.5931 | 2.49532 | 1.93207 |
| 731 |  | Grating Assy | 3.37129 | 3.29815 | 2.55501 | 18.28401 | 7.0271 |
| 741 |  | Red Detector * | 1.725 | 1.70322 | 1.61925 | 4.14104 | 2.15461 |
| 742 |  | Red Detector CRE | 3.36692 | 3.29393 | 2.55199 | 17.97055 | 6.99855 |
| 743 |  | CFRP-Strut Red Det. | 2.53899 | 2.49126 | 2.08827 | 13.5095 | 4.8156 |
| 744 |  | Harness Red Det. Int | 2.69719 | 2.6438 | 2.14694 | 13.3129 | 5.27767 |
| 751 |  | Blue Detector * | 1.92976 | 1.90307 | 1.68537 | 7.59815 | 2.76049 |
| 752 |  | Blue Detector CRE | 3.36776 | 3.29474 | 2.55227 | 18.00899 | 7.00119 |
| 753 |  | CFRP-Strut Blue Det. | 2.64137 | 2.59118 | 2.12133 | 14.19125 | 5.10643 |
| 754 |  | Harness Blue Det. Int | 2.76059 | 2.70607 | 2.17145 | 13.89535 | 5.4021 |
| 761 |  | Photometer Cooler Pump | 1.66712 | 1.64828 | 1.58167 | 1.89409 | 1.84096 |
| 762 |  | Photometer Cooler Evap | 1.6665 | 1.6474 | 1.58461 | 2.08941 | 1.89149 |
| 763 |  | Photometer Buffer * | 1.79766 | 1.77658 | 1.61731 | 3.76506 | 2.24055 |
| 771 |  | CFRP-Strut (OB) 1 | 7.33043 | 7.21414 | 5.52975 | 25.39512 | 7.52049 |
| 772 |  | CFRP-Strut (OB) 2 | 7.18148 | 7.07221 | 5.45036 | 23.34913 | 6.56443 |
| 773 |  | CFRP-Strut (OB) 3 | 7.33121 | 7.21479 | 5.5307 | 25.41198 | 7.53168 |
| 781 |  | Level 1,1 I/F | 3.08342 | 3.02046 | 2.40582 | 15.95617 | 6.14047 |
| 782 |  | Level 1,2 I/F | 3.2085 | 3.14228 | 2.4757 | 16.98625 | 6.4578 |
| 783 |  | Level 1,3 I/F | 3.26564 | 3.19795 | 2.51041 | 17.29353 | 6.58145 |
|  |  | SPIRE LABEL |  |  |  |  |  |
| 800 |  | L1 Strap IF1 @ SOB | 4.37841 | 4.29202 | 3.36775 | 19.98691 | 6.50062 |
| 801 |  | PH_JFET_ENCLOSURE | 11.21819 | 11.06768 | 8.42674 | 31.28367 | 8.91815 |
| 802 |  | SP_JFET_ENCLOSURE | 11.10664 | 10.9632 | 8.38956 | 29.76922 | 7.05767 |
| 803 |  | FPU_OPTICAL_BENCH | 4.57588 | 4.47553 | 3.47071 | 27.2172 | 7.69911 |
| 804 |  | RF_FILTER_BOXES | 4.62637 | 4.52653 | 3.50263 | 27.22638 | 7.70697 |
| 805 |  | BSM | 4.60013 | 4.50047 | 3.47071 | 27.21718 | 7.7118 |
| 806 |  | SMECm | 4.59418 | 4.49436 | 3.47071 | 27.2172 | 7.70866 |
| 807 |  | PH_CALIB | 4.60074 | 4.5011 | 3.47071 | 27.21717 | 7.71213 |
| 808 |  | SPEC_CALIB | 4.57588 | 4.47553 | 3.47071 | 27.2172 | 7.69912 |
| 809 |  | PH_DETECTOR_Enclosure | 1.85497 | 1.82815 | 1.69482 | 8.72635 | 2.46832 |
| 810 |  | SP_DETECTOR_Enclosure | 1.72262 | 1.7005 | 1.61931 | 5.82039 | 2.122 |
| 811 |  | L0 Enclosure Flexible S | 1.70638 | 1.68502 | 1.61061 | 4.91651 | 2.06969 |
| 812 |  | L0 Pump Flexible Strap | 1.70799 | 1.68708 | 1.58536 | 2.19175 | 1.97534 |
| 813 |  | L0 Evap Flexible Strap | 1.6592 | 1.64024 | 1.58317 | 2.02229 | 1.83427 |
| 814 |  | L0 Enclosure External S | 1.68967 | 1.6691 | 1.60167 | 3.9931 | 2.01581 |
| 815 |  | L0 Pump External Strap | 1.69474 | 1.67433 | 1.58424 | 2.10221 | 1.94614 |
| 816 |  | L0 Evaporator External | 1.65726 | 1.63835 | 1.5826 | 1.97549 | 1.82999 |
| 817 |  | COOLER_PUMP | 1.73969 | 1.71887 | 1.69596 | 7.89807 | 2.00879 |
| 818 |  | COOLER_SHUNT | 1.66496 | 1.64601 | 1.58367 | 2.0663 | 1.84145 |
| 819 |  | COOLER_EVAP | 0.29 | 0.29 | 1.70986 | 8.6867 | 0.29 |
| 820 |  | COOLER_EVAP_HS | 1.6609 | 1.6419 | 1.58362 | 2.05906 | 1.83776 |
| 821 |  | COOLER_PUMP_HS | 1.71904 | 1.69805 | 1.58624 | 2.26124 | 1.98999 |
| 822 |  | PH_DETECTORS | 0.30018 | 0.29987 | 1.70982 | 8.68733 | 0.30819 |
| 823 |  | SP DETECTORS | 0.29479 | 0.29464 | 1.70972 | 8.66588 | 0.2979 |
| 830 |  | L1 Strap IF2 @ SOB | 4.46215 | 4.37339 | 3.41494 | 20.48779 | 6.53509 |
| 831 |  | PH_L3 IF | 11.15325 | 11.00668 | 8.40308 | 30.68902 | 8.3112 |
| 832 |  | SP_L3 IF | 11.09604 | 10.95409 | 8.38584 | 29.51194 | 6.79444 |
|  |  | HIFI LABEL |  |  |  |  |  |
| 910 |  | HIFI_FPU_Main_structure | 10.09852 | 9.97087 | 7.8604 | 30.77624 | 8.21042 |
| 911 |  | Calibration_source_assem | 10.10401 | 9.97645 | 7.8604 | 30.77623 | 8.21762 |
| 912 |  | Focal_Plane_Chopper | 10.10291 | 9.97533 | 7.8604 | 30.77623 | 8.21619 |
| 913 |  | Diplexer_Rooftop_Transla | 10.09852 | 9.97087 | 7.8604 | 30.77623 | 8.21044 |
| 914 |  | Second_stage_amplifier | 10.12486 | 9.99765 | 7.8604 | 30.77623 | 8.24486 |
| 919 |  | L2-boundary | 10.09562 | 9.96802 | 7.86496 | 30.55516 | 8.13368 |
| 920 |  | Mixer_Sub_Assembly | 10.09105 | 9.96414 | 7.83784 | 30.57872 | 8.21606 |
| 921 |  | First_stage_amplifier | 10.11303 | 9.98649 | 7.83784 | 30.57871 | 8.24474 |
| 922 |  | EMC-filtering | 10.10029 | 9.97353 | 7.83784 | 30.57871 | 8.22813 |
| 925 |  | Magnet_current_dissipati | 8.14052 | 8.04487 | 6.32364 | 23.717 | 6.77211 |
| 930 |  | Console_level1_decks | 5.31428 | 5.26831 | 4.10711 | 14.01785 | 4.77601 |
| 935 |  | Magnet_current_dissipati | 4.05545 | 4.01959 | 3.19332 | 10.33276 | 3.74369 |
| 939 |  | L1_boundary | 5.29872 | 5.25317 | 4.09608 | 13.93261 | 4.76677 |
| 940 |  | Console_level0_decks | 1.75887 | 1.7376 | 1.63798 | 3.03208 | 2.06989 |
| 941 |  | Mixer_Unit | 1.76447 | 1.74328 | 1.63798 | 3.03208 | 2.07446 |
| 942 |  | Heater | 1.75887 | 1.7376 | 1.63798 | 3.03208 | 2.06989 |
| 943 |  | LO-power | 1.75971 | 1.73845 | 1.63798 | 3.03208 | 2.07058 |
| 949 |  | L0-boundary | 1.74923 | 1.72808 | 1.63291 | 2.95706 | 2.04295 |
|  |  | CCC LABEL |  |  |  |  |  |
| 4800 |  | Cryostat Cover dome | 65.00841 | 60.30404 | 58.48373 | 295 | 295 |
| 4801 |  | Cover Shield | 64.43342 | 58.91948 | 57.33485 | 251.06612 | 79.75083 |
| 4802 |  | Radiation shield 1 | 64.44063 | 58.93569 | 57.34781 | 255.20944 | 114.67927 |
| 4803 |  | Radiation shield 2 | 64.44651 | 58.94728 | 57.35674 | 264.14978 | 156.95711 |
| 4810 |  | Inlet Junction | 64.9223 | 60.09771 | 58.31234 | 288.58035 | 46.69204 |
| 4811 |  | Outlet Junction | 64.9223 | 60.09771 | 58.31234 | 288.58035 | 99.1878 |
| 4820 |  | Cover Dewar | N/A | N/A | N/A | N/A | 4.2 |
| 4821 |  | GHe cover dome inlet | N/A | N/A | N/A | N/A | 17.66359 |
| 4822 |  | GHe cover shield outlet | N/A | N/A | N/A | N/A | 76.66037 |
| 4823 |  | GHe cover dome outlet | N/A | N/A | N/A | N/A | 87.65451 |
|  |  | SVM LABEL |  |  |  |  |  |
| 6001 |  | SVM wall pZ | 318 | 291 | 265 | 293 | 293 |
| 6002 |  | SVM wall pYpZ | 318 | 291 | 265 | 293 | 293 |
| 6003 |  | SVM wall pY | 318 | 291 | 265 | 293 | 293 |
| 6004 |  | SVM wall pYmZ | 318 | 291 | 265 | 293 | 293 |
| 6005 |  | SVM wall mZ | 318 | 291 | 265 | 293 | 293 |
| 6006 |  | SVM wall mYmZ | 318 | 291 | 265 | 293 | 293 |
| 6007 |  | SVM wall mY | 318 | 291 | 265 | 293 | 293 |
| 6008 |  | SVM wall mYpZ | 318 | 291 | 265 | 293 | 293 |
| 6020 |  | SVM I/F to CVV struts | 293 | 293 | 245 | 293 | 293 |
| 6021 |  | SVM I/F to SVM shield | 293 | 266 | 240 | 293 | 293 |
| 6022 |  | SVM I/F to Sshld str. | 293 | 266 | 240 | 293 | 293 |
| 6023 |  | SVM I/F to waveguides | 293 | 266 | 240 | 293 | 293 |
| 6024 |  | SVM I/F to harness | 293 | 266 | 240 | 293 | 293 |
| 6051 |  | SVM top pZ | 230 | 203 | 168 | 293 | 293 |
| 6052 |  | SVM top pYpZ | 230 | 203 | 168 | 293 | 293 |
| 6053 |  | SVM top pY | 230 | 203 | 168 | 293 | 293 |
| 6054 |  | SVM top pYmZ | 230 | 203 | 168 | 293 | 293 |
| 6055 |  | SVM top mZ | 230 | 203 | 168 | 293 | 293 |
| 6056 |  | SVM top mYmZ | 230 | 203 | 168 | 293 | 293 |
| 6057 |  | SVM top mY | 230 | 203 | 168 | 293 | 293 |
| 6058 |  | SVM top mYpZ | 230 | 203 | 168 | 293 | 293 |
| 6101 |  | SVM top disc pZ | 230 | 203 | 168 | 293 | 293 |
| 6102 |  | SVM top disc pYpZ | 230 | 203 | 168 | 293 | 293 |
| 6103 |  | SVM top disc pY | 230 | 203 | 168 | 293 | 293 |
| 6104 |  | SVM top disc pYmZ | 230 | 203 | 168 | 293 | 293 |
| 6105 |  | SVM top disc mZ | 230 | 203 | 168 | 293 | 293 |
| 6106 |  | SVM top disc mYmZ | 230 | 203 | 168 | 293 | 293 |
| 6107 |  | SVM top disc mY | 230 | 203 | 168 | 293 | 293 |
| 6108 |  | SVM top disc mYpZ | 230 | 203 | 168 | 293 | 293 |
| 6151 |  | MLI THR pZ | 230 | 203 | 168 | 293 | 293 |
| 6152 |  | MLI THR pY | 230 | 203 | 168 | 293 | 293 |
| 6153 |  | MLI THR mZ | 230 | 203 | 168 | 293 | 293 |
| 6154 |  | MLI THR mY | 230 | 203 | 168 | 293 | 293 |
| 6155 |  | MLI SAS pZ | 230 | 203 | 168 | 293 | 293 |
| 6156 |  | MLI SAS pZ BRK | 230 | 203 | 168 | 293 | 293 |
| 6157 |  | MLI SAS mZ | 230 | 203 | 168 | 293 | 293 |
| 6158 |  | MLI SAS mZ BRK | 230 | 203 | 168 | 293 | 293 |
| 6159 |  | MLI AAD | 230 | 203 | 168 | 293 | 293 |
| 6160 |  | MLI VMC | 230 | 203 | 168 | 293 | 293 |
| 6161 |  | MLI SREM | 230 | 203 | 168 | 293 | 293 |

|  | Name | Dep./Comp. |  | Name | Dep./Comp. |
| --- | --- | --- | --- | --- | --- |
|  | Alberti von Mathias Dr. | SM 34 |  | Schmidt Rudolf | ACE 32 |
|  | Alo Hakan | OTN/LP 45 |  | Schweickert Gunn | SM 34 |
|  | Barlage Bernhard | ED 11 |  | Stauss Oliver | SM 33 |
|  | Bayer Thomas | ED 541 |  | Steininger Eric | ED 422 |
|  | Faas Horst | EA 65 |  | Stritter Rene | ED 11 |
|  | Fehringer Alexander | SM 33 |  | Suttner Klaus | SM 32 |
|  | Frey Albrecht | ED 422 |  | Tenhaeff Dieter | SM 34 |
|  | Gerner Willi | ED 11 |  | Thörmer Klaus-Horst Dr. | OTN/ED 65 |
|  | Grasl Andreas | OTN/EN 64 |  | Wagner Adalbert | OTN/LP 45 |
|  | Grasshoff Brigitte | ED 521 |  | Wagner Klaus | SM 31 |
|  | Hartmann Hans Dr. | ED 422 |  | Wietbrock, Walter | ED 521 |
|  | Hauser Armin | SM 31 |  | Wöhler Hans | SM 34 |
|  | Hinger Jürgen | SM 31 |  | Zipf Ludwig | ACE 32 |
|  | Hohn Rüdiger | ED 541 |  |  |  |
|  | Hölzle Edgar | ED 421 |  | Alcatel | ASP |
|  | Huber Johann | ED 543 |  | ESA/ESTEC | ESA |
|  | Hund Walter | SE 76 |  |  |  |
|  | Idler Siegmund | ED 432 |  | Instruments: |  |
|  | Ivády von András | ACE 32 |  | MPE (PACS) | MPE |
|  | Jahn Gerd Dr. | SM 31 |  | RAL (SPIRE) | RAL |
|  | Kalde Clemens | ED 532 |  | SRON (HIFI) | SRON |
|  | Kameter Rudolf | OTN/EN 64 |  | Subcontractors: |  |
|  | Kersting Stefan | OTN/EN 63 |  | Air Liquide, Space Department | AIR |
|  | Kettner Bernhard | SM 34 |  | Air Liquide, Space Department | AIRS |
|  | Knoblauch August | ED 531 |  | Air Liquide, Orbital System | AIRT |
|  | Koelle Markus | ED 523 |  | Alcatel Bell Space | ABSP |
|  | Kroeker Jürgen | ED 542 |  | Astrium Sub-Subsyst. & Equipment | ASSE |
|  | Kunz Oliver | SM 31 |  | Austrian Aerospace | AAE |
|  | Lamprecht Ernst | OTN/SM 222 |  | Austrian Aerospace | AAEM |
|  | Lang Jürgen | SE 76 |  | APCO Technologies S. A. | APCO |
|  | Langfermann Michael | ED 541 |  | Astrium GmbH Space Infrastr. | ASIP |
|  | Mack Paul | OTN/EN 64 |  | Bieri Engineering B. V. | BIER |
|  | Moritz Konrad Dr. | ED 65 |  | BOC Edwards | BOCE |
|  | Muhl Eckhard | OTN/EN 64 |  | Dutch Space Solar Arrays | DSSA |
|  | Pastorino Michel | ASPI Resid. |  | EADS CASA Espacio | CASA |
|  | Peitzker Helmut | ED 65 |  | EADS CASA Espacio | ECAS |
|  | Peltz Heinz-Willi | SM 33 |  | Eurocopter | ECD |
|  | Peters, Gerhard | ED 531 |  | HTS AG Zürich | HTSZ |
|  | Pietroboni Karin | ED 65 |  | Linde | LIND |
|  | Puttlitz Joachim | OTN/EN 64 |  | Patria New Technologies Oy | PANT |
|  | Rebholz Reinhold | ED 541 |  | Phoenix, Volkmarsen | PHOE |
|  | Reuß Friedhelm | ED 62 |  | Prototech AS | PROT |
|  | Rühe Wolfgang | ED 6 |  | QMC Instruments Ltd. | QMC |
|  | Runge Axel | OTN/EN 64 |  | Rembe, Brilon | REMB |
|  | Sachsse Bernt | ED 21 |  | SENER Ingenieria SA | SEN |
|  | Schäffler Johannes | OTN/EN 64 |  | Stöhr, Königsbrunn | STOE |
|  | Schink Dietmar | ED 422 |  | Rosemount Aerospace GmbH | ROSE |
|  | Schlosser Christian | OTN/EN 64 |  | RYMSA, Radiación y Microondas S.A. | RYM |

# Text boxes

Das Ändern der Daten wie Datum, Dokumententyp, Ausgabe und Dokumenten-Nummer erfolgt über die Datenvorgabe in den Properties (Eigenschaften). Vorgehensweise: File (Datei) ( Properties (Eigenschaften) und dann den Rider (Reiter) Custom (Anpassen) wählen. Dort können die Daten geändert werden. Nach der Eingabe oben auf Change (Ändern) klicken, dann wird das Dokument aktualisiert. Achtung: Dieser Text wird nicht mitgedruckt, deshalb bitte NICHT löschen!!!!!