| Assembly / Subsystem | PEM | Phone | Section | Date |
| --- | --- | --- | --- | --- |
| SPIRE | Martin Herman | (818) 354-8541 | 385 | 17 June, 2005 |
| Drawing/ Part No. | Dwg. Rev. | Nomenclature | Serial No. | Model | Type | Final IR No. | Mass (Meas. / Req.) |
| 10209750-1 | B | JFET Module | 016 | FLT-Spare | N/A | 926198 | 273.4 gm / 305 gm |
| Check applicable answer and provide explanation in remarks column | YES | NO | N A | R e m a r k s | Data Attachments | Signature & Date |
| 1. Are all drawings and specifications complete, approved, released and frozen? | X |  |  |  | 14. Latest Top Assembly drawings Attached None | Cognizant Engineer |
| 2. Do the released drawings and specifications reflect all approved changes? | X |  |  |  | 15. List of open ECRs Attached None | PEM |
| 3. Is hardware identical to other hardware delivered? If no, provide difference list. | X |  |  |  | 16. Waivers (RFW request for waiver) Attached None | QA Engineer |
| 4. Does the hardware meet its functional requirements, specifications, waivers, ICDs? | X |  |  | EIDP attached. Also see item # 8 attachments. | 17. Open MRB Attached None | Environments/Reliability |
| 5. Are all IR and MRB dispositioned and concurred by QA? | X |  |  |  | 18. Open PFR on this H/W Attached None | Mission Assurance Mgr. |
| 6. Is complete as-built list information included in the build book? | X |  |  |  | 19. Open PFR on similar H/W Attached None | Project Office |
| 7. Have all required environmental tests & analyses been completed? | X |  |  | ETAS attached | 20. Handling Document (See Item 11 Attached None | P I |
| 8. Is all required assembly and/or subsystem level functional testing complete? | X |  |  | Performance Test Data Attached. Also see EIDP in item # 4. | 21. Shortage List Attached None |  |
| 9. Have all piece parts, processes and materials been approved by JPL? | X |  |  |  | 22. Requirements Verification Matrix Attached (See #4, #7, #8) None |  |
| 10. Does this hardware meet all contamination control requirements? | X |  |  | Parts, processes and MIUL met all contamination control and out-gassing requirements. | 23. Qualification Status Attached None |  |
| 11. Are all shipping containers, shipping and special handling procedures ready? | X |  |  | See Attached Document D-26790 | 24. Mate / Demate Record Attached None |  |
| 12. Is additional work required to bring this hardware to flight (flight-spare) readiness? |  | X |  |  | 25. Operating Log Attached (See Item # 24) None |  |
| 13. Is this hardware acceptable for flight? | X |  |  |  | 26. MICD Attached None |  |

RAL EIDP Table of Contents   Versus   JPL HRCR Check List Item Numbers

| RAL EIDP Section Number | RAL EIDP Title | JPL HRCR Check List Item Number | Notes |
| --- | --- | --- | --- |
| 1 | Shipping Documents |  | Shipper and Final IR |
| 2 | Transportation, Packing, Handling & Integration Procedures | 11 | Special Handling Document D-26790 |
| 3 | Certificate of Conformance / Delivery Review Board MOM |  | HRCR book is the C of C |
| 4 | As Built Configuration Status List | 1 & 2 | Assembly Drawings |
| 5 | List of Waivers | 4 | RFW (request for waiver) Attached |
| 6 | Copies of Waivers | 4 & 7 | RFW (request for waiver) Attached |
| 7 | List of Non-Conformance Reports |  | See RFW in 4 & 7 |
| 8 | Copies of Non-Conformance Reports |  | See RFW in 4 & 7 |
| 9 | Cleanliness Statement |  | Final IR QA Inspection |
| 10 | Operational Manual |  | NA |
| 11 | Top Level Drawings (inc. Family Tree) | 14 | Top Assembly Drawing |
| 12 | Interface Drawings | 26 | MICD Drawing |
| 13 | Functional, Block & Mechanical Drawings |  | NA |
| 14 | Electrical Circuit Drawings |  | NA |
| 15 | Serialized Components List |  | In build books – not shipped |
| 16 | Mass Properties/ Power Budget | HRCR Check List Page 1 | Mass listed in HRCR check list |
| 17 | Qualification Status List / Test Matrix | 23 | Qualification Unit Test Matrix |
| 18 | Test Reports | 4, 7, 8, 23 |  |
| 19 | Open Work / Deferred Work / Open Tests |  | NA |
| 20 | Calibration Data |  | NA |
| 21 | Historical Record | 23 | Qualification Unit Test Matrix |
| 22 | Manufacturing Logbook(s) |  | In build books – not shipped |
| 23 | Operating Time / Cycle Record | 25 |  |
| 24 | Connector Mating Record | 24 |  |
| 25 | Age Sensitive Items Record |  | NA |
| 26 | Pressure Vessels – History/Test Record |  | NA |
| 27 | Temporary Installation Record |  | NA |
| 28 | Reference List of EIDPs (Lower level) |  | NA |
| 29 | Other Useful Information |  | NA |

JPL Hardware Requirements

Certification Review (HRCR)

Junction Field Effect Transistor (JFET)

Flight Module

10209750-1		S/N 016

SPIRE Element

Herschel Space Observatory Project

June 17, 2005

Configuration of Module, Boards & Membranes

| Module 10209750-1 | S/N 16 | S/N 16 |
| --- | --- | --- |
| PWB 10209760-1 | S/N 040 | S/N 045 |
| Membrane 10209758-1 | J6.16.3 | J6.17.1 |

Attachment of HRCR Items #1

Drawing Release Status

ALL ASSEMBLY & PARTS DRAWINGS ARE RELEASED IN PDMS

Released Drawings:

10209719-1	assembly built per released Rev. A drawing (studlock)

10209722-1	assembly built per released Rev. B drawing (interface drawing)

10209750-1	assembly built per released Rev. B drawing (module assy)

10209751-1	assembly built per released Rev. B drawing (chassis 1)

10209752-1	assembly built per released Rev. A drawing (chassis 2)

10209753-1	assembly built per released Rev. A drawing (chassis 3)

10209754-1	assembly built per released Rev. C drawing (mount)

10209756-1	assembly built per released Rev. B drawing (chassis lid)

10209757-1	assembly built per released Rev. A drawing (membrane)

10209758-1	assembly built per released Rev. A drawing (membrane assy)

10209759-1,-2,-4     redlined Rev. B drawing (gasket)

10209760-1	assembly built per released Rev. C drawing (board assembly)

10209761-1	assembly built per released Rev. C drawing (solder connector)

10209769-1	assembly built per released Rev. A drawing (stiffener)

10209777-1	assembly built per released Rev. B drawing (board)

10209858-2	assembly built per released Rev. A drawing (special fastener)

10217636-1	assembly built per released Rev. A drawing (clip)

Attachment of HRCR Item #4: EIDP (End Item Data Package)

Attachment of HRCR Item #7:  RFW (Request For Waiver)

Attachment of HRCR Item #7:  ETAS (Environmental Test Summary)

Attachment of HRCR Item #7:  ETAS (Environmental Test Summary)

Attachment of HRCR Item #7:  ETAS (Environmental Test Summary)

Attachment of HRCR Item # 8: Test Data - Source Voltage Data

Attachment of HRCR Item # 8: Noise Test Data

Attachment of HRCR Item # 8: Test Data - Source Voltage & Noise

Attachment of HRCR Item # 9: SPIRE MIUL Cover Page

MIUL = Material Identification & Utilization List

Declared Materials List's and Processes List are not included in this HRCR

Attachment of HRCR Item # 11:

See End of This HRCR Package for

“JFET Module Handling Document”

Attachment of HRCR Item # 14: JFET Module Top Assembly Drawing 10209750-1

Attachment of HRCR Item # 23:  Qualification Compliance Test

Attachment of HRCR Item # 24 & #25:  Mate/Demate & Operation Logs

Attachment of HRCR Item # 24 & #25:  Mate/Demate & Operation Logs (continued)

Attachment of HRCR Items # 24 & # 25:  Mate/Demate & Operation Logs

Attachment of HRCR Item # 26:  MICD -  JFET Interface Drawing 10209722 (p 1 of 2)

Attachment of HRCR Item # 26:  MICD -  JFET Interface Drawing 10209722 (p 2 of 2)

Attachment of HRCR Item # 11:

JFET Module

Handling Document D-26790

Field Effect Transistor (JFET) Module 10209750-1

Prepared by: Kalyani Sukhatme		10 September, 2003

Revised by:  Roger Welker & Steve Tseng	15 June, 2005

D-26790

1. Introduction

This document provides guidelines for electrical handling for the SPIRE JFET Module.

1.1 Hardware Description

Each JFET module has two sets of 24 JFET channels. The JFET channels are populated on 1.0 micron thick Silicon Nitride membranes which provides thermal isolation. The operating temperature for these JFETs is ~120 K. The process of powering up the JFETs dissipates heat into the membrane resulting in a temperature increase with respect to the base temperature (4K to 10 K). Higher the power dissipation, higher is the temperature of the JFETs.

Each JFET channel consists of a matched pair of FETs (Figure 1.1-1) with a requirement for the offset voltage of less than 15 mV between the matched pair. [The characteristic offset voltage is the difference between the source voltages (Vsa and Vsb with respect to ground) of the two FETs.]

Figure 1.1-1

The Gates of the JFETs are the ‘Inputs’ of the circuit and the Sources (Vsa and Vsb) of the JFETs are the outputs, as marked in Figure 1.1-1. Vdd and Vss are the power lines for the circuit.

# 2. Handling

- The JFET Module is Contamination Sensitive:  Open shipment suitcase in an ISO 14644 Class 7 (FED-STD-209 Class 10,000) or cleaner cleanroom.  Handle hardware with approved nitrile or polyurethane ESD safe cleanroom gloves.

D-26790

- The JFET Module is ESD Sensitive:

Please handle with appropriate ESD hardware handling procedures.  Handle with grounding straps, ESD-safe gloves, ESD smocks at an ESD-safe workstation.

ESD:  Handle with approved wrist straps, ESD-safe gloves and ESD smocks at an approved ESD protected workstation. All personnel within 1 meter of unprotected ESD sensitive hardware shall be certified for ESD awareness.  Maintain shorting plugs on the unit at all times, except when the unit is installed in the final assembly of the SPIRE instrument.  JFET modules are shipped with two shorting plugs for ESD protection.   Refer to attached electrical handling document for other important safety precautions. Follow all instructions for the use of wrist straps, ESD smocks, static protected work areas, ionizers, packing/unpacking and cable handling per JPL standard D-1348, rev. F (This document is available through the public domain by the following URL: http://acquisition.jpl.nasa.gov/rfp/miri/dewar/DL-2671-584331/JPL_D-1348.pdf).

ESD - Ionizer: Prior to mate or demate of any connector, turn on an ionizer approved for ESD sensitive components in clean room environment at least 5 minutes in advance and place/hold both sides of the connections in front of the ionized air stream for a minimum of 10 seconds before mating/demating operation. Position the ionizer near the hardware within the required distance per manufacturer’s manual. Different makes and models of ionizers have different positioning requirements. During the mating/demating operations, it is necessary to follow the requirements for handling ESD sensitive hardware.

ESD - Connection to GSE: It is essential to ensure that all signal and bias lines of the GSE are grounded prior to mating the JFET hardware to the GSE.  A save-to-mate check must be performed prior to connecting the JFET to the GSE.  No excessive voltages and currents on all signal and bias lines shall be observed while the hardware is connected.

QA Oversight:  Quality Assurance personnel should witness all handling, electrical testing, operation and integration of JFET flight hardware.  At a minimum, a "two person" rule should be invoked at all times, where oversight by an independent party is provided to ensure hardware safety during handling, test and integration operations.

Humidity Sensitive: Place hardware in a humidity controlled ISO 14644 Class 7 (FED-STD 209 Class 10,000) cleanroom.  Maintain humidity level at 35%-50% RH typical, for ESD safety.

- The JFET Module is Fragile:  Please do not drop or otherwise shock the unit including the shipping suitcase and container.  Do not remove the cover of the JFET Module.

D-26790

# 3. Power ON Procedure

- The JFET Module should be powered on WITH the shorting plugs (JPL Supplied Protection connectors) in place and with the inputs shorted to ground. Pins #9 and #15 on the 15-pin MDM connectors on the JFET Module are the bias grounds on the module. These pins should also be shorted to the power supply ground. The unit may be powered up without the shorting plug only when the inputs are connected to the detector system.

Under no circumstances the unit should be powered up without the inputs shorted to ground either via the shorting plug (JPL Supplied) or via the detector system.

- Do not exceed a voltage of +5 V for the Vdd line and –5 V for the Vss line of the JFET Module.

- When removing the shorting plugs from the unit for installation into the instrument, please use standard ESD precautions including grounding straps, ESD-safe gloves, ESD smocks at an ESD-safe workstation.

# 4. Electrical Check-out Test: Characteristic Offset Voltage Measurement

- Verify that the gates of the JFET channels (Inputs) are shorted together and grounded.

- Apply the power supply ground to the bias ground pins on the unit (Pins 9 and 15 on the 15-pin MDM connectors)

- Power on the JFET modules with Vdd = +3 V and Vss = -1.5 V

- Verify that the handheld multimeter is in calibration.

- Connect one side of the handheld multimeter to ground (Power supply ground).

- And measure the voltage with respect to ground of each side (Vsa and Vsb) of each channel.

- Calculate the characteristic offset voltage (Voffset) for each channel (Voffset= Vsa-Vsb)

- Compare the values for each of the channels with the specific datasheet provided with the unit.

The datasheets accompanying the unit also provides the values for the drain and source currents for a similar test performed at JPL.

REFER TO MEASURED SOURCE VOLTAGE DATA FOR ACTUAL HARDWARE.  Here is an example of the source voltage values and the drain and the source currents obtained for such a test at room temperature are given in the Table 4-1

| T, JFET | rm T |
| --- | --- |
| Vdd | 3 V |
| Vss | -1.5 V |
| Idd | 1.564 mA |
| Iss | 1.5686 mA |
| Channel # | (V) | DELTA (V) |
| 1 | 1.130 | 0 |
|  | 1.130 |  |
| 2 | 1.075 | 0.001 |
|  | 1.074 |  |
| 3 | 0.781 | 0.001 |
|  | 0.780 |  |
| 4 | 1.088 | 0.005 |
|  | 1.093 |  |
| 5 | 0.834 | 0.001 |
|  | 0.833 |  |
| 6 | 1.012 | 0.003 |
|  | 1.015 |  |
| 7 | 0.785 | 0.002 |
|  | 0.787 |  |
| 8 | 1.148 | 0.004 |
|  | 1.144 |  |
| 9 | 0.753 | 0 |
|  | 0.753 |  |
| 10 | 0.693 | 0.008 |
|  | 0.701 |  |
| 11 | 1.110 | 0.004 |
|  | 1.114 |  |
| 12 | 0.758 | 0.001 |
|  | 0.759 |  |
| 13 | 0.832 | 0.002 |
|  | 0.830 |  |
| 14 | 1.264 | 0.001 |
|  | 1.265 |  |
| 15 | 1.206 | 0 |
|  | 1.206 |  |
| 16 | 0.818 | 0.001 |
|  | 0.819 |  |
| 17 | 0.526 | 0.005 |
|  | 0.521 |  |
| 18 | 1.423 | 0 |
|  | 1.423 |  |
| 19 | 0.773 | 0.002 |
|  | 0.775 |  |
| 20 | 0.873 | 0.004 |
|  | 0.877 |  |
| 21 | 1.387 | 0.006 |
|  | 1.393 |  |
| 22 | 1.417 | 0.003 |
|  | 1.420 |  |
| 23 | 0.887 | 0.002 |
|  | 0.889 |  |
| 24 | 0.888 | 0.003 |
|  | 0.891 |  |

-   END OF    -

Attachment of HRCR Item # 11:

“JFET Module Handling Document D-26790”

END OF

HRCR PACKAGE

# Footnotes

JPL approved ESD safe cleanroom gloves are:

Nitrile:

Ansell-Edmont Nitrilite		http://www.ansellpro.com/ce/products3.asp?pid=87

Ansell-Edmont Nitrilite Silky	http://www.ansellpro.com/ce/products3.asp?pid=149

Ansell-Edmont Silky Ultra-Clean	http://www.ansellpro.com/ce/products3.asp?pid=150

Safeskin Critical (white)		http://www.safeskin.com/crit_nt_glv.asp

Polyurethane:

Wilshire Technology DuraCLEAN	call in US, 323-259-6469 for ordering information

JPL approved wrist straps are:

Speidel Twist-o-Flex ™ brand metal expansion bracelet wrist straps

3M model 4600 adjustable molded thermoplastic wrist straps

All work areas shall be certified and operated in compliance with the requirements of the following subsections sections of JPL-STD D-1348 rev. F section 2.3: subsections: 6, 8-11, 14-19, 21, 23 – 27, 29 – 36, 38 – 43 and 45.

All personnel shall be trained and certified to the requirements of section 2.3.3 of JPL STD_D-1348 rev. F.

The ionizer performance shall be verified to comply with the requirements of JPL-STD-D-1348 rev. F, Table 1 for devices with human body model ESD sensitivity less than 50 volts. The ionizer shall discharge from ± 1000 volts to less than ± 20 volts in less than 20 seconds and have a float potential of less than ± 20 volts.

# Text boxes

Rss

Inputa

Vdd

Vss

Outputa

Rd

Inputb

Outputb

(Vsa)

(Vsb)