| Assembly / Subsystem | PEM | Phone | Section | Date |
| --- | --- | --- | --- | --- |
| SPIRE | Martin Herman | (818) 354-8541 | 386 | 3 February, 2005 |
| Drawing/ Part No. | Dwg. Rev. | Nomenclature | Serial No. | Model | Type | Final IR No. | Mass (Meas. / Req.) |
| 10209750-1 | B | JFET Module | 015 | FLIGHT | N/A | 923847 | 276.9 gm / 305 gm |
| Check applicable answer and provide explanation in remarks column | YES | NO | N A | R e m a r k s | Data Attachments | Signature & Date |
| 1. Are all drawings and specifications complete, approved, released and frozen? | X |  |  |  | 14. Latest Top Assembly drawings Attached None | Cognizant Engineer |
| 2. Do the released drawings and specifications reflect all approved changes? | X |  |  |  | 15. List of open ECRs Attached None | PEM |
| 3. Is hardware identical to other hardware delivered? If no, provide difference list. | X |  |  |  | 16. Waivers (RFW request for waiver) Attached None | QA Engineer |
| 4. Does the hardware meet its functional requirements, specifications, waivers, ICDs? | X |  |  | EIDP attached. Also see item # 8 attachments. | 17. Open MRB Attached None | Environments/Reliability |
| 5. Are all IR and MRB dispositioned and concurred by QA? | X |  |  |  | 18. Open PFR on this H/W Attached None | Mission Assurance Mgr. |
| 6. Is complete as-built list information included in the build book? | X |  |  |  | 19. Open PFR on similar H/W Attached None | Project Office |
| 7. Have all required environmental tests & analyses been completed? | X |  |  | ETAS attached | 20. Handling Document (See Item 11 Attached None | P I |
| 8. Is all required assembly and/or subsystem level functional testing complete? | X |  |  | Performance Test Data Attached. Also see EIDP in item # 4. | 21. Shortage List Attached None |  |
| 9. Have all piece parts, processes and materials been approved by JPL? | X |  |  |  | 22. Requirements Verification Matrix Attached (See #4, #7, #8) None |  |
| 10. Does this hardware meet all contamination control requirements? | X |  |  | Parts, processes and MIUL met all contamination control and out-gassing requirements. | 23. Qualification Status Attached None |  |
| 11. Are all shipping containers, shipping and special handling procedures ready? | X |  |  | See Attached Document D-26790 | 24. Mate / Demate Record Attached None |  |
| 12. Is additional work required to bring this hardware to flight readiness? |  | X |  |  | 25. Operating Log Attached (See Item # 24) None |  |
| 13. Is this hardware acceptable for flight? | X |  |  |  | 26. MICD Attached None |  |

RAL EIDP Table of Contents   Versus   JPL HRCR Check List Item Numbers

| RAL EIDP Section Number | RAL EIDP Title | JPL HRCR Check List Item Number | Notes |
| --- | --- | --- | --- |
| 1 | Shipping Documents |  | Shipper and Final IR |
| 2 | Transportation, Packing, Handling & Integration Procedures | 11 | Special Handling Document D-26790 |
| 3 | Certificate of Conformance / Delivery Review Board MOM |  | HRCR book is the C of C |
| 4 | As Built Configuration Status List | 1 & 2 | Assembly Drawings |
| 5 | List of Waivers | 4 | RFW (request for waiver) Attached |
| 6 | Copies of Waivers | 4 & 7 | RFW (request for waiver) Attached |
| 7 | List of Non-Conformance Reports |  | See RFW in 4 & 7 |
| 8 | Copies of Non-Conformance Reports |  | See RFW in 4 & 7 |
| 9 | Cleanliness Statement |  | Final IR QA Inspection |
| 10 | Operational Manual |  | NA |
| 11 | Top Level Drawings (inc. Family Tree) | 14 | Top Assembly Drawing |
| 12 | Interface Drawings | 26 | MICD Drawing |
| 13 | Functional, Block & Mechanical Drawings |  | NA |
| 14 | Electrical Circuit Drawings |  | NA |
| 15 | Serialized Components List |  | In build books – not shipped |
| 16 | Mass Properties/ Power Budget | HRCR Check List Page 1 | Mass listed in HRCR check list |
| 17 | Qualification Status List / Test Matrix | 23 | Qualification Unit Test Matrix |
| 18 | Test Reports | 4, 7, 8, 23 |  |
| 19 | Open Work / Deferred Work / Open Tests |  | NA |
| 20 | Calibration Data |  | NA |
| 21 | Historical Record | 23 | Qualification Unit Test Matrix |
| 22 | Manufacturing Logbook(s) |  | In build books – not shipped |
| 23 | Operating Time / Cycle Record | 25 |  |
| 24 | Connector Mating Record | 24 |  |
| 25 | Age Sensitive Items Record |  | NA |
| 26 | Pressure Vessels – History/Test Record |  | NA |
| 27 | Temporary Installation Record |  | NA |
| 28 | Reference List of EIDPs (Lower level) |  | NA |
| 29 | Other Useful Information |  | NA |

JPL Hardware Requirements

Certification Review (HRCR)

Junction Field Effect Transistor (JFET)

Flight Module

10209750-1		S/N 015

SPIRE Element

Herschel Space Observatory Project

February 3, 2005

Configuration of Module, Boards & Membranes

| Module 10209750-1 | S/N 15 | S/N 15 |
| --- | --- | --- |
| PWB 10209760-1 | S/N 34 | S/N 35 |
| Membrane 10209758-1 | J6.4.1 | J6.4.4 |

Attachment of HRCR Items #1

Drawing Release Status

ALL ASSEMBLY & PARTS DRAWINGS ARE RELEASED IN PDMS

Released Drawings:

10209719-1	assembly built per released Rev. A drawing (studlock)

10209722-1	assembly built per released Rev. B drawing (interface drawing)

10209750-1	assembly built per released Rev. B drawing (module assy)

10209751-1	assembly built per released Rev. B drawing (chassis 1)

10209752-1	assembly built per released Rev. A drawing (chassis 2)

10209753-1	assembly built per released Rev. A drawing (chassis 3)

10209754-1	assembly built per released Rev. C drawing (mount)

10209756-1	assembly built per released Rev. B drawing (chassis lid)

10209757-1	assembly built per released Rev. A drawing (membrane)

10209758-1	assembly built per released Rev. A drawing (membrane assy)

10209759-1,-2,-4     redlined Rev. B drawing (gasket)

10209760-1	assembly built per released Rev. C drawing (board assembly)

10209761-1	assembly built per released Rev. C drawing (solder connector)

10209769-1	assembly built per released Rev. A drawing (stiffener)

10209777-1	assembly built per released Rev. B drawing (board)

10209858-2	assembly built per released Rev. A drawing (special fastener)

10217636-1	assembly built per released Rev. A drawing (clip)

Attachment of HRCR Item #4: EIDP

Attachment of HRCR Item # 4:  RFW (request for waiver)

| RFW/RFD Number: | HR-SP-JPL-RFW-016 |
| --- | --- |
| Spacecraft / Project | Herschel | Originator’s Name | Steve Tseng |
| System / Experiment / Model | SPIRE | Signature / Date |  |
| Sub-System | detectors | Request Type (Highlight applicable request) | Waiver (RFW) | Deviation (RFD) |
| Assembly | JFET modules | Organisation | Jet Propulsion Laboratory |
| Sub-Assembly |  | Ref. Doc. / Drwg No. | SPIRE-JPL-PRJ-000456 |
| Item |  | References |  |
| Serial No. |  |  |  |
| RFW/RFD Title | JFET Power Dissipation s/n 015 |
| End Items(s) Affected (Hardware, Software) |
| Name | CI-Number | Model(s) |
| JFET Module p/n 10209750 s/n 012 |  | PFM |
| Requirement / Interface Documents Affected |
| Specification/Drawing Title | Number | Issue | Date | App. Paragraph |
| BDA-SSSD | SPIRE-JPL-PRJ-0004456 | 3.2 | 7/1/03 | JFET-PER-01 JFET-PER-02 JFET-TEC-05 |
| Description of Deviation / Discrepancy / Non-Conformance |
| Requirement states that dissipation of photometer JFETs is to be less than 7 mW average, while supplying 90% of channels with voltage noise < 15 nV/rtHz according to BDA-SSSD JFET-PER-01, JFET-PER-02, JFET-TEC-05. Measured JFET performance of the JFETs indicates that 9.14 mW of power dissipation will be required to meet the specified yield and noise performance specifications. |
| Other Items or Requirements (Potentially) Affected |
| Overall sensitivity of the bolometer sub-system is affected by JFET noise performance. JFET power dissipation impacts the heat sink temperature of the 3He refrigerator and may in turn increase the base detector temperature. Dissipation of JFETs affects power dissipation on cryostat. |
| Need for RFW/RFD and Rationale for Acceptance |
| Measured JFET performance of JFETs indicates that 10.30 mW of power dissipation will be required to meet the specified yield and noise performance specifications. JPL is unable to significantly alter the JFET fabrication process in order to meet the power specification without undue risk to the stated PFM/FS delivery dates. Furthermore, JPL requests a full system optimisation to revisit the noise and power requirements on the JFETs. The JFET modules can meet the noise design value with 100 % yield at higher dissipation. |
|  | Approved | Rejected | Name | Date |
| Engineering: |  |  |  |  |
| Product Assurance: |  |  |  |  |
| CCB-Chairman: |  |  |  |  |
| Principal Investigator |  |  |  |  |
| Product Assurance: |  |  |  |  |
| Co-Investigator |  |  |  |  |
| Prime Contractor |  |  |  |  |
| ESA Project Office |  |  |  |  |

Attachment of HRCR Item #7:  RFW (request for waiver)

| RFW/RFD Number: | HR-SP-JPL-RFW-005 |
| --- | --- |
| Spacecraft / Project | Herschel | Originator’s Name | Kalyani Sukhatme |
| System / Experiment / Model | SPIRE | Signature / Date |  |
| Sub-System | detectors | Request Type (Highlight applicable request) | Waiver (RFW) | Deviation (RFD) |
| Assembly |  | Organisation | Jet Propulsion Laboratory |
| Sub-Assembly |  | Ref. Doc. / Drwg No. | SPIRE-JPL-PRJ-000456 |
| Item |  | References |  |
| Serial No. |  |  |  |
| RFW/RFD Title | BDA and JFET module sine test deletion |
| End Items(s) Affected (Hardware, Software) |
| Name | CI-Number | Model(s) |
| Bolometric Detector Assemblies JFET Modules |  | CQM, PFM, FS CQM, PFM, FS |
| Requirement / Interface Documents Affected |
| Specification/Drawing Title | Number | Issue | Date | App. Paragraph |
| BDA-SSSD (SPIRE-JPL-PRJ-000456) |  | 3.2 | Jan 7, 2003 | BDA-DES-10, JFET-DES-07 |
| Description of Deviation / Discrepancy / Non-Conformance |
| High Level Sine- Vibe Test is not performed on these units |
| Other Items or Requirements (Potentially) Affected |
| Need for RFW/RFD and Rationale for Acceptance |
| The hardware has to be qualified under a cold vibration test and is installed in the cold vibration facility for the purpose of the test. The high level sine vibration test configuration will put the hardware and the personnel at risk since the cold vibration facility is not structurally capable of withstanding the high levels. Obtaining additional resources (cost and schedule) for developing a new set-up is not feasible at this time. |
|  | Approved | Rejected | Name | Date |
| JPL Engineering: |  |  |  |  |
| JPL Product Assurance: |  |  |  |  |
| CCB-Chairman: |  |  |  |  |
| Principal Investigator |  |  |  |  |
| Product Assurance: |  |  |  |  |
| Co-Investigator |  |  |  |  |
| Prime Contractor |  |  |  |  |
| ESA Project Office |  |  |  |  |

Attachment of HRCR Item #7:  ETAS (environmental test summary)

Attachment of HRCR Item #7:  ETAS (environmental test summary)

Attachment of HRCR Item #7:  ETAS (environmental test summary)

Attachment of HRCR Item # 8: Test Data - Source Voltage & Noise

For Module 15

Attachment of HRCR Item # 8: Test Data - Source Voltage & Noise

Board S/N 034 in Module S/N 015

Attachment of HRCR Item # 8: Test Data - Source Voltage & Noise

Board S/N 035 in Module S/N 015

Attachment of HRCR Item # 9: SPIRE MIUL Cover Page

MIUL = Material Identification & Utilization List

Attachment of HRCR Item # 11:

See End of This HRCR Package for

“JFET Module Handling Document”

Attachment of HRCR Item # 14: JFET Module Top Assembly Drawing 10209750-1

Attachment of HRCR Item # 23:  Qualification Compliance Test

Attachment of HRCR Item # 24 & #25:  Mate/Demate & Operation Logs

Attachment of HRCR Item # 24 & #25:  Mate/Demate & Operation Logs (continued)

Attachment of HRCR Items # 24 & # 25:  Mate/Demate & Operation Logs (PWB S/N 034)

Attachment of HRCR Items # 24 & # 25:  Mate/Demate & Operation Logs (PWB S/N 035)

Attachment of HRCR Item # 26:  MICD -  JFET Interface Drawing 10209722 (p 1 of 2)

Attachment of HRCR Item # 26:  MICD -  JFET Interface Drawing 10209722 (p 2 of 2)

Attachment of HRCR Item # 11:

SPIRE

Handling Document

Field Effect Transistor (JFET) Module

10209750-1

Prepared by: Kalyani Sukhatme

10 September, 2003

Hardware Handling Guidelines

Contamination: Open shipment suitcase in a FED-STD-209 Class 10,000 clean room (ISO 14644-1 class 7) or better.  Handle hardware with gloves.

ESD:  Handle with grounding straps, ESD-safe gloves and ESD smocks at an ESD-safe workstation.  Maintain shorting plugs on the unit whenever ESD is a concern.  Refer to attached electrical handling document for other important safety precautions.

Fragile: Do not drop or otherwise shock the hardware including the shipping suitcase and container.

Humidity Sensitive: Place hardware in a humidity controlled Class 10,000 clean room.  Maintain humidity level at 35%-50% RH typical, for ESD safety.

SPIRE JFET Electrical Handling Document

1	Introduction	1

1.1	Hardware Description	1

2	Handling	2

3	Power ON Procedure	2

4	Electrical Check-out Test: Characteristic Offset Voltage Measurement	3

1. Introduction

This document provides guidelines for electrical handling for the SPIRE JFET Module.

1.1 Hardware Description

Each JFET module has two sets of 24 JFET channels. The JFET channels are populated on 1.0 micron thick Silicon Nitride membranes which provides thermal isolation. The operating temperature for these JFETs is ~120 K. The process of powering up the JFETs dissipates heat into the membrane resulting in a temperature increase with respect to the base temperature (4K to 10 K). Higher the power dissipation, higher is the temperature of the JFETs.

Each JFET channel consists of a matched pair of FETs (Figure 1.1-1) with a requirement for the offset voltage of less than 15 mV between the matched pair. [The characteristic offset voltage is the difference between the source voltages (Vsa and Vsb with respect to ground) of the two FETs.]

Figure 1.1-1

The Gates of the JFETs are the ‘Inputs’ of the circuit and the Sources (Vsa and Vsb) of the JFETs are the outputs, as marked in Figure 1.1-1. Vdd and Vss are the power lines for the circuit.

# Handling

- The JFET Module is Contamination Sensitive:  Handle the unit with Gloves only in a FED-STD-209 Class 100000 clean room (ISO 14644-1 class 7) or better.

- The JFET Module is ESD Sensitive: Please handle with appropriate ESD hardware handling procedures.  Handle with grounding straps, ESD-safe gloves, ESD smocks at an ESD-safe workstation.

- The JFET Module is Fragile:  Please do not drop or otherwise shock the unit. Please DO NOT remove the cover of the JFET Module.

# Power ON Procedure

- The JFET Module should be powered on WITH the shorting plugs (JPL Supplied Protection connectors) in place and with the inputs shorted to ground. Pins #9 and #15 on the 15-pin MDM connectors on the JFET Module are the bias grounds on the module. These pins should also be shorted to the power supply ground. The unit may be powered up without the shorting plug only when the inputs are connected to the detector system.

Under no circumstances the unit should be powered up without the inputs shorted to ground either via the shorting plug (JPL Supplied) or via the detector system.

- Do not exceed a voltage of +5 V for the Vdd line and –5 V for the Vss line of the JFET Module.

- When removing the shorting plugs from the unit for installation into the instrument, please use standard ESD precautions including grounding straps, ESD-safe gloves, ESD smocks at an ESD-safe workstation.

# Electrical Check-out Test: Characteristic Offset Voltage Measurement

- Verify that the gates of the JFET channels (Inputs) are shorted together and grounded.

- Apply the power supply ground to the bias ground pins on the unit (Pins 9 and 15 on the 15-pin MDM connectors)

- Power on the JFET modules with Vdd = +3 V and Vss = -1.5 V

- Verify that the handheld multimeter is in calibration.

- Connect one side of the handheld multimeter to ground (Power supply ground).

- And measure the voltage with respect to ground of each side (Vsa and Vsb) of each channel.

- Calculate the characteristic offset voltage (Voffset) for each channel (Voffset= Vsa-Vsb)

- Compare the values for each of the channels with the specific datasheet provided with the unit.

The datasheets accompanying the unit also provides the values for the drain and source currents for a similar test performed at JPL.

REFER TO MEASURED SOURCE VOLTAGE DATA FOR ACTUAL HARDWARE.  Here is an example of the source voltage values and the drain and the source currents obtained for such a test at room temperature are given in the Table 4-1

| T, JFET | rm T |
| --- | --- |
| Vdd | 3 V |
| Vss | -1.5 V |
| Idd | 1.564 mA |
| Iss | 1.5686 mA |
| Channel # | (V) | DELTA (V) |
| 1 | 1.130 | 0 |
|  | 1.130 |  |
| 2 | 1.075 | 0.001 |
|  | 1.074 |  |
| 3 | 0.781 | 0.001 |
|  | 0.780 |  |
| 4 | 1.088 | 0.005 |
|  | 1.093 |  |
| 5 | 0.834 | 0.001 |
|  | 0.833 |  |
| 6 | 1.012 | 0.003 |
|  | 1.015 |  |
| 7 | 0.785 | 0.002 |
|  | 0.787 |  |
| 8 | 1.148 | 0.004 |
|  | 1.144 |  |
| 9 | 0.753 | 0 |
|  | 0.753 |  |
| 10 | 0.693 | 0.008 |
|  | 0.701 |  |
| 11 | 1.110 | 0.004 |
|  | 1.114 |  |
| 12 | 0.758 | 0.001 |
|  | 0.759 |  |
| 13 | 0.832 | 0.002 |
|  | 0.830 |  |
| 14 | 1.264 | 0.001 |
|  | 1.265 |  |
| 15 | 1.206 | 0 |
|  | 1.206 |  |
| 16 | 0.818 | 0.001 |
|  | 0.819 |  |
| 17 | 0.526 | 0.005 |
|  | 0.521 |  |
| 18 | 1.423 | 0 |
|  | 1.423 |  |
| 19 | 0.773 | 0.002 |
|  | 0.775 |  |
| 20 | 0.873 | 0.004 |
|  | 0.877 |  |
| 21 | 1.387 | 0.006 |
|  | 1.393 |  |
| 22 | 1.417 | 0.003 |
|  | 1.420 |  |
| 23 | 0.887 | 0.002 |
|  | 0.889 |  |
| 24 | 0.888 | 0.003 |
|  | 0.891 |  |

-   END OF    -

Attachment of HRCR Item # 11:

JFET Module Handling Document

END OF

HRCR PACKAGE

# Text boxes

(Vsb)

(Vsa)

Outputb

Inputb

Rd

Outputa

Vss

Vdd

Inputa

Rss