HERSCHEL/PACS

SPU High Level SoftWare

Specification Document

Document Ref.: PACS-TW-GS-001

Issue: 4.8

Distribution Record

| Issue / Revision | Draft 0 | Draft 1 | Draft 2 | 1.0 | 1.1 | 1.2 | 1.3 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Distribution Date | 16.07.2000 | 29.08.2000 | 16.03.2001 | 22.05.2001 | 02.09.2001 | 15.11.2001 | 29.01.2002 |
| Issue / Revision | 1.4 | 2.0 | 2.1 | 2.2 | 3.0 | 4.0 | 4.1 |
| Distribution Date | 08.04.2002 | 06.08.2002 | 12.09.2002 | 17.02.2003 | 10.03.2003 | 23.09.2003 | 13.10.2003 |
| Issue / Revision | 4.2 | 4.3 | 4.4 | 4.5 | 4.6 | 4.7 | 4.8 |
| Distribution Date | 27.02.2004 | 30.03.2004 | 13.04.2006 | 04.09.2006 | 05.11.2007 | 01.07.2008 | 18.02.2009 |

| INTERNAL | EXTERNAL |
| --- | --- |
| Department | Name | Qty | Company | Name | Qty |
| UVIE/ASTRO | F. Kerschbaum | 1 | MPE | H. Feuchtgruber, O. Bauer, E. Wieprecht, A. Contursi, T. Müller, G. Wildgruber | 1 |
|  |  |  | CSL | J.M. Gillis, A. Mazy | 1 |
|  |  |  | IAC | J.M. Herreros, P. Gomez | 1 |
|  |  |  | IFSI | R. Orfei, S. Pezzuto | 1 |
|  |  |  | MPE | PACS Project Office (pacs@mpe.mpg.de) PACS Warm Electronic (pacs-we@ster.kuleuven.ac.be) | 1 |
|  |  | Electronic Archives at Leuven http://pacs.ster.kuleuven.ac.be | 1 |

Document Change Records

| Document Title HERSCHEL – PACS SPU High Level Software Document |
| --- |
| Issue | Date | Reason for Change |
| Draft 0 | 15/07/2000 | Initial Issue |
| Draft 1 | 22/08/2000 | Comments from MPE |
| Draft 2 | 16/03/2001 | Comments from Consortia and OBS#4, document structure update |
| 1.0 | 16/05/2001 | Comments from the SPU HLSW Meeting #1 |
| 1.1 | 02/09/2001 | Comments from OBS#5 |
| 1.2 | 28/10/2001 | Inclusion of the HLSW Design |
| 1.3 | 29/01/2002 | Update taking into account new version of the documents |
| 1.4 | 08/04/2002 | Include the SW Tables structure |
| 2.0 | 05/08/2002 | Comments from IBDR, reorganized |
| 2.1 | 11/09/2002 | Comments from SPU HLSW Version 1 AVM Delivery |
| 2.2 | 17/02/2003 | New Perform Activity (RCS) added, description of expected TM Rates for all Compression Modes in Phot./Spec. added, CEH size changed to 28 Bytes, detailed Label description inserted, parameters RCXNB and RCX in DET_CST_SPEC/DET_CST_PHOT tables deleted. Triple and Quadruple Compression Modes in photometry and spectroscopy are removed because Default and Double Compression Mode fulfil the TM requirements. Further integration may be performed on ground if required Lossless Coding Only Compression Mode in photometry and spectroscopy is removed. This mode is already covered by The Lossless Compression Mode. SPU Test Compression Mode in photometry and spectroscopy is removed. This mode is already covered by The Default Compression Mode + Raw Channel, and by the SPU Internal Test Mode (where data are generated inside the SPU). |
| 3.0 | 10/03/2003 | Updated for SPU HLSW Version 3.0 |
| 4.0 | 23/09/2003 | Updated for SPU HLSW Version 6.0 Include two new DPU commands: “Copy data from RAM to EEPROM” and “Connect to DEC/MEC”. Update the logical model (Watch Process and Command Interpretation and Acknowledgment) by including the two new commands Include a description of SPU HLSW SMCS handling in Section 5.1. Include a list of HLSW HK parameters and update the HK rate in Section 5.5 Compression SW Scheme updated (Figure 16) Raw Channel data compression included (Appendix A.1.3 and Section 5.9.1) Updated description for ramp fitting in Spectroscopy (Section 5.9.4 and Appendix B.2.2.7) where several slopes can derived out of a ramp. Update the Section 6 “Feasibility and Resource Estimates”, and delete the decompression SW description from this Section Update Section 7 and 8 “Traceability Matrices” Include a CRISA document as reference document “RD015” Update the tables for the Write command in Section 5.7.11 |
| 4.1 | 13/10/2003 | Include software specifications for lossless compression ode (Section3.4.3.1.4) Update the traceability matrices according to the added scpecifications above (Section78) Update Section 5.9.6 according to the specifications above |
| 4.2 | 27/02/2004 | Include a parameter for the Half Compression Mode in Photometry (20Hz readout rate) Modify the DIFS field in Compressed entity Header by REAL (reduction algorithm) used on-board. Include two parameters for the Write command in spectroscopy (Reduction algorithm to use, the use of glitch or not) Update the appendixes for the used algorithms in HLSW version 8. Include the description of new data sorting algorithm in Appendix (Reorder) Include in Appendix the description of subramp fitting Update the TM rate calculated for Buffer transmission mode after increasing the transmission rate (SPU-DPU) in photometry and after including the TM packet header |
| 4.3 | 26/03/2004 | Include SW requirements SPU-HSR-FN0202 and SPU-HSR-FN0203 Update the HK Table parameters Section 5.5. Update Fill_InputBuffer Section 5.6 including the functions used for mrmory scrubbing. Updated Section 5.8.5 for Buffer Transmission Mode in Photometry Noise resampling algorithm is implemented in the peak-up module. Update the the Peak-up description Section 5.13. Update the traceability matices in Section7 and 8 include the new software requirements |
| 4.4 | 13/04/2006 | Include SW requirements (for FDIR) SPU-HSR-SA0010, SPU-HSR-SA0011 and SPU-HSR-SA0012 Update the traceability matix in 8 include the new software requirements Include Section 9 Software Requirements vs. Software Verification & Validation Traceability Matrix Implementation of the reworked CASE Tool diagrams in Section 2.2. Update llc.c component description (Section 5.9.7) Update Section A.1 of currently implemented algorithms for the lossless compression Update Section A.2 of library of available algorithms for the lossless compression Update Section B.2 of library of available algorithms for the fitting algorithms |
| 4.5 | 01/09/2006 | Update and include SW requirements according to CAPTEC code review comments (see 588-200b_SPU_SSD_Comments.xls) Update Section 9 (Software Requirements vs. Software Verification & Validation Traceability Matrix) Update Sections according to CAPTEC code review comments (see 588-200b_SPU_SSD_Comments.xls) |
| 4.6 | 05/11/2007 | Adaption of requirements to HLSW version 13.8 Apply new naming conventions from the “cleaned version” (e.g. bol1_2 ( bol_ex, …) Add new algorithms in Section A.1: RZIP2 Add new algorithms in Section A.2: RZIP2, Data Resorting (Reorder), FM Arithmetic Compression and VBWL_short Add new Section B.2.4: Averaging and Rounding in Photometry |
| 4.7 | 01/07/2008 | Added Compressed Sensing mode short description (table 4) Added Section “FM Averaging” in appendix B |
| 4.8 | 18/02/2009 | Added appendix B.3: Decimation |

Contents

1	Introduction	16

1.1	Purpose of the document	16

1.2	Definitions, Acronyms and Abbreviations	16

1.3	References	20

1.3.1	Applicable Documents	20

1.3.2	Reference Documents	20

1.4	Overview of the document	21

2	Model Description	22

2.1	General	22

2.1.1	The Signal Processing Unit (SPU)	23

2.1.2	The SPU High Level Software (HLSW)	25

2.2	Logical Model	26

3	Specific Requirements	35

3.1	Functional Requirements	35

3.1.1	The Watch Process	35

3.1.2	Application Software	39

3.1.3	HK Module	40

3.2	Performance Requirements	41

3.3	Interface Requirements	41

3.3.1	DPU Commands	41

3.3.1.1	LOAD Command	41

3.3.1.2	DUMP Command	42

3.3.1.3	CHECK Command	42

3.3.1.4	RESET Command	42

3.3.1.5	RAW_CHAN_TRAN_MODE Command	43

3.3.1.6	STOP_REDUCT_COMPR Command	43

3.3.1.7	START_REDUCT_COMPR Command	43

3.3.1.8	ACT_TEST_PHOT Command	43

3.3.1.9	ACT_TEST_SPEC	43

3.3.1.10	ACT_BOL_BGND_CANCEL Command	44

3.3.1.11	Write Commands	44

3.3.1.12	CP_DATA_RAM_EEPROM Command	44

3.3.1.13	CONNECT_DMC Command	44

3.3.2	The Compressed Entity	45

3.3.3	DEC/MEC to SPU Interface	45

3.4	Operational Requirements	46

3.4.1	DEC/MEC Header Usage	46

3.4.1.1	Spectroscopy	46

3.4.1.2	Photometry	51

3.4.2	Instrument Configuration	55

3.4.2.1	Instrument Operating Modes	55

3.4.2.2	Instrument Observing Modes	55

3.4.3	SPU HLSW Compression Modes	56

3.4.3.1	Compressed Data Transmission Mode	56

3.4.3.1.1	Default Compression Mode	57

3.4.3.1.2	Double Compression Mode	57

3.4.3.1.3	Half-Compression Mode (Photometry only)	57

3.4.3.1.4	Lossless Compression Mode	57

3.4.3.2	SPU Test Mode	58

3.4.3.3	Transparent Mode	58

3.4.3.4	Buffer Transmission Mode	58

3.4.3.5	Compression Mode for 4s Reset (Spectroscopy only)	58

3.5	Resource Requirements	59

3.6	Verification Requirements	59

3.7	Acceptance Testing Requirements	60

3.8	Documentation Requirements	60

3.9	Portability Requirements	60

3.10	Quality Requirements	61

3.11	Reliability Requirements	61

3.12	Maintainability Requirements	62

3.13	Safety Requirements	63

4	System Design	64

4.1	Design Method	64

4.2	Decomposition Description	64

4.2.1	The Watch Process and Command Interpretation and Acknowledgement	64

4.2.2	The Application SW	66

4.2.2.1	Supervisor	66

4.2.2.2	Compression Software	67

4.2.2.2.1	HLSW Compression Modes	68

4.2.2.2.2	Summary of Compression Modes	69

4.2.3	The HK Module	71

5	Component and Functional Description	72

5.1	Main Task	73

5.2	Watch Process	77

5.3	Supervisor	80

5.4	Data Transmission	89

5.5	Housekeeping	92

5.6	Fill_InputBuffer	94

5.7	Command Interpretation and Acknowledgement	96

5.7.1	LOAD Command	96

5.7.2	DUMP Command	98

5.7.3	CHECK Command	100

5.7.4	Perform Activity Command	102

5.7.5	CP_DATA_RAM_EEPROM Command	105

5.7.6	RESET Command	107

5.7.7	RAW_CHAN_TRAN_MODE Command	109

5.7.8	START/STOP_REDUCT_COMPR Command	111

5.7.9	ACT_TEST_PHOT/SPEC Command	113

5.7.10	CONNECT_DMC Command	115

5.7.11	Write Command	117

5.8	Compression Software	120

5.8.1	Compression Software Main Task	120

5.8.2	Photometry Modes 0, 1 and 2	123

5.8.3	Photometry Mode 3	125

5.8.4	Photometry Mode 4	127

5.8.5	Photometry Buffer Transmission Mode	129

5.8.6	Spectroscopy Modes 1 and 2	132

5.8.7	Spectroscopy Mode 3	134

5.8.8	Spectroscopy Mode 4	136

5.8.9	Spectroscopy Buffer Transmission Mode	137

5.9	Compression SW Modules	139

5.9.1	Detector Selection	139

5.9.2	Preprocessing	141

5.9.3	Robust Averaging	143

5.9.4	Ramp Fitting	145

5.9.5	Integration (obsolete)	148

5.9.6	Temporal and Spatial Redundancy Reduction	150

5.9.7	Lossless Coding	153

5.9.8	Header Compression	155

5.9.9	Fill_OutputBuffer	157

5.10	Supervisor for Test Mode	160

5.11	Photometry Data Generator	165

5.12	Spectroscopy Data Generator	167

6	Feasibility and Resource Estimates	169

6.1	Memory Allocation	169

6.2	Processing Power	170

6.3	Application SW Estimates	170

6.3.1	Compression Ratio	170

6.3.2	Entropy Estimates for Redundancy Reduction	171

6.4	Data Rates Estimate	172

6.4.1	Photometry	173

6.4.2	Spectroscopy	175

7	User Requirements vs. Software Traceability Matrix	177

8	Software Requirements vs. Components Traceability Matrix	179

9	Software Requirements vs. Software Verification & Validation Traceability Matrix	185

Appendices	191

A.1 Currently implemented Algorithms	193

A.1.1 Lossless DEC/MEC Header Compression	193

A.1.2 Lossless Science Data Compression	193

A.1.3 Raw Channel Data Compression	194

A.2. Library of LLC Algorithms	195

A.2.1 List of Available Algorithms	195

A.2.2 Dynamic and Static Temporal Redundancy Reduction (D_S_TRR)	195

A.2.3 Simple Zero Repetition Suppression (ZRS)	196

A.2.4 RZIP/RZIP2	196

A.2.5 Arithmetic Coding (ARC)	198

A.2.6 Data Resorting (Reorder)	199

A.2.7 PACS Codec (new_srt)	200

A.2.8 FM Arithmetic Compression	200

A.2.9 VBWL	201

B.1 Currently implemented Algorithms	203

B.1.1 Robust Averaging in Photometry	203

B.1.2 Ramp-Fitting in Spectroscopy	203

B.2 Library of Fitting Algorithms	204

B.2.1 List of Available Algorithms	204

B.2.2 Robust Averaging in Photometry	205

B.2.2.1 Glitch Detection and Rejection	205

B.2.2.1.1 Sample Deviation Detection Method	205

B.2.2.2 Averaging	206

B.2.2.2.1 FM Averaging	206

B.2.2.2.2 Mean Value Calculation	206

B.2.3 Ramp-Fitting in Spectroscopy	207

B.2.3.1 Glitch Detection and Rejection	207

B.2.3.1.1 Crossed Slope Deviation Detection	207

B.2.3.2 Ramp-Fitting	208

B.2.3.2.1 Least Squares Fitting	208

B.2.3.2.4 Two-Sample-Fit	211

B.2.3.2.5 Slope Deviation Detection Method	212

B.2.3.2.6 Two-Samples Difference Method	215

B.2.3.2.7 Subramp Fitting	216

B.2.4 Averaging and Rounding in Photometry	217

B.3 Decimation	2037

B.3.1 Decimation in Photometry	20417

B.3.2 Decimation in Spectroscopy	20417

Index of Figures

Figure 1. PACS Instrument Block Diagram	22

Figure 2. Communication Links between SPU and other Subsystems	24

Figure 3. SPU HLSW Architecture	26

Figure 4. WP_and_CIA Module	27

Figure 5. Watch Process Module	28

Figure 6. ASW Module	29

Figure 7. CSW Module	30

Figure 8. Components of Spectroscopy Mode 1 (Spec1) Module	31

Figure 10. Components of Spectroscopy Mode 3 (Spec3) Module	32

Figure 11. Components of Spectroscopy Mode 4 (Spec4) and Photometry Mode 4 (Bol4) Module	32

Figure 12. Buffer Transmission Mode in Spectroscopy (BUF_Spec) and Photometry (BUF_Bol)	33

Figure 13. Components of Photometry Mode (Bol_ex) Module	33

Figure 15. Components of Photometry Mode 3 (Bol3) Module	34

Figure 18. Flowchart of the Supervisor Algorithm	67

Figure 19. Compression SW Scheme.	70

Figure 20. Flowchart of the Main Taks.	75

Figure 21. Flowchart of the Watch Process Task	78

Figure 22. Detector array for the Spectroscopy.	80

Figure 23. Configuration of the (a) SWL-Detector Arrays and of the (b) LWL-Detector Arrays.	81

Figure 24. Resulting DMC packet structure for Spectroscopy.	81

Figure 25. Resulting DMC packet structure for (a) SWL-Photometry and for (b) LWL-Photometry.	82

Figure 26. Flowchart of the Supervisor Task (Part 1)	85

Figure 27. Flowchart of the Supervisor Task (Part 2)	85

Figure 28. Flowchart of the Supervisor Task (Part 3)	85

Figure 29. Flowchart of the Data Transmission Task.	90

Figure 30. Flowchart of the Housekeeping Task	93

Figure 31. Flowchart of the Fill_InputBuffer Procedure	95

Figure 32. Flowchart of the Procedure for Load Command Handling	97

Figure 33. Flowchart of the Procedure for Dump Command Handling	99

Figure 34. Flowchart of the Procedure for Check Command Handling	101

Figure 35. Flowchart of the Procedure for the Perform Activity Command Handling	103

Figure 36. Flowchart of the Procedure for Copy Data from RAM to EEPROM Command Handling	106

Figure 37. Flowchart of the Procedure for Warm Reset Command Handling	108

Figure 38. Flowchart of the Procedure for Raw Channel Selection Command Handling	110

Figure 39. Flowchart of the Procedure for the Start and Stop Commands Handling	112

Figure 40. Flowchart of theProcedure for SPU Test Command Handling	114

Figure 41. Flowchart of the Procedure for Connect to DEC/MEC Command Handling	116

Figure 42. Flowchart of the Procedure for Write Command Handling	119

Figure 43. Flowchart of the Compression Software Main Task (Part 1)	121

Figure 44. Flowchart of the Compression Software Main Task (Part 2)	122

Figure 45. Flowchart of the Bol_ex Procedure	124

Figure 46. Flowchart of the Bol3 Procedure	126

Figure 47. Flowchart of the Bol4 Procedure	128

Figure 48. Flowchart of the BUF_Bol Procedure	130

Figure 49. Flowchart of the Spec1_2 Procedure	133

Figure 50. Flowchart of the Spec3 Procedure	135

Figure 51. Flowchart of the Spec4 Procedure	136

Figure 52. Flowchart of the BUF_Spec Procedure	138

Figure 53. Flowchart of the Detector Selection Procedure	140

Figure 54. Flowchart of the Preprocessing Procedure	142

Figure 55. Flowchart of the Robust Averaging Procedure	144

Figure 56. Flowchart of the Ramp-fitting Procedure	146

Figure 57. Flowchart of the Integration Procedure	149

Figure 58. Flowchart of the Temporal and Spatial Redundancy Reduction Procedure for Spectroscopy	151

Figure 59. Flowchart of the Temporal and Spatial Redundancy Reduction Procedure for Photometry	152

Figure 60. Flowchart of the Lossless Compression Procedure	154

Figure 61. Flowchart of the DEC/MEC Header Compression Procedure	156

Figure 62. Splitting of the Compressed Entity and the Resulting Science Data Blocks	157

Figure 63. Flowchart of the Fill_OutputBuffer Procedure	158

Figure 64. Flowchart of the Supervisor for Test Mode Task (Part 1)	161

Figure 65. Flowchart of the Supervisor for Test Mode Task (Part 2)	161

Figure 66. Flowchart of the Supervisor for Test Mode Task (Part 3)	161

Figure 67. Flowchart of the Supervisor for Test Mode Task (Part 4)	164

Figure 68. Flowchart of the Photometry Data Generator Task	166

Figure 69. Flowchart of the Spectroscopy Data Generator Task	168

Figure 70. SPU HLSW Memory Map.	169

Figure 71. Redundancy Reduction.	171

Figure 72. Scheme of the PACS Codec algorithm.	200

Figure 73. Example showing the sample deviation detection method	205

Figure 77. Example showing the crossed slope deviation detection	207

Figure 78. Least Square Fitting (1)	208

Figure 79. Least Square Fitting (2)	208

Figure 83. Example showing the ramp-fitting method (fit and residuals)	211

Figure 84 Example showing the slope deviation detection method	212

Figure 85. Photoconductor Readouts from 1 Channel with Additive Noise	213

Figure 86. Successive Slopes in the Ramp	213

Figure 87. Successive Slope Deviations in the Ramp	214

Figure 88. Example showing the Two-Samples Difference Method	215

Figure 89. Illustration of Sub-ramp Fitting	216

Index of Tables

Table 1. PACS Instrument Operating Modes	55

Table 2.  PACS Instrument Observing Modes	56

Table 3, Acceptance Test	60

Table 4. Photometric and Spectroscopic compression modes	69

Table 5. Software Files of the SPU HLSW	72

Table 7. List of Compression Parameters for Photometry and Spectroscopy	83

Table 12. Memory Allocation of the SPU HLSW.	169

Table 13. Number of Bits Allocated to the Noise.	172

Table 14. Expected Data Rates for the Compression Modes in Photometry	172

Table 15. Expected Data Rates for the Compression Modes in Spectroscopy	173

Table 16. Nominal Data Rates for Photometry.	174

Table 17. Nominal Data Rates for Spectroscopy.	175

Table 18. List of available LLC algorithms.	195

Table 19. Keys for RZIP Combinationss	197

Table 20. The Basic Arithmetic Coding Process	198

Table 21. List of available fitting algorithms.	204

# Introduction

## Purpose of the document

The purpose of this document is to describe the software specifications of the SPU HLSW developed by UVIE/TUVIE according to the ESA Software Engineering Standards described in RD001, which includes the Software Requirement Definition Phase (SR), Architectural Design Phase (AD) and the Software Design Phase (SD). These specifications include the SW concept, design, requirements and library of data reduction algorithms.

The SPU HLSW consists mainly of the ASW (Reduction/Compression), the watch process (it acts upon DPU commands) and communication protocols with other sub-units. The rest of the SPU development, which consists of HW-LLSW, is part of the IAC responsibility and out of the scope of this document.

## Definitions, Acronyms and Abbreviations

| Acronyms and Abbreviations | Description |
| --- | --- |
| ADSP | Analog device DSP |
| AID | Activity ID |
| AOCS | Attitude and Orbit Control Subsystem |
| ASW | Application SoftWare |
| AVM | AVionics Model |
| BOL | BOLometers |
| CDMS | Command and Data Management System |
| CPU | Central Processing Unit |
| CQM | Cryogenic Qualification Model |
| CRE | Cold Readout Electronics |
| CSL CVS | Centre Spatial de Liège Concurrent Versions System |
| DDR | Detailed Design Review |
| DEC/MEC | Detector Controller/Mechanisms Controller |
| DMC | DEC/MEC |
| DMCH | DEC/MEC Header |
| DPU | Digital Processing Unit |
| DRCU | Detector Readout and Control Unit |
| DSP | Digital Signal Processor |
| EDAC | Error Detection And Correction |
| EEPROM | Electrically Erasable Programmable Read Only Memory |
| FCU | FPU Control Unit |
| FIRST | Far Infrared and Sub-millimetre Telescope |
| FPU | Focal Plane Unit |
| FS | Flight Spare (Model) |
| HIFI | Heterodyne Instrument for HERSCHEL (HiFi instrument) |
| HK | House-Keeping |
| HLSW | High Level SW |
| HS | High Speed |
| HSO | Herschel Space Observatory |
| HW | HardWare |
| I/F | Interface |
| IAC | Instituto de Astrofísica de Canarias |
| ID | Identification |
| IFSI | Istituto di Fisica dello Spazio Interplanetario |
| LLSW | Low Level SW |
| LSB | Least Significant Byte |
| LWL | Long WaveLength |
| MFCU | Mechanisms and Focal plane electronics Control Unit |
| MSB | Most Significant Byte |
| OBCP | On-Board Control Procedure |
| OBS | On-Board Software |
| PACS | Photo-detector Array Camera and Spectrometer |
| PFM | Proto-Flight Model |
| PHC | PhotoConductors |
| PMA | Program Memory Address |
| PMD | Program Memory Data |
| PRIP | Pattern Recognition and Image Processing |
| PROM | Programmable Read Only Memory |
| RAM | Random Access Memory |
| ROM | Read Only Memory |
| SAU | Smallest Addressable Unit |
| SCR | Software Change Request |
| SDE | Software Development Environment |
| SEU | Single Error Upsets |
| SID | Structure ID |
| SPIRE | Spectral and Photometric Imaging Receiver |
| SPR | Software Problem Report |
| SPU | Signal Processing Unit |
| SW | SoftWare |
| SWL | Short WaveLength |
| TBC | To Be Confirmed |
| TBD | To Be Defined |
| TBU | To Be Updated |
| TBW | To Be Written |
| TC | TeleCommand |
| TM | TeleMetry |
| TUVIE | Technical UVIE |
| UR | User Requirement |
| URD | User Requirements Document |
| UVIE | University of Vienna |
| WE | Warm Electronics |
| Definition | Description |
| BBID | Building Block Identification |
| BSID | Bolometer Setup Identification |
| CDH | Compressed DEC/MEC Header |
| CDHS | Compressed DEC/MEC Header Size |
| CEH | Compressed Entity Header |
| CI | Counter Increments |
| CMM | Compression Mode |
| CPR | Chopper Position Readback |
| CR | Compression Ratio achieved |
| CRCRMP | Current Readout Count in a RaMP |
| CRDC | Current ReaDout Count |
| CRDCCP | Current ReaDout Count in Chopper Position |
| CRECR | CRE Control Readback |
| CSD | Compressed Science Data |
| CSW | Compression SoftWare |
| DBID | Data Block ID |
| DECID | DEcompression Code IDentification |
| DXS ID | Detectors Selection table IDentification |
| GPR | Grating Position Readback |
| HK | HouseKeeping |
| LBL | Label |
| MEM_STATUS_CNTS | MEMory STATUS CouNTerS |
| NACK | Negative Acknowledgement |
| OBSID | Observation Identification |
| PACK | Positive Acknowledgement |
| PIX | Packet Index |
| RCS | Raw Channel Selection |
| RCX | Raw Channel IndeX |
| REAL | REduction ALgorithm |
| ROSP | Readout Specifications in Photometry |
| ROSS | Readout Specifications in Spectroscopy |
| RRR | Readouts in Ramp Readback |
| SCIS | compressed SCIence data Size |
| SPR | Spare |
| SPUID | SPU ID |
| TMP | Timing Parameters |
| VID | Version ID |
| VLD | Validity |
| WPR | Wheel Position Readback |

To identify all software requirements they are structured as follows:

ID-type.number

Where

ID	System identification (SPU-OBS for On Board Software User Requirements or SPU-HSR for HLSW Requirements)

type	type of the requirement

… for ID = SPU-HSR:

FN	Functional

IF	Interface

OP	Operational

RS	Resource

VF	Verification

AT	Acceptance Testing

DO	Documentation

SA	Safety

QA	Quality

… for ID = SPU-OBS:

ON	Switch On

OF	Switch Off

SW	Software

CR	Communication

TM	Telemetry

number	serial number of the requirement

## References

### Applicable Documents

| AD001 AD002 AD003 AD004 AD005 AD006 AD007 | PT-PACS-02126 SCI-PT-ICD-7527 PACS-ME-ID-001 PACS-ME-SP-001 ESA-TM-06 PACS-ME-RS-005 IFSI/OBS/PL/2000-001 | FIRST/PLANCK Instrument Interface Document - Part B – Instrument PACS Packet Structure Interface Control Document PACS Instrument Interface Requirement Document The Photoconductor Array Camera & Spectrometer (PACS) for the Far InfraRed and Submillimetre Telescope (FIRST) Handbook of Data Compression Algorithms PACS Instrument Requirement Document DPU/ICU On Board Software Product Assurance Plan |
| --- | --- | --- |

### Reference Documents

| RD001 RD002 RD003 RD004 RD005 RD006 RD007 RD008 RD009 RD010 RD011 RD012 RD013 RD014 RD015 RD016 RD017 RD018 RD019 RD020 | BSSC(96)2 PACS-ME-PL-006 SCI-PT-IIDA-04624 PACS-ME-PL-005 DIPSAPII-DAS-31-06 PACS-TW-SR-001 PACS-TW-ID-001 PACS-IC-RD-001 PACS-CL-ID-004 FPL-IC-1214-01-CRS FPL-IC-1214-04-CRS FPL-TN-1214-03-CRS Analog Devices Com. ACM 24 Jun. 1981 FPL-SDD-1214-01-CRS PACS-TW-HM-002 PACS-TW-TS-004 Proc. of SPIE Vol. 5487 (2004), Part 1, p. 481 PACS-CR-UM-024 PACS-TW-TN-014 | Guide to applying the ESA software engineering standards to small software projects PACS Project Configuration Management Plan FIRST/PLANCK Instrument Interface Document IID - Part A - Operating Modes of the PACS Instrument SMCS332 User Manual Issue2 PACS SPU HLSW User Requirement Document PACS SPU HLSW to DPU Interface Description PACS SPU Start-Up SW and LLSW Drivers URD DEC/MEC to SPU Interface Description PACS SPU HW-SW Interface Control Document PACS SPU LLSW drivers SW ICD Planck/Herschel PACS SPU Technical Description (17. July 2001, issue 2) ADSP-21020 User’s Manual. Second Edition, USA 1995 Random sample consensus: A paradigm for model fitting with applications to image analysis and automated cartography HERSHEL PACS Start up and LLSW Drivers SDD (issue 1) PACS SPU HLSW User Manual PACS SPU HLSW Acceptance Test Plan for FM Delivery “Herschel/PACS On-noard Reduction/Compression Software Implementation” (by R. Ottensamer et al.) DPU OBS User Manual The flightdata file from the compression point of view |
| --- | --- | --- |

## Overview of the document

This document is structured as follows:

- Section 1, an introduction and an outline of this document is given.

- Section 2 contains the logical model description of the SPU High Level Software.

- In Section 3, the SW requirements are listed.

- Section 4, a detailed description of the SPU HLSW design is given.

- Section 5 contains details about the SW components and their functions.

- Section 6 includes the summarisation of the computer resources required to build, operate and maintain the software.

- Section 7 contains the User Requirements vs. Software Traceability Matrix

- Section 8 includes the Software Requirements vs. Components Traceability Matrix and

- Section 9 displays the Software Requirements vs. Software Verification & Validation Traceability Matrix

# Model Description

## General

The Herschel Space Observatory is the fourth cornerstone mission of the European Space Agency (ESA) `Horizon 2000' science plan. It will be implemented together with the Planck mission as a single project. It is defined as a multi-user “observatory type” mission with the goal to open up the wavelength range ( 60-600 (m to photometry and spectroscopy with unprecedented sensitivity and spatial resolution, unobscured by the Earth's atmosphere. The Herschel space observatory will be launched in 2008 to operate at a distance of 1.5 million km far from the earth. The scientific topics of the mission include the formation and evolution of galaxies in the early universe, the search for protostars in our own Galaxy, and the evolution of planetary systems including the Solar System.

Figure 1. PACS Instrument Block Diagram

A payload complement of three instruments is housed inside a super fluid helium cryostat of the Telescope: “HIFI”, “SPIRE” and “PACS”. Three consortia develop them. Many of the involved processes are known to emit most of their luminosity in the far-infrared and sub-millimetre band, both as continuum radiation from dust and as spectral line features. The shortest wavelength band, 60-210 (m, will be covered by the Photoconductor Array Camera & Spectrometer (PACS), which will provide both photometric and spectroscopic observing modes suited to address the key scientific topics of the HERSCHEL mission. The electrical, thermal and configuration aspect of the PACS instrument is given in Figure 1. As shown in this diagram, the instrument contains several sub-units, which are developed by different institutions in a consortium led by MPE, Garching, Germany.

DEC/MEC, SPU, and DPU represent PACS warm electronic sub-units. CSL, IAC/UVIE and IFSI respectively have the task to develop these modules. They are responsible for data handling and processing according to ground instructions.

### The Signal Processing Unit (SPU)

The main function of the Signal Processing Unit (SPU) of the PACS instrument consists of the data reduction and compression for transmission purpose. This task is achieved by the ASW and related programs, implemented on the DSPs. Furthermore, the SPU has to control the communication functionality with DEC/MEC and DPU. Figure 2 represents the communication links between the SPU unit, DEC/MEC and DPU. Transmission of science data from DEC/MEC is ensured by two IEEE 1355/spacewire data links. Two links also lie between SPU and DPU. They will allow the transmission of compressed data, HLSW HK and DPU/SPU commands/responses. The SPU development consists of two main parts: SPU HW+LLSW and SPU HLSW. We only consider the HLSW in this document.

Figure 2. Communication Links between SPU and other Subsystems

The SPU unit consists of two CPU boards, which work independently. They are called SWL SPU and LWL SPU. The HLSW will be identically implemented in each SPU sub-unit (SWL and LWL). As both CPUs have equivalent functionality, we only focus on the HLSW description of one board. The SPU contains two data inputs:

- Science data + header from DEC/MEC

- Commands from DPU

and three data outputs:

- Compressed data to DPU

- HK to DPU

- Command response to DPU

The HLSW operates with these inputs to provide the required output data. The overall DEC/MEC raw data description can be found in the specific document RD009.

### The SPU High Level Software (HLSW)

The detector readouts are collected by the DEC/MEC and put into packets. A header is attached to each packet including the data type, the observation configuration and the compression parameters. Then data packets and headers are sent to SPU. The science data are reduced and compressed by the SPU HLSW regarding the DEC/MEC header information. The DEC/MEC header parameters will also be compressed and packaged with the compressed science data and will be sent to the DPU. The HK parameters, which consist either of data reduction-compression results of the HLSW whenever raw data are received from DEC/MEC or the SPU status while no observation is performed, will also be sent to DPU. The compression mode, which represents the way the reduction and compression should be done, is read from the DEC/MEC header. It defines the way the compression should be done.

The HLSW deals with the instrument configuration through the DEC/MEC header information as specified in Section 3.4.2. The PACS instrument configuration consists of the instrument operating and observing modes described in the document RD004.

- Instrument Operating Modes: They represent the basic activities carried out within the PACS instrument.

- Instrument Observing Modes: They represent the kind of imaging performed by the PACS instrument. The data stream, size, and behaviour will depend on the mode used.

## Logical Model

The SPU HLSW is developed according to ESA engineering software standards described in RD001. The definition of the functions and procedures to establish the software assurance for the SPU HLSW is written in AD007 (approved Product Assurance Plan from DPU SW). The software design methodology is the Yourdon-deMarco structured analysis method with the Hatley-Phirbai real-time extensions.

The interaction between the HLSW, SUSW and LLSW as well as the handover to the SPU HLSW is given in RD015. The general layout of the SPU HLSW is represented in Figure 3.

Figure 3. SPU HLSW Architecture

The WP_and_CIA (Watch Process and Command Interpretation and Acknowledgment) module is depicted in Figure 4.

Figure 4. WP_and_CIA Module

The Watch Process module is illustrated in Figure 5.

Figure 5. Watch Process Module

The components of the ASW (Application Software) module are shown in Figure 6.

Figure 6. ASW Module

The CSW (Compression Software) concept is given in Figure 7.

Figure 7. CSW Module

The modules for all HLSW compression modes for Spectroscopy (Spec1 to Spec5 and BUF_Spec) and for Photometry (Bol1 to Bol4 and BUF_Bol) are represented in Figure 8 to .

Figure 8. Components of Spectroscopy Mode 1 (Spec1) Module

Figure 9. Components of Spectroscopy Mode 3 (Spec3) Module

Figure 10. Components of Spectroscopy Mode 4 (Spec4) and Photometry Mode 4 (Bol4) Module

Figure 11. Buffer Transmission Mode in Spectroscopy (BUF_Spec) and Photometry (BUF_Bol)

Figure 12. Components of Photometry Mode (Bol_ex) Module

Figure 13. Components of Photometry Mode 3 (Bol3) Module

# Specific Requirements

## Functional Requirements

### The Watch Process

SPU-HSR-FN0001

If the Watch Process detects a received DPU command, it shall read it.

SPU-HSR-FN0002

The Watch Process shall check whether the received DPU command is Load, Dump, Check, Perform, Write or Invalid command by use of reference table.

SPU-HSR-FN0003

The Watch Process shall abort data compression for any received command.

SPU-HSR-FN0004

If the received command is a Load command, attached data shall be checked (via checksum calculation) and written into memory if checksum is right. If the checksum is wrong a NACK will be signalled.

SPU-HSR-FN0005

The correctness of the Load shall be verified by checking (via checksum calculation) the data written into memory. If the checksum is wrong a NACK will be signalled.

SPU-HSR-FN0007

If the received command is a Dump command, the required length of data is read from memory. A checksum over the read data is calculated and attached to the dumped data.

SPU-HSR-FN0009

If the received command is a Check command, the required length of memory is checked via the checksum calculation

SPU-HSR-FN0010

Program RAM, Data RAM, Extended Data RAM and Dual Port RAM can be checked by HLSW. The HLSW does not check the EEPROM and the PROM.

SPU-HSR-FN0011

If the received command is a Perform command, the validity of the attached activity shall be checked using a reference table.

SPU-HSR-FN0012

If Warm Reset command is received, HLSW shall clean the data buffers (Input Data buffer, Processing buffer, Compressed DMC Header buffer and RC data buffer), reset the counters (CI and PIX) to zero and reset the connection to DPU and DEC/MEC (reset SMCS chip).

SPU-HSR-FN0013

If Raw Channel Selection command is received, HLSW shall upgrade the Raw Channel Selection table with the attached parameters. The default value of Raw Channel Selection components at HLSW start-up is zero (no selected channel and default channel index is zero).

SPU-HSR-FN0014

If Stop command is received, Watch Process shall signal the abortion of the data compression. If there is no data compression when a Stop command is received no action will be performed.

SPU-HSR-FN0015

If Start command is received, Watch Process shall signal the begin of the data compression. If Start command is received when data compression is ongoing the data compression will be aborted (compound of Stop-Start command).

SPU-HSR-FN0016

If SW Test command for photometry is received, Watch Process shall disable the DEC/MEC link interrupt, enables the internal data generation through Phot_gn and then signal the begin of data compression.

SPU-HSR-FN0017

If SW Test command for spectroscopy is received, Watch Process shall disable the DEC/MEC link interrupt, enables the internal data generation through Spec_gn and then signal the begin of data compression.

SPU-HSR-FN0020

If the received command is a Write command, the validity of the attached parameters shall be checked using a reference table. The write command only checks for valid Parameter ID, valid length and valid checksum, but never checks the content of the attached data. If the checksum is wrong a NACK will be signalled.

SPU-HSR-FN0021

If the received command is a Write DXS1 (Blue Bolometer sub-array1) command, attached data shall be checked (via checksum calculation). If checksum is correct, HLSW shall upgrade the Table DXS1 with the attached data. If the checksum is wrong a NACK will be signalled.

SPU-HSR-FN0022

If the received command is a Write DXS2 (Blue Bolometer sub-array2) command, attached data shall be checked (via checksum calculation). If checksum is correct, HLSW shall upgrade the Table DXS2 with the attached data. If the checksum is wrong a NACK will be signalled.

SPU-HSR-FN0023

If the received command is a Write DXS3 (Blue Bolometer sub-array3) command, attached data shall be checked (via checksum calculation). If checksum is correct, HLSW shall upgrade the Table DXS3 with the attached data. If the checksum is wrong a NACK will be signalled.

SPU-HSR-FN0024

If the received command is a Write DXS4 (Blue Bolometer sub-array4) command, attached data shall be checked (via checksum calculation). If checksum is correct, HLSW shall upgrade the Table DXS4 with the attached data. If the checksum is wrong a NACK will be signalled.

SPU-HSR-FN0025

If the received command is a Write DXS5 (Red Bolometer) command, attached data shall be checked (via checksum calculation). If checksum is correct, HLSW shall upgrade the Table DXS5 with the attached data. If the checksum is wrong a NACK will be signalled.

SPU-HSR-FN0026

If the received command is a Write DXS6 (Photoconductor main array “Blue array for Blue SPU or Red Array for Red SPU”) command, attached data shall be checked (via checksum calculation). If checksum is correct, HLSW shall upgrade the Table DXS6 with the attached data. If the checksum is wrong a NACK will be signalled.

SPU-HSR-FN0027

If the received command is a Write DXS7 (Photoconductor secondary array “Red array for Blue SPU or Blue Array for Red SPU”) command, attached data shall be checked (via checksum calculation). If checksum is correct, HLSW shall upgrade the Table DXS7 with the attached data. If the checksum is wrong a NACK will be signalled.

SPU-HSR-FN0028

If the received command is a Write Detector Constants for Photometry command, attached data shall be checked (via checksum calculation). If checksum is correct, HLSW shall upgrade the Detector Constants for Photometry Table with the attached data. If the checksum is wrong a NACK will be signalled.

SPU-HSR-FN0029

If the received command is a Write Detector Constants for Spectroscopy command, attached data shall be checked (via checksum calculation). If checksum is correct, HLSW shall upgrade the Detector Constants for Spectroscopy Table with the attached data. If the checksum is wrong a NACK will be signalled.

SPU-HSR-FN0030

If the received command is a Write Simulated Data command, attached data shall be checked (via checksum calculation). If checksum is correct, HLSW shall upgrade the Simulated Data Table with the attached data. If the checksum is wrong a NACK will be signalled.

SPU-HSR-FN0031

If Copy Data from RAM to EEPROM command is received, the HLSW shall copy the program source code data from RAM to EEPROM.

SPU-HSR-FN0032

If Connect to DEC/MEC command is received, the HLSW should start the link to DEC/MEC as slave or master depending on the attached parameter.

### Application Software

SPU-HSR-FN0100

If the Application SW detects DEC/MEC data, it shall read them.

SPU-HSR-FN0101

The Application SW shall be able to trigger the Compression Software in case of the START command.

SPU-HSR-FN0102

In case of HLSW Started Mode (i.e. Start command received), the Application SW shall check whether the received data are photometric, spectroscopic or invalid data.

SPU-HSR-FN0103

After reception of Start command, HLSW buffers data starting from the first sample in ramp “spectroscopy”. Data read up to this sample are ignored except in Buffer Transmission Mode.

SPU-HSR-FN0104

A buffer ready for compression shall contain data with uniform header i.e. valid-flagged data, one OBSID, and one compression mode. In case of non-uniform header (i.e. transition to a new OBSID or compression mode), the data buffers are cleaned and filled with new input data.

SPU-HSR-FN0105

The application software shall be able to process data according to the received compressed mode and make it ready to DPU.

### HK Module

SPU-HSR-FN0200

HLSW shall transmit HK packets to DPU at maximum time interval of 2000 ms.

SPU-HSR-FN0201

Successive HK packets shall contain an incremental counter starting from 0.

SPU-HSR-FN0202

EDAC status concerning single error correction and double error detection in RAM is signalled within the HK. Memory check status word is generated in every HK packet in SPU idle mode and for every 256 HK packets in SPU started mode.

SPU-HSR-FN0203

Ground SW has to detect the permanent memory errors by dumping and analyzing the failing addresses reported with EDAC check. Information for dumping the array of failing addresses can be found in RD016.

SPU-HSR-FN204

To correct single errors and avoid additional double errors memory scrubbing shall be performed every minute in idle mode and every 20 min when the SW is started.

## Performance Requirements

SPU-HSR-FN0300

In started mode, HLSW shall process a data buffer and transmit the resulted compressed packets before a new buffer is filled and ready for processing.

SPU-HSR-FN0301

In started mode, HLSW shall not integrate slopes from different chopper plateaus.

## Interface Requirements

### DPU Commands

SPU-HSR-IF0001

If a DPU command is received, HLSW shall abort any running activity (data compression).

SPU-HSR-IF0002

The maximum response time for the DPU command is 200 ms. In case of Dump and Check commands, data length shall not exceed 10 KB to fulfil the max response time requirement.

SPU-HSR-IF0003

The HLSW shall acknowledge any received DPU commands (NACK or PACK) according to the protocol described in RD007.

#### LOAD Command

SPU-HSR-IF0010

If a Load command is received, HLSW shall abort any running activity, acknowledge the execution of the command according to the protocol described in RD007.

SPU-HSR-IF0011

Data can only be loaded to Data RAM, Extended Data RAM and Dual Port RAM. The HLSW does not write data into Program RAM or EEPROM.

#### DUMP Command

SPU-HSR-IF0020

If a Dump command is received, HLSW shall abort any running activity, acknowledge the execution of the command according to the protocol described in RD007.

SPU-HSR-IF0021

Data can be dumped from Program RAM, Data RAM, Extended Data RAM and Dual Port RAM. The HLSW does not read the EEPROM and the PROM.

#### CHECK Command

SPU-HSR-IF0030

If a Check command is received, HLSW shall abort any running activity, acknowledge the execution of the command if correct parameters according to the protocol described in RD007.

#### RESET Command

SPU-HSR-IF0050

If a Warm Reset command is received, HLSW shall abort any running activity, acknowledge the reception of the command, and execute the command if correct parameters.

#### RAW_CHAN_TRAN_MODE Command

SPU-HSR-IF0060

If Raw Channel Selection command is received, HLSW shall abort any running activity, acknowledge the execution of the command and update the Raw Channel  table.

#### STOP_REDUCT_COMPR Command

SPU-HSR-IF0070

If Stop command is received, HLSW shall acknowledge the reception of the command, and execute the command. If there is no data compression when a Stop command is received no action will be performed.

#### START_REDUCT_COMPR Command

SPU-HSR-IF0080

If Start command is received, HLSW shall abort any running activity, acknowledge the reception of the command, and execute the command if parameters are correct.

#### ACT_TEST_PHOT Command

SPU-HSR-IF0090

If SPU Test command for photometry is received, HLSW shall abort any running activity, acknowledge the reception of the command, and execute the command if parameters are correct.

#### ACT_TEST_SPEC

SPU-HSR-IF0100

If SPU Test command for spectroscopy is received, HLSW shall abort any running activity, acknowledge the reception of the command, and execute the command if parameters are correct.

#### ACT_BOL_BGND_CANCEL Command

SPU-HSR-IF0110 … deleted

If Bolometer Background Cancelling command is received, HLSW shall abort any running activity, acknowledge the reception of the command, and execute the command if correct parameters.

#### Write Commands

SPU-HSR-IF0120

If a Write command is received, HLSW shall abort any running activity, acknowledge the execution of the command.

#### CP_DATA_RAM_EEPROM Command

SPU-HSR-IF0130

If a Copy Data from RAM to EEPROM command is received, the HLSW acknowledges the reception of the command and starts copying data into EEPROM if parameters are correct. If the copy to EEPROM fails, the failure shall be reflected in the HK.

SPU-HSR-IF0131

While data is copied from RAM to EEPROM, no HK packets are transmitted to DPU.

#### CONNECT_DMC Command

SPU-HSR-IF0140

If a Connect to DEC/MEC command is received, HLSW acknowledges the reception of the command and starts the Link to DEC/MEC as Master or Slave according to the command parameter settings. The status of the link connection with DEC/MEC is reported in the HK.

### The Compressed Entity

SPU-HSR-IF0200

HLSW transmits TM packets with fixed size of 1012 Bytes. The useful data size in the last TM packet is calculated using this formula:

Data Size in Last TM Packet = (250 * Total Nb. of TM Packets per Compressed entity) – (7+SCIS+CDMHS)

The size unit is 4-byte words.

SPU-HSR-IF0201

In started mode, HLSW transmits output packets (TM packets or HK packets) to DPU. HLSW may buffer a maximum number of 75 output packets in a FIFO whenever DPU is not ready to receive packets from SPU. Overflowing this number of packets, TM packets are lost. Remark: the DPU is not informed that the buffer has overflowed. The DPU input buffer is limited to 400 packets (RD019), therefore modes with higher data rates than 120 kbit/s (Buffer Transmission Mode) must send the data delayed.

### DEC/MEC to SPU Interface

SPU-HSR-IF0300

HLSW does not acknowledge the reception of DEC/MEC data packets.

SPU-HSR-IF0301

HLSW shall detect corrupted DEC/MEC data packets through the fields: Type and CMM. Packets must be of valid Type and CMM, otherwise they are designated as corrupt.

SPU-HSR-IF0302

HLSW shall distinguish between photometric and spectroscopic data through the Type field.

SPU-HSR-IF0303

The HLSW shall signal the DMC Link connection status in the SPU HK.

SPU-HSR-IF0304

The maximum DEC/MEC packet size accepted by the HLSW is 250 Word in spectroscopy and 272 Word in photometry as specified in RD009. If the received packet lengths differs from these specifications a DEC/MEC header error is signalled in the HK.

## Operational Requirements

### DEC/MEC Header Usage

#### Spectroscopy

Generality

SPU-HSR-OP0001 … obsolete (this restriction does no longer apply)

Buffer granularity of the compression SW is 8Hz. i.e. SPU starts data compression if at least 32 frames (256Hz readout rate) are collected for a coherent DEC/MEC header. If not the already stored data frames are deleted and a new buffering will start. Coherent header refers to the label usage (see Label Section)

SPU-HSR-OP0002

SPU starts compression after collecting a maximum number of frames of 512 (2s Buffer at 256Hz readout rate).

SPU-HSR-OP0003

DEC/MEC header is compressed lossless and transmitted within TM.

SPUID

SPU-HSR-OP0010

SPUID is not taken into account. It is deleted from the buffer.

Type

SPU-HSR-OP0020

If the Type is not conform to the specifications (1 for Spectroscopy packet and 2 for Photometry packet), the science data is not buffered and a DEC/MEC header error is signalled in the SPU HK.

SPU-HSR-OP0021

If the Type is set to 1 „Spectroscopy packet“, HLSW checks CRCRMP to start buffering with the first sample of a ramp.

Current Readout Count in a Ramp

SPU-HSR-OP0030

This field signals the begin of a ramp. It is the first readout stored in a buffer.

SPU-HSR-OP0031

Each begin of a ramp, chopper position, grating position and validity fields are checked and stored as lookup table for processing this buffer.

Readout in Ramp Readback

SPU-HSR-OP0040

This field together with CRCRMP signals the begin of a ramp.

SPU-HSR-OP0041

The last RRR is used for the compression i.e. if a begin and an end of buffer has different RRR, then ramps are fit using the last received RRR.

Compression parameter

SPU-HSR-OP0050

If a buffer is stored with compression parameter not conform to the specifications, a DEC/MEC header error is signalled in the SPU HK and the buffer is compressed in the default compression mode for spectroscopy.

SPU-HSR-OP0051

If a buffer storage is not completed (Frames collected are less than 512) and the compression parameter has changed, the previous buffer is closed, compressed and transmitted. Then a new buffer storage begins. The last ramp of the previous buffer may be cancelled if the new CMM value arrives within a ramp

Validity

SPU-HSR-OP0070

This field is checked for every ramp once. It is only checked for the first sample of a ramp.

SPU-HSR-OP0071 … obsolete

If several ramps should be integrated, invalid-flagged ramps are not included.

SPU-HSR-OP0072

If no integration over ramps is required on board, invalid ramps are also transmitted within the TM.

Chopper Position Readback

SPU-HSR-OP0080

This field is checked for every ramp once. It is only checked for the first sample of a ramp.

SPU-HSR-OP0081 … obsolete

If several ramps should be integrated, only successive ramps from the same chopper plateau are integrated together. Ramps from different chopper plateaus are not together integrated.

SPU-HSR-OP0082

A slope is calculated over a ramp within chopper motion if not invalid-flagged.

SPU-HSR-OP0083

The default value for the max allowed chopper position deviation is 100. It is calculated as following:

Max.Chopper position deviation = Abs (Actual CPR – Previous CPR)

Label

SPU-HSR-OP0090

Bit 0 of this field is checked. It set to 1, and then the DEC/MEC sequence for wavelength switching mode is running. The grating position is taken into account for the integration. Chopper positions are not taken into account.

SPU-HSR-OP0091

If label is signalled, the previous stored buffer is closed (if bigger than buffer granularity), and individually compressed while a new buffer will begin. If there is no previous stored buffer nothing will be sent and a new buffer will begin.

Grating Position Readback

SPU-HSR-OP0100

This field is checked only in the wavelength-switching mode. It is checked for every ramp once. It is only checked for the first sample of a ramp.

SPU-HSR-OP0101 … obsolete

If several ramps should be integrated, only successive ramps for the same grating position are integrated together. Ramps from different grating positions are not together integrated.

SPU-HSR-OP0102

The default value for the max allowed grating position deviation is 100. It is calculated as following:

Max. grating position deviation = Abs (Actual GPR – Pervious GPR)

BBID

SPU-HSR-OP0110

BBID is not taken into account in the compression. It is transmitted within the TM packet.

Time

SPU-HSR-OP0120

Time is not taken into account in the compression. It is transmitted within the TM packet.

Wheel Position Readback

SPU-HSR-OP0130

WPR is not taken into account in the compression. It is transmitted within the TM packet.

CRECR

SPU-HSR-OP0140

CRECR is not taken into account in the compression. It is transmitted within the TM packet.

#### Photometry

Generality

SPU-HSR-OP0200 … obsolete (no granularity)

Buffer granularity of the compression SW is 10Hz for the Blue SPU and 2.5Hz for the red SPU i.e. SPU starts data compression if at least 4 frames for blue and 16 frames for red SPU (40Hz readout rate) are collected for a coherent DEC/MEC header. If not, the already stored data frames are deleted and a new buffering will starts. Coherent header refers to the label usage (see Label Section)

SPU-HSR-OP0201

SPU starts compression after collecting a maximum number of frames of 120 frames for Blue SPU and 480 frames for red SPU (3s and 12s Buffer at 40Hz readout rate). Compression also starts for less collected number of frames if the label field is signalled (See label section)

SPU-HSR-OP0202

DEC/MEC header is compressed lossless and transmitted within TM.

SPUID

SPU-HSR-OP0210

SPUID is not taken into account. It is deleted from the buffer in the actual version of the SPU HLSW.

Type

SPU-HSR-OP0220

If the Type is set to 2 „Photometry packet“, HLSW checks CRDCCP to start buffering with the first sample in chopper plateau.

Current Readout Count in a Chopper Plateau

SPU-HSR-OP0230

This field signals the begin of a chopper plateau „average“. It is the first readout stored in a buffer.

SPU-HSR-OP0231

Each time this counter is set to 1, chopper position is checked and stored as lookup table for processing this buffer.

Current Readout Count

SPU-HSR-OP0240

This field is not taken into account in the compression. It is transmitted within the TM.

Compression parameter

SPU-HSR-OP0250

If a buffer is stored with compression parameter not conforming to the specifications, a DEC/MEC header error is signalled in the SPU HK and the buffer is compressed in the default compression mode for photometry.

SPU-HSR-OP0251

If a buffer storage is not completed (Frames collected are less than 120 for blue or 480 for red SPU) and the compression parameter has changed, the previous buffer is closed, compressed and transmitted. Then a new buffer storage begins.

Validity

SPU-HSR-OP0270

This field is checked for every readout.

SPU-HSR-OP0271

Invalid-flagged readouts are discarded and the averaging always begins using the first valid sample.

SPU-HSR-OP0272

If all samples for an average are flagged invalid, they will not be transmitted within the TM.

Chopper Position Readback

SPU-HSR-OP0280

If integration, only successive averages from the same chopper plateau are integrated together. Averages from different chopper plateaus are not together integrated. This may affect the compression rate in the parallel mode if chopper is moving faster than 5 Hz.

SPU-HSR-OP0281

The default value for the max allowed chopper position deviation is 100. It is calculated as following:

Max.Chopper position deviation = Abs (Actual CPR – Pervious CPR)

Label

SPU-HSR-OP0290

Bit 0 of this field shall be checked. It indicates the start of a sequence, if set to 1.

SPU-HSR-OP0291

If label is signalled, the previous stored buffer is closed, and individually compressed while a new buffer will begin.

Data Block ID

SPU-HSR-OP0300

This field is used to distinguish between blue and red SPU. An incorrect value will cause a DMC header error signalled in the HK.

BBID

SPU-HSR-OP0310

BBID is not taken into account in the compression. It is transmitted within the TM packet.

Time

SPU-HSR-OP0320

Time is not taken into account in the compression. It is transmitted within the TM packet.

Wheel Position Readback

SPU-HSR-OP0330

WPR is not taken into account in the compression. It is transmitted within the TM packet.

BSID

SPU-HSR-OP0340

BSID is not taken into account in the compression. It is transmitted within the TM packet.

### Instrument Configuration

#### Instrument Operating Modes

SPU-HSR-OP0400

The SPU HLSW shall be adapted to operate with any of the instrument operating modes described in Table 1.

| Mode | Description | SPU Task |
| --- | --- | --- |
| Safe | PACS is in this mode when other instrument are prime | HK transmission |
| Standby | State needed for the stabilization of the CRE | Compressed data + HK transmission |
| Prime | All instrument observing modes listed below in Table 2 | Compressed data + HK transmission |
| Parallel | All instrument observing modes listed below in Table 2 | Compressed data + HK transmission |
| Test | Check instrument functionality with synthetic data | Compressed data + HK transmission |

Table 1. PACS Instrument Operating Modes

SPU-HSR-OP0401

The SPU HLSW shall allow a safe transition from a mode to another with a minimum loss of useful scientific data.

SPU-HSR-OP0402

The parameters of the instrument-operating mode are not sent to the SPU HLSW with the DEC/MEC raw data.

#### Instrument Observing Modes

SPU-HSR-OP0500

The SPU HLSW shall be adapted to operate with any of the instrument observing modes described in Table 2.

| Mode | Description |
| --- | --- |
| Dual-Band Photometry | Standard photometry mode. Both detector arrays are operating simultaneously (BOL) |
| Single-Band Photometry | One detector array is operating (BOL). |
| Line Spectroscopy | A short spectral coverage for each pixel is produced. Both detector arrays (PHC) are used at a time |
| Range Spectroscopy | Large spectral range coverage for each pixel is produced. Both detector arrays (PHC) are used at a time |
| Parallel | Dual-Band and Single-Band Photometry are used |
| Calibration Measurements/Observations | Various instrumental settings |

Table 2.  PACS Instrument Observing Modes

SPU-HSR-OP0501

The instrument observing parameters are not sent within the DEC/MEC header to the SPU HLSW.

### SPU HLSW Compression Modes

#### Compressed Data Transmission Mode

SPU-HSR-OP0600

The transmission of additional raw data is optional. The remaining difference to the maximum data rate (120 kbits/s) could be used for transmission of lossless-compressed raw data from a few consecutive channels if Raw Channel Selection parameters are set accordingly.

SPU-HSR-OP0601

The DEC/MEC header shall be compressed and transmitted with the compressed data except in the buffer transmission mode.

SPU-HSR-OP0602

The following parameters shall be sent within the SPU HLSW HK: Housekeeping Header, Observation Identification, Packet Index, Counter Increment, Reduction Algorithm used, Saturation Flag, Glitch counter information, Number of maintained subramps, CPU workload, DEC/MEC link status, Number of integrated ramps, SW Version Identification, Raw Channel Index, DEC/MEC header error, Counters for EDAC Memory Checks, SW Sub-version, Invalid LLC Parameter and Monitored Write Parameter.

SPU-HSR-OP0603

In nominal case one compressed entity is generated every 12 seconds for red photometry (LWL) while it is generated at 3 seconds interval for blue photometry (SWL).

SPU-HSR-OP0604

In nominal case one compressed entity is generated every 2 seconds for spectroscopy (LWL and SWL).

##### Default Compression Mode

SPU-HSR-OP0610

HLSW shall be able to support the TM rate of 120 Kbits/s in the default compression mode.

SPU-HSR-OP0611

In started compression SW, the transmitted HK packet following an already-sent compression entity shall contain the compression results as described in RD007.

##### Double Compression Mode

SPU-HSR-OP0620

HLSW shall be able to support the TM rate of parallel mode by integrating over a predefined set of readouts.

##### Half-Compression Mode (Photometry only)

SPU-HSR-OP0625

For 20 Hz readout rate in photometry, every two successive samples are reduced (averaged) in nominal case. One compressed entity is generated every 24 seconds for red photometry (LWL) while it is generated at 6 seconds interval for blue photometry (SWL).

##### Lossless Compression Mode

SPU-HSR-OP0630

HLSW shall be able to select a few detectors data through DXS tables, to compress them lossless and to make them available to DPU.

SPU-HSR-OP0631

HLSW shall not compress all selected pixels lossless to avoid SW crash. Maximum data size for lossless compression mode  is decribed in Section 5.9.6.

SPU-HSR-OP0632

If all pixels are selected, HLSW shall be able to select few detectors data (Maximum data size) and compress them lossless.

#### SPU Test Mode

SPU-HSR-OP0640

HLSW shall be able to support SPU test mode. It generates internally simulated data and compresses them.

#### Transparent Mode

SPU-HSR-OP0650

HLSW shall be able to support SPU transparent mode with a few selected pixels.

#### Buffer Transmission Mode

SPU-HSR-OP0660

Buffer transmission mode (described in Section 5.8.5 for photometry and Section 5.8.9 for spectroscopy) shall be used in PACS Burst mode. Remark: the DPU is not informed that burst mode is executing.

SPU-HSR-OP0661

Compression software shall be in stopped state before the run of the buffer compression and vice versa. The switch to the buffer transmission mode from an already commanded compression mode, while compression software is started, may lead to an unpredictable result.

#### Compression Mode for 4s Reset (Spectroscopy only)

SPU-HSR-OP0670

The 4 seconds data buffer shall be subdivided to two identical 2 seconds buffers, where each sub-buffer is independently compressed and put into telemetry.

## Resource Requirements

SPU-HSR-RS0001

HLSW shall have 20% more memory capacity at the time of DDR.

SPU-HSR-RS0100

HLSW software shall have 20% spare processing capacity at the time of the DDR.

## Verification Requirements

SPU-HSR-VF0001

The software shall undergo acceptance verification based at the validation and verification test plan at the following levels:

- Equipment level

- Subsystem level

- System level

SPU-HSR-VF0002

It should be ensured that compressed data can be decompressed to yield the original data.

SPU-HSR-VF0003

It should be ensured that test data sets are chosen to fully execute all paths of the algorithm logic, and to demonstrate handling of worst-case data.

## Acceptance Testing Requirements

SPU-HSR-AT0001

For Acceptance Tests the test cases listed in the following table shall be performed.

| Task name | AVM | CQM | PFM | FS |
| --- | --- | --- | --- | --- |
| DPU to SPU SWL Communication Interface |  |  |  |  |
| SWTC.1 | X | X | X | X |
| DEC/MEC to SPU SWL Communication Interface |  |  |  |  |
| SWTC.2 | X | X | X | X |
| Application Software Test |  |  |  |  |
| SWTC.3 | X | X | X | X |
| Integration of HLSW in LWL SPU |  |  |  |  |
| SWTC.4 | X | X | X | X |

Table 3, Acceptance Test

## Documentation Requirements

SPU-HSR-DO0001

The software specification document shall replace the three documents: Architectural Design Document, Detailed Design Document and the Software Requirement Document.

## Portability Requirements

SPU-HSR-PT0001

The software shall be compiled with G21K from Analog Devices. It is runnable on the ADSP 21020 with the communication chip SMCS332 and under Virtuoso Operating System.

## Quality Requirements

SPU-HSR-QA0001

The software development shall be performed in compliance with the Software Quality Assurance Plan (see AD007).

SPU-HSR-QA0002

The software source code shall be commented according to the rules described in AD007.

## Reliability Requirements

SPU-HSR-QA0100

The software shall handle anomalies with respect to:

- Command execution

SPU-HSR-QA0101

The software shall be designed to avoid

- deadlock, starvation and endless looping.

- dynamic memory allocation.

SPU-HSR-QA0102

The software shall include mechanisms in respect to protect data and resources shared between processes.

SPU-HSR-QA0103

The software shall be able to handle RAM and EEPROM SEU.

SPU-HSR-QA0104

The software shall be able to handle corrupt and incomplete DEC/MEC data.

SPU-HSR-QA0105

The software shall be able to detect and handle arithmetic errors. Divisions by 0 shall yield to the result 0xFFFFFFFF (-1).

SPU-HSR-QA0106

The software shall not lead to buffer overflow/underrun.

## Maintainability Requirements

SPU-HSR-QA0200

The software shall be maintainable to later extent.

SPU-HSR-QA0201

Maintainability shall contain error detection and fault repair until launch.

SPU-HSR-QA0202

The SW build shall follow automated procedures using deliverable scripts.

SPU-HSR-QA0203

The SDE shall include all software licences and tools to be frozen and made available to MPE.

SPU-HSR-QA0204

The SW deliveries shall include a detailed map file produced by ADSP compiler.

SPU-HSR-QA0205

The in-house tools needed in development or test shall be documented.

SPU-HSR-QA0206

For problem reporting the SPR/SCR system at http://pacs.ster.kuleuven.ac.be/ shall be used and for CVS repository management the CVS system at http://cvs.ster.kuleuven.be/ shall be used.

## Safety Requirements

SPU-HSR-SA0001

The order of commands, HK and telemetry are classified as safety critical. The commanding must strictly follow the User Manual (RD016).

SPU-HSR-SA0010

The HK shall provide a detailed SPU HLSW status, which should indicate memory failures on the SPU or data consistency failures (DEC/MEC Header).

SPU-HSR-SA0011

Memory failures detected by the EDAC should be indicated in the HK  The corresponding HK parameter is described in RD016. Permanent memory errors should be isolated and recovered by dumping and analyzing the failing addresses.

SPU-HSR-SA0012

The HLSW shall signal DEC/MEC header errors in the HK. The list of errors is given in RD016.

# System Design

## Design Method

A top down approach is used for structuring the HLSW in small modules.

## Decomposition Description

The HLSW has been decomposed in three main tasks

- The Watch Process: This task listens to the DPU link. It interrupts the Application SW whenever a command is received for its acknowledgment. Basically, any running activity on board SPU is interrupted whenever a command is received from DPU.

- The Application Software: This task performs data reduction and compression according to DEC/MEC header received within the raw data. Its responsibility is to achieve the required compression ratio according to telemetry requirements and to the compression mode.

- The HK module: This task generates HK, which is sent to the DPU at 1.9 seconds interval.

A detailed component description follows in Section 5.

### The Watch Process and Command Interpretation and Acknowledgement

The responsibility of this module is to listen to the DPU communication link. If a DPU command is received, actual running activities are interrupted and the command is acknowledged and executed. In fact, the DPU command consist of memory load, dump, check, write or perform the sub-unit warm reset, start/stop compression, start SPU test mode and raw channel selection. The description of these commands is reported in RD007.

### The Application SW

This task performs data reduction and compression according to the DEC/MEC header. The ASW consists of 2 main parts:

- Supervisor

- Compression software

#### Supervisor

The DEC/MEC science data + header are composed of scientific data and information about the observation configuration and the compression parameters.

The supervisor is implemented at the top of the SPU ASW. It reads from the DEC/MEC header the way the compression should be done. Then, it buffers the separately DEC/MEC header and the science data. Finally, it activates the compression software whenever a buffer is ready for compression.

Furthermore, the supervisor listens to the watch process and wait for a signal to start or stop data processing.

Figure 15. Flowchart of the Supervisor Algorithm

#### Compression Software

Figure 16 represents the general layout of the compression software modules. This part represents the core of the SPU HLSW. It is the SW part in which data is reduced and/or compressed using arithmetical and logical operations.

This module is responsible of:

- Science data compression following the DEC/MEC header logic

- DEC/MEC header compression

- Putting the compression results in the HK

- Building the compressed entity packet

- Transmission of the compressed data

- Raw channel data lossless compression

The CSW performs data reduction and compression according to the header information. It consists of a sequence of functions to fulfil the required compression mode.

##### HLSW Compression Modes

The SPU HLSW has 12 possible compression modes, which are listed and described below.

Compressed Data Transmission Mode

In the compressed data transmission mode, reduced and compressed data including DEC/MEC header have to be transmitted to DPU. They consist of either sample average rates in photometry mode or slope rates of ramps generated by the ramp-fitting module in spectroscopy imaging. Then, data may also be treated by the integration module to achieve the required compression ratio. This data will be further processed by redundancy reduction modules and finally by a lossless coding module, which will produce a stream of 16 bit words. The following compression modes are available:

- Default Compression Mode: BOL1 (Photometry), SPEC1 (Spectroscopy)

- Double Compression Mode: BOL2 (Photometry), SPEC2 (Spectroscopy)

- Half Compression Mode: BOL0 (Photometry)

- Compressed Sensing Mode: BOLCS (Photometry)

Lossless Compression Mode

In the lossless compression mode, a selection of measurement values shall be transmitted without any loss of information, while the non-selected data are omitted. Therefore, data from selected detectors will be compressed (lossless compression only), and then transmitted to the DPU subsystem. The following modes are available:

- BOL3 (Photometry), SPEC3 (Spectroscopy)

Transparent Mode

In the transparent mode, data from selected detectors are transmitted without any compression. Furthermore, the DEC/MEC header is compressed and transmitted to DPU within the science data packet. The following modes are available:

- BOL4 (Photometry), SPEC4 (Spectroscopy).

Buffer Transmission Mode

In the buffer transmission mode, data from all detectors are transmitted without any compression. Therefore the whole data memory apart the output buffer will be filled with a continuous raw data stream. The following modes are available:

- BUF_BOL (Photometry), BUF_SPEC (Spectroscopy).

Compressed Sensing Mode (Photometry only)

In this compression mode a selection of samples from a projection onto an incoherent basis will be made. The following mode is available:

- BOLCS (Photometry).

Compression Mode for 4s Reset (Spectroscopy only)

In this compression mode a 4 seconds buffer will be subdivided into two 2-seconds buffers. Each buffer will be independently processed using the default compression mode in spectroscopy. The following mode is available:

- SPEC5 (Spectroscopy).

##### Summary of Compression Modes

The compression modes are represented in Table 4. It shows the used functions for each mode.

| HLSW Compression Mode | DXS | PRE | RBA/ RPF DEG | T_SRR | LLC | raw data sel. | Memory use | CMM |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| BOL0 | ( | ( | ( | ( | ( |  | 1 Buffer | 0x02 |
| BOL1 | ( | ( | ( | ( | ( |  | 1 Buffer | 0x00 |
| BOL2 | ( | ( | ( | ( | ( |  | 1 Buffer | 0x01 |
| BOL3 | ( |  |  | ( | ( |  | 1 Buffer | 0x04 |
| BOL4 | ( |  |  |  |  |  | 1 Buffer | 0x07 |
| BUF_BOL |  |  |  |  |  |  | 5 Buffers | 0x09 |
| BOLCS |  |  |  |  | ( |  | 1 Buffer | 0x0C |
| SPEC1 | ( | ( | ( | ( | ( | ( | 1 Buffer | 0x10 |
| SPEC2 | ( | ( | ( | ( | ( | ( | 1 Buffer | 0x11 |
| SPEC3 | ( |  |  | ( | ( |  | 1 Buffer | 0x14 |
| SPEC4 | ( |  |  |  |  |  | 1 Buffer | 0x17 |
| SPEC5 | ( | ( | ( |  |  | ( | 2 Buffers | 0x18 |
| BUF_SPEC |  |  |  |  |  |  | 5 Buffers | 0x19 |

Table 4. Photometric and Spectroscopic compression modes

Figure 16. Compression SW Scheme.

### The HK Module

The SPU HLSW HK is sent from the SPU to the DPU. It consists either of compression results and status of the HLSW whenever raw data are received from DEC/MEC, or the SPU HLSW status while no observation is performed. Depending on their availability, the SPU HLSW HK are transmitted at a data rate compatible with the overall PACS HK.

The functionality of the SPU HLSW is continuously checked by the DPU monitoring some SPU HLSW HK data. The “Are you alive SPU” is described in the document RD007.

# Component and Functional Description

| SW Component | Files |
| --- | --- |
| Header Files | “bitmodel.h”, “pacscod.h”, “qsmodel.h”, “rangecod.h”, “genspu.h”, “spu_io.h”, “spuasw.h”, “spulib.h” |
| Low Level Driver Library | “l_dsp.h”, “l_errcod.h”, “l_gendef.h“, “l_hwmap.h“, “l_smcsco.h”, “l_smcsge.h”, “l_smcsin.h”, “l_smcsre.h”, “l_smcstr.h”, “l_itlmis.oba”, “l_memory.oba”, “l_memory.obc”, “l_smcsge.obc”, “l_smcsco.obc”, “l_smcsin.obc”, “l_smcsre.obc”, “l_smcstr.obc”, “l_dsp.oba”, “l_dsp.obc” , “l_pscgen.obc” , “l_eeprom.obc” |
| Communication Interface | “datatx.c”, ”dorada.s”, ”spu_io.c”, “supervs.c”, “watchpc.c” |
| Command Acknowledgment | “C2EEPROM.c”, “check.c”, “DMC_Con.c” “dump.c”, “Load.c”, “perform.c”, “Rc_Sel.c”, “spu_tst.c”, “Str_Stp.c”, “w_reset.c”, “write.c” |
| Compression Software | ”average.c”, “bitmodel.c”, “bol_ex.c”, “bol1_2.c”, “bol3.c”, “bol4.c”, ”buf_bol.c”, ”buf_spec.c”, “csw.c”, “dmch_cp.c”, ”dxs.c”, “fill_in.c”, “fill_out.c” , “integ.c” , “llc.c” , “pacscod.c”, “p_proc.c” , “pacs_srt.c”, “qsmodel.c”, “ramp_ft.c”, “rangecod.c”, “spec1_2.c” , “spec3.c” , “spec4.c” , “T_S_Red.c”, “T_S_fm.c” |
| Housekeeping | “Hk.c” |
| Miscellaneous | “phot_gn.c”, “pkup_pg.c”, “spec_gn.c”, ”Spvs_Tst.c”, “rolib_a.s” |

Table 5. Software Files of the SPU HLSW

## Main Task

### Type

spu_io.c   –   main task

### Function

This is the main program task of the HLSW. It configures and initialises the connection SPU-DPU and SPU-DEC/MEC. When connection is established, it starts the HLSW task (Watch process, Supervisor, HK,…).

The following functions are contained:

DpuConnect	Start the Link towards DPU

ConnectLinkAsSlave	Start the Link Connection as Slave

ConnectLinkAsMaster	Start the Link Connection as Master

DMCLinkConnect	Start the Link Connection to DEC/MEC as Slave or Master

LinkSmcsRead	Reads from SMCS communication link memory

Link1355Write	Writes to SMCS communication link memory

Memory_Error_Check	Checks for Single and/or Double Error Failure in memory

MemoryScrubbing	Scrubs the Memory and correct Single Bit Error Failure in memory

ResetLink	Resets the SMCS communication link

SMCSHandlerC	Wrapper for Assembly ISR

#### SMCS Chip Handling by SPU HLSW

- SPU Handover to HLSW

The SPU HLSW is configured to start the DPU Link as Master (see link Start-up Protocol in RD005). When the SPU control is handed over from LLSW to the HLSW, the following steps are performed :

- Reset SMCS chip

- Set the DEC/MEC Link Connection Status in the HK to OFF

- Set Nominal Configuration of the SMCS

- Set DSP Interrupt at IRQ2 to Signal SMCS Events

- Configure SMCS sub-interrupt for the two links (DPU and DMC). Unmask the following sub-interrupt (CH1_PAR_DIS_ERR, CH1_DATA_TXED, CH1_EOP_RXED, CH2_PAR_DIS_ERR, CH2_DATA_TXED and CH2_EOP_RXED)

- Start the link to DPU as Master

- Wait 9 seconds

- If Connection to DPU is not established, then go back to Step 1.

- Start the Application SW tasks

  - Communication Tasks and HK

  - Compression Tasks

  - Tasks for SPU Test Mode

The link start-up to DMC is performed under request using the command CONNECT_DMC. The start-up protocol (Master/Slave) could be chosen by the user.

The DEC/MEC Link Connection Status in the HK is set to ON, whenever the connection between SPU and DMC is established.

- Connection Loss between SPU and Other Subunits

▪  DPU-SPU Disconnect Error

When the SPU HLSW detects a disconnect error on the DPU link, the following steps are performed:

- Stop the Application SW tasks

    - Communication Tasks and HK

    - Compression Tasks

    - Tasks for SPU Test Mode

- Perform the Steps 1-9 in the Paragraph ‘SPU Handover to HLSW’ above.

▪  DMC-SPU Disconnect Error

When the SPU HLSW detects a disconnect error on the DMC link, the DMC Link Status in the HK is set to OFF.

### Interfaces

Call: KS_TaskGroupStart(SPU_INIT)	Starts communication and HK tasks

Call: KS_TaskGroupStart(SPU_ASW)	Starts compression software task

Call: KS_TaskGroupStart(SPU_TEST_TASKS)	Starts data generators for photometry and spectr. tasks

Call: KS_TaskGroupAbort(SPU_INIT)	Aborts communication and HK tasks

Call: KS_TaskGroupAbort(SPU_ASW)	Aborts compression software task

Call: KS_TaskGroupAbort(SPU_TEST_TASKS)	Aborts data generators for photometry and spectr. Tasks

Call: KS_TaskSleep	Time delay

### Dependencies

None

### Processing

See flowchart in Figure 17.

Figure 17. Flowchart of the Main Taks.

### Data

None

### Resources

SMCS Chip

## Watch Process

### Type

watchpc.c  –   task

### Function

The watch process program listens to the DPU link. When a command is received, all running activities (except the HK task) are interrupted and the respective function is called to acknowledge and execute the command.

### Interfaces

Call: Link1355Read	Reads from SMCS communication link towards DPU

Call: LinkSMCSRead	Reads from SMCS communication link

Call: InitDetectorSelectionTables	Initialise the Data Selection Table

Call: InitTables	Initialise the Bit Mask Table

Call: KS_FIFOPut	Send the response packet to the FIFO (Data Transmission task)

Call: KS_SemaSignal	Signals the start of HK transmission

Call: KS_TaskSleep	Time delay

Call: Load	Calls procedure to acknowledge and perform the Load Command request

Call: Dump	Calls procedure to acknowledge and perform the Dump Command request

Call: Check	Calls procedure to acknowledge and perform the Check Command request

Call: Perform	Calls procedure to acknowledge and perform the Perform Activity command request

Call: Write	Calls procedure to acknowledge and perform the Write Command request

### Dependencies

Called from the main task.

### Processing

See flowchart in Figure 18.

Figure 18. Flowchart of the Watch Process Task

### Data

Read data from SMCS Link1.

### Resources

SMCS Chip

## Supervisor

### Type

supervs.c   –   task

### Function

The supervisor task listens to the DMC link. It reads DMC packets whenever received. If a start CSW command is signalled, the DMC packets are buffered and the compression is started. Otherwise, new DMC packets will overwrite the old ones (DMC data are ignored).

Furthermore, the Supervisor prepares the lookup tables from the received DMC header and makes them ready for the CSW, whenever the CSW is started.

The DMC packet structure is outlined below. More details can be found in RD009.

DEC/MEC Raw Data Stream to SPU

Figure 19 represents one detector array in spectroscopy. They consist of a total of 18x25 detectors. Each detector will deliver a 16-bit signal. One row of 18 detector data is added at the DEC level. Therefore, the total science data frame size is 468 words.

Figure 19. Detector array for the Spectroscopy.

Figure 20a represents the 8 arrays of the SWL photometer and Figure 20b the 2 arrays of the LWL photometer. They consist of a total of 2048 detectors for SWL and 512 detectors for LWL. Each detector will deliver a 16-bit signal.

Figure 20. Configuration of the (a) SWL-Detector Arrays and of the (b) LWL-Detector Arrays.

The maximum packet size sent from DEC/MEC to SPU is 250 words (64 Bytes DMC header + 26x18x16/8 Bytes science data = 1000 Bytes) in spectroscopy and 272  words (64 Bytes DMC header + 16x16x2x16/8 Bytes science Data = 1088 Bytes) in photometry as depicted in Figure 21 and Figure 22.

Figure 21. Resulting DMC packet structure for Spectroscopy.

Figure 22. Resulting DMC packet structure for (a) SWL-Photometry and for (b) LWL-Photometry.

DEC/MEC Header Structure

The DEC/MEC header structure is represented in RD016 (HLSW User Manual)

Label (LBL)

The Label statement is meant to indicate to the SPU-HLSW across which "quadruples" it has to average in photometry. It is further used also to indicate the number of discrete chopper steps within a sequence. In spectroscopy the Label statement is used in wavelength switching mode when Bit 1 and Bit 6 are set. Hereafter, the following conventions for the Label in photometry:

If Label is set to 0, then no sequence is active otherwise

Bit 1 … is set to 1, to indicate that DMC sequence is active.

Bit 2-6 … counts chopper positions within sequence

Bit 7 … signal from BB1

Bit 8 … signal from BB2

LABEL = 63 has a special meaning and indicates "freeze frame mode"

Validity (VLD)

The “Validity” statement defines if the data is valid or not. If the data is declared invalid the data will be ignored and the buffer is cleaned until valid data is arriving.

Compression Parameters

The compression and transmission mode which corresponds to the Compression Parameters field in  are listed in Table 6.

| Comp. and Trans. Mode ID | Photometry | Spectroscopy |
| --- | --- | --- |
| 0x00 | Default Mode | None |
| 0x01 | Double Compression Mode | None |
| 0x02 | Half Compression Mode | None |
| 0x04 | Lossless Compression Mode | None |
| 0x07 | Transparent Mode | None |
| 0x09 | Buffer Transmission Mode | None |
| 0x10 | None | Default Mode |
| 0x11 | None | Double Compression Mode |
| 0x14 | None | Lossless Compression Mode |
| 0x17 | None | Transparent Mode |
| 0x18 | None | Compression Mode for 4 second reset |
| 0x19 | None | Buffer Transmission Mode |

Table 6. List of Compression Parameters for Photometry and Spectroscopy

### Interfaces

Call: Link1355Read	Reads from SMCS link towards DPU

Call: LinkSmcsRead	Reads from SMCS link

Call: WriteInCircularBuffer	Calls procedure to fill the Input Buffer with Science data

Call: KS_SemaSignal(SEMA_ASW)	Signals the start of the compression software task

Call: ResetCircularBuffers	Memory allocation for buffering of DMC header, science and telemetry data

### Dependencies

Called from the main task.

### Processing

See flowchart in Figure 23, Figure 24, Figure 25 and .

‘Compress_Now = true’ in the flowchart means: “Close the actual buffer and make it ready for compression. Begin to store data in a new buffer.”

Figure 23. Flowchart of the Supervisor Task (Part 1)

Figure 24. Flowchart of the Supervisor Task (Part 2)

see next page

Figure 25. Flowchart of the Supervisor Task (Part 3)

see page after next

### Data

Read data from SMCS Link2.

### Resources

SMCS Chip

1 MB allocated Data Memory

## Data Transmission

### Type

datatx.c   –   task

### Function

The data transmission program module waits for the tasks outputs and sends them to the DPU. This task organizes the data flow from SPU to DPU.

### Interfaces

Call: LinkSmcsWrite	Writes to SMCS communication link

Call: KS_FIFOGetW	Wait that another task writes in the FIFO

### Dependencies

Called from the main task.

### Processing

See flowchart in Figure 26.

Figure 26. Flowchart of the Data Transmission Task.

### Data

Data read from FIFO.

### Resources

SMCS Chip

## Housekeeping

### Type

hk.c  –   task

### Function

This program module produces HK parameters at 1.9 seconds interval. One relevant parameter is an incremental counter as described in RD007 (“Are You Alive SPU”). When the CSW is started some parameters are read from HK buffer (compression information).

Following parameters are included in the HK:

| HK_HEADER | Housekeeping Header |
| --- | --- |
| OBSID | Observation Identification |
| PIX | Packet Index |
| CI | Counter Increment |
| REAL | Reduction Algorithm used |
| SATUR_FLAG | Saturation Flag |
| SAMP_CORR | Glitch counter information |
| MAINT_RAMPS | Number of maintained subramps |
| CPU_WORKLOAD | CPU workload |
| DMC_LINK_STATUS | DEC/MEC link status |
| INTEG_RAMPS | Number of integrated ramps |
| VID | Version Identification |
| RCX | Raw Channel Index |
| DMC_ERROR | DEC/MEC header error |
| MEM_STATUS_CNTS | Counters for EDAC Memory Checks |
| SUBVERSION | Subversion of the SPU HLSW |
| LLC_ERROR | Invalid LLC Parameter |
| PAR_MONITOR | Monitored Write Parameter |

### Interfaces

Call: KS_FIFOPut	Sends the HK packet to the FIFO (Data Transmission task)

Call: KS_TaskSleep	Time delay

### Dependencies

Called from the main task.

### Processing

Figure 27. Flowchart of the Housekeeping Task

### Data

Writes data to the FIFO.

### Resources

None

## Fill_InputBuffer

### Type

fill_in.c   –   procedure

### Function

The Fill_InputBuffer programme module is used to handle the data flow from/to the memory. It consists of circular buffer and functions to load and dump data to/from the memory.

Contains of following functions:

DeclareCircularBuffer	Reserves a memory space in the SPU RAM for data buffering

WriteInCircularBuffer	Fills the input buffer with the DEC/MEC science data

ReadInCircularBuffer	Reads the science data from input buffer

CircularBufferQuerySpace	Checks the empty memory space in science data input buffer

CircularBufferQueryUsed	Checks the used memory space in science data input buffer

CircularBufferRemoveLastWrittenValues	Remove the last values from a circular buffer

CircularBufferRemove	Clears a circular buffer by depletion

ResetCircularBuffers	Memory allocation for buffering of science header, DMC and telemetry data

### Interfaces

None

### Dependencies

Called from Supervisor or Supervisor_Test.

### Processing

Figure 28. Flowchart of the Fill_InputBuffer Procedure

### Data

None

### Resources

2 MB Memory

## Command Interpretation and Acknowledgement

### LOAD Command

#### Type

load.c   –   procedure

#### Function

This procedure acknowledges and executes (if Load parameters are correct) the Load command received from DPU. This command is used to transfer data in SPU DRAM and DPRAM. For more details see RD007.

#### Interfaces

Call: KS_FIFOPut	Sends the response packet to the FIFO (Data Transmission task)

#### Dependencies

Called from watch process.

#### Processing

See flowchart in Figure 29.

Figure 29. Flowchart of the Procedure for Load Command Handling

#### Data

Writes data to the FIFO.

#### Resources

None

### DUMP Command

#### Type

dump.c   –   procedure

#### Function

This procedure acknowledges and executes (if Dump parameters are correct) the Dump command received from DPU. This command is used to transfer data from SPU RAM. For more details see RD007.

#### Interfaces

Call: KS_FIFOPut	Sends the response packet to the FIFO (Data Transmission task)

Call: KS_TaskSleep	Time delay

#### Dependencies

Called from watch process.

#### Processing

See flowchart in Figure 30.

Figure 30. Flowchart of the Procedure for Dump Command Handling

#### Data

Writes data to the FIFO.

#### Resources

None

### CHECK Command

#### Type

check.c   –   procedure

#### Function

This procedure acknowledges and executes (if Check parameters are correct) the Check command received from DPU. This command is used to check the SPU RAM. For more details see RD007.

Contains of following functions:

Crc	Calculates the Checksum

#### Interfaces

Call: KS_FIFOPut	Sends the response packet to the FIFO (Data Transmission task)

#### Dependencies

Called from watch process.

#### Processing

See flowchart in Figure 31

Figure 31. Flowchart of the Procedure for Check Command Handling

#### Data

Writes data to the FIFO.

#### Resources

2 MB Data Memory

### Perform Activity Command

#### Type

perform.c   –   procedure

#### Function

This procedure acknowledges the reception of the Perform command and starts the appropriate function according to the received Activity ID.

#### Interfaces

Call: PerformCopyToEeprom	Copy Data from RAM to EEPROM

Call: PerformWarmReset	Warm Reset function

Call: PerformRawChannelSelection	Raw Channel Selection function

Call: PerformStartStop	Start or Stop CSW function

Call: PerformSpuTestMode	SPU Test for Spectroscopy or Photometry function

Call: PerformConnectToDmc	Start Link to DEC/MEC as Master or Slave

Call: KS_FIFOPut	Sends the response packet to the FIFO (Data Transmission task)

#### Dependencies

Called from watch process.

#### Processing

See Flowchart in Figure 32.

Figure 32. Flowchart of the Procedure for the Perform Activity Command Handling

#### Data

Writes data to the FIFO.

#### Resources

None

### CP_DATA_RAM_EEPROM Command

#### Type

C2EEPROM.c   –   procedure

#### Function

This procedure acknowledges the reception of the Copy data from RAM to EEPROM command and updates the HLSW in SPU EEPROM. It Copies the HLSW from PRAM and/or DRAM to EEPROM..

#### Interfaces

Call: PerformCopyToEeprom	Copies Data from RAM to EEPROM

Call: KS_FIFOPut	Sends the response packet to the FIFO (Data Transmission task)

Call: KS_TaskSleep	Time delay

#### Dependencies

Called from perform activity command module.

#### Processing

See flowchart in Figure 33.

Figure 33. Flowchart of the Procedure for Copy Data from RAM to EEPROM Command Handling

#### Data

Writes data to the FIFO.

#### Resources

None

### RESET Command

#### Type

w_reset.c   –   procedure

#### Function

This procedure performs a Warm Reset of the HLSW. If SPU HLSW receives the Warm Reset command it cleans all buffers (DCMH data, science data and telemetry data buffers), reset the HK counter CI and PIX, kill all tasks (Supervisor, Watch Process, Data Transmission and HK) , reset the SMCS chip and restart the link connection to DPU.

#### Interfaces

Call: KS_FIFOPut	Sends the response packet to the FIFO (Data Transmission task)

Call: KS_TaskSleep	Time delay

Call: KS_SemaSignal(WARM_RESET_SEMA)	Reset SMCS chip and all the tasks apart the spu_io

#### Dependencies

Called from perform activity command module.

#### Processing

See flowchart in Figure 34.

Figure 34. Flowchart of the Procedure for Warm Reset Command Handling

#### Data

Writes data to the FIFO.

#### Resources

None

### RAW_CHAN_TRAN_MODE Command

#### Type

Rc_Sel.c   –   procedure

#### Function

This procedure is used to select the number and index of channels from which data should be lossless compressed and transmitted. The channels index and number could be selected for photoconductors and bolometers. At startup this index and number are set to zero.

#### Interfaces

Call: KS_FIFOPut	Sends the response packet to the FIFO (Data Transmission task)

#### Dependencies

Called from perform activity command module.

#### Processing

See flowchart in Figure 35.

Figure 35. Flowchart of the Procedure for Raw Channel Selection Command Handling

#### Data

Writes data to the FIFO.

#### Resources

None

### START/STOP_REDUCT_COMPR Command

#### Type

Str_Stp.c   –   procedure

#### Function

This procedure is used to Start or Stop the CSW.

- The Start command is performed to run the SPU CSW for DEC/MEC data.

- The Stop command is used to abort any running activity. When called it deletes the buffered data (DCMH data, science data and telemetry data buffers).

#### Interfaces

Call: KS_FIFOPut	Sends the response packet to the FIFO (Data Transmission task)

Call: KS_TaskSleep	Time delay

Call: ResetCircularBuffers	Memory allocation for buffering of science header, DMC and telemetry data

#### Dependencies

Called from perform activity command module.

#### Processing

See flowchart in Figure 36.

Figure 36. Flowchart of the Procedure for the Start and Stop Commands Handling

#### Data

Writes data to the FIFO.

#### Resources

None

### ACT_TEST_PHOT/SPEC Command

#### Type

Spu_tst.c   –   procedure

#### Function

This procedure is used to start the SPU Test Mode for Spectroscopy or Photometry.

#### Interfaces

Call: KS_FIFOPut	Sends the response packet to the FIFO (Data Transmission task)

Call: KS_SemaSignal(SPU_SPVS_TST)	Signals the start of the Supervisor for the SPU Test

Call: KS_SemaSignal(SEMA_SPUTESTS)	Signals the start of the data generator of photometry' frames

Call: KS_SemaSignal(SEMA_SPUTESTP)	Signals the start of the data generator of spectroscopy' frames

#### Dependencies

Called from perform activity command module.

#### Processing

See flowchart in Figure 37.

Figure 37. Flowchart of theProcedure for SPU Test Command Handling

#### Data

Writes data to the FIFO.

#### Resources

None

### CONNECT_DMC Command

#### Type

DMC_Con.c   –   procedure

#### Function

This procedure acknowledges the reception of the Connect to DEC/MEC command and starts the link to DEC/MEC as Master or Slave depending on the attached parameter.

#### Interfaces

Call: PerformConnectToDmc	DEC/MEC Link Start Task

Call: KS_FIFOPut	Sends the response packet to the FIFO (Data Transmission task)

Call: KS_TaskSleep	Time delay

#### Dependencies

Called from perform activity command module.

#### Processing

See flowchart in Figure 38.

Figure 38. Flowchart of the Procedure for Connect to DEC/MEC Command Handling

#### Data

Writes data to the FIFO.

#### Resources

None

### Write Command

#### Type

write.c   –   procedure

#### Function

This procedure is used to update the compression lookup tables (DXS, DET_CST_PHOT, DET_CST_SPEC and SIM_DATA tables).

It contains the following functions:

InitDetectorSelectionTables	Initialises the Data Selection Table

InitTables	Initialises the Bit Mask Tables

A short description of the ten-lookup tables is given below.

- Write of Detectors Selection Table in the SPU Memory (WRT_DXS)

Seven write commands allow the upgrade of the detectors tables from which data are requested. The detectors (photoconductors and bolometers) information is written in seven tables. Five for the bolometers and two for the photoconductors. The length of each DXS table is 96 Bytes (0x18 words).

The same HLSW is running in both SPUs Red and Blue. The SW accepts all seven write commands WRT_DXS1-7. The user has to choose the command to send depending on the Detector type (photometer WRT_DXS1-5 or spectrometer WRT_DXS6-7).

Both SPUs have the same set of commands, the SW accepts all commands but the usage of the tables depends on the observing mode (photometry or spectroscopy) and the wavelength (SWL and LWL).

- WRT_DXS1-5 commands are required for photometry data processing for both SPUs

- WRT_DXS6 command is actually required for spectroscopy for both SPUs

- WRT_DXS1-4 and WRT_DXS6 commands are required for SWL data processing in any  SPU

- WRT_DXS5 and WRT_DXS6 commands are required for LWL data processing in any SPU

- WRT_DXS7 command may be used in degraded mode whenever one SPU sub-unit  has to process data from both detectors (SWL and LWL). In the current SW version WRT_DXS7 is not exploited as the degraded mode is not implemented .

See RD016 (HLSW User Manual) for more details.

- Write of Detectors Constants for Spectroscopy in the SPU Memory (WRT_DET_CST_SPEC)

It allows the upgrade of the table of photoconductor constants, which are relevant for the pre-processing step in spectroscopy. The table length is 96 Bytes (0x18 words). See RD016 (HLSW User Manual) for more details.

- Write of Detectors Constants for Photometry in the SPU Memory (WRT_DET_CST_PHOT)

It allows the upgrade of the table of bolometer constants, which are relevant for the pre-processing step in photometry. The table length is 96 Bytes (0x18 words). See RD016 (HLSW User Manual) for more details.

- Write of Simulated Data Parameters in the SPU Memory (WRT_SIM_DATA)

It allows the upgrade of the parameters table, which will be used for data generation in the SPU test mode. The table length is 96 Bytes (0x18 words). See RD016 (HLSW User Manual) for more details.

#### Interfaces

Call: InitDetectorSelectionTables	Initialises the Data Selection Table

Call: KS_FIFOPut	Sends the response packet to the FIFO (Data Transmission task)

#### Dependencies

Called from watch process.

#### Processing

See flowchart in Figure 39.

Figure 39. Flowchart of the Procedure for Write Command Handling

#### Data

Writes data to the FIFO and the data memory.

#### Resources

None

## Compression Software

### Compression Software Main Task

#### Type

csw.c   –   task

#### Function

The compression software compresses the science data according to the required compressed mode. The compressed parameter is received via the supervisor. The compression software will accordingly start appropriate tasks.

#### Interfaces

Call: PhotoReductionAndCompression	Bol1 and Bol2 compression procedure

Call: PhotoLosslessCompressionMode	Bol3 compression procedure

Call: PhotoTransparentMode	Bol4 compression procedure

Call: PhotoBufferTransmissionMode	Procedure for Buffer Transmission Mode in Photometry

Call: SpectroReductionAndCompressionMode	Spec1 and Spec2 compression procedure

Call: SpectroLosslessCompressionMode	Spec3 compression procedure

Call: SpectroTransparentMode	Spec4 compression procedure

Call: SpectroBufferTransmissionMode	Procedure for Buffer Transmission Mode in Spectroscopy

Call: KS_TaskSleep	Time delay

Call: KS_SemaSignal	Signals the start of HK transmission

#### Dependencies

Called from the main task.

Activated by Supervisor or Supervisor_Test task.

#### Processing

See flowchart in Figure 40 and Figure 41.

Figure 40. Flowchart of the Compression Software Main Task (Part 1)

Figure 41. Flowchart of the Compression Software Main Task (Part 2)

#### Data

None

#### Resources

None

### Photometry Modes 0, 1 and 2

#### Type

bol_ex.c   –   procedure

#### Function

This procedure performs data compression in photometry for the Bol1 or Bol2 modes depending on the received compression parameter.

* 	Bol1 (Default Compression Mode): This is the default mode for photometry.

* 	Bol2 (Double the Compression Ratio): This mode is used whenever the default compression ratio should be doubled.

* 	Bol0 (Half Compression Mode): This mode is used whenever the readout rate in photometry is decreased to 20 Hz. It performs 2 sample averaging for reduction.

#### Interfaces

Call: DmcHeaderCompression	DMC header extraction and compression

Call: Dxs	Detector selection

Call: PreProcessing	Pre-processing of the data

Call: FloatAveraging	when averaging arbitrary number of samples

Call: Averaging4Samples	default averaging

Call: PhotoCompression	Temporal and spatial redundancy reduction, lossless coding

Call: PhotoCompression2	Temporal and spatial redundancy reduction, lossless coding

Call: BuildCompressedEntity	Write the compressed data into the output buffer

#### Dependencies

Called from the compression software main task.

#### Processing

See flowchart in Figure 42.

Figure 42. Flowchart of the Bol_ex Procedure

#### Data

None

#### Resources

None

### Photometry Mode 3

#### Type

bol3.c   –   procedure

#### Function

Bol3 (Lossless Compression Mode) is used for the lossless compression of photometry data from selected detectors.

#### Interfaces

Call: DmcHeaderCompression	DMC header extraction and compression

Call: Dxs	Detector selection

Call: TSReductionForPhotoLlc_	Temporal and spatial redundancy reduction

Call: LosslessCompressionForPhoto	Lossless Coding

Call: BuildCompressedEntity	Write the compressed data into the output buffer

#### Dependencies

Called from the compression software main task.

#### Processing

See flowchart in Figure 43.

Figure 43. Flowchart of the Bol3 Procedure

#### Data

None

#### Resources

None

### Photometry Mode 4

#### Type

bol4.c   –   procedure

#### Function

Bol4 (Transparent Mode) is used for the transparent mode. It transmits raw data from selected detectors without compression.

#### Interfaces

Call: DmcHeaderCompression	DMC header extraction and compression

Call: Dxs	Detector selection

Call: BuildCompressedEntity	Write the compressed data into the output buffer

#### Dependencies

Called from the compression software main task.

#### Processing

See flowchart in Figure 44.

Figure 44. Flowchart of the Bol4 Procedure

#### Data

None

#### Resources

None

### Photometry Buffer Transmission Mode

#### Type

buf_bol.c   –   procedure

#### Function

This procedure deals with the Buffer Transmission mode in photometry. It fills the memory for a certain time with the data, then sends them in raw mode.

BUF_Bol (Buffer Transmission Mode): The entire memory buffers will be filled with DEC/MEC header and science data (Blue SPU: 5 x 3 seconds; Red SPU: 5 x 12 seconds). After 15/60 seconds (Blue/Red SPU) the SPU HLSW ignores the input DEC/MEC data and start sending the buffered data for duration of 150 seconds in case of Blue SPU and 155 seconds in case of Red SPU. The data is then transmitted to the DPU with rate compatible to the telemetry rate in burst mode. The telemetry packets are transmitted at 60 msec average time intervals to DPU i.e. 37 TM packets are made ready for DPU every 2220 msec

In SWL the buffers will be filled with 15 seconds data from all detectors. This data will be stored in five buffers (buffer1, buffer2, buffer3, buffer4 and buffer5). Therefore, each buffer includes 3 seconds of data. Then the SPU HLSW ignores all incoming data from DMC and begins to transmit the buffered 15 seconds data to DPU. They will be sent in the following sequence: buffer5, buffer1, buffer2, buffer3 and then buffer4. The data consists of uncompressed DMCH (only from 1 array ID) and uncompressed science data. In the compressed entity header the CDHS is set to Zero while SCIS contains the full data size (size = 0x1E618 words = 497760 Bytes). During this period HK are transmitted at regular rate to DPU.

- Blue SPU: 	5 x 498 packets = 2490 packets of 1000 Bytes are sent at average time interval of 50 ms

- SPU puts every 2220 msec 37 TM packets to DPU (2220/37=60 ms time interval between two TM packets).

- 28 B + 497760 B (SD & DMH) + 24 B (TM Header) x 498 packets = 509740 Bytes x5 = 2548700Bytes

- 2548700Bytes*60ms/1024Bytes = 149,4sec (150sec)

- 2548700Bytes /(150+15) sec = 121 kbit/s

- The averaged TM rate for the blue SPU is 121 kbit/s

In LWL the buffers will be filled with 60 seconds data from all detectors. This data will be stored in five buffers (buffer1, buffer2, buffer3, buffer4 and buffer5). Therefore, each buffer includes 12 seconds of data. Then the SPU HLSW ignores all incoming data from DMC and begins to transmit the buffered 60 seconds to DPU. They will be sent in the following sequence: buffer5, buffer1, buffer2, buffer3 and then buffer4. The data consists of uncompressed DMCH and uncompressed science data. In the compressed entity header the CDHS is set to Zero while SCIS contains the full data size (size = 0x1F860 word = 516480 Bytes). During this period HK are transmitted at regular rate to DPU.

- Red SPU: 	5 x 517 packets = 2585 packets of 1000 Bytes are sent at average time interval of 50 ms

- SPU puts every 2220 msec 37 TM packets to DPU (2220/37=60 ms time interval between two TM packets).

- 28 B + 516480 B (SD & DMH) + 24 B x 517 packets = 528916 Bytes x5 = 2644580 Bytes

- 2644580 Bytes*60ms/1024Bytes = 154.9 sec (155sec)

- 2644580 Bytes/(155+60) sec = 90kbit/s

- The averaged TM rate for the red SPU is 90 kbit/s

- The averaged TM rate for both SPUs is 211 kbit/s.

#### Interfaces

Call: ReadInCircularBuffer	Reads the science data from input buffer

Call: BuildCompressedEntity	Write the compressed data into the output buffer

#### Dependencies

Called from the compression software main task.

#### Processing

See flowchart in Figure 45.

Figure 45. Flowchart of the BUF_Bol Procedure

#### Data

None

#### Resources

It requires at least 3 MB of memory.

### Spectroscopy Modes 1 and 2

#### Type

spec1_2.c   –   procedure

#### Function

This procedure performs data compression in spectroscopy for the Spec1, Spec2 or Spec5 modes depending on the received compression parameter.

* 	Spec1 (Default Compression Mode): This is the default mode for spectroscopy.

*	Spec2 (Double the Compression Ratio): This mode is used whenever the default compression ratio should be doubled.

The Spec5 mode performs a default compression mode for a 4-second ramp. The ramp is subdivided to 2 sub-ramps of 2-second length.

* 	Spec5 (Compression Mode for 4s Reset): This mode is used to handle detectors data with a reset interval of 4s. The compression software receives 1024 frames and put them into two buffers. Each buffer contains 512 frames. Then the SW resamples the data from 256Hz to 8Hz with the implemented fitting algorithm.

#### Interfaces

Call: DmcHeaderCompression	DMC header extraction and compression

Call: Dxs	Detector selection

Call: PreProcessing	Pre-processing of the data

Call: RampFit	Ramp fitting and glitch rejection

Call: TSReductionForSpectro	Resorting the data and Temporal and spatial redundancy reduction

Call: LosslessCompressionForSpectro	Lossless Coding

Call: BuildCompressedEntity	Write the compressed data into the output buffer

#### Dependencies

Called from the compression software main task.

#### Processing

See flowchart in Figure 46.

Figure 46. Flowchart of the Spec1_2 Procedure

#### Data

None

#### Resources

None

### Spectroscopy Mode 3

#### Type

spec3.c   –   procedure

#### Function

Spec3 (Lossless Compression Mode) is used for the lossless compression of spectroscopy data from selected detectors.

#### Interfaces

Call: DmcHeaderCompression	DMC header extraction and compression

Call: Dxs	Detector selection

Call: TSReductionForSpectro	Resorting the data and Temporal and spatial redundancy reduction

Call: LosslessCompressionForSpectro	Lossless Coding

Call: BuildCompressedEntity	Write the compressed data into the output buffer

#### Dependencies

Called from the compression software main task.

#### Processing

See flowchart in Figure 47.

Figure 47. Flowchart of the Spec3 Procedure

#### Data

None

#### Resources

None

### Spectroscopy Mode 4

#### Type

spec4.c   –   procedure

#### Function

Spec4 (Transparent Mode) is used for the transparent mode. It transmits raw data from selected detectors without compression.

#### Interfaces

Call: DmcHeaderCompression	DMC header extraction and compression

Call: Dxs	Detector selection

Call: BuildCompressedEntity	Write the compressed data into the output buffer

#### Dependencies

Called from the compression software main task.

#### Processing

See flowchart in Figure 48.

Figure 48. Flowchart of the Spec4 Procedure

#### Data

None

#### Resources

None

### Spectroscopy Buffer Transmission Mode

#### Type

buf_spec.c   –   procedure

#### Function

This procedure deals with the Buffer Transmission mode in spectroscopy. It fills the memory for a certain period with data, and then sends them in raw mode.

BUF_Spec (Buffer Transmission Mode): The entire memory buffers will be filled with DEC/MEC header and science data (Blue and Red SPU: 5 x 2 seconds). After 10 seconds the SPU HLSW ignores the input DEC/MEC data and start sending the buffered data for duration of 152 seconds. The data is then transmitted to the DPU with rate compatible to the telemetry rate in burst mode. The telemetry packets are transmitted at 60 msec average time intervals to DPU i.e. 37 TM packets are made ready for DPU every 2220 msec.

In LWL and SWL the buffers will be filled with 10 seconds data from all detectors. This data will be stored in five buffers (buffer1, buffer2, buffer3, buffer4 and buffer5). Therefore, each buffer includes 2 seconds of data. Then the SPU HLSW ignores all incoming data from DMC and begins to transmit the buffered 10 seconds data to DPU. They will be sent in the following sequence: buffer5, buffer1, buffer2, buffer3 and then buffer4. The data consists of uncompressed DMCH and uncompressed science data. In the compressed entity header the CDHS is set to Zero while SCIS contains the full data size (size = 0x1EE00 words = 494 kB). During this period HK are transmitted at regular rate to DPU.

- Blue/Red SPU:  5 buffer x 506 packets = 2530 packets of 1000 Bytes are sent at average time interval of 60 ms.

- SPU puts every 2220 msec 37 TM packets to DPU (2220/37=60 ms time interval between two TM packets).

- 28 B + 494 KB (SD & DMH) + 24 B (TM  packet header) x 506 packets = 518028 Bytes x5 = 2590140 Bytes

- 2590140 Bytes /1024B*60ms = 151.77sec (152sec)

- 2590140/(152+10) sec = 124.91kbit/s

The averaged TM rate per SPU board is 124.91 kbit/s.

The averaged TM rate for both SPUs is 249,82 kbit/s.

#### Interfaces

Call: ReadInCircularBuffer	Reads the science data from input buffer

Call: BuildCompressedEntity	Write the compressed data into the output buffer

#### Dependencies

Called from the compression software main task.

#### Processing

See flowchart in Figure 49.

Figure 49. Flowchart of the BUF_Spec Procedure

#### Data

None

#### Resources

It requires at least 3 MB of memory.

## Compression SW Modules

### Detector Selection

#### Type

dxs.c   –   procedure

#### Function

This procedure performs the data selection according to the detector tables. The detectors selection tables are directly set by DPU in the SPU memory using a write command. This is used to identify the selected detectors from which data are solicited.

The solicited data are transmitted to DPU using the predefined compression mode. If the compression mode requires data reduction (compression modes spec1_2, spec5 or bol_ex), additional raw data from few channels can be transmitted lossless-compressed to fill the TM bandwidth.

#### Interfaces

None

#### Dependencies

Called from Bol_ex, Bol3, Bol4, Spec1_2, Spec3 or Spec4 procedure.

#### Processing

Detector selection procedure is depicted in Figure 50.

Figure 50. Flowchart of the Detector Selection Procedure

The currently implemented raw channel data compression algorithm is described in Appendix A.1.3.

#### Data

None

#### Resources

2 MB data memory

### Preprocessing

#### Type

p_proc.c   –   procedure

#### Function

This procedure is used in photometry and spectroscopy mode in order to transform the received signal to the appropriate form (linear ramps in spectroscopy and constant signal in photometry). In fact, the use of this module is still TBD depending on the efficiency of the electronics and the electric filters.

#### Interfaces

None

#### Dependencies

Called from Bol_ex or Spec1_2 procedure.

#### Processing

See flowchart in Figure 51.

Figure 51. Flowchart of the Preprocessing Procedure

#### Data

None

#### Resources

None

### Robust Averaging

#### Type

average.c   –   procedure

#### Function

This procedure is used to perform glitch rejection and oversampling reduction of the photometry data.

#### Interfaces

None

#### Dependencies

Called from Bol_ex procedure.

#### Processing

See flowchart in Figure 52.

A library of fitting algorithms for photometry data is proposed in Appendix B.2.1.

Figure 52. Flowchart of the Robust Averaging Procedure

The currently implemented averaging algorithm is described in Appendix B.1.1.

#### Data

None

#### Resources

None

### Ramp Fitting

#### Type

ramp_ft.c   –   procedure

#### Function

This procedure is used to perform glitch rejection and calculating a slope or a mean out of a predefined set of samples in spectroscopy. The number of samples to use can be set using the write detectors constants in spectroscopy command (Section 5.7.11). From one to several slopes/means can be derived out of a ramp depending on the set parameter (Number of sample per sub-ramp)

#### Interfaces

None

#### Dependencies

Called from Spec1_2 procedure.

#### Processing

See the following  flowchart.

A library of fitting algorithms for spectroscopy data is proposed in Appendix B.2.1.

Figure 53. Flowchart of the Ramp-fitting Procedure

The currently implemented ramp-fitting algorithm is described in Appendix B.1.2.

#### Data

None

#### Resources

None

### Integration (obsolete)

#### Type

integ.c   –   procedure

#### Function

This procedure performs on-board integration over the sensor readings in order to achieve the desired compression ratio.

#### Interfaces

None

#### Dependencies

Called from Bol_ex or Spec1_2 procedure.

#### Processing

See flowchart in Figure 54.

Figure 54. Flowchart of the Integration Procedure

#### Data

None

#### Resources

None

### Temporal and Spatial Redundancy Reduction

#### Type

T_S_Red.c   –   procedure

#### Function

The aim of this procedure is to eliminate the temporal and spatial correlation of the sensor readings and resorting the data for better peroformance of lossless coding.

In case of Lossless Compression Mode, this module checks and selects the maximum data size allowed for lossless compression.

Maximum data size= 120 Kbytes:

- First 60 detectors (Figure 19) in spectroscopy are chosen

- First  256 detectors (Figure 20) in photometry are chosen for SWL SPU

- First  64 detectors (Figure 20) in photometry are chosen for LWL SPU

#### Interfaces

None

#### Dependencies

Called from Bol_ex, Bol3, Spec1_2 or Spec3 procedure.

#### Processing

See the flowchart in Figure 55 for spectroscopy and Figure 56 for photometry.

Figure 55. Flowchart of the Temporal and Spatial Redundancy Reduction Procedure for Spectroscopy

Figure 56. Flowchart of the Temporal and Spatial Redundancy Reduction Procedure for Photometry

#### Data

None

#### Resources

None

### Lossless Coding

#### Type

llc.c   –   procedure

#### Function

This procedure performs the lossless coding of the data.

#### Interfaces

Call: pacs_srt	Sorts the data for following compression algorithm

Call: initmodel (in pacs_cod.c)	initialization of the dynamical model for the range coder

Call: pacs_encode (in pacs_cod.c)	applies the model and calls the range coder

Call: deletemodel (in pacs_cod.c)	deletes the model

#### Dependencies

Called from Bol_ex, Bol3, Spec1_2 or Spec3 procedure.

#### Processing

See flowchart in Figure 57.

A library of Lossless Coding (LLC) algorithms is proposed in Appendix A.2.

Figure 57. Flowchart of the Lossless Compression Procedure

The currently implemented Lossless Coding algorithm for science data can be found in Appendix A.1.2.

#### Data

None

#### Resources

None

### Header Compression

#### Type

dmch_cp.c   –   procedure

#### Function

This procedure performs a lossless compression of the received DEC/MEC header.

#### Interfaces

Call: ReadInCircularBuffer	Reads the DMC header from input buffer

#### Dependencies

Called from Bol_ex, Bol3, Bol4, Spec1_2, Spec3 or Spec4 procedure.

#### Processing

See flowchart in Figure 57.

A library of Lossless Coding (LLC) algorithms is proposed in Appendix A.2.

Figure 58. Flowchart of the DEC/MEC Header Compression Procedure

The currently implemented lossless compression algorithm for DEC/MEC header can be found in Appendix A.1.1.

#### Data

None

#### Resources

None

### Fill_OutputBuffer

#### Type

fill_out.c   –   procedure

#### Function

The Fill_OutputBuffer procedure is used to prepare the compressed entity and build the PUS packets. It sets the packet ready-to-transmit to the data transmission function.

The compressed entity represents the data packet sent from the SPU to the DPU. It consists of the compressed science data and the compressed DEC/MEC header. It should be packaged and split into blocks, which fit in the telemetry packets (AD002) and made available to the DPU according to document RD007. The compressed entity packet structure is described in the document RD007.

The compressed entity is split by the SPU into blocks to fit into the telemetry packets (AD002). A header of 12 Bytes (Block Header) is added to each block before it is sent to the DPU (Figure 59). 8 Bytes of this header will be ignored in the DPU as described in RD007.

Figure 59. Splitting of the Compressed Entity and the Resulting Science Data Blocks

#### Interfaces

Call: KS_FIFOPut	Sends the response packet to the FIFO (Data Transmission task)

Call: KS_TaskSleep	Time delay

Call: WriteInCircularBuffer	Store The TM packet in the output buffer

Call: KS_SemaSignal	Signals the start of HK transmission

#### Dependencies

Called from Bol_ex, Bol3, Bol4, BUF_Bol, Spec1_2, Spec3, Spec4, Spec5 and BUF_Spec procedure.

#### Processing

See flowchart in Figure 60.

Figure 60. Flowchart of the Fill_OutputBuffer Procedure

#### Data

Writes data to the FIFO.

#### Resources

1 MB data memory

## Supervisor for Test Mode

### Type

Spvs_Tst.c   –   task

### Function

The supervisor for test mode task listens to the data generators. It reads test data packets whenever received. If a start CSW command is signalled, then the test data packets are buffered and the compression is started.

It performs the supervisor activities while SPU test mode is activated.

### Interfaces

Call: WriteInCircularBuffer	Calls procedure to fill the Input Buffer with Science data

Call: KS_SemaSignal(SEMA_ASW)	Signals the start of the compression software task

### Dependencies

Called from the main task.

### Processing

See flowchart in Figure 61, Figure 62, Figure 63 and Figure 64.

‘Compress_Now = true’ in the flowchart means: “Close the actual buffer and make it ready for compression. Begin to store data in a new buffer.”

Figure 61. Flowchart of the Supervisor for Test Mode Task (Part 1)

Figure 62. Flowchart of the Supervisor for Test Mode Task (Part 2)

See next page

Figure 63. Flowchart of the Supervisor for Test Mode Task (Part 3)

See page after next

Figure 64. Flowchart of the Supervisor for Test Mode Task (Part 4)

### Data

Read data from the data generator.

### Resources

1 MB allocated Data Memory

## Photometry Data Generator

### Type

phot_gen.c   –   task

### Function

This program generates simulated data for photometry.

### Interfaces

Call: KS_SemaSignal(SPU_TEST)	Signals the start of the SPU Test Mode

Call: KS_TaskSleep	Time Delay

### Dependencies

Called from Spu_tst procedure.

### Processing

See flowchart in Figure 65.

Figure 65. Flowchart of the Photometry Data Generator Task

### Data

None

### Resources

None

## Spectroscopy Data Generator

### Type

spec_gen.c   –   task

### Function

This program generates simulated data for spectroscopy.

### Interfaces

Call: KS_SemaSignal(SPU_TEST)	Signals the start of the SPU Test Mode.

Call: KS_TaskSleep	Time Delay

### Dependencies

Called from Spu_tst procedure.

### Processing

See flowchart in Figure 66.

Figure 66. Flowchart of the Spectroscopy Data Generator Task

### Data

None

### Resources

None

# Feasibility and Resource Estimates

## Memory Allocation

The operations of the SPU HLSW are limited by the available memory size. Figure 67 represents the memory allocation within one SPU board. Table 7 shows the memory allocation for the SPU HLSW.

| Memory Type | Memory Size [MB] | Memory Allocation [%] | Description |
| --- | --- | --- | --- |
| EEPROM | 1.5 | 17 | for storage and backup of the program code to avoid several uplinks of the same program code in case of SPU switch off/on, RAM corruption etc. |
| Program Memory (PRAM) | 3.0 | 25 | used to store and run the program code. |
| Data Memory (DRAM) | 4.0 | 94 | for static data allocation and data processing storage. |
| SMCS Memory (DPRAM) | 32 kB | 87.5 | used for data transfer between SPU – DEC/MEC and SPU – DPU. |

Table 7. Memory Allocation of the SPU HLSW.

The memory usage is at least 10% less than the memory allocated.

Figure 67. SPU HLSW Memory Map.

In data memory (DRAM) three circular buffers are available per SPU board for data acquisition, storage and transmission, in addition to the processing memory. For data compression the SPU HLSW swaps between two 0.5 Mbytes buffered data. After the buffering of 0.5 Mbytes of input data (science data and DEC/MEC header) the compression of this data starts while the second 0.5 Mbytes buffer is filled.

The memory map is given in RD016. The PRAM is not protected from overwriting by the HLSW because the PRAM is used by two compression modes for data buffering (Buffer Transmission Mode and 4s Reset mode in spectroscopy). Furthermore, the write command is able to access the PRAM area.

## Processing Power

The SPU consists of two CPU boards (TSC21020). The clock frequency of each CPU is 18 MHz with  54 MFLOPs (peak) and 36 MFLOPs (sustained) (see RD012, page 11). The exact CPU workload derived for all compression modes, for a HLSW version, can be found in the respective HLSW user manual (RD016).

## Application SW Estimates

In this section, additional requirements of the compression SW (ASW) on the signal in order to achieve the required compression ratio are given.

### Compression Ratio

Nominal PACS science data rate is about 120 kbits/s in prime mode. Therefore, the allocated rate for science data excluding the header is about 118 kbits/s.

Based on this assumption the minimum required compression ratio is calculated below.

Photometry

Science Data Input	(2048 + 512) detectors x 40 Hz x 16 bit = 1600 kbit/s

Minimum CR in photometry: 		1600/118 = 13.56

Spectroscopy

Science Data Input	2 (boards) x (26x18) detectors x 256 Hz x 16 bit = 3744 kbit/s

Minimum CR in spectroscopy		3744/118 = 31.73

### Entropy Estimates for Redundancy Reduction

In this Section, we calculate the redundancy in the signal, in terms of bits, that is required to achieve the minimum compression ratio. We only consider the lossless compression part of the ASW. A compression factor (see Table 8) should be already achieved by the lossy compression module in nominal compression modes.

In the lossless compression module one reference value is kept every tref time interval. The differences to the reference are calculated (see also Figure 68) and coded in nbit bits (noise). For more details see Section 5.9.6.

Figure 68. Redundancy Reduction.

The compression ratio (CR) achieved by the redundancy reduction module can be calculated as follows:

CR = [16 x Nd x tref x S / CR_fit] / [chop_pos x 16 + nbit x (Nd x tref x S / CR_fit – chop_pos)]

where

Nd 	number of detectors

S 	sampling frequency

CR_fit	compression ratio of the previous lossy compression step (averaging/ramp fitting module)

chop_pos	number of chopper positions (one reference per chopper plateau).

Therefore, the maximum number of bits allocated to the noise can be calculated as follows:

nbit = [(16 x Nd x tref x S / CR_fit) / CR – chop_pos x 16] / [Nd x tref x S  / CR_fit – chop_pos] .

Table 8 depicts the maximum number of bits allocated to the noise required to fulfil the TM rate. They are calculated for 4 Hz chopper frequency.

| Observing Mode | Minimum CR | CR by lossy compression module | CR by lossless compression module | number of bits allocated to the noise |
| --- | --- | --- | --- | --- |
| Photometry | 13.56 | 4 | 3.390 | 4.72 |
| Spectroscopy | 31.73 | 32 | 0.992 | 16.13 |
|  |  | 16 | 1.983 | 8.06 |
|  |  | 8 | 3.966 | 4.03 |
|  |  | 4 | 7.933 | 2.02 |
|  |  | 2 | 15.865 | 1.01 |

Table 8. Number of Bits Allocated to the Noise.

## Data Rates Estimate

Table 9 and Table 10 show the data rates estimate for all compression modes in photometry and spectroscopy. These numbers are calculated as presented in the next subsections.

| Compression Mode in Photometry | Description | Selected Detectors | Expected TM Rate [kbits/s] | Packets per second |
| --- | --- | --- | --- | --- |
|  |  | SPU LWL | SPU SWL | SPU LWL | SPU SWL | Total |  |
| BOL0 | Half Compression Mode | 512 | 2048 | 87.44 | 29.93 | 117.37 | 15.05 |
| BOL1 | Default Mode | 512 | 2048 | 81.95 | 21.53 | 103.48 | 13.17 |
| BOL2 | Double Compression Mode | 512 | 2048 | 41.68 | 11.45 | 53.13 | 6.76 |
| BOL3 | Lossless Compression Mode | 512 148 | 2048 592 | 323.39 94.53 | 81.89 24.67 | 405.28 119.20 | 51.57 15.17 |
| BOL4 | Transparent Mode | 512 37 | 2048 148 | 1289.11 94.48 | 323.28 24.63 | 1612.39 119.11 | 205.15 15.16 |
| BUF_Bol | Buffer Transmission Mode | 512 | 2048 | 94.50 | 118.60 | 213.10 | 27.11 |

Table 9. Expected Data Rates for the Compression Modes in Photometry

| Compression Mode in Spectroscopy | Description | Selected Detectors | Expected TM Rate [kbits/s] | Packets per second |
| --- | --- | --- | --- | --- |
|  |  | SPU LWL | SPU SWL | SPU LWL | SPU SWL | Total |  |
| SPEC1 | Default Mode | 450 | 450 | 58.76 | 58.76 | 117.52 | 14.95 |
| SPEC2 | Double Compression Mode | 450 | 450 | 30.47 | 30.47 | 60.94 | 7.75 |
| SPEC3 | Lossless Compression Mode | 450 57 | 450 57 | 454.88 59.53 | 454.88 59.53 | 909.75 119.06 | 115.75 15.14 |
| SPEC4 | Transparent Mode | 450 14 | 450 14 | 1812.94 58.46 | 1812.94 58.46 | 3625.88 116.92 | 461.34 14.88 |
| SPEC5 | Compression Mode for 4s Reset | 450 | 450 | 58.73 | 58.73 | 117.47 | 14.95 |
| BUF_Spec | Buffer Transmission Mode | 450 | 450 | 122.71 | 122.71 | 245.42 | 31.23 |

Table 10. Expected Data Rates for the Compression Modes in Spectroscopy

The data rate for one raw channel in photometry is

40 Hz x 16 bit = 0,625 kbits/s

and for one raw channel in spectroscopy

256 Hz x 16 bit = 4 kbits/s .

### Photometry

The nominal data rates in photometry are calculated as follows:

Step 1: Averaging

Since we have to average 4 samples, we reduce the input science data by a factor of 4.

The input science data of 1280 + 320 = 1600 kbit/s are reduced to 320 + 80 = 400 kbit/s here.

Step 2: Redundancy Reduction

- 	SWL:

16 bits x 10 (averages) x 2048 (detectors) after data averaging = 327680 bits per array

(4 x 16 bits) + 4 bits x (10 x 2048 detectors - 4) = 81968 bits per array

The ratio achieved in this step is 327680/81968 = 3.9977

-	LWL:

16 bits x 10 (averages) x 512 (detectors) after data averaging = 81920 bits per array

(4 x 16 bits) + 4 bits x (10 x 512 detectors - 4) = 20528 bits per array

The ratio achieved for the red SPU is 81920/20528 = 3.9906

The science data is reduced to 80.0469 + 20.0469 = 100.0938 kbit/s here.

Table 11 shows the nominal data rates for photometry. The calculation of the header rates is described below.

|  | SWL [kbits/s] | LWL [kbits/s] | SWL & SWL [kbits/s] |
| --- | --- | --- | --- |
| Compressed Science Data | 80.0469 | 20.0469 | 100.0938 |
| Compressed DEC/MEC Header Rate | 1.3333 | 1.3333 | 2.6667 |
| Compressed Entity Header | 0.0729 | 0.0182 | 0.0911 |
| Packet Header | 0.5000 | 0.1289 | 0.6289 |
| Total | 81.9531 | 21.5273 | 103.4805 |

Table 11. Nominal Data Rates for Photometry.

Compressed DEC/MEC Header Rate

If we consider 512 Bytes per compressed entity for the compressed DEC/MEC header then we get

SWL:		512 Bytes / 3 s = 170.67 Bytes/s (1.333 kbits/s)

LWL:		2048 Bytes / 12 s = 170.67 Bytes/s (1.333 kbits/s)

Compressed Entity Header Rate

If we consider 28 Bytes per compressed entity for the CEH then we get

SWL:		28 Bytes / 3 s = 9.333 Bytes/s (0.0729 kbits/s)

LWL:		28 Bytes / 12 s = 2.333 Bytes/s (0.0182 kbits/s)

Packet Header Rate

If we consider a packet size of 1000 Bytes we get the number of packets

SWL	(28B + 512B + [3s x 2048 x 40Hz x 2B / 15.9976(CR)]) / 1000B = 31.265

→ 32 packets/buffer; 32 packets / 3s = 10.667 packets/s

LWL	(28B + 2048B + [12s x 512 x 40Hz x 2B / 15.9908 (CR)]) / 1000B = 32.814

→ 33 packets/buffer; 33 packets / 12s = 2.75 packets/s

If we consider 6 Bytes per packet then we get a packet header rate of

SWL:		10.667 packets/s x 0.046875 kbits = 0.5 kbits/s

LWL:		2.75 packets/s x 0.046875 kbits = 0.1289 kbits/s

### Spectroscopy

The nomunal data rates in spectroscopy are calculated as follows:

Step 1: Ramp Fitting

Since we have to fit over 8 samples, we reduce the input science data by a factor of 8.

The input science data of 2 x 1800 = 3600 kbit/s are reduced to 2 x 225 = 450 kbit/s here.

Step 2: Redundancy Reduction

- 	SWL & LWL:

16 bits x 32 (slopes) x 450 (detectors) after data fitting = 230400 bits per array

(4 x 16 bits) + 4 bits x (32 x 450 detectors - 4) = 57648 bits per array

The ratio achieved in this step is 230400/57648 = 3.9967

The science data is reduced to 2 x 56.2969 = 112.5938 kbit/s here.

Table 12 shows the nominal data rates for spectroscopy. The calculation of the header rates is described below.

|  | SWL [kbits/s] | LWL [kbits/s] | SWL & SWL [kbits/s] |
| --- | --- | --- | --- |
| Compressed Science Data | 56.2969 | 56.2969 | 112.5938 |
| Compressed DEC/MEC Header Rate | 2.0000 | 2.0000 | 4.0000 |
| Compressed Entity Header | 0.1094 | 0.1094 | 0.2188 |
| Packet Header | 0.3516 | 0.3516 | 0.7031 |
| Total | 58.7578 | 58.7578 | 117.5156 |

Table 12. Nominal Data Rates for Spectroscopy.

Compressed DEC/MEC Header Rate

If we consider 512 Bytes per compressed entity for the compressed DEC/MEC header then we get

SWL & LWL:	512 Bytes / 2 s = 256 Bytes/s (2 kbits/s)

Compressed Entity Header Rate

If we consider 28 Bytes per compressed entity for the CEH then we get

SWL & LWL:	28 Bytes / 2 s = 14 Bytes/s (0.1094 kbits/s)

Packet Header Rate

If we consider a packet size of 1000 Bytes we get the number of packets

SWL & LWL:	(28B + 512B + [2s x 450 x 256Hz x 2B / 31.97 (CR)]) / 1000B = 14.95

→ 15 packets/buffer; 15 packets / 2s = 7.5 packets/s

If we consider 6 Bytes per packet then we get a packet header rate of

SWL & LWL:	7.5 packets/s x 0.046875 kbits = 0,3516 kbits/s

# User Requirements vs. Software Traceability Matrix

| User Requirements | Software Requirements | Description |
| --- | --- | --- |
| SPU-OBS-ON1 | SPU-SUSW-2610 | SPU handover to HLSW (see RD015 page 41) |
| SPU-OBS-ON2 | SPU-HSR-FN0200 | HK to DPU |
| SPU-OBS-OF1 | --- | No data storage before the switch off of the SPU unit |
| SPU-OBS-SW1 | SPU-HSR-FN0102..105 | HLSW performs the data reduction and compression according to DEC/MEC header |
| SPU-OBS-SW2 | SPU-HSR-FN0005 SPU-HSR-FN0202 SPU-HSR-FN0203 | HLSW has the possibility to detect data corruption in the Loaded memory area |
| SPU-OBS-SW3 | SPU-HSR-OP0611 | The compression results are included in the HK whenever compression is started |
| SPU-OBS-SW4 | SPU-HSR-FN0020..30 | HLSW upgrades the parameters for data reduction |
| SPU-OBS-SW5 | SPU-HSR-FN0014, SPU-HSR-IF0003, SPU-HSR-IF0070 | HLSW aborts data processing whenever a stop command is received |
| SPU-OBS-SW6 | SPU-HSR-FN0015, SPU-HSR-IF0003, SPU-HSR-IF0080 | HLSW starts data processing whenever a start command is received |
| SPU-OBS-SW7 | SPU-HSR-FN0012, SPU-HSR-IF0003, SPU-HSR-IF0050 | HLSW performs the warm reset when a reset command is received |
| SPU-OBS-SW8 deleted | SPU-HSR-FN0018, SPU-HSR-IF0003, SPU-HSR-IF0040 | HLSW starts the peak-up program when a peak-up command is received |
| SPU-OBS-SW9 | SPU-HSR-OP0400, SPU-HSR-OP0500 | HLSW supports all the operating and observing modes of the PACS instrument |
| SPU-OBS-SW10 | SPU-HSR-FN0016, SPU-HSR-FN0017, SPU-HSR-IF0003, SPU-HSR-IF0090, SPU-HSR-IF0100, SPU-HSR-OP0640 | HLSW generates simulated data for test purpose, triggered by DPU command |
| SPU-OBS-SW11 | SPU-HSR-FN0007, SPU-HSR-FN0008, SPU-HSR-IF0002, SPU-HSR-IF0003, SPU-HSR-IF0020 | HLSW could dump data from RAM |
| SPU-OBS-SW12 | SPU-HSR-FN0004, SPU-HSR-FN0005, SPU-HSR-FN0006, SPU-HSR-IF0003, SPU-HSR-IF0010 | HLSW could Load data into RAM |
| SPU-OBS-SW13 | SPU-HSR-FN0009, SPU-HSR-FN0010, SPU-HSR-IF0002, SPU-HSR-IF0003, SPU-HSR-IF0030, | HLSW could check a specific RAM area |
| SPU-OBS-SW14 | SPU-HSR-FN0020..30, SPU-HSR-IF0003, SPU-HSR-IF0120 | HLSW could write detector selection tables and detector constant tables to RAM |
| SPU-OBS-SW15 deleted | SPU-HSR-FN0019, SPU-HSR-IF0003, SPU-HSR-IF0110 | HLSW performs the Bolometer Background Cancelling mode whenever a BBC command is received |
| SPU-OBS-CR1 | SPU-HSR-FN0102..105 | HLSW performs the data reduction and compression according to DEC/MEC header |
| SPU-OBS-CR2 | SPU-HSR-FN0300 | No data loss during data acquisition |
| SPU-OBS-CR3 | SPU-HSR-OP0600..04, SPU-HSR-OP0610..11, SPU-HSR-OP0620, SPU-HSR-OP0625, SPU-HSR-OP0630, SPU-HSR-OP0631, SPU-HSR-OP0632, SPU-HSR-OP0640, SPU-HSR-OP0650, SPU-HSR-OP0660..62, SPU-HSR-OP0670 | HLSW supports several compression modes |
| SPU-OBS-CR4 | SPU-HSR-IF0200..01 | Compression data is split into packets which fit into the telemetry packet |
| SPU-OBS-CR5 | SPU-HSR-IF0200..01 | Compressed data packet structure fulfil the protocol described in RD007 |
| SPU-OBS-CR6 | SPU-HSR-IF0300..04 | HLSW is able to receive data packets from DEC/MEC |
| SPU-OBS-CR7 | SPU-HSR-RS0001, SPU-HSR-RS0100 | HLSW is adapted to the SPU hardware |
| SPU-OBS-CR8 | SPU-HSR-IF0003 | HLSW acknowledges the reception of all DPU commands |
| SPU-OBS-CR9 | SPU-HSR-FN0200 | HLSW sends HK to DPU |
| SPU-OBS-CR10 | SPU-HSR-FN0200 | Regular rate for the HLSW HK transmission to DPU |
| SPU-OBS-CR11 | SPU-HSR-FN0201 | “Are You Alive” SPU is available in the HLSW HK |
| SPU-OBS-TM1 | SPU-HSR-OP0610 | HLSW supports the PACS prime mode (120 Kbits/s ) |
| SPU-OBS-TM2 | SPU-HSR-OP0660 | HLSW supports the PACS burst mode (~300 Kbits/s ) |
| SPU-OBS-TM3 | SPU-HSR-OP0620 | HLSW supports the PACS parallel mode |
| SPU-OBS-TM4 | SPU-HSR-OP0611 | The compression results are included in the HK whenever compression is started |
| SPU-OBS-TM5 | SPU-HSR-IF0200..01 | Compression data is split into packets which fit into the telemetry packet |

# Software Requirements vs. Components Traceability Matrix

| Software Requirements | Component | Description |
| --- | --- | --- |
| SPU-HSR-FN0001 | spu_io.c, watchp.c | HLSW is able to receive command packets from DPU |
| SPU-HSR-FN0002 | watchp.c | HLSW is able to identify the DPU command |
| SPU-HSR-FN0003 | watchp.c | HLSW aborts data compression if DPU command is received |
| SPU-HSR-FN0004 | watchp.c, Load.c | HLSW can load data into SPU RAM |
| SPU-HSR-FN0005 | Load.c | HLSW checks the consistency of the data before the load |
| SPU-HSR-FN0006 transfered to SPU-HSR-IF0011 | Load.c | Data load only to DRAM, Ext. DRAM and DPRAM |
| SPU-HSR-FN0007 | watchp.c, dump.c | HLSW can dump data from SPU RAM |
| SPU-HSR-FN0008 transfered to SPU-HSR-IF0021 | dump.c | Data dump only from PRAM, DRAM, Ext. DRAM and DPRAM |
| SPU-HSR-FN0009 | watchp.c, check.c | HLSW can check SPU RAM |
| SPU-HSR-FN0010 | check.c | Data check only for PRAM, DRAM, Ext. DRAM and DPRAM |
| SPU-HSR-FN0011 | watchp.c, perform.c | HLSW checks consistency of the parameter of the perform activity command |
| SPU-HSR-FN0012 | w_reset.c, fill_in.c, spu_io.c | HLSW can perform warm reset |
| SPU-HSR-FN0013 | Rc_Sel.c | HLSW can transmit data from selected channels in raw |
| SPU-HSR-FN0014 | Str_Stp.c | HLSW can abort data compression |
| SPU-HSR-FN0015 | Str_Stp.c | HLSW can start data compression |
| SPU-HSR-FN0016 | spu_tst.c, phot_gn.c, Spvs_Tst.c | HLSW can generate simulated photometry data on board for test purposes |
| SPU-HSR-FN0017 | spu_tst.c, spec_gn.c, Spvs_Tst.c | HLSW can generate simulated spectroscopy data on board for test purposes |
| SPU-HSR-FN0018 deleted | peak_up.c, pkup_pg.c, csw.c | HLSW provides an interface to the peak-up program |
| SPU-HSR-FN0019 deleted | bol_bc.c, bbc_pg.c, csw.c | HLSW provides an interface to the bolometer background cancelling program |
| SPU-HSR-FN0020 | watchp.c, write.c | HLSW checks consistency of the parameter of the write command |
| SPU-HSR-FN0021 | write.c | HLSW can load detectors table from subarray 1 in photometry |
| SPU-HSR-FN0022 | write.c | HLSW can load detectors table from subarray 2 in photometry |
| SPU-HSR-FN0023 | write.c | HLSW can load detectors table from subarray 3 in photometry |
| SPU-HSR-FN0024 | write.c | HLSW can load detectors table from subarray 4 in photometry |
| SPU-HSR-FN0025 | write.c | HLSW can load detectors table from subarray 5 in photometry |
| SPU-HSR-FN0026 | write.c | HLSW can load detectors table from subarray 1 in spectroscopy |
| SPU-HSR-FN0027 | write.c | HLSW can load detectors table from subarray 2 in spectroscopy |
| SPU-HSR-FN0028 | write.c | HLSW can load detector constants table in photometry |
| SPU-HSR-FN0029 | write.c | HLSW can load detector constants table in spectroscopy |
| SPU-HSR-FN0030 | write.c | HLSW can load simulated data table for SPU test mode |
| SPU-HSR-FN0031 | C2EEPROM.c | HLSW can copy SW code from RAM to EEPROM |
| SPU-HSR-FN0032 | DMC_Con.c, spu_io.c | HLSW connects to DEC/MEC upon DPU command |
| SPU-HSR-FN0100 | spu_io.c, supervs.c | HLSW is able to receive data packets from DPU |
| SPU-HSR-FN0101 | csw.c | HLSW can start data compression |
| SPU-HSR-FN0102 | Supervs.c | HLSW can distinguish between photometry and spectroscopy data |
| SPU-HSR-FN0103 | Supervs.c, fill_in.c | HLSW is able to buffer DEC/MEC data to memory |
| SPU-HSR-FN0104 | Supervs.c, csw.c | For real time processing procedures are implemented in HLSW to handle the buffers |
| SPU-HSR-FN0105 | csw.c, bol_ex.c, bol3.c, bol4.c, buf_bol.c, spec1_2.c, spec3.c, spec4.c, spec5.c, buf_spec.c | HLSW supports eleven compression modes |
| SPU-HSR-FN0200 | hk.c, datatx.c | HLSW send permanently HK packets to DPU |
| SPU-HSR-FN0201 | hk.c | „Are You Alive“ SPU is implemented in the HLSW HK |
| SPU-HSR-FN0202 | hk.c | EDAC check status is implemented in the HLSW HK |
| SPU-HSR-FN0203 | hk.c | Ground people are responsible for analyzing the failing memory addresses detected using EDAC check |
| SPU-HSR-FN0300 | All | HLSW fulfils real time data processing requirement |
| SPU-HSR-FN0301 | Supervs.c, integ.c | HLSW doesn’t allow science data loss |
| SPU-HSR-IF0001 | watchp.c | HLSW aborts any running activity, if DPU command is received |
| SPU-HSR-IF0002 | watchp.c, Load.c, dump.c, C2EEPROM.c, check.c, DMC_Con.c, perform.c, w_reset.c, Rc_Sel.c, Str_Stp.c, spu_tst.c, write.c, datatx.c | Maximum response time for DPU commands is 200ms |
| SPU-HSR-IF0003 | watchp.c, Load.c, dump.c, C2EEPROM.c, check.c, DMC_Con.c, perform.c, w_reset.c, Rc_Sel.c, Str_Stp.c, spu_tst.c, write.c, datatx.c | HLSW acknowledges any received DPU command according to the defined protocol |
| SPU-HSR-IF0010 | watchp.c, Load.c, datatx.c | HLSW acknowledges the execution of the load command |
| SPU-HSR-IF0011 | Load.c | Data load only to DRAM, Ext. DRAM and DPRAM |
| SPU-HSR-IF0020 | watchp.c, dump.c, datatx.c | HLSW acknowledges the execution of the dump command |
| SPU-HSR-IF0021 | dump.c | Data dump only from PRAM, DRAM, Ext. DRAM and DPRAM |
| SPU-HSR-IF0030 | watchp.c, check.c, datatx.c | HLSW acknowledges the execution of the check command |
| SPU-HSR-IF0040 deleted | watchp.c, perform.c, peak_up.c, pkup_pg.c, csw.c, datatx.c | HLSW acknowledges the reception of the peak-up command |
| SPU-HSR-IF0050 | watchp.c, perform.c, w_reset.c, datatx.c, spu_io.c | HLSW acknowledges the reception of the warm reset command |
| SPU-HSR-IF0060 | watchp.c, perform.c, Rc_Sel.c, datatx.c | HLSW acknowledges the execution of the raw channel selection command |
| SPU-HSR-IF0070 | watchp.c, perform.c, Str_Stp.c, datatx.c | HLSW acknowledges the reception of the stop command |
| SPU-HSR-IF0080 | watchp.c, perform.c, Str_Stp.c, datatx.c | HLSW acknowledges the reception of the start command |
| SPU-HSR-IF0090 | watchp.c, perform.c, spu_tst.c, phot_gn.c, Spvs_Tst.c, datatx.c | HLSW acknowledges the reception of the SPU test in photometry command |
| SPU-HSR-IF0100 | watchp.c, perform.c, spu_tst.c, spec_gn.c, Spvs_Tst.c, datatx.c | HLSW acknowledges the reception of the SPU test in spectroscopy command |
| SPU-HSR-IF0110 deleted | watchp.c, perform.c, bol_bc.c, bbc_pg.c, csw.c, datatx.c | HLSW acknowledges the reception of the Bolometer Background Cancelling command |
| SPU-HSR-IF0120 | watchp.c, write.c, datatx.c | HLSW acknowledges the execution of the write command |
| SPU-HSR-IF0130 | watchp.c, perform.c, C2EEPROM.c, datatx.c | HLSW acknowledges the reception of the Copy Data to EEPROM command |
| SPU-HSR-IF0131 | C2EEPROM.c | No HK packet are transmitted to DPU while data are copied to EEPROM |
| SPU-HSR-IF0140 | watchp.c, perform.c, DMC_Con.c, spu_io.c | HLSW acknowledges the reception of the Connect to DEC/MEC command |
| SPU-HSR-IF0200 | fill_out.c, datatx.c | HLSW is able to transmit TM packets to DPU |
| SPU-HSR-IF0201 | fill_in.c, datatx.c, spu_io.c | HLSW can buffer a maximum number of 75 TM packets |
| SPU-HSR-IF0300 | Supervs.c | HLSW doesn’t acknowledge the reception of DEC/MEC packets |
| SPU-HSR-IF0301 | Supervs.c, csw.c, hk.c | HLSW can detect some corrupted fields in the DEC/MEC packets |
| SPU-HSR-IF0302 | Supervs.c | HLSW can distinguish between photometry and spectroscopy packets |
| SPU-HSR-IF0303 | spu_io.c, hk.c | DEC/MEC link connection status is set in the HLSW HK |
| SPU-HSR-IF0304 | Supervs.c, csw.c, hk.c | DEC/MEC packet size |
| SPU-HSR-OP0001 obsolete | Supervs.c, csw.c | HLSW set the buffer granularity in spectroscopy to 8 Hz |
| SPU-HSR-OP0002 | Supervs.c, fill_in.c, csw.c | HLSW can compress a maximum buffer size of 468kB in spectroscopy |
| SPU-HSR-OP0003 | dmch_cp.c, fill_out.c, datatx.c | HLSW compresses DEC/MEC header lossless |
| SPU-HSR-OP0010 | Supervs.c | DEC/MEC header field in spectroscopy (SPUID) |
| SPU-HSR-OP0020 | Supervs.c, csw.c, hk.c | DEC/MEC header field in spectroscopy (Type) |
| SPU-HSR-OP0021 | Supervs.c | DEC/MEC header field in spectroscopy (Type) |
| SPU-HSR-OP0030 | Supervs.c | DEC/MEC header field in spectroscopy (CRDCR) |
| SPU-HSR-OP0031 | Supervs.c | DEC/MEC header field in spectroscopy (CRDCR) |
| SPU-HSR-OP0040 | Supervs.c | DEC/MEC header field in spectroscopy (RRR) |
| SPU-HSR-OP0041 | Supervs.c | DEC/MEC header field in spectroscopy (RRR) |
| SPU-HSR-OP0050 | csw.c, hk.c, spec1_2.c | DEC/MEC header field in spectroscopy (CMM) |
| SPU-HSR-OP0051 | supervs.c, csw.c, spec1_2.c, spec3.c, spec4.c, spec5.c, fill_in.c | DEC/MEC header field in spectroscopy (CMM) |
| SPU-HSR-OP0060 deleted | supervs.c, csw.c, spec1_2.c, spec3.c, spec4.c, spec5.c, fill_in.c | DEC/MEC header field in spectroscopy (OBSID) |
| SPU-HSR-OP0070 | supervs.c | DEC/MEC header field in spectroscopy (Validity) |
| SPU-HSR-OP0071 obsolete | supervs.c, integ.c | DEC/MEC header field in spectroscopy (Validity) |
| SPU-HSR-OP0072 | Supervs.c | DEC/MEC header field in spectroscopy (Validity) |
| SPU-HSR-OP0080 | Supervs.c | DEC/MEC header field in spectroscopy (CPR) |
| SPU-HSR-OP0081 obsolete | Supervs.c, integ.c | DEC/MEC header field in spectroscopy (CPR) |
| SPU-HSR-OP0082 | supervs.c, ramp_ft.c | DEC/MEC header field in spectroscopy (CPR) |
| SPU-HSR-OP0083 | supervs.c | DEC/MEC header field in spectroscopy (CPR) |
| SPU-HSR-OP0090 | supervs.c | DEC/MEC header field in spectroscopy (Label) |
| SPU-HSR-OP0091 | supervs.c, csw.c, fill_in.c | DEC/MEC header field in spectroscopy (Label) |
| SPU-HSR-OP0100 | supervs.c | DEC/MEC header field in spectroscopy (GPR) |
| SPU-HSR-OP0101 obsolete | supervs.c, integ.c | DEC/MEC header field in spectroscopy (GPR) |
| SPU-HSR-OP0102 | supervs.c | DEC/MEC header field in spectroscopy (GPR) |
| SPU-HSR-OP0110 | supervs.c, fill_out.c, datatx.c | DEC/MEC header field in spectroscopy (BBID) |
| SPU-HSR-OP0120 | supervs.c, fill_out.c, datatx.c | DEC/MEC header field in spectroscopy (Time) |
| SPU-HSR-OP0130 | supervs.c, fill_out.c, datatx.c | DEC/MEC header field in spectroscopy (WPR) |
| SPU-HSR-OP0140 | supervs.c, fill_out.c, datatx.c | DEC/MEC header field in spectroscopy (CRECR) |
| SPU-HSR-OP0200 obsolete | supervs.c, csw.c, fill_in.c | HLSW set the buffer granularity in photometry to 10 Hz in SWL and 2.5 Hz in LWL |
| SPU-HSR-OP0201 | supervs.c, csw.c, bol_ex.c, bol3.c, bol4.c, fill_in.c | HLSW can compress a maximum buffer size of 480kB in photometry |
| SPU-HSR-OP0202 | dmch_cp.c, fill_out.c, datatx.c | HLSW compresses DEC/MEC header lossless |
| SPU-HSR-OP0210 | supervs.c | DEC/MEC header field in photometry (SPUID) |
| SPU-HSR-OP0220 | supervs.c, csw.c, hk.c | DEC/MEC header field in photometry (Type) |
| SPU-HSR-OP0230 | supervs.c | DEC/MEC header field in photometry (CRDCCP) |
| SPU-HSR-OP0231 | supervs.c | DEC/MEC header field in photometry (CRDCCP) |
| SPU-HSR-OP0240 | supervs.c, fill_out.c, datatx.c | DEC/MEC header field in photometry (CRC) |
| SPU-HSR-OP0250 | csw.c, hk.c, bol_ex.c | DEC/MEC header field in photometry (CMM) |
| SPU-HSR-OP0251 | supervs.c, csw.c, bol_ex.c, bol3.c, bol4.c, fill_in.c | DEC/MEC header field in photometry (CMM) |
| SPU-HSR-OP0260 deleted | supervs.c, csw.c, bol_ex.c, bol3.c, bol4.c, fill_in.c | DEC/MEC header field in photometry (OBSID) |
| SPU-HSR-OP0270 | supervs.c | DEC/MEC header field in photometry (Validity) |
| SPU-HSR-OP0271 | average.c | DEC/MEC header field in photometry (Validity) |
| SPU-HSR-OP0272 | average.c | DEC/MEC header field in photometry (Validity) |
| SPU-HSR-OP0280 | integ.c | DEC/MEC header field in photometry (CPR) |
| SPU-HSR-OP0281 | supervs.c | DEC/MEC header field in photometry (CPR) |
| SPU-HSR-OP0290 | supervs.c | DEC/MEC header field in photometry (Label) |
| SPU-HSR-OP0291 | supervs.c, csw.c, bol_ex.c, bol3.c, bol4.c, fill_in.c | DEC/MEC header field in photometry (Label) |
| SPU-HSR-OP0300 | supervs.c | DEC/MEC header field in photometry (DBID) |
| SPU-HSR-OP0310 | supervs.c, fill_out.c, datatx.c | DEC/MEC header field in photometry (BBID) |
| SPU-HSR-OP0320 | supervs.c, fill_out.c, datatx.c | DEC/MEC header field in photometry (Time) |
| SPU-HSR-OP0330 | supervs.c, fill_out.c, datatx.c | DEC/MEC header field in photometry (WPR) |
| SPU-HSR-OP0340 | supervs.c, fill_out.c, datatx.c | DEC/MEC header field in photometry (BSID) |
| SPU-HSR-OP0400 | supervs.c, csw.c, hk.c | HLSW supports PACS operating modes |
| SPU-HSR-OP0401 | supervs.c | Flexibility of the HLSW in science data compression |
| SPU-HSR-OP0402 | none (see RD009) | mode parameters are not sent within DEC/MEC data |
| SPU-HSR-OP0500 | supervs.c, csw.c | HLSW supports PACS observing modes |
| SPU-HSR-OP0501 | none (see RD009) | mode parameters are not sent within DEC/MEC data |
| SPU-HSR-OP0600 | dxs.c, llc.c, fill_out.c, datatx.c, Rc_Sel.c | Raw data from selected channels can be sent if required |
| SPU-HSR-OP0601 | dmch_cp.c, fill_out.c, datatx.c | DEC/MEC header is compressed lossless apart in the buffer transmission mode |
| SPU-HSR-OP0602 | hk.c, fill_out.c, ramp_ft.c, average.c | Specified parameters are included in the HLSW HK |
| SPU-HSR-OP0603 | supervs.c, spuasw.h, fill_out.c | Nominal compressed entity time interval is 12s for LWL and 3s for SWL in photometry |
| SPU-HSR-OP0604 | supervs.c, spuasw.h, fill_out.c | Nominal compressed entity time interval is 2s for LWL and SWL in spectroscopy |
| SPU-HSR-OP0610 | csw.c, bol_ex.c, spec1_2.c | HLSW supports the PACS prime mode |
| SPU-HSR-OP0611 | hk.c, fill_out.c | Compression results are included in the HLSW HK |
| SPU-HSR-OP0620 | csw.c, bol_ex.c, spec1_2.c | HLSW supports the PACS parallel mode |
| SPU-HSR-OP0625 | csw.c, bol_ex.c | HLSW supports the PACS prime mode |
| SPU-HSR-OP0630 | csw.c, bol3.c, spec3.c, dxs.c | HLSW can compress data from selected detectors lossless |
| SPU-HSR-OP0631 | csw.c, bol3.c, spec3.c, dxs.c, T_S_Red.c | HLSW can compress data from selected detectors lossless |
| SPU-HSR-OP0632 | csw.c, bol3.c, spec3.c, dxs.c, T_S_Red.c | HLSW can compress data from selected detectors lossless |
| SPU-HSR-OP0640 | Spvs_Test.c, spu_tst.c, csw.c, phot_gn.c, spec_gn.c | HLSW supports SPU test mode |
| SPU-HSR-OP0650 | csw.c, bol4.c, spec4.c | HLSW can transmit data from selected detectors without compression |
| SPU-HSR-OP0660 | csw.c, buf_bol.c, buf_spec.c, fill_out.c | HLSW supports buffer transmission mode |
| SPU-HSR-OP0661 | supervs.c, csw.c | HLSW should be in stopped compression mode before running the buffer transmission mode |
| SPU-HSR-OP0670 | csw.c, spec5.c, spec1_2.c | HLSW splits 4s ramp in two 2s ramps |
| SPU-HSR-RS0001 | All | memory processing |
| SPU-HSR-RS0100 | All | processing capacity |
| SPU-HSR-VF0001 | All | SW acceptance verification |
| SPU-HSR-VF0002 | All (+ decompression SW components) | ensure compression/decompression yields to orig. data |
| SPU-HSR-VF0003 | All | ensure fully execution of algorithm logic by test data |
| SPU-HSR-AT0001 | All | test cases for acceptance tests |
| SPU-HSR-DO0001 | All | SDD replaces ADD, DDD and SRD |
| SPU-HSR-PT0001 | All | Compiler G21K, Processor ADSP 21020, Communication Chip SMC S332, Operating System VirtuosoTM |
| SPU-HSR-QA0001 | All | HLSW development complies with the QA plan |
| SPU-HSR-QA0002 | All | HLSW source code is commented |
| SPU-HSR-QA0100 | watchp.c | handle anomalies with respect to command execution |
| SPU-HSR-QA0101 | All | SW design to avoid flaws |
| SPU-HSR-QA0102 | All | mechanisms to protect data and resources |
| SPU-HSR-QA0103 | spu_io.c, supervs.c, fill_in.c, hk.c | handle RAM and EEPROM SEU |
| SPU-HSR-QA0104 | supervs.c | handle corrupt and incomplete DEC/MEC data |
| SPU-HSR-QA0105 | asmlib.s | detect and handle arithmetic errors |
| SPU-HSR-QA0106 | llc.c | not lead to buffer overflow/underrun |
| SPU-HSR-QA0200 | All (+ documentation) | maintainable to later extend |
| SPU-HSR-QA0201 | All (+ documentation) | error detection and fault repair |
| SPU-HSR-QA0202 | make.bat (in CVS: / obsw/ spu/ tools/ compilation) | deliverable scripts for SW build |
| SPU-HSR-QA0203 | files in CVS: / obsw/ spu/ tools | SDE includes SW licences and tools |
| SPU-HSR-QA0204 | HLSW.MAP (in CVS: / obsw/ spu/ tools/ compilation) | detailed map for SW deliveries |
| SPU-HSR-QA0205 | files in CVS: / obsw/ spu/ tools | documentation of in-house tools |
| SPU-HSR-QA0206 | see http://pacs.ster.kuleuven.ac.be/ shall and http://cvs.ster.kuleuven.be/ | use of SPR/SCR and CVS management |
| SPU-HSR-SA0001 | All | order of commands, HK and telemetry |
| SPU-HSR-SA0010 | hk.c | HK provide detailed SPU status |
| SPU-HSR-SA0011 | hk.c, spu_io.c, fill_in.c | Memory failure detection |
| SPU-HSR-SA0012 | hk.c | DEC/MEC Header Errors |

# Software Requirements vs. Software Verification & Validation Traceability Matrix

| Software Requirements | Verification Activity in RD017 | Description |
| --- | --- | --- |
| SPU-HSR-FN0001 | Proc. 3.4.4.1 – 15 | HLSW is able to receive command packets from DPU |
| SPU-HSR-FN0002 | Proc. 3.4.4.1 – 15 | HLSW is able to identify the DPU command |
| SPU-HSR-FN0003 | Proc. 3.5.4.1 – 6 (spec) Proc. 3.6.4.1 – 6 (phot) | HLSW aborts data compression if DPU command is received |
| SPU-HSR-FN0004 | Proc. 3.4.4.1 | HLSW can load data into SPU RAM |
| SPU-HSR-FN0005 | Proc. 3.4.4.1 | HLSW checks the consistency of the data before the load |
| SPU-HSR-FN0006 transfered to SPU-HSR-IF0011 | Proc. 3.4.4.1 | Data load only to DRAM, Ext. DRAM and DPRAM |
| SPU-HSR-FN0007 | Proc. 3.4.4.2 | HLSW can dump data from SPU RAM |
| SPU-HSR-FN0008 transfered to SPU-HSR-IF0021 | Proc. 3.4.4.2 | Data dump only from PRAM, DRAM, Ext. DRAM and DPRAM |
| SPU-HSR-FN0009 | Proc. 3.4.4.3 | HLSW can check SPU RAM |
| SPU-HSR-FN0010 | Proc. 3.4.4.3 | Data check only for PRAM, DRAM, Ext. DRAM and DPRAM |
| SPU-HSR-FN0011 | Proc. 3.4.4.4 – 15 | HLSW checks consistency of the parameter of the perform activity command |
| SPU-HSR-FN0012 | Proc. 3.4.4.4 | HLSW can perform warm reset |
| SPU-HSR-FN0013 | Proc. 3.5.4.7 – 16 (spec) Proc. 3.6.4.7 – 28 (phot) | HLSW can transmit data from selected channels in raw |
| SPU-HSR-FN0014 | Proc. 3.4.4.6 – 8 (sim), Proc. 3.4.4.9 – 11 (sim) Proc. 3.5.4.1 – 4 & 6 (spec) Proc. 3.6.4.1 – 4 & 6 (phot) | HLSW can abort data compression |
| SPU-HSR-FN0015 | Proc. 3.5.4.1 – 2 (spec) Proc. 3.6.4.1 – 2 (phot) | HLSW can start data compression |
| SPU-HSR-FN0016 | Proc. 3.4.4.9 – 10 | HLSW can generate simulated photometry data on board for test purposes |
| SPU-HSR-FN0017 | Proc. 3.4.4.6 – 7 | HLSW can generate simulated spectroscopy data on board for test purposes |
| SPU-HSR-FN0018 deleted | N/A | HLSW provides an interface to the peak-up program |
| SPU-HSR-FN0019 deleted | N/A | HLSW provides an interface to the bolometer background cancelling program |
| SPU-HSR-FN0020 | Proc. 3.4.4.6, Proc. 3.4.4.9 | HLSW checks consistency of the parameter of the write command |
| SPU-HSR-FN0021 | Proc. 3.6.4.7 – 10 | HLSW can load detectors table from subarray 1 in photometry |
| SPU-HSR-FN0022 | Proc. 3.6.4.11 – 14 | HLSW can load detectors table from subarray 2 in photometry |
| SPU-HSR-FN0023 | Proc. 3.6.4.15 – 18 | HLSW can load detectors table from subarray 3 in photometry |
| SPU-HSR-FN0024 | Proc. 3.6.4.19 – 22 | HLSW can load detectors table from subarray 4 in photometry |
| SPU-HSR-FN0025 | Proc. 3.6.4.23 – 26 | HLSW can load detectors table from subarray 5 in photometry |
| SPU-HSR-FN0026 | Proc. 3.5.4.7 – 10 | HLSW can load detectors table from subarray 1 in spectroscopy |
| SPU-HSR-FN0027 | Proc. 3.6.4.11 – 14 | HLSW can load detectors table from subarray 2 in spectroscopy |
| SPU-HSR-FN0028 | Proc. 3.4.4.13 | HLSW can load detector constants table in photometry |
| SPU-HSR-FN0029 | Proc. 3.4.4.12 | HLSW can load detector constants table in spectroscopy |
| SPU-HSR-FN0030 | Proc. 3.4.4.6 (spec) Proc. 3.4.4.9 (phot) | HLSW can load simulated data table for SPU test mode |
| SPU-HSR-FN0031 | Proc. 3.4.4.12 | HLSW can copy SW code from RAM to EEPROM |
| SPU-HSR-FN0032 | Proc. 3.2 (item 16) | HLSW connects to DEC/MEC upon DPU command |
| SPU-HSR-FN0100 | Proc. 3.5.4.1 – 2 (spec) Proc. 3.6.4.1 – 2 (phot) | HLSW is able to receive data packets from DMC |
| SPU-HSR-FN0101 | Proc. 3.5.4.1 – 6 (spec) Proc. 3.6.4.1 – 6 (phot) | HLSW can start data compression |
| SPU-HSR-FN0102 | Proc. 3.5.4.1 – 2 (spec) Proc. 3.6.4.1 – 2 (phot) | HLSW can distinguish between photometry and spectroscopy data |
| SPU-HSR-FN0103 | Proc. 3.5.4.18 – 20 (spec) Proc. 3.6.4.30 – 32 (phot) | HLSW is able to buffer DEC/MEC data to memory |
| SPU-HSR-FN0104 | Proc. 3.5.4.1 – 6 (spec) Proc. 3.6.4.1 – 6 (phot) | For real time processing procedures are implemented in HLSW to handle the buffers |
| SPU-HSR-FN0105 | Proc. 3.5.4.1 – 23 (spec) Proc. 3.6.4.1 – 35 (phot) | HLSW supports eleven compression modes |
| SPU-HSR-FN0200 | Proc. 3.5.4.1 – 6 (spec) Proc. 3.6.4.1 – 6 (phot) | HLSW send permanently HK packets to DPU |
| SPU-HSR-FN0201 | Proc. 3.5.4.1 – 6 (spec) => HK analysis Proc. 3.6.4.1 – 6 (phot) => HK analysis | „Are You Alive“ SPU is implemented in the HLSW HK |
| SPU-HSR-FN0202 | Proc. 3.5.4.1 – 6 (spec) => HK analysis Proc. 3.6.4.1 – 6 (phot) => HK analysis | EDAC check status is implemented in the HLSW HK |
| SPU-HSR-FN0203 | Proc. 3.5.4.1 – 6 (spec) => HK analysis Proc. 3.6.4.1 – 6 (phot) => HK analysis | Ground people are responsible for analyzing the failing memory addresses detected using EDAC check |
| SPU-HSR-FN0300 | Proc. 3.5.4.1 – 6 (spec) Proc. 3.6.4.1 – 6 (phot) | HLSW fulfils real time data processing requirement |
| SPU-HSR-FN0301 | Proc. 3.5.4.1 – 6 (spec) => TM Packet analysis Proc. 3.6.4.1 – 6 (phot) => TM Packet analysis | HLSW doesn’t allow science data loss |
| SPU-HSR-IF0001 | Proc. 3.5.4.1 – 6 (spec) Proc. 3.6.4.1 – 6 (phot) | HLSW aborts any running activity, if DPU command is received |
| SPU-HSR-IF0002 | Proc. 3.4.4.1 – 15 | Maximum response time for DPU commands is 200ms |
| SPU-HSR-IF0003 | Proc. 3.4.4.1 – 15 | HLSW acknowledges any received DPU command according to the defined protocol |
| SPU-HSR-IF0010 | Proc. 3.4.4.1 | HLSW acknowledges the execution of the load command |
| SPU-HSR-IF0011 | Proc. 3.4.4.1 | Data load only to DRAM, Ext. DRAM and DPRAM |
| SPU-HSR-IF0020 | Proc. 3.4.4.2 | HLSW acknowledges the execution of the dump command |
| SPU-HSR-IF0021 | Proc. 3.4.4.2 | Data dump only from PRAM, DRAM, Ext. DRAM and DPRAM |
| SPU-HSR-IF0030 | Proc. 3.4.4.3 | HLSW acknowledges the execution of the check command |
| SPU-HSR-IF0040 deleted | N/A | HLSW acknowledges the reception of the peak-up command |
| SPU-HSR-IF0050 | Proc. 3.4.4.4 | HLSW acknowledges the reception of the warm reset command |
| SPU-HSR-IF0060 | Proc. 3.4.4.5 | HLSW acknowledges the execution of the raw channel selection command |
| SPU-HSR-IF0070 | Proc. 3.4.4.8, Proc. 3.4.4.11 | HLSW acknowledges the reception of the stop command |
| SPU-HSR-IF0080 | Proc. 3.5.4.2 (spec) Proc. 3.6.4.2 (phot) | HLSW acknowledges the reception of the start command |
| SPU-HSR-IF0090 | Proc. 3.4.4.10 | HLSW acknowledges the reception of the SPU test in photometry command |
| SPU-HSR-IF0100 | Proc. 3.4.4.7 | HLSW acknowledges the reception of the SPU test in spectroscopy command |
| SPU-HSR-IF0110 deleted | N/A | HLSW acknowledges the reception of the Bolometer Background Cancelling command |
| SPU-HSR-IF0120 | Proc. 3.4.4.6, Proc. 3.4.4.9 | HLSW acknowledges the execution of the write command |
| SPU-HSR-IF0130 | Proc. 3.4.4.12 | HLSW acknowledges the reception of the Copy Data to EEPROM command |
| SPU-HSR-IF0131 | Proc. 3.4.4.12 | No HK packet are transmitted to DPU while data are copied to EEPROM |
| SPU-HSR-IF0140 | Proc. 3.2 (item 16) | HLSW acknowledges the reception of the Connect to DEC/MEC command |
| SPU-HSR-IF0200 | Proc. 3.4.4.6 / 7 (sim), Proc. 3.4.4.9 / 10 (sim) Proc. 3.5.4.1 – 2 (spec) Proc. 3.6.4.1 – 2 (phot) | HLSW is able to transmit TM packets to DPU |
| SPU-HSR-IF0201 | Proc. 3.5.4.1 – 6 (spec) => TM Packet analysis Proc. 3.6.4.1 – 6 (phot) => TM Packet analysis | HLSW can buffer a maximum number of 75 TM packets |
| SPU-HSR-IF0300 | Proc. 3.5.4.1 – 6 (spec) Proc. 3.6.4.1 – 6 (phot) | HLSW doesn’t acknowledge the reception of DEC/MEC packets |
| SPU-HSR-IF0301 | Proc. 3.5.4.1 – 6 (spec) => HK analysis Proc. 3.6.4.1 – 6 (phot) => HK analysis | HLSW can detect some corrupted fields in the DEC/MEC packets |
| SPU-HSR-IF0302 | Proc. 3.5.4.1 – 6 (spec) Proc. 3.6.4.1 – 6 (phot) | HLSW can distinguish between photometry and spectroscopy packets |
| SPU-HSR-IF0303 | Proc. 3.5.4.1 – 6 (spec) => HK analysis Proc. 3.6.4.1 – 6 (phot) => HK analysis | DEC/MEC link connection status is set in the HLSW HK |
| SPU-HSR-IF0304 | Proc. 3.5.4.1 – 6 (spec) => HK analysis Proc. 3.6.4.1 – 6 (phot) => HK analysis | DEC/MEC packet size |
| SPU-HSR-OP0001 | Proc. 3.5.4.1 – 6 => TM analysis | HLSW set the buffer granularity in spectroscopy to 8 Hz |
| SPU-HSR-OP0002 | Proc. 3.5.4.1 – 6 => TM analysis | HLSW can compress a maximum buffer size of 468kB in spectroscopy |
| SPU-HSR-OP0003 | Proc. 3.5.4.1 – 6 => TM analysis | HLSW compresses DEC/MEC header lossless |
| SPU-HSR-OP0010 | is not taken into account by HLSW | DEC/MEC header field in spectroscopy (SPUID) |
| SPU-HSR-OP0020 | Verifiable by code inspection | DEC/MEC header field in spectroscopy (Type) |
| SPU-HSR-OP0021 | Proc. 3.5.4.1 – 6 => TM analysis | DEC/MEC header field in spectroscopy (Type) |
| SPU-HSR-OP0030 | Proc. 3.5.4.1 – 6 => TM analysis | DEC/MEC header field in spectroscopy (CRDCR) |
| SPU-HSR-OP0031 | Proc. 3.5.4.1 – 6 => TM analysis | DEC/MEC header field in spectroscopy (CRDCR) |
| SPU-HSR-OP0040 | Proc. 3.5.4.1 – 6 => TM analysis | DEC/MEC header field in spectroscopy (RRR) |
| SPU-HSR-OP0041 | Proc. 3.5.4.1 – 6 => TM analysis | DEC/MEC header field in spectroscopy (RRR) |
| SPU-HSR-OP0050 | Proc. 3.5.4.1 – 65 | DEC/MEC header field in spectroscopy (CMM) |
| SPU-HSR-OP0051 | Proc. 3.5.4.1 – 6 => TM analysis | DEC/MEC header field in spectroscopy (CMM) |
| SPU-HSR-OP0060 deleted | Proc. 3.5.4.1 – 6 | DEC/MEC header field in spectroscopy (OBSID) |
| SPU-HSR-OP0070 | Proc. 3.5.4.1 – 6 => TM analysis | DEC/MEC header field in spectroscopy (Validity) |
| SPU-HSR-OP0071 | Proc. 3.5.4.1 – 6 => TM analysis | DEC/MEC header field in spectroscopy (Validity) |
| SPU-HSR-OP0072 | Proc. 3.5.4.1 – 6 => TM analysis | DEC/MEC header field in spectroscopy (Validity) |
| SPU-HSR-OP0080 | Proc. 3.5.4.1 – 6 => TM analysis | DEC/MEC header field in spectroscopy (CPR) |
| SPU-HSR-OP0081 | Proc. 3.5.4.1 – 6 => TM analysis | DEC/MEC header field in spectroscopy (CPR) |
| SPU-HSR-OP0082 | Proc. 3.5.4.1 – 6 => TM analysis | DEC/MEC header field in spectroscopy (CPR) |
| SPU-HSR-OP0083 | Proc. 3.5.4.1 – 6 => TM analysis | DEC/MEC header field in spectroscopy (CPR) |
| SPU-HSR-OP0090 | Proc. 3.5.4.1 – 6 => TM analysis | DEC/MEC header field in spectroscopy (Label) |
| SPU-HSR-OP0091 | Proc. 3.5.4.1 – 6 => TM analysis | DEC/MEC header field in spectroscopy (Label) |
| SPU-HSR-OP0100 | Proc. 3.5.4.1 – 6 => TM analysis | DEC/MEC header field in spectroscopy (GPR) |
| SPU-HSR-OP0101 | Proc. 3.5.4.1 – 6 => TM analysis | DEC/MEC header field in spectroscopy (GPR) |
| SPU-HSR-OP0102 | Proc. 3.5.4.1 – 6 => TM analysis | DEC/MEC header field in spectroscopy (GPR) |
| SPU-HSR-OP0110 | is not taken into account by HLSW | DEC/MEC header field in spectroscopy (BBID) |
| SPU-HSR-OP0120 | is not taken into account by HLSW | DEC/MEC header field in spectroscopy (Time) |
| SPU-HSR-OP0130 | is not taken into account by HLSW | DEC/MEC header field in spectroscopy (WPR) |
| SPU-HSR-OP0140 | is not taken into account by HLSW | DEC/MEC header field in spectroscopy (CRECR) |
| SPU-HSR-OP0200 | Proc. 3.6.4.1 – 6 => TM analysis | HLSW set the buffer granularity in photometry to 10 Hz in SWL and 2.5 Hz in LWL |
| SPU-HSR-OP0201 | Proc. 3.6.4.1 – 6 => TM analysis | HLSW can compress a maximum buffer size of 480kB in photometry |
| SPU-HSR-OP0202 | Proc. 3.6.4.1 – 6 => TM analysis | HLSW compresses DEC/MEC header lossless |
| SPU-HSR-OP0210 | is not taken into account by HLSW | DEC/MEC header field in photometry (SPUID) |
| SPU-HSR-OP0220 | Proc. 3.6.4.1 – 6 => TM analysis | DEC/MEC header field in photometry (Type) |
| SPU-HSR-OP0230 | Proc. 3.6.4.1 – 6 => TM analysis | DEC/MEC header field in photometry (CRDCCP) |
| SPU-HSR-OP0231 | Proc. 3.6.4.1 – 6 => TM analysis | DEC/MEC header field in photometry (CRDCCP) |
| SPU-HSR-OP0240 | is not taken into account by HLSW | DEC/MEC header field in photometry (CRC) |
| SPU-HSR-OP0250 | Proc. 3.6.4.1 – 6 | DEC/MEC header field in photometry (CMM) |
| SPU-HSR-OP0251 | Proc. 3.6.4.1 – 6 => TM analysis | DEC/MEC header field in photometry (CMM) |
| SPU-HSR-OP0260 deleted | Proc. 3.6.4.1 – 6 | DEC/MEC header field in photometry (OBSID) |
| SPU-HSR-OP0270 | Proc. 3.6.4.1 – 6 => TM analysis | DEC/MEC header field in photometry (Validity) |
| SPU-HSR-OP0271 | Proc. 3.6.4.1 – 6 => TM analysis | DEC/MEC header field in photometry (Validity) |
| SPU-HSR-OP0272 | Proc. 3.6.4.1 – 6 => TM analysis | DEC/MEC header field in photometry (Validity) |
| SPU-HSR-OP0280 | Proc. 3.6.4.1 – 6 => TM analysis | DEC/MEC header field in photometry (CPR) |
| SPU-HSR-OP0281 | Proc. 3.6.4.1 – 6 => TM analysis | DEC/MEC header field in photometry (CPR) |
| SPU-HSR-OP0290 | Proc. 3.6.4.1 – 5 => TM analysis | DEC/MEC header field in photometry (Label) |
| SPU-HSR-OP0291 | Proc. 3.6.4.1 – 5 => TM analysis | DEC/MEC header field in photometry (Label) |
| SPU-HSR-OP0300 | is not taken into account by HLSW | DEC/MEC header field in photometry (DBID) |
| SPU-HSR-OP0310 | is not taken into account by HLSW | DEC/MEC header field in photometry (BBID) |
| SPU-HSR-OP0320 | is not taken into account by HLSW | DEC/MEC header field in photometry (Time) |
| SPU-HSR-OP0330 | is not taken into account by HLSW | DEC/MEC header field in photometry (WPR) |
| SPU-HSR-OP0340 | is not taken into account by HLSW | DEC/MEC header field in photometry (BSID) |
| SPU-HSR-OP0400 | 3.5.4.1 – 32 (spec) 3.6.4.1 – 41 (phot) | HLSW supports PACS operating modes |
| SPU-HSR-OP0401 | 3.5.4.1 – 32 (spec) 3.6.4.1 – 41 (phot) | Flexibility of the HLSW in science data compression |
| SPU-HSR-OP0402 | is not taken into account by HLSW | mode parameters are not sent within DEC/MEC data |
| SPU-HSR-OP0500 | 3.5.4.1 – 32 (spec) 3.6.4.1 – 41 (phot) | HLSW supports PACS observing modes |
| SPU-HSR-OP0501 | is not taken into account by HLSW | mode parameters are not sent within DEC/MEC data |
| SPU-HSR-OP0600 | Proc. 3.5.4.1 – 2 (spec) Proc. 3.6.4.1 – 2 (phot) | Raw data from selected channels can be sent if required |
| SPU-HSR-OP0601 | Proc. 3.5.4.1 – 32 (spec) => TM analysis Proc. 3.6.4.1 – 41 (phot) => TM analysis | DEC/MEC header is compressed lossless apart in the buffer transmission mode |
| SPU-HSR-OP0602 | Proc. 3.5.4.1 – 32 (spec) => HK analysis Proc. 3.6.4.1 – 41 (phot) => HK analysis | Specified parameters are included in the HLSW HK |
| SPU-HSR-OP0603 | Proc. 3.6.4.1 – 32 => TM analysis | Nominal compressed entity time interval is 12s for LWL and 3s for SWL in photometry |
| SPU-HSR-OP0604 | Proc. 3.5.4.1 – 41 => TM analysis | Nominal compressed entity time interval is 2s for LWL and SWL in spectroscopy |
| SPU-HSR-OP0610 | Proc. 3.5.4.1 – 2 (spec) Proc. 3.6.4.1 – 2 (phot) | HLSW supports the PACS prime mode |
| SPU-HSR-OP0611 | Proc. 3.5.4.1 – 32 (spec) => HK analysis Proc. 3.6.4.1 – 41 (phot) => HK analysis | Compression results are included in the HLSW HK |
| SPU-HSR-OP0620 | Proc. 3.5.4.1 – 2 (spec) Proc. 3.6.4.1 – 2 (phot) | HLSW supports the PACS parallel mode |
| SPU-HSR-OP0625 | Proc. 3.5.4.1 – 32 (spec) Proc. 3.6.4.1 – 41 (phot) | HLSW supports the PACS prime mode |
| SPU-HSR-OP0630 | Proc. 3.5.4.7 – 10 (spec) Proc. 3.6.4.7 – 10 (phot) | HLSW can compress data from selected detectors lossless |
| SPU-HSR-OP0631 | Proc. 3.5.4.7 – 16 (spec) Proc. 3.6.4.7 – 28 (phot) | HLSW can compress data from selected detectors lossless |
| SPU-HSR-OP0632 | Proc. 3.5.4.7 – 10 (spec) Proc. 3.6.4.7 – 10 (phot) | HLSW can compress data from selected detectors lossless |
| SPU-HSR-OP0640 | Proc. 3.4.4.6 – 7 (sim spec) Proc. 3.4.4.9 – 10 (sim phot) | HLSW supports SPU test mode |
| SPU-HSR-OP0650 | Proc. 3.5.4.11 – 17 (spec) Proc. 3.6.4.23 – 29 (phot) | HLSW can transmit data from selected detectors without compression |
| SPU-HSR-OP0660 | Proc. 3.5.4.11 – 20 (spec) Proc. 3.6.4.23 – 32 (phot) | HLSW supports buffer transmission mode |
| SPU-HSR-OP0661 | Proc. 3.5.4.11 – 20 (spec) Proc. 3.6.4.23 – 32 (phot) | HLSW should be in stopped compression mode before running the buffer transmission mode |
| SPU-HSR-OP0670 | Proc. 3.5.4.21 – 23 (spec) | HLSW splits 4s ramp in two 2s ramps |
| SPU-HSR-RS0001 | Proc. 3.5.4.1 – 32 (spec) => TM/HK analysis Proc. 3.6.4.1 – 41 (phot) => TM/HK analysis | 20% more memory capacity |
| SPU-HSR-RS0100 | Proc. 3.5.4.1 – 32 (spec) => TM/HK analysis Proc. 3.6.4.1 – 41 (phot) => TM/HK analysis | 20% spare processing capacity |
| SPU-HSR-VF0001 | All | SW acceptance verification |
| SPU-HSR-VF0002 | All (+ PCSS test harness) | ensure compression/decompression yields to orig. data |
| SPU-HSR-VF0003 | All | ensure fully execution of algorithm logic by test data |
| SPU-HSR-AT0001 | All | test cases for acceptance tests |
| SPU-HSR-DO0001 | see RD001 | SSD replaces ADD, DDD and SRD |
| SPU-HSR-PT0001 | see RD016 | Compiler G21K, Processor ADSP 21020, Communication Chip SMC S332, Operating System VirtuosoTM |
| SPU-HSR-QA0001 | Verifiable by code inspection | HLSW development complies with the QA plan |
| SPU-HSR-QA0002 | Verifiable by code inspection | HLSW source code is commented |
| SPU-HSR-QA0100 | Proc. 3.5.4.1 – 6 (spec) Proc. 3.6.4.1 – 6 (phot) | handle anomalies with respect to command execution |
| SPU-HSR-QA0101 | All | SW design to avoid flaws |
| SPU-HSR-QA0102 | All | mechanisms to protect data and resources |
| SPU-HSR-QA0103 | Verifiable by code inspection | handle RAM and EEPROM SEU |
| SPU-HSR-QA0104 | Proc. 3.5.4.1 – 32 (spec) => TM/HK analysis Proc. 3.6.4.1 – 41 (phot) => TM/HK analysis | handle corrupt and incomplete DEC/MEC data |
| SPU-HSR-QA0105 | Verifiable by code inspection | detect and handle arithmetic errors |
| SPU-HSR-QA0106 | Verifiable by code inspection | not lead to buffer overflow/underrun |
| SPU-HSR-QA0200 | Verifiable by code inspection (+ see RD016) | maintainable to later extend |
| SPU-HSR-QA0201 | Verifiable by code inspection (+ see RD016) | error detection and fault repair |
| SPU-HSR-QA0202 | N/A | deliverable scripts for SW build |
| SPU-HSR-QA0203 | N/A | SDE includes SW licences and tools |
| SPU-HSR-QA0204 | N/A | detailed map for SW deliveries |
| SPU-HSR-QA0205 | N/A | documentation of in-house tools |
| SPU-HSR-QA0206 | N/A | use of SPR/SCR and CVS management |
| SPU-HSR-SA0001 | Verifiable by code inspection (+ see RD016) | order of commands, HK and telemetry |
| SPU-HSR-SA0010 | Proc. 3.5.4.1 – 32 (spec) => TM/HK analysis Proc. 3.6.4.1 – 41 (phot) => TM/HK analysis | HK provide detailed SPU status |
| SPU-HSR-SA0011 | Proc. 3.5.4.1 – 32 (spec) => TM/HK analysis Proc. 3.6.4.1 – 41 (phot) => TM/HK analysis | Memory failure detection |
| SPU-HSR-SA0012 | Proc. 3.5.4.1 – 32 (spec) => TM/HK analysis Proc. 3.6.4.1 – 41 (phot) => TM/HK analysis | DEC/MEC Header Errors |

Note: 	N/A indicates that this requirements could not be tested or visualised at SVV level (HK, TM or code insepction) or belongs to SW management or deleted SW tasks.

# Appendices

Appendix A:
LLC Algorithms

## A.1 Currently implemented Algorithms

## A.1.1 Lossless DEC/MEC Header Compression

The actually implemented algorithms in SPU HLSW version 13.8 are:

- D_S_TRR

- ZRS

- RZIP

- RZIP2

See Appendix A.2 for more detail. These algorithms have been tested for the worst case with several variations in the DEC/MEC header. The maximum compressed header size will not exceed 0.5 Kbytes.

## A.1.2 Lossless Science Data Compression

The actually implemented lossless compression algorithms in SPU HLSW version 13.8 are:

- Photometry

  - Temporal and Spatial redundancy Reduction

  - VBWL encoder

  - FM Arithmetic Coding

- Specstropcopy

  - Data Sorting and Spatial Redundancy Reduction

  - pacs_codec

  - RZIP (with range 3)

  - Temporal Redundancy Reduction

  - Rampdiff

  - FM Arithmetic Coding

See Appendix A.2 for more details.

## A.1.3 Raw Channel Data Compression

The actually implemented Raw Channel compression algorithms in SPU HLSW version 13.8 are:

- Photometry

  - D_S_TRR

  - RZIP (with range 7)

  - RZIP (with range 6)

  - RZIP (with range 4)

- Specstropcopy

  - Data Sorting and Spatial Redundancy Reduction

  - RZIP (with range 3)

See Appendix A.2 for more details.

## A.2. Library of LLC Algorithms

## A.2.1 List of Available Algorithms

The following table shows a summary of possible LLC algorithms.

| Name of Algorithm | Description | Implemented in HLSW v13.8 |
| --- | --- | --- |
| Dynamic and Static Temporal Redundancy Reduction (D_S_TRR) | see section A.2.2 | ( |
| Simple Zero Repetition Suppression (ZRS) | see section A.2.3 | ( |
| RZIP/RZIP2 | see section A.2.4 | ( |
| Arithmetic Coding (ARC) | see section A.2.5 | ( |
| Data Resorting (Reorder) | see section A.2.6 | ( |
| PACS Codec (new_srt) | see section A.2.7 | ( |
| FM Aritmetic Compression | see section A.2.8 | ( |
| VBWL_short | see section A.2.9 | ( |

Table 13. List of available LLC algorithms.

## A.2.2 Dynamic and Static Temporal Redundancy Reduction (D_S_TRR)

We consider 512 frames whereas each contains 13 words of data (DMCH). Then the algorithm of the DTRR is as follows:

Frame001 is not changed

Frame002new = Frame001 – Frame002

Frame003new = Frame002 – Frame003

Frame004new = Frame003 – Frame004

…

Frame512new = Frame511 – Frame512

In the next step the STRR algorithm is done:

Frame001 is not changed

Frame002new = Frame001 – Frame002

Frame003newnew = Frame002new – Frame003new

Frame004newnew = Frame002new – Frame004new

…

Frame512newnew = Frame002new – Frame512new

## A.2.3 Simple Zero Repetition Suppression (ZRS)

ZRS is a small algorithm to quickly get rid of buffers with many zeroes. It simply ignores zeroes by encoding non-zero symbols and their relative position in the original buffer - or, in other words, the number of zeroes between the symbol and the one that was encoded before.

A symbol sequence of

A 0 B 0 0 0 0 0 0 0 C 0 0 0 A

Is encoded to

A 0 B 1 C 7 A 3

Note that the first symbol’s position information is always 0. Another thing is that a buffer, which does not at least contain as many 0s as other symbols, is not compressed but expanded.

## A.2.4 RZIP/RZIP2

Rzip is a simple lexicographic compression algorithm written for PACS OBSW DMC header compression (see RD018). The goal is to achieve maximum compression with a minimum of processing power on a 32-Bit big endian DSP. Though its power lies within iteration, it is considerably faster than conventional lz-based algorithms and much more efficient than encoders using DPCM and VBWL.

Let SOURCE be a buffer of data to compress with a size of SSIZE.

Let DEST be the destination buffer where the compressed data will be put.

Let ALPHA be a working buffer of SSIZE (it could be SSIZE bits, but this would be slow).

SYMBOLSIZE is a parameter, which determines the number of bits to use for the symbols.

RANGEWIDTH is a parameter, which determines the number of bits to use for encoding ranges.

A width of 3 means that the RANGE will be 7 (23-1).

Let the SYMBOLSIZE be 32bit. Let our SSIZE be 128 Bytes. Hence the SOURCE consists of 128*8/32 symbols. Add the necessary empty bits to the buffer if it is not separable by the SYMBOLSIZE. Store the number of bits added that way in TAIL, which will contribute to the compressed header information. In our example we have 32 symbols a 32 bit and the tail is 0.

We will now take a look at the symbols. Our buffer may look like:

A-A-B-C-A-B-A-C-D-… (32 32bit Symbols)

0-0-0-0-0-0-0-0-0-… (This is our alpha channel)

- Select the first unused (alpha=0) Symbol. This is shown bold above. Set the Alpha 1.

- Look ahead if you find the symbol in the next symbols within RANGE. If you do so, code YES in 1 bit plus the RANGE within RANGEWIDTH bits. Set the Alpha of the found symbol 1. Reset the RANGE to 0 and continue until no further occurrences are found. Code NO in 1 bit.

- Go back to a) until the buffer is finished.

- Encode the original size plus the tail in the header. You may also encode a version number, the symbol size and the range width optionally.

NOTE THAT:

The difference between A-A will be encoded 0 (0 symbols are between them).

The difference between A-X-X-A will be encoded 2.

Once you have already coded all As, the difference between the Bs in

B-A-C-B will be encoded as 1 (the As are already invisible due to the ALPHA).

Our DEST looks like:

A-Y0-Y2-Y1-…-N

B-Y1-…-N

C-Y0-…-N

D…

Iteration:

Once you have coded your buffer with a set of parameters, it can be encoded another time with different parameters. For example, for DMC compression a 32-5 32-3 32-5 triple run showed the best compression.

The following keys are used for compression-decompression interface to identify the different RZIP combination.

| RZIP Combination (in term of range) | Key |
| --- | --- |
| 3 | 0x30xxxxxx |
| 3-3 | 0x22xxxxxx |
| 3-3-3 | 0x03xxxxxx |
| 7 | 0x70xxxxxx |
| 6-6 | 0x00xxxxxx |
| 7-6-4 | 0x07xxxxxx |

Table 14. Keys for RZIP Combinationss

RZIP2 works in principle in the same way as RZIP, except that the symbols, answers and ranges are stored in a separated way. First, the 32-bit symbols are stored, then the block of ranges, padded by the block of answers. That way better iterative characteristics are achieved.

## A.2.5 Arithmetic Coding (ARC)

The algorithm for encoding data using arithmetic coding works conceptually as follows:

- The encoding process begins with a current interval [L ; H[ initialised to [0 ; 1[.

- For each symbol of the file, two steps are performed:

  - The current interval is divided into subintervals, one for each possible alphabet symbol. The size of a symbol's subinterval is proportional to the estimated probability that the symbol will be the next symbol in the file, according to the model of the input.

  - The subinterval corresponding to the symbol that actually occurs next in the file is selected as the new current interval.

- Enough bits are output to distinguish the final current interval from all other possible final intervals.

The length of the final subinterval is clearly equal to the product of the probabilities of the individual symbols, which is the probability p of the particular sequence of symbols in the file. The final step uses almost exactly - log2 p bits to distinguish the file from all other possible files. An additional mechanism is needed to indicate the end of the file, either a special end-of-file symbol coded just once, or some external indication of the file's length.

In the second step, it is required to compute only the subinterval corresponding to the symbol that actually occurs. To do this, two cumulative probabilities are defined, Pci = Σ pk (for k = 1 to i-1) (the cumulative probability) and Pni = Σ pk (for k = 1 to i) (the next cumulative probability). The new subinterval is [ L+Pci (H-L), L+Pni (H-L) ]. The need to maintain and supply cumulative probabilities requires the model to have a complicated data structure.

Example: a non-adaptive code, encoding the stream bbb using arbitrary fixed probability estimates pa = 0.4, pb = 0.5, and pEOF = 0.1.

Encoding proceeds as shown in Table 15.

| Current Interval | Action | Subinterval a | Subinterval b | Subinterval EOF | Input |
| --- | --- | --- | --- | --- | --- |
| [0.0000 ;1.0000[ | Subdivide | [0.0000 ; 0.4000[ | [0.4000 ; 0.9000[ | [0.9000 ; 1.0000[ | b |
| [0.4000 ;0.9000[ | Subdivide | [0.4000 ; 0.6000[ | [0.6000 ; 0.8500[ | [0.8500 ; 0.9000[ | b |
| [0.6000 ;0.8500[ | Subdivide | [0.6000 ; 0.7000[ | [0.7000 ; 0.8250[ | [0.8250 ; 0.8500[ | b |
| [0.7000 ;0.8250[ | Subdivide | [0.7000 ; 0.7500[ | [0.7500 ; 0.8125[ | [0.8125 ; 0.8250[ | EOF |
| [0.8125 ;0.8250[ | Subdivide |  |  |  |  |

Table 15. The Basic Arithmetic Coding Process

The final interval is [0.8125, 0.8250[, which in binary is approximately [0.11010 00000, 0.11010 01100[. This interval is uniquely identified by outputting 11010 00. According to the fixed model, the probability p of this particular file is (0.5)3 (0.1) = 0.0125 (exactly the size of the final interval) and the code length (in bits) should be - log2 p ≈ 6.322. In practice, 7 bits are needed.

For further details see AD005.

## A.2.6 Data Resorting (Reorder)

The aim of this algorithm is to increase the local redundancy (between successive samples) of the data but resorting the samples.

We consider 64 ramps from 450 detectors wher each ramp contains 8 samples. The  Reorder algorithm sort the data as follows:

1st sample of 1st ramp of 1st detector

1st sample of 2nd ramp of 1st detector

…

1st sample of 64th ramp of 1st detector

1st sample of 1st ramp of 2nd detector

1st sample of 2nd ramp of 2nd detector

…

1st sample of 64th ramp of 2nd detector

….

1st sample of 64th ramp of 450th detector

2nd sample of 1st ramp of 1st detector

2nd sample of 2nd ramp of 1st detector

…

2nd sample of 64th ramp of 1st detector

……

8th sample of 1st ramp of 450th detector

8th sample of 2nd ramp of 450th detector

…

8th sample of 64th ramp of 450th detector

## A.2.7 PACS Codec (new_srt)

This algorithm is based on szip, which uses a Burrows-Wheeler Transform like block sorting technique, followed by a dynamic model range coder.

Figure 69. Scheme of the PACS Codec algorithm.

A.2.8 FM Arithmetic Compression

The compression scheme has been adapted to address the data from the FM detectors in a better way. In principle, the encoding process is still the same as in the standard Arithmetic Compression, with a few modifications:

- the chunksize is fixed at 8192 byte to replace the division by a right shift.

- The input symbol width is 32 bit

- Input values bigger than 255 are encoded with the “spill symbol” and sent to the “spillover”

- The “spillover” is a separate buffer which will be compressed by VBWL. The VBWL algorithm used is a slight modification of in the VBWL only setting.

- The data model is semi-static: The fitst chunk is compressed with a built-in statistic, each next chunk is compressed with a statistic derived from the previous chunk.

## A.2.9 VBWL

A standard VBWL implementation with a few modifications, allowing for better flexibility. The blocksize is pretty short (4 symbols). Three different code lengths are used: the standard length is 3 bits, addressing the majority of the encoded (positive) differences. A 7-bit length is used for encoding  bigger differences.

Appendix B:
Fitting Algorithms

# B.1 Currently implemented Algorithms

## B.1.1 Robust Averaging in Photometry

The actually implemented algorithm in SPU HLSW version 12.2 is:

1.) Mean Value Calculation for signed or unsigned integers (see Appendix B.2.1.2).

## B.1.2 Ramp-Fitting in Spectroscopy

The actually implemented algorithm in SPU HLSW version 12.2 is:

- Least Squares Fit for more than 2 samples to fit (default) (see Appendix B.2.2.2)

- Two-sample difference (see Appendix B.2.2.7) if least square fit if selected and 2 samples per subramps are considered

- Mean algorithm if selected (see Appendix B.2.1.2)

## B.2 Library of Fitting Algorithms

## B.2.1 List of Available Algorithms

# The following table shows a summary of possible fitting algorithms for robust averaging in photometry and ramp-fitting in spectroscopy.

| Action | Name of Algorithm | Description | Implemented in HLSW v13.8 |
| --- | --- | --- | --- |
| Photometry |  |
| Glitch Detection and Rejection | Sample Deviation Detection Method | see section B.2.2.1.1 | ( |
|  | Averaging with Median + Mean Value Calculation | see section B.2.2.1.2 | ( |
| Averaging | Mean Value Calculation | see section B.2.2.2.1 | ( |
| Spectroscopy |  |
| Glitch Detection and Rejection | Crossed Slope Deviation Detection | see section B.2.3.1.1 | ( |
| Ramp-Fitting | Least Squares Fitting | see section B.2.3.2.1 | ( |
|  | Two-Sample-Fit | see section B.2.3.2.4 | ( |
|  | Slope Deviation Detection Method | see section B.2.3.2.5 | ( |
|  | Two-Samples Difference Method | see section B.2.3.2.6 | ( |
|  | Subramp Fitting | see section B.2.3.2.7 | ( |
| Averaging | Mean Value Calculation | see section B.2.2.2.1 | ( |

Table 16. List of available fitting algorithms.

## B.2.2 Robust Averaging in Photometry

## B.2.2.1 Glitch Detection and Rejection

## B.2.2.1.1 Sample Deviation Detection Method

The glitch detection uses the Sample Deviation Detection Method. It performs the following:

- Calculate the sum of valid quadruples.

S(i DIV 4) = sum(X(4*(i DIV 4):4*(i DIV 4)+3))

- Calculate the deviation  (using the weighted sample) of every sample in the quadruple comparing to the calculated sum.

Dev(i) = 4X(i) – S(i DIV 4)

If no glitches occur, all deviations would be less than a predefined Threshold

- Remove all deviations that are above a certain threshold

- Average all the remaining readouts with the currently implemented averaging algorithm.

Figure 70. Example showing the sample deviation detection method

## B.2.2.2 Averaging

## B.2.2.2.1 FM Averaging algorithm

## Beginning with software version 13.9, photometry and spectroscopy both use the same statistical averaging algorithm for the calculation of mean values. It supports arbitrary number of samples to average and additional bit rounding at the same time. There is also a random number generator involved for statistically correct up/down-rounding.

## The mean value of this averaging method is generated as follows:

## Where n is the number of samples to average, r is the number of bits to round, sgn() is the signum function and rand(1) is a random number being 0 or 1. After calculation, the result is cast to an integer. Note that the mean is right shifted yb r bits if bit rounding is used.

## For both, spectroscopy and photometry it is possible to use the “old” averaging algorithms via a parameter in the detector constants photometry/spectroscopy table.

## B.2.2.2.2 Mean Value Calculation

This averaging method consists of calculating of the mean value. All points in the support set are taken for the mean calculation. The advantage of this method is the simplicity of the mean value calculation. One assumption on the support set is that any kind of drift, skewness, detector behaviour, etc. is corrected by the preprocessing step.

The main objective of the averaging method is a robust oversampling reduction to facilitate the data processing. Further data processing can be performed on ground.

The mean value of this averaging method is generated for 4 data values as follows

where y represent either signed or unsigned integer values. In the software the mean is calculated like below.

Pseudo-Code example:

Mean_val= ((y[x] + y[x+1] + y[x+2] + y[x+3]) + 2) >> 2

Definitions :

signed :	int Mean_val, y;

unsigned int x;

unsigned :	unsigned int Mean_val, y, x ;

After the summation a bitwise shift by two was performed. This is equal to a division by 4. The result of this mean value calculation is either signed or unsigned integer. The remainder of the division is truncated.

## B.2.3 Ramp-Fitting in Spectroscopy

## B.2.3.1 Glitch Detection and Rejection

## B.2.3.1.1 Crossed Slope Deviation Detection

The glitch detection and rejection using the Wide Slope Deviation Detection method (Figure 71) is performed as described below:

- Calculate the differences between samples in a ramp as follows:

D(i,dist) = X(i) – X(i+dist)

- Calculate the deviation of these differences as follows.

Dev(i,dist) = D(i,dist) – dist * D(i,1)

For the first sub-ramp the difference of the first two samples is compared with the difference of the first and last sample in the sub-ramp. For all the following sub-ramps the difference of the last two samples of the previous sub-ramp is compared to the last sample of the new sub-ramp.

If deviations are under a certain threshold, then no information of glitches is available.

- Fit all safe readouts in a ramp with the currently implemented ramp-fitting algorithm till glitch information occurs.  If a glitch occurs then reject the 8 following samples and go to point 1Average all fitted slopes when the whole ramp was processed.

Figure 71. Example showing the crossed slope deviation detection

## B.2.3.2 Ramp-Fitting

## B.2.3.2.1 Least Squares Fitting

The least squares solution can be easily calculated in analytic form and it is optimal with respect to the Gaussian noise process. However, in case of heavy outliers (i.e., glitches) it performs very poor.

Figure 72(a) shows an example where least squares is performing very well, whereas Figure 72(b) shows the least squares solution on the same data as in Figure 72(a) where one sample is an outlier. One can clearly see that the obtained ramp is far from being perfect.

Figure 72. Least Square Fitting (1)

Figure 73. Least Square Fitting (2)

The slope of this fitting method is generated for a ramp or sub-ramps as follows

where

:= sumX

:= Sum_of_X_Square

:= Sum_of_X_By_X

:= sumXY

:= sumY

are float values. The result is an integer value where the float result is truncated.

Pseudo-Code example:

/*=================================*/

/* Least Square Tables Preparation */

Sum_of_X[0]=Sum_of_X_Square[0]= Sum_of_X_By_X[0]=0;

LSQ_Denominator[0]= 1; /* To Avoid Division By Zero */

for(i=1;i<512;i++)

{

Sum_of_X[i] = i+Sum_of_X[i-1];

Sum_of_X_Square[i] =(i*i)+Sum_of_X_Square[i-1];

Sum_of_X_By_X[i]= Sum_of_X[i]*Sum_of_X[i];

LSQ_Denominator[i]= ((i+1) * Sum_of_X_Square[i] - Sum_of_X_By_X[i]);

}

Definitions :

float Sum_of_X, Sum_of_X_By_X, Sum_of_X_Square, LSQ_Denominator;

unsigned int i;

/*===========================================*/

/* Slope Calculation for Every Ramp/Sub-ramp */

/* calculated in ramp_ft.c */

/* denominator isset in write.c */

for(i=0; i<ramps; i++)

{

sumY = sumXY = 0;

/* Intermediate Sums */

for(j=0; j<RRR; j++)

{

sumXY += j*y[j];

sumY += y[j];

}

/* Intermediate Results */

slope_z = (RRR * sumXY - sumY * sumX[RRR -1]);

slope_n = denominator[RRR-1];

if(slope_z>0) /* Choose the Rounding Error for the Division */

/* Write The Final Result into Buffer */

MEMWRITE((u4*)(buffer+i+1), (int)((slope_z/slope_n)*RRR+0.5)&0xffff);

else

/* Write The Final Result into Buffer */

MEMWRITE((u4*)(buffer+i+1), (int)((slope_z/slope_n)*RRR-0.5)&0xffff);

y += RRR;

}

Definitions :

float sumX, sumY, sumXY, denominator, slope_z, slope_n;

int y;

unsigned int i, j, RRR;

Example:

with RRR = 64

sumX = 26.

Sum_of_X_Square = 174.

Sum_of_X_By_X = 676.

sumXY = 326208.

sumY = 50145.

The numerator is:

slope_z = sumX sumY – n sumXY = 1303770. – 1304832. = -1062.

The denominator is:

slope_n = Sum_of_X_By_X – n Sum_of_X_Square = 676. – 696. = -20.

The result is therefore:

slope = (slope_z/slope_n)*RRR±0.5 = 53.1*64-0.5 (float) => slope = 3397 (integer)

## B.2.3.2.4 Two-Sample-Fit

This ramp-fitting method consists of calculating the slope by the difference of the second and last but one sample point. The advantage of this method is the simplicity of the difference value calculation. The disadvantage is that all other samples of the ramp are neglected. But in mind of a cumulative process where all information of the preceding samples are included in the last sample point this method

Assumptions on the points of the support set:

- No glitches (should be eliminated by the deglitching task)

- No non-linearity (e.g. saturation, etc.)

The calculation of the differences is performed as follows:

D(i) = X((i – 1) *N + 2) – X(i*N – 1)		for N ≥ 4

The differences are represented as unsigned integer values.  Figure 74 shows the ramp-fitting method.

Figure 74. Example showing the ramp-fitting method (fit and residuals)

## B.2.3.2.5 Slope Deviation Detection Method

The idea of the ramp fitting using the Slope Deviation Detection Method is very simple (Figure 76 shows one example ramp using the Matlab generator with three glitches). It performs the following:

- Calculate the differences between all successive readouts in a ramp. As the readout interval is equidistant, the differences represent the slopes using two successive readouts.

D(i) = X(i) – X(i+1)  (Figure 77)

- Calculate the deviation of these slopes. It is the differences of the differences of successive samples.

Dev(i) = D(i+1) –D(i)   (Figure 78)

If no glitches occur, all deviations would be close to zero

- Remove all deviations that are above 0.03 (3% of slope precision)

- Average all the remaining slopes (This is the result)

Figure 75 Example showing the slope deviation detection method

Figure 76. Photoconductor Readouts from 1 Channel with Additive Noise

Figure 77. Successive Slopes in the Ramp

Figure 78. Successive Slope Deviations in the Ramp

Advantages of the Method

- Very Robust as all the slopes are tested

- Very fast it only calculates samples differences. For N readouts (3N-3) operations are required

- Well-suited for PACS. As each readout is equivalent to the number of photon/time. For an equidistant readout interval, this number is fix in the ideal case. It only changes with any temperature drift (Glitch), which will be easily detected and rejected.

- It could be generalized for other applications

Disadvantages of the Method

- Not suited to short ramps. If a glitch occurs, it would be hard to find the best slope for a long relaxation time (For PACS, we decided to have ramps no shorter to one second as the CRE are only stable and precise for a long ramp)

Conclusion

The method was tested for several ramp cases and compared with standard methods (RANSAC and Least Squares). It gives the best results with a very low complexity. We have also optimised the complexity of the algorithm to 3N/2-1 for the same precision.

## B.2.3.2.6 Two-Samples Difference Method

In case of 2 samples to fit, the slope is calculated using the difference between two successive samples i.e. 32 slopes are calculated out of a 64 samples ramp

The calculation of the differences is performed as follows:

D(i) = X(2*i – 1) – X(2*i)

The differences are represented as unsigned integer values.

Figure 79. Example showing the Two-Samples Difference Method

## B.2.3.2.7 Subramp Fitting

The SPU On-board SW reduces the ramp by deriving either the ramp slope or the ramp mean depending on the algorithm chosen by the the user. It contains an option to derive not only 1 slope/mean per reset interval, but also slopes/means for every 2,4,8,16,32,... samples within a ramp. The number of samples to fit is a commandable parameter. Figure 80 illustrates the sub-ramp fitting procedure. The fitting result is then subslope (in case of least square fit) of submean (in case of mean algorithm). The used algorithm could be read from the compressed entity header (See RD016 for more details).

Figure 80. Illustration of Sub-ramp Fitting

## B.2.4 Averaging and Rounding in Photometry

Averaging and rounding in photometry is now also done by the FM Averaging algorithm (see a few pages above). The “old” algorithm can still be used and is described hereafter.

Rounding has been developed and implemented as a countermeasure against high noise settings. In the default averaging process 4 samples are added up and divided by 4. The datatype is 16 bit short and no decimal digits are kept, so the value 2 has to be added before division to get a rounded average instead of a truncated one. In other words, there is already a 2-bit rounding made in the nominal averaging process. The SPU software is able to intensify the rounding inside the averaging process.

Instead of the default      additional roundings can be

calculated by      and so on.

In addition to that, the number of samples to average is also freely configurable. Instead of 4 samples, 3, 5, or any other number 0<n<120 can be chosen.

For more information see document RD020.

## B.3 Decimation

## B.3.1 Decimation in Photometry

## Beginning with SPU SW version 13.95 frame dropping is implemented via two uploadble parameters DPRE and DPOST (see user manual for usage). DPRE determines the number of frames to be discarded at the beginning of an averaging group and DPOST does so for the end. An averaging group is 4 frames in default mode, 8 frames in double mode or any number of frames when the number of frames to average is overridden with the NAVG parameter. The implementation is done by a preprocessing module (in p_proc.c) that copies (in place) frames to be averaged and leaves out frames to be dropped. The reduced number of frames and the modified number of frames to average are then passed to the averaging module.

## B.3.2 Decimation in Spectroscopy

## Similarly, frames at the start of a complete ramp and at its end can be dropped. The implementation is the same as in photometry with the difference that not the averaging groups (= the submeans) are decimated, but the whole ramp is.

# Footnotes

The previous name of Herschel Space Observatory was Far InfraRed and Submillimeter Telescope ‘FIRST’

These are the HK for the bolometer background cancelling mode (see Section 12)

In the buffer transmission mode (see Section 5.8.5 and Section 5.8.9) program memory is also used for data buffering. Therefore the program memory allocation increases to 99.95%.

# Text boxes

No

Yes

Yes

Yes

Set NACK parameters for invalid memory block

No

memblock = ok?

Example: 32-sample ramp

CMM= 33

Set NACK parameters for invalid checksum

Store compressed raw channel data in the output buffer

Compress_Now = true

No

No

Yes

END

Set NACK parameters for invalid address

No

checksum = ok?

preproc.?

Addition of the offset to the data

Write the compressed data into the output buffer

Set NACK parameters for 
Invalid Memory ID

Call Lossless Coding

END

Yes

MemID = ok?

Yes

Call Temporal and Spatial Redundancy Reduction

Call Robust Averaging and Glitch Rejection

Division?

multipli-cation?

Multiply the offset by data samples

Subtraction of the offset to the data

Call Pre-processing

Addition?

Call Detector Selection 1 time

Raw channel selection in phot.?

address 
= ok?

Divide the data samples by offset

Noise Resampling procedure in Spectroscopy

No

Yes

No

Buffer under granularity size?

1

Read parameters

from HK buffer

1

2

Set HK parameters for invalid Compression Mode  and call default compression procedure for Spectroscopy

Free DMC Header & Science  Data Buffers

Raw 
Data 
Selection

NACK 
"Invalid Command"

No

Send Packet to DPU

Yes

Write HK

parameters to FIFO

1

Increment Counter

Raw 
Data 
Selection

Lossless Coding

Store validity information for this ramp

NACK 
"Write"

##### No

CID = WRITE

##### No

##### Yes

Proceed with

current activity

DPU command

Send Housekeeping

Yes

Stop the Compression SW

Yes

Start the Compression SW

Read the Activity ID

Run the Write Routines:

DXS1..7, DET_CST_SPEC, DET_CST_PHOT or SIM_DATA

1

Yes

ActivityID  = Warm Reset?

Time

No

END

Slope1/ Mean1

2

Buffer new data

Multiply the offset by data samples

END

Subtraction of the offset to the data

Addition?

Sub-traction?

Write the compressed data into the output buffer

Set PACK parameters

Calculate checksum of the data field

Read the load command parameters

END

Set NACK parameters for invalid memory type

Write the compressed data into the output buffer

Yes

No

No

Yes

preproc.?

Write data to memory

memtype = ok?

2

Yes

Perform SPU Test for Spectroscopy

Yes

Perform SPU Test for Photometry

Yes

No

2

1

BEGIN

Set HK parameters for Invalid Observing Mode

No

Yes

No Sequence is running

Compress_Now = true

Call Lossless Coding

1st sample in ramp?

Lossless Coding

No

No

No

Yes

Yes

Yes

Store grating informat.

No

No

1

Set the end of a Sequence

Call Temporal and Spatial Redundancy Reduction

Call Detector Selection for 1 time

BEGIN

Spectroscopy?

Buffer Transmisson Mode  procedure in Spectroscopy

Addition of the offset to the data

Write the compressed data into the output buffer

Yes

No

Perform a Warm Reset

Check if begin of sequence

##### No

END

No

Yes

Compressed data

Command/response / HK

Raw Data

END

Yes

Grating_info = false

Load command?

3

1

Invalid Command ID

Compress_Now = true

No

Default compression procedure in Spectroscopy for 4s reset

Yes

No

Yes

No

Get new frame

Half Compression procedure 
in Photometry

Yes

Stop command?

Store up to the max. nb. of TM packets in TM buffer

Stop command?

1

1

Stop command?

No

Transmit every TM buffer within 4440 ms

Yes

Perform Spatial Redundancy Reduction

Calculate sample differences and perform Spatial Redundancy Reduction

Reorder the data and perform Spatial Redundancy Reduction

Reorder and calculate differences of the data, perform Spatial Redundancy Reduction

No

No

Yes

Yes

-pixels

reference pixel

pixels of frame 5

pixels of frame 4

pixels of frame 3

pixels of frame 2

pixels of frame 1

reference pixel

-pixels

reference pixel

channel x

time

samples of channel x

Interrupt tasks (CSW and Test Tasks)

Listen to the DPU link

Initialisation of the DXS tables and bit mask tables at start-up

Initialisation of the parameters for the SPU Idle Mode

BEGIN

No

1

Yes

Data generator started?

No

1

Yes

Compressed data

Command/response / HK

Raw Data

Command/response

SPU LWL

DEC/

MEC

SPU SWL

DPU

Prepared by: 	Ahmed Nabil BELBACHIR  		         	       Date:  18. Feb 2009

Roland OTTENSAMER

Christian REIMERS

Checked and Approved by: Franz KERSCHBAUM

Checked and Approved by: Helmut FEUCHTGRUBER

Yes

Yes

Yes

Invalid Activity ID

Run the Check Routine

##### No

##### No

##### No

CID = CHECK

Store validity information for this ramp

##### No

Store choppper informat.

##### No

Take initial parameters

Delay of 1.5 seconds

CSW started?

No

Yes

BEGIN

chopper

Chopper_info = false

Blue Bolometers?

No

Yes

Output Buffer

(74.1 kB, circular)

Chopper_info = true

Blue Bolometers?

##### No

##### No

No

AID=TEST_P

DEC/MEC Header extraction and compression

DEC/MEC Header extraction and compression

Call Lossless Coding

PACK 
"Write"

Start compression of stored buffer using the actual look-up tables

Call Lossless Coding

Call Temporal and Spatial Redundancy Reduction

##### No

ASW semastate?

Run the Dump Routine

Run the Load Routine

CID = LOAD

CID = DUMP

Yes

CID = PFA

Same chopper plateau?

Yes

Yes

No

Bolometer Arrays (SWL)

Bolometer Arrays (LWL)

HK HBC

parameter 4

HK HBC

parameter 3

HK HBC

parameter 2

HK HBC

parameter 1

10

9

8

4

7

3

6

Voltage

No

Slope3/ Mean3

No

2

5

1

468

1

Header

row

column

26

1

18

1

Data generator started?

Write the new data size

No

(b)

Check command?

Perform command?

Dump command?

Lossless compress raw channel data for some detectors

Lossless compress raw channel data for some detectors

Yes

No

AID=TEST_S

Write the compressed data into the output buffer

Detector Selection

No

256

1

256

END

sort_me

Detector Selection

Pre-processing

Redundancy Reduction

##### Yes

##### No

Read the Command ID

DPU command

Yes

Perform SPU link start-up to DEC/MEC

##### No

Check chopper position

Compress_Now = true

1

3

5

Store DMC Header

Within a Sequence?

Begin of Sequence?

DMC Sequence?

END

Set PACK Parameters

Integration

Glitch Detection and Averaging

Pre-processing

Redundancy Reduction

Integration

Glitch Detection and Ramp Fitting

1280 kbit/s

320 kbit/s

Photometry

1872   kbit/s

1872 kbit/s

Spectroscopy

≤120 kbit/s

Fill DMC Header and Science Data Buffer

1

Read Compression

Mode

5

No

1

array 10

512

Yes

Copy data from RAM to EEPROM

##### No

AID=CONNECT_DMC

No

Yes

Misc. SW

phot_gn.c

spec_gn.c

Com. I/F

datatx.c

Application SW

supervs.c csw.c

Housekeeping

Hk.c

Watch Process

watchpc.c

HLSW Main

spu_io.c

Kernel Initialisation

Stack and Heap

(0.6 MB)

DMCH Buffer

(52.1 kB, circular)

Science Data Buffer

(960.5 kB, circular)

I/O Buffers

(1.1 MB)

Static Data Allocation and 
Processing Memory

(2.3 MB)

DRAM (4 MB)

Margin

(2.5 MB)

Program Code 
and Data

(0.5 MB)

PRAM (3 MB)

DPRAM (32 kB)

No

Yes

Yes

Grating_info = true

Same grating position?

Check grating position

1st sample in ramp?

4

Store DMC Header

Photometry?

DEC/MEC Header Error signalling in the HK

No

Call Detector Selection 1 time

No Sequence for WL_Switching is running

Write the compressed data into the output buffer

Yes

No

Blue Bolometers?

DEC/MEC Header extraction and compression

Filter the data with the Detector Selection Table

Transparent or LLC  mode?

Store maximum number of TM packets in TM buffer

Yes

Buffer Transmission Mode?

TM Blocks = 0

Copy the compressed raw channel data in the compressed entity, if selected

Send HK packet after compressed entity

Fill the HK packet

No

No

No

Transmit the stored TM packets

BEGIN

Yes

AID = RESET

Slope2/ Mean2

Initialise the Block Counter

array 9

1

Header

(a)

256

256

Yes

Spectroscopy?

Yes

No

Test data

received?

2

Compression of the data if buffer is full

Fill DMC Header and Science Data Buffer

1

1

AID = C2EEPROM

BEGIN

Read Compression

Mode

##### No

##### Yes

Read the Type

Photometry?

##### Yes

MAIN

Virtuoso Node

##### No

Stop CSW command?

##### Yes

##### No

DMC Raw Data?

BEGIN

256

256

256

256

256

1

1

1

1

1

1

1

256

Set the end of a Sequence

No

Yes

CSW started?

Listen to the data generator

1

No

BEGIN

Store Science Data

1

Compress_Now = true

Compress_Now = true

2

No

No

No

Yes

Yes

Yes

Store grating informat.

Grating_info = false

No

No

Yes

Yes

Grating_info = true

Same grating position?

Check grating position

1st sample in ramp?

4

Store DMC Header

1

array 2

512

array 1

1

Header

array 4

512

array 3

1

Header

array 6

512

array 5

1

Header

array 8

512

array 7

1

Header

(b)

(a)

241

32

16

256

17

1

array 10

241

32

16

256

17

1

array 9

16

1

No Sequence for WL_Switching is running

Set the end of a Sequence

Within a Sequence?

Begin of Sequence?

Label  or WL_Switching_Mode set?

Store choppper informat.

Chopper_info = false

No

Yes

column

Chopper_info = true

Same chopper plateau?

Check chopper position

row

16

1

32

17

241

32

16

256

17

1

array 8

241

32

16

256

17

1

array 7

241

32

16

256

17

1

array 4

241

32

16

256

17

1

array 3

241

32

16

256

17

1

array 6

241

32

16

256

17

1

array 2

241

32

16

256

17

1

array 5

241

32

16

256

17

1

array 1

49

64

48

33

32

17

16

1

column

row

16

1

32

17

Store Science Data

1

Compress_Now = true

No

Yes

1st sample in chopper plateau?

Yes

No

Yes

No

Frame  valid?

New Frame?

No

No

No

No

Yes

Yes

Within a Sequence?

Begin of Sequence?

Label  or WL_Switching_Mode set?

Store choppper informat.

Chopper_info = false

No

Yes

Chopper_info = true

Same chopper plateau?

Check chopper position

No

Yes

Store validity information for this ramp

1st sample in ramp?

No

No

No

No

Yes

Yes

Yes

Yes

Compress_Now = true

CMM or OBSID are not identical?

Reset frame counter

1

Increment the Frame Counter

Frame Counter = 512 or Compress_Now = true?

Store_Now = true?

Store_Now = true

Start compression of buffer

Yes

3

1

No

Photometry?

DEC/MEC Header Error signaling in the HK

No

Yes

Spectroscopy?

Yes

No

DMC data

received?

2

No

Yes

CSW started?

Listen to DEC/MEC link

1

Memory Allocation for Data Buffering

BEGIN

END

Yes

No

END

Yes

Yes

CMM=2

Slope4/ Mean4

Dump the buffer to a proccesing memory

END

Read the size of the obtained data

Lossless compression of the DMC header data

BEGIN

Calculate total size of compressed entity, the number of TM Blocks and set the max size of TM packets

Averaging over 2 samples

END

T_S_SortingFunction = 4?

Call DMC_Con function

END

BEGIN

Lossless compression of the science data using predefined algorithm

T_S_Sorting Function = 2?

Yes

Yes

Yes

Yes

Yes

Yes

Yes

Yes

Yes

No

No

Yes

NACK "Perform"

No

Yes

PACK 
"Perform"

Yes

No

No

Send dump data to FIFO

sub-traction?

1

Set the packet header according to the data type

Figure 14. Flowchart of the Watch Process + Command Acknowledgment Algorithm

No

Yes

NACK 
"Check"

No

Yes

PACK 
"Check"

No

Yes

1

2

1

NACK 
"Dump"

No

Send Packet to DPU

Yes

PACK 
"Dump of the LastPacket"

No

Yes

PACK "Dump of the Intermediate or First Packet"

No

Yes

NACK 
"Load"

No

Yes

Copy the science data in the compressed entity

Copy the compressed DMC header in the compressed entity

PACK 
"Load"

No

Yes

Science Data Packet in Photometry

Prepare the compr. entity header

Calculate the size of science data

Block

Header

1012 Bytes

Data

Block

Header

1012 Bytes

Data

Block

Header

1012 Bytes

Data

( ( ( ( ( (

( ( ( ( ( (

Data (1000 Bytes)

Data (1000 Bytes)

Data (1000Bytes)

Data (1000 Bytes)

CSD

CDH

CEH

Address = ok?

No

memblock = PRAM?

memtype = program memory?

No

No

Send NACK (Invalid Memory Type) to FIFO

Send NACK (invalid Address) to FIFO

Send response packet to the FIFO

END

Yes

memtype = data memory?

Yes

No

Read the dump command parameters

No

No

No

No

No

No

Yes

division?

multipli-cation?

Divide the data samples by offset

Send NACK (Invalid Memory ID) to FIFO

Yes

No

Yes

No

Calculate checksum and set PACK parameters

Address = ok?

memblock = PRAM?

memtype = program memory?

No

Set NACK parameters for Invalid Memory Type

Set NACK parameters for Invalid Address

Yes

memtype = data memory?

Read the check command parameters

Set NACK parameters for Invalid Memory ID

Yes

Yes

No

BEGIN

No

No

Yes

END

Send NACK (Invalid Activity ID)

Call bol_bc function (Bolometer Background Cancelling SW)

ActivityID  = Bol. Background Cancelling?

Yes

No

Call Spu_tst function (SPU Test for Spectroscopy or Photometry)

ActivityID  = SPU Test for Spectroscopy?

Yes

No

ActivityID  = SPU Test for Photometry?

Yes

No

Call Peak_Up function (Peak-Up SW)

ActivityID  = Peak-Up?

Yes

No

Call Str_Stp function (Start or Stop CSW)

ActivityID  = Start?

Yes

No

ActivityID  = Stop?

Yes

No

Call Rc_Sel function (Raw Channel Selection)

ActivityID  = Raw Channel Selection?

Yes

No

Call W_Reset function (Warm Reset)

ActivityID  = Warm Reset?

Read the perform command Parameters

Yes

No

BEGIN

Store DXS ID and Setup Table

Set NACK parameters for 
Invalid Length

Length = ok ?

Yes

Yes

No

END

Set PACK Parameters

Call DX_Table_Init

Send the Response Packet to the FIFO

Set NACK parameters for 
Invalid Checksum

DXS?

No

Yes

Read Write parameters
(Data Length and Checksum)

Read Parameter ID

Calculate Checksum

Set Address according to Parameter ID

Set NACK parameters for 
Invalid Parameter ID

Send the Response Packet to the DPU

Update the table
(DCS, DCP or SDP)

Checksum = ok ?

Yes

1

Buffer Transmission Mode?

Buffer Transmission Mode?

Update the look-up tables with the actual DEC/MEC header information (validity and chopper) for the compression task

Update the look-up tables with the actual DEC/MEC header information (validity, chopper and grating) for the compression task

Re-initialize the variables after closing a buffer (frame counter, PIX, etc.)

Store_Now = false (Set the begin of a new buffer)

Yes

Yes

CMM or OBSID are not identical?

Set parameters OBSID and CMM

1

Store Science Data and increment Frame counter

Frame counter = 480(Red)/120(Blue) or Compress_Now = true?

Store_Now = true?

Store_Now = true

First sample on a chopper plateau and in buffer?

Compression of the data if buffer is full

END

Integrate over valid samples from the same chopper plateau

Integrate over valid samples

Check grating information

Spectroscopy?

Point to the buffered data

No

BEGIN

Yes

Re-initialize the variables after closing a buffer (frame counter, PIX, etc.)

Store_Now = false (Set the begin of a new buffer)

Start compression of stored buffer using the actual look-up tables

4

No

Buffer new data

Buffer new data

No

No

Yes

Yes

Write the compressed data into the output buffer

Buffer number = 4

Science Data extraction from the 4 sub-regions

DMCH extraction

Buffer number < 4

Last DMCH extraction

Last Science Data ex-traction for the 4 sub-r.

Ignore DMC data

No

Set NACK parameters for 
Invalid Structure ID

Send the Response Packet to the FIFO

Copy PRAM to EEPROM

Call Detector Selection 4 times for 4 sub-arrays

BEGIN

Yes

1

Call Detector Selection 4 times for 4 sub-arrays

BEGIN

Call Temporal and Spatial Redundancy Reduction

Call Robust Averaging and Glitch Rejection

No

Yes

Yes

END

Write the compressed data into the output buffer

Buffer number = 4

Science Data extraction from the 4 sub-regions

DMCH extraction

Buffer number < 4

BEGIN

END

Check for saturation

Stop the CSW

Write the compressed data into the output buffer

Last DMCH extraction

Yes

No

Last Science Data ex-traction for the 4 sub-r.

Ignore DMC data

Call Lossless Coding

Call Temporal and Spatial Redundancy Reduction

Call Ramp Fitting and Glitch Rejection

Call Pre-processing

Stop CSW?

END

No

Yes

Call Detector Selection

Yes

SID != 0

BEGIN

Set NACK parameters for Invalid Structure ID

Send the Response Packet to the FIFO

SID = 5?

BEGIN

No

Yes

DEC/MEC Header extraction and compression

BEGIN

Set NACK parameters for Invalid SID Parameter 2 and send Response Packet to FIFO

END

Set NACK parameters for Invalid SID Parameter 1 and send Response Packet to FIFO

Write the compressed data into the output buffer

Call Lossless Coding

Call Temporal and Spatial Redundancy Reduction

Call Detector Selection

Observing Mode = ok?

RCNB Parameter = ok?

Set Raw Channel Selection for Photometry

No

Yes

Observing Mode = 1?

END

DEC/MEC Header extraction and compression

No

Yes

SID != 5

Set NACK parameters for Invalid Structure ID

BEGIN

Yes

Reset the SMCS chip and all the tasks apart the spu_io

Call C2EEPROM function

Yes

Send the Response Packet to the FIFO

BEGIN

Set PACK parameters

Send the Response Packet to the FIFO

Set Raw Channel Selection for Spectroscopy

Send the Response Packet to the FIFO

END

No

No

No

Yes

Yes

SID != 0

Call DMC_Con function

Set NACK Parameters for Invalid Structure ID

ActivityID  = Connect to DEC/MEC?

ActivityID  = Copy RAM to EEPROM?

AID = RCS

Yes

Perform Raw Channel Selection Settings

Frame counter = 0

Send the Response Packet to the FIFO

No

BEGIN

Delay to Alow the Transmission of the PACK

Yes

Set PACK Parameters

Raw channel selection in spec.?

AID = START

Yes

Write the compressed data into the output buffer

Buffer number = 4

Science Data extraction

DMCH extraction

Buffer number < 4

Check sample index

Blue Bolometers?

Last DMCH extraction

Write the compressed data into the output buffer

Call Detector Selection

DEC/MEC Header extraction and compression

Store compressed raw channel data in the output buffer

Send the Response Packet to the FIFO

Last Science Data extraction.

Ignore DMC data

END

Call C2EEPROM function

Yes

BEGIN

BEGIN

No

Yes

Yes

Call Pre-processing

Call Detector Selection 4 times for 4 sub-arrays

No

BEGIN

Parameter ID = ok?

No

END

No

Yes

SID != 0

Set NACK Parameters for Invalid Structure ID

Send the Response Packet to the FIFO

BEGIN

Set PACK Parameters

Signal the Start of the Peak-Up Program

Send the Response Packet to the FIFO

Yes

END

No

Yes

SID != 1

Set NACK Parameters for Invalid Structure ID

Send the Response Packet to the FIFO

BEGIN

Set PACK Parameters

Signal the Start of the Background Cancelling Program

Send the Response Packet to the FIFO

Read from FIFO

Yes

No

Signal the start of the CSW

Stop the TM data transmission

Delete  the on-board buffered science and DMC header data

Restart the HK for idle mode

Stop the buffer transmission mode and reset the buffer

No

BEGIN

No

Yes

Send the Response Packet to the FIFO

Set PACK Parameters

Signal the Start of the SPU HLSW Test

Call the Supervisor for the SPU Test

Test Mode Photometry?

Call Data Generator of Spectroscopy’ Frames

Call Data Generator of Photometry’ Frames

END

No

Yes

SID != 0

Set NACK Parameters for Invalid Structure ID

Send the Response Packet to the FIFO

BEGIN

BEGIN

No

Yes

Test Mode started?

Start the DMC Link respective to the Link Start-up Parameter

Generate science data for two chopper plateaus

2

BEGIN

Transparent mode  procedure in Spectroscopy

Send the Response Packet to the FIFO

Continue running ASW tasks

2

Start the link to DPU as Master

Define number of averages to generate by buffer

Set default parameters if the table is not available

Read the number of samples per average

Read the SPU ID and Compression Mode

Clean the Sema of the Warm Reset

Start high level SMCS Driver  the 1st time

Send the Response Packet to the FIFO

Set NACK parameters for 
Invalid SID Parameter

No

No

Yes

Photometry?

No

Yes

Yes

AID = STOP

Yes

BEGIN

1

ActivityID  = Connect to DEC/MEC?

1

2

CMM= 1

Yes

1

Read the size of the obtained data

(Part 3)

(Part 2)

(Part 3)

(Part 2)

Prepares the DEC/MEC header

Prepares the DEC/MEC header

BEGIN

Test Mode started?

1

No

Yes

Generate science data for two chopper plateaus

Define number of ramps to generate by buffer

Set default parameters if the table is not available

Read the number of samples per ramp

Read the SPU ID and Compression Mode

2

Set HK parameters for invalid Compression Mode and call default compression procedure for Photometry

Free DMC Header & Science Data  Buffers

Buffer Transmission Mode procedure in Photometry

Transparent mode  procedure 
in Photometry

Lossless compression  procedure in Photometry

Default compression  procedure in Photometry

Double compression  procedure in Photometry

Yes

No

Buffer under granularity size?

Yes

No

CMM=9

Yes

No

No

CMM=7

Yes

BEGIN

No

CMM=4

No

No

Yes

Set NACK parameters for 
invalid checksum after re-reading

No

Yes

No

checksum = ok?

Calculate checksum 
of the data

Re-read data from memory

T_S_Sorting Function = 1?

T_S_Sorting Function = 0?

Yes

No

Yes

No

CMM= 0

No

Check chopper information

Science Data Packet in Spectroscopy

No

Yes

Glitch 
detection ?

Yes

Calculate sample differences, reorder the data and perform Spatial Redundancy Reduction

T_S_Sorting Function = 3?

END

No

No

Yes

Listen to tasks output

BEGIN

HK Packet

No

Yes

No

No

Yes

Yes

Yes

Yes

Perform
two samples algorithm

No

Yes

Glitch 
detection ?

Perform
mean value algorithm

Glitch 
detection ?

Read the size of the obtained data and number of samples to fit

No

Yes

Glitch rejection and perform 
the currently implemented algorithm

2 samples per subramp ?

Check for saturation

No

Yes

Glitch rejection and perform
mean value algorithm

END

BEGIN

Mean aglorithm selected?

No

Get the Observing and Compression Modes from the Supervisor

CSW?

Perform the currently implemented fitting algorithm

Yes

Perform Spatial Redundancy Reduction

BEGIN

BEGIN

2 samples to average ?

Averaging over the required number of samples

Dump the buffer to a proccesing memory

Spectroscopy?

Yes

No

No

DMC sequence running?

Yes

No

Yes

Yes

Yes

Yes

Compress_Now = true

CMM or OBSID are not identical?

Set parameters OBSID and CMM

1

Increment the Frame Counter

Frame Counter = 512 or Compress_Now = true?

Store_Now = true?

Store_Now = true

First sample in a ramp and in buffer?

Start compression of stored buffer using the actual look-up tables

5

No

Yes

1

Buffer Transmission Mode?

Update the look-up tables with the actual DEC/MEC header information (validity and chopper) for the compression task

Re-initialize the variables after closing a buffer (frame counter, PIX, etc.)

Store_Now = false (Set the begin of a new buffer)

Start compression of stored buffer using the actual look-up tables

4

No

Yes

1

Buffer Transmission Mode?

Update the look-up tables with the actual DEC/MEC header information (validity, chopper and grating) for the compression task

Re-initialize the variables after closing a buffer (frame counter, PIX, etc.)

Store_Now = false (Set the begin of a new buffer)

No

Yes

No Sequence is running

Compress_Now = true

Set the end of a Sequence

Compress_Now = true

No

Yes

No

Yes

Store validity information for this ramp

Store choppper informat.

Chopper_info = false

No

Yes

Chopper_info = true

Same chopper plateau?

Check chopper position

Compress_Now = true

1

3

5

Store DMC Header

Within a Sequence?

Begin of Sequence?

DMC Sequence?

No

Yes

1st sample in chopper plateau?

Yes

No

Yes

No

Frame  valid?

New Frame?

No

No

No

No

Yes

Yes

Yes

Yes

CMM or OBSID are not identical?

Set parameters OBSID and CMM

1

Store Science Data and increment Frame counter

Frame counter = 480(Red)/120(Blue) or Compress_Now = true?

Store_Now = true?

Store_Now = true

First sample on a chopper plateau and in buffer?

1

Source address = PRAM?

Set NACK parameters for 
Invalid EEPROM length

EEPROM length = ok?

Set NACK parameters for 
Invalid EEPROM address

EEPROM address = ok?

Copy DRAM to EEPROM

No

No

No

No

No

Yes

Yes

Yes

Yes

Yes

1

1

1

Yes

No

DPU command received?

Call Write function

Call Perform Activity function

Call Check function

Call Dump function

Call Load function

No

Send NACK (Invalid Command ID)

Glitch rejection and averaging over the required number of samples

Write command?

Parameter for Link Start-up = ok?

Yes

No

END

Set PACK Parameters

Lossless compression  procedure in Spectroscopy

Default compression  procedure in Spectroscopy

Set NACK parameters for 
Invalid Structure ID

Send the Response Packet to the FIFO

Send the Response Packet to the FIFO

Configure (Unmask) SMCS Interrupt for DPU and DEC/MEC Link

BEGIN

SID = 1?

No

Yes

Set DSP Interrupt at IRQ2 to Signal SMCS Events

Set Nominal Configuration of the SMCS

Reset the SMCS chip

No

No

No

Yes

Yes

Yes

1

Yes

No

Connection to DPU  estabished?

Set DMC Link status in HK to OFF

Abort all ASW tasks

DMC Link disconnection error?

DPU Link disconnection  error?

2

Warm Reset command?

Start all ASW tasks

Set the DEC/MEC Link Connection Status to Not Connected

Set the link connection timeout to 9sec

BEGIN

Yes

No

CMM=25

Yes

No

CMM= 24

Read the remaining size R to the end of the circular buffer

Yes

1

Yes

No

Enough space in the circular buffer?

No

CMM=23

Yes

No

Store S – R of the data in the circular buffer

1

CMM= 20

Yes

Store R of the data in the circular buffer

Store the data in the circular buffer

Reset the address pointer of the circular buffer

Set the address pointer address of the circular buffer

BEGIN

Read size S of data to buffer

Increment the address pointer by S

No

CMM=16

No

Yes

Spectroscopy?

BEGIN

END

No

No

Yes

Yes

Reorder, reduce resolution and align the data, perform Spatial Redundancy Reduction

Reorder and reduce resolution of the data, perform Spatial Redundancy Reduction

8 bit resampling?

BOLC Test Pattern?

Calculate sample differences and perform Spatial Redundancy Reduction

BEGIN

time [s]

D(0)

D(0) = X(0) – X(1)

D(1) = X(2) – X(3)

D(2) = …

D(1)

D(2)

-----+------

X     Y

-----+------

5   12457

6   12509

7   12563

8   12616

-----+------

Convert buffered data from 4Bytes to 1Byte alignment

Dev(0,3) = D(0,3) – 3 * D(0,1)

Dev(2,5) = D(2,5) – 5 * D(2,1)

D(0,1)

D(2,5)

D(2,1)

D(0,3)

time [s]

N = 8:

D(1)

D(0) = X(1) – X(6)

D(1) = X(9) – X(14)

D(2) = …

D(0)

time [s]

D(2)

D(1)

Dev(0) = D(1) – D(0)

Dev(1) = D(2) – D(1)

Dev(2) = …

D(0)

time [s]

Dev(1)

Dev(0)

S(0)

Dev(0)

pacs_srt (in pacs_srt.c)

deletemodel (in pacs_cod.c)

S(0) = X(0) + X(1) + X(2) + X(3)

Dev(0) = 4*X(0) – S(0)

Dev(1) = 4*X(1) – S(0)

Dev(2) = 4*X(2) – S(0)

Dev(3) = 4*X(3) – S(0)

S(1) = X(4) + X(5) + X(6) + X(7)

Dev(4) = 4*X(4) – S(1)

Dev(5) = …

time [s]

time [s]

Dev(1)

Dev(2)

Dev(3)

S(1)

Dev(4)

Dev(5)

Dev(6)

Dev(7)

Dev(8)

Dev(9)

Dev(10)

Dev(11)

Dev(12)

Dev(13)

Dev(14)

Dev(15)

S(2)

S(3)

pacs_encode (in pacs_cod.c)

fixafterfirst (in pacs_cod.c)

pacs_encode (in pacs_cod.c)

initmodel (in pacs_cod.c)

compress_me

convert_byte_to_int

convert_byte_to_int

No

ActivityID  = Copy RAM to EEPROM?

END

Send NACK (Invalid Activity ID)

Call Spu_tst function (SPU Test for Spectroscopy or Photometry)

ActivityID  = SPU Test for Spectroscopy?

ActivityID  = SPU Test for Photometry?

Call Str_Stp function (Start or Stop CSW)

ActivityID  = Start?

ActivityID  = Stop?

Call Rc_Sel function (Raw Channel Selection)

ActivityID  = Raw Channel Selection?

Call W_Reset function (Warm Reset)

Read the perform command Parameters

BEGIN

512 frames received or signal to compr.?

Increment the frame counter

Store science data in buffer

Store DMC header data in buffer

Signal compression

Identical compression mode?

Signal synchronization

Signal synchronization

Synchronized?

Set DMC Error = 0x11

ramp begin and fill buffer synchron.?

Store the Relevant Information of DEC/MEC Header from 1st Frame

Store the Relevant Information of DEC/MEC Header from 1st Frame

Frame counter = 0?

Buffer Transmission Mode?

(Part 2)

(Part 3)

3

Get new frame

ASW semastate?

Check if begin of sequence

Initialize the buffer to start storage with 1st sample

1

Start compression of buffer

Reset frame counter

512 frames received or signal to compr.?

Increment the frame counter

Store science data in buffer

Yes

Signal compression

Identical compression mode?

Signal synchronization

Signal synchronization

Synchronized?

Set DMC Error = 0x01

ramp begin and fill buffer synchron.?

Store the Relevant Information of DEC/MEC Header from 1st Frame

Store the Relevant Information of DEC/MEC Header from 1st Frame

Frame counter = 0?

Buffer Transmission Mode?

Check and store DEC/MEC header only one time as it is identical for all sub-arrays

Yes

Yes

Yes

Yes

Yes

Yes

Yes

Yes

Yes

Yes

Yes

Yes

Yes

No

No

No

No

No

No

No

No

No

No

No

No

No

No